# risk assessment

# Cadmium oxide

# Cadmium metal

# CAS-No.: 1306-19-0

# CAS-No.: 7440-43-9

(Final : December 2005)

# Foreword to Draft Risk Assessment Reports

This Draft Risk Assessment Report is carried out in accordance with Council Regulation (EEC) 793/93 on the evaluation and control of the risks of “existing” substances. Regulation 793/93 provides a systematic framework for the evaluation of the risks to human health and the environment of these substances if they are produced or imported into the Community in volumes above 10 tonnes per year.

There are four overall stages in the Regulation for reducing the risks: data collection, priority setting, risk assessment and risk reduction. Data provided by Industry are used by Member States and the Commission services to determine the priority of the substances which need to be assessed.  For each substance on a priority list, a Member State volunteers to act as “Rapporteur”, undertaking the in-depth Risk Assessment and recommending a strategy to limit the risks of exposure to the substance, if necessary.

The methods for carrying out an in-depth Risk Assessment at Community level are laid down in Commission Regulation (EC) 1488/94 which is supported by a technical guidance document3. Normally, the “Rapporteur” and individual companies producing, importing and/or using the chemicals work closely together to develop a draft Risk Assessment Report, which is then presented to the Competent Group of Member State experts for endorsement. Observers from Industry, Consumer Organisations, Trade Unions, Environmental Organisations and certain International Organisations are also invited to attend the meetings. The Risk Assessment Report is then peer-reviewed by the Scientific Committee on Toxicity, Eco-toxicity and the Environment (SCTEE) which gives its opinion to the European Commission on the quality of the risk assessment.

This Draft Risk Assessment Report is currently under discussion in the Competent Group of Member State experts with the aim of reaching consensus. In doing so, the scientific interpretation of the underlying information may change, more information may be included and even the conclusions reached in this draft may change. Competent Group of Member State experts seek as wide a distribution of these drafts as possible, in order to assure as complete and accurate an information basis as possible. The information contained in this Draft Risk Assessment Report therefore does not necessarily provide a sound basis for decision making regarding the hazards, exposures or the risks associated with the priority substance.

This Draft Risk Assessment Report is the responsibility of the Member State rapporteur. In order to avoid possible misinterpretations or misuse of the findings in this draft, anyone wishing to cite, quote or copy this report is advised to contact the Member State rapporteur beforehand.

# See: Contact Details of the Rapporteur(s) on page 3

Information on the rapporteur :

# BE Rapporteur :

# Federal Public Service Health, Food Chain Safety and Environment

Environment Directorate-general

Roland Moreau, general-director

Service of Risk Management

Place Victor Horta, B 10

1060 Brussels

Belgium

Contact person for the rapporteur : linda.debacker@health.fgov.be

# Scientific expertise :

# Risk assessment: global/overall part: all sections excluding those on batteries’ related issues

Erik Smolders, Ilse Schoeters, Nadia Waegeneers, Uldeen Ghesquiere, Pieter Jan Haest and Roel Merckx

Laboratory of Soil and Water Management

Kasteelpark Arenberg 20

B-3001 Heverlee

Belgium

erik.smolders@agr.kuleuven.ac.be

Risk assessment: batteries’ related life cycle steps

Marnix Vangheluwe, Marleen Vandenbroele and Patrick Van Sprang

EURAS bvba

Grote Baan 199

B-9920 Lovendegem

Belgium

E-mail: marnix.vangheluwe@euras.be

T: 32 9 257 13 99

F: 32 9 257 13 98

www.euras.be

Risk assessment : update based on recent site-specific exposure data regards all scenarios (except disposal)

EURAS cfr here above

Contact person: Marleen Vandenbroele

# Contents

0	OVERALL CONCLUSIONS/RESULTS OF THE RISK ASSESSMENT	10

0.1	General remark on the scope, the approach and the limitations of the study	10

0.1.1	The so-called ‘global’ or ‘overall’ risk assessment on cadmium (based on data from around 1996)	11

0.1.2 	The so-called Targeted  Risk Assessment on cadmium as used in batteries	14

0.1.3	Update assessment for site-specific exposure data (reference year 2002)	15

0.2	overall conclusions for environment: cadmium oxide and cadmium metal	16

0.3	overall conclusions for human health	19

1	GENERAL SUBSTANCE INFORMATION	20

1.1	Identification of the substance	20

1.2	Purity/impurities, additives	20

1.3	Physico-chemical properties	21

1.4	CLASSIFICATION	24

1.4.1	Classification at the start of the risk assessment	24

1.4.2	Proposed classification	25

1.4.2.1	ENVIRONMENTAL CLASSIFICATION AND LABELLING	25

1.4.2.1.1	Introduction	25

1.4.2.1.2	Dissolution test results	25

1.4.2.1.3	Result short-term toxicity tests	28

1.4.2.1.4	Conclusion and discussion	29

1.4.2.1.5	Overall classification for the environment as proposed by the rapporteur	29

1.4.2.1.6	Classification for the environment – proposal for Annex I adaptation	30

1.4.2.2	classification and labelling: human health	30

1.4.2.2.1	Completeness of the base-set (Annex VIIA Dir. 67/548/EEC)	30

1.4.2.2.2	The Rapporteur’s proposal for classification:	31

1.4.2.2.3	The decision of the CMR WG:	31

1.4.3	current classification as in annex i	32

2	GENERAL INFORMATION ON EXPOSURE	34

2.1	Production	34

2.1.1	Production process	34

2.1.2	Production volumes	38

2.1.2.1	Data for the reference year 1996	38

2.1.2.2	Update date (reference year 2002)	43

2.2	Uses	46

2.2.1	General overview	46

2.2.2	Batteries	52

2.2.2.1	Used terminology on Nickel-Cadmium batteries	52

2.2.2.2	Ni-Cd chemistry and composition	55

2.2.2.3	Production, recycling and use	56

2.2.2.3.1	Ni-Cd batteries manufacturing processes	56

2.2.2.3.2	Mass balance	65

2.2.2.3.3	Ni-Cd batteries producing/recycling companies	71

2.2.2.4	Market and sales data	71

2.2.2.4.1	General	71

2.2.2.4.2	Portable Nickel-Cadmium batteries	72

2.2.2.4.2.1	General	72

2.2.2.4.2.2	Data for portable Ni-Cd Batteries by market segments/applications (CollectNiCad. 1)	73

2.2.2.4.2.3	Data for portable Ni-Cd Batteries based on production data (CollectNiCad 2)	74

2.2.2.4.2.4	Historical market  development	74

2.2.2.4.3	Industrial Ni-Cd batteries (CollectNiCad 2000c)	75

2.2.2.4.4	Country by country data	76

2.2.2.4.4.1	Portable Ni-Cd batteries	77

2.2.2.4.4.2	Industrial batteries	78

2.2.2.4.4.3	Market trends	79

2.2.2.5	COLLECTION/RECYCLING DATA	80

2.2.2.5.1	Country by country data	80

2.2.2.5.1.1	Portable Nickel-cadmium batteries	81

2.2.2.5.1.2	Industrial Nickel-Cadmium batteries	82

2.2.2.5.2	Collection rate/Collection efficiency	83

2.2.3	Update data (reference year 2002)	85

2.2.3.1	Introduction	85

2.2.3.2	Ni-Cd Batteries	87

2.2.3.3	Cd containing Pigments	87

2.2.3.4	Cd containing stabilisers	88

2.2.3.5	Alloys, plating and other uses	88

2.3	Legislative control measures	88

2.3.1	EU legislation	88

2.3.2	National legislation	97

2.4	Voluntary control measures	100

2.5	Other supranational instruments	100

3	ENVIRONMENT	102

3.1	Environmental exposure	102

3.1.1	Methods and definitions: added Cd, natural background and ambient concentrations	102

3.1.2	Emissions	103

3.1.2.1	Releases during production and use (excluding batteries’ related scenarios)	103

3.1.2.1.1	Source of data	103

3.1.2.1.2	Emission reduction during production and use	111

3.1.2.1.2.1	Emission reduction during production	111

3.1.2.1.2.2	Emission reduction during use and end-of-life	112

3.1.2.2	Releases due to batteries’ related scenarios	112

3.1.2.2.1	Life cycle stage 1: Manufacturing of Ni-Cd batteries and/or battery packs	113

3.1.2.2.2	Life cycle stage 2: Incorporation into battery-powered devices and applications	119

3.1.2.2.3	Life cycle stage 3: Use, recharging and maintenance by end user	119

3.1.2.2.4	Life cycle stage 4: Recycling	119

3.1.2.2.5	Life cycle stage 5: Disposal	124

3.1.2.2.5.1	Scope definition	124

3.1.2.2.5.2	Contribution of Ni-Cd batteries to the cadmium content of Municipal Solid Waste: current situation	125

3.1.2.2.5.3	Forecasts of future battery waste arisings	131

3.1.2.2.5.4	Waste management Strategies in Europe	136

3.1.2.2.5.5	Overall cadmium emissions from incineration MSW	138

3.1.2.2.5.5.1	Current emissions	138

3.1.2.2.5.5.2	Future emissions	159

3.1.2.2.5.6	Overall cadmium emissions from landfilling MSW	166

3.1.2.2.5.7	Sensitivity analysis	186

3.1.2.2.6	Summary: releases to the environment due to battery related life cycle steps	189

3.1.2.3	Releases based on update site-specific exposure data (reference year 2002)	194

3.1.2.3.1	Cadmium metal and cadmium oxide production	194

3.1.2.3.2	Release during processing and use	199

3.1.2.3.2.1	Ni-Cd batteries’ production and recycling	199

3.1.2.3.2.2	Production of Cd containing pigments	204

3.1.2.3.2.3	Production of Cd containing stabilisers	206

3.1.2.3.2.4	Use of Cd/CdO in alloys, plating and other uses	209

3.1.2.3.3	Releases during the production of other non-ferrous metals	209

3.1.3	Predicted environmental concentrations (PEC)	209

3.1.3.1	Local exposure assessment: in production, processing and use scenarios excluding those related to batteries	209

3.1.3.1.1	Aquatic compartment	209

3.1.3.1.2	The sediment	214

3.1.3.1.3	Atmospheric compartment	216

3.1.3.1.4	Terrestrial compartment	221

3.1.3.2	Local exposure assessment: batteries’ related scenarios	226

3.1.3.2.1	Aquatic compartment	226

3.1.3.2.2	Sediment compartment	240

3.1.3.2.3	Atmospheric compartment	246

3.1.3.2.4	Terrestrial compartment	251

3.1.3.3	Local exposure: all scenarios: update data (reference year 2002)	254

3.1.3.3.1	Aquatic compartment: calculated PECs	254

3.1.3.3.1.1	Surface water	255

3.1.3.3.1.1.1	Introduction	255

3.1.3.3.1.1.2	Cd metal and Cd oxide production	255

3.1.3.3.1.1.3	Production and recycling of Ni-Cd batteries	256

3.1.3.3.1.1.4	Production of Cd containing pigments	258

3.1.3.3.1.1.5	Production of Cd containing stabilisers	259

3.1.3.3.1.1.6	Use of Cd/CdO in alloys, plating and other uses	260

3.1.3.3.1.2	Calculation of Predicted Environmental Concentration for Sewage Treatment Plants (PECstp)	260

3.1.3.3.1.3	Calculation of PECsediment	264

3.1.3.3.1.4	Summary of calculated PECs for surface water	267

3.1.3.3.1.5	Measured data in the aquatic compartment	268

3.1.3.3.2	Terrestrial compartment	275

3.1.3.3.2.1	Calculated PEC for soil	275

3.1.3.3.2.2	Measured levels in soil	279

3.1.3.3.3	Atmospheric compartment	279

3.1.3.3.3.1	Calculation of PEClocalair	279

3.1.3.3.3.2	Measured levels	284

3.1.3.3.3.3	Comparison of PECs with measured data	288

3.1.3.3.4	Non compartment specific effects relevant for the food chain	290

3.1.3.4	Regional and continental exposure assessment	290

3.1.3.4.1	Regional and continental concentrations calculated according to the TGD	290

3.1.3.4.1.1	Contribution of batteries’ related life-cycle steps	300

3.1.3.4.2	An alternative model predicting regional and continental concentrations in agricultural soils	319

3.1.3.4.3	Measured regional data in the environment	335

3.1.3.4.4	Comparison of measured and calculated data	372

3.2	Effects Assessment	373

3.2.0	Methods and definitions	373

3.2.0.1	Data quality	373

3.2.0.2	Definitions of critical concentrations	373

3.2.1	Aquatic compartment	375

3.2.1.1	General	375

3.2.1.1.1	Data quality: definitions of Reliability Indices (RI’s)	375

3.2.1.1.2	Source of data and its limitations for risk assessment	376

3.2.1.2	Acute and chronic toxicity to fish/amphibians	379

3.2.1.3	Acute and chronic toxicity to aquatic invertebrates	388

3.2.1.4	Toxicity to primary producers.	399

3.2.1.5	Discussion.	404

3.2.1.6	The PNECwater.	405

3.2.1.6.1	The NOEC data	405

3.2.1.6.2	Species sensitivity distributions at different levels of data quality	405

3.2.1.6.3	Calculation of the generic PNECwater	417

3.2.1.6.4	PNECwater as a function of water characteristics	423

3.2.1.7	Conclusion	427

3.2.2	Terrestrial compartment.	428

3.2.2.1	General	428

3.2.2.1.1	Data quality: definitions of Reliability Indices (RI’s)	428

3.2.2.1.2	Source of data and its limitations for risk assessment	429

3.2.2.2	Toxicity to soil microflora	432

3.2.2.3	Toxicity to soil fauna	439

3.2.2.4	Toxicity to higher plants	444

3.2.2.5	Discussion	449

3.2.2.6	The PNECsoil	450

3.2.2.6.1	Species sensitivity distributions at different levels of data quality	450

3.2.2.6.2	Calculation of the generic PNECsoil	460

3.2.2.6.3	PNECsoil in relation to soil properties	465

3.2.2.7	Conclusion	467

3.2.3	Toxicity to benthic organisms.	469

3.2.3.1	Influence of sediment properties on toxicity of Cd	469

3.2.3.2	Acute and prolonged toxicity to benthic organisms	470

3.2.3.3	The PNECsediment.	475

3.2.4	Atmospheric compartment.	478

3.2.5	Toxicity for micro-organisms in a sewage treatment plant (STP)	478

3.2.6	Assessment of secondary poisoning	480

3.2.6.1	Source of data and limitations for risk assessment	480

3.2.6.2	The aquatic compartment	480

3.2.6.2.1	The bioconcentration factor in water	480

3.2.6.2.2	The bioaccumulation factor in water	488

3.2.6.2.3	Secondary poisoning within the aquatic compartment	489

3.2.6.3	The terrestrial compartment	494

3.2.6.3.1	Bioconcentration and bioaccumulation factors in soil	494

3.2.6.3.2	Secondary poisoning within the lower terrestrial foodchain	502

3.2.6.4	The sediment compartment	505

3.2.6.4.1	Bioaccumulation in sediment	505

3.2.6.5	Toxicity to mammalian and avian organisms	508

3.2.6.5.1	Derivation of the PNECoral	508

3.2.6.5.2	An alternative approach for wildlife in the terrestrial environment based on renal thresholds	513

3.2.6.5.2.1	Critical concentration of Cd in kidney	519

3.2.6.5.2.2	Critical soil Cd concentrations for wildlife	520

3.3	Risk characterisation	524

3.3.1	Introduction	524

3.3.2	Risk characterisation for production and use (excluding batteries)	525

3.3.2.1	The aquatic compartment (including sediment and STP)	525

3.3.2.2	The terrestrial compartment	537

3.3.2.3	Secondary poisoning	540

3.3.2.4	The atmospheric compartment	542

3.3.2.5	Conclusions	542

3.3.3	Risk characterisation for battery related life cycle steps	544

3.3.3.1	Overview assumptions and built-in conservatism	544

3.3.3.2	The aquatic compartment (including sediment and STP)	553

3.3.3.3	The atmospheric compartment	566

3.3.3.4	The terrestrial compartment	567

3.3.4	Risk characterisation for all scenarios: update data (year 2002)	568

3.3.4.1	The aquatic compartment (including sediment)	568

3.3.4.2	The terrestrial compartment	576

3.3.4.3	The atmospheric compartment	577

3.3.4.4	Non compartment specific effects relevant for the food chain (Secondary poisoning)	578

4	HUMAN HEALTH	579

5	CONCLUSIONS/RESULTS	580

5.0	introduction	580

5.1	local level: current situation (=updated with 2002 data and assessment)	582

5.1.1	Conclusions on cadmium metal	582

5.1.2	Conclusions on cadmium oxide	584

5.2	local level: disposal step: future situation and/or and sensitivity analysis	587

5.2.1	Conclusions on cadmium metal and cadmium oxide	587

5.3	REGIONAL LEVEL	589

5.3.1	Conclusions on cadmium metal and cadmium oxide	589

6	references (HH still included; env still to complete/check references from revisions after SCTEE opinion)	592

GLOSSARY	668

annexes	674

# OVERALL CONCLUSIONS/RESULTS OF THE RISK ASSESSMENT

## General remark on the scope, the approach and the limitations of the study

The present document contains the semi-integration of three study reports that were started at different years and conducted over different time lines i.e. the so-called overall or global RAR, the targeted risk assessment on batteries (‘TRAR’) and the update risk assessment. The first and main report was started in 1997 and based essentially on exposure data from around 1996. Few years later the study on batteries was initiated as a separate investigation and exposure data are mainly  from 1999/2000. This report was previously presented as a separate document, the TRAR, in Annex to the first report. Finally, an update assessment for the local scenarios was started end 2004 and based on site specific exposure data for the reference year 2002.

The structure of the present document still reflects to some degree the scope and content of each of these three studies and reports (see Table 0.1.1). More in particular, chapters 2 (production volumes, uses) and 3 (i.e. 3.1 environmental exposure and 3.3 risk chracterisation) present the following general structure: first the subsections related to all production and use scenarios are given with the exception of those related to batteries and their further life-cycle. Then the subsections follow dedicated to the batteries’ related issues (inclusive their waste management). Finally the subsections reporting update site-specific informations on all production, processing and use scenarios are given (thus the scenarios of the overall RAR and of the TRAR). However no disposal scenarios are included in this update.

The regional exposure assessment (section 3.1.3.3 and further) and the effect assessment (whole section 3.2) are common to all three studies and thus do not present the aforementioned substructure.

Table 0.1.1: Overview of the structure of the present document as composed of the three studies and reports related to the risk assessment of cadmium metal and cadmium oxide for the environment.

| Section : current document | Content | Source document identification and its section |
| --- | --- | --- |
| 1. | General substance information | Global/overall RAR (1.) |
| 2.1.1. | Production process | Global/overall RAR (2.1.1) |
| 2.1.2 | Production volume | Global/overall RAR (2.1.2) |
| 2.1.2.1 | Data for the reference year 1996 | Global/overall RAR (2.1.2) |
| 2.1.2.2 | Update data (for the reference year 2002) | Update document (2.1.2) |
| 2.2 | Uses |  |
| 2.2.1 | General overview | Global/overall RAR (2.1.3) |
| 2.2.2 | Batteries | TRAR (on/in batteries) (2.) |
| 2.2.3 | Update data (for the reference year 2002) | Update document (2.2.1) |
| 2.3 | Legislative control measures | Global/overall RAR (2.2) |
| 2.4 | Voluntary control measures | Global/overall RAR (2.3) |
| 2.5 | Other supranational instruments | Global/overall RAR (2.4) |
| 3.1 | Environmental exposure | Global/overall RAR (3.1) |
| 3.1.1 | Methods and definitions | Global/overall RAR (3.1.1) |
| 3.1.2 | Emissions | Global/overall RAR (3.1.2) |
| 3.1.2.1 | Source of data | Global/overall RAR (3.1.2.1) |
| 3.1.2.2 | Emissions during production and use | Global/overall RAR (3.1.2.2) |
| 3.1.2.2 | Releases due to batteries’ related scenarios | TRAR (on/in batteries) (3.1.2) |
|  | Life cycle stage 1 | TRAR on/in batteries (3.1.2.1) |
|  | Life cycle stage 2 | TRAR on/in batteries (3.1.2.2) |
|  | Life cycle stage 3 | TRAR on/in batteries (3.1.2.3) |
|  | Life cycle stage 4 | TRAR on/in batteries (3.1.2.4) |
|  | Life cycle stage 5 | TRAR on/in batteries (3.1.2.5) |
|  | Summary | TRAR on/in batteries (3.1.2.6) |
| 3.1.2.3 | Releases based on update site-specific exposure data (reference year 2002) | Update document (3.1.1.1) |
|  | Cd metal and CdO production | Update document (3.1.1.1.1) |
|  | Release during processing and use | Update document (3.1.1.1.2&3) |
|  | Releases during the production of other non-ferrous metals | Update document (3.1.1.1.4) |
| 3.1.3 |  |  |
| 3.1.3.1 | Local exposure assessment: production, processing and use scenarios excl. those related to batteries | Global/overall RAR (3.1.2.3) |
|  | Aquatic compartment | Global/overall RAR (3.1.2.3.1) |
|  | Sediment | Global/overall RAR (3.1.2.3.2) |
|  | Atmospheric compartment | Global/overall RAR (3.1.2.3.3) |
|  | Terrestrial compartment | Global/overall RAR (3.1.2.3.4) |
| 3.1.3.2 | Local exposure assessment: batteries related scenarios | TRAR on/in batteries (3.1.3.2) |
|  | Aquatic compartment | TRAR on/in batteries (3.1.3.2.1) |
|  | Sediment | TRAR on/in batteries (3.1.3.2.1) |
|  | Atmospheric compartment | TRAR on/in batteries (3.1.3.2.1) |
|  | Aquatic compartment | TRAR on/in batteries (3.1.3.2.4) |
| 3.1.3.3 | Local exposure assessment: update data (reference year 2002) | Update document |
|  | Aquatic compartment: calculated PECs | Update document (3.1.2.1 & 3.1.2.2) |
|  | Terrestrial compartment | Update document (3.1.3) |
|  | Atmospheric compartment | Update document (3.1.4) |
|  | Non compartment specific effects relevant to the food chain | Update document (3.1.5) |
| 3.1.3.4 | Regional and continental exposure assessment | Global/overall RAR (3.1.2.4) |
|  | Regional and continental concentrations calculated according to TGD | Global/overall RAR (3.1.2.4.1) |
|  | An alternative model predicting regional and continental concentrations in soils | Global/overall RAR (3.1.2.4.2) |
|  | Measured regional data in the environment | Global/overall RAR (3.1.2.4.3) |
| 3.2 | Effects assessment | Global/overall RAR (3.2) |
| 3.3 | Risk characterisation |  |
| 3.3.1 | Introduction | Global/overall RAR (3.3.1) |
| 3.3.2 | Risk characterisation for production and use (excluding batteries) | Global/overall RAR (3.3.2 to 3.3.6) |
| 3.3.3 | Risk characterisation for battery related life cycle steps | TRAR in batteries (3.3.1 to 3.3.4) |
| 3.3.4 | Risk characterisation for all scenarios: update data (year 2002) | Update document (3.3.1 to 3.3.4) |
| 4 | Human health | In separate document/report |
| 5 | Conclusions |  |
| 5.0 | Introduction |  |
| 5.1 | Local level: current situation (updated for 2002) | Update document (4.2), TRAR (5.1) and global/overall RAR (5.2) |
| 5.2 | Local level: disposal step: future situation and/or sensitivity analysis | TRAR (5.2) |
| 5.3 | Regional level | Global/overall RAR (5.2) [TRAR (5.3)] |
| Section : current document | Content | Source document identification and its section |

Important : all references to ‘Global or overall RAR’, ‘TRAR in/on batteries’ and ‘Update document’ are references to the previously stand-alone source documents.

### The so-called ‘global’ or ‘overall’ risk assessment on cadmium (based on data from around 1996)

This study is focused on assessing the risks of the two priority substances cadmium metal and cadmium oxide as foreseen under the Regulation 793/93/EEC, and thus especially during the production and the intentional use of these two specific substances.

Several other studies on ‘cadmium’ (generic) are dealing with other fields and/or compounds (e.g. the studies and reports performed in the framework of the Fertiliser Directive (76/116/EEC), the Cadmium Directive (91/338/EEC), the Ambient Air Directive, etc).

The present study does not cover all fields and all compounds and it is advised to consult the aforementioned studies for detailed (risk) assessment of these compounds in these fields.

The current study essentially covers the production of cadmium metal and cadmium oxide, the use of these substances in the production of stabilisers, pigments, alloys and plated products. Further down-stream uses are not or only limitedly included.

However, major attention is attributed to the most important application, i.e. batteries with the whole life-cycle covered, thus including the main waste management options (recycling, incineration and landfill). For more details on the scope and limitations of the latter study i.e. the so-called targeted risk assessment of cadmium (oxide) as used in batteries, reference is made to the Ni-Cd batteries’ related (sub)sections. In addition to the standard current scenarios an attempt was made to include some future scenarios.

For the environment, at regional level, the inventory of anthropogenic cadmium emissions has attempted to include all cadmium sources, thus including emissions from fertilisers, sludge, waste incineration, other industrial activities, etc.  Sources and data were retrieved from open literature and unpublished reports available at the time this section was most importantly revised (reporting year 2000, based mainly on data from the 90-ties). Stormwater and combined sewer overflows, being identified as a significant Cd-source to the surface water, have not been quantified in this assessment and may not be entirely covered.

The risk of cadmium (oxide) to the marine environment is not assessed (it is judged inappropriate to apply freshwater chemistry and ecotoxicity thresholds to the marine environment).

Cadmium in fertilisers (where cadmium is present as an impurity of the phosphate nutrient) and the potential risk linked with the use of sewage sludge on arable land, is covered to the extent needed for an appropriate assessment of the indirect exposure pathway (i.e. the use of fertilisers and sewage sludge is taken into account at the regional and continental scale). For more detailed in-depth examination of the fertilisers’ topic, reference is made to the studies of national authorities and the EC reports made in that framework (cfr Legislative control measures in section 2.3). The emissions from the rest of the sewage sludge (applications other than on arable land) could not be quantified.

As to the general assessment’s approach, it was, for several reasons, preferred to adopt the ‘total risk approach’ in contrast with the ‘added’ approach in (some) other risk assessments on metals under the Existing Substances’ Regulation.

In the total risk approach, the risk characterization is performed on the ‘total cadmium’ concentrations in the environment, i.e. including the natural background and past anthropogenic (diffuse) input. As mentioned above, the anthropogenic sources are limited here by the context of the Regulation. Cadmium emissions of historic origin are taken into account for the soil and sediment compartment given the (very) long retention time of the substance (generic) in these compartments. The regional and continental risk characterisation for the environment is mainly based on measured data because of the limited predictive power of the exposure models at that scale.

More specifically, the following observations are made related to the environmental part of the present study. It should be born in mind that these findings are of the utmost importance in the development of an adequate risk reduction strategy.

It is estimated in the actual assessment that the emissions by cadmium(oxide) producing and using companies contribute only 3.8% to the total emissions of cadmium in water and 3.8% to total emissions to air. For water, the total EU emission by the Cd(O) producing and using plants is estimated at 1.5 tons per year (see Table 3.1.155). Emissions of other sources at regional level are estimated at >39.2 tons per year (see Table 3.1.155: Cd EU emission data to water). Hence, it is concluded that the cadmium emission from the cadmium(oxide) industry only amounts to 3.8% (1.5 tons versus a total of 1.5+39.2 tons) of the total cadmium emission to surface water.

The total European emissions to air from all other sectors is estimated at >124 tons Cd per year while the total EU cadmium(oxide) industry emission is estimated at 4.7 tons/year (approx. 3.8% of the total  124 +  4.7  tons emitted).

Total Cd emissions to agricultural soils are mainly related to P fertiliser application and are about 230 tons Cd year-1 (see Table 3.1.156). Additional net Cd sources are imported animal feed, sewage sludge and atmospheric deposition. The Cd deposition onto agricultural land, derived from Cd(O) production, processing and recycling is estimated to be 1.2  tons Cd year-1 (i.e. 4.7 tons Cd year-1 multiplied by 0.27, the fraction surface area that is agricultural soil).

The actual assessment assumes good waste practices by all cadmium(oxide) producers and users.

Some future scenarios are included in the assessment.

Related to the arable soil compartment (within section 4.1.1.3 of the human part of the present study, in separate document):

A number of scenarios were developed to represent agricultural practices in the EU. Besides other input and output factors these scenarios relate to distinct uses of fertilisers. The impact of the food-chain being more critical for human than for the ecosystem, the assessment is limited to the derivation via food-chain modelling of the so-called critical soil cadmium concentration and the comparison of the predicted future soil concentrations with this threshold.

### The so-called Targeted  Risk Assessment on cadmium as used in batteries

This study previously presented as stand-alone document and shortly called TRAR on batteries, is focused on assessing the risks for the environment of cadmium as used in Ni-Cd batteries over different life cycle stages such as manufacturing, recycling and disposal. Guidance on how to estimate the emissions from the waste disposal stage is not provided within the Technical Guidance Document (TGD, 1996). The revised TGD includes some sections on waste disposal but no specific guidance is given on how to quantify these emissions.  A full assessment of cadmium from Ni-Cd batteries from the waste life cycle stage is thus not included. This section gives an overview of the concern areas that have been assessed in the present TRAR/batteries’ related (sub)sections and which areas that have not been dealt with, either because of lack of methodology  or because those areas are regarded as being outside the scope of the study.

Emissions of the disposal phase were quantified for Municipal Solid Waste (MSW) landfills and MSW incinerators only where the contribution of sealed portable Ni-Cd batteries to the waste stream have been considered. Industrial Ni-Cd batteries, representing 20 % of the cadmium used in Ni-Cd batteries, are recycled and/or disposed off in industrial landfills. The emissions related to the disposal of industrial Ni-Cd batteries i.e. via industrial landfills and hazardous waste incinerators are not addressed in this report.

Quantifying the specific cadmium emissions caused by landfills or incineration of Ni-Cd batteries is hampered by the fact that available data on landfill and incineration emissions always represent the total emissions of cadmium containing materials present in the waste stream. Therefore the total cadmium emissions were calculated first. By using a specific allocation key specific contribution of Ni-Cd batteries to the overall cadmium emission/risk could be quantified. Since waste management strategies may differ considerably between the Member States, due consideration is given to these differences by means of including several scenarios (with the extremes: 100 % landfilling and 100 % incineration).

Main emissions of cadmium from incineration of waste are expected to occur through air and the disposal and/or re-use of incineration residues (bottom ash and fly ash). The re-use and/or landfilling of incineration residues may result in a long-term diffuse emission potentially contaminating groundwater, surface water and soil. Neither the delayed cadmium emissions of the re-use of incineration residues nor the impact of future expected increase in cadmium content of bottom ash and fly ash on the re-usability of these incineration residues have been quantified. The major environmental concerns associated with metals in landfills are usually related to the generation and eventual discharge of leachate into the environment. The risks associated with the discharge of these leachates in surface water have been quantified. The contamination of the groundwater compartment due to fugitive emissions of landfills has been quantified in this report but no risk characterisation on this compartment has been performed

If Ni-Cd batteries cannot be collected efficaciously, the future cadmium content in the MSW is predicted to increase. The impact of this potential increase on future emissions has been assessed for MSW incineration only. The impact of a future change in the MSW composition on the composition of the leachate of a landfill could not be judged based on the current lack of knowledge and methodology. The contribution of Ni-Cd batteries on the overall cadmium content is calculated for a worst case scenario where only 10 % of the Ni-Cd batteries is being collected and a scenario in which 75 % of the Ni-Cd batteries is being collected.

Within the approach used in the TRAR/batteries’ related (sub)sections to estimate the cadmium emissions associated with  waste management strategies such as landfilling and incinerations different assumptions have been made that lack validation due to the limited availability of data on this subject. Although due to this paucity of data it is sometimes difficult to really judge if all assumptions taken are indeed worst case, as a general premise it was tried to use reasonable worst case conditions (based on expert judgement) to perform the calculations . In other cases average values were used instead of worst case estimates in order to conserve the environmental realisms of the estimates. Table 3.3.9 in section 3.3.3.1 provides an overview of the assumptions and default values taken in this report and the associated level of conservatism introduced with them.

However, by means of a rudimentary sensitivity analysis an attempt was made to determine the key parameters having an effect on the overall results.

An overview of the different scenarios for the disposal phase investigated in the TRAR/batteries’ related (sub)sections of this report is given in section 5, figure 5.1. The risk assessment for the waste life cycle step was made in a comparative way meaning that the risks of the total cadmium was compared with the risks of the total cadmium without Ni-Cd batteries.

### Update assessment for site-specific exposure data (reference year 2002)

The update report provides a re-assessment of the risks of the two priority substances cadmium metal and cadmium oxide on the basis of new emission information collected from cadmium and cadmium oxide production and processing industries (i.e. cadmium metal production, cadmium oxide production, production and recycling of Ni-Cd batteries, production of cadmium containing pigments, production of cadmium containing stabilisers) for the reference year 2002. Concerning the use of Cd/CdO in alloys, plating and other uses, no update information was submitted to the Rapporteur.

Since the finalisation of the final overall Cd/CdO ENV RA report (July 2003) for submission to SCTEE, a number of updates were made regards the identity of the producing facilities and the produced amounts of each of the priority substances. The number of Cd metal and Cd oxide producing plants reduced from 14 in 1996 to 4 in 2002. The total number of processing plants participating in the update exercise by submitting new exposure data is 13 compared to 23 in 1996. Next to the closures of companies in this time period and the stopping of cadmium related processes, improvements in air and water emission measures have been made by several companies, thus resulting in a reduction of the total site emissions.

In the update document, re-assessments have been made of PEClocals for different environmental compartments on the basis of update emission information for specific sites while the PECs regional and the PNEC values were extracted from the overall Cd/CdO RAR (July 2005), now included in the same and present integrated report under section 3.2.

## overall conclusions for environment: cadmium oxide and cadmium metal

# Remark:

General scope and limitations cfr herebefore.

No assessment could be done for the atmosphere.

No assessment for the marine environment is included.

(X)	i)	There is a need for further information and/or testing

For the aquatic compartment, there is a need for better information regarding the toxic effects of cadmium to aquatic organisms under low water hardness conditions.

In particular, information is required on:

- Cd toxicity testing in very soft waters (H below about 10mg CaCO3/L). There are no data for the very soft waters and these areas may be unprotected by the proposed PNECwater for soft water (0.08 µg Cd/L).

For sediment, there is a need for further information regarding the bioavailability of cadmium in order to possibly refine the assessment at regional and local level.

In particular:

- the AVS and OC normalisation should be further validated (cfr outcome of concl i) program, see separate document: ‘RAR Stage II’)

(X)	ii)	There is at present no need for further information and/or testing and for risk reduction measures beyond those which are being applied already

This conclusion applies to the assessment of:

- the local surface water compartment for the CdO production site, for some NiCd batteries production sites (6 and 7) and one NiCd recycling site (site 2) because there are no emissions to water at these sites.

- the local surface water compartment for the Cd metal production site 6, NiCd battery producing sites (2, 3 and 4), Cd piments producing site B and all (two) Cd stabilizer production sites (X, Y) emitting to the aquatic compartment.

- the local surface water compartment for a hypothetical landfill currently releasing a leachate with 5 µg/L of cadmium directly or indirectly in the aquatic environmen, and for current hypothetical incinerator (equipped with an on-site WWTP) discharging total Cd emissions in a river with a dilution factor of 100  to 1,000. Removal of Ni-Cd batteries in the MSW has a negligible influence on the calculated risk ratios.

- no risk is predicted for the local sediment compartment for the CdO production site, some NiCd batteries producers (site 6 and 7) and NiCd recycler plant 2 because there are no emissions to water and no additional risk arises from their operations.

- no risk is predicted for the micro-organsims in the off-site STP for Cd stabilizer production site (X) discharging its effluents to a municipal STP, for the hypothetical landfill site discharging a leachate with a cadmium concentration of 5µg/L to a STP and for the hypothetical incinerator plant (equipped with an on-site WWTP) discharging to a STP.

- modelled local soil Cd concentrations for Cd metal production, CdO production and processing/user i.e. stabilizers and pigments production plants, NiCd batteries producing and recycling plants and hypothetical MSW incineration plant (equipped with an on-site WWTP) (10 years aerial deposition) indicate no risks neither for the terrestrial compartment nor for secondary poisoning.

- modelled regional soil Cd concentrations that include natural soil, industrial soil and 8 different agricultural scenario’s are all below the PNECsoil. All these modelled values are total concentrations that are expected after 60 years (agricultural soils) or far beyond that (natural and industrial soils) with current regional emissions to soil. The starting concentrations are EU average values for the ambient concentrations. If 90th percentiles of measured concentrations would have been used in such calculations , then risk cannot be excluded.

- secondary poisoning as field data (body burden: kidney and liver Cd data) of birds (excluding pelagic birds) do not indicate Cd poisoning, even in top predators. No risk to mammals is predicted from modelled regional soil Cd concentrations.

(X)	iii)	There is a need for limiting the risks; risk reduction measures which are already being applied shall be taken into account

This conclusion applies to the assessment of: (still to update for Nov 2005 version!)

- the local surface water at 1 Cd metal production site (site 1), and 4 processing ( pigments production sites (A and C), plating and alloy) sites/scenarios. Both latter are generic scenarios (‘Cd plating’ and ‘Cd alloys’). Local concentrations are based on modelling using standard default values and could possibly have been refined if substantial monitoring data would have been provided. Monitoring data are available for the Cd metal production site 1: these data indicate risk at background level but do not allow a judgment regarding potential additional risk caused by the site’s operations.

- the local surface water at one NiCd batteries recycling site where modelled freshwater Cd concentrations exceed the PNECwater. This risk would be removed if no assessment factor (i.e. 2 and reflecting most of the uncertainty) is applied in deriving the PNEC. Monitoring data are available for this site: these data indicate risk at background level but do not allow a judgment regarding potential additional risk caused by the site’s operations.

- the modelled regional PEC of surface water has a risk factor of 0.6 using a mean Kp value for EU while the risk factor is 1.7 using a Kp value that is distinctly smaller than average. This suggests potential regional risk. However, it is proposed to use measured values for the risk characterization because of the uncertainties in the choice of the natural background (which is combined with the added concentration to derive the regional PEC) and in the coverage of the surface water with small Kp values. Monitoring data were collected for 13 EU countries (of the EU-16 surveyed) but limitation in data quality (detection limit, geographical coverage etc.) reduced this information to 8 countries (as proxy for regions) for which conclusions can be derived. The regional averages of 90th percentiles of measured Cd concentrations of European rivers and lakes in these regions range from 0.2 to 3.5). The majority of regional averaged 90th percentiles have a risk factor < 1 whereas these values are >1 in the UK (based on a limited dataset of 1996) and the Walloon region of Belgium. Outliers have a large impact on the risk factors as, for example, 20 sites of the 728 investigated in the largest database of UK (data of 2003) determine risk in UK. The PNEC for water was derived with an assessment factor of 2 reflecting most of the uncertainties in the effects assessment. The conclusions about risk in the regions mentioned is not affected by either in- or excluding this assessment factor. During the development of the RRS, decision about (possible) reduction measures has to take into account the information on potential cadmium emission sources in these regions. In order to better characterise the regional risks to surface water in part of the EU which have not been covered in this assessment (i.e. eastern and southern Europe are underrepresented in the entire dataset, because detection limits are often too high and because fractionation is often not reported) it might be useful to obtain more information for these regions. It may be that the foreseen monitoring actions under for example the Water Framework Directive will provide this information in the future.

- the local terrestrial compartment: there are potential risks at cadmium plating and alloy production sites.

- the regional terrestrial ecosystem: the 90th percentiles of measured Cd concentrations of European soils have risk factors 0.4-1.6 (mean: 0.86; data from 6 EU countries). Regional risk for the terrestrial ecosystem cannot be excluded in one region (UK). However, it should be noted that the 90th percentile for the UK falls within the range of the proposed PNECsoil based on direct toxicity to soil microbial processes (see Table 3.3.1). Hence risk cannot be excluded but will depend on the magnitude of the assessment factor chosen (either 1 or 2, see 3.2.2.7) in the derivation of the PNECsoil.

- the secondary poisoning (regional level) as measured soil Cd concentrations of European soils have risk factors 0.4-1.6 for poisoning to mammals (mean: 0.86; data from 6 EU countries). Regional risk for the terrestrial ecosystem cannot be excluded in one region (UK). The uncertainty surrounding the effects assessment, however, suggests that this is a borderline situation: the available information shows that literature data on Cd uptake in mammals dwelling in acid soils sensitively influences the effects assessment. If data on acid soils (pH <4.2) are excluded from the effects assessment, a larger PNEC is obtained and risk in the UK would be excluded. That conclusion would only remove concern provided that the P90 value in UK does not refer to acid soils, which is unknown. This analysis is, morever, qualitatively because there is no validated model to estimate risk to mammals along the entire range of soil pH.

- the wastewater treatment plants: as risk is predicted for the micro-organisms of the STP for the NiCd battery recycling plant (site 2) discharging its effluent to an off-site STP. Risk to on-site and off-site STP cannot be excluded for Cd plating and alloy industry.

## overall conclusions for human health

See separate document.

# GENERAL SUBSTANCE INFORMATION

As much of the (eco)toxicological information on Cadmium metal is derived from Cadmium oxide (and other cadmium compounds), and as a close relationship exists between both priority substances (cfr mass-balance) it was proposed that both RARs should be merged for the sections 1 to 4 with exception of the risk characterization in the Human Health part where for each substance a separate section on risk characterization and conclusions should be developed.

Primary source of information for this section and more particularly sections 1.1, 1.2 and 1.3, was the ‘ANNEX VIIA’ document provided by Industry (Lead-company) in 1997 as a background document and complement to the HEDSETs.

## Identification of the substance

| CAS-n°: | 7440-43-9 | 1306-19-0 |
| --- | --- | --- |
| EINECS-n°: | 231-152-8 | 215-146-2 |
| IUPAC name: | Cadmium | Cadmium oxide |
| Synonyms: | Not applicable | Not applicable |
| Molecular formula: | Cd | CdO |
| Atomic weight: | 112.41 (several naturally-occurring isotopes ranging from 106-116 (Lexicon, 1972; WHO, 1992) |  |
| Molecular weight |  | 128.41 |
| Color | blue-white (Sax and Lewis, in: ATSDR, 1998) | varies from greenish-yellow through brown to nearly black, depending on the thermal history (due to lattice defects) and on the particle size |

## Purity/impurities, additives

|  | Cadmium | Cadmium oxide |
| --- | --- | --- |
| Purity (powder): | Min. 99.9% | min. 99.999% (Annex VIIA, 1997) |
| Purity (massive): | Min. 99.99% |  |
| Impurities (max.): | for 99.99% Cd metal: Fe: 10 ppm; Cu: 20 ppm; Ni: 10 ppm; Pb: 100 ppm; Zn: 30 ppm, Th: 35 ppm. Other levels are specified for other purity grades. (ASTM B440-00) | n.a. powder reagent grade: max. chloride 0,002%; nitrate 0,01%; sulphate 0,20%; copper 0,005%; iron 0,002%; lead 0,01% (JT Baker chemical Co, 1984) |
| Additives: | none | none |

Remark: it is stated that the purity levels and chemical analyses indicated here are purely arbitrary as many grades of both cadmium metal and cadmium oxide exist. It is recommended that the ranges or specifications should be listed using the appropriate ISO or EN standards (ICdA, com. 2003). However, only the ASTM standard was provided for Cd metal grades 99.95, 99.99 and 99.995%.

## Physico-chemical properties

|  | Cadmium | Cadmium oxide |
| --- | --- | --- |
| Physical state: | solid (massive or powder) | solid (powder) |
| Crystal structure: | distorted hexagonal close-packed | cubic structure with each ion surrounded by six ions of opposite electric charge, octahedrally arranged. Also an amorphous form exists: stable at lower temperatures, forming crystals of the cubic type at red heat |
| Melting point: | 320,9 °C (Lexicon, 1972, Sax & Lewis: in ATSDR, 1998;CRC: in Annex VIIA, 1997) | Decomposes at 900-1000 °C (CRC, 1985; Annex VIIA, 1997) |
| Boiling point: | 765 °C (idem); 767 °C (Sax & Lewis: in ATSDR, 1998) | CdO is non-fusible but volatilizes at high temperature. Sublimation at 1559°C |
| Relative density: | 8.64 g/cm3 (Lexicon, 1972, Sax & Lewis: in ATSDR, 1998: analysis by WIAUX S.A., in LISEC, 1998e). | 8.15 g/cm3 (cubic form); 6.95 g/cm3 (amorphous) (EPA 1985). |
| Vapour pressure: | 1 mmHg at 394 °C (Sax & Lewis: in ATSDR, 1998 133 hPa at 394 °C (CRC, in: Annex VIIA, 1997) | 1 mmHg at 1000 °C (Sax, N.I., 1984) |
| Water solubility: | quoted as ‘insoluble’ (The Merck index; in: ATSDR, 1998; CRC, in: Annex VIIA, 1997). However it was mentioned: 0,05 mg/1 at pH 10,5 a curve in function of pH and hardness: at pH 7: solubility is 10 to 100 times higher than at pH 8.5 dependent on the total carbonate concentration (M. Farnsworth, 1980). Measured dissolved cadmium concentrations after 7 days transformation/dissolution test with cadmium metal powder at loading 1 – 100 mg/l, were in the range 0.192 – 0.135 mg/l (at pH +/- 8) (LISEC, 1998e). | quoted as ‘insoluble’ However measured dissolved cadmium concentrations after 7 days transformation/dissolution test with cadmium oxide powder at loading 1 – 100 mg/l were in the range 0.095 – 0.227 mg/l (at pH +/- 8) (LISEC, 1998f). Soluble in acids and solutions of ammonium salts (Farnsworth, 1980). |
| Partition coëfficient: | No data | No data |
| n-octanol/water(log-value): | Not applicable | Not applicable |
| Flammability: | Slight fire hazard. The finely divided metal may be pyrophoric in air (MSDS, 1992; Annex VIIA, 1997)* GLP testing conform EC Testing methods A.10, A.12 and A.13 (BAM, 2002): Cadmium metal ‘powder’ [particle size distribution (in volume-%): d(0.1): 3.462µm; d(0.5): 7.154µm; d(0.9): 14.117µm; mean water content: 0.03] and cadmium ‘fine billes’ [particle size distribution (in volume-%): d(0.1): 2.485µm; d(0.5): 7.040µm; d(0.9): 15.753µm; mean water content: 0.05] are not flammable and do not have pyrophoric properties in sense of the EC-methods, Dir. 92/69/EEC. | Not flammable |
| Explosive properties: | Dust/air mixture may be explosive. Even as fine powder, cadmium is hardly explosive (MSDS, 1992; INRS, 1987) |  |
| Self-ignition: | Not applicable | Not applicable |
| Oxidizing properties: | Not applicable | Not applicable |
| Granulometry: | The average spherical diameter of cadmium powder prepared by distillation is about 18 µm +/- 13.3 µm (S.D.) (inhalable fraction) and the specific surface area : 580.4 cm2/g (analysis by WIAUX S.A., in: LISEC, 1998e). Particle size and surface area depend very much upon the specific process and specific application. For example, INMETCO produces a cadmium metal shot which is many times larger than the aforementioned cadmium metal powder (ICdA, com. 2003). See also remark related to flammability testing. | The average spherical diameter of CdO powder prepared by oxidation of Cd metal is about 0.55 µm (respirable fraction) (La Floridienne, 1997). Particle size and surface area depend very much upon the specific process and specific application (ICdA, com. 2003). |
| Odour treshold: | No data | No data |
| Ionisation potential: | E°Cd/Cd2+ = 0.4025 eV (= fairly reactive) |  |
| Caloric value | 0.16 Cal/g |  |

* the Rapporteur requested appropriate testing related to flammability, that was supported by the TM and it was adviced to extend to testing on pyrophoric properties (tests A.10, A.12 and A.13 according to Directive 92/69/EEC; under well-defined conditions) and sent for information/approval to the C&L Working Group, 14.01.2002.

GLP testing on flammability and pyrophoric properties of the products, Cadmium metal powder and Cadmium ‘fine billes’ according to the EC Methods A.10, A.12 and A.13 was performed by Industry (ICdA) on a voluntary basis (final report of BAM, October 2002). The substances are not flammable and do not have pyrophoric properties in sense of the EC-methods, Dir. 92/69/EEC and are thus not to be classified (and labelled) related to these properties.

The grade Cadmium ‘fines billes’ is stated as being the finest grade of Cadmium ‘powder’ from current EU manufacturing that is put on the market (since 2001). However, other qualities may be manufactured elsewhere e.g. in Japan and China (ICdA, pers. com. 2003).

The physical, thermal, electrical, magnetic, optical, and nuclear properties of cadmium metal are summarized by Morrow (2001), however without indication of testing specifications or the primary source. Where available, this source confirms the aforementioned entries for physico-chemical properties.

## CLASSIFICATION

### Classification at the start of the risk assessment

# Cadmium metal

- Classification: not yet classified

Remark: (some) cadmium compounds fall under the Directive 67/548/EEC and are classified and labelled according to the 15th ATP.

# Industry proposes: Xn; R20/21/22 (MSDS, 1995)

# Cadmium oxide

- Classification according to Annex I (15th ATP):

Human health:

Carc. Cat2; R49		May cause cancer by inhalation

T; R48/23/25	Toxic: danger of serious damage to health by prolonged exposure through inhalation and if swallowed

Xn; R22 				Harmful if swallowed

Note E

# S53-45: 				Avoid exposure - obtain special instructions before use

In case of accident or if you feel unwell, seek medical advice (show the label where possible)

# Environment: not (yet) classified

### Proposed classification

#### ENVIRONMENTAL CLASSIFICATION AND LABELLING

##### Introduction

A general introduction and description of the strategy on classification and labelling of insoluble and sparingly soluble metals, including the dissolution test and the criteria for classification is given in the RAR on zinc metal (see pre-Draft November 1998).

It should be noted that the ‘critical surface approach’ as suggested in OECD context is not (yet) considered in the reports on neither cadmium metal nor cadmium oxide.

##### Dissolution test results

# Cadmium metal: powder form

A transformation/dissolution test report  (LISEC, 1998e) conform to the recommended EU full test protocol is available for cadmium metal powder (smallest representative particle size on the market). This test is conducted with cadmium powder from Wiaux S.A. in a modified ISO 6341 medium. The selection of the test pH (+/- 8) may be criticised: the solubility of cadmium is higher at lower pH (see under point 1.3; M. Farnsworth, 1980). This derivation however, does not affect the outcome of classification.

The test parameters and results of the tests in the LISEC-report are presented in Annex 1.4.2.B The parameters which deviated from the recommended dissolution test are also indicated in Annex 1.4.2.A

The test results are briefly described below.

The dissolved metal concentration after 7 days and 28 days, which corresponds with the duration of a full test, is taken into consideration for classification. Concentrations were measured. Results are shown in Table 1.4.2.1. At 100 mg/l it was not possible to determine the transformation/dissolution kinetics of the metal powder even in pH buffered test medium (test no. 3 at pH+/-8). At that loading the maximal dissolved concentration was observed after 3 - 4 hours (1.50 - 1.74 mg Cd/l). Thereafter a decrease was observed that could not be related to measured variation of environmental co-variables such as temperature, pH or dissolved oxygen.

At 1 mg/l loading rate, the dissolved cadmium concentration increased with time and arrived at an apparent steady-state equilibrium after 28 days.

The dissolved cadmium concentration increased with an increasing mass loading. The fraction dissolved versus loading rate is however lower at higher loading: maximum 1.7% at 100 mg/l and 17% at 1mg/l loading rate.

The results of the 1 mg/l test – the short term dissolution value (0.1923 mg/l) as well as the long term value (0.1985 mg/l) - are used for classifcation of the powder.

Table 1.4.2.1 Measured dissolved cadmium concentration (in mg/l) after 7 and 28 days, respectively, at loading rates of 1 and 100 mg/l (LISEC, 1998e).

| Cadmium powder WIAUX Particle size: 14.9 mm1 | Measured concentration after 7 days (+/- S.D.) and pH | Measured concentration after 28 days |
| --- | --- | --- |
| Loading rate (mg/l) |  |  |
| 1 | 0.192 (+/-0.0019) at pH 7.95 +/- 0.07 | 0.198 |
| 100 | 0.0202 (+/-0.005) at pH 9.64 +/- 0.01 |  |
| 100 (pH +/-8) | 0.1352 (+/-0.026) at pH 7.99 +/- 0.02 | - |

1. Tests were conducted in sterilised and filtered modified ISO 6341 medium (dissolved Cd concentration < 0.0012mg/l).

2. Large variations in the measured dissolved cadmium concentrations were observed. Hence, the results could not be fitted neither in a first nor second order model.

# Cadmium metal: massive form

A 7-days transformation/dissolution test report  (LISEC, 2002) is available for massive cadmium metal ‘shot’ (presumably the smallest representative particle size during manufacturing and use). The selection of the test pH (+/- 8) may be criticised: the solubility of cadmium is higher at lower pH (see under point 1.3; M. Farnsworth, 1980). Another deviation concerns the fact that not all prescribed loading rates were tested (the lowest loading rate prescribed by the test protocol, 1 mg/l, is missing).

The test parameters and results of the tests in the LISEC-report are presented in Annex 1.4.2.D. The parameters which deviated from the recommended dissolution test (OECD Guidance Document, April 2001) are indicated in Annex 1.4.2.C.

The test results are briefly described below.

The dissolved metal concentration after 7 days from the lowest to the highest loading rate are taken into consideration for classification. Concentrations were measured. Results are shown in Table 1.4.2.2. At none of the tested loadings it was possible to determine the transformation/dissolution kinetics of the metal shot. Within and between vessels’ variability was high (resp. exceeding 10% and 20%). This variability was considered – by the testing lab director – to be probably attributable to the different forms of the tested material. The Table 1.4.2.2. therefore reports the disssolved cadmium concentrations of the individual vessels. Alkalinity and hardness of the medium were not measured at the end of the test.

At the different loadings (resp. 10, 50 and 100 mg/l) the concentrations after 7 days testing are interpreted as almost reaching an equilibrium resp. in 2 of the 3 vessels (10 mg/l), not reaching an equilibrium in 2 of the 3 vessels (3rd vessel no conclusions can be drawn at 50 mg/l) and none of the vessels reaching an equilibrium at the highest loading rate (100 mg/l).

The dissolved cadmium concentration tends to increase with an increasing mass loading.

Overall the reliability of the test is (very) low. Nevertheless the overall results of the tests are used as starting point for the classifcation of massive cadmium metal.

Table 1.4.2.2 Measured dissolved cadmium concentration (in mg/l) after 7 days, respectively, at loading rates of 10, 50 and 100 mg/l (LISEC, 2001).

| Cadmium ‘shot’ Particle size: approx. 2.4 +/- 0.2 mm1 | Measured concentrations2 and standard deviation in the individual test vessels, after 7 days |
| --- | --- |
| Loading rate (mg/l) |  |
| 10 | 0.1375 (0.0049); 0.0294 (0.0008); 0.0196 (0.0001) |
| 50 | 0.0369 (0.0001); 0.0181 (0.0001); 0.0121 (0.0002) |
| 100 (pH +/-8) | 0.0418 (0.0013); 0.0401 (0.0011); 0.0212 (0.0000) |

1. Tests were conducted in sterilised (filtered: 0.2 µm) ISO 6341 medium (dissolved Cd concentration < 0.0012mg/l).

2. Large variations in the measured dissolved cadmium concentrations were observed within and between the individual vessels at the same loading rate and sampling time. Hence, the overall results per sampling time could not be fitted neither in a first nor a second order model.

# Cadmium oxide: powder

A transformation/dissolution test report  (LISEC, 1998f) conform to the recommended EU full test protocol is available for cadmium oxide powder (presumably smallest representative particle size on the market). This test is conducted with cadmium oxide powder (batch n°: CDO_007) in a modified ISO 6341 medium. The selection of the test pH (+/- 8) may be criticised: indeed, the solubility of cadmium oxide might be higher at a lower pH (see section 1.3). This derivation however, does not affect the outcome of classification.

The test parameters and results of the tests in the LISEC-report are presented in Annex 1.4.2.F The parameters which deviated from the recommended dissolution test are also indicated in Annex 1.4.2.E.

The test results are briefly described below.

The dissolved metal concentration after 7 days and 28 days, which corresponds with the duration of a full test, is taken into consideration for classification. Concentrations were both measured and calculated with a fitting model. Results are shown in Table 1.4.2.3. At 100 mg/l it was not possible to determine the transformation/dissolution kinetics of the cadmium oxide powder. At that loading the maximal dissolved concentration was observed after 4 hours (1.075mg Cd/l). Thereafter a decrease was observed. The alkalinity and hardness of the medium were not measured at the end of the test.

At 1 mg/l loading rate, the dissolved cadmium concentration increased with time and reached an apparent steady-state equilibrium after +/- 7 days of testing.

With increasing mass loading, the dissolved cadmium concentration increased. However, the fraction dissolved versus loading rate is lower at higher loading: maximum 1% at 100mg CdO/l and 11% at 1mg CdO/l loading rate.

# The results of the 1 mg/l test are used for classifcation of the powder.

Table 1.4.2.3 Measured dissolved cadmium concentration (in mg/l) after 7 and 28 days, respectively, at loading rates of 1 and 100 mg CdO/l (LISEC, 1998f).

| Cadmium oxide powder Mean particle size: 14.9 mm1 | Measured concentration after 7 days (+/- S.D.) and pH | Measured concentration after 28 days |
| --- | --- | --- |
| Loading rate (mg CdO/l) |  |  |
| 1 | 0.095 (+/- 0.004) pH 8.27 +/- 0.02 | 0.094 |
| 100 | 0.2272 (+/- 0.062) pH 8.51 +/_0.01 | - |

# 1. Test were conducted in sterilised and filtered modified ISO 6341 medium (dissolved cadmium concentration < 0.0012mg/l).

# 2. Large variations in the measured dissolved cadmium concentrations were observed. Hence, the results could not be fitted neither in a first nor a second order model.

##### Result short-term toxicity tests

# Cadmium metal

Several short-term toxicity tests were performed on metallic cadmium (powder). The majority of these tests are, however, performed at higher hardness than that of the medium in which the transformation was measured. One test was performed on the dissolution test solution and comparable conditions (cfr LISEC test n° 1, 1998a). The outcome of the latter test is used in the classification context: EbC50, 72h growth inhibition (cell number) on green algae: 23µg Cd/l. The ErC50, 72h growth rate inhibition: 89 µg/l, value extrapolated outside the range of tested concentrations. The NOECs for growth and growth rate (expressed as initial concentrations) are 2.5 and 9.5µg/l respectively (expressed in measured end concentration: NOEC < or = 1.25µg Cd/l).

Moreover, a base-set of L(E)C50/NOEC values of soluble cadmium salts are presented in Section 3 of the risk assessment report on cadmium oxide. Many L(E)C50/NOEC values are found below resp.0.1mg Cd/l and 1µg Cd/l (see Table 3.2.7).

# Cadmium oxide

Several short-term toxicity tests were performed on cadmium oxide powder. The majority of these tests were performed at higher hardness than that of the medium in which the transformation was tested. One test was performed on dissolution test solution and comparable conditions (LISEC, 1998b). The latter test is identified as key test and will be used as starting point for the purpose of classification. The EC50 for unicellular algae (S. capricornutum) is 0.018 mg Cd/l and the EC50 for growth rate is 0.079 mg Cd/l. These concentrations are lower than the dissolved concentration at a loading of 1 mg CdO/l.

Moreover, a base-set of L(E)C50 and NOEC values of soluble cadmium salts is presented in Section 3 with many L(E)C50/NOEC values below resp. 0.1mg Cd/l and 1µg Cd/l (Table 3.2.7).

##### Conclusion and discussion

# Cadmium metal: powder

The measured dissolved cadmium concentration after 7 days at a loading rate of 1 mg/l is 0.192mg/l and exceeds the lowest 72-hour EbC50 for algae (0.02mg Cd/l, dissolved fraction; test performed on metallic cadmium and under comparable test conditions as in the dissolution test). On the basis of this result, and supported by other acute and chronic toxicity test results on cadmium salts (see Section 3, Table 3.2.7.), cadmium powder will be classified with N; R50-R53.

The LISEC test deviation in pH, when corrected (= lowered), would obviously have resulted in increased dissolved cadmium ion concentrations. Given that the actual proposal is the most stringent classification that is possible, the overall conclusion for the classification and labelling of cadmium would be maintained.

# Metallic cadmium in massive form

Although the poor reliability of the recently conducted transformation/dissolution test, it is seen that the overall lowest measured cadmium concentrations at any loading rate and any sampling time are exceeding the available lowest (acute) toxicity test results on aquatic organisms (cfr Table 3.2.7). Indeed, the lowest measured concentrations on individual vessel basis after 7 days for the different tested loadings, 10 mg/l, 50 mg/l and 100 mg/l were resp. 0.0196 mg/l at pH 8.06, 0.0121 mg/l at pH 7.97 and 0.0212 mg/l at pH 7.93 (means per sampling time i.e. 7 days: at 10 mg/l: 0.0621+/- 0.0586 (+/- S.D.) at pH 8.10+/-0.04; 50 mg/l: 0.0223+/-0.0116 at pH 7.98+/-0.02; 100 mg/l: 0.0344+/-0.0103) at pH 7.93+/-0.00. The values after 2 hours of testing were resp. 0.0026 mg/l at pH 8.26, 0.0036 mg/l at pH 8.18 and 0.0043 mg/l at pH 8.14 (means per sampling time i.e. 2 h.: at 10 mg/l: 0.0027+/-0.0001 at pH 8.24+/-0.04; 50 mg/l: 0.0043+/-0.0011 at pH 8.19+/-0.01; 100 mg/l: 0.0051+/-0.0005 (+/- S.D.) at pH 8.12+/-0.02.

On this basis, it is proposed to classify massive cadmium with N; R50-R53 unless the results of new adequate testing gives prove of the contrary.

# Cadmium oxide

The measured and calculated dissolved cadmium concentration after 7 days at a loading rate of 1 mg/l exceeds the ErC50, 72h for algae (18µg Cd/l) as well as the EbC50, 72h for algae (79µg Cd/l). On the basis of these results cadmium oxide will be classified with N; R50 - R53.

This proposal is further supported by many other L(E)C50 and NOEC values found in the cadmium concentration range 0.1 mg Cd/l – 1 µg Cd/l and below (see Table 3.2.7 in Section 3).

The LISEC test deviation in pH, when corrected (= lowered), would obviously have resulted in increased dissolved cadmium concentrations. Given that the actual proposal is the most stringent classification that is possible, the overall conclusion for the classification and labelling of cadmium oxide would not be altered.

##### Overall classification for the environment as proposed by the rapporteur

# Cadmium metal

- Classification : not yet classified for the environment.

- Proposal of the rapporteur: 	cadmium powder: N; R50-53 and S60, S61

cadmium in massive form: N; R50-53 and S60, S61

# Cadmium oxide

- Classification according to Annex I: not (yet) classified.

- Proposal of the rapporteur: N; R50-R53 and S60, S61

##### Classification for the environment – proposal for Annex I adaptation

# Cadmium metal

Decided by the C&L ENV WG:

cadmium powder: N; R50-53 (ECBI/82/00-Rev. 1)

cadmium in massive form: N; R50-53 (ECBI/37/02-Rev. 2)

# Cadmium oxide

Decided by the C&L ENV WG:

cadmium powder: N; R50-53 (ECBI/82/00-Rev. 1)

#### classification and labelling: human health

##### Completeness of the base-set (Annex VIIA Dir. 67/548/EEC)

# Cadmium metal and Cadmium oxide:

The base-set Annex VII requirements are not fulfilled.

The need for further base-set testing on toxicological properties as tentatively requested by the Rapporteur was not supported by the TM. The reasons for objecting to the proposal were: a) Cadmium oxide has an Annex I entry as Carc. Cat. 2 (by inhalation) that is confirmed by the current RAR and presumes sufficient risk reduction measures to be (put) in place as to also protect humans from the impacts of the acute effects on skin and eye (irritation and sensitization), b) arguments of animal welfare, c) lateness of the request in the evaluation process and d) the unlikeness for sensitizing effects to occur in humans on the basis of the evidence gained at the workplace.

# The request on flammability/pyrophoric properties was supported (cfr section  1.3).

Furthermore, for Cadmium metal cross-reading from the data-set on Cadmium oxide was approved in general. This results in a classification and labelling proposal being identical at least for what concerns the toxicological properties.

##### The Rapporteur’s proposal for classification:

# Cadmium metal

Carc. Cat2; R49		May cause cancer by inhalation

T; R48/23/25	Toxic: danger of serious damage to health by prolonged exposure through inhalation and if swallowed

# T; R23/25

[Xi. R37 			Irritating to respiratory system]

Muta. Cat3 ; R68		Possible risk of irreversible effects

Repro.Cat3; R62		Possible risk of impaired fertility

# Note F

# S53-45: 				Avoid exposure - obtain special instructions before use

In case of accident or if you feel unwell, seek medical advice (show the label where possible)

# Cadmium oxide

Carc. Cat2; R49  		May cause cancer by inhalation

T; R48/23/25  	Toxic: danger of serious damage to health by prolonged exposure through inhalation and if swallowed

# T; R23/25

[Xi. R37 			Irritating to respiratory system]

Muta. Cat3 ; R68		Possible risk of irreversible effects

Repro. Cat3; R62		Possible risk of impaired fertility

# Note F

# S53-45: 				Avoid exposure - obtain special instructions before use

In case of accident or if you feel unwell, seek medical advice (show the label where possible)

##### The decision of the CMR WG:

The classification of Cadmium metal and Cadmium oxide has been reviewed by the CMR WG during 2002.

The CMR WG (Jan. ’03) decided to classify Cd metal and CdO as follows and this decision will be included in the draft proposal for the 29th ATP of Annex I (ECBI/30/03 (draft); IPH, pers. com. 2003).

Cadmium (metal)

048-011-00-X (pyrophoric) 	T; R48/23/25

T+; R26

F;R10

Car.Cat.2, R45

Muta.Cat.3, R68

Repr.Cat.3; R62-63

Nota E

Cadmium (metal) [1] and cadmium oxide [2]

048-002-00-0 (non-pyrophoric)

# T; R48/23/25

# T+; R26

Car.Cat.2, R45

Muta.Cat.3, R68

Repr.Cat.3; R62-63

Nota E

### current classification as in annex i

Cadmium (metal) (pyrophoric)

048-011-00-X 		 	T; R48/23/25

T+; R26

F; R17

Car.Cat.2, R45

Muta.Cat.3, R68

Repr.Cat.3; R62-63

Nota E

Labelling:				F; T+; N

R: 45-17-26-48/23/25-62-63-68-50/53

S: 53-45-7/8-43-60-61

Cadmium (metal) (non-pyrophoric) [1]

Cadmium oxide (non-pyrophoric) [2]

048-002-00-0

# T ; R48/23/25

# T+ ; R26

# N ; R50-53

Car.Cat.2, R45

Muta.Cat.3, R68

Repr.Cat.3; R62-63

Nota E

Labelling:

T+; N

R: 45-26-48/23/25-62-63-68-50/53

S: 53-45-60-61

Source : EC, 2004b (O.J. L216, p.3 16/06/04).

# GENERAL INFORMATION ON EXPOSURE

## Production

# Cadmium metal

Cadmium is a naturally occurring element with ubiquitous distribution. Although cadmium ores also exist (greenockite) these are not commercially important. Zinc (sulphide) ores are the primary source for cadmium production. Smaller amounts of cadmium are produced during the production of other non-ferrous metals such as lead. In the refining of these ores cadmium is obtained as a by-product (Technical notes on cadmium, 1991).

Whereas the extraction and refining of the primary non-ferrous metal from the ores can be obtained either by pyrometallurgical or electrolytic processes, the final step of cadmium production is done by fractional distillation or electrolysis.

# Cadmium oxide

Although cadmium oxide is an important commercial compound it is not manufactured from the zinc or mixed non-ferrous metal ores, phosphate rock, coal or other rock forms, as cadmium oxide but indirectly from the cadmium produced as a by-product in the manufacture of zinc and lead. The substance is important commercially for itself and also because of its extensive use in the preparation of other cadmium compounds.

### Production process

# Cadmium metal

The primary non-ferrous metal can be produced via two distinct types of production.

The formerly used pyrometallurgical processes. Here the residual sintered concentrate (calcine) containing oxidised zinc and cadmium materials is heated to about 1 100 to 1 350 °C, reduced by carbonaceous material and the zinc and cadmium volatilized. The metal vapours are condensed and collected as metal dust. Most of the cadmium collects with the zinc metal and may be removed in the refining of zinc by fractional distillation (refluxing). In  this process the boiling points of the metals present (cadmium 767°C, zinc 906°C and lead 1 750°C) are well separated and the cadmium can be concentrated in a cadmium-zinc alloy. Further repeating the distillation process under reducing conditions will result in cadmium metal with increasing purity.

The present-day electrolytic process has the following main features. During the production of zinc, at the purification of the solutions of zinc sulphate, before the electrolysis, cadmium is present in dissolved impurities (CdSO4). Cadmium is precipitated herein by adding zinc (as zinc powder or dust). The resulting impure cadmium residue (cadmium sponge) is purified and leached with aqueous sulphuric acid solution. A reasonably pure cadmium sponge is produced after two additional acid solution/zinc dust precipitation stages. The sponge is again dissolved in sulphuric acid and the solution, if sufficiently pure, is passed into electrolytic cells where the cadmium is deposited on cathodes (see Fig. 2.1.1.).

After deposition, the cathodes are stripped and the cadmium melted and cast into the required shapes (sticks and balls). The metal is typically either 99.95 or 99.99 per cent pure. Higher purity grades for special purposes can be obtained by further vacuum distillation (Lexicon, 1971; Technical notes on cadmium, 1991).

Variations in the production flow-sheet exist from one production site to the other. These may be due to differences in the type of the ores (zinc, lead), origin, form and content, the purity of the end-product that is aimed at, legal environmental criteria and the extent of (auto) recycling activities (scraps, flue dust,..).

In the EU cadmium metal is produced mainly as a by-producst of zinc production via electrolytic processes (approximately 77.5% of the total volume). The rest is obtained in association with pyrometallurgical refining processes (Industry Questionnaire, 1997).

Figure 2.1.1: Cadmium production flow-sheet: an example of electrolytic process in a closed production system (Union Minière, 1998)

# Cadmium oxide

In the commercial production process, cadmium oxide is prepared by the reaction of cadmium metal vapour with air. For the production of cadmium as part of the refining of zinc ores, we refer to the aformentioned paragraph. Other production possibilities are thermal decomposition of the carbonate, nitrate, sulphate or hydroxide but these are stated not to be in use for current industrial production (IcdA, com., 2003).

Cadmium oxide is available on the market in powder form. Its average particle size (spherical diameter) is 0,5 to 0,55µm (Annex VIIA, 1997).

It is packaged in metal drums, big bags, flo bins or containers (Annex VIIA, 1997).

Figure 2.1.2.A: Cadmium oxide production: flow-sheet

Figure 2.1.2.B: Production of cadmium oxide (PC WIAUX company information, 1998)

The manufacturing process for cadmium oxide is partly enclosed. Cadmium metal in ingots is manually placed in furnaces heated at 320°C. Emitted fumes are oxidised by contact with air in a closed system. The produced CdO powder is filtered and collected in bags, flo bins and metal drums or directly into silo. The packaging station has local exhaust ventilation at the discharge point. Workers have to place and adjust the bag or drum under the discharge and to set the process in motion (semi-automated process). Filled bags and drums are subsequently closed and carried to the storage area.

### Production volumes

#### Data for the reference year 1996

# Cadmium metal

The world primary cadmium production is estimated at 14 000 to 16 000t/y, the corresponding figure for Europe was approximately 5 000t/y (1994)- 5 800t/y (1996) (Industry, 1997), produced at 12 sites all over the EU territorial surface with, in these years, a major site localised in Belgium.

The amount imported in Europe in the same period is estimated at 1 500t/y - 960t/y (figure representative for Jan.-July ‘96) (Eurostat, 1997; in: Annex VIIA, 1997). Export out of Europe is estimated at 2 200t/y (1996). This latter figure is obtained by substracting the total EU consumption from the total EU production (IZA, personal comm., 1997).

Table 2.1.2.1 Cadmium production plant size distribution for 1996

| Tons | Number of cooperating companies |
| --- | --- |
| <300 tons | 5 |
| 300-600 tons | 4 |
| >600 tons | 3 |

Table 2.1.2.2. Production sites of metallic Cadmium in the EU ( in the range 10 to >1 000 t/y, EUREX), IUCLID 1997 (ECB)

| Company (and plant) | Country |
| --- | --- |
| Produits Chimiques Wiaux SA* | Belgium |
| Asturiana de Zinc | Spain |
| Britannia Zinc Limited | UK |
| Budel Zink BV | the Netherlands |
| Enirisorse | Italy |
| Espanola Del Zinc S.A.** | Spain |
| Metaleurop Nord S.A.S. | France |
| Metaleurop Weser Zink GmbH | Germany |
| Norzink | Norway |
| Outokumpu Zinc OY | Finland |
| Ruhr-Zink GmbH | Germany |
| Union Miniere Balen*** | Belgium |

* production/conversion stopped in 2001 (plant is closed down; Ind., pers. Comm., 2002)

** last cadmium production in 1991; since: zinc refinery without cadmium production

*** company’s name became UMICORE (2001) and production stopped in 2002

Remark: one company identified by the EUREX CD ROM is not included in the risk assessment process (phase 3 company with a production/import volume between 10 and 1 000tons/y.). Apparently it concerns a German pigment manufacturer presumably importing/using cadmium metal for further processing only (p.m. to check further).

An update provided by Industry (IcdA, com., 2003) reveals that Asturiana de Zinc in Spain no longer produces cadmium. Britannia Zinc and Metaleurope (France) have both recently closed down.  Española del Zinc and Ruhr-Zink have not produced for many years. Outokumpu  and Umicore exited the cadmium production business more recently. The table 2.1.2.2 needs thus some serious revision. It gives the impression that there are 12 active cadmium production plants in Europe when in fact there are now only three, possibly four: Budel (now known as Pasminco Budel), Norzink (now known as Norzinc Outokumpu), Enirisorse (now known as Porto Vesme, owned by Glencore) and possibly Metaleurop Weser Zink (recently taken over by Glencore). No more details were submitted.

Table 2.1.2.3 Raw EU production, import, export and consumption data of cadmium metal  in metric tons (Industry site specific questionnaire, 1997)

| Year | EU production | EU import | EU export | EU consumption |
| --- | --- | --- | --- | --- |
| 1994 | 5 000 | 1.582 | n.d. | n.d. |
| 1995 | 5 648 | 2.822 | ? (4.953) | 3.517 |
| 1996 | 5 808 | 960 (until July) | 2.200 (derived) | n.d. |

n.d.: no data

The available figure for 1996 has been derived from the production figure and the consumption figure of 1995 (assuming that this remained roughly the same in 1996); IZA, personal comm., 1997). The consumption figure for 1995 has been roughly derived from the information on production volumes used downstream in plating, pigments, stabilisers and batteries production facilities (IcdA, 1997).

# Cadmium oxide

The world production of cadmium (metallic) is estimated at 14 000 to 16 000 tons/y. The production of cadmium oxide for Europe was approximately 3 070 t/y (1994) - 2 536 t/y (1996) (Industry Questionnaire, 1997), produced at 2 major sites in the EU (Belgium).

Table 2.1.2.4  Production sites of cadmium oxide in the EU (EUREX), IUCLID 1997 (ECB)

| Company (and plant) | Country |
| --- | --- |
| Floridienne Chimie S.A., Ath | Belgium |
| Produits Chimiques Wiaux SA* | Belgium |

*production was taken over by Floridienne in 2000, and was definitively stopped in 2001 (Ind., pers. Comm., 2002)

Remark: one company identified by the EUREX CD ROM is not included in the risk assessment process (the concerned company has a production volume in the range: 10 – 1 000 tons/y.). It concerns a pigment manufacturer presumably importing/using cadmium metal for further processing – via an in-house production of cadmium oxide - to pigments only.

The amount of cadmium oxide imported in Europe is unknown with the exception of the first half of 1996 (Jan. to July) for which 23 tons was reported (Annex VIIA file, 1997). The latter document does not cite information on export. The site-specific information however mentions an important export activity taking place every year (ca. 1000t/y leave the EU).

Table 2.1.2.5 Raw EU production, import, export and consumption data of cadmium oxide in metric tons (Annex VIIA, 1997; Industry site specific questionnaire, 1998)

| Year | production | import | export | consumption |
| --- | --- | --- | --- | --- |
| 1994 | 3 069 | n.d. | >or= 1 050 | n.d. |
| 1995 | 2 757 | n.d. | >or= 1 350 | n.d. |
| 1996 | 2 536 | 23 (until July) | 1 000 | n.d. |

Production, import, export and consumption figures for both priority substances, cadmium metal and cadmium oxide, submitted by Industry are fragmentary.

In 2000, Industry provided a mass-balance for the reference year 1996, accompanied by an explanatory note (see Figure 2.1.2.1 and further), reflecting the best possible estimate at the moment.

An update for the year 2000 was provided in the context of the batteries’ targeted risk assessment (see Figures 2.2.5 and 2.2.6 in section 2.2.2.3.2) and estimates for the year 2002 in the context of the update site-specific assessment (see Figure 2.2.7 in section 2.2.3).

Two important confounding factors make it difficult to establish accurate cadmium consumption figures: 1) the conversion of cadmium metal into cadmium oxide and other cadmium compounds and 2) shipments of cadmium-containing residues to zinc smelters from recycling operations (Morrow, 2001).

Figure 2.1.2.1: CADMIUM MASS FLOW SHEET (METRIC TONNES)-REFERENCE YEAR 1996 (Source: IZA-Europe, IcdA, UM and CollectNiCd, 2000 & 200)

# Explanatory note to the mass-flow of cadmium (as provided by Industry)

The mass balance reveals that 5,808 tonnes of cadmium were produced in Europe in the reference year (1996). The imports were estimated to 1,920 tonnes including the contribution of the metal present in imported consumer/sealed portable nickel-cadmium batteries. Cd metal stocks exists in Rotterdam which may influence the trading balance but the data reported hereafter have been mainly obtained from use at the industrial level for the various applications.

It can be observed that a large industrial activity consists in the transformation of cadmium metal in the oxide: the equivalent of 2,536 tonnes of cadmium are used in the production of cadmium oxide.

The EU regional use of metal reaches the value of 2638 tonnes, which are distributed for 75.2. % to Ni-Cd batteries, 14.9 % to pigments, 5 %  to stabilisers and 5 % into alloys and plating.

Portable Nickel-Cadmium batteries are introduced on the market as a power source incorporated in Electrical and Electronic equipment in more than 90 % of the cases. This is the origin of a significant export ratio for batteries. This ratio has been estimated between 33 % to 50 % (according to applications and countries) for the consumer/sealed portable batteries produced in Europe on the basis of the Import- Export balance.

Industrial Ni-Cd batteries are not imported in significant quantities (less than 5 %). They are manufactured in European countries and are exported in a significant proportion, estimated to 35 % for the global European market. The net export of cadmium from batteries reaches the estimated volume of 750 tonnes.

The largest export quantity is found in the cadmium metal produced by European companies in order to satisfy the demand in USA, Asia and South America. A significant fraction of the cadmium oxide produced in Europe is exported to non-European battery manufacturers which demonstrates the competitiveness of this European industry involved in the transformation of Cadmium into the oxide. When the battery is marketed, the cadmium content is present as cadmium hydroxide (discharged battery) or as cadmium metal (charged battery).

It has been estimated that cadmium from recycling operations reached approximately 337 Tonnes from used batteries collected from the market and industrial sources. In addition, there are two types of stocks to be considered. First, the manufacturing rejects and secondly, a cadmium stock for the work in progress. Those have been presented in a closed loop independently of the total inlet and outlet of the primary cadmium. Indeed recycling operations leads to a 99 % recovery of the cadmium content of the battery. The metal has a purity higher than 99.9 % and is re-used in new battery manufacture. The battery manufacturing capacity will produce a new volume of waste equivalent to the treated one, which is re-introduced in the circuit. At the same time, the management of a stock required for the “work in progress” is considered.

----

Mass-balances are available for several EU countries, and years (e.g. Denmark for 1996 (Danish EPA, 1994 & 2000), Germany for 1990, 1991, 1992, 1993 and 1994 (UBA, 1996), the Netherlands for 1980 (VROM, 1991), France for 1995/1996 (l’Académie des Sciences Rapport N° 42, 1998) and Greece for 1993 and 1997 (EUPHEMET, 2000). From these documents, the overall consumption patterns and trends are roughly confirmed, with a largely predominant flow of cadmium in batteries that dramatically increased since the eigthies and continued during the nineties while most other uses have been declining.

#### Update date (reference year 2002)

In 1997, from the companies liable to the Regulation 793/93/EEC, there were 12 companies producing cadmium metal and 2 producers of cadmium oxide. Regards the import of the substances, one company for cadmium metal and one company for cadmium oxide were active in the field and were subject to the existing substances regulation.

In 2005, this picture has significantly changed. An overview is given here below.

Cadmium metal

The companies that stopped the production of cadmium metal/cadmium oxide and the approximate date are listed inTable 2.1.2.6.

Table 2.1.2.6: Production sites of metallic cadmium/CdO in the EU in the range 10 to > 1000 t/y that stopped production

| Company (and plant) | Country | Date/year of production stop |
| --- | --- | --- |
| Asturiana de Zinc (now: Xstrata Zinc) | Spain | 1998 |
| Britannia Zinc Limited (in liquidation: 2003) | UK | 2003 |
| Enirisorse | Italy | 2005 (? To re-confirm by Industry) |
| Espanola del Zinc S.A. | Spain | 1991/1992 |
| Metaleurop Nord S.A.S. | France | 2003 |
| Outokumpu Zinc OY (now: Boliden Kokkola) | Finland | 2002 |
| Ruhr-Zink GmbH | Germany | 1998-1999 |
| Union Minière Balen (now : Umicore) | Belgium | 2002 |
| Produits Chimiques Wiaux S.A. | Belgium | 2000/2001 |

Former activities at Produits Chimiques Wiaux S.A.: limited to the conversion of massive cadmium metal into cadmium metal powder

The companies still manufacturing cadmium metal in 2005 are reported in Table 2.1.2.7. All companies produce the substance in massive form (e.g. plates, sticks, balls).

Table 2.1.2.7: Current producers of cadmium metal liable to the Regulation 793/93/EEC

| Company (and site) | Country |
| --- | --- |
| Budel Zink (now: Zinifex Budel) | The Netherlands |
| Norzink (now: Boliden Odda A.S.) | Norway |
| Metal Europ Weser Zink (now: Xstrata Zinc GmbH) | Germany |

Updated data on EU-16 production data are given in Table 2.1.2.8. No data are available on the situation in the EU-25.

Table 2.1.2.8: EU production, import, export and consumption data on primary cadmium metal in metric tons (Industry site specific questionnaire, 2004/2005)

| Year | EU production | EU import | EU export | EU consumption |
| --- | --- | --- | --- | --- |
| 2002 | 1114 | n.d. | n.d. | n.d. |
| 2003 | 1207 | n.d. | n.d. | n.d. |

n.d. no data available

Based on the data of one producer 85% of the production volume is exported outside the EU-25. A second company mentions 100% export but it is not clear if this is meant as outside the EU or outside country where production is located.

The amount of secondary cadmium produced by recycling is given under section 2.2.1.1.

The total volume of cadmium consumed within the old EU-16 (including Norway) and the new EU-25 territory is unknown.

Cadmium oxide

Update information regards the producers of cadmium oxide is given in the Table 2.1.2.9 and Table 2.1.2.10.

Table 2.1.2.9: Production sites of metallic cadmium in the EU in the range 10 to > 1000 t/y that stopped production.

| Company (and plant) | Country | Date/year of production stop |
| --- | --- | --- |
| Produits Chimiques Wiaux S.A. | Belgium | 2000/2001 |

Former activities at Produits Chimiques Wiaux S.A.: limited to the conversion of massive cadmium metal into cadmium oxide

Table 2.1.2.10: Production sites of cadmium oxide in the EU with volume > 1000 t/y (reference year: 2002)

| Company (and site) | Country |
| --- | --- |
| La Floridienne | Belgium |

Information on the total production of cadmium oxide by La Floridienne was submitted for the reference year 2002. Since 1996 there is an increase of the production volume.

## Uses

### General overview

Cadmium metal

Metallic cadmium is mainly used in the production of batteries, cadmium compounds ( cadmium oxide and to a lesser extent cadmium hydroxide). Further also in coatings, alloys and other miscellaneous uses (see Table 2.2.1 showing the industrial and use categories of cadmium). The two types of  ‘Main categories’ for cadmium are characterised as non dispersive use and use resulting into or onto a matrix.

Metallic cadmium is commercialised in different forms: powder, balls (3-5 cm diameter), plates (10-200-200 to 1.000mm) or sticks (200 to 240-10 to12 mm) (Annex VIIA, 1997).

# CdO production

An important proportion of the cadmium metal produced is subsequently used in the production of cadmium oxide powder. This substance has several applications and constitutes the (principal) raw material in the production of other cadmium compounds.

The CdO produced has a high purity (at least 99% CdO) resulting in a cadmium wt% of 87.25 to 87.5.

A short description of the uses of respectively cadmium metal and cadmium oxide and processes involved is given below (source: IcdA, 1997, unless specified otherwise).

# Cadmium metal

# Batteries

# Cfr the batteries’ related sections (2.2.2).

# Plating

By plating of metals or alloys a coating is provided that is resistant to corrosion by alkalis, salt water and atmosphere. Furthermore these coatings are highly ductile and easily soldered.

Cadmium coatings have low coefficients of friction and maintain high electrical conductivity, and hence are used mainly in applications where both corrosion resistance and lubricity or good electrical conductivity are required (IcdA, com., 2003). Cd-Ti and Cd-Sn electroplated coatings are used to resist hydrogen embrittlement in high strength steel fasteners.

The coating can be realised by electrochemical reaction: cadmium is the anode in the cell formed with an iron substrate in water. Other technologies for coating are vacuum deposition (mainly cyanide baths), dipping or spraying , or mechanical plating with cadmium powder, where glass shot is used. Cadmium ion vapour deposition is another technique also used. For further details on the processes reference is made to section 4.1.1., human part of the RAR on Cd/CdO, in separate document.

Electrodeposition of cadmium on a metal substrate accounts for 90% of the cadmium used in plating. The remaining 10% is applied by vacuum deposition, metal spraying7 or mechanical8 plating.

Cadmium plating by electrodeposition uses an alkaline cyanide solution of the metal as starting material. The plating solutions can be purchased direct from chemical manufactures; alternatively they can be prepared on-site from cadmium metal or oxide. The plating solution normally contains 18 - 22 g/l Cd. Baths usually have cadmium bars or ball anodes, placed in steel anode baskets with a surface area of cadmium equal to the plating load. Barrel plating usually uses and electrolytes with less cadmium (15 g/l). After electroplating, and heat treatment if required, a chromate conversion coating is usually applied on a subsequent bath (IcdA, 1997).

# Plating contains 99,95% cadmium (Annex VIIA file, 1997).

# Alloys

Cadmium has been a common component of many alloys which uses are related to their melting temperatures, e.g. tin-lead-bismuth-cadmium alloy joining metal parts which may be heat sensitive; silver-cadmium-copper-zinc-nickel alloy for joining tungsten carbide to steel tools…The EU use of cadmium as a constituent of alloys (mainly Cu-Cd and Ag-CdO) has declined in importance in the recent years (4% of total use in 1985, about 0.6% in 1996) as these have been substituted by cadmium free alloys with comparable characteristics of ductility and strength in the majority of uses.

Cu-Cd alloys are prepared by re-melting high conductivity copper in suitable furnaces and adding the necessary cadmium in the form of a copper-cadmium master alloy, or by ‘side-casting’ from holding furnaces fed by the large reverberatories of refineries.

During the manufacturing of the master alloys, drosses containing Cd are released. Usually, they are recycled internally or in other metal plants.

The normal form of the casting is a wire bar, which is hot rolled before drawing to wire. Normal practise is followed in drawing the rod to wire, using dies of suitable shape in the case of trolley wire. Limited quantities of sheet and strip are produced by rolling, and of rod by extrusion and drawing (IcdA, 1997).

Cu-Cd alloys contain usually 0,2-0,8% cadmium. The production of these alloys occurs via pre-alloys (containing 49-51% cadmium) which are further processed by other industries to prepare the final Cu-Cd alloys (Annex VIIA file, 1997).

Ag-CdO electrical contact alloys are produced by internally oxidizing an Ag-Cd alloy. The percentage of Cd in Ag-CdO alloys is generally in the range of 5% to 15% (IcdA, pers. Com., 2003).

# Other uses

Applications as reported by Farnsworth (1980): deoxidizer in nickel plating, in process engraving, in electrodes for cadmium vapour lamps, in photoelectric cells and in the photometry of ultraviolet sunlamps, in selenium rectifiers and Jones reductors andapplication of cadmium powder as an amalgam (1Cd:4Hg) in dentistry, are stated by Industry as no longer in use (IcdA, pers. Com., 2003).

# Cadmium oxide

Cadmium oxide is used as starting material for a wide variety of other cadmium compounds (PVC heat stabilisers, pigments). Cadmium oxide has been used as a stabiliser for the cadmium sulphide and sulpho-selenide forms in glass. In nitrile rubbers the substance improves heat resistance; in plastics, it improves high temperature properties.

Another field of (minor) applications is based on the catalytic properties of cadmium oxide. It catalyses reactions between inorganic compounds, as well as organic reactions such as oxidation-reduction, dehydrogenation, cleavage and polymerisation (use as vulcanizer). It sensitises photochemical reactions.

Other (former) uses included phosphors, semi-conductors, manufacture of silver alloys, and as nematocide-anthelmintic in swine and poultry.

A short description of the uses and processes involved is given below (source: IcdA, 1997, unless specified otherwise).

# Batteries

Although cadmium metal is one of the principle raw materials, cadmium oxide is used in the manufacture of certain types of cadmium electrodes (IcdA, 1997). See the batteries’ related sections (2.2.2).

# Stabilisers

Barium cadmium stabilisers can be manufactured in a number of ways. The starting materials are usually the metals or the metal oxide. They are combined with various organic compounds. Three general processes can prepare the salts:

- Direct dissolution of finely divided metal oxides in heated organic acids

- Precipitation from aqueous solution of metal salts (chlorides or nitrates) and alkali soaps

- Fusion of metal oxides with organic acids.

For liquid barium/cadmium stabilisers the production starts from metal oxides which are dissolved directly in the heated organic acids in the presence of solvents. The reaction water is removed and the finished product filtered.

Solid stabilisers are prepared by the precipitation process through the method of preparing metal soaps of natural fatty acids to give for example, cadmium laurate. Following precipitation the resultant slurry is filtered and dried (IcdA, 1997).

# Pigments

There is a number of proprietary manufacturing processes, which use either cadmium metal, or cadmium oxide as the essential raw material. In general the manufacturing process involves the preparation of a cadmium sulphate or nitrate solution; filtration to remove recoverable solids; addition of sodium sulphide and precipitation of cadmium sulphide, with simultaneous additions of other salts to alter colour characteristics; filtration to define precipitate and drying; calcination to convert crystal structure to more stable form; further rinsing, milling and blending followed by packaging (IcdA: compilation of Industry data, 1997).

Table 2.2.1: Industrial and use categories of cadmium in the EU (HEDSET, 1994)

| Industrial category | EC no. | Use category | EC no. |
| --- | --- | --- | --- |
| Chemical industry: basic chemical | 2 |  |  |
| Chemical industry: chemicals used in synthesis | 3 | Intermediates Laboratory chemicals | 33 34 |
| Electrical/electronic engineering industry | 4 | Conductive agents Batteries and cells... | 12 |
| Personal domestic | 5 | ? (see Product Register) |  |
| Metal extraction, refining and processing industry | 8 | Electroplating agents Others: Alloys | 17 55 |
| Paint, lacquers and varnishes | 14 | Reprographic agents | 45 |
| Others: Basic metal used in metal industry | 15 | Corrosion inhibitors | 14 |

Table 2.2.2: Industrial and use categories of cadmium oxide in the EU (HEDSET, 1995; Product Registers, 1997 and 1998)

| Industrial category | EC no. | Use category | EC no. |
| --- | --- | --- | --- |
| Chemical industry: basic chemical | 2 |  |  |
| Chemical industry: chemicals used in synthesis | 3 | Intermediates Laboratory chemicals Raw material for the production of other cadmium chemicals | 33 34 55 |
| Electrical/electronic engineering industry | 4 | Conductive agents Electroplating agent | 12 17 |
| Polymers industry | 11 | Stabilisers | 49 |
| Paints, lacquers and varnishes industry | 14 | Colouring agents Fillers Reprographic agents | 10 20 45 |
| Others: Industrial : other = colours/frits Other : Ceramic industry Other: Glass and related industry | ? 15 15 | ? Colouring agents Colouring agents | ? 10 10 |

This Table reflects the information as reported by Industry falling under the HEDSET obligation and was further completed by information contained in the Product Registers (see Annex 2.1.3.1).

# Other data on uses of the substances: Product Registers (see also Annexes 2.1.3.2)

# Cadmium metal

The Danish product register (1997) reports under the CAS number of metallic cadmium, in descending order of involved amount: construction industry and chemical industry (private household insignificant). In the same way, product types are listed: paints, lacquers and varnishes, construction materials and laboratory chemicals. With 31 out of 49 products containing 0-1% cadmium and 3 products with 80-100% cadmium content. The total quantity used in products in 1997 was lower than 1 ton for Denmark.

The register of 1998 gives a similar picture. The additional information concerns the content in the different product types: paints, lacquers and varnishes: 12 of the 26 products contain lesser than 1% of the substance; construction materials: all products contain maximum 1% cadmium; laboratory chemicals: two of the three products have a content of 80-100% cadmium; colouring agents: eight products of the twelve contain maximum 1% cadmium. The quantity for each major product type is smaller than 10kg and the overall quantity is less than 1 tonne/year.

The Swedish product register (15/09/97) reflects the presence of the substance - albeit at low concentration (< or = 10%) – in a range of products and trades. The largest number of products and highest volume are used in dyestuffs (pigments) and in fillers plastic, paints,... The total volume in products did not exceed 1 tonne in 1996. More details of the industrial and use categories can be found in Annex 2.1.3.1.

When overviewing the information contained in the product registers it could be questioned if the entry with CAS-N° of cadmium metal (i.e. 7440-43-9) is not used also to report on cadmium in a (more) generic way.

# Cadmium oxide

The Danish product register (April 1997) reports 14 of the 25 products containing 1-10% cadmium oxide and two products with 80-100% of the substance. The major Industry implicated is the manufacturing of electronic equipment. Product types (in descending order of used substance’s quantity): Laboratory chemicals and conductive agents. The total quantity in products is less than 1t/year. For 1998 the Register is very similar. Nevertheless, here reprographic agents seem quantitatively most important, followed by conductive agents (11 products) and laboratory chemicals. The total quantity of the substance used in products is less than 1t/year.

# Details of the Swedish Register (1997: figures of 1996) are annexed (see Annex 2.1.3.2).

# The consumption pattern of cadmium (oxide and other cadmium compounds):

The world wide overall consumption pattern of cadmium (and its compounds) has been estimated by the International Cadmium Association (cited in Pearse, 1996) as follows: batteries (61%), pigments (20%), stabilisers (10%), plating (8%), alloys (3%) and other uses (4%).

For the Western World, Morrow came for the year 1996 to the following figures: batteries (69%), pigments (13%), stabilsers (8%), coatings (8%) and alloys & other (2%) (cited in: Morrow, 1998). In the context of the ESR Programme, Industry estimated the consumption pattern of cadmium (oxide) in Western Europe for the year 1996 as follows: batteries (60%), stabilisers (20%) and pigments (20%). Other uses are considered insignificant (Annex VIIA, 1997) and estimated to be less than 0.1% (IcdA, CollectNiCad, pers. Com., 2002). The figures were reviewed by Industry, refined and reported in the mass-balance (see Figure 2.1.2.1).

# Use of Production, Consumption and Import/Export data

The data from the HEDSET/Annex VIIA, 1997 and the site specific Questionnaire (producers/importers of Cd (O)) provide the basis for the exposure assessment of these industrial sources.

The data from WS Atkins and underlying completed Questionnaires were used for the exposure assessment of pigments as well as stabiliser producers and users.

For plating an EU generic scenario is used (by lack of any site-specific exposure data) and based on the amount of cadmium estimated to be consumed in this application in the EU as a whole (estimation from IcdA, 1997).

Site-specific data (collated by the Questionnaires 1998, 2000 and 2001) are used for the exposure assessment of the batteries’ producing and cadmium recycling companies.

Data on the cadmium flow related to batteries and recyclers cfr the mass-balance (updated for the year 2000) are used in the targeted risk assessment on cadmium (oxide) as used in batteries and in particular for estimating the emissions due to their waste disposal (cfr batteries’ related section 2.2.2.3.2).

Site-specific data collected via the Questionnaires (2004) are used to update the local assessment for all scenarios related to production and use of the priority substances for which new data were submitted (cfr section 2.2.3). The reference year for the latter update was set at the year 2002.

### Batteries

#### Used terminology on Nickel-Cadmium batteries

Electrochemical cells and batteries are identified as primary (non-rechargeable) or secondary (rechargeable), depending on their capability of being electrically recharged. Within this classification different types of battery formats exist.

A battery can consist of only one cell or can be put together of several cells, which are connected among each other. There are cylindrical cells, button cells, prismatic batteries and battery packs available on the market (Table 2.2.3) depending on application type, use, equipment.

Table 2.2.3: Overview of the different battery formats and chemistry

| Product Group | Sub-groups |
| --- | --- |
| Batteries type and geometry | Rechargeability | Format | System |
|  | Primary (non-rechargeable) | Button | Lithium: LiMnO2, Li(CFx)n |
|  |  |  | Others: AM, ZnO2, ZnAgO, ZnHgO |
|  |  | Cylindrical | Lithium: LiMnO2, Li(CFx)n, LiSOCl2, ZnO2 |
|  |  |  | Others: ZN, AM |
|  |  | Prismatics Packs | Lithium: LiMnO2, Li(CFx)n |
|  |  |  | Others: ZN (E-Block 9V, normal 4,5 V), AM (E-Block 9V) |
|  | Secondary (rechargeable) | Buttons | NiCd, NiMH |
|  |  | Cylindrical | NiCd, NiMH, AM, Pb-acid, Lithium: Li-ion |
|  |  | Prismatics Packs | NiCd, NiMH |
|  |  |  | Pb-acid |
|  |  |  | Lithium: Li-ion |

| LiMnO2 | Lithium manganese dioxide | ZnO2 | Zinc-air |
| --- | --- | --- | --- |
| Li(CFx)n LiSOCl2 | Lithium polycarbonmonofluoride Lithium thionyl chloride | ZnAgO | Zinc silver oxide |
| AM | Alkali-manganese | ZnHgO | Zinc mercury oxide |
| ZN | Zinc-carbon | NiCd | Nickel-cadmium |
| NiMH | Nickel-metal-hydride | Pb-acid | lead-acid |

Source: IOW, 1997

Ni-Cd batteries are generally viewed as high performance battery chemistries with good energy density and power density, especially suitable for high drain rate applications.  Included in their best performance characteristics are their long useful life, wide temperature operating range, resistance to electrical/mechanical abuse and rapid charge/discharge characteristics. Disadvantages are low energy density, the so-called ‘memory effect’ and higher costs than lead-acid batteries. Nickel-cadmium batteries may readily be formulated into many different types, shapes and sizes of batteries designed to meet the specific requirements of many different applications.

The pocket-plate battery is the oldest and most mature of the various designs of nickel-cadmium batteries available and is manufactured in a wide capacity range, 5 to more than 1200 Ah and is used in a number of applications. Developmental work has been conducted continuously since the introduction of the pocket-plate nickel-cadmium battery to improve the performance characteristics and reduce battery weight. These innovations have resulted in the sintered-plate, fiber-structured and plastic-bonded or pressed-plate technologies (Evjes & Catotti, 2002). The sintered plate battery consists of a perforated mechanical substrate (e.g. nickel-plated steel or nickel-clad steel wire) coated with a highly porous sintered nickel matrix which is impregnated with nickel hydroxide (positive electrode) or cadmium hydroxide (negative electrode).  The fiber (foam) structure technology uses a three-dimensional nickel-plated fiber matrix, which is highly porous.

Within these technologies a further distinction can be made between vented (open) and sealed cells. A functional vented battery generates a stoichiometric mixture of hydrogen and oxygen gases during overcharge and expels them normally from the cell into the battery container. Most often vented batteries have been used in industrial applications.

Sealed nickel-cadmium batteries incorporate specific battery design features to prevent a build-up of pressure in the battery caused by gassing during overcharge. As a result, batteries can be sealed and require no servicing or maintenance other than recharging.

Since both the term sealed and portable can be applied to some industrial batteries the term consumer batteries was initially used in the questionnaire sent to the Member States to indicate batteries with mainly domestic application. However, in general sealed, portable batteries not exceeding a weight limit (e.g. < 3 kg) irrespective of some other uses, are referred to under this terminology. Furthermore since household applications represent to date less than 20 % of the market by weight (cfr Table 2.2.17) it is deemed more appropriate to use the term portable batteries in order to indicate that the figures presented in this report may include professional applications next to household applications.

A battery is made of cells assembled in series. Roughly Ni-Cd batteries can be divided into the following weight categories. Sealed cells: cell weight between 10 and 150 grams (maximum 500g), usually assembled by 3 to 10 to make packs for portable applications. The most common are 3 and 4 cell packs. Larger batteries do exist for stationary industrial applications. Vented cells: cell weight between 1 and 70 kg (typically 3 to 10), usually assembled by at least 10 cells but up to several hundred. (CollectNiCad, personal communication, October 2002). A compilation of some of the different subtypes of Ni-Cd batteries and their specific characteristics is given in Table 2.2.4.

Table 2.2.4: Format, size and characteristics of Ni-Cd batteries

| Product group | Subgroup |
| --- | --- |
|  | Format and size | IEC n° (US-Standard) | Weight (in g) | Nominal Voltage (in V) | Capacity (in Ah) | Cadmium content (in g per 100 g battery) |
| Portable batteries | Button |  |  | 1.2 | up to 1 Ah | 11-15 typical/average content = 13.8 |
|  | Cylindrical | R 20 (D) | 145 | 1.2 |  |  |
|  |  | R 14 (C) | 75 22 12 | 1.2 |  |  |
|  |  | R 6 (AA) |  | 1.2 |  |  |
|  |  | R 03 (AAA) |  | 1.2 |  |  |
|  |  | KR6 | 26 | 1.2 | 0.75 |  |
|  |  |  | 35 |  |  |  |
|  | Prismatics | 9 V E-block |  | 9.6 V |  |  |
|  | Packs |  | 20-450 |  |  |  |
| Industrial/ professional use | Automotive vehicles Safety and back-up systems Aviation |  | 200 kg 200 g to 1,000 kg 20 kg (per battery) > 1 kg (per cell) |  |  | 8 |

Sources: individual producers/recyclers (via Questionnaire 1998, 2000/2001)

#### Ni-Cd chemistry and composition

The nickel-cadmium (Ni-Cd) battery is a rechargeable battery system based on the reversible electrochemical reactions of nickel and cadmium in an alkaline potassium hydroxide electrolyte.  The chemical compositions of Ni-Cd batteries can vary widely depending on the type and its specific application. For industrial batteries cadmium content may vary between 3 and 11 %. For portable batteries values between 11 and 15 % have been reported (battery questionnaire 2000). In addition, most Ni-Cd batteries contain significant amounts of nickel, iron, plastics and electrolytes and small amounts of metals such as cobalt and copper (Morrow & Keating, 1997).

Ni-Cd cells use a reversible electrochemical reaction between nickel and cadmium electrodes packed in an alkaline electrolyte (potassium hydroxide or sodium hydroxide and lithium hydroxide as an additive). The active materials are insoluble in the electrolyte, whose ions act only as a charge carrier and do not take part in the electrochemical charge/discharge reactions (Cornu, 1995). At the cadmium electrode during discharge, cadmium is oxidised by combining with two OH- ions to form cadmium hydroxide [Cd(OH)2] and releasing two electrons [US EPA,1993, Gross,1995).  During charging the reverse happens. Hydrated nickel (III) oxide is reduced to nickel (II) hydroxide at the other electrode (US EPA,1993). The charge-discharge equation is as follows (Cornu, 1995):

2 Ni(OH)2 + Cd(OH)2  + 2 e ( 2 NiOOH + Cd + 2H20

2 Ni(OH)2 + Cd(OH)2 ( 2 NiOOH + Cd + 2H20 – 2e

The principal difference between the various types of Ni-Cd cells is the nature of the cell electrodes. The three primary types of positive electrodes used are pocket plate, sintered plate, and fiber plate. The hydrated nickel oxide electrode is usually in powder form and is held in pocket plates or suspended in a gel or paste and placed in sintered (perforated mechanical support) or fiber electrodes (US EPA, 1993).

The negative electrodes use pocket plate, sintered plate, fiber plate, foam or plastic banded supports to hold the cadmium (hydroxide) in place. Graphite or iron oxide is commonly added to improve the conductivity of both the nickel and cadmium hydroxide.  Since the individual cells are recycled before assembling into batteries, it is not important whether the negative electrodes are originally impregnated with Cd(OH)2 (the product of discharge reactions) or Cd metal (the product of charging reactions) (US EPA, 1993).

A typical chemical composition for a Ni-Cd cell is given in Table 2.2.5.

Table 2.2.5: Average chemical composition for a Ni-Cd battery

| Material | Weight % |
| --- | --- |
|  | Portablea Ni-Cd battery | Industrialb Ni-Cd battery |
| Iron | 35 | 48 |
| Nickel | 22 | 8 |
| Cadmiumc | 13.8c | 8c |
| Plastic | 10 | 10 |
| (OH)2 | 9 | 5 |
| Water | 5 | 16 |
| Potassium hydroxide | 2 | 5 |
| Others | 3.2 | 0 |
| Total | 100 | 100 |

Source of the figures:  EPBA and EUROBAT  product information (1997) in ERM (1997)

a Portable Ni-Cd battery, are batteries weighing between 10 g and 3 kg. Since household applications represent to date less than 20 % of the market by weight it is deemed more appropriate to use the term  portable batteries in order to indicate that the figures presented in this report may include professional applications next to  household applications.

b Industrial Ni-Cd battery: large size batteries weighing over 3 kg in weight

c latest update of information from industry i.e. manufacturers/recyclers (CollectNiCad,,2000)

Large, industrial-size batteries contain on average approximately 8 % cadmium. Small, portable-type batteries contain approximately 13.8 % cadmium. These figures refer to actual manufacturing and production data and  have been confirmed by the information collected from individual battery producers via the Battery Questionnaire 2000 and will be used in this report as representative for industrial batteries and portable batteries respectively.

#### Production, recycling and use

##### Ni-Cd batteries manufacturing processes

Nickel-Cadmium batteries are widely used in many different applications where an autonomous energy source is required. Each application demands a different battery design, adapted to its performance requirements. For industrial applications different battery technologies are available: pocket plate cells, sintered plate cells, nickel fiber plate cells, plastic bonded plate cells.

Pocket plate batteries represent the conventional battery technology. Pocket plate electrodes contain the active materials in perforated steel pockets. This type of plates is mechanically very strong and the steel strip retains the active material during cycling, minimising swelling. In each cell a number of positive and negative electrodes are paralleled to form the plate group. Nickel-plated steel is used for connecting the elements and the terminals. The electrodes and separators are immersed in the alkaline electrolyte and the cell has a vented design.

A process flow diagram for the pocket plate batteries process is shown in Figure 2.2.1.

The reported emission/waste data represent site specific data (local worst case) from a pocket plate Ni-Cd batteries manufacturing plant (Industry Questionnaire, 2000/2001). The emission factors for air and water were calculated using the used Cd amount for the manufacturing of Ni-Cd batteries and the emissions to air/water. The sludge factor for cadmium in the WWTP sludge was calculated from plant supplied data (Cd content of sludge, amount of sludge, Cd used during manufacturing).

The emissions/wastes from the production of this type of battery include the following:

- Wastewaters containing cadmium. The sources of these wastewaters are the manufacturing of active materials, nickel strip manufacturing and the cell formation process. This wastewater is estimated to amount to 0.124 kg per ton of Cd used in the battery manufacturing process (Fww=1.24 x 10-4).

- Air emissions occur during manufacturing of pocket plates and during assembling. For this specific plant no air emission data were reported. However for another pocket plate manufacturing plant –recycling its emissions to water- an air emission factor of 0.464 kg/ton Cd used was reported.

- Sludges recovered from treatment of wastewaters (manufacturing of active materials, nickel strip manufacturing, cell formation process). These are estimated to contain 17,7 kg cadmium per ton of Cd used. The sludge from the wastewater treatment plant is sent to an external recycling plant.

- Rejected battery cells from the test and package step: 118.8 tonnes/year. This waste is treated at a recycling plant.

- Other waste: raw material bags, substituted filters, cleaning materials and tools: 1.15 tonnes/year.

Nickel fiber batteries are characterised by the use of a nickel fiber mat as electrode support. The active materials are impregnated by mechanical or electrochemical methods. Average diameter of the nickel fibers is around 20 µm. Porosity, pore size and electrode thickness can be adjusted as required for every application: lower porosity, smaller pores and thinner plates are adequate for high rate applications, while higher porosity, bigger pores and thicker plates are the choice for medium rate batteries. Thickness, porosity, pore size and the impregnation method are then adjusted to each specific application, in order to achieve the best electrical performance/battery cost ratio.

A process flow diagram for the nickel fiber plate process is shown in Figure 2.2.2.

The reported emission/waste data represent site specific data (local worst case) from a fiber plate Ni-Cd batteries manufacturing plant. The emission factors for air and water were calculated using the used Cd amount for the manufacturing of Ni-Cd batteries and the emissions to air/water. The emission factor for cadmium in the filter cake was calculated from plant supplied data (Cd content of filter cake, amount of filter cake, Cd used during manufacturing).

The emissions/wastes from the production of this type of battery include the following:

- Wastewaters containing cadmium. The source of this waste is the impregnation step. This wastewater is estimated to amount to 0.769 kg per ton of Cd used in the battery manufacturing process. This wastewater is collected and recycled in an external recycling plant.

- Emissions to air occur during assembling are very small; 0.00027 g per ton of Cd used.

- Filter cake recovered from formation process. This is estimated to contain 10.5 kg Cd per ton of Cd used. The filter cake is recycled.

- Rejected batteries (no information)

Sintered plate batteries contain a cadmium anode, a potassium hydroxide electrolyte, and a nickel oxide cathode. For the electrodes, sintered plates containing the active materials are used. In one operation, the plates are made by impregnating sintered nickel substrates with nickel and cadmium nitrate salts. The nickel and cadmium nitrates are converted to hydroxides in sodium hydroxide solution. The plates are then washed thoroughly and dried in a hot oven. The impregnation cycle is repeated to deposit the desired amount of active material. The plates then go through a formation treatment, which removes impurities and brings the active materials to a condition similar to that existing in working electrodes. The cell is assembled into final form using an absorbent plastic separator and a nickel-plated steel case. With the addition of the alkaline electrolyte, they are ready for electrical testing, packing, and shipping.

There are currently three distinct manufacturing processes used for preparing the electrodes of the electrodes of the sintered plate batteries. The preceding paragraph described the worst case from an environmental standpoint of the three, due to the high concentration of cadmium and nickel compounds contained in the wash water. The other processes in use are:

- An electrolytic deposition process which deposits active materials directly on the sintered plates – this process produces wastewater containing nickel and cadmium compounds, though the amount is not as large as in the impregnation process described above; and

- A pressed powder process involving active materials mixed with binders in a dry powder form.The powder mix is pressed onto a wire mesh or expanded metal grid in an mold. This is a dry process and no wastewater is involved.

A process flow diagram for the impregnation-sintered plate process is shown in Figure 2.2.3.

The reported emission/waste data represent site specific data (local worst case) from a sintered-plate Ni-Cd batteries manufacturing plant. The emission factors for air and water were calculated using the used Cd amount for the manufacturing of Ni-Cd batteries and the emissions to air/water. The sludge factor for cadmium in the WWTP sludge was calculated from plant supplied data (Cd content of sludge, amount of sludge, Cd used during manufacturing).

The emissions/wastes from the production of this type of battery include the following:

- Wastewaters containing cadmium and nickel salts together with sodium hydroxide. The source of this waste is the washing step. This wastewater is estimated to amount to  0.048 kg) per ton of Cd used in the battery manufacturing process.

- Atmospheric emissions are stated not to occur since the process is merely wet.

- Sludges recovered from treatment of wastewater. These are estimated to contain cadmium ( 6.3 kg per ton of Cd used) and nickel hydroxide. The WWTP sludges are landfilled (special landfill class I).

- Rejected batteries from the test and package step, together with other scrap, are externally recycled for cadmium.

Recycling processes

Ni-Cd batteries might be recycled either pyrometallurgical (high-temperature) or hydrometallurgical (wet chemical) processes. Today, commercial Ni-Cd battery and manufacturing scrap-recycling systems are usually based upon pyrometallurgical (high temperature) processes. Hydrometallurgical (wet chemical) systems have also been designed and have reached the pilot plant stage, but no purely hydrometallurgical systems are utilised today to recycle Ni-Cd batteries. Some recycling systems may have elements of both pyrometallurgical and hydrometallurgical processes in their overall system. (Morrow,1997).

In pyrometallurgical recycling processes, cadmium-containing wastes or used batteries are heated at a low temperature to drive off moisture and organic compounds, and then heated to above 800 °C to volatilise the cadmium. The vapour is then condensed, either as cadmium oxide or metal, and collected for final processing into high purity material (>99.99 %) suitable for any re-use in industrial applications. In hydrometallurgical processes the cadmium-containing wastes are dissolved in a suitable reagent, usually a strong acid, and then subjected to a series of wet chemical reactions designed to successively remove impurities. The final cadmium product is normally a cadmium sulphate, chloride or nitrate solution from which high purity cadmium may be electrochemically obtained. Ion exchange techniques have been utilised in some hydrometallurgical recycling schemes, depending on the nature of other impurities present. (OECD, 1996).

A schematic presentation of the recycling processes for industrial and portable Ni-Cd batteries is supplied in Figure 2.2.4.

The reported emission/waste data represent site specific data from a Ni-Cd batteries recycling plant. The emission factors for air and water were calculated using the recycled Cd amount from  Ni-Cd batteries only and the emissions to air/water. The emission factor for cadmium in waste was calculated from plant supplied data (Cd content of waste, amount of waste, Cd recycled (from batteries only).

The emissions/waste from the recycling of Ni-Cd batteries include the following:

- Wastewaters containing cadmium. The source of this waste is the dismantling step. This wastewater is estimated to amount to 0.32 g per ton of Cd recycled (from batteries only).

- Emissions to air occur during pyrolysis and distillation; 4.7 g per ton of Cd recycled (from batteries only).

- Waste:

- plastic boxes from batteries: 0.0011 kg/ton Cd recycled (batteries) (landfilled)

- metallic boxes from batteries: 1.23 kg/ton Cd recycled (batteries) (externally recycled)

- Fe/Cd electrodes after treatment: 1,2 kg/ton Cd recycled (batteries) (ext. recycled)

- Conc. electrolytes: 5,7 kg/ton Cd recycled (batteries) (ext. scrap treatment)

- Process slag: 154 kg CdO/ton Cd recycled (batteries) (internal treatment)

- Air treatment dust: 61kg CdO/ton Cd recycled (batteries) (internal treatment)

- Used filters: 0.138 kg/ton Cd recycled (batteries) (internal treatment)

- Rainwater sludges: 0.0016 kg/ton Cd recycled (batteries) (internal treatment)

In Table 2.2.6 a summary  is given of the Cd processing facilities in the world along with their location, type and estimated processing capacity (Morrow, 1999).

Table 2.2.6: Worldwide Cd processing facilities

| Company | Location | Type | Capacity (tonnes of Ni-Cd/year) |
| --- | --- | --- | --- |
| Accurec Gmbh | Germany | NiCd Recycler | 1,000 |
| INMETCO | USA | Stainless steel | 3,000 |
| Japan Recycle Center | Japan/Korea | NiCd recycler | 3,000 |
| Kansai Catalist | Japan | Zinc refinery | 500 |
| Mitsui Mining & Smelting | Japan | Zinc Refinery | 1,800 |
| SAFT AB | Sweden | NiCd Recycler | 1,500 |
| SNAM | France | NiCd Recycler | 5,400* |
| Toho Zinc Co, Ltd | Japan | Zinc Refinery | 1,700 |

*: SNAM St. Quentin stopped its recycling activities (2001), it has now become a battery sorting plant, all recycling capacity is transferred to the Viviez site.

The present capacities of the world’s Ni-Cd battery recycling plants vary from 500 tonnes to 5,400 tonnes with a present total effective capacity of approximately 15,000 tonnes (Morrow and Keating, 1999). The total EU capacity is estimated at 7,900 ton.

The facilities located in the EU i.e. SAFT AB (Sweden), SNAM (France), and ACCUREC (Germany) are being considered in this report.

##### Mass balance

A complete overview of the mass balance for cadmium in the EU for the reference year 1996 is given in figure 2.1.2.1 (section 2.1.2.1). The production volume of cadmium in the EU in 1996 is estimated to be 5,808 tonnes/year. Corrected for import/export 5,528 tonnes/year is available for different applications. Approximately 2,733 tonnes/year is used for battery manufacturing which equals approximately 47 % of the cadmium being produced in Europe. The EU regional consumption of cadmium reaches the value of 2,638 tonnes, which are distributed for 75.2 % to Ni-Cd batteries, 14.9 % to pigments, 5 % to stabilisers and 5 % into alloys and plating.

Table 2.2.7:	Cadmium consumption in the Western World (1990 and 1994) or EU (1996) by application

| Application | % of total consumption |
| --- | --- |
|  | 1990a | 1994a | 1996b |
| Ni-Cd batteries | 55 | 60 | 75.2 |
| Cadmium pigments | 20 | 16 | 14.9 |
| Stabilisers for PVC | 10 | 12 | 5 |
| Protective coatings | 8 | 7 | 4 |
| Cadmium containing alloys | 3 | 2 | 0.9 |
| Miscellaneous | 4 | 3 | < 0.1 |
| Total | 100 | 100 | 100 |
| Total production in the Western world (in tonnes) | 15,900c | 16,500c | 13, 840c |

a Source: Cadmium Association, OECD Risk Reduction Monograph N° 5 (1994); b source: mass balance (section: 2.1.2.1), EU consumption only; c Source: World Bureau of Metal Statistics (2000), production in the Western world (does not include Central and Eastern European countries)

Updated (year 2000) and detailed mass balances for industrial and sealed/portable Ni-Cd batteries (Cd content) are presented in Figures 2.2.5 and 2.2.6 respectively.

Figure 2.2.5: Industrial Ni-Cd batteries mass balance (EU-16 + Switzerland, Year 2000) (Cadmium content)

(CollectNiCad, 2002a, revised July 2002)

Figure 2.2.6: Portable Ni-Cd batteries mass balance (EU-16 + Switzerland, Year 2000) (Cadmium content)

(CollectNiCad, 2002a, revised July 2002)

##### Ni-Cd batteries producing/recycling companies

In the present study the exposure data were generated by a number of companies that collaborated voluntarily in the data collection (Industry Questionnaire, 1998 and update questionnaire 2000/2001). The list of companies given in Table 2.2.8 is considered as giving a complete overview of the Ni-Cd batteries producing/recycling companies.

Table 2.2.8: Companies producing/recycling Ni-Cd batteries in EU

| Ni-Cd producers |
| --- |
| Country | Location | Company |
| France | Roullet St. Estephe | SAFT Nersac |
|  | Bordeaux | SAFT Bordeaux |
| Germany | Duisburg | Friwo (EXIDE-group)c |
|  | Brilon | Hoppecke |
|  | Zwickau | GAZ (Zwickau) |
| Spain | Torrejon De Ardoz/ Madrid | EMISA (EXIDE- group)b |
| Sweden | Oskarhamn | SAFT-ABa |
| Ni-Cd recyclers |
| Country | Location | Company |
| France | Viviez | SNAM |
| Germany | Mülheim | ACCUREC |
| Sweden | Oskarhamn | SAFT-ABa |

a production and recycling at the same site

b EMISA stopped the manufacturing of Ni-Cd batteries in 2003, SAFT, May 2003.

c FRIWO, production stopped (year?), ICdA, pers.com. 2005.

SNAM St. Quentin stopped recycling (2001) with transfer of recycling capacity to the site of Viviez; VARTA stopped production (end 2000); SANYO: no production of battery cells in the EU, only assembly of imported constituents, therefore not included under manufacturers (pers. comm. 2001); PHILIPS stopped manufacturing cells and shifted to assembly (of non-EU manufactured cells into packs) only since June 2001, Panasonic (former Philips), letter 30.09.02.

At world scale other major manufacturers are Sanyo, Panasonic, GP Batteries, BYD and many of them are importers of batteries incorporated in OEMs equipment.

#### Market and sales data

##### General

Portable rechargeable batteries are utilised for a wide variety of products and applications. The most important application fields are Cordless Power Tools (CPT), Emergency Lighting Units (ELU) and applications in various Electrical and Electronic Equipment (EEE). Industrial applications of rechargeable batteries include military and space applications, transportation applications, power systems such as reserve power supply for industrial processes.

The nickel-cadmium portable battery market has been analysed in several different ways, in some cases according to geography, in others according to millions of cells sold, and yet in others in terms of the total sales value. In compiling these data, in particular those related to the historical market, EURAS has relied heavily on work done by Industry (e.g. CollectNiCad, 2000c).

##### Portable Nickel-Cadmium batteries

###### General

A compilation of the available data from different data sources on Ni-Cd battery sales in the EU is given in Table 2.2.9.

Table 2.2.9:	Summary of the market data (million units) available on portable Ni-Cd batteries in the EU

| Year | Market study |
| --- | --- |
|  | ERMa | EPBAb | Nomurac | SANYOd | SAFTe | CollectNiCad1f | CollectNiCd2f |
| 1970 |  |  |  |  | 12.5 |  |  |
| 1975 |  |  |  |  | 21 |  |  |
| 1980 |  |  |  |  | 42 |  |  |
| 1985 | 66 | 66 |  |  |  |  |  |
| 1986 |  |  |  |  |  |  |  |
| 1987 |  |  |  |  | 143 |  |  |
| 1988 |  |  |  |  | 177 |  |  |
| 1989 |  |  | 201 |  |  |  |  |
| 1990 | 203 | 203 | 226.5 |  |  |  |  |
| 1991 |  | 286 | 276 |  |  |  |  |
| 1992 |  |  | 287 |  |  |  |  |
| 1993 |  |  | 315 | 310 |  |  |  |
| 1994 |  | 244 | 343 | 350 |  |  |  |
| 1995 | 620 | 564 | 356 | 360 |  |  |  |
| 1996 |  | 213 | 334 | 290 |  |  |  |
| 1997 |  | 233 | 356 | 260 |  |  |  |
| 1998 |  | 236 | 353 | 250 |  |  |  |
| 1999 |  |  | 352 | 250 |  | 338 | 343 |

a ERM (1997)

b EPBA production sheets

c Nomura (1994) in CollectNiCad 2000c

d Carcone (1998) in CollectNiCad 2000c

e Eloy (in CollectNiCad 2000c

f CollectNiCad(2000c)

The results of the ERM study have been based on data provided by EPBA (European Portable Battery Association). While the presented results for the years 1985 and 1990 are in concordance with the results of the other studies the figure of 1995 is clearly out of scope. The main reason for this discrepancy is the assumption taken in the other market studies in deducing the EU share from the world market data. The EU market share in the ERM study mounts up to 40 % of the world market in 1995, while the EU world market share in the other studies have been assumed to be respectively 25 % in the Nomura and SANYO study and 20 % for the SAFT study. The latest survey conducted by CollectNiCad (CollectNiCad, 2000c) supports these latter suppositions and will be discussed in more detail here below.

The European sales volume for the year 1999 for portable  Ni-Cd batteries has been established) on the basis of data obtained from battery manufacturers and original equipment manufacturers O’EM's. Two different and independent methodologies have been used.

The first method (CollectNiCad. 1) calculates the total sales of Ni-Cd batteries from the number of cells used in the three major application areas: cordless power tools, emergency lighting, household equipment (shavers, dust busters, dental care, ...), telecommunications and the sales of single cells.  In order to translate the number of cells into a weight estimate an average weight of 38.0 g of one cell has been assumed, calculated from the total number of cells introduced on the EU Countries market.

The second method (CollectNiCad 2) is based on production data (in number of cells and in tons of batteries) of all Ni-Cd battery manufacturers active in Europe and corrected for import/export ratios of cells and packs as well as of batteries incorporated in electrical and electronic equipment.

###### Data for portable Ni-Cd Batteries by market segments/applications (CollectNiCad. 1)

For the breakdown of the market data by application an in depth analysis was performed of the European sales of portable Ni-Cd batteries in the three major applications areas: cordless power tools, emergency lighting and household and ‘electrical and electronic equipment’ (EEE).

Table 2.2.10 provides a summary of the market data by application. Those data show a total annual market of 12,700 tons in 1999.

Table 2.2.10: Portable Ni-Cd batteries EU market, sales by application (million cells/year) reference year 1999.

| Electrical and Electronic Equipment (EEE) |
| --- |
| Application | Average weight/cell (g) | Sales (million cells/year) |
| Household equipment | 22 | 28 |
| Dust buster | 48 | 12 |
| Toys | 55 | 5 |
| Audio-Video | 26 | 10 |
| Single cells & others | 22 | 54 |
| Cordless phones | 14 | 50 |
| Emergency lighting |
| Application | Average weight/cell (g) | Sales (million cells/year) |
| Emergency light | 120 | 26 |
| Power tools |
| Application | Average weight/cell (g) | Sales (million cells/year) |
| Cordless tool | 41 | 138 |
| Others |
| Application | Average weight/cell (g) | Sales (million cells/year) |
| Medical | 20 | 10 |
| Military | 40 | 5 |
| Average weight/unit | 37.8 |  |
| Total sales |  | 338 |

Source: CollectNiCad (2000d)

The average weight of approximately 38 g for a portable Ni-Cd battery is used in the further calculations

###### Data for portable Ni-Cd Batteries based on production data (CollectNiCad 2)

The data obtained by the second method are presented in Table 2.2.11.

Table 2.2.11: Overview EU market corrected for import and export in 1999

|  | Local annual sales (millions of cells) | Domestic sales (%) | Export sales (%) | Import Europe (%) | Net EU market (millions of cells) |
| --- | --- | --- | --- | --- | --- |
| Japan | 158 | n.d. | 50 | 30 | 23.7 |
| Europe | 324 | 65 | 35 |  | 210.6 |
| North America | 457 | n.d. | 15 | 50 | 34.3 |
| Asia | 530 | n.d. | 70 | 20 | 74.2 |
| Total | 1,469 | n.d. | n.d. | n.d. | 342.8 |

n.d.: no data available

Those data indicate that a total market of approximately 1,4 billion of Ni-Cd cells have been reached in 1998 and 1999. To evaluate the market in the E.U. countries the import-export of Ni-Cd cells assembled into packs and of packs incorporated in EEE were taken into account (Table 2.2.11). The net EU market contribution for each country/continent was calculated with the following formula:

Net EU market contribution = Local annual sales X export (%) X import Europe (%).

According to Table 2.2.11, 342.8 millions of cells have been sold in 1999 within the 15 E.U. Member States corresponding to approximately 23.3 % of the world market. The assumption of the EU market share of 20-25 % is therefore confirmed and will be used to select data to built a historical market curve. In this respect the high ERM figure for 1995 is being rejected.

###### Historical market  development

In order to make any predictions on the amounts of batteries available for collection and/or disposal it is imperative to have a good picture of the historical market development. In Table 2.2.12 the selected data for the portable consumer/sealed portable market are summarised. To express these market figures in tonnes/year these values have been multiplied with the estimated average unit weight of 38 grams. Missing values were extracted by interpolation.

Table 2.2.12: Overview of the historical reference data for portable Ni-Cd batteries

| Year | millions/cells | tonnes/year | Year | millions/cells | tonnes/year |
| --- | --- | --- | --- | --- | --- |
| 1980 | 42 | 1,596 | 1991 | 276 | 10,488 |
| 1981 | n.d | 1,778 | 1992 | 287 | 10,906 |
| 1982 | n.d | 1,960 | 1993 | 315 | 11,970 |
| 1983 | n.d | 2,142 | 1994 | 343 | 13,034 |
| 1984 | n.d | 2,324 | 1995 | 356 | 13,528 |
| 1985 | 66 | 2,508 | 1996 | 334 | 12,692 |
| 1986 | n.d | 3,971 | 1997 | 356 | 13,528 |
| 1987 | 143 | 5,434 | 1998 | 353 | 13,414 |
| 1988 | 177 | 6,726 | 1999 | 352 | 13,376 |
| 1989 | 201 | 7,638 | 2000 | 314 | 11,930 |
| 1990 | 226.5 | 8,607 | 2001 | 275 | 10,995 |

n.d : no data available

figures denoted in italics are interpolated

##### Industrial Ni-Cd batteries (CollectNiCad 2000c)

The European market for industrial batteries can be split into a number of well-defined sectors as follows:

- Standby, or stationary, applications - safety, and back-up systems at airports, hospitals, power stations, offshore installations etc.

- Transportation - railways, metro cars, etc.

- Aviation - starting of engines, oilboard safety systems, etc.

- Electric vehicles (EV)

The batteries within the two largest segments - standby and transportation - are used within a country's infrastructure. The need for batteries for new installations is the largest during this infrastructure development phase. Batteries for standby applications are often purchased by equipment manufacturer (OEM) and delivered together with the equipment to the user. Many of these OEM's are situated in Western Europe while the users are situated in e.g. the Middle East and Far East.  Thus, the batteries are purchased by and invoiced to a European customer, but they are very often re-exported to other parts of the world. In some of the Member states with important OEM'S, the re-export factor of standby batteries can be as high as 50 %.

Batteries for transportation and aviation purposes are to a higher extent delivered directly to the end user and the re-export factor is lower (15 %). The EV (Electric Vehicles) market is still at a low level. Main part of the EV nickel-cadmium is produced in EU and is used within EU.

The volumes of the different industrial Ni-Cd batteries for use within the EU market has been estimated from data of the three major suppliers (representing more than 95 % of the market supply) with addition for an estimated volume of imported batteries and are listed in Table 2.2.13.

Table  2.2.13: Industrial Ni-Cd batteries EU market sales (tonnes/y)

| Year | Industrial Ni-Cd battery (tonnes/year) |
| --- | --- |
| 1995 | 3,242 |
| 1996 | 3,608 |
| 1997 | 3,625 |
| 1998 | 3,964 |
| 1999 | 3,697 |
| 2000 | 3,566 |

Sources: original references Saft, Exide and Hoppecke in CollectNiCad (2000c,2002)

From this table it is clear that the industrial batteries’ market has reached a stable level of 3,500 to 4,000 tons per year. Cross-validation with the ERM study shows the same magnitude (4,000 tons in 1995).

##### Country by country data

The data presented in this section are obtained mainly by two ways. The first was through the Questionnaire on Batteries sent out in 2000 by the MSR to the national authorities of the EU and Norway, the collector organisations as well as the EU associations of manufacturers (i.e. EPBA). The second series of data was compiled via the efforts run in parallel by Industry (CollectNiCad 2000d).

It needs to be mentioned that to date the information in this document is rather limited and no attempt was made to verify the correctness of each figure. Another remark concerns the fact that figures obtained via different sources are not necessarily independently generated (e.g. the data provided by the national collector organisations may be the only data available at the authority level). Finally the data obtained via different ways may in some case be ‘complementary’ to each other (e.g. the data on collection as provided by the collection organisation versus Industry’s data obtained from the recyclers) and thus allowing for at least some approximate direct check by comparison.

Data sources:

Responders to the Questionnaire are indicated by a figure between brackets in the last column of the Tables and accompanied by details in a footnote, if needed. The figure (1) is used when data were obtained from the MS (national authority). The indication (1C) is used when Collection organisation(s) replied. The main primary generators of data in so far as these are known, are indicated under the corresponding subsections. Data compiled and submitted by CollectNiCad are indicated by the figure (2).

Data errors and deviations:

Besides the well known sources of errors e.g. reporting, (de)coding, transcription, etc deviation of data generated by different types of sources may be due to (a different degree of taking into account) stockpiling, as well as import and/or export of new, spent or recycled material or appliances containing batteries. On the other hand, differences in used definitions of e.g. ‘portable’, ‘consumer’ and ‘industrial’ but also ‘marketing’ and the specific sorting or not of Ni-Cds may cause divergences between figures generated by different MS, collector organisations and Industry. Finally, difficulties may arise due to the different units in which marketing figures versus collection amounts are expressed. The former are in generally in units (or mAh) while the latter are reported in weight units. Together with the variation in battery weight, this may cause deviations.

###### Portable Ni-Cd batteries

A summary of the available data is given in Table 2.2.14 for consumer/sealed portable Ni-Cd batteries.

Table 2.2.14: Portable Ni-Cd battery market data (tonnes/year) for EU countries

| Country | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | Reference |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Austria |  |  |  | 62 | 98 | 97 309 | 286 | 247 | (1C)* (2) |
| Belgium |  |  | 381 | 388 | 368 | 327 | 302 | 261 | (1) (2) |
| Denmark | 214b | 233b | 218-328b | 291 | 242 | 210 137 | 127 | 110 | (1C) (2) |
| Finlanda |  |  | 250 |  |  | 134 | 124 | 107 | (1) (2) |
| France |  |  |  |  |  | 130 2,212 | 2,046 | 1,768 | (1)* (2) |
| Germany | 3,095 | 2,642 | 2,334 | 2,214 | 2,050 | 3,210 2,261 | 2,091 | 2,880 1,808 | (1C) (2) |
| Greece |  |  |  |  |  | 404 | 374 | 323 | (2) |
| Ireland |  |  |  |  |  | 233 | 216 | 186 | (2) |
| Italy |  |  |  |  |  | 1,567 | 1,449 | 1,253 | (2) |
| Luxembourg |  |  |  |  |  | 25 | 23 | 20 | (2) |
| The Netherlands |  |  |  |  |  | 652 | 603 | 521 | (2) |
| Portugal |  |  |  |  |  | 241 | 223 | 193 | (2) |
| Spain |  |  |  |  |  | 1,168 | 1,080 | 934 | (2) |
| Sweden | 486 | 338 | 333 | 328 | 190 | 175 249 | 230 | 199 | (1) (2) |
| UKa | 2,001 | 1,766 | 1,958 | 2,167 | 2,652 | 2,983 2,706 | 2,503 | 2,163 | (1) (2) |
| Norway |  | 199 | 187 | 124 | 175 | 215 125 | 116 | 100 | (1) (2) |
| Total EU-16a |  |  |  |  |  | 14,005 | 11,793 | 11,265 |  |
| Switzerland |  |  |  |  |  | 274 | 253 |  | (2) |
| Totala |  |  |  |  |  | 14,279 | 12,046 |  |  |

(1): Questionnaire Member States (2000). Primary sources: (B): BEBAT, (F): only SCRA members, (UK): ERM, (S): based on information from importers and manufacturers, updated ’02: Ni-Cd batteries that have been put on the Swedish market, as reported to the Swedish EPA, (NO): sealed cells, separate or in appliances, in this table: with the assumption that all cells in appliances are totally attributed to consumer application.

(1C): Questionnaire (2000) Collection organisations. (A) : only data via UFB (Incl. some industrial uses, DK: Danish Battery Association, (DE): Data provided by ARGE Batterien, data for 2001 submitted by UBA, 2002.

* incomplete data-set(2): Industry Country by country data (CollectNiCad  2000d)

a  upper limit used and assuming average battery cadmium content of 13.8 % cfr. Table 2.2.5

b Miljoprojekt (2000)

For the data submitted by the authorities, the way the data are obtained/generated and the surrounding uncertainties are in general not explicitly specified.  Industry (CollectNiCad) compiled data mainly through the information given by manufacturers and their commercial network (no primary data are available).

Six Member States have submitted their figures on the sales of portable Ni-Cd batteries. Additional data for 17 countries were provided by CollectNiCad (2000f) for the year 1999. In general the latter figures are in concordance with the figures reported by the Member States. However, the market figures provided for France collated from the Member State Questionnaire are incomplete (130 vs. 2,212 tonnes/year). In comparison with countries of a similar population size (UK, Italy) the industry’s estimate seems a more realistic one. The industry’s estimates for Denmark,  Norway and Germany are approximately 30-40 % lower than the figures provided by these countries. According to Industry the differences in the market data for Germany are mainly related to exports. A considerable amount is claimed to represent exported batteries, amount which is said by Industry to be neglected as such in the German data provided by the DE MS (neither primary data nor details from Arge Batterien were submitted to the Rapporteur).

Overall it can be concluded that approximately a maximum of 14,000 tonnes of portable Ni-Cd batteries is put on the EU-16 market (including Norway) for the reference year 1999.

Recent data given by industry indicate a decrease in the weight volume introduced on the market with respectively 11,930 and 10,995 tonnes/year for the years 2000 and 2001.

###### Industrial batteries

Very few countries replied on the Questionnaire 2000. The primary data sources for Industry’s submitted data are in the first place the manufacturers. An overview of the present available data is given in Table 2.2.15 for industrial Ni-Cd batteries.

Table 2.2.15: Industrial Ni-Cd battery market data (tonnes/year) for the EU member states

| Country | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | Reference |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Austria |  |  |  |  |  | 144 | (2) |
| Belgium |  |  |  |  |  | 97 | (2) |
| Denmark |  |  |  | 48-54c |  | 20 | (2) |
| Finlanda |  |  | 23 | 121 | 104 | 68 87 | (1) (2) |
| France |  |  |  |  |  | 1,097 | (2) |
| Germany |  |  |  |  |  | 213? 251 | (1*) (2) |
| Greece |  |  |  |  |  | 230 | (2) |
| Ireland |  |  |  |  |  |  |  |
| Italy |  |  |  |  |  | 243 | (2) |
| Luxembourg |  |  |  |  |  | 1 | (2) |
| The Netherlands |  |  |  |  |  | 80 | (2) |
| Portugal |  |  |  |  |  | 13 | (2) |
| Spain |  |  |  |  |  | 758 | (2) |
| Sweden | 250 | 200 | 200 | 200 | 150 | 150 142 | (1) (2) |
| UKa | 853 | 858 | 862 | 907 | 958 | 1,008 404b | (1) (2) |
| Norway |  | 95 | 104 | 119 | 84 | 57 1 | (1) (2) |
| Total EU-16a |  |  |  |  |  | 3,632 |  |
| Switzerland |  |  |  |  |  | 93 | (2) |
| Totala |  |  |  |  |  | 3,725 |  |

(1): Questionnaire Member States (2000) Primary sources: (B): BEBAT, (F): only SCRA members, (UK): ERM, (S): SAFT

(1C): Questionnaire (2000) Collection organisations (DE) : only data from VfW-REBAT (consumer/sealed portable + industrial): data from ZVEI  not available

(2): Industry Country by country data (CollectNiCad, 2000f)

*: incomplete data-set on country basis

a  upper limit used except for UK figure(s) that were corrected cfr text

b UK + Ireland

c Miljoproject (2000)

Four Member States have submitted market data on industrial Ni-Cd batteries. Additional data for 17 countries were provided for the year 1999 by industry. For the few cases where comparison is possible, the figures are in concordance with the figures provided by the Member States. Industry’s estimate for the UK is much lower then the figure submitted by the UK-MS (DTI). ERM (on behalf of UK) provided this estimate based on sales information from SAFT and Exide ranging from 600-1000 tonnes. It was acknowledged by ERM that they did not correct for export that is estimated to be 50 % (ERM, Pers. com., 2000).  Applying the export rate gives an estimated figure for the UK market ranging from 400 to 670 tonnes (the figure ‘404’ is used for calculating the totals for the year 1999).

Overall approximately 3,700 tonnes of industrial Ni-Cd batteries is put on the EU-16 market (EU including Norway) for the reference year 1999.

###### Market trends

Most of the data related to market evolution come from Industry. The data submitted by CollectNiCad relate to the past and to semi-quantitative information on the application’s market shares (see paragraph below). No precise information is (made) available on how the Ni-Cd battery market is likely to evolve in the future.

Ni-Cd batteries can be classified into four lines of products according to their market applications: industrial batteries, Emergency Lighting units (ELU), Cordless Power Tools (CPT) and applications in numerous Electrical and Electronic Equipment (EEE).

The largest application field for Ni-Cd batteries and a growing market have become the CPT applications (separated between the Professionals and Consumer market). The ELU market is under a slight growth rate with higher market shares in countries like France, United Kingdom, Italy and Spain, by opposition to Germany where centralised units powered by lead-acid batteries are used. The EEE market, which has been the largest market segment for Ni-Cd batteries during the first half of the nineties, is declining. From 1995, Ni-Cd batteries have gradually being replaced on the market by other types of batteries like the Nickel-Metal Hydride, the Lithium-Ion and the Lithium-Polymer batteries. Industrial Ni-Cd batteries are continuously in competition with lead-acid batteries but forms a stable market. A summary of the market shares for the different applications for the years 1999 and 2000 is given in Table 2.2.16 and Table 2.2.17.

Table 2.2.16: Weight distribution in percent of the market share of Ni-Cd batteries by applications- reference year 1999

| Industrial 22 % (Stable) | Portable CPT 35 % ( growing) |
| --- | --- |
| Portable ELU 18 % (Stable) | Portable EEE 25 % (Declining) |

Source: CollectNiCad (2000e)

Table 2.2.17: Weight distribution in percent of the market share of Ni-Cd batteries by applications (reference year 2000)

| Industrial 24 % (Stable) | Portable CPT 35 % (growing) |
| --- | --- |
| Portable ELU 19 % (Stable) | Portable EEE 16 % (Declining) |
| Specialities (Aviation, Industrial Comm. & Computing) 6 % and growing |  |

Source: CollectNiCad (2002b)

From the previous sections (section 2.2.2.4.4.1 and 2.2.2.4.4.3) it can be concluded that the Ni-Cd market has increased significantly in the 80's to reach a more or less stable level in the late 1990's of around 13,500 tons/year for consumer/sealed portable nickel-cadmium batteries and 3,500 to 4,000 tons/year for the industrial nickel-cadmium battery market.

To date, no market projections are available for the amount of portable Ni-Cd batteries, which will be put on the market in the future. A study by ERM (2000) employed a positive common growth rate for all types of portable secondary batteries. However, since the market evolution is stated to be mainly technology driven and, as there is confidential business implication, it is difficult to get any good specific estimate for the growth rate of Ni-Cd chemistry applications.

Between 1996 and 1999 the portable Ni-Cd battery market in the EU seems to be oscillating around 13,000 -14,000 tonnes. Although recent figures for 2000 and 2001 indicate a decrease in sales, the figure of 13,500 tonnes has been chosen as a worst case scenario to forecast future battery waste arising. The industrial batteries remain at the level of 3,600 tonnes.

#### COLLECTION/RECYCLING DATA

##### Country by country data

###### Portable Nickel-cadmium batteries

Data on the Ni-Cd battery collection/recycling efforts for individual EU countries were collated from the Questionnaire 2000. In addition Industry (CollectNiCad) provided a second series of data for the year 1999 and 2000. The latter represent the amount collected and processed for recycling. An overview of the available data is given in Table 2.2.18 for portable Ni-Cd batteries.

Table 2.2.18: Total weight (tonnes/year) of collected/recycled portable Ni-Cd batteries for the individual EU countries

| Country | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | Reference |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Austria | 22.5 | 26.7 | 42.5 | 61.8 | 97 | 97 | 53 | 84 | (2) (A) |
| Belgium | 9 | 10 | 10 | 37 50 | 79 66 | 59 59 | 177 115 | 70 | (1) (2) (B) |
| Denmark | 34 34 | 54 54 | 9 -- | 94 103 | 80 78 | 66 | 59 | 108 | (1C) (2) (Dk) |
| Finland |  | 1 | 6 |  | 91 12 | 113 5 | 10 | 1 | (1) (2) |
| France | 33 60 | 50 35 | 65 70 | 95 105 | 100 92 | 140 | 140 | 182 | (1) (2) |
| Germany | 220 | 206 | 303 | 440 | 403 | 596 | 1,001 950 | 921 | (1) (2) (GRS) |
| Greece |  |  |  |  |  |  | 1 | 1 | (2) |
| Ireland |  |  |  |  |  | 9 | 11 | 5 | (2) |
| Italy | 1 |  |  | 2 | 1 | 25 | 33 | 36 | (2) |
| Luxembourg |  |  |  |  | 5 | 5 | 5 | 5 | (2) |
| The Netherlands | 10 | 29 | 35 | 75 | 119 | 150 | 210 | 160 | (2) (NL) |
| Portugal |  |  |  |  |  |  | 1 | 1 | (2) |
| Spain |  | 4 |  |  |  | 38 | 30 | 66 | (2) |
| Sweden | 111 | 112 108 | 113 110 | 141 142 | 144 143 | 170 169 | 142 147 | 167 167 | (1) (2) |
| UK | 18 | 63 | 72 | 94 | 50 46 | 106 75 | 78 | 93 | (1) (2) |
| Norway |  | 2 | 10 | 66 | 63 | 53 12 | 10 | 43 | (1) (2) |
| Total EU-16a | 459 | 539 | 663 | 1,106 | 1,125 | 1,446 | 1,852 | 1,943 |  |
| Switzerland | 34 | 96 | 46 | 21 | 114 | 48 | 194 | 198 | (2) |
| Totala |  |  |  |  |  | 1,494 | 2,046 | 2,141 | (2) |

(1): Questionnaire (2000) Member States. Sources: (B):data from BEBAT  figure of 2000 is still provisional: lower figure: amount of sorted batteries, upper figure: amount of recycled batteries during the year 2000, (F): Ministere de l’amenagement du territoire et de l’environment, (UK): data as from SNAM, (S):data as from SAFT, (DE): data from UBA, comments 2002.

(1C): Questionnaire (2000) Collection organisation. DK: Danish Battery Association: figure of ’95 includes collection till 31 March’96

(2): Industry Country by country data (CollectNiCad, 2000f & 2001a) (A) Rumpold AG, (B) BEBAT, (Dk) Battery Association Denmark, (GRS) Gemeinsames Rücknamesystem Batterien, (NL) STIBAT

a = lower limit used

The primary data source for Member states is data on collection as obtained via governmental or private collection organisations. Additional verification procedures by external independent organisms may enhance the confidence in these figures. Industry (CollectNiCad) compiled its series of figures through information obtained via the recycling companies and/or collection organisations (primary data are not available to the MSR). The transboundary movement of spent Ni-Cd batteries is liable to the Basel Convention administrative rules and offers a means to trace back collected amounts on national basis.

For the few cases where comparison is possible, no large differences are observed between the data provided by industry and the Member States. Overall approximately 1,852 ton of portable Ni-Cd batteries has been collected in the EU-16 for the year 2000 and 1,943 ton for the reference year 2001. Countries for which no (or poor) data are available have most often not yet a dedicated Ni-Cd collection system in place. A short overview of the situation in the EU is given by CollectNiCad in Table 2.2.19. The information on existing Ni-Cd collection schemes and programs present in Europe gathered by the Questionnaire is limited (only DK, S, UK, F, FIN and NO) and mostly does not provide many further details than those already reported in other publications (ERM, 1997; EUPHEMET, 2000 and CollectNiCad, 2000f). More details are available in Annex I.

Table 2.2.19: Overview of Ni-Cd Collection programs running in various European countries

| Country | Collection Ni-Cd | Collection all type (primary and rechargeables) | Start | NCRAa | Sorting | Financial system (€/kg) |
| --- | --- | --- | --- | --- | --- | --- |
| Austria | Yes | Yes | 1990 | UFB | Yes | 2 |
| Belgium | Yes | Yes | 1993 | BEBAT | Yes | 3 |
| Denmark | Yes* |  | 1996** | Ministry** | No* | 16 |
| Finland | Yes |  |  | Municipalities/ importers/retailers | Some |  |
| France | Yes |  | 1999 | SCRA | Yes | 2 |
| Germany | Yes | Yes | 1998 | GRS | Yes | 2 |
| Greece |  |  |  |  |  |  |
| Italy |  |  |  |  |  |  |
| Luxembourg |  |  |  |  |  |  |
| Portugal |  |  |  |  |  |  |
| Spain | Yes-local | Yes-local | 1999 |  |  |  |
| Sweden | Yes | Yes | 1998 | Municipalities | Yes | 34 |
| The Netherlands | Yes | Yes | 1995 | STIBAT | Yes | 2 |
| UK + Ireland | Partial |  | 1994 | REBAT |  |  |
| Norway | Yes |  | 1997 | Batteriretur |  |  |
| Switzerland | Yes | Yes | 1990 | BESO | Yes | 3-5 |

Source: CollectNiCad (2000g), adapted.

*: will change in future: all batteries (primary and rechargeable will have to be collected); **: before that date: other in place e.g. Danish Battery Association

a NCRA = National Collection and Recycling Association

###### Industrial Nickel-Cadmium batteries

Data on the Ni-Cd battery collection/recycling efforts for individual EU countries were collated from the questionnaire 2000. In addition CollectNiCad provided data for the year 1999. An overview of the available data for industrial Ni-Cd batteries is given in Table 2.2.20.

Table 2.2.20: Total weight (tonnes/year) of collected/recycled industrial Ni-Cd batteries for the individual EU countries

| Country | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | Reference |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Austria |  | 91 | 115 | 173 |  | 148 | 304 | 134 | (2) |
| Belgium | 14 | 105 | 71 | 140 | 112 | 65 | 91 | 104 | (2) |
| Denmark |  | 3 | 5 14b | 3 | 1 | 7 | 11 | 34 | (2) |
| Finland |  | 41 | 47 | 70 | 70 98 | 160 131 | 82 | 188 | (1) (2) |
| France | 158 528 | 153 560 | 251 1,100 | 383 560 | 400 618 | 529 | 817 | 780 | (1) (2) |
| Germany | 935 | 1,074 | 987 | 1,124 | 1,295 | 998 | 799 | 826 | (2) |
| Greece |  |  | 3 |  |  |  |  |  |  |
| Ireland |  |  |  |  |  | 20 | 8 | 8 | (2) |
| Italy | 31 | 103 | 131 | 151 | 41 | 125 | 194 | 190 | (2) |
| Luxem-bourg |  |  |  | 4 | 3 |  | 10 | 5 | (2) |
| The Nether-lands | 83 | 127 | 261 | 185 | 172 | 150 | 146 | 124 | (2) |
| Portugal |  |  |  |  |  |  |  |  |  |
| Spain |  | 12 |  | 41 | 181 | 160 | 94 | 154 | (2) |
| Sweden | 136 | 157 147 | 254 254 | 204 204 | 189 189 | 200 | 216 | 295 | (1) (2) |
| UK | 29 | 21 | 24 | 80 | 52 51 | 112 112 | 136 | 112 | (1) (2) |
| Norway |  | 53 | 53 | 57 | 20 34 | 32 67 | 55 | 84 | (1) (2) |
| Total EU-16a |  |  |  |  |  | 2,677 | 2,963 | 3,038 |  |
| Switzer-land | 39 | 19 | 18 | 20 | 23 | 21 | 160 | 42 | (2) |

(1): Questionnaire Member States (2000) Primary sources: (B): BEBAT, (F): Ministere de l’amenagement du territoire et de l’environment, (UK): SNAM, (S):SAFT

(2): Industry Country by country data (CollectNiCad, 2000), updated for the years 2000 and 2001 (CollectNiCad, 2002)

a = lower limit used

b = Miljoprojekt (2000)

In the few cases where two sets of data are available, no large differences are observed between the data provided by industry and the Member States. Overall approximately 2,677 tonnes of industrial Ni-Cd batteries have been collected in 1999.

##### Collection rate/Collection efficiency

Data on the absolute amounts of Ni-Cd batteries being collected is presented in section 2.2.6 and was obtained from a questionnaire submitted in 2000 to the EU Member States. In addition CollectNiCad provided country by country data for the year 1999. Collection percentages mentioned in the questionnaires are not given in the Tables (2.2.18 and 2.2.20). Any comparison of these numbers should be performed with caution since most often the rationale behind the calculation of collection rates are not the same for the various EU member states. Typically, collection rates are being calculated as the percentage collected batteries of a base year sale.  In that case the collected amount corresponds to only a small percentage of same years’ sales of portable Ni-Cd batteries (e.g. UK). However, this kind of approach is difficult to apply for long life articles such as Ni-Cd batteries for which no correlation can be found between the base year sales data and the collected quantities for that same year.

So, Industry as well as Member states developed a number of alternative calculation formulas. One of the most recent is the so-called  ‘collection efficiency’ being defined by STIBAT as the ratio between the amount of Ni-Cd batteries collected over the maximally available amount for collection (STIBAT, Deauville, 1999) with the latter equalling the sum of the collected Ni-Cd batteries and the quantity of Ni-Cd batteries disposed in the municipal waste stream.

Calculating the collection efficiency

Collection efficiency =  =

Q. Ni-Cd Coll = Quantities of batteries collected separately

Q. Ni-Cd MSW = Quantities of batteries eliminated with Municipal Solid Waste

Although this equation may have advantages (i.e. independent of present market volume and battery’s lifetime) it needs to be mentioned that detailed studies dealing with the analysis of MSW are complex and for the moment limited to a few countries. Furthermore the amount of Ni-Cd batteries found in MSW might not be completely representative for all Ni-Cd batteries going into the waste stream. For example, replacement of batteries in emergency lighting units is not common. Therefore, the majority of end-of-life Ni-Cd batteries in emergency lighting become waste during building refurbishment and are generally disposed of as mixed industrial and some as municipal waste (ERM, 2000). For pure conceptual and mathematical reasons the use of a collection ratio, defined as a simple percentage of the total amount of used Ni-Cd batteries coming available for collection and that will effectively be collected for recycling, is preferred. By subtraction, the remaining amount of batteries arriving into the waste stream is obtained.

Since not all European countries have a (Ni-Cd) battery collection system in place two collection ratio’s are considered further in this report:

- 10 % collection of the Ni-Cd batteries coming available for collection: representative for a country with  a collection system with low efficiency

- 75 % collection of the Ni-Cd batteries coming available for collection: considered by Industry as representing an EU-wide realistic target (CollectNiCad, Pers. com., July 2002) and chosen to be representative for a country with a collection system with a high efficiency.

The span of 10-75 % is believed to cover all possible combinations in the EU ( limited to waste management options).  Hence, in this regard the development of country specific scenarios are not deemed necessary.

### Update data (reference year 2002)

#### Introduction

Quantitative update information regards the use of the substances in the different applications is fragmentary.

Consumption volumes are updated for the uses in batteries, in pigments and in stabilisers for those companies that participated in the updating exercise (seeTable 2.2.21).

Furthermore some producers provided tentative data regards the break-down of the quantities cadmium metal and cadmium oxide: the uses of cadmium oxide expressed as percentages of the production in 2002 are estimated as follows: batteries: 83.5%, stabilisers:  ca. 27% pigments: 1.5% and others: 4%. This latter information is substantially different from the data provided by the processors/users of the substances.

No update consumption data are available for Cd plating, alloys and others.

Table 2.2.21: Consumption data on cadmium metal and cadmium oxide for the major use applications (amounts  in metric tons and expressed as elemental cadmium)

| Year | Batteries | Pigments | Stabilisers |
| --- | --- | --- | --- |
| 2002 | 1634.6* | n.d. | in the range 50 to 150 |
| 2003 | 1725* | 299 | in the range 50 to 120 |

n.d.: no data available; *: figures based on the information provided by 3 companies

Recently, an update of the mass-balance of cadmium in the EU (year 2000-2002) was provided by industry (Figure 2.2.7). The production volume of cadmium in the EU in 2000-2002 is estimated to be 1,114 tonnes/year. Corrected for import/export 2,850 tonnes/year is available for different applications.

#### Ni-Cd Batteries

Since the previous update of information in 2002/2003, the number of companies producing Ni-Cd batteries has further decreased. The Table 2.2.22 mentions those companies that ceased the production of these batteries. Current producers are given in Table 2.2.23.

Table 2.2.22: Companies formerly producing Ni-Cd batteries and date/year of ceasing production

| Company (and plant) | Country | Date/year of production stop |
| --- | --- | --- |
| Friwo (EXIDE-group) | Germany | p.m. date to specify |
| EMISA (EXIDE- group) | Spain | 2003 |

Table 2.2.23: Current producers of Ni-Cd batteries in EU*-16

| Company (and location) | Country |
| --- | --- |
| SAFT Nersac | France |
| SAFT Bordeaux | France |
| Hoppecke | Germany |
| GAZ (Zwickau) | Germany |
| SAFT-AB | Sweden |

Table 2.2.24: Current recyclers of Ni-Cd batteries in EU*-16

| Company (and site) | Country |
| --- | --- |
| SNAM | France |
| ACCUREC | Germany |
| SAFT-AB | Sweden |

The amount of cadmium (metal and oxide) used by three out of respectively seven (for the year 2002) and five (for the year 2003) companies is approximately 1635 metric tonnes for the year 2002. A slightly higher amount is reported for the year 2003 (see Table 2.2.21).

The volume of secondary cadmium produced in the EU-16 by the recycling of batteries, production scrap and other sources, was about 974 tonnes for the year (of which 56% batteries) 2002 and 1023 tonnes for the year 2003 (of which 52% batteries). These figures are based on the information provided by 2 out of the 3 recycling companies (data of the company with highest capacity are included).

#### Cd containing Pigments

Compiled update information from the producers of cadmium containing pigments was submitted to the Rapporteur. Currently only three companies are producing these pigments in the EU-16. General Chimica and Degussa ceased production respectively in 2003 and (? p.m. date to be included; no official document delivered to the rapporteur).

Compiled data on the mass-balance of cadmium in pigments for the year 2003 was provided by the pigment producing companies and is given in Table 2.2.25.

Table 2.2.25: Mass-flow of cadmium within pigments for the year 2003 (in metric tons)

|  | Cd in pigments | Cd content |
| --- | --- | --- |
| Production | 1216 | 730 |
| Exports outside EU-16 | 750 | 450 |
| EU-16 sales | 466 | 280 |
| Imports outside EU-16 | 33 | 20 |
| EU-16 consumption | 499 | 299 |

Note: the calculation of the consumption figures assumes that the volumes of export and import of coloured articles are the same

#### Cd containing stabilisers

The production of stabilisers containing cadmium (compounds) decreased significantly since the end nineties in view of the Vinyl 2010 commitment. It should be noticed that any production of stabilisers by the companies adhering to this agreement, is destinated solely for export and cannot be sold in the EU-15. The number of producers in the EU-16 dropped to only a few. Currently only 2 companies (three sites) acknowledged to the Rapporteur that some production still took place at their sites located in Italy and Germany.

Only two of these use the priority substances as starting material in their process.

The consumption data of cadmium metal and cadmium oxide for this use are given as a range: between 50 and 150 tonnes in 2002. Somewhat lower values are given for the year 2003 (see Table 2.2.21).

Any EU production of stabilisers is for export and cannot be sold in the 15 original EU countries that are part of the Vinyl 2010 commitment.

#### Alloys, plating and other uses

For these uses, no update information was submitted to the Rapporteur.

## Legislative control measures

### EU legislation

Cadmium (and its compounds) is a multi-regulated substance: in the EEC several directives have been adopted spread over the whole spectrum of risk reduction legislative instruments actually in use in the EU i.e. limitations in the marketing and use, environmental quality standards (emission and immission standards, protection of natural resources (groundwater, drinking water)), workplace (OEL’s, etc) and consumer (see Section 4: human health part, in separate document).

The directives, regulating at the source, are the Council Directive 76/769 (10th amendment; 91/338/EEC) relating to the restrictions on the marketing and use (see Table 2.3.1), and the Council Directive 91/157/EEC on batteries and accumulators. The latter directive establishes a marketing ban on batteries and accumulators with a high mercury content as well as an obligation for Member States to undertake steps to ensure the separate collection of batteries with a view to their recovery or separate disposal. The latter obligation concerns spent batteries and accumulators containing certain amounts of cadmium, lead or mercury.

Table 2.3.1 Limitations and prohibitions on the marketing and use of Cadmium and its compounds (Directive 76/769/EEC, amendment Dir. 91/338 and Dir. 99/51/CE)

| Cd and its compounds 91/ 338/EEC | May not be used to give colour to finished products 1.1.manufactured from the substances and preparations listed below: polyvinyl chloride (PVC) (3904 10( (3904 21( (3904 22( polyurethane (PUR) (3909 50( low-density polyethylene (LDPE), (with the exception of low-density polyethylene used for the production of coloured master batch( (3901 10( cellulose acetate (CA) (3912 11( (3912 12( cellulose acetate butyrate (CAB) (3912 11( (3912 12( epoxy resins (3907 30( melamine-formaldehyde (MF) resins (3909 20( urea-formaldehyde (UF) resins (3909 10( unsaturated polyesters (UP) (3907 91( polyethylene terephtalate (PET) (3907 60( polybutylene terephthalate (PBT) transparent/general purpose polystyrene (3903 11( (3903 19( acrylonitrile methylmethacrylate (AMMA) cross-linked polyethylene (VPE) high-impact polystyrene polypropylene (PP) (3902 10( In any case, whatever their use or intended final purpose, finished products or components of products manufactured from the substances and preparations listed coloured with cadmium may not be placed on the market if their cadmium content (expressed as cadmium metal) exceeds 0.01% by mass of the plastic material. EXCEPTED for products to be coloured for safety reasons 1.2. May not be used in paints. However if the paints have a high zinc content, their residual concentration of cadmium must be as low as possible and at all events not exceed 0,1% by mass. May not be used to stabilize: 2.1. the finished products listed below manufactured from polymers or copolymers of vinylchloride: packaging materials (bags, containers, bottles, lids) office or school supplies fittings for furniture, coachwork or the like articles of apparel and clothing accessories (including gloves) floor and wall coverings impregnated, coated, covered or laminated textile fabrics imitation leather gramophone records tubes and pipes and their fittings swing doors vehicles for road transport (interior, exterior, underbody) coating of steel sheet used in construction or in industry insulation for electrical wiring In any case, whatever their use or intended final purpose the placing on the market of the above finished (components of) products is prohibited if their cadmium content (expressed as Cd metal) exceeds 0,01% by mass of the polymer. EXCEPTED for products using cadmium based stabilizers for safety reasons. 3. May not be used for cadmium plating metallic products or components of the products used in the sectors/applications listed below: Equipment and machinery for: food production agriculture cooling and freezing printing and book-binding Equipment and machinery for the production of: household goods furniture sanitary ware central heating and air conditioning plant and the manufactured products as listed in this subsection Equipment et machinery for the production of: paper and board textiles and clothing Equipment and machinery for the production of: road and agriculture vehicles rolling stock vessels industrial handling equipment et machinery and the manufactured products as listed in this subsection In any case, whatever their use or intended final purpose the placing on the market of cadmium plated products or components of such products used in the sectors/applications listed and of the products manufactured in the sectors listed is prohibited. EXCEPTED sectors: aeronautical, aerospace, mining, off shore and nuclear whose applications require high safety standards and in safety devices in road and agricultural vehicles, rolling stock and vessels. EXCEPTED electrical contacts, in any sector of use, on account of the reliability required of the apparatus on which they are installed. |
| --- | --- |
| 99/ 51 /EC | Exemptions for Austria and Sweden, already applying stricter provisions than the aforementioned, are granted until 31 December 2002, time by which the European regulations will be reconsidered and adapted to technical progress. See in this context the study reports by WS Atkins (1999a, b) and RPA Ltd (2000), on the risks to health and the environment by cadmium contained in certain products (i.e. used as a colouring agent or as stabiliser in polymers and for metal plating), as commissioned by the EC (DG Enterprise). |

In addition to Dir. 91/338/EEC, toys should also comply to Directive 88/378/EEC (‘Safety of Toys Directive’) thus fulfilling the daily limit value for cadmium for the bioavailability resulting from the use of toys i.e. 0.6 µg per day (EC, 2003). Consumer protection is further also aimed at through the establishment of regulatory standards (e.g. European Standard EN 71 part 3) in circumstances where prevention from exposure is of particular importance, i.e. in toys and articles which come into contact with food (ICdA, 1997).

Commission Regulation EC 466/2001 sets maximum levels for certain contaminants in foodstuffs.

Table 2.3.2: Commission Regulation (EC) 466/2001: Maximum levels of Cd in food from aquatic sources (Official Journal L 077 , 16/03/2001)

| Product | maximum level (mg/kg wet weight) |
| --- | --- |
| 3.2.5 Muscle meat of fish, excluding fish species listed in 3.2.5.1 | 0.05 |
| 3.2.5.1 Muscle meat of Dicologoglossa cunneata, Anguilla anguilla, Engraulis encrasicholus, Luvarus imperialis, Trachurus trachurus, Mugil labrosus labrosus, Diplodus vulgaris, Sardina pilchardus | 0.1 |
| 3.2.6 Crustaceans, excluding brown meat of crab | 0.5 |
| 3.2.7 Bivalve molluscs | 1.0 |
| 3.2.8 Cephalopods (without viscera) | 1.0 |

(information extracted from EC Working document EQS for cadmium, 2003)

End of pipe EEC directives concern putting limits to discharges/emissions of cadmium in the different environmental compartments (air, water, sewage sludge for agricultural use).

Quality objectives have been adopted for the workplace as well as for different environmental compartments.

Water

Standards for surface freshwater intended for for the abstraction of drinking water, and for water intended for human consumption have been fixed resp. through the Council Directives 75/440/EEC (will repealed in december 2007 due to 2000/60/EC; the Water Framework Directive) and 80/778/EEC (+ revisions) (will be repealed in january 2004 due to 98/83/EC )

(MAC: max. admissible concentration, GL: Guide Levels, MRC minimum required concentration). The reference detection method in this medium is given: i.e. atomic absorption.

Table 2.3.3 Directive 75/440/EEC concerning the quality required of surface water intended for the abstraction of drinking water iin the Member States

| Standard in mg/l | Details | Source |
| --- | --- | --- |
| 0.005 mg/l | Permissible level; >or= 95% of samples Guidance levels for several water parameters pH, zinc, max. Susp. matter,… | O.J. L 194 , 1975 |
| Standards adopted in Member States |
| n.d. | n.d. | n.d. |

Table 2.3.4 Directive 80/778/EEC and Directive 98/83/EC on water for human consumption

| Standard in µg/l | Details | Source |
| --- | --- | --- |
| 5µg/l | MAC; min. total hardness 60mg/l Ca (or analogous cations | O.J. N° L 229, 1981 O.J. N° L 330, 1998 |
| Standards adopted in Member States |
| n.d. | n.d. | n.d. |

Council Directive 80/68/EEC for groundwater comprises cadmium compounds in List I for which MS must prohibit the direct and avoid the indirect introduction to the groundwater. The directive shall be repealed in 2013 due to 2000/60/EC. Specific measures to prevent and control groundwater pollution will be adopted within the implementation of art. 17 of 2000/60/EC.

Table 2.3.5 Directive 80/68/EEC: on the protection of groundwater against pollution caused by certain dangerous substances.

| No explicit standard |  |  |
| --- | --- | --- |
| Standards adopted in Member States |
| n.d. | n.d. | n.d. |

In Council Directive 78/659/EEC on the quality of fresh water for fish and Council Directive 79/923 on shellfish waters, no specific cadmium concentration is given. The latter Directive only stipulates that no harmful effects on shellfish and larvae should occur and aim good quality of shellfish products. Atomic absorption spectrometry preceded if needed by concentration and/or extraction, is indicated as the reference detection method.

Council Directive 76/160/EEC concerning the quality of bathing water specifies cadmium but has yet not specified a ‘Guide value’ or ‘Mandatory value’.

Council Directive 76/464/EEC  on pollution by certain dangerous  substances, and its daughter directive, Council Directive 83/513/EEC on the limit values and quality objectives for cadmium discharges, require Member States to set up an (prior) authorisation system for discharges of cadmium.

For most industrial discharges, with the exception of industrial plants manufacturing phosphoric acid and/or fertilisers, emission. Limit values are laid down . By way of alternative, Member States may base their authorisations on the quality objectives laid down for different types of waters.

Reference methods of measurement and monitoring procedures for cadmium in water, sediments and shellfish (i.e. AAS preceded by appropriate conservation and treatment of the sample) are laid down in Annexe III Incl. details on accuracy, precision and flow of the effluent.

Table 2.3.6 Directive 76/464/EEC: on pollution caused by certain dangerous substances discharged into the aquatic environment of the Community (Directive 83/513/EEC, the so-called Cadmium Discharges Directive)

| Limit values* for zinc mining, refining lead and zinc and production of non-ferrous metals and metallic cadmium | Details | Source |
| --- | --- | --- |
| 0.2mg cadmium/l effluent | monthly mean measurements (limits for mean of daily measurements = 2-fold) | O.J. N° L 129, 1976 |
| Limit values for the production of cadmium (compounds) | Details |  |
| 0.2mg cadmium/l effluent | mean of one month; total cadmium concentration |  |
| 0.5g cadmium/kg processed cadmium |  |  |
| Minimum standards for the protection of aquatic life |  |  |
| < or = 5 µg/l | in surface water; total cadmium conc |  |
| < or = 5 µg/l | estuaries; dissolved cadmium |  |
| < or = 2.5 µg/l | in marine territorial waters, coastal waters; dissolved cadmium |  |
| Quality objective (target value)** |  |  |
| < or = 1 µg/l | in surface water; total cadmium conc |  |
| < or = 1 µg/l | estuaries; dissolved cadmium |  |
| < or = 0.5 µg/l | in marine territorial waters, coastal waters; dissolved cadmium |  |
| and no significant increase of concentration of cadmium in sediments or in ….shellfish and mollusca (e.g. Mytillus edulis) |
| Standards adopted by Member States |
| 0.06 | Nl; max. permissible conc.; dissolved | van Hout, 1994; in Pearse, 1996 |
| 0.01 | Nl; target value; dissolved | van Hout, 1994; in Pearse, 1996 |

*: to be considered as ‘emission limit value’ under the Dir. 2000/60/EC

**: to be considered as ‘environmental quality standards’ under Dir. 2000/60/EC

The Water Framework Directive 2000/60/EC (O.J. L 327, 22.12.2000, p.1-73) aims at the establishing of a framework for the protection of surface, transitional, coastal waters and groundwater which prevents further deterioration and protects and enhances the status of the aquatic ecosystems and depending terrestrial ecosystems and wetlands; promotes sustainable water use; aims at enhanced protection and improvement of aquatic environment through specific measures for the progressive reduction of discharges, emissions and losses of priority substances and the cessation of phasing-out of discharges, emissions and losses of priority hazardous substances, pollution; contributes to mitigating the effects of floods and droughts. Herewith the objectives of relevant international agreements including those which aim to prevent and eliminate pollution of the marine environment with the ultimate aim of achieving concentrations of priority hazardous substances near the background values for naturally occurring substances (e.g cadmium) and close to zero for man-made synthetic substances.

The list of priority substances (Annex X of Directive 2000/60/EC) has been established by Decision N° 2455/2001/EC, as has specified cadmium as a Priority Hazardous Substance.

This implies (art. 16 of 2000/60/EC) that the European Commission has to submit proposals for progressive reduction of discharges, emissions and losses, but also, as cadmium is listed as Priority Hazardous Substance, cessation or phasing-out of discharges, emissions and losses within 20 years after adoption of the proposals.

The proposals must at least cover quality standards –for water, sediment or biota- and emission controls for point sources, and also review the Cadmium Discharges Directive (83/513/EEC). If no agreement on the proposals is reached at Community level by 2006, Member States have to establish themselves quality standards and controls on the principal sources.

As the quality standards are part of the surface water status, these would have to be reached at the latest by 2015.

# Air

Waste Incineration Directives: 89/369 and 89/429 set emission limit values to air based on BAT for resp. new and existing municipal waste incineration plants (new = exploitation permit delivered after 1/12/1990). For new installations (with a nominal capacity of at least 1 ton waste /h) the emission value for cadmium and mercury is fixed at 0.2 mg/Nm3 off-gas. Old installation with minimal 6t/h nominal capacity must apply to this value at the latest by 1/12/96.

The hazardous waste incineration Directive (94/67) controls emissions of heavy metals by prior authorisation procedure of plants. Emission limits in flue gas (?) for existing installations (before 31/12/1996): the sum of cadmium(compounds), expressed as cadmium and thallium(compounds) must be lower than 0.1 mg/m3. For new installations, the corresponding limit is fixed at 0.05 mg/m3.

In addition to Directive 75/442/EEC, Directive 2000/76/EC on the incineration of waste sets stricter emission limit values, in particular for cadmium to air (the total emission limit value of ‘Cd + Tl’ = 0.05 mg/(N)m3 as daily average value suitably standardised depending on the type of combustion; air emission limit value for cadmium and its compounds: all average values over sampling period of a minimum of 30 minutes and a maximum of 8 hours: expressed as cadmium: total: 0.05 mg/m3; exemption until 1.1.2007 for existing plants and certain conditions, hazardous waste incinerators only), water (the emission limit value for the discharges of waste water from the cleaning of exhaust gases, mentions for cadmium and its compounds, expressed as cadmium and in mass concentration for unfiltered samples: 0.05 mg/l). These emission limit values should be met by means of stringent operational conditions and technical requirements of the installations (existing plants as from 28.12.2005; for new plants as from 28.12.2002).

Council Directive 96/62/EC of 27 September 1996 on ambient air quality assessment and management (O.J. L 296, 21.11.1996, p. 5-63) aims to define the basic principles of a common strategy to define and establish objectives for ambient air quality (AAQ i.e. related to outdoor air excluding workplaces) in the Community designed to avoid, prevent or reduce harmful effects on human health and the environment as a whole; assess the ambient air quality in the MSs on the basis of common methods and obtain adequate information on the issue and ensure its public accessability (e.g. by means of alert thresholds) maintain AAQ where it is good and improve it in other cases. Cadmium is mentioned in the list of atmospheric pollutants to be taken into account in the assessment and management of AAQ (for cadmium, an air quality standard of 5 ng/m3 has been proposed).

# Soil

Council Directive 86/278/EEC concerns the protection of the environment, and in particular of the soil when sewage sludge is used in agriculture. Limit values concentrations have been set of the substance in soil, in sludge for the agricultural use and for the maximum amounts of cadmium which may be add annually to the agricultural land.

Table 2.3.7 Directive 86/278/EEC: on the protection of the environment and in particular of the soil, when sewage sludge is used in agriculture (Annex IA).

| Annex IA |
| --- |
| limit values in soils in mg/kg | Details | Source |
| 1 up to 3 |  | O.J. N° 181, 1986 |
| Standards adopted by Member States (COM(97) 23 final) |
| 1 up to 3 | BE; Flanders: sandy soil: 1 clay soil: 3; Wallonia: 1 |  |
| 1 up to 3 | E: pH<7: 1; pH>7: 3 |  |
| 2 | F |  |
| 1 up to 4 | P: pH<5.5: 1; pH 5.5<7: 3; pH>7: 4 |  |
| 3 | UK |  |

Remark: for DE: limit values: 1.5 mg/kg (or 1 mg/kg dry weight) at pH> 5 and <6 (UBA, comments 2000).

Table 2.3.8 Directive 86/278/EEC: on the protection of the environment and in particular of the soil, when sewage sludge is used in agriculture (Annex IB).

| Annex IB |
| --- |
| Limite values in sludge (mg/kg) | Details | Source |
| 20 to 40 |  | O.J. |
| Standards adopted in Member States (COM(97) 23 final) |
| 10 and 12 | BE; Flanders: 12; Wallonia: 10 |  |
| 20 up to 40 | E: pH<7: 20; pH>7: 40 |  |
| 20 and 40 | F: reference value: 20; limit value: 40 |  |
| 20 | P |  |

Remark: here there are no data for UK; for S: A charge of 30 SEK per gram of cadmium exceeding 50 g/ton P (changed to 5 g Cd/ton P) was introduced in Sweden in 1994 and was changed to a tax in July 1995 (KEMI, comments 2000); for DE: limit value: 10 mg/kg (or 5 mg/kg dry weight) at pH >5 and < 6 (UBA, comments 2000).

Table 2.3.9 Directive 86/278/EEC: on the protection of the environment and in particular of the soil, when sewage sludge is used in agriculture (Annex IC).

| Annex IC |
| --- |
| Limit values for the introduction of metals in arable soils in kg/ha/year |  |  |
| 0.15 |  |  |
| Standards adopted by Members States (representative for the p’riod ’91 – ‘94) (COM(97) 23 final) |
| 0.012 and 0.024 | BE: Flanders: grassland: 0.012; culture land: 0.024 |  |
| 0.15 | E |  |
| 0.06 | F |  |
| 0.15 | P |  |
| 0.15 | UK |  |

Remark: for DE: limit value: max. 0.017 kg Cd/ha/a (based on the limit value in sludge and the max. sludge application), max. sludge application of 5 t/ha/3 years (UBA, comments 2000).

The Fertiliser Directive (76/116/EEC) is currently under revision. In that framework, extensive work has been done by Member States in performing national risk assessment reports and by the EC (see ERM, final reports of January 2000 and June 2001, commissioned by DG Enterprise). The aim of the exercise is to review the data on the exposure of risk groups and on environmental conditions in the MS to judge whether or not cadmium in fertlisers presents an unacceptable risk and thus to harmonise the situation within the EU (Austria, Finland and Sweden have a derogation from Article 7 of the Directive in so far it concerns cadmium i.e. these MS may prohibit the marketing of fertilisers containing cadmium at concentrations in excess of those which were fixed nationally at the date of Accession) and to adopt EU-wide risk management measures related to the cadmium (content) in fertilisers, if needed so. In that context several MS have implemented national regulations limiting the maximum cadmium concentration in fertilisers, the cadmium input in and/or the cadmium concentration in agricultural soil. A non-exhaustive overview of these figures is given in Table 3.1.177 of Section 3.1.3.4.2 in this report.

# Waste

Council Directive 78/319/EEC on toxic and dangerous waste determined cadmium and its compounds as requiring priority consideration in the control, prevention, recovery and recycling of any waste containing or contaminated by the substance.

The packaging and packaging waste Directive (i.e. Dir. 94/62/EC of 20 December 1994; Commission Decisions 1999/177/EC and 2001/171/EC) aims to reduce the impact of these materials (and waste arisings) by limiting the total quantity that may be put on the market, by enhancing re-use and recycling and by setting limits to hazardous substances. The sum of the concentrations of four heavy metals (lead, cadmium, mercyury and hexavalent chromium) in packaging which are not to be exceeded at different points in time, are: 600 ppm (July 1998); 250 ppm (July, 1999) and 100 ppm (July 2001). Exemptions are included in the Directive (e.g. packaging made entirely of lead crystal glass) and following COM decisions (for recycled material used in closed product loops and controlled chain i.e. plastic crates and pallets, and for glass packaging).

The Directive on ‘End of Life Vehicles’ (Dir. 2000/53/EC) aims at the prevention of waste from vehicles and at re-use, recycling and other forms of recovery of end-of life vehicles and their components so as to reduce the disposal of waste as well as at the improvement in the environmental performance of all economic operators involved and especially those directly involved in the treatment of end-of- life vehicles. Limitations of the use of hazardous substances in vehicles are encouraged and the use of heavy metals (lead, mercury, cadmium and hexavalent chromium) in materials and components of vehicles put on the market after July 2003 are prohibited, with exemptions (e.g. cadmium in batteries for electrical vehicles) foreseen in Annex II under the specified conditions (at least until 1 January 2003).

Directive 2002/95/EC on the restriction of the use of certain hazardous substances in electrical and electronic equipment (EEE) requires the substitution of various heavy metals (incl. Cadmium) and other chemicals in new EEE put on the market from 1 July 2006. Exempted is Cd plating except for applications banned by Directive 76/769/EEC. The Directive 2002/95/EC should apply without prejudice to other Community legislation in particular the Batteries Directive (91/157). Directive 2002/96/EC on waste electrical and electronic equipment aims at the prevention of the waste of EEE  (EEE: including large and small household appliances, IT and telecommunications equipment, tools, toys, medical devices, etc) by promoting re-use, recycling and other forms of recovery. The list of materials and components of WEEE that should be selectively treated (i.e. removed) mentions ‘batteries’.

### National legislation

Nordic countries have been even more comprehensive in regulating cadmium and its compounds resulting in a stricter legislation than that on community level (Nordiske Seminar- og Arbejdsrapporter, 1992). Since the early eighties the use of the substance in pigments, in stabilisers (and in plating) has been banned in Denmark (since 1983) and Sweden (since 1982). All Nordic countries have strictly regulated the content of the substance in fertilisers and in sewage sludge since 1992 at the latest. Regulations on batteries did exist years before the adoption at EEC level of a directive with similar objectives.

A non-exhaustive overview of the Danish legislation focusing in particular to issues related to the environment, is given as to exemplify the extent of regulation in Nordic countries (DEPA, Pers. comm.. 2001).

Table 2.3.10 Danish environmental legislation on cadmium (Danish EPA, Pers. com., 2001).

| Regulation | Content |
| --- | --- |
| No. 223 of April 5, 1989 Statutory order from the Ministry of the Environment on the content of cadmium in phosphorus-containing fertilizers | The phosphorous fertilisers are regulated on the content in phosphorous containing fertilisers sets the maximum content of cadmium relative to phosphorus in fertilisers containing (1% phosphorus be weight. The order does not cover manure, compost, sludge or other waste products they are added phosphorous manufactured from raw phosphate. After 01.07.1998 the maximum content of cadmium in phosphorous fertilisers are 100 mg Cd/kg P. |
| No. 1199 of December 23, 1992 Statutory order from the Ministry of Environment and Energy on the prohibition of sale, import and manufacture of cadmium-containing products | Importation, sale and manufacture of cadmium-containing products are prohibited. For the purpose of this Order cadmium-containing products means products in which cadmium is used either as surface treatment agent (cadmium plating), colour pigment or plastic stabilizer with more than 75 ppm in the homogeneous components of the product. Irrespective of the prohibition in subsection 1 above, manufacture, importation and sale of cadmium-containing products are permitted for the purposes specified in the Annex to this Order, within the stated deadlines. |
| No. 93 of February 22, 1996 Statutory order from the Ministry of Environment and Energy on collection of hermetically sealed nickel-cadmium accumulators (closed nickel-cadmium batteries) and remuneration for collection and disposal for recycling | Remuneration may be paid for environmentally sound collection and disposal for recycling of hermetically sealed nickel-cadmium accumulators (closed nickel-cadmium batteries). Remuneration may be paid to private persons and public enterprises, associations, municipalities etc. collecting and delivering or being in charge of delivery of closed nickel-cadmium batteries for recycling. In this Statutory Order recycling means recovery of the cadmium and possibly the nickel content of closed nickel-cadmium batteries. |
| No. 130 of February 10, 1997 Statutory order from the Ministry of Environment and Energy on provision of information by export of certain used production plants | This Order lays down rules on the duty to provide information on export of used production plants from heavily polluting enterprises (listed activ–ties - including wastewater containing cadmium), including non-complete plants, located in Denmark. The rules apply to categories of production plants which have been installed in the types of enterprises listed in Annex 1A, and which meet one or more of the criteria listed in Annex 1B. The duty to provide information applies no matter whether the used plant is exported for the purpose of final mounting and operation in the receiving country, or with a view to resale only. The disposer of a plant listed in Annexes 1A and B of this Order shall notify the supervision authority of agreements made for export of the plant. Notification may take place before the final agreement is concluded, when the question of importing country and receiving party is decided. |
| No. 298 of April 30, 1997 Statutory order from the Ministry of Environment and Energy on certain requirements for packaging | This Statutory Order lays down provisions for essential requirements for the manufacture, composition, and utilisation of packaging, as well as limit values for the content of heavy metals (including cadmium) in packaging. The provisions of the Statutory Order apply to all packaging, including packaging containing products. Roads, railways, ships, and airfreight containers are outside the scope of this Statutory Order. This Statutory Order shall apply without prejudice to existing quality requirements for packaging, including requirements for health, protection of health and hygiene for the packed products, or existing requirements for the transport of hazardous goods. Between 30 June 1999 and 30 June 2001, packaging and packaging components may only be placed on the market in Denmark provided the sum of concentration levels of lead, cadmium, mercury, and hexavalent chromium does not exceed 250 ppm by weight. After 30 June 2001 packaging and packaging components may only be placed on the market in Denmark provided the sum of concentration levels of lead, cadmium, mercury, and hexavalent chromium does not exceed 100 ppm by weight. |
| Statutory order no. 1065 of November 30, 2000 Statutory order from the Ministry of Environment and Energy on classification, packaging, labelling, sale and storage of chemical substances and products. | This Order applies to chemical substances and products. Chemical substances means chemical elements and their compounds in the natural state or obtained by any production process, including any additive necessary to preserve the stability of the substance and any impurity deriving from the process used, but excluding any solvent which may be separated without affecting the stability of the substance or changing its composition. Dangerous chemical substances and products shall be classified in one or more of the following danger categories: explosive, oxidizing, extremely flammable, highly flammable, flammable, very toxic, toxic, harmful, corrosive, irritant, sensitizing, carcinogenic, mutagenic and toxic to reproduction as well as (for substances only) dangerous for the environment. Dangerous chemical substances and products shall be assigned danger symbols and indications of danger risk indications (R-phrases),and safety advices (S-phrases). |
| No. 594 of June 6, 2000 Statutory order from the Ministry of Environment and Energy on cosmetic products | This Order shall apply to cosmetic products, which are marketed and to substances used in such products. According to this order cadmium and its substances may not be uses in cosmetic products. |
| No. 1044 of December 16, 1999 Statutory order from the Ministry of Environment and Energy on certain batteries and accumulators containing dangerous substances | Import and sale of batteries and accumulators containing: more than 0.025% cadmium by weight, shall not take place unless the battery or accumulator is marked with one of the symbols indicated in Annex 1 to this Order, with a view to separate collection and subsequent recovery or disposal. |
| No. 1042 of December 17, 1997 Statutory order from the Ministry of Environment and Energy on regulation of sale and usage of some dangerous chemicals and products to some specific purposes | Use of cadmium in paints and varnishes is forbidden. Use of cadmium in foodstuffs and stimulants is not allowed The cadmium content in glazing and decorative paintings is not allowed to be more than 0,002 percent. |
| No. 733 of July 31, 2000 Statutory order from the Ministry of Environment and Energy on the list of dangerous substances. | Classification of dangerous substances including cadmium compounds. |

## Voluntary control measures

On the Swedish food market, voluntary cadmium-limits are already imposed on products through initiatives taken by producer associations as well as retailing companies. These limits, which are stricter than the legally imposed criteria, have been set as a response to the perceived consumer demands. Also the tax on cadmium reduces the profitable level of cadmium in phosphorus fertiliser substantially below the allowed limit.

As an example, the co-operatives supplying the farmer with fertilisers, the Swedish Farmers Regional Selling and Purchaser Associations (sw: Lantmännen) have introduced its own limit value for soil, 0,30 mg/kg, for its most important trademark. If the top soil of a single field contains more Cd, the farmer may proceed to the second step, which consist of an analysis of the cadmium content in the wheat grains. If this level is below 0,100 mg Cd/kg, the crop can be sold under the trademark, otherwise not (KEMI, 2000, as derived from Drake and Hellstrand, 1998, The economics of the Swedish Policy to Reduce cadmium in Fertilisers, KemI PM 2/98).

The voluntary commitment of the European PVC Industry aimed – amongst other targets – to phase out the use of cadmium in all stabilisers systems placed on the EU market (i.e. by ESPA members). This target was achieved in March 2002 (Vinyl 2010, The Voluntary Commitment of the PVC Industry, Progress Report 2002).

## Other supranational instruments

Cadmium is included in several international declarations and programmes on reduction of micropollutants.

The OECD started in 1990 a Risk Management Programme on five chemicals, one of them cadmium, for which Risk Reduction Monographs were published. The OECD programme on Cadmium actually recommends collection and recycling of Ni-Cd batteries as a means of reducing risk.

Cadmium falls under the UN-ECE-LRTAP Protocol for Heavy Metals, the aim of which is the reduction of heavy metal emissions due to human activity (at stationary sources) and with the potential of causing harmful effects at long distance from the source via transport trough the atmosphere.

The WHO air quality guideline value for cadmium is 5 ng/m3 (this value was established to prevent any further increase of cadmium in agricultural soils that could increase the dietary intake of future generation, given that no reliable unit risk could be derived to estimate the excess lifetime risk for lung cancer in the general population).

In 1998, the Ministerial Meeting of the OSPAR Commission in Sintra identified Cadmium (among other substances) as a substance for priority action under its Hazardous Substances Strategy. A Background document on Cadmium was prepared and adopted in 2002.

Several PARCOM Recommendations have been adopted related to the substance i.e. Rec. 92/3 concerning New secondary steel production and rolling mills, and Rec. 92/4 relating Electroplating industry. Cadmium is one of the substances that should be substituted in the latter field of uses.

The Rhine Commission has adopted a Ministerial declaration on heavy metals (with cadmium included) that have to be banned.

In 1998, the Helsinki Commission (HELCOM) Recommendation 19/5 was adopted including cadmium on the list of substances for priority action.

Cadmium also appears on the list of candidate-substances to include in the next extension of the monitoring programme of the International Commission for Protection of the river Scheldt.

The substance is also identified within the North Sea Conference framework (1990), and is one of the substances that ‘cause a major threat to the marine environment...’ for which ‘reductions between 1985 and 1995 of all inputs of the order of 70% or more - provided that the use of BAT or other low waste technology measures enable such reductions’ - should be achieved. Atmospheric emissions by 1995, or by 1999 at the latest, should be significantly reduced (by 50% or more). Within that framework, harmonized quantification and reporting procedures for chemicals were developed. One of these procedures concerns Cadmium.

# ENVIRONMENT

## Environmental exposure

### Methods and definitions: added Cd, natural background and ambient concentrations

The environmental exposure to Cd is calculated based on all known current anthropogenic emissions of Cd, i.e. Cd that is emitted by the Cd/CdO producers and processors and Cd in diffuse sources such as fertilisers, steel production, traffic, waste incineration, landfills etc.  Local exposure assessment is based on emissions from Cd/CdO producers and processors.  Regional and continental exposure assessment is based on all anthropogenic Cd emissions, including diffuse emissions. Actual Cd concentrations in the environment (ambient concentrations) are furthermore determined by the natural background of Cd (from geological origin or from natural processes) and Cd that was added to the environment in the past by man (historical pollution).

The natural Cd and Cd from historical pollution determine the background Cd concentrations in the environment.  The predicted environmental concentrations (PEC’s) are based on predicted added (anthropogenic) concentrations plus the background concentrations..  The background Cd in surface water and air is assumed to be the natural background.  The residence time of Cd in these two compartments is less than one year (3.1.3.4.1) and historical pollution should, therefore, not affect actual Cd concentrations. Background Cd in air originates from natural processes such as volcanic eruptions, bush fires etc. and, therefore, these diffuse Cd sources are not included in the anthropogenic emission inventory. Background Cd in surface water originates from runoff, leaching and atmospheric deposition of Cd from natural origin. Again, none of these processes are included in the anthropogenic emission inventory. Runoff and leaching of Cd added by man are, however, included in the anthropogenic emissions to water. The natural background in surface water and air is estimated in section 3.1.2.4.3 and is added to the continental anthropogenic Cd concentrations, yielding the PECcontinental.  This PECcontinental is then used in the PECregional and PEClocal according to standard procedures of the TGD.  The approach is different for soils and sediments where the residence time of Cd is at least several decades (3.1.3.4.1).  The historical Cd emissions by man affect ambient Cd concentrations in soils and sediments, even far away from point sources such as smelters (3.1.3.4.3 and 4.1.1.4.7, see separate document).  Therefore, the actual background of Cd in soils and sediments exceeds the natural background.  Background Cd concentrations in soils and sediments are estimated from the ambient Cd concentrations in areas away from point sources (3.1.3.4.3).  That background Cd is added to the predicted added anthropogenic Cd concentration, yielding the PECcontinental which, in turn, is used for the PECregional and PEClocal.

The standard TGD procedure to calculate the PECregional in soil appears not adequate for various reasons (see 3.1.3.4.1&2).  Because soil Cd is an important compartment in Cd risk assessment, an alternative model for the TGD protocol was developed (3.1.3.4.2).  This model predicts future trends in soil Cd based with a more detailed Cd input/output balance than the TGD model.

The metallic Cd and the CdO powder are less harmful in the environment than soluble Cd2+. However, the metallic Cd and the CdO powder transform in the environment to the toxic Cd2+.  Details on the extent of transformation in water and in soil are given in the sections 1.4.2.1.2, 3.2.1.1.2 and 3.2.2.1.2 of this report. The source of Cd (from the Cd/CdO producers and processors, from the diffuse sources or from the background) is not taken into account in the environmental risk assessment.  Releases to the aquatic compartment by the producers and processors are often based on measurements in effluents after the sewage treatment plant (STP). Most Cd/CdO particles are retained in the STP and the Cd in the effluent is mainly present as dissolved Cd.  Atmospheric losses are deposited onto soil where the metal or metal-oxide readily transforms to a species with the same fate as soluble Cd2+ (section 3.2.2.1.2). Arguments for similar bioavailability of soil background Cd and recently added Cd are given in section 4.1.1.4.8 (human part of the RAR, see separate document) where soil-plant transfer of Cd is discussed.

No attempt was made to express environmental Cd concentrations as bioavailable concentrations, with the exception of Cd concentrations in water where only the dissolved fraction is considered.  The bioavailability of Cd is known to vary with properties of the compartment (see section 3.2). Unfortunately, there are no standard procedures to correct for that variance.  This variance is however accounted for in the effect assessment where PNEC values are calculated as a function of properties of the compartment. Predicted total concentrations are then compared with the properties specific PNEC’s for risk characterisation.

### Emissions

#### Releases during production and use (excluding batteries’ related scenarios)

##### Source of data

In this section, input of cadmium into the environment of the EU is calculated. Major anthropogenic sources of cadmium into the environment are associated with Cd-production and -processing, with iron and steel production, with cement manufacturing, with combustion of fossil fuels, with the use and disposal of Cd containing products and with the use of Cd containing fertilisers.

Emissions from the Cd and CdO producing industry are based on plant information submitted by the Cd-producing industries of the EU and Norway (further denoted as EU-16). These emissions are annual averages. This information was collated from a questionnaire submitted in 1997 to all Cd and CdO producing plants in EU-16.  Data of two plants that are dedicated Cd recycling plants also provided emission data.  Information on Cd losses associated with processing of Cd in pigments and in stabilisers is based on detailed data reported by WS Atkins (1998). The data are those for 1996. In Corden et al. (2001) some more recent data are available. Information on Cd losses at EU-level from plating processes is also based on the WS Atkins report. More general information is provided by the IPPC report on the surface treatment of metals (2004). This reports indicates that in this sector process waters are often treated on-site and then discharged usually to municipal (urban) waste water (sewage) treatment plants, or if the effluent is treated to a suitable standard (i.e. in compliance with the national/regional limit values for the discharge of waste water: for the metal treatment sector: in general the regulatory limit value (in total Cd) varies between 0.2mg/l and 0.6mg/l although lower limits are provided by law for some areas), directly to surface waters.

No accurate information on Cd emissions during processing of Cd in alloys was found. Estimated total EU emission data from processing of Cd in alloys reported by ERL (1990) and ICdA (1998) were used for the atmospheric compartment. Calculation of local PEC's from processing of Cd in plating and alloys was done by treating the emission at EU-level as point sources and by using standard values (section 3.1.2.3.). No emission data to the aquatic compartment were available for Cd alloy processing sites. The default emission factor to water (A-table) is 0.5 and which is a large value compared to all other emission factors (Table 3.1.1). Therefore, emission factor for alloy production was selected based on data obtained for the Cd plating sites (2360 g t-1 processed).  This value is 30-fold larger than the worst-case-scenario proposed for Zn alloy processing sites (80 g Zn t-1) in the Zn RAR (2004).

The Cd emission during use and disposal of Cd containing products and from other sources such as iron and steel production, cement manufacturing, municipal waste incineration, fuel combustion and use of Cd containing fertilisers are calculated in two ways. The first way is based on calculations according to the TGD (1996) with Cd emission data at the EU-level (including Norway) (section 3.1.3.4.1). The second approach consists of alternative calculations, only made for agricultural soils for which measured (or estimated) emissions are collated for different European countries (section 3.1.3.4.2). Sewage sludge application as a source of Cd is included in the diffuse source inventory described in that section. Country average fluxes are used in this assessment and not the fluxes in the restricted number of soils where sludge is applied. Sewage sludge is a minor source of Cd for soils on an average basis; however it is a major source of Cd in soils where sludge is applied. This RAR does not assess the risks of Cd on theses soils where sludge is applied.  Sludge borne Cd has a different fate and effect than Cd added through fertilizer or atmospheric emissions. The lower bioavailability of sludge born metals soil is conserved on the long-term, even if most of the sludge organic carbon has decayed (Brown et al., 1998 and references therein).  Therefore, the assessment of effects and the transfer to the foodchain are different between sewage sludge treated soils and soils enriched by inorganic Cd sources. The Cd fluxes through sludge vary widely and depend on local restrictions on the use of sludge in agriculture. Legislation in EU-16 countries is either based on maximal Cd concentrations in sludge (i.e. 1.2-10 mg Cd kg-1) or maximum Cd fluxes (e.g. 3-15 g ha-1y-1). Some countries restrict a cumulative load (OECD, 1994).  Total Cd input from sludge in the EU-16 is estimated to be at least 11.6 ton y-1 (Table 3.1.156).

There are no specific use scenario’s described in this RAR. The main use of Cd/CdO is in NiCd batteries and emissions during the whole life-cycle (incl. disposal) are described in the TRAR/batteries’ related (sub)sections. Current worst case Cd disposal scenario’s are predicted to increase Cd emission to the environment in the future and the effect of the predicted future emissions on the PEC’s are described in section 3.1.3.4 as an illustration. In the present document, the risk charaterisation is made using actual Cd emission.

The Cd emission, from Cd/CdO production and processing industry are presented in Tables 3.1.1 and 3.1.2.  The total EU-16-emission to the aquatic environment from Cd/CdO -producing and -processing plants in 1996 is 1504 kg y-1 with 81% originating from the Cd producing industry. In general, industrial effluents are treated in a sewage treatment plant (STP) before being discharged into surface waters. Unless mentioned in the table, all data refer to concentrations measured after the STP. Five of the Cd producing plants emit their effluents to the sea or a bay. These plants are indicated in italics and emit 497 kg Cd y-1 or 33% of the total amount emitted to the aquatic environment. Plant number 9 produces only minor amounts of Cd. Its Cd-emission is mainly due to the production of Zn.

The total EU-16-emission to the atmospheric compartment in 1996 from Cd-producing and processing plants is 4646 kg y-1 with 83% originating from Cd producing plants.

There are no direct local emissions to the soil compartment (i.e. local disposal) originating from Cd- and CdO-producing plants. Wastes from production are recycled or disposed off to controlled industrial landfill sites (IZA-Europe, pers. communication). No such information is available for the Cd processors. However, much of the waste produced (e.g. sludge) from process activities is likely to be classified as hazardous (for the surface treatment of metals, see IPPC, 2004; EU legislation in: EC, 1991; EC, 2000) and therefore excluded from the use in agricultural soil practices.

Emissions during the conversion of Cd to CdO are very low. According to the emission data from two CdO-producing plants in Belgium, there are no emissions to water as the production of CdO from Cd is a dry process. Water -mainly cleaning water- containing Cd and CdO is recycled. Emissions to air are very low -2.16 kg y-1- due to installation of air filters. Cadmium and CdO retained in the filters are recycled as is the waste containing Cd and CdO. During a monitoring program of a CdO-producing plant, Cd concentrations were measured in the ambient air at 150 to 200 m from the emission point. An average value of 7.6 ng Cd m-³ was recorded (Industry Questionnaire, 1997). However, at the same site, Zn-chemicals are produced, another emission source of Cd to the environment. The emission data represent losses from both production processes together and it is not possible to distinguish which part is due to the production of CdO. The same comments apply to the other CdO-producing plant where besides CdO also Cd-powder is produced.

It needs to be mentioned that during the last years (in particular since 2001) a significant number of Cd metal producers stopped the cadmium production (some with, others without stopping the refining of the primary metal zinc/copper/lead). The same occurred in the area of CdO production (cfr section 2.1.2.1 and section 2.1.2.2).

A very recent update provided by Industry (ICdA, com., 2003) reveals that from the initial list of cadmium production plants in Europe (drawn in 1997 on the basis of data from 1996) to date only three, possibly four remained active in the field of cadmium production. However, further details (i.e. on current production, import, export and exposure data) were not submitted for more recent years.

Table 3.1.1:	aquatic emissions from Cd-producing and -processing plants in the EU-16.

| use- category | plant N° | production/ consumption volume | production emission¶ | processing emission¶ | emission factor | conc. in effluent(c) | number of production days | concentration in effluent(a) | effluent flow(a) | flow receiving water(a) | year |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | ton y-1 | kg y-1 | kg y-1 | g ton-1 |  |  | mg l-1 | m³ d-1 | m³ d-1 |  |
| Cd-producers(e) | 1 | 683 | 23.9(g) |  | 35 | M (T) | 365 | 0.045 | 1440 | 16000 | 1996 |
|  | 2 | 510 | 614 |  | 1204 | M (T) | 365 | 0.44 | 3823 | 1204245 | 1996 |
|  | 3* | 596 | 15.7 |  | 91 | M (D) | 70 | 0.01 | 7476 | -* | 1996 |
|  | 4* | 14.7 | 21.6(g) |  | 1469 | M (D) | 15 | 0.12 | 4000 | -* | 1996 |
|  | 5 | 208 | 77.8(f) |  | 374 | M (D) | 243 | 0.16 | 2000(b) | 18000(d) | 1996 |
|  | 6 | 262 | 0.18(g) |  | 0.69 | M (T) | 105 | 0.00068 | 1320 | 39 106 (h) | 1996 |
|  | 7*£ | 274 | 70 |  | 255 | M (T) | 365 | 0.06 | 3196 | -* | 1998 |
|  | 8 | 378 | 11 |  | 19 | M (T) | 151 | 0.03 | 1821 | 1700000 (h) | 1996 |
|  | 9* | 0.696 | 29.4(g) |  | 42241 | M (T) | 365 | 0.0058 | 13820 | -* | 1999 |
|  | 10 | 1579 | 0 |  | 0 | (1) | 316 | (1) | (1) | (1) | 1996 |
|  | 11 | 32 | 0 |  | 0 | (2) | 32 | (2) | (2) | (2) | 1996 |
|  | 13* | 307 | 372 |  | 1212 | M (D) | 123 | 0.17 | 17790 | -* | 1996 |
| CdO-producers | 11 | 1256 |  | 0 | 0 | (2) | 251 | (2) | (2) | (2) | 1996 |
|  | 12 | 1280 |  | 0 | 0 | (2) | 256 | (2) | (2) | (2) | 1993 |
| Cd-stabilisers | F |  |  | 0.03 |  | M(T) | 20 | 0.001 | 1490 | 725760 | 1996 |
|  | G |  |  | 0.5 |  | M(T) | 48 | 0.013 | 749 | 18000(d) | 1996 |
|  | H |  |  | 0.78 |  | M(T) | 60 | 0.008 | 2571 | 259200 | 1996 |
|  | I |  |  | 0.1 |  | E(T) | 13 | 0.0004(3) | 2000(b) | 18000(d) | 1996 |
|  | J |  |  | 0 |  | M(T) | 13 | 0 | 0 | 0 | 1996 |
|  | K |  |  | 4.1 |  | E(T) | 12 | 0.017(3) | 2000(b) | 18000(d) | 1996 |
|  | L |  |  | 0 |  | M(T) | 155 | 0 | 0 | 0 | 1996 |
|  | M |  |  | 0 |  | M(T) | 155 | 0 | 0 | 0 | 1996 |
|  | window manufacturer |  |  | 0 |  | M(T) | 350 | 0 | 0 | 0 | 1996 |
| Cd-pigments | A | 237 |  | 0.6 | 3 | M(T) | 230 | 0.02 | 131 | 6000 | 1996 |
|  | B | 82.5 |  | 4.02 | 49 | M(T) | 231 | 0.002 | 5112 | 5045760 | 1996 |
|  | C | 186 |  | 5.9 | 32 | M(T) | 276 | 0.08 | 200 | 135000 | 1996 |
|  | D | 283 |  | 0.9 | 3 | M(T) | 230 | 0.022 | 130 | 32739 | 1996 |
|  | E | 66 |  | 13.4 | 203 | M(T) | 85 | 0.044 | 3618 | 89856000(h) | 1996 |
| Cd-plating | EU | 106 |  | 250 | 2360 | E (T) | 155 | 0.081 | 2000(b) | 18000(d) | 1996 |
| Cd-alloys | EU | 26 |  | 61.3 | 2360 | E (T) | 62 | 0.05 | 2000(b) | 18000(d) | 1996 |

n.a. not available;*emission to the sea; ¶annual averages; (1) no water emissions: waste waters are recycled; (2) no water emission: dry process; (3) value based on 90% elimination in sewer; (a) mean annual; (b) default value: 2000 m³ d-1; (c) M: measured value, E: estimated value, D: dissolved concentration, T: total concentration; (d) default value: 18000 m3 d-1; (e) emissions included these from Cd recycling; (f) emission of Cd from Pb and Zn production; no waste water related to Cd-production; (g) emission of Cd from Zn or Zn and Pb production; (h) emission to big river; £: emission data are reported to have decreased in more recent years to average concentration of 0.038 mgCd/L in effluent water for the year 2003 (Industry/company information, 2004)

Table 3.1.2: atmospheric emission from Cd-producing and -processing plants in the EU-16.

| use- | plant | production/consumption | production | processing | emission | year |
| --- | --- | --- | --- | --- | --- | --- |
| category | N° | volume | emission amount¶ | emission amount¶ | factor |  |
|  |  | ton y-1 | kg y-1 | kg y-1 | g ton-1 |  |
| Cd-production | 1 | 683 | 54(b) |  | 80 | 1996 |
|  | 2 | 510 | 1683(b) (e) |  | 3300 | 1996 |
|  | 3 | 596 | 800(b) |  | 4598 | 1996 |
|  | 4 | 14.7(d) | 3.03 |  | 206 | 1996 |
|  | 5 | 208 | 946(b) |  | 4548 | 1996 |
|  | 6 | 262 | 6.24(b) |  | 23.8 | 1996 |
|  | 7 | 274 | 200(b) |  | 730 | 1996 |
|  | 8 | 378 | 28.6 |  | 76 | 1996 |
|  | 9 | 648 | 110 |  | 170 | 1996 |
|  | 10 | 1579 | 3.32 |  | 2.1 | 1996 |
|  | 11 | 32.2 | 1.61 |  | 50 | 1996 |
|  | 13 | 307 | 24.6(a) |  | 80 | 1996 |
| CdO-producers | 11 | 1256 |  | 0.30 | 0.24 | 1996 |
|  | 12 | 1280 |  | 0.31(c) | 0.24 | 1996 |
| Cd-stabilisers | F |  |  | 0.09 | n.a. | 1996 |
|  | G |  |  | 0.8 | n.a. | 1996 |
|  | H |  |  | 0.5 | n.a. | 1996 |
|  | I |  |  | 0.1 | n.a. | 1996 |
|  | J |  |  | 0.7 | n.a. | 1996 |
|  | K |  |  | 0.04 | n.a. | 1996 |
|  | L |  |  | n.a. | n.a. | 1996 |
|  | M |  |  | 0 | n.a. | 1996 |
|  | window manufacturer |  |  | n.a. | n.a. | 1996 |
| Cd-pigments | A | 237 |  | 1.15 | 4.9 | 1996 |
|  | B | 82.5 |  | 2.37 | 29 | 1996 |
|  | C | 186 |  | 3.6 | 19 | 1996 |
|  | D | 283 |  | 5.8 | 21 | 1996 |
|  | E | 66 |  | 0.2 | 3.0 | 1996 |
| Cd-plating | EU |  |  | 0 | n.a. | 1996 |
| Cd-alloys | EU |  |  | 770 | n.a. | 1996 |

n.a.: not available; ¶annual averages;  (a)Estimated from a typical emission factor; (b)Cd emission from whole plant (including Zn and/or Pb production); (c)1996 value extrapolated from 1993 emission factor; (d)Production volume in 1991; (e) pyrometallurgical processes

Previous estimates of total Cd inputs to the EU environment from Cd producing- and processing plants (Hutton, 1982; Jensen and Bro-Rasmussen, 1992;OECD, 1994, EUPHEMET, 2000) are much higher than those given in the current RAR (Table 3.1.3.).

Table 3.1.3: total, direct emissions in the EU (T y-1). A comparison of different studies

|  | to Air (T y-1) | to Water (T y-1) |
| --- | --- | --- |
|  | Cd-producing plants | Cd-processing plants | Cd-producing plants | Cd-processing plants |
| Hutton, 1982 | 19.5 | 8.8 | 50 | 107 |
| Jensen & Bro-Rasmussen, 1992 | 22.8 | 12.2 | 17.3 | 45 |
| OECD, 1994 | / | 4.05 | / | 1.6 |
| EUPHEMET, 2000 | <15 | ~15 | ~15 | <3 |
| RAR-Cd, 2002(1) | 3.9 | 0.8 | 1.2 | 0.3 |

(1) Data from the EU + Norway

Data in the Hutton report are based on estimated emission data and emission factors of the end of 1970s. Data in the report of Jensen & Bro-Rasmussen (1992) are based on the ERL-study (1990) which, in turn, is based on estimated emission data and emission factors of the end of 1980s. The emission results reported in the OECD report (1994) are based on the same production data but emission factors were adapted with some more recent estimates. The assessments of EUPHEMET (2000) are based on previous generic calculations and reported results based on production data, as well as on the conclusions of a previous version of this report (RAR CdO, 1999). The RAR Cd/CdO (2002) data are based on actual production and measured emission data of the mid 1990's, and therefore, at the moment, closer to reality than the EUPHEMET (2000) report.

The comparison in Table 3.1.3 indicates a general decrease in the Cd emission from the Cd-producing and processing industry. Since the end of the 1970's emissions to air decreased more than 80%, while emission to water decreased more than 97%. This trend, based on measured data, confirms earlier performed estimates.  Elgersma et al. (1992) studied the change in the industrial Cd discharge to the River Rhine basin from 1970 to 1988. Emissions from primary Zn winning decreased from 2 T y-1 in 1970 to 0.05 T y-1 in 1988. The trend was the consequence of increasing regulatory pressure on Cd emitting industry and the consequent implementation of wastewater treatment plants in the seventies. The North Sea Conference report (1995) mentions a decrease in the Cd emission to water of about 50% over the period 1985-1995.

In Belgium a small decrease in Cd emission to water from non-ferrous-metal industry from 0.5 T y-1 in 1980 to 0.4 T y-1 in 1995 was recorded and further estimated to 0.2 T in 2000 (BMM, 1997 and 2001). In Germany a decrease was calculated from 0.5 T y-1 in 1990 to 0.2 T y-1 in 1994 for the same sector (Barbier, 1996). Pacyna et al. (1991) estimated a 60% decrease of Cd emission to air in Europe between 1975 and 1982. The North Sea Conference report (1995) mentions a decrease in the Cd emission to air in EU between 50% and 70% over the period 1985-1995. In Belgium, Cd emission to air from non-ferrous-metal industry decreased from 6.9 T y-1 in 1980 to to 2.1 T per year in 1995 and a further reduction to 0.36 T per year for 2000 is estimated (VMM, 1997; BMM, 2001). Cadmium emission to air from the German non-ferrous-metal industry decreased from 1.1 T y-1 in 1990 to 0.9 T y-1 in 1994 (Barbier, 1996).

This general decreasing trend is also reflected in the measured Cd-levels in air and water (see part 3.1.3.4 and Table 4.1.3.3 (in human part of the RAR, see separate document)). Recent trends of Cd in air, water and sediments are given in Annex 3.1.2. The reductions are most likely the result from increasing environmental regulations in the EU, which prompted the implementation of technologies abating Cd losses.

##### Emission reduction during production and use

Various types of measures and initiatives on national and international level are being taken to reduce Cd emissions from the Cd producing- and processing industries to the environment.

###### Emission reduction during production

# Water

Wastewater treatment at Cd-producing and -processing plants involves filtration and precipitation. Liquid effluents from the different stages during production and processing of Cd are collected and treated with sodium carbonate at alkaline pH to precipitate Cd.  Filtration aids and flocculating agents are added. The sludge is then filtered from the solution. The filtrate is neutralised prior to discharge to the environment. At industrial non-ferrous metal producing sites and waste water treatment plants (WWTP) a cadmium removal efficiency of at least 90% is reported based on physico-chemical techniques only, to achieve total cadmium concentrations within the range 1 – 0.1 mg/l (IPPC report, 2000). EUSES calculations give a corroborating removal rate (WS Atkins, 1998 and RPA, 2001): the Simple Treat model run with the Kp value of 130 000 l/kg yields the following distribution in the waste water treatment plant: 90% in sludge and 10% in water.

However, for municipal STP in practice, the average removal efficiency can vary widely from >80% (based on measurements of influent and effluent cadmium concentrations and the water flows; VMM, pers. com. 2002) to 60% (CUWVO, 1986; in: CBS/Milieucompendium, 2000). The latter, lower figure will be used in this RAR.

# Air

The major categories of available control techniques for Cd emission abatement to air are primary measures such as raw material substitution and low-emission process technologies, and secondary measures such as fugitive emission control and off-gas cleaning. In the case of particle-bound emission of Cd, dust-cleaning devices are used such as fabric filters, dry and wet electrostatic precipitators and scrubbers. In the pyrometallurgical production process, furnaces can be provided with a double bell furnace top. The dust collected in the filters is recycled within the production process. When scrubbing is applied, Cd is removed as a slurry after sedimentation in a settling tank. These slurries can be further processed or landfilled.

To reduce fugitive emissions from discharging, handling, and stockpiling of raw materials or by-products, these activities are removed to completely enclosed buildings, which may be equipped with ventilation and dust filters or spray systems.

# Land

Slugs and ashes formed during the melting process can be recycled when it contains sufficiently high Cd content. If the material meets the requirements of regulatory leaching tests, it may be used for road construction. All solid wastes from the production of NiCd batteries are recycled to recover the Cd and other metals.

Emissions of leachates of modern landfills are reduced to a minimum through the installation of containment, collection and attenuation practices. Basins are lined with plastic or impervious clay. Leachates are controlled and neutralised or recirculated. In order to minimise the quantities of residues to be landfilled, recycling and prevention campaigns of wastes are promoted by regulations.

###### Emission reduction during use and end-of-life

Since the 1980’s restrictions exists in several OECD-countries on the use of Cd in pigments, stabilisers and plating. This has led to a significant decrease of Cd consumption in these products.

#### Releases due to batteries’ related scenarios

Releases to the environment have been estimated for different life cycles stages of Nickel-Cadmium batteries (Table 3.1.4).

Table 3.1.4: Overview of the main life cycle stages of Ni-Cd batteries

| Life cycle stages | Phase |
| --- | --- |
| 1. Production/manufacturing of Ni-Cd Batteries and/or Battery Packs | PRODUCTION |
| 2. Incorporation into Battery-Powered Devices and Applications (EEE)a b |  |
| 3. Use, Recharging and Maintenance by End Usersa | USE/USEFUL LIFE |
| 4. Recycling Collection Sorting Processing Recovery | WASTE-MANAGEMENT |
| 5. Disposal Incineration Landfilling |  |

a Life cycle stage 2 and 3 are not deemed  relevant for the RA of the substance under study

b Life cycle stage 2 is a facultative step not relevant for individual cells or batteries put on the market

##### Life cycle stage 1: Manufacturing of Ni-Cd batteries and/or battery packs

The emissions to air and water from the Ni-Cd battery manufacturers are presented in Tables 3.1.5 and 3.1.6. Site specific information on the local Waste Water Treatment Plant (i.e. quantity of sludge produced, Cd content, destination of sludge) is presented in Table 3.1.7. Information on waste -other than sludge- is given in Table 3.1.8. The data for 1999/2000 were obtained from Industry Questionnaire, 2000/2001.

It must be noted that plant 2 is a producer and recycler; since no distinction could be made between emissions from production/recycling, the company is listed with Ni-Cd producing companies.

All plants except 1 (i.e. plant 2) release Cd to freshwater (surface water). Plant 2 emits to the marine environment. The total EU-emission to the aquatic environment from Ni-Cd batteries producing plants in 1999/2000 is 62 kg/y. Emission factors to surface water varying between 1.1 and 48 g/ton Cd used (average: 18.7 g/ton Cd used) are calculated. In comparison with emission data from 1996 (presented in Annex IV), very similar emission factors are obtained for water (1.6-145 g/ton Cd used and on average: 29.5 g/ton Cd used respectively). The large variation in emission factors cannot be explained by distinguishing between consumer/sealed portable batteries (plant 4 (partly)) and industrial batteries producers (other plants). On the basis of the information available on electrode production processes for the sites no conclusions can be formulated with regard to differences in emission factors due to different production processes (see Table 3.1.5).

The processing emission of plant 1 decreased substantially from 9.6  kg/y (in 1996) to 2.1 kg/y in 2000. In 1999 still 4.9 kg/y was emitted. The reduction in cadmium emission is due to the implementation of a new treatment plant (fully operational mid 2001) and the changing in the production process (since January 2000, no further details available) and cleaning method (from  wet to mainly dry cleaning).

In general industrial effluents from the plants are treated in an on-site Waste Water Treatment Plant (WWTP) before being discharged into surface waters unless mentioned otherwise. All data refer to concentrations measured after the WWTP. Plant 1 and plant 5 discharge after on-site treatment into the public sewer system. These discharges will undergo an extra dilution before entering the surface water. Plant 6 and 7 report that the wastewater is collected separately and treated off-site (external recycling). Since no additional information concerning the Cd content of influents of the local treatment plant was provided by industry, the emissions to wastewater and sludge could not be specified. However, in the questionnaires, specific information was requested with regard to quantity, Cd content and destination of waste generated (including WWTP sludge). This information reveals that the total amount of sludge produced by the companies is 730 t/y with an average Cd content varying between 1.7 and 12.5%. The total quantity of generated WWTP sludges is sent to recycling plants (Table 3.1.7).

The total EU emission to the atmospheric compartment in 1999/2000 from NiCd batteries producing plants is 51 kg/y. The calculated emission factors to air for the different plants are situated between 0.27 and 464 g/ton Cd used (on average: 23 g/ton Cd used). Data from 1996 (Annex II) showed higher emission factors between 1.16 and 901 g/ton Cd used (average: 31.45 g/ton Cd used). Reductions in air emissions can be explained by improvements in air treatment systems. On the basis of the information available no conclusions can be drawn with regard to differences in emission factors between industrial/ portable battery producing sites and different electrode production processes (see Table 3.1.6). No data regarding emissions to air could be provided for company 1 and 3. However, plant 3 stated that since it concerns wet processes, the Cd emissions are mainly through effluents. It should be noted that plant 7 -processing less than 5% of total Cd amount- emits 28.99 kg/year to air, that corresponds with 57% of the total air emissions of all Ni-Cd batteries manufacturing plants.

The total amount of waste –apart from on site WWTP sludge- generated by the Ni-Cd batteries producing industry is 2,353 t/y. It should be noted that this waste includes packaging material, NiCd batteries material (plates, cells, electrolytes), cakes and filters from off site wastewater treatment,…. The majority (91.7%) of this waste is recycled; the other fraction (8.3%) is disposed in a landfill. 2,091 tonnes of this waste is sent to an external recycling plant, 66 tonnes is internally recycled.

In analogy with the Cd/CdO producing plants the receiving environmental compartments for the emissions of the NiCd batteries plants are water and air. The total amount of cadmium released to the environment during manufacturing of Ni-Cd batteries in 1999/2000 is 116 kg/y. The total use of cadmium for the production of batteries is 2,166 ton (based on individual plant data for 1999/2000).

Table 3.1.5 Aquatic emissions from NiCd batteries producing plants in the EU (UC 12: Conductive agents)

| plant N° | Battery type | Electrode production process | consumption volume | processing emission | emission factor | conc. in effluentb | number of production days | Concentration in effluent | effluent flow | flow receiving watera | year |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | Ton/y1 | kg/y | g/ton |  |  | mg/L | m³/d | m³/d |  |
| 1 | Industrial | Pocket plate | 39.5 | 4.9 | 124 | M (T) | 225 | 0.43 (P90) | 127 (P90) | External to municipal STP | 1999 |
| 2b | Industrial | Po–cket plate -vented | 395 (production only) (507) (total, inclusive recycling) (Cd from batteries: 85) | 7.3 | 18.5 | M (T) | 330 | 0.12 (P90) | 367c (P90) | 432,000 | 2000 |
| 3 | Industrial | Sintered and PBE | 635 | 30.5 | 48 | M (T) | 315 | 0.12 (P90) | 960 | 13 106 | 2000 |
| 4 | Portable | Sealed cylindrical shaped/ sintered and PBE | 842 | 21.9 | 26 | M (T) | 330 | 0.13 (P90) | 771 (P90) | 5.4 105 | 2000 |
| 5 | Industrial | Fiber and (Pocket plate: imported) | 59.7 | <0.07 | <1.1 | M (T) | 230 | < 0.03 | 5 | External to municipal STP | 2000 |
| 6f | Industrial | Fiber plate | 132.7 | 0d | 0d | N/A | 250 | N/A | N/A | N/A | 1999 |
| 7g | Industrial | Pocket plate -vented | 62.5 | 0e | 0e | N/A | 300 | N/A | N/A | N/A | 1999 |
|  |  |  | Total amount of Cd used during production of batteries (ton/y) | Total Cd emission to water (kg/y) | Emission factor (g/ on Cd used) |  |  |  |  |  |  |
|  | 2,166 | 65 | 31.1 |  |  |  |  |  |  |

N/A: not applicable b M: measured value, T: total concentration   a minimum flow rate  b Company 2 emits to the marine environment. cIf cadmium emissions via storm water are included the effluent flow increases to 424 m3    fdAll process wastewater is collected and sent to recycling company, no emissions to water gemissions to water from cleaning operations are disposed in alkaline solution and externally recycled, no emissions to water; PBE: Plastic Bonded Electrode

Table 3.1.6 Atmospheric emissions from NiCd batteries producing plants in the EU (UC 12: Conductive agents)

| plant | Battery | Electrode | production/consumption | Processing | emission | year |
| --- | --- | --- | --- | --- | --- | --- |
| N° | type | production process | volume | Emission amount | factor |  |
|  |  |  | ton/y | kg/y | g/ ton |  |
| 1 | Industrial | Pocket plate | 39.5 | n.d.a | n.d.a | 1999 |
| 2 | Industrial | Pocket plate -vented | 395 (production only) (507) (total, inclusive recycling) (Cd from batteries: 85) | 1.6 | 4.1 | 2000 |
| 3 | Industrial | Sintered and PBE | 635 | n.d.a | n.d.a | 2000 |
| 4 | Portable (emergency lighting) | Sealed cylindrical shaped/ sintered and PBE | 842 | 13.5 | 16 | 2000 |
| 5 | Industrial | (Pocket plate: imported) and fiber | 59 | 7 | 119 | 1999 |
| 6 | Industrial | Fiber plate | 132.7 | 0.036 | 0.27 | 1999 |
| 7a | Industrial | Pocket plate -vented | 62.5 | 28.99 | 464 | 1999 |
|  |  |  | Total amount of Cd used during production of batteries (ton/ y) | Total Cd emission to air (kg/y) | Emission factor (g/ ton Cd used) |  |
|  |  |  | 2,166 | 51 | 23 |  |

a No data. However, it is noted that it concerns a wet process, so the emissions of Cd are mainly through effluents.

PBE: Plastic Bonded Electrode

It should be noted that plant 7 -processing less than 5% of total Cd amount- emits 28.99 kg/year to air, that corresponds with 57%  of the total air emissions of all Ni-Cd batteries manufacturing plants.

Table 3.1.7 On-site Waste Water Treatment Plant (WWTP) and sludge information (UC 12: Conductive agents)

| plant N° | Type of WWTP | Efficiency (% removal) | Amount of sludge produced (t/y) | Cd Content (%) | Destination sludge | year |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Physico-chemical treatment | n.d. | 17.5 | 2-4 (<30% water) | External recycling plant | 1999 |
| 2a | Flocculation and filtration facility | 99.7% | 128.7 | 2 (water content : 55%) | (On site) recycling plant | 2000 |
| 3 | Flocculation, flottation, filtration | 99.2% | 244 | 1.7 (water content : 57%) | Landfilled | 2000 |
| 4 | Flocculation and filtration facility | 99.9% | 330 | 9.7 (water content : 50%) | External recycling plant | 2000 |
| 5 | Filtration | n.d. | 10 | n.d. | External recycling plant | 1999 |
| 6b | No emissions to water (recycled) | / | / | / | / | 1999 |
| 7c | No emissions to water (disposed of) | / | / | / | / | 1999 |
|  |  |  | 730.2/y |  |  |  |

a Producer and recycler

b All process wastewater is collected and sent to recycling company

c emissions to water from cleaning operations are disposed in alkaline solution and externally recycled

n.d:. no data available

Table 3.1.8 Waste information (UC 12: Conductive agents)

| plant N° | Type of waste produced | Quantity of waste (t/year) | Cd content | Waste disposal type | year |
| --- | --- | --- | --- | --- | --- |
| 1 | Industrial battery cells Raw material bags Substituted filters Cleaning materials and tools | 118.8 0.4 0.25 0.5 | <3% (overall average content) | External recycling plant (98 %) Landfill (2 %) | 1999 |
| 2a | Barium sulphate Used filtersb | 194 66 | <0.001% <0.1% | Landfilled External recycling plant | 2000 |
| 3 | Scraps | 380 | 17.4% | External recycling plant | 2000 |
| 4 | Plates (neg.) Cells | 46 181 | 50% 11% | External recycling plant | 2000 |
| 5 | Pocket plate Dust Batteries Electrolyte | 6.2 3.3 8.1 126.4 | 30-40% 45% 3-10% 0.2% | External recycling plant | 1999 |
| 6 | Used KOH from formation process Wastewater from impregnation Filter cake from wastewater formation process | 852 102 7 | Trace conc 1 g/L 20% | External recycling plant External recycling plant External recycling plant | 1999 |
| 7 | Electrode overlefts Old alk. Sol. | 52.66 208 | n.d. | External recycling plant | 1999 |

a Producer and recyler

b after Cd and Ni dust removal (dust is on site recycled)

n.d.:  no data available

Since the manufacturing activities of Ni-Cd batteries are restricted to a small number of sites in a limited number of EU countries (i.e. Sweden, France, Germany, Spain and Belgium), and hence are not equally distributed over the EU territory, it is not possible to apply the 10% rule for estimation of the regional emissions. In that case it is recommended to use the EU volume as input for the region and to apply another percentage or to use specific values as input for the regional model (e.g. emissions from the largest emitter). In this case the emissions from the largest emitter to air and water were allocated to the region. (EC, 1998).

Table 3.1.9: Summary emissions from production of Ni-Cd batteries (life cycle stage 1)

| Compartment | Total | Regional | Continental |
| --- | --- | --- | --- |
|  | kg/y | kg/y | kg/y |
| Air | 51 | 28.99 | 22.01 |
| Wastewater | 4.97 | 4.9 | 0.07 |
| Surface water | 60 | 30.5 | 29.5 |
| Soil, urban/ind | 0 | 0 | 0 |
| Total | 116 | 64.4 | 51.6 |

##### Life cycle stage 2: Incorporation into battery-powered devices and applications

No emissions of the substance under study are expected.

##### Life cycle stage 3: Use, recharging and maintenance by end user

No direct emissions of cadmium of the substances under study are expected from the use of batteries, except possibly in the cases of battery corrosion or destruction of the battery. The number of batteries affected in these ways are expected to be small. The indirect cadmium emissions (generation of electric power, e.g. combustion of coal) associated with recharging of batteries have not been considered in this report. Lankey (1998) estimated an average total energy consumption of 286 ± 222 MJ/kg for the use phase (1,000 charge cycles over the life of the battery). These figures are deemed negligible in comparison with the overall energy consumption and related indirect cadmium emissions.

##### Life cycle stage 4: Recycling

The emissions to air and water during the recycling of batteries are presented in Table 3.1.10 and 3.1.11 (Industry Questionnaire, 2000/2001). From the questionnaires it is also clear that information concerning on site wastewater treatment is lacking (plant 1). Information on waste quantities generated – other than on site WWTP sludge-is presented in Table 3.1.12.

Plant 2 stated that there are no “open treatment steps” at their site. As a consequence they do not emit Cd to either compartment. The wastewater produced is collected and treated off site. The sludge produced during this process is landfilled. One company that is both producer and recycler is reported as a Ni-Cd producer (cfr section 3.1.2.2.1), since a split up of emissions was not feasible.

The total Cd emission to the aquatic compartment from Cd recyclers in the EU is based on information from 1 plant only and is 0.126 kg/y. The accompanying emission factor for that plant is 0.16 g/ton Cd recycled. In comparison with emission data from 1996 (presented in Annex IV), a very similar emission factor of 0.19 g/ton Cd recycled is obtained. No emission factor was calculated for recycling plant 2 since the on-site operating processes are zero emission processes. In general industrial effluents from the plants are treated in an on site Waste Water Treatment Plant (WWTP) before being discharged into surface waters. However, plant 2 collects its wastewater for off site treatment. Since no additional information concerning the Cd content of influents of the local treatment plant was provided by industry, the emissions to wastewater and sludge could not be specified.

The total EU emission to the atmospheric compartment in 1999/2000 from Cd recyclers producing plants is 1.77 kg/y (based on plant 1 only). The calculated emission factor to air for plant 1 is 2.21 g/ton Cd recycled. Data from 1996 (Annex IV) showed a higher emission factor of 9.7 g/ton Cd recycled. Reductions in air emissions can be explained by improvements in air treatment systems. No emission factor was calculated for recycling plant 2 since the operating processes are zero emission processes.

The total amount of waste –including the off-site treated wastewater from plant 2- generated by the Cd recycling industry is 1,045 t/y. It should be noted that this waste solely includes Cd containing material. The majority of this waste is sent to an external recycling plant (66.3%) internally treated (8%) or sent to a specialised landfill (25.6%). Taking into account the Cd content of this waste, it can be concluded that in total <907 kg Cd is externally recycled, 134 kg Cd is internally treated and 0.4 kg Cd is landfilled.

The overall Cd emission to the environment is only 1.9 kg/y. 93 % of this emission is directed to air. Since 842,300 kg/y is produced by the Cd recycling plants a very low total emission factor of 0.0002 % can be calculated.

Table 3.1.10 Aquatic emissions from Cd recycling plants in the EU (Cd recycled from batteries, production scrap & other sources)

| plant N° | production/ consumption volume | processing emission | emission factor | conc. in effluentb | number of production days | Concentration in effluent | effluent flow | flow receiving water | year |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | ton y-1 | kg/y | g/ton |  |  | mg/L | m³/d | m³/d |  |
| 1a | 800.5 (376 .8 batteries: 47.1% | 0.126 | 0.16 | M(T) | 350 | 0.45 (P90) Average: 0.17 | 6.1 (P90) Average: 3.8 | 11,500 | 2000 |
| 2 | 41.8 (37.6 batteries :89.9%) | 0c | 0 | N/A | 240 | N/A | N/A | N/A | 1999 |
| TOTAL | 842.3b (414.4 from batteries ) | 0.126 |  |  |  |  |  |  |  |

a Only two recyclers (instead of three) have been listed under Cd-recyclers. The reason is that one company is both recycler and producer. A further breakdown of the submitted figures between the producing process and the recycling process was not feasible. For this reason this company has been listed with the other producers.

b this total amount represents not only the cadmium recycled from Ni-Cd batteries (414.4 t (256.3 tonnes portable batteries; 158.1 tonnes industrial batteries)) but includes also other Cd containing waste (production scrap: 286.4 t/y, other sources (not specified): 141.5 t/y). On average 81% of the batteries recycled are EU batteries; 19% is imported (Industry Questionnaires, 2000/2001; information from SNAM & SAFT). On the other hand, the recycled amount of Cd produced by the third recycler (115 t (battery fraction: 85t)) is not included in the given figure.

c no “open” treatment steps; no emissions. Wastewater is collected and treated off-site. No further information is provided. Sludge is landfilled

M (T): measured total concentration after WWTP i.e. Cd concentration virtually equal to dissolved Cd concentration

N/A: not applicable

Table 3.1.11 Atmospheric emissions from Cd recycling plants in the EU (Cd recycled from batteries, production scrap & other sources)

| Plant | production/consumption | processing | emission | year |
| --- | --- | --- | --- | --- |
| N° | volume | emission amount | factor |  |
|  | ton/y | kg/y | g/ton |  |
| 1a | 800.5 (376.8 batteries: 47.1%) | 1.77 | 2.21 | 2000 |
| 2 | 41.8 (37.6 batteries: 89.9%) | 0c | 0 | 1999 |
| TOTAL | 842.3b (414.4 from batteries ) | 1.77 |  |  |

a Only two recyclers (instead of three) have been listed under Cd-recyclers. The reason is that one company is both recycler and producer. A further breakdown of the submitted figures between the producing process and the recycling process was not feasible. For this reason this company has been listed with the other producers.

b this total amount represents not only the cadmium recycled from Ni-Cd batteries (414.4 t (256.3 tonnes portable batteries; 158.1 tonnes industrial batteries)) but includes also other Cd containing waste (production scrap: 286.4 t/y, other sources (not specified): 141.5 t/y). On average 81% of the batteries recycled are EU batteries; 19% is imported. (Industry Questionnaires, 2000/2001; information from SNAM & SAFT). On the other hand, the recycled amount of Cd produced by the third recycler (115 t (battery fraction: 85t)) is not included in the given figure

c no “open” treatment steps; no emissions. Wastewater is collected and treated off site. No further information is provided. Sludge is landfilled

Table 3.1.12 Waste information for Cd recyclers in the EU

| plant N° | Type of waste produced | Quantity of waste (t/year) | Cd content | Waste disposal type | year |
| --- | --- | --- | --- | --- | --- |
|  |  |  | mg/kg |  |  |
| 1a | Batteries plastic boxes Batteries metallic boxes Fe/Cd electrodes after treatment Concentrated electrolytes Process slag Air treatment dust Used filters Rainwater sludges | 268 231 221 216 58 23 2.6 0.2 | 1.5 <2,000 <2,000 10,000 Pure CdO Pure CdO 20,000 3,000 | Special landfill External recycling External recycling External scrap treatment Internal treatment Internal treatment Internal treatment Internal treatment | 2000 |
| 2 | Plastic waste Wastewater condensed with vacuum treatment furnace | Small 25 | <0.005% Cd n.d. | n.d. External treatment, Sludges are landfilled | 1999 |

a Only two recyclers (instead of three) have been listed under Cd-recyclers. The reason is that one company is both recycler and producer. A further breakdown in the submitted figures between the producing process and the recycling process was not feasible. For this reason this company has been listed with the other producers.

n.d.: no data available

Since the recycling activities of Ni-Cd batteries are restricted to a small number of sites in a limited number of EU countries (i.e. Sweden, France and Germany), and hence are not equally distributed over the EU territory, it is not possible to apply the 10% rule for estimation of the regional emissions. In that case it is recommended to use the EU volume as input for the region and to apply another percentage or to use specific values as input for the regional model (e.g. emissions from the largest emitter). In this case the emissions from the largest (and only) emitter to air and water were allocated to the region. (EC, 1998).

Table 3.1.13: Summary emission from recycling of NiCd batteries (life cycle stage 4)

| Compartment | Total | Regional |
| --- | --- | --- |
|  | kg/y | kg/y |
| Air | 1.77 | 1.77 |
| Wastewater | 0 | 0 |
| Surface water | 0.13 | 0.13 |
| Soil, urban/ind | 0 | 0 |
| Total | 1.9 | 1.9 |

##### Life cycle stage 5: Disposal

###### Scope definition

At the end of their technical lifetime batteries or equipment containing Ni-Cd batteries may end up in the waste stream or in private or municipal collection points. The end of life management of batteries consists of collection, recycling, landfills and incineration. A schematic overview of the cadmium flows related to the life cycle of Ni-Cd batteries is given in figure 3.1.1.

Figure 3.1.1: the life cycle of Ni-Cd batteries

The size of the battery waste stream is related to the amount of batteries sold/used in previous years. In the case of Ni-Cd batteries there is a considerable time lapse between the end of service life for the product and the occurrence of emissions from the waste treatment processing. The delay between marketing and emissions is mainly governed by (1) the service life-span (2) possible intermediate storage (stockpiling/hoarding) and (3) the transformation/transportation processes in landfills or incineration residues. As a result, current emissions probably may not be representative for the potential future emissions that are expected to take place several decades after production and processing of a substance have ceased.

In this regard this report addresses both the instantaneous cadmium emissions because of waste treatment (e.g. incineration) and the cumulative cadmium emissions of landfills. Guidance on how to estimate the emissions from the waste disposal stage is not provided within the Technical Guidance Document (TGD, 1996). The revised TGD includes some sections on waste disposal and has been taken as the starting point for the proposed approach as outlined here below.

Both the current and future cadmium emissions will be assessed albeit in a semi-quantitative way. Current emissions will initially be estimated based on an overall European situation. However, since waste management strategies may differ considerably between the Member States, due consideration will be given to these differences by means of including several scenarios (with the extremes: 100 % landfilling and 100 % incineration). Main emissions of cadmium from incineration of waste are expected to occur through air if no adequate flue gas treatment is in place and the disposal and/or re-use of incineration residues.  However, neither the delayed cadmium emissions of the re-use of incineration residues nor the impact of future expected increase in cadmium content of bottom ash and fly ash on the re-usability of these incineration residues have been quantified. The major environmental concerns associated with metals in landfills are usually related to the generation and eventual discharge of leachate into the environment. Therefore the aforementioned emissions will be the focal point of this report. However, the impact of a future change in the MSW composition on the composition of the leachate of a landfill could not be judged based on the current lack of knowledge and methodology. Emissions of recycling are taken into account in this report at the manufacturing phase in section 3.1.2.2.4.

###### Contribution of Ni-Cd batteries to the cadmium content of Municipal Solid Waste: current situation

MSW consists of vast array of materials discarded after their useful life and is very heterogeneous of nature. Reported total concentrations of cadmium in MSW are summarised in Table 3.1.14 and visualized in Figure 3.1.2. and range between 0.3-12 g Cd/tonne dry wt. The observed differences are due to the heterogeneity of the Municipal Solid Waste stream, the methodology used to estimate the total cadmium concentration and possible pre-treatment steps  For example the study of Maystre (1994) calculated the total flow of cadmium as a result of the individual cadmium content in a given type of material and the fraction of this material in the total amount of MSW. The obtained total cadmium concentration of 6 g/tonne dry wt. does not include the contribution of Ni-Cd batteries. Brunner & Mönch (1986) and Brunner & Ernst (1986) reported total Cd values of 8.7-12 g/tonne dry wt. These values were calculated from the analysis of the composition of the incineration products. Direct waste analysis (Otte, 1995; ADEME, 1988 and 1993) revealed similar figures.

Table 3.1.14 Total cadmium concentrations (g/tonne dry wt.) in MSW

| Country | g/tonne | Methodology used | Reference |
| --- | --- | --- | --- |
| Finland | 0.3-4.3 | Direct Waste Analysis | Assmuth (1992) |
| Switzerland | 8.7 12 | Analysis incineration products | Brunner & Mönch, (1986) and Brunner & Ernst (1986) |
| Switzerland | 8.6 |  | Titalyse (1997) |
| Germany | 10 | Not specified | Horch (1987) cited in Reimann (1989) |
| Germany | 10 | Not specified | Reimann (1989) |
| Germany | 12 | Not specified | Reimann (2002) |
| The Netherlands | 3.5 | Direct Waste Analysis | Otte (1995) |
| The Netherlands | 6.4 | Not specified | Rijpkema (1993b) cited in Bernard et al. (2000) |
| The Netherlands | 2.6 | Direct waste analysis after sorting | Wiaux (2002) |
| The Netherlands | 10.2 | Not specified | Rijpkema (1996) cited in Mersiowsky (2002) |
| The Netherlands | 8.4 | Analysis incineration products | Krajenbrink & Eggels (1997) (MSW of 1994) |
| UK | 1.7 | Direct Waste Analysis | (Ross et al, 2000) |
| UK | Average 0.8 P50: 0.7 P90: 1.5 | Direct Waste Analysis (data 1992-1993) | NETC (1995) |
| Sweden | 2.1-5.8 | Direct Waste Analysis | Flyhammer & Hakansson (1999) |
| Sweden | 8.3 | Not specified | Statens Energiverk (1986) cited in Flyhammer et al, 1998) |
| France | 6a | Mass Flow | Maystre (1994) |
| France | 8 | Direct Waste Analysis | ADEME (1988) in SFSP (1999) |
| France | 4 | Direct Waste Analysis | ADEME (1993) |

a batteries were not included

Figure 3.1.2: Evolution of Cd concentration (g/tonnes dw) in MSW

In general there seems to be a slight tendency that higher cadmium concentrations in the MSW have been found in the past (8-12 g/tonne dry wt.) than at present (0.3-8 g/tonne dry wt) (Figure 3.1.2: Since data are scarce and a large uncertainty surrounds the reported figures all data were, however, pooled together. Based on the pooled data the average Cd content of MSW is 6.2 mg/kg dry wt. (median = P50 = 6.4 mg/kg dry wt.). In the EU-16, 160,058 ktonnes of MSW is generated (section 3.1.2.2.5.4). The moisture content of MSW is typically on average 30 % (Van der Poel, 1999, Mersiowsky, 2001; DTU, 2001) yielding 112,041 ktonnes of MSW (dry weight). The reasonable worst case total cadmium content of MSW on a dry weight basis is derived as the 90th percentile and equals 10 g Cd/tonne dry wt. This value is taken forward in the calculations of the emissions (chapter 3) and equals a cadmium  load of 1.1 ktonnes.

Only a fraction of this total cadmium content originates from Ni-Cd batteries. Table 3.1.15 illustrates the typical average metal concentrations of MSW constituents.

Table 3.1.15 Average concentration (mg/kg dry wt.)  of  metals in MSW components (Maystre et al., 1994 adapted)

| Types of Materials | Cu | Zn | Cd | Hg | Pb |
| --- | --- | --- | --- | --- | --- |
| Plants and Food | 28 | 74 | 3 | <1 | 235 |
| Meat waste | 24 | 96 | 4 | <1 | 82 |
| Natural Fibers | 58 | 104 | <2 | <1 | 24 |
| Synthetic Fibers | 9 | 43 | 2 | <1 | 19 |
| Leather | 75 | 437 | 5 | <1 | 372 |
| Aluminium | 2 | 17 | 53 | <1 | 84 |
| Non Ferrous | 1792 | 46827 | 10 | <1 | 30010 |
| Electronic Equipment | 30333 | 17689 | 509 | <1 | 29805 |
| Plastic foam | 155 | 283 | 8 | <1 | 288 |
| Rubber | 28 | 7028 | 8 | <1 | 197 |
| Molded Plastic Bodies | 19 | 39 | 138 | <1 | 259 |
| Primary Batteries Zn-C | 2725 | 95305 | 5 | 72 | 102 |
| Paper | 280 | 35 | 8 | <1 | 399 |
| Cardboard | 84 | 60 | 2 | <1 | 43 |
| Dust Bin Bags | 200 | 363 | 6 | 86 | 470 |
| Paper + Paraffine | 210 | 77 | 4 | <1 | 263 |
| Nickel-Cadmium Batteriesa | - | < 100 | 130’000 | <1 | 1.0 |

a In the study of Maystre (1994) Nickel-Cadmium batteries were not reported as a specifically identified type of material entering the composition of Municipal Solid Waste but for the purpose of Comparison. they  have been added in Table 3.1.15.

It is obvious that Ni-Cd batteries have the highest concentration of cadmium when compared to other types of materials. The final contribution, however, to the overall cadmium content is of course dependent on the weight distribution of the different waste components.

Different studies attempted to estimate the specific contribution of Ni-Cd batteries to the overall cadmium load in MSW. Reported estimates of the amount of cadmium in the MSW originating from Ni-Cd batteries vary widely from 10-85 % (EPA, 1989, Walker, 1995, Chandler, 1995, STIBAT 1998 & 2000, SCRELEC, 1999, Lemann, 1995). The reason for this large variation is among other things related to the relative small sample volumes, the heterogeneity of the municipal waste stream and the method that is used to quantify the amount of Ni-Cd batteries in MSW.

Roughly two approaches can be distinguished. The first approach tries to predict the MSW composition indirectly through a material flow analysis. In the second approach MSW is being sorted and the cadmium concentration of the constituents are directly analysed. Typically, a material flow analysis is based on the collection of product historical data on the quantity of cadmium consumed in the production of a product. Finally, after correction for import and export the time it takes for the cadmium to reach the waste stream is projected by estimating the life time of the product and assuming that the product will be discarded at the end of this period. These estimates of gross discards are adjusted for materials recovery (recycling) and the remaining portion is the estimate of the net discard in MSW. In the available mass flow studies on Ni-Cd batteries hoarding has not been taken into account resulting in an overestimation of the contribution of Ni-Cd batteries to the overall cadmium emissions in MSW in Europe. The Lemann study (1995) indicating the highest contribution (85%) of Ni-Cd batteries was considered unreliable after a critical evaluation of the data presented. In this study an element and material balance of the Municipal Solid Waste incinerator Hagenholz was conducted in 1995 in parallel with a detailed slag analysis. The results revealed that only 3.64 tonnes Ni-Cd scrap/year could be recovered. This figure was approximately 4 times lower than the estimated mass flow of Ni-Cd batteries reaching the incineration plant, based on FOEFL statistics on the use of batteries in 1992 (11.5 tonnes/year on average). The authors of the study explained these conflicting results by the simple fact that more than three-quarters of the batteries decompose completely during the incineration process and are therefore unrecognisable in the crude slag. Based on the latter assumption the FOEFL statistics of 1992 were still used (the data from 1992 were compared with the analysis from March 1995 because the average life time for Ni-Cd batteries were estimated to be between 1-3 years). Since the total cadmium load for 1994 was estimated to be 2,437 tonnes/year it was concluded that Ni-Cd accumulators caused 85 % of the cadmium input in the Hagenholz incinerator. However, if the measured discard of 3.64 ton of Ni-Cd  is used only 20 % is attributable to Ni-Cd batteries (assuming an average Cd content of 13.8 %).

Another method of estimating cadmium in MSW is to examine actual concentrations of cadmium found in municipal refuse samples and to scale these concentrations to the overall waste stream. The analysis of the cadmium content of MSW offers the advantage of being a direct approach circumventing the above mentioned constraints. However, waste composition data are uncertain, and the proportions of individual components typically vary considerably from sample to sample. Sample numbers and waste quantity analysed should be sufficient high to develop a statistically reliable picture of composition. At present, while some data are available from various countries in waste quantities and component distribution, data that consider the chemical composition of the various components in the waste stream is limited. Three major campaigns for sorting portable batteries from M.S.W. streams have been realised in the Netherlands and France, during the last years. The results of those campaigns are presented in Table 3.1.16.  They indicate that the fraction of primary battery is found in the weight fraction range of 150 to 170 ppm. The rechargeable batteries’ fraction, composed mainly of consumer/sealed portable Ni-Cd batteries are in the range of 4 to 9 ppm (on a wet weight basis). As such it can be concluded that Ni-Cd batteries as a percentage of all battery types found in MSW is in the range of 2.6-6.6% (cfr Table 3.1.16). Similar figures have been reported by the Witzenhausen Institut (Witzenhauzen, 2001) with Ni-Cd contributions ranging from 3.5-8.4 %. A weighted average of 6 % has been reported by Witzenhausen Institut (2004). Taken into account that on average a portable sealed Ni-Cd battery contains 13.8 % of Cd and contains 5 % water (Table 2.2.5) a lower limit of 0.5 g Cd/tonne wet wt.  (4 X 0.138 x 0.95 = 0.52) and an upper limit of 1.2 g Cd/tonne wet wt. can be calculated (9 X 0.138 X 0.95 = 1.17). The moisture content of MSW is typically on average 30 % (Mersiowsky, 2001; DTU, 2001).  Based on this the above figures can be converted to a dry weight basis and a lower and upper limit of respectively  0.7 and 1.7 g Cd/tonne dry wt. is obtained.

Table 3.1.16: Fraction of Batteries found in MSW: Primary and sealed portable Ni-Cd batteries in various European countries.

| Country | Year | Primary Battery Weight Ratio In M.S.W.(ppm) | Ni-Cd Battery In M.S.W (mg/kg wet wt.) | Quantity of M.S.W. studied In Tons | Source |
| --- | --- | --- | --- | --- | --- |
| The Netherlands | 1998 | 170 | 8 | 10,000 (continuous) | STIBAT |
| The Netherlands | 2000 | 160 | 9 | 10,000 (continuous) | STIBAT |
| Austria | 2000 | 230 | 11 | 377 (sampling methodology) | U.B.F. |
| Belgium | 1998 and 1999 | 100 | 5a | 4.5 (sampling methodology) | I.B.G.E |
| Germany | 2000 | 370 | 23b | 400 (sampling methodology) | GRS |
| Sweden | 1996 | 100-200 | 6-6-13.2c | (sampling methodology) | RVF |
| France | 1999 | 150 | 4 | 8,900 (one month campaign) | SCRELEC & ADEME |

a Calculated on the basis of the estimate that the amount of NiCd is 5 % of total consumer/sealed portable batteries

b Based on 82 millions inhabitants and 25.5 millions of tonnes MSW per year (1999).

c Data supplied by Renova (2000)

Similar campaigns have been conducted in Austria, Belgium and Germany but on a much smaller scale (4.5-400 tonnes of MSW). These studies report values between 5 and 23 mg/kg wet wt. resulting in a maximum Ni-Cd battery contribution of 3.01 g Cd/tonne wet wt. (23 x 0.138 x 0.95) or 4.3 g Cd/tonne dry wt.

As a reasonable worst case it is assumed in this report that the total cadmium content of MSW equals 10 g Cd/tonne dry wt. The influence of this parameter to the overall assessment is explored in the sensitivity analysis (3.1.2.2.5.7). Most of the prevailing evidence coming from MSW sorting studies, supports a contribution of Ni-Cd batteries to the overall cadmium load between 0.7 and 1.7 g/ton dry wt., i.e. a Ni-Cd contribution of 10-20 %.  Based on the maximum obtained Ni-Cd contribution of 4.3 g Cd/tonne dry wt. an allocation of 43 % can be calculated. Taken into account the uncertainty surrounding the proposition of one figure, an allocation range of 10 -50 % is maintained in this report for the assessment of the current emissions due to Ni-Cd batteries. For the current scenarios the 10 % is representative of the typical situation. The 50 % is representative of the worst case contribution However, in modelling towards the future, the assumption of 10 % will result in a worst case estimate.

###### Forecasts of future battery waste arisings

In order to calculate future emissions due to the presence of Ni-Cd batteries in waste it is imperative that realistic forecasts of battery waste arisings can be made. For the Municipal Solid Waste stream only the contribution of sealed portable Ni-Cd batteries have been considered.

The predictions of future battery waste arisings are hampered by the fact that the length of time between sale/first use and disposal of a battery by the user varies largely according to the type of the battery and its application. The amount of Ni-Cd batteries ending up for the majority of cases in the MSW waste stream is function of the efficiency of collection and the amounts available for collection. The latter is again subject to the battery lifetime and the “hoarding” process.  A schematic overview of the different phases in the calculation of the future waste arisings is given in Figure 3.1.3.

Figure 3.1.3: Rationale used for calculating waste arisings for  Ni-Cd batteries

The different steps are explained more in detail hereafter.

Calculation of the amount of used Ni-Cd batteries coming available for collection

Future battery waste arisings are calculated based on the amount of batteries coming available for collection in a certain year.

The amount of used Ni-Cd batteries available for collection varies with the lifetime of the batteries and the hoarding behaviour of the end user. Since both battery lifetime and hoarding behaviour are difficult to assess, calculating the amount available for collection will thus be subject to an error proportional to the uncertainty over these parameters.

An alternative method, not sensitive to the above uncertainties, is the use of a battery half-life instead of a battery lifetime. The battery half-life is defined as the time needed to collect 50 % of the quantity introduced to the market in a given year. This battery half-life can be derived from measurements of the quantity of batteries present in MSW wastes, mixed wastes and industrial wastes in conjunction with battery Date Coding campaigns.

In absence of more data on the subject the amount available for collection will be calculated based on the historical market base line (e.g. section 2.2.2.4.2.4 for consumer/sealed portable Ni-Cd batteries) following two models. The first model is a simplified worst case model just taking into account that the batteries will come available for collection/disposal within the average battery lifetime and ignoring the effect of hoarding. In the second model hoarding (especially important for portable sealed Ni-Cd batteries) is incorporated. Inclusion of a hoarding period will have the effect of delaying the reporting of a battery to the waste stream over the assumed hoarding period.

The actual lifetime of a Ni-Cd battery may be five years to twenty-five years depending upon the specific battery design and its application. Reported values for consumer/sealed portable batteries typically range between 3-10 years (Cloke, 1999, Fujimoto, 1999). Similar values (4-8 years) are reported in a Danish study on the mass balance on cadmium (Miljostyrelsen, 2000). In this report the concept of an average battery lifetime for batteries will be used and is defined as the average lifetime until the battery is being collected. For portable batteries an average battery lifetime of 5 years will be used. Industrial batteries are assumed to have an average battery lifetime of 10 years. Results of hoarding studies indicate that the overall hoarded supply on consumer/sealed portable Ni-Cd batteries 15 years after the useful lifetime is 65 % (Fujimoto, 1999). Recent information obtained from a similar hoarding study in Europe revealed an average hoarding rate for replacement batteries of 62 %. For batteries in large appliances that are disposed of without prior removal of the batteries the hoarding rate can be as high as 95 % (TMO-CSA, 2001).

Projections of future battery waste arisings

The amount of Ni-Cd batteries that will end up in the waste stream in a certain reference year is calculated by summing up the respective fractions coming available for collection in that reference year and correcting this amount with the collection ratio. Since some countries have not yet started with collecting Ni-Cd batteries a range of collection ratios covering both the lower as upper ranges is recommended (section 2.2.2.5.2) as input in the model to predict future battery waste arisings.

Future battery waste arisings for (sealed) portable Ni-Cd batteries

An overview of the models for the (sealed) portable Ni-Cd batteries is given in Table 3.1.17. Further details related to the models’ calculations are available in Annex III.

Table 3.1.17: Overview of the clearance rates (% initial market volume/year) used in the models for predicting waste arising due to (sealed) portable Ni-Cd batteries.

| MODEL 1: Based on average lifetime of 5 year |
| --- |
| Period (year) | Description | Clearance rate (%/year) | % marketed volume left at the end of the period concerned |
| 1-5 | No hoarding (worst case) | 20 | 0 |
| MODEL 2 : GRADUAL |
| Period (year) | Description | Clearance rate (%/year) | % marketed volume left at the end of the period concerned |
| 1 – 5 | Useful life-time | 1 | 95 |
| 6 – 20 | Home storage/hoarding | 2.2 | 62 |
| 21 – 30 | Destock | 6.2 | 0 |

In Model 1 no hoarding is considered. It is assumed that the purchased (sealed) portable Ni-Cd batteries will come available for collection/disposal over a period of 5 years. In Model 2 a more gradual approach is being assumed taking into account the hoarding behaviour of the end user. Within the presumed maximum technical lifetime of 30 years the following clearance rates can be distinguished. Five years after market introduction, due to defects or malfunctions, 5 % will be available for collection or disposal. Another 33 % will be disposed of over the next 15 years. Finally the remaining volume (62 % of the initial market volume) will be destocked within 10 years.

It should be clear that neither the choice of the model nor the battery lifetime will alter the predictions of the future risks associated with landfills due to the fact that the gradual model will only result in a time shift when compared to the model without hoarding. The model without hoarding is not realistic but is given in this report to illustrate the statement above.

For each model only those scenarios were considered which are most likely to occur:

- Scenario 1: Production of portable Ni-Cd batteries will continue at a rate of 13,500 tonnes per year until the hypothetical cadmium ban in 2008 is imposed.

- Scenario 2: Production of portable Ni-Cd batteries will continue at a rate of 13,500 tonnes per year.

For both scenarios collection/recycling was taken into account. Until 2001 the reported collection/recycling weights were used (table 2.2.18). Before 1994 no collection/recycling was assumed. After the year 2001 the scenarios have been run for the assumption of respectively 10 and 75 % collection of Ni-Cd batteries.

The evolution of the cadmium content of MSW solely due to Ni-Cd batteries is summarised in the Tables 3.1.18 and 3.1.19. These figures were obtained by dividing the weight of the disposed Ni-Cd batteries with the average yearly amount of MSW (expressed as dry weight). Between 1995-2001 160,058 ktonnes (wet weight.) of MSW was generated. With a content of 70 % dry matter this can be converted to 112,041 ktonnes (dry weight). Probably the amount of MSW will increase in the future (EEA, 2000) but this has not been taken into account.

Table 3.1.18: Cadmium content (g Cd/tonne waste dry wt.) in MSW due to sealed portable Ni-Cd batteries. Scenario 1: ban imposed

|  | Cd due to other sources | Contribution (sealed) portable Ni-Cd batteries |
| --- | --- | --- |
|  |  | MODEL 1: ACCELERATED | MODEL 2: GRADUAL |
| Year |  | 10 % collection | 75 % collection | 10 % collection | 75 % collection |
| 1981 | 9 | 0.4 | 0.4 | 0.01 | 0.01 |
| 1985 | 9 | 2.4 | 2.4 | 0.1 | 0.1 |
| 1990 | 9 | 6.5 | 6.5 | 0.6 | 0.6 |
| 1995 | 9 | 12.9 | 12.9 | 1.0 | 1.0 |
| 2000 | 9 | 14.1 | 14.1 | 1.0 | 1.0 |
| 2005 | 9 | 15 | 4.2 | 4.9 | 1.4 |
| 2010 | 9 | 9 | 2.5 | 7.5 | 2.1 |
| 2015 | 9 | 0 | 0 | 9.8 | 2.7 |
| 2020 | 9 | 0 | 0 | 11.0 | 3.0 |
| 2025 | 9 | 0 | 0 | 10.2 | 2.8 |
| 2030 | 9 | 0 | 0 | 7.4 | 2.1 |
| 2035 | 9 | 0 | 0 | 2.8 | 0.8 |
| 2040 | 9 | 0 | 0 |  |  |

If a ban is imposed the maximum cadmium content in the MSW due to Ni-Cd batteries is 10.8 g Cd/tonne dry wt. for the gradual model and 15 g Cd/tonne dry wt. for the accelerated model. In both cases no more Ni-Cd batteries are expected to occur in the waste by the year 2040.

Table 3.1.19: Cadmium content (g/tonne dry wt. waste) in MSW due to portable sealed Ni-Cd batteries. Scenario 2: no ban

|  | Cd due to other sources | Contribution (sealed) portable Ni-Cd batteries |
| --- | --- | --- |
|  |  | MODEL 1: ACCELERATED | MODEL 2: GRADUAL |
| Year |  | 10 % collection | 75 % collection | 10 % collection | 75 % collection |
| 1981 | 9 | 0.4 | 0.4 | 0.0 | 0.0 |
| 1985 | 9 | 2.4 | 2.4 | 0.1 | 0.1 |
| 1990 | 9 | 6.5 | 6.5 | 0.6 | 0.6 |
| 1995 | 9 | 12.9 | 12.9 | 1.0 | 1.0 |
| 2000 | 9 | 14.1 | 14.1 | 1.0 | 1.0 |
| 2005 | 9 | 15.0 | 4.2 | 4.9 | 1.4 |
| 2010 | 9 | 15.0 | 4.2 | 7.8 | 2.2 |
| 2015 | 9 | 15.0 | 4.2 | 11.2 | 3.1 |
| 2020 | 9 | 15.0 | 4.2 | 14.0 | 3.9 |
| 2025 | 9 | 15.0 | 4.2 | 14.9 | 4.1 |
| 2030 | 9 | 15.0 | 4.2 | 15.0 | 4.2 |
| 2035 | 9 | 15.0 | 4.2 | 15.0 | 4.2 |
| 2040 | 9 | 15.0 | 4.2 | 15.0 | 4.2 |

If no ban is imposed the cadmium concentration in the MSW due to Ni-Cd batteries will increase until a steady state is reached. The steady state cadmium concentration in the MSW obtained is  ranging between 4.2 and 15.0 g Cd/tonne dry wt. irrespective of the model used.  The Ni-Cd contribution for the year 2000 is estimated with the gradual model to be 1.0 g Cd/tonne dry wt. Remark: note that the lower range of the currently presumed Ni-Cd contribution is 0.7 g Cd/tonne dry wt. (upper range = 1.71. g Cd/tonne dry wt.).

Future cadmium content in MSW

From the previous paragraph a steady state cadmium concentration solely due to the presence of Ni-Cd batteries in MSW is estimated between  4.2 to 15 g/tonne dry wt.).

The current overall cadmium content of MSW is estimated to be 10 g/tonne dry wt. If it is assumed that at present only 10 % of this content can be allocated to the presence of Ni-Cd batteries a current contribution of all other cadmium sources of 9 g/tonnes dry wt. can be calculated (resulting in a worst case assumption for the future Cd content in MSW). If it is further assumed that this contribution will not change in the future this figure can be taken as the starting figure for the calculation of the future cadmium content in the MSW (Table 3.1.20).

Table 3.1.20: Future cadmium content of MSW

| Collection (%) | Cd contribution due to Ni-Cd batteries (g Cd/tonne dry wt.) | Cd contribution due to other sources (g Cd/tonne dry wt.) | Total future Cd content in MSW (g Cd/tonne dry wt.) |
| --- | --- | --- | --- |
| 10 | 15 | 9 | 24 |
| 75 | 4.2 | 9 | 13.2 |

In the worst case scenario, where the collection rate is only 10 %, the cadmium contribution from Ni-Cd batteries may rise to 15 ppm with a batteries’ contribution of 63 % of the total cadmium content in MSW. When collection is at a 75 % rate, the cadmium contribution from Ni-Cd batteries may rise to 13.2 ppm with a batteries contribution of 32 % of the total cadmium content in MSW.

###### Waste management Strategies in Europe

Waste management practices vary considerably among different countries and regions in the EU. The current status of waste management strategies for the different EU countries is presented in Table 3.1.21 and Table 3.1.22. Most  data were extracted from the databank provided by ETWC (ETWC, 2002) which on its turn  is a compilation of  the results of an joined Eurostat/OECD Questionnaire (2000) or based on national reports (France, Norway, Belgium, Sweden, Finland, Austria, Luxembourg and the Netherlands) and OECD statistics (Greece, Italy, Ireland, Spain and Portugal). The data for Germany (landfill and incineration), Spain (incineration) and Portugal (incineration and landfill) were updated with the latest information made available by the Member State.

Table 3.1.21: Landfilling and incineration of MSW (in ktonnes WW) in Europe for the period 1995-2001

| Country | Year | MSW landfilled (ktonnes wet wt.) | MSW incinerated (ktonnes wet wt.) |
| --- | --- | --- | --- |
| Austriaa | 1999 | 1,099 | 479 |
| Belgiuma | 1998 | 1,473 | 1,369 |
| Denmarkc | 1999 | 361 | 1,730 |
| Finlanda | 1997 | 1,610 | 80 |
| Francea | 1998 | 23,352 | 10,781 |
| Germanyb | 2001 | 16,000 | 12,000 |
| Greeced | 1997 | 3,561 | 0 |
| Irelandd | 1995 | 1,432 | 0 |
| Italya | 1998 | 20,768 | 1,949 |
| Luxembourga | 1998 | 62 | 123 |
| Netherlandsa | 1999 | 1,136 | 3,859 |
| Norwaya | 1998 | 1,843 | 374 |
| Portugala,e | 1999-2002 | 2,603 | 1,060 |
| Spaina | 1999 | 17,477 | 1,327 |
| Swedena | 1998 | 1,300 | 1,400 |
| UKa | 1999 | 26,860 | 2,590 |
| Total EU-16 | 160,058 | 120,937 | 39,121 |

a Wastebase (ETWC, 2002)

b Umweltsbundesamt (UBA, 2001)

c Waste Statistics, 1999 (Danish EPA, 2001)

d OECD compendium 1999

e Lipor II, Calheiros JM and Almeida A., pers. com., 2002

The calculation of the share (%) of MSW waste being landfilled or incinerated is calculated using only the ratio between incineration and landfilling in the different Member States.

Table 3.1.22: Landfilling and incineration practices (in %) in Europe for the period 1995-2001

| Country | Year | % of MSW landfilled | % of MSW incinerated |
| --- | --- | --- | --- |
| Austria | 1999 | 69.6 | 30.4 |
| Belgium | 1998 | 51.8 | 48.2 |
| Denmark | 1999 | 17.3 | 82.7 |
| Finland | 1997 | 95.3 | 4.7 |
| France | 1998 | 68.4 | 31.6 |
| Germany | 2001 | 57.1 | 42.9 |
| Greece | 1997 | 100 | 0 |
| Ireland | 1995 | 100 | 0 |
| Italy | 1998 | 91.4 | 8.6 |
| Luxembourg | 1998 | 33.5 | 66.5 |
| Netherlands | 1999 | 22.7 | 77.3 |
| Norway | 1998 | 83.1 | 16.9 |
| Portugal | 1999 | 71.1 | 28.9 |
| Spain | 1999 | 92.9 | 7.1 |
| Sweden | 1998 | 48.1 | 51.9 |
| UK | 1999 | 91.2 | 8.8 |
| Total EU-16 |  | 75.6 | 24.4 |

Overall it can be concluded that landfilling remains the predominant disposal route for waste while there is a growing trend towards increased incineration. (EEA, 2000). The overall ratio between incineration and landfilling of MSW within the European Union is 24.4 to 75.6 (situation 1995-2001).

Quantifying the cadmium emissions caused by landfills or incineration of Ni-Cd batteries is hampered by the fact that available data on landfill and incineration emissions always represent the total emissions of cadmium containing materials present in the waste stream. Therefore the overall cadmium emissions is calculated first. By using a specific allocation key the specific contribution of Ni-Cd batteries to the overall cadmium emission can be quantified.

The overall cadmium emissions may vary considerably depending on the used Flue Gas Cleaning System or the presence of a leachate treating system/protective lining in the case of landfills.

In this report the scenario based on the European average situation (24.4 % incineration and 75.6 % landfill) will be completed by two scenario’s (100 % landfilling and 100 % incineration) to perform a rudimentary sensitivity analysis in order to reflect the extremes in waste management option.

###### Overall cadmium emissions from incineration MSW

Current emissions

Cadmium entering into standard MSW incineration will be distributed among various output fractions such as stack emissions (flue gas), wastewater, fly ash, bottom ash and slag. The distribution pattern of cadmium over these incineration residues is depending on the physical-chemical properties, the gas cleaning technology and the operation and maintenance conditions. While the flue gas and wastewater emissions are immediate, emissions of the incineration residues (via disposal and/or re-use) are delayed.

Flue gas emissions

Approximately 5,000-6,000 Nm3 flue gas is generated per tonne waste (wet wt.) incinerated (Van De Wijdeven, 1991). Today, almost all incineration plants have some kind of flue gas cleaning system (FGCS) in place. The amounts of household waste incinerated per flue gas cleaning system in use by the different Member States are presented in Table 3.1.23 and were extracted from the national data collected by ISWA (2002).  It should be noted that not all countries or incinerators present in a country has been covered. The distribution of the FGCS in percent (based on a weight basis) is presented in Table 3.1.24.

Table 3.1.23: Amounts of household waste (ktonnes wet wt.) treated per Flue Gas Cleaning System (reference year 1999) (ISWA, 2002)

| Country | Dry | SD | WET | Dry + WET | SD +WET | ESP | FF | O | Total |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Austria | 0 | 0 | 437 | 0 | 0 | 0 | 0 | 0 | 437 |
| Belgiuma | 38 | 304 | 208 | 0 | 203 | 0 | 0 | 0 | 753 |
| Denmark | 170 | 367 | 718 | 0 | 0 | 5 | 21 | 0 | 1,280 |
| France | 803 | 0 | 6,465 | 0 | 0 | 706 | 0 | 351 | 8,326 |
| Germany | 155 | 1,117 | 5,024 | 272 | 1,656 | 0 | 0 | 0 | 8,225 |
| UK | 150 | 488 | 0 | 0 | 0 | 0 | 0 | 0 | 639 |
| Netherlands | 0 | 20 | 1,876 | 0 | 917 | 0 | 0 | 0 | 2,813 |
| Norway | 0 | 11 | 305 | 0 | 0 | 0 | 0 | 0 | 316 |
| Portugalc | 0 | 1,060 | 0 | 0 | 0 | 0 | 0 | 0 | 1,060 |
| Spainb | 21 | 991 | 320 | 0 | 0 | 0 | 0 | 0 | 963 |
| Sweden | 322 | 0 | 645 | 283 | 0 | 0 | 53 | 0 | 1,303 |
| Total | 1,660 | 4,358 | 15,997 | 555 | 2,776 | 712 | 74 | 351 | 26,483 |

Source: ISWA, 2002. Dry: Dry scrubbing; SD: Semi dry scrubbing; WET: Wet scrubbing; FF: Fabric Filter; ESP: Electrostatic precipitator; O: other)

a updated figures for Flanders (OVAM, P. Loncke, pers. com., 2002)

b updated figures for Spain (MMA, 2002)

c updated figures for Portugal (LIPOR II, Calheiros JM and Almeida A., pers. com., 2002)

Table 3.1.24: Distribution (%) of Flue Gas Cleaning Systems for different Member States

| Country | Dry | SD | WET | Dry + WET | SD +WET | ESP | FF | O | Total |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Austria | 0 | 0 | 100 | 0 | 0 | 0 | 0 | 0 | 100 |
| Belgium | 5 | 40.4 | 27.6 | 0 | 27 | 0 | 0 | 0 | 100 |
| Denmark | 13.3 | 28.6 | 56.1 | 0 | 0 | 0.4 | 1.6 | 0 | 100 |
| France | 9.7 | 0 | 77.6 | 0 | 0 | 8.5 | 0 | 4.2 | 100 |
| Germany | 1.9 | 13.6 | 61.1 | 3.3 | 20.1 | 0 | 0 | 0 | 100 |
| UK | 23.5 | 76.5 | 0 | 0 | 0 | 0 | 0 | 0 | 100 |
| Netherlands | 0 | 0.7 | 66.7 | 0 | 32.6 | 0 | 0 | 0 | 100 |
| Norway | 0 | 3.4 | 96.6 | 0 | 0 | 0 | 0 | 0 | 100 |
| Portugal | 0 | 100 | 0 | 0 | 0 | 0 | 0 | 0 | 100 |
| Spain | 1.6 | 74.4 | 24.0 | 0 | 0 | 0 | 0 | 0 | 100 |
| Sweden | 24.7 | 0 | 49.5 | 21.7 | 0 | 0 | 4.1 | 0 | 100 |
| Total | 6.3 | 16.5 | 60.4 | 2.1 | 10.5 | 2.7 | 0.3 | 1.3 | 100 |

Source: ISWA, 2002. Dry: Dry scrubbing; SD: Semi dry scrubbing; WET: Wet scrubbing; FF: Fabric Filter; ESP: Electrostatic precipitator; O: other

From Table 3.1.24 it can be concluded that approximately 22 % of all the household waste incinerated in Europe is followed by dry and  semi-dry flue gas cleaning. Wet flue gas cleaning accounts for 63 %. 3 % of the household waste incinerated is followed by ESP or FF only.

Actual measured air emissions of cadmium by Municipal Solid Waste incinerators were available for a number of Member States and when available preference was given to these measured data (indicated in bold/italic). For some Member States (UK, France and Portugal) actual measured emission data (figures in bold/italic) were available. For other Member States a mix of measured and calculated data were available as best estimates. For example in Germany the cadmium emissions due to MSW incineration is estimated to be 0.3 tonnes in the year 1995 (Rentz et al. 1997; Jockel & Hartje, 1995) and was calculated by multiplying the average cadmium concentration measured in the flue gas of 20 incinerators with the amount of gas formed by the total amount of municipal waste incinerated in Germany.  A similar approach has been followed  for Spain and Belgium.

In the case no measured data were available the emission to air was estimated by applying the highest emission factor (based on measured  data) to the amount of MSW incinerated (Table 3.1.21).

:

The modelled/measured annual releases of cadmium to air for the different countries through the incineration of MSW are presented in Table 3.1.25 for the scenario: 24.4 % incineration.

Table 3.1.25: Overall cadmium emissions to air (in kg/year) in Europe due to incineration of MSW. Scenario current incineration 24.4 %

| Country | MSW incinerated (ktonnes wet wt.) | Measured/modelled emissions (kg/year)a,b | Emission factor (g/tonne wet wt.)c |
| --- | --- | --- | --- |
| Austria | 479 | 86d | 0.18 |
| Belgium | 1,369 | 63 | 0.046 |
| Denmark | 1,730 | 300 | 0.17 |
| Finland | 80 | 14 | 0.18 |
| France | 10,781 | 1,922 | 0.18 |
| Germany | 12,000 | 300 | 0.025 |
| Greece | 0 | 0 | 0 |
| Ireland | 0 | 0 | 0 |
| Italy | 1,949 | 351 | 0.18 |
| Luxembourg | 123 | 22 | 0.18 |
| Netherlands | 3,859 | 53 | 0.014 |
| Norway | 374 | 41 | 0.110 |
| Portugal | 1,060 | 3.2 | 0.003 |
| Spain | 1,327 | 54 | 0.041 |
| Sweden | 1,400 | 5 | 0.004 |
| UK | 2,590 | 17 | 0.007 |
| Total EU-16 | 39,121 | 3,231 |  |

a Measured data Belgium (FEA, OVAM 2001, MMUM, 2001); Measured data France: ADEME, 1999; Measured data Norway and Netherlands HARP-HAZ 2002, Measured data Spain:MMA 2002, Measured data Portugal: Lipor, 2002, Measured data Denmark (Miljostyrelsen, 2000), Measured data ’weden, (RVF's Faktarapport 2001 om Avfallsförbränning, cited in ‘com_302+303_env_S9_annex_I provided by KEMI). Measured data UK: Environment Agency inventory 2001.

b Measured data indicated in bold/italic are most of the time best estimates based on a combination of modelled and measured data

c In case no measured data were available the highest measured emission factor (i.e. France: 0.18 g/tonne) has been applied. This was the case for Austria, Finland, Italy and Luxembourg,

d Please note that recently measured data came available for Austrian incinerators which show emissions that are much lower, i.e. 4.2 kg/year (Stubenvoll et al., 2002). Since the current air emissions for the EU 16 already have a negligible contribution to the overall cadmium air emission from all sources (see Tabl 3.1.61)  in the EU, the regional calculations were not recalculated (the modelled data were kept as such). Only the local emissions were changed.

The total amount of MSW being incinerated in 1995-2001 for the EU-16 was 39,121 ktonnes corresponding with an overall EU incineration share of 24.4 %. Based on the calculations above the cadmium emission to the air compartment due to this incineration activity is 3.2 tonnes Cd on a yearly basis.

The observed differences reflect the current technological improvements that have been made in the abatement of air emissions. For example Spain reported that in 2000 almost all incinerators included an active carbon step (Lipor II, personal communication, 2002). The large difference between the UK and France could also be explained by less stringent maximum emission levels in France. The figure of 3,231 kg Cd/year is taken forward for the calculations.

Based on the emission factor (g/ton) calculated for each country, the cadmium emission to air has been calculated for the 100 % scenario (table 3.1.26).

Table 3.1.26: Cadmium emissions to air (in kg/year) in Europe due to incineration of MSW. Scenario 100 % incineration.

| Country | MSW incinerated (ktonnes wet wt.) | Emissions (kg/year) Scenario 100 % |
| --- | --- | --- |
| Austria | 1,578 | 283 |
| Belgium | 2,842 | 131 |
| Denmark | 2,091 | 363 |
| Finland | 1,690 | 296 |
| France | 34,133 | 6,085 |
| Germany | 28,000 | 525 |
| Greece | 3,561 | 641 |
| Ireland | 1,432 | 258 |
| Italy | 22,717 | 4,091 |
| Luxembourg | 185 | 33 |
| Netherlands | 4,995 | 69 |
| Norway | 2,217 | 243 |
| Portugal | 3,663 | 11 |
| Spain | 18,804 | 764 |
| Sweden | 2,700 | 10 |
| UK | 29,450 | 216 |
| Total EU-16 | 160,058 | 14,018 |

Based on the calculations above the cadmium emission to air in a 100 % incineration scenario would result in an emission of 14 tonnes Cd/year.

Emissions from wastewater

Emissions to water results essentially from the discharge of wastewater from incineration plants with wet flue gas cleaning systems. The wastewater has been shown to be contaminated with metals and inorganic salts and have high acidity’s or alkalinity’s (Reimann, 1987). The main sources of wastewater from incinerators are from flue gas treatment as flue gas scrubber water, e.g. alkaline scrubbing of the gases to remove acid gases, and the quenching of incinerator ash.Water pollution from incinerators is generally not regarded as an important problem, because the limited amount of wastewater generated is of the order of 0.5-2.5 m3 per tonne of municipal waste incinerated (Williams, 1998). Reimann (2002) reported a water consumption of 1.1 m3/tonnes for the FGCS and 0.25 m3/tonne as boiler water. Stubenvoll et al (2002) reported amounts of waste water between 0.3-0.4 m3 /tonne. In the BREF document on waste incineration (BREF, 2005) volumes between 0.15-0.3 m3 has been reported. As a worst case assumption the highest volume of wastewater generated  (i.e. 2.5 m3) is used to calculate the regional contributions. For the local assessment both a lower limit (i.e. ± 0.5 m3) as the higher limit is used to calculate the dilution factors (Table 3.1.93).

Reported wastewater cadmium concentrations (before treatment) are given in Table 3.1.27.

Table 3.1.27: Average cadmium concentrations in incinerator wastewater (mg/L) (influent) before treatment.

|  | Cd concentration (mg/L) | Reference |
| --- | --- | --- |
| Flue gas scrubber water | 0.46 | Ozvacic et al (1985) |
|  | 0.5 | Reiman (1989) |
|  | 0.17 | Novem/RIVM (1992) cited in Anthonissen & Meyer (1993) |
|  | 0.303 (incinerator 1) (average concentration 3 samples) | Aminal (1994) |
|  | 0.117 (incinerator 2) (average concentration 3 samples) | Aminal (1994) |
|  | 0.45 (stage 1 acid scrubber phase) (average concentration 104 measurements) min-max = < 0.01-0.76 0.37 (stage 2 alkaline scrubber phase) (average concentration 104 measurements) min-max = 0.1-0.62 | Reimann (2002) |
| P50 (of average values) | 0.3 | Selected for regional calculations |
| P90 (of average values) | 0.47 | Selected for local calculations |

Reduction of metal concentrations and mercury/cadmium concentration is usually through neutralisation via precipitation with calcium hydroxide in the presence of organic sulphides (e.g. the additive TMT15 (trimercaptotriazine) (Reimann, 1987, BREF, 2005). Treatment of an effluent with an average cadmium concentration (104 measurements) of 0.45 mg/L with TMT resulted in a cadmium concentration of < 0.01 mg/L indicating a removal efficiency of at least 98.8 % (Reimann, 2002). For the calculations in this report it will be assumed that 98.8 % of the cadmium is removed to sludge going to a hazardous landfill and that 1.2 % remains in the wastewater. This results in  effluent concentration of approximately 0.004 mg/L (for the median value) and 0.0056 mg/L (for the P90 value). Reported Cd concentrations in the effluents of three Austrian MSW incinerator plants (reference year 2000) are 4 to 5.6 times lower and were respectively < 0.001 mg/L, 0.001 mg/L and < 0.05 mg/L (Stubenvoll et al , 2002). Measured effluent concentrations for  two incinerators in Norway (Brobekk and Klemterud) in the Oslo region are a factor 2.5 lower and were 0.00159 mg/L and 0.00158 mg/L, respectively (Personal communication Jon-Ivar Andersen, Email 03-03-2003).

The annual releases of cadmium to water for the different countries through the incineration of MSW are presented in Table 3.1.28 and Table 3.1.29 for two scenario’s: 24.4 % incineration and 100 % incineration. Since 89 % of the incinerated MSW is followed by some kind of semy dry or wet FGCS it was assumed that for all countries the total incinerator process produced wastewater.

As indicated above for the regional emissions it has been assumed as a worst case estimate that  2.5 m3 waste water per tonne wet wt. of MSW is generated. For the regional calculations the median influent concentration of 0.3 mg/L has been used (i.e.  effluent concentration of 0.004 mg/L). For the local calculations (section 3.1.3.2) the 90th percentile influent concentration of 0.47 mg/L has been used (i.e. 0.0056 mg/L effluent concentration). However, since information on measured effluent concentration are limited an additional scenario have been developed as sensitivity analysis with the maximum measured influent concentration of 0.76 mg/L (i.e 0.009 mg/L in the effluent)

Table 3.1.28: Overall cadmium emissions to water and sludge (in kg/year) in Europe due to incineration of MSW. Scenario current incineration 24.4 %.

| Country | MSW incinerated ((ktonnes wet wt.) | Influent WWTP (kg/year) | Emissions to water (kg/year) Scenario 24.4 % | Emissions to sludge (kg/year) Scenario 24.4 % |
| --- | --- | --- | --- | --- |
|  |  |  | 1.2 % | 98.8% |
| Austria | 479 | 359 | 4 | 355 |
| Belgium | 1,369 | 1,027 | 12 | 1,014 |
| Denmark | 1,730 | 1,298 | 16 | 1,282 |
| Finland | 80 | 60 | 1 | 59 |
| France | 10,781 | 8,086 | 97 | 7,989 |
| Germany | 12,000 | 9,000 | 108 | 8,892 |
| Greece | 0 | 0 | 0 | 0 |
| Ireland | 0 | 0 | 0 | 0 |
| Italy | 1,949 | 1,462 | 18 | 1,444 |
| Luxembourg | 123 | 92 | 1 | 91 |
| Netherlands | 3,859 | 2,894 | 35 | 2,860 |
| Norway | 374 | 281 | 3 | 277 |
| Portugal | 1,060 | 795 | 10 | 785 |
| Spain | 1,327 | 995 | 12 | 983 |
| Sweden | 1,400 | 1,050 | 13 | 1,037 |
| UK | 2,590 | 1,943 | 23 | 1,919 |
| Total EU-16 | 39,121 | 29,341 | 352 | 28,989 |

Based on the calculations above the cadmium emission due to this incineration of MSW is approximately 0.35 tonnes Cd/year to water and 28.9 tonnes Cd/year to sludge.

Table 3.1.29: Overall cadmium emissions to water and sludge (in kg/year) in Europe due to incineration of MSW. Scenario 100 % incineration.

| Country | MSW incinerated ((ktonnes wet wt.) | Influent WWTP (kg/year) | Emissions to water (kg/year) Scenario 100 % | Emissions to sludge (kg/year) Scenario 100 % |
| --- | --- | --- | --- | --- |
|  |  |  | 1.2 % | 98.8% |
| Austria | 1,578 | 1,184 | 14 | 1,169 |
| Belgium | 2,842 | 2,132 | 26 | 2,106 |
| Denmark | 2,091 | 1,568 | 19 | 1,549 |
| Finland | 1,690 | 1,268 | 15 | 1,252 |
| France | 34,133 | 25,600 | 307 | 25,293 |
| Germany | 28,000 | 21,000 | 252 | 20,748 |
| Greece | 3,561 | 2,671 | 32 | 2,639 |
| Ireland | 1,432 | 1,074 | 13 | 1,061 |
| Italy | 22,717 | 17,038 | 204 | 16,833 |
| Luxembourg | 185 | 139 | 2 | 137 |
| Netherlands | 4,995 | 3,746 | 45 | 3,701 |
| Norway | 2,217 | 1,663 | 20 | 1,643 |
| Portugal | 3,663 | 2,747 | 33 | 2,714 |
| Spain | 18,804 | 14,103 | 169 | 13,934 |
| Sweden | 2,700 | 2,025 | 24 | 2,001 |
| UK | 29,450 | 22,088 | 265 | 21,822 |
| Total EU-16 | 160,058 | 120,044 | 1,441 | 118,603 |

Based on the calculations above the cadmium emission  to water in a 100 % incineration scenario would result in an emission of approximately 1.4 tonnes Cd/year to water and 118.6 tonnes Cd/year to sludge.

Delayed emissions from incinerator residues

While the emissions with flue gas are immediate, emissions from the residual fractions will be delayed and may result in a diffuse emission of cadmium to the environment. In this study a distinction is only made between bottom ash and fly ash. Other flue gas cleaning products generated in the process of removing acid gases are not specifically addressed.

A number of studies have been carried out concerning the fate and distribution of cadmium in municipal solid waste incineration plants. The distribution of cadmium as a mass balance for incinerators equipped with different FGCs is given. in table 3.1.30.

Table 3.1.30: Partitioning of cadmium (%) in the various  output fractions of a MSW incinerator

| Flue gas (%) | Bottom- and boiler ash (%) | Fly ash (%) | Waste water (%) | Sludge and salt (%) | FGCS | Reference |
| --- | --- | --- | --- | --- | --- | --- |
| 12.1 | 10.8 | 77.1 | / | / | ESP | Zimmerman (1996) |
| 12 | 12 | 76 | / | / | ESP | Brunner and Monch (1986) |
| < 2.5 | 15 | 80 | N.A. | 3 | / | IAGW (1995) |
| 0.1 | 21.5 | 78.5 | < 0.1 | N.A. | ESP/WET/AC | Morf et al (2000) |
| 0.02 | 15 | 72 | < 0.001 | 13 | ESP/WET | VROM (1997) |
| 2.6 | 5.5 | 69.9 | 0 | 21.4 | ESP/WET | Wiaux (1997) |
| 0 | 7 | 89 | 0 | 4 | ESP/WET | Lemann et al. (1995) |

/  = not applicable

N.A: not available

ESP: Electrostatic precipitator

WET:  Wet scrubbing

AC: Active carbon

In general the largest fraction of cadmium can be found in FGCS residues such as fly ash (77-89 %), i.e. the particulate material collected by electrostatic precipitators also called ESP dust. On average 78 % of the cadmium can be found in the fly ash and 12 % in the bottom ash. If only the solid residues are considered this ratio becomes 87 % fly ash and 13 % bottom ash.

Data on amounts of bottom ash and fly ash generated in the different member states (ISWA, 2002) are presented in Table 3.1.31.

Table 3.1.31: Distribution of bottom ash and fly ash for different Member States (reference year 1999) based on ISWA (2002)

| Country | Total waste incinerated (ktonnes wet wt.)a | Bottom ash (ktonnes dry wt.) | Fly ash (ktonnes dry wt.) | Bottom ash (%) | Fly ash (%) |
| --- | --- | --- | --- | --- | --- |
| Austria | 450 | 107 | 8 | 23.9 | 1.8 |
| Belgium | 191 | 25 | 5 | 13.1 | 2.6 |
| Denmark | 2,359 | 473 | 63 | 20.1 | 2.7 |
| France | 10,852 | 1840 | 210 | 17.0 | 1.9 |
| Germany | 12,853 | 3200 | 366 | 24.9 | 2.8 |
| UK | 1,074 | 289 | 31 | 26.9 | 2.9 |
| Netherlands | 2,379 | 590 | 84 | 24.8 | 3.5 |
| Norway | 144 | 25 | 4 | 17.0 | 2.6 |
| Portugal | 322 | 59 | 27 | 18.4 | 8.5 |
| Spain | 996 | 188 | 59 | 18.8 | 5.9 |
| Sweden | 1,968 | 371 | 87 | 18.9 | 4.4 |
| Total | 33,589 | 7,167 | 944 | 21.3 | 2.8 |

a household waste + industrial waste

In general it can be concluded from Table 3.1.31  that on average bottom ash constitutes 21.3 % by weight of the waste input and fly ash 2.8 % by weight of the waste input. Van der Poel (1999) reports similar figures.

These figures were used to calculate the amount of bottom- and fly ash produced by incineration MSW (Table 3.1.32).

Table 3.1.32: Distribution of bottom ash and fly ash for different Member States Scenario current incineration 24.4 %

| Country | MSW incinerated (ktonnes wet wt.) | Bottom ash (ktonnes dry wt.) | Fly ash (ktonnes dry wt.) |
| --- | --- | --- | --- |
| Austria | 479 | 102 | 13 |
| Belgium | 1,369 | 292 | 38 |
| Denmark | 1,730 | 368 | 48 |
| Finland | 80 | 17 | 2 |
| France | 10,781 | 2,296 | 302 |
| Germany | 12,000 | 2,556 | 336 |
| Greece | 0 | 0 | 0 |
| Ireland | 0 | 0 | 0 |
| Italy | 1,949 | 415 | 55 |
| Luxembourg | 123 | 26 | 3 |
| Netherlands | 3,859 | 822 | 108 |
| Norway | 374 | 80 | 10 |
| Portugal | 1,060 | 226 | 30 |
| Spain | 1,327 | 283 | 37 |
| Sweden | 1,400 | 298 | 39 |
| UK | 2,590 | 552 | 73 |
| Total EU-16 | 39,121 | 8,333 | 1,095 |

From Table 3.1.32 it can be concluded that at present 8,333 ktonnes of bottom ash and 1,095 ktonnes of fly ash have to be disposed of on a yearly basis. The cadmium concentrations in the fly ash and bottom ash are calculated based on the cadmium balances for scenario 1 (24.4 % incineration) presented in Figure 3.1.3.  For bottom ash a concentration of 3.8 mg Cd/kg dry wt. can be calculated (31,366 kg Cd/8,333 ktonnes bottom ash). For fly ash a concentration of 192 mg Cd/kg dry wt. is obtained (209,908 kg Cd/1,095 ktonnes).

These figures are in concordance with data reported in the literature. Reported cadmium concentrations in fly ash range from 50 to 1,000 mg/kg dry wt. (EEA, 2000) but can be substantially higher (EPA, 1991). Cadmium concentrations in bottom ash are in general lower. Ranges reported in the Netherlands are 0.1-25 mg/kg dry wt. for bottom ash and 8-337 mg/kgdry wt. for fly ashes (Anthonissen & Meijer, 1993; Verhagen & Meijer, 2000). Typical cadmium concentrations in bottom ash and fly ash as reported by the International Ash Working Group are 0.3-70.5 mg/kg dry wt. for bottom ash and 50-450 mg/kg.dry wt. for fly ash (IAWG, 1997). The calculated concentrations (3.8 mg/kgdry wt. for bottom ash and 192 mg/kg dry wt. for fly ash) are well in the range of these literature values.

Most of the fly ash generated by incinerators in the EC is landfilled with or without prior treatment. For fly ash it is general practice that they are placed in hazardous waste landfills or used for reclamation of old mine shafts or quarries. If treated the most common treatment form in the EC Member States is probably solidification/stabilisation with hydraulic binders (cement or cement-like substances) often supplemented with the mixing of various additives (Argus, 2000). However, in some countries fly ash are (still) re-used. The Netherlands produced in 1999 90 ktonnes of fly-ash from which 41 ktonnes (= 45 %) was re-used with the largest application being as fill material in asphalt (25-30 %) (VVAV, 2000, Anthonissen & Meijer, 1993). Belgium and the UK also indicate a re-use of fly ash (Jacobs et al, 2001; EA 2002). In the framework of the upcoming legislation it is, however, unlikely that the use of fly ashes in asphalt will be a viable option for the future.

The use of processed bottom ash in engineering applications just started in some countries like the UK whereas its use in the Netherlands in civil engineering started since the 1980’s. The ashes are used unbounded as a bulk fill, for example, to construct embankments, as a substitute aggregate or for bound uses through incorporation into road paving (tarmac, asphalt) or construction blocs.

In the UK bottom ash processing in the year 2000 reached 270 ktonnes or 42 % of the bottom ash production for that year (EA 2002). The percentage of bottom ash recycled in other countries such as the Netherlands, Denmark and France is respectively 100 %, 70 % and 50 % (EA, 2002). In Germany ca. 80% of bottom ash is being re-used mainly in road and street construction and 20% of the bottom ash is presently deposited into landfills (personal communication with Bernt Johnke, Umweltbundesamt, Germany, 31.7.2002).

The re-use and/or landfilling of incineration residues may result in a long-term diffuse emission potentially contaminating groundwater, surface water and soil. A field study examining the leaching from two road construction sites showed that substantial leaching of metals from the road construction occurred but, transport through the underlying soil layer was limited due to soil-metal binding processes (Wesselink, 1995). In general two approaches can be used to determine the composition – and thus the potential future emissions -of residual leachates: (1) the generation of simulated leachates, and (2) the study of field-generated leachates. Most often laboratory leachability simulation studies are being used to understand the potential leachability of cadmium in MSW ash. But because a number of such leaching procedures exists, the data generated from these leachate tests have been criticised for the variability in experimental conditions, and for their inability to predict long-term leaching behaviour for all type of disposal options (EPA, 1991). Whether or not the results of these laboratory tests underestimate or overestimate the potential release of contaminants is still under discussion. But most often, the re-use of incineration residues is dependent on the outcome of these leaching tests. If the results of the leaching test are exceeding an imposed limit the bottom- or fly ash is classified as hazardous waste and should be landfilled in a hazardous landfill. For example some countries such as Belgium and the Netherlands provide guidance on acceptable contaminant levels in construction materials in terms of potential impacts on health and the environment. Both the Netherlands and Belgium rely for their conclusion, on whether the material can be used as construction material or not, on the outcome of the column test NEN 7343 (VLAREA, 1998, Aalbers et al, 1996). For non-prefabricated construction materials (unbounded use) maximal allowable cadmium emissions of 0.03 -0.07 mg/kg have been reported. For prefabricated construction materials 1.1 mg/m2 is reported. Furthermore the total cadmium concentration should preferentially below the target value of 10 mg/kg dry wt.. In Germany similar legislation is in place. For cadmium the target value for re-use is 20 mg/kg dry wt. and the cadmium concentration in the eluate should not exceed 5 µg/L (LAGA 1994 cited in Förstner and Hirschmann, 1997).

It can be concluded that at present 8,333 ktonnes of bottom ash and 1,095 ktonnes of fly ash have to be disposed of on a yearly basis. The cadmium concentrations in the bottom ash and fly ash are respectively 3.8 mg Cd/kg dry wt. and 192 mg Cd/kg dry wt.. The re-use and/or landfilling of incineration residues may result in a long-term diffuse emission potentially contaminating groundwater, surface water and soil.

The use of incineration residues is only allowed if the results of leaching tests are favourable. How limit values can be established in relation to the results of leaching tests have also not been addressed. The impact of the expected increase in cadmium content of bottom ash and fly ash (see 3.1.2.2.5.5.2) on the re-usability of these incineration residues has also not been quantified because it is believed that this issue represents a general waste management problem rather than belonging to a substance specific risk assessment. For example most often the classification as hazardous waste or the re-use of incinerator residues is governed by the leachability of other metals as well such as copper, lead or zinc (OVAM, 2001; RIVM/LAE, 1998). The emissions associated with landfilling of incineration products have not been assessed.

Summary of overall cadmium emissions due to incineration of MSW

An overview of the overall cadmium releases to the different compartments due to incineration of MSW containing 10g/Cd tonne dry wt is summarized for the different scenarios in Figures  3.1.4-3.1.5.

An example calculation is given hereunder for the current incineration practice (24.4 %):

- Cd-content MSW = 10 g/tonne dry wt.

- Total volume of waste incinerated = 39,121,000 tonnes wet weight = 27,384,700 tonnes dry wt.

- Cadmium load present in MSW: 10 g/tonne dry wt x 27,384,700 tonnes dry wt = 273.8 tonnes Cd

- Direct cadmium emissions to air  = 3,231 kg (Table 3.1.22) = 3.2 tonnes

- Direct cadmium emissions to water = 352 kg (Table 3.1.25) = 0.4 tonnes

- Cadmium load to hazardous sludge = 28,989 kg (Table 3.1.25) = 28.9 tonnes

- Cadmium flow to incinerator residues = 273.8 tonnes Cd – 3.2 tonnes – 0.4 tonnes – 28.9 tonnes = 241.3 tonnes

- Cadmium load to bottom ash = 241.3 tonnes x 0.13  = 31.4 tonnes

- Cadmium load to fly ash = 241.3 x 0.87 = 209.9  tonnes

Figure 3.1.4: Overall cadmium flow (tonnes) due to incinerating MSW containing 10 g Cd/tonne dry wt-Scenario 24.4 % incineration. (a) most often fly ash is landfilled but some countries (Netherlands, UK, Belgium)  still re-use a part  of their fly ash;  (b) depending on the leaching results bottom ash can either be landfilled or re-used in road construction; (c) the delayed water emissions of re-use in road constructions and hazardous landfills have not been quantified .

Figure 3.1.5: Overall cadmium flow (tonnes) due to incinerating MSW MSW containing 10 g Cd/tonne dry wt -100 % incineration. (a) most often fly ash is landfilled but some countries (Netherlands, UK, Belgium)  still re-use a part  of their fly ash;  (b) depending on the leaching results bottom ash can either be landfilled or re-used in road construction; (c) the delayed water emissions of re-use in road constructions and hazardous landfills have not been quantified (c).

Allocation of current air emissions to a regional/local scale

The allocation of the total EU air emission amount to the regional and the local scale has been performed by dividing the regional emissions with the number of incinerators per country  (Table 3.1.33). Measured data are indicated in bold/italic. For those countries where no measured data were available an emission factor of 0.18 g Cd/tonne MSW wet wt. has been used.

Table 3.1.33: Allocation of air emissions to regional/local scale. Scenario current incineration 24.4 %.

| Country | No. incineration plantsa | Air emissions/country (kg/year) scenario 24.4 % (cfr Table 3.1.22) | Air emissions/ plant (kg/year.plant) |
| --- | --- | --- | --- |
| Austriab | 3 | 86h | 28.6h |
| Belgium | 18 | 63 | 3.5 |
| Denmarkf | 31 | 300 | 9.7 |
| Finlandc | 1 | 14 | 14 |
| France | 117 | 1,922 | 16.4 |
| Germany | 60 | 300 | 5 |
| Italy | 62 | 351 | 5.7 |
| Luxembourgc | 1 | 22 | 22 |
| Netherlands | 11 | 53 | 4.8 |
| Norwayd | 8 | 41 | 5.1 |
| Portugal | 2 | 3.2 | 1.6 |
| Spain | 8 | 54 | 6.8 |
| Swedene | 22 | 5 | 0.2 |
| UKg | 11 | 17 | 1.5 |
| Total | 355 | 3,231 |  |
| Average | 25 plants/ country (=355/14) | 231 kg/year/country (= 3,231/14) 10 % rule = 323 | 9.1 kg/year/plant = (3,231/355) |

a Based on ISWA 2002

b Schuster, 1999,

c Juniper 1997

d SFT, 2002

e RVF, 2002

f Waste Statistics 1999, Danish EPA (2001)

g Environment Agency 2002

h actual measured data have come available recently (Stubenvoll et al., 2002). These values indicate a cadmium emission of 4.2 kg/y or, on average, 1.4 kg/year plant

Since emissions incineration plants are not (yet) considered in the TGD emission tables, the following approach is proposed to allocate incineration plant emissions to the regional/local scale. On the basis of country specific information -for 14 EU countries - a country average number of incineration plants of 25 can be calculated. In these 25 plants a hypothetical amount of 2,794 ktonnes of MSW (cfr. Table 3.1.25: 39,121/14) can be incinerated, thereby emitting a Cd amount to air of 231 kg/year (scenario 24.4 %). Comparing these data to the emitted Cd amounts for individual countries, it seems that 9 out of 14 countries are covered -except for Denmark, France, Italy and Germany. Measured/estimated data in Belgium are between 1-12 kg/plant. For the UK typically concentration between 0.5 and 5 kg/plant are reported.  Although France is accounting for 59 % of the total EU air emission it is proposed to use the 10 % rule to derive a reasonable worst case emission estimate of the regional emission since incineration activities (large number of site) are reasonably spread over the EU territory. Applying the TGD 10% rule to the total EU air emission amount gives a regional air emission amount of 323 kg/y which is comparable with the calculated 231 kg/y per region. On the basis of country specific information for incineration plants (air emission and number of incineration plants), an EU weighted average emitted Cd amount per plant of 9.1 kg/year can be calculated. In comparison with the average emission per plant in each country it seems that Luxembourg, France, Denmark and Finland are the countries not completely covered. Individual measured data were available for France. The 90th percentile of these measurements is 36.7 kg/year/plant. Measured data in Austira (Stubenvoll et al (2002) indicate an emission of 1.4 kg/year. This value has been used for the local PEC calculations for Austrian incinerators.

The country specific local air emission estimates ranging between 0.2-16.4 kg/year/plant have been used in the local PEC calculations (section 3.1.3.2.3). These values have been taken forward in the risk characterisation together with the generic scenario based on the 10 % rule and average emission of 9.1 kg Cd/year.plant.Since France contributes for 59 % of the total emission to air and individual measured data were available an additional scenario for France based on these measured data was also taken forward into the risk characterisation (i.e. 36.7 kg)

In the 100% incineration scenario the allocation from the EU scale to the regional scale is performed applying the 10% rule to the EU emission amount. A regional emission amount of 1,402 kg/year is calculated. Comparing this value to the country specific emission amounts shows that 14 out of 16 countries are covered. Larger air emissions have been obtained for France and Italy. In the 100% incineration scenario it is assumed that the number of incineration plants is proportionally increased to the amount of MSW to incinerate. Hence, on a local scale the exposure scenario will be similar to that from the 24.4 % incineration scenario.

Measured cadmium loads to the surface water was lacking for most incinerators. Therefore the calculated water emissions (Table 3.1.28) based on a generic median effluent concentration of 0.004 mg/L. have been used to calculate the EU emissions to surface water using the 10% rule in analogy to the air emission estimate. For the local scenario (PEC calculation and risk characterisation) the 90th percentile Cd effluent concentration (0.005 mg/L = (1.2 x 0.42)/100) has been used.

A summary of all continental and regional emissions to air and surface water is given in Table

3.1.34.

Table 3.1.34: Total annual amount of Cd emissions to air and water within the EU from incineration plants.

| Scenario | Released amount Cadmium (kg/y) | Continental (90 %) (kg/y) | Regional (10 %) (kg/y) |
| --- | --- | --- | --- |
|  | AIR |
| 24.4 % incineration | 3,231 | 2,908 | 323 |
| 100 % incineration | 14,018 | 12,616 | 1,402 |
|  | WATER |
| 24.4 % incineration | 352 | 317 | 35 |
| 100 % incineration | 1,441 | 1,297 | 144 |
|  | LANDFILL |
| 24.4 % incineration | 240,465 | 216,419 | 24,047 |
| 100 % incineration | 1,104,947 | 994,452 | 110,495 |

Contribution of Ni-Cd  batteries to the overall cadmium emissions

With the assumption that Ni-Cd batteries account for 10-50 % of the total MSW cadmium content, the contribution of Ni-Cd batteries can be calculated by multiplying the overall cadmium emissions as presented in Figures 3.1.3 to 3.1.6 by respectively 0.1 and 0.5 (Tables 3.1.35 and 3.1.36).

Table 3.1.35:	Contribution of Ni-Cd batteries to the overall cadmium emissions due to incineration- Scenario 10 mg/kg dry wt. total cadmium in MSW

| Scenario | 24.4 % incineration | 100 % incineration |
| --- | --- | --- |
| Allocation key | 10% | 50% | 10% | 50% |
| Compartment | Direct emissions (kg/year) |
| Air | 323 | 1,617 | 1,402 | 7,009 |
| Water | 35 | 176 | 144 | 721 |
| Compartment | (kg) |
| Cadmium going to landfill | 24,047 | 120,233 | 110,495 | 552,473 |

Table 3.1.36: Contribution of Ni-Cd batteries to the continental and regional cadmium emissions due to incineration. Scenario 10 mg/kg dry wt. total cadmium in MSW

| Scenario |  | Released amount Cadmium (kg/y) | Continental (90 %) (kg/y) | Regional (10 %) (kg/y) |
| --- | --- | --- | --- | --- |
|  |  | AIR |
| 24.4 % incineration | 0.1 | 323 | 291 | 32 |
|  | 0.5 | 1,617 | 1,455 | 162 |
| 100 % incineration | 0.1 | 1,402 | 1,262 | 140 |
|  | 0.5 | 7,009 | 6,308 | 701 |
|  |  | WATER |
| 24.4 % incineration | 0.1 | 35 | 31.5 | 4 |
|  | 0.5 | 176 | 158 | 18 |
| 100 % incineration | 0.1 | 144 | 130 | 14 |
|  | 0.5 | 721 | 649 | 72 |
|  |  | LANDFILL |
| 24.4 % incineration | 0.1 | 24,047 | 21,642 | 2,405 |
|  | 0.5 | 149,113 | 134,202 | 14,911 |
| 100 % incineration | 0.1 | 110,495 | 99,456 | 11,050 |
|  | 0.5 | 552,473 | 497,226 | 55,247 |

Future emissions

The future total cadmium concentration in MSW is expected to range between 13.2 and 24 g/ton dry wt  (cfr Table 3.1.20) with an estimated specific contribution of Ni-Cd batteries of respectively 4.2 g/ton dry wt. (= 4.2/13.2 =32 %) and 15 g/ton DW (= 15/24 = 63 %).

As a worst case exercise the future emissions due to the expected increase of cadmium in the MSW for a 100 % incineration scenario are presented.

Future cadmium emissions to air

There is no evidence for increased cadmium air emission due to an increase in cadmium load in the MSW unless the gas cleaning system fails (van der Poel, 1999). Therefore these emissions can be dealt with irrespective of the cadmium concentration in the MSW (an increase in cadmium concentration will of course be translated into higher cadmium concentrations in the solid residues). Higher overall cadmium air emissions are expected to occur related to an increase in the incineration practice and the higher amount of MSW that is likely to be generated in the future (EEA, 2000). However, the latter has not been taken into account. It is assumed that each year the same amount of MSW is being incinerated (i.e. 160,058 ktonnes wet wt.) resulting in an overall emission of 14 tonnes Cd/year (cfr Table 3.1.26).

Future cadmium emissions from wastewater

Due to an increased cadmium load it can be expected that the washing water from the scrubber system will contain a higher cadmium concentration. If a linear relationship between the effluent concentration and the cadmium content in the MSW is assumed the cadmium concentration in the untreated effluent can then be adjusted for an altered waste composition, based on the ratio of the cadmium concentration in the influent for the current reference situation (10 g/tonne dry wt. cadmium). The equation hereunder demonstrates how future changes in cadmium wastewater concentration (before treatment) due to changing cadmium content of the MSW can be calculated with the assumption of a linear relationship (Table 3.1.37).

=  x

CdConc Future, Wastewater = future cadmium concentration in the wastewater (mg/L)

CdConc Present, wastewater  = present cadmium concentration in the wastewater (mg/L) = 0.3 mg/L (Table 3.1.24)

CdConc Future, MSW = future cadmium concentration in MSW (g)

CdConc Present, MSW = present cadmium concentration in MSW (g) = 10 g/tonne

Table 3.1.37: Future cadmium content of wastewater produced by the incineration process (influent of on-site treatment plant)

| Collection (%) | Total future Cd content in MSW (g/ton) | Cd concentration in wastewatera (mg/L) |
| --- | --- | --- |
| 10 | 24 | 0.72 |
| 75 | 13.2 | 0.4 |

a before treatment

After treatment 98.8 % of the cadmium will be removed resulting in effluent concentrations of  0.005-0.009 mg/L.. These effluent concentrations have been used for the regional scenario. For the local scenarios future effluent concentrations have been calculated based on the current 90th percentile influent concentration of 0.47 mg/L resulting in future influent concentrations of 0.62 and 1.13 mg/L (i.e. 0.007- 0.0135 mg/L effluent concentration).

Future cadmium content of residues

The increase of the cadmium content in the MSW will be translated into an increase in the cadmium concentration of the incineration residues such as bottom ash and fly ash. In Table 3.1.38 the expected bottom ash and fly ash concentrations have been calculated based on the assumption that bottom ash constitutes 21.3 % by weight of the waste input and fly ash 2.8 % by weight of the waste input and the Figures 3.1.6-3.1.7.

Table 3.1.38: Future cadmium content (mg/kg dry wt.) of bottom ash and fly ash: current and future scenarios

| Total Cd content in MSW (g/tonne) | Scenario | Cd content in bottom ash (mg/kg dry wt.) | Cd content in fly ash (mg/kg dry wt.) |
| --- | --- | --- | --- |
| 10 | 24.4 % incineration | 3.8 | 192 |
| 13.2 | 100 % incineration | 5.0 | 253 |
| 24 | 100 % incineration | 9.1 | 463 |

N.B. Shaded cells represent the current scenario

From these results it can be concluded that the future cadmium content in fly ash and bottom ash is likely to double in the future under the 10 % collection scenario (total Cd content in MSW: 24 g/tonne). In case the collection efficiency is 75 % (total Cd content in MSW: 13.2 g/tonne) the cadmium content is expected to increase with 25 %.

An overview of the future overall cadmium releases for a 100 % incineration scenario to the different compartments due to incineration of MSW is summarised for the different scenarios in Figures 3.1.6-3.1.7.

Figure 3.1.6: Overall cadmium flow (tonnes) due to incinerating MSW MSW containing 13.2 g Cd/tonne dry wt -100 % incineration with a 10 % collection scenario. (a) most often fly ash is landfilled but some countries (Netherlands, UK, Belgium)  still re-use a part  of their fly ash;  (b) depending on the leaching results bottom ash can either be landfilled or re-used in road construction; (c) the delayed water emissions of re-use in road constructions and hazardous landfills have not been quantified (c).

Figure 3.1.7: Overall cadmium flow (tonnes) due to incinerating MSW MSW containing 24 g Cd/tonne dry wt -100 % incineration with a 75 % collection scenario. (a) most often fly ash is landfilled but some countries (Netherlands, UK, Belgium)  still re-use a part  of their fly ash;  (b) depending on the leaching results bottom ash can either be landfilled or re-used in road construction; (c) the delayed water emissions of re-use in road constructions and hazardous landfills have not been quantified (c).

Allocation of future EU air and water emissions to the continental and regional scale

For the 100% incineration scenario the allocation from the EU scale to the regional scale is performed applying the 10% rule to the EU emission amount. A regional emission amount of 4,199 kg/year is calculated. Analogous to the air emission estimation, the EU emissions to surface water are allocated to the region using the 10% rule.

Table 3.1.39: Total annual amount of overall Cd emissions to air and surface water within the EU from incineration plants- Future scenario’s

| Scenario | Cd content MSW (g/ton) | Released amount Cadmium (kg/y) | Continental (90 %) (kg/y) | Regional (10 %) (kg/y) |
| --- | --- | --- | --- | --- |
|  |  | AIR |
| 100 % inc. 75% coll. | 13.2 | 14,018 | 12,616 | 1,402 |
| 100 % inc. 10% coll. | 24 | 14,018 | 12,616 | 1,402 |
|  |  | SURFACE WATER |
| 100 % inc. 75% coll. | 13.2 | 1,921 | 1,729 | 192 |
| 100 % inc. 10% coll. | 24 | 3,457 | 3,111 | 346 |
|  |  | LANDFILL |
| 100 % inc. 75% coll. | 13.2 | 1,462,997 | 1,316,697 | 146,300 |
| 100 % inc. 10% coll. | 24 | 2,671,499 | 2,404,349 | 240,435 |

The specific  contribution of Ni-Cd batteries for all waste streams of MSW incineration is given in Table 3.1.40 and Table 3.1.41.

Table 3.1.40: Future contribution of Ni-Cd batteries to the overall cadmium emissions due to incineration

| Scenario | 100 % inc (75 % collection, 13.2 g cadmium/tonne MSW dry wt) | 100 % inc.(10 % collection, 24 g Cd/tonne MSW dry wt.) |
| --- | --- | --- |
| Allocation key (%) | 32 | 63 |
| Compartment | Direct emissions (kg/year) |
| Air | 4,486 | 8,831 |
| Water | 615 | 2,178 |
| Compartment | (kg) |
| Cadmium going to landfill | 468,159 | 1,683,044 |

Table 3.1.41: Contribution of Ni-Cd batteries to the continental and regional cadmium emissions due to incineration

| Scenario | Allocation key (%) | Released amount Cadmium (kg/y) | Continental (90 %) (kg/y) | Regional (10 %) (kg/y) |
| --- | --- | --- | --- | --- |
|  |  | AIR |
| 100 % inc. 75% coll. | 32 | 4,486 | 4,037 | 449 |
| 100 % inc. 10% coll. | 63 | 8,831 | 7,948 | 883 |
|  |  | SURFACE WATER |
| 100 % inc. 75% coll. | 32 | 615 | 554 | 62 |
| 100 % inc. 10% coll. | 63 | 2,178 | 1,960 | 218 |
|  |  | LANDFILL |
| 100 % inc. 75% coll. | 32 | 468,159 | 421,343 | 46,816 |
| 100 % inc. 10% coll. | 63 | 1,683,044 | 1,514,734 | 168,304 |

###### Overall cadmium emissions from landfilling MSW

Release of pollutants from a landfill can occur over an indefinite period. Hence, the daily or annual release may result in a very small PEC and does not reflect the long-term emissions of a landfill. For the moment no specific guidance is provided by the TGD on how to quantify the current and future landfill emissions. Due to the large uncertainties associated with this subject, the analysis that is performed in this report should merely be considered as a semi-quantitative approach.

Both regional and local emissions of landfilling have been addressed. Only for the local scenario the issue of dilution in time (long term emissions) has been analysed. The local emissions associated with landfilling MSW are given in this report for three separate time horizons beginning from waste placement:

- Short term time frame (20 years) corresponding roughly to the landfill’s period of active decomposition.

- Intermediate term time frame (100 years) corresponding roughly to the life span of a given generation.

- Long term time frame (500 years) corresponding to an indefinite time reference where emissions of any given environmental flow have reached or nearly reached their theoretical yield.

Leachate generation

Emissions of landfills can occur primarily by generation of landfill gasses and leaching of contaminants. In the case of metals, emissions by generation of landfill gas are negligible in all cases except for Hg and possibly Cd (Baccini et al, 1987, Finnveden, 1996). However, in this document the pollution via leachate release is being considered as the most important long term flux impacting the environment since production of landfill gas lasts about one to two decades.

Leachate is generated as a result of the expulsion of liquid from the waste due to its own weight or compaction loading (termed primary leachate) and the percolation of water through a landfill (termed secondary leachate). The source of percolating water could be precipitation, irrigation, groundwater or leachate recirculated through the landfill.

Leachate quality

Current situation

In general, metals (specifically chromium, nickel, copper, zinc, cadmium, lead and mercury) are currently not present in high amounts in leachates from municipal landfills. Typical contaminant concentrations (µg/L) found in the interstitial water (leachate) of municipal solid waste landfills as collected by Assmuth (1992) are given in Table 3.1.42.

Table 3.1.42 Typical contaminant concentrations (µg/L) of municipal solid waste leachates

| Substance | Mean | Maximum |
| --- | --- | --- |
| Cd | < 0.5-3.4 | 5 |
| Cr | 4.9-14 | 39 |
| Cu | 1.5-30 | 90 |
| Pb | 4.9-19 | 800 |
| Zn | 23-60 | 90 |
| Toluene | < 0.1-200 | 200 |
| Dichlormethane | 1.1-55 | 84 |
| PCB compounds | < 0.05-0.71 | 0.71 |
| Pentahlorophenol | 0.05-5.3 | 13 |

An overview of reported cadmium concentrations in MSW leachates is given in Table 3.1.43.

Table 3.1.43 Overview of total cadmium concentrations (µg/L) in leachates of MSW landfills

| N° of landfills | Type/origin | Min | Max | Mean | Percentiles | Reference |
| --- | --- | --- | --- | --- | --- | --- |
| 180 71 | Germany: mainly old landfills with unknow solid content closed 15-20 years ago Switzerland: closed within 10 years are still in use France, Italy and Japan |  | 1,330/173/136 100 µg/L (1 site) |  | P90 < 5 P80 < 5 P75 < 3 | Eggenberger& Waber (2000) |
| 13 | Finland: MSW and industrial landfills |  | 5 | 0.5-3.4 |  | Assmuth (1992) |
| 21 | UK: landfills with primarily domestic waste inputs | < 10 | 20 | < 10 |  | Robinson (1995) |
| Not reported | Sweden: active municipal landfills | < 0.5 | 2,700 |  | P50 = 5 | Seman (1986) cited in Flyhammer (1995) |
| Not reported | Sweden: active municipal landfills | < 3 | 14 |  | P50 < 3 | Björklund (1989) cited in Flyhammer (1995) |
| Not reported | MSW and co-disposal landfills: France Germany Netherlands UK |  | up to 30 with co-disposal | < 10 6 4 < 10 |  | Hjelmar et al. (1994) |
| Not reported | MSW landfills | 0.5 0.7 | 1,400 525 | 6 37.5 |  | Ehrig (1990) cited in Dahm et al (1994) Kruse et al. (1993) cited in Dahm et al (1994) |
| 1 | Sweden: 95 % MSW, 5 % sewage sludge 1 years 2 years 20-22 years |  |  | 40 15 6 |  | Flyhammar et al (1998) |
| 71 | Landfills (USA/France) with more than 75 % MSW. Recent sites (< 1 year) and older sites more than 20 years. |  |  |  | P50: 2.5-7 | EREF (1999) |
| 51 landfill total 10 landf/30 measurement points 16/55 19/110 6/21 | Germany 1-5 years 6-10 years 11-20 years 21-30 years | 0.2 0.2 0.1 0.2 | 50 192 70 18 | 11 5.8 3.9 2.8 |  | Krümpelbeck (1999) |

The data compiled by Eggenberger and Waber (2000) from 71 investigated landfills in Switzerland, Italy, Japan and France indicate that about 80 % of the leachates have Cd concentrations below 5 µg/L and 75 % below 3 µg/L. A similar distribution of Cd-concentrations in landfill leachates and contaminated ground water is obtained for old landfills (closed 15-25 years ago) in Germany. The results of 1,422 analyses from leachates of mainly old landfills (180) in Germany and more recent landfills (closed 10 years or still in use) in Switzerland and some data from France, Italy and Japan, revealed that roughly 90 % of the investigated leachates Cd-concentrations is  below 5 µg/L. It has to be mentioned that the Cd background concentrations as measured in uncontaminated shallow groundwater are very low, being generally below 1 µg/L. Flyhammer (1995) reported different cadmium concentrations in leachates from landfills in different countries and suggested to use 5 µg Cd/L as an average concentration in leachate from landfills (active and closed landfills) in Nordic countries. Similar values were reported in the Netherlands, Finland, US and France (see Table 3.1.40). Overall there seems to be a decreasing trend of the cadmium concentration in the leachate with the age of the landfill (Krümpelbeck, 1999, Flyhammar et al, 1998).

The measured concentration value represents the cadmium leached out from all cadmium sources present in the MSW. Since data on leachability of cadmium in MSW compounds is limited it is very difficult to assess the contribution of the Ni-Cd batteries to this value. Only a few leaching tests have been conducted with Ni-Cd batteries. These tests conducted under both aerobic and anaerobic conditions at a temperature of 50 °C for 100 days showed corrosion around the positive terminal. Analysis of the leachate revealed total concentrations less than 0.01 mg/L. Field studies where Ni-Cd batteries were deposited in a municipal landfill for seven months showed similar signs of corrosion at the positive terminal but less than had been produced in the anaerobic leachate test (Bromley et al, 1983). Similar observations were obtained in another study on the degradation of Ni-Cd batteries under domestic waste landfill conditions (Jones et al, 1977). Long-term burial tests (not under landfill simulating conditions) with Ni-Cd batteries have shown that after 13 years no exposure of the battery interior components had yet occurred. Only the exterior of the battery did show signs of corrosion (Oda, 1993). From the studies indicated above it is not possible to draw a general conclusion on when the interior of a Ni-Cd battery will be exposed. According to Bromley et al (1983) this is not expected to occur between 1 and 5 years after deposition. Data on the leaching after exposure of the interior have not been found.

In this report the current overall cadmium concentration, most representative for the average situation, in an MSW landfill leachate is considered to be 5 µg/L and this value was used to perform the regional calculation. In the risk characterisation next to a local scenario with a leachate concentration of 5 µg/L an additional scenario have been developed based on an assumed cadmium leachate concentration of 50 µg/L (see future changes in leachate quality).

Furthermore it is assumed in this report that each waste component has the same likelihood of leaching out one gram of cadmium (e.g. one gram of cadmium in a certain amount of paper was assumed to have the same likelihood of leaching out as one gram of cadmium in Ni-Cd batteries).

As a result the emissions due to Ni-Cd batteries can be estimated to be 0.5-2.5 µg/L (based on the finding that 10-50 % of the overall cadmium content in MSW is due to Ni-Cd batteries).

Future changes in leachate quality

The impact of increasing cadmium content in the MSW on the composition of the leachate cannot be predicted on the basis of current knowledge since there is no direct relationship between the total content of Cd and the leachability of Cd. A 10 % increase in total content of Cd in the MSW landfilled will not necessarily lead to a 10 % increase in the leached amount of Cd. The leachability will depend on the chemical nature of the cadmium and the leaching conditions.

In this report the cadmium concentration in the leachate originating from a fixed amount of cadmium being landfilled is assumed to be constant over time. The question arises whether or not it is reasonable to assume one constant leachate concentration since the conditions in landfills are changing during the different degradation phases in a landfill. For metals the critical phase in the short term of a landfill is the acid anaerobic phase where the pH will drop due to the decomposition of the easily degradable material. Few studies have attempted to characterise leachates as being acetogenic or methanogenic (Ehrig, 1983 and Robinson and Gronnow, 1993 in Finnveden 1996). From these studies it can be concluded that the constant concentration assumption for the surveyable time period is reasonable for the metal cadmium. However, it is acknowledged that landfills have not yet reached their final development stage and as a result it is unclear what may happen after 100 year. Considering the geochemical evolution of waste deposits towards more oxidising and more acidic conditions with time, at first  higher emissions could be expected in the future (Eggenberger & Waber, 2000). However, according to simulation work by Belevi and Baccini (1989), it is more plausible that alkaline conditions will be maintained for 2000 years and that hence higher remobilization rate of some metals due to lower pH is not expected at least for many centuries (Bozkurt et al., 2000). The effect of varying redox potentials and the effect of acid rain on the chemical equilibrium of a waste body was investigated by Gade et al. (1998). The results showed that severe mobilisation is not expected and a long term entrance of acid rain is not expected to exhaust the carbonate buffer before 400,000 years. And even if the carbonate buffer would be exhausted there will be still another buffer (silicates) effective.

Overall the cadmium concentration in the leachate seems to decrease with the age of the landfill (Krümpelbeck, 1999, Flyhammar et al, 1998). According to Gade et al (1997, 1998, 1999, 2000), who investigated the behaviour of two Bavarian hazardous waste landfills with regard to their mineralogy, secondarily newly formed minerals (carbonates, phosphates, sulfates) reduced the mobility of the metals present in the waste. Under anaerobic conditions metals that form sulfides (e.g. cadmium, copper, zinc, nickel and lead) will tend to be immobilized as sulfides. In the long run when landfills develop aerobic conditions additional solubility limiting phases including carbonates and hydroxides will retard metal mobility in the future.

Johnson et al (1999) suggested that CdCO3 (otavite) precipitation is important for cadmium. Recent modelling work (Ross et al, 2000) on the retention and speciation of heavy metals (cadmium, chromium and zinc) in both immature and mature post methanogenic leachates indeed indicated that carbonate precipitation is likely the solubility limiting phase for cadmium.  According to the performed geochemical modelling on mature waste, carbonate precipitation is likely to prevent cadmium concentrations rising above 60 to 90 µg/l. The laboratory results indicated, however, that for the aerobic columns, cadmium concentrations generally remained below 10 µg/L suggesting that the retention mechanism is probably not precipitation alone. Similar observations were observed  by Gade et al (1999) who predict a maximum cadmium concentration of 81 µg/l but observed a measured concentration of one order of magnitude lower i.e. 7.8 µg/L.suggesting that other mechanisms such as adsorption phenomena are also limiting cadmium release.

In order to assess possible impact on the environment from possible higher cadmium concentrations in the future the risks will be quantified in the sensitivity analysis (section 3.1.2.2.5.7) for an arbitrary chosen leachate concentration (i.e. 50 µg/L which is close to the solubility limit for cadmium carbonate). The leachate concentration of 50 µg/L can be considered as a conservative/worst case leachate concentration because in this case we are assuming that aerobic precipitation is the only metal retention mechanisms.

Leachate quantity

Leachate production is highly depended on the landfill design and local climatic conditions. Precipitation represents the largest single contribution to the production of leachate. There is some variation in the potential generation of leachate within the EU because precipitation and evapotranspiration depends on geographical location. In Mediterranean areas (Greece, Spain, Italy) leachate generation is the smallest during summer season and leachate generation occurs principally during the colder, wet season (i.e. from October to April). For example an annual leachate production, expressed as height of water of 40-80 mm/year has been calculated for a landfill site  near Athens  (Greece, rainfall:  387 mm/y, Kouzeli-Katsiri et al, 1993). In a landfill site near Madrid  (Gössele, 1993) the leachate production was calculated to be 7 mm/year and in a landfill near Pavia (Italy, Baldi et al, 1993) it was 82 mm/year. Leachate quantities tend to be higher in the North of the EU than the South.  In Sweden an average leachate volume of 250-300 mm/year is reported during operation (Nilsson, 1993). In Denmark similar figures have been reported:  320-400 mm during operation and 56-89 mm/year (Hjelmar, 1988-1989). But equally large variations can be found from East to West and over relatively short distances within Member States (Hjelmar et al, 1994). Reported leachate volumes vary from 25 m3 to 3,000 m3 per hectare (Flyhammer, 1995, Qiang et al, 2002).

The results of various empirical studies are indicating that the average percentage of precipitation that result in leachate production depends on the age of the landfill and is largely controlled by the presence and type of cover.  In general it has been noted that the amount of leachate produced is between 15 and 50 % of the respective rainfall, depending mainly on the final landfill cover type and the manner of waste compaction (Canziani and Cossu, 1989). As a average to realistic worst case scenario in this report the water balances has been calculated for a relatively high precipitation rate (800 mm/year) for different scenarios representative for common nowadays (or modern) landfill practices.

Scenario development

The EU directive on the landfill of waste (1999/31/EC) indicates that appropriate measures shall be taken, with respect to the characteristics of the landfill and the meteorological condition in order to:

- control water from precipitation to enter the landfill

- to collect contaminated water and leachate

- and to treat contaminated water and leachate collected from the landfill to the appropriate standard required for their discharge.

It is further stated that protection of groundwater has to be achieved by the combination of a geological barrier and a bottom liner during the operational/active phase and by the combination of a geological barrier and a top liner during the passive post closure phase. For non hazardous landfills it is therefore required to have a leachate collection and bottom sealing (consisting of an artificial sealing liner and drainage liner > 0.5 m in addition to a geological barrier (> 0.5 m). If the prevention of leachate formation is necessary a surface sealing can be applied. The requirements for a top cover are at least a topsoil cover (> 1m) and a drainage layer (> 0.5m).

Although in the future all landfills will have to meet the requirements of the new EU landfill directive it is acknowledged that at the moment different landfill practices exist. Therefore the leachate generation simulations have been conducted in this report for 4 different sets of conditions representative for different landfill practices and the consecutive life stages of a landfill.

Set 1: corresponds with a landfill with no top cover

Set 2: corresponds with a landfill with daily top cover

Set 3: corresponds with a landfill with an intermediate top cover

Set 4: corresponds with a landfill with a final top cover

In addition two sub-scenarios have been added in which the composition of the bottom liner or top liner has been changed:

- In this report both a single compacted clay liner as a single composite liner system are considered as a bottom liner. Proper functioning of a bottom liner system is critical to the containment effectiveness of a landfill. During the past few decades the trend has been to use composite liner systems comprising both clay and synthetic geomembranes together with interspersed drainage layers.

- For a final cap or cover system the following systems are considered in this report: 1) a cover system consisting of a top soil, drainage layer and a single compacted clay liner, 2) a cover system consisting of a top soil, drainage layer and a single composite clay line. The main purpose of a landfill final cover is to minimise water infiltration into the landfill to reduce the amount of leachate generated after closure.

An overview of the different landfill profiles considered in this report is given in Figure 3.1.8. The thickness of the layers and final cover materials are in agreement with the new landfill directive and are representative for common landfill practice.

|  | Set 1: No cover | Set 2: Daily cover | Set 3: Intermediate cover | Set 4: Final cover |
| --- | --- | --- | --- | --- |
| Top cover |  |  |  |  |  |
| Waste |  |  |  |  |
| Bottom |  |  |  |  |  |  |  |  |

Figure 3.1.8  Landfill profile structure for different landfill designs

Water balance

The most common way to calculate the amount of leachate is a simple water balance. In a water balance the amount of leachate is calculated as being the amount of precipitation minus the surface run-off, evapotranspiration, change in soil cover and waste moisture content.

L = P – R/O – ET –(ST –(SWST

L = Leachate quantity

P = Precipitation

R/O = run off

(ST = change in soil moisture content

ET = Evapotranspiration

(SWST = change in solid waste moisture content

In this report the leachate production has been addressed with the theoretical landfill leachate model HELP (Hydrologic Evaluation of Landfill Production, US-EPA, Schroeder et al., 1994a and b). The HELP model is a sophisticated version of the water balance method and is used all over the world to predict leachate generation. The configuration of the model allows handling any type of cover, liner and can even address leakage.

In order to perform the model calculations a generic landfill has been defined. At the moment an average representative European standard landfill is hard to define. Since future landfills are assumed to be reasonably large a landfill of 20 hectares have been chosen for the generic reasonable worst case (large surface area hence more leachate production) local scenario. An overview of the main input data used in the modelling is given in Table 3.1.44. Default values chosen were based on values most commonly cited in literature (Kjeldsen & Christensen, 2001; Nielsen and Hausschild, 1998; Nielsen et al, 1998; EREF, 1999; Schroeder et al, 1994; Hjelmar et al, 1994; etc.).

Table 3.1.44 Default values used for the generic landfill

| Parameter | Unit | Value |
| --- | --- | --- |
| Surface of the landfill | m2 | 200,000 |
| Total depth of MSW landfilled | m | 10-20 |
| Bulk density of MSW |  | 0.6 |
| Volumetric water content in MSW |  | 0.3 |
| Field capacity MSW | % | 29.2 |
| Wilting point MSW | % | 7.7 |
| Duration of operation phase | Year | 15 |
| Duration of post closure phase | Year | 30 |
| Moderately compacted clay cover | m | 1 |
| Drainage layer (sand) | m | 0.5 |
| Slope drainage layer | % | 1 |
| Top cover (sandy loam) | m | 0.3 (daily cover) 1.5 (final cover) |
| Slope top cover | % | 1a |
| HDPE liner | m | 0.01 |
| Precipitation | m/year | 0.8 (i.e. 0.799)b |

a the choice was made to represent a reasonable worst case situation (OVAM, pers. com., 2002)

b calculated default value

The HELP model was run for the 4 different sets of data and for one landfill location. As location for the landfill the Netherlands was chosen. The HELP model generated the weather and climatic data over a simulation period of 100 years. This resulted in an average annual precipitation of 0.799 m/year for the Netherlands and is used as a default average to realistic worst case scenario with regard to the amount of leachate generated for the different landfill scenarios. Mediterranean countries will have lower leachate volumes. Scandinavian countries will have similar leachate volumes as in the Netherlands.

During the operation phase the landfill cells are relatively flat. Therefore the area subjected to runoff was set to zero. Runoff was only taken into account when the final top cover was in place. In the cases where runoff is ignored any precipitation will result in more leachate resulting in a maximum leachate generation during landfill operations.

Tables 3.1.45-48 show the average annual results of the HELP model for a generic landfill taking into account the different landfill stages.

Table 3.1.45:  Annual leachate generation for a landfill with no top cover and a bottom liner consisting of a single compacted clay liner or a single composite liner

|  | Scenario 1 : No top cover |
| --- | --- |
|  | Bottom liner: single compacted clay | Bottom liner: composite liner |
| Parameter | m3/ha.y | % | m3/ha.y | % |
| Precipitation | 7,999 | 100 | 7,999 | 100 |
| Run-off | 0 | 0 | 0 | 0 |
| Evapotranspiration | 5,645 | 70.6 | 5,645 | 70.6 |
| Change in water storage | - 3.9 | 0.05 | 262 | 3.3 |
| Leachate collected from drainage layer | 119 | 1,5 | 2,024 | 25 |
| Fugitive leachate | 2,239 | 28 | 68 | 0.8 |

Table 3.1.46:  Annual leachate generation for a landfill with a daily cover and a bottom liner consisting of a single compacted clay liner or a single composite liner

|  | Scenario 2: Daily cover |
| --- | --- |
|  | Bottom liner: single compacted clay | Bottom liner: composite liner |
| Parameter | m3/ha.y | % | m3/ha.y | % |
| Precipitation | 7,999 | 100 | 7,999 | 100 |
| Run-off | 0 | 0 | 0 | 0 |
| Evapotranspiration | 5,454 | 68.2 | 5,454 | 68.2 |
| Change in water storage | - 3 | 0.03 | 300 | 3.5 |
| Leachate collected from drainage layer | 143 | 1.8 | 2,193 | 27.4 |
| Fugitive leachate | 2,406 | 30.1 | 73 | 0.9 |

Table 3.1.47:  Annual leachate generation for a landfill with an intermediate cover and a bottom liner consisting of a single compacted clay liner or a single composite liner

|  | Scenario 3: Intermediate cover |
| --- | --- |
|  | Bottom liner: single compacted clay | Bottom liner: composite liner |
| Parameter | m3/ha.y | % | m3/ha.y | % |
| Precipitation | 7,999 | 100 | 7,999 | 100 |
| Run-off | 0 | 0 | 0 | 0 |
| Evapotranspiration | 5,454 | 68.2 | 5,454 | 68.2 |
| Change in water storage | 2 | 0.03 | 284 | 3.5 |
| Leachate collected from drainage layer | 136 | 1.7 | 2,189 | 27.4 |
| Fugitive leachate | 2,412 | 30.1 | 73 | 0.9 |

Table 3.1.48:  Annual leachate generation for a landfill with a final cover (with or without a composite liner) and a bottom liner consisting of a single compacted clay liner or a single composite liner.

|  | Scenario 4: Final cover |
| --- | --- |
|  | Final top cover: top soil , sand, composite liner |
|  | Bottom liner: single compacted clay | Bottom liner: composite liner |
| Parameter | m3/ha.y | % | m3/ha.y | % |
| Precipitation | 7,999 | 100 | 7,999 | 100 |
| Run-off | 1,850 | 23.1 | 1,850 | 23.1 |
| Evapotranspiration | 6,101 | 76.3 | 6,101 | 76.3 |
| Change in water storage | 31 | 0.4 | 32 | 0.4 |
| Leachate collected from drainage layer | 0.4 | 0.005 | 15.3 | 0.2 |
| Fugitive leachate | 16 | 0.2 | 0.25 | 0.003 |
|  | Final top cover: top soil, sand, single compacted clay liner |
|  | Bottom liner: single compacted clay | Bottom liner: composite liner |
| Parameter | m3/ha.y | % | m3/ha.y | % |
| Precipitation | 7,999 | 100 | 7,999 | 100 |
| Run-off | 39 | 0.5 | 39 | 0.5 |
| Evapotranspiration | 5,454 | 68.2 | 5,454 | 68.2 |
| Change in water storage | 3.5 | 0.04 | 288 | 3.6 |
| Leachate collected from drainage layer | 105 | 1,3 | 2,148 | 26.8 |
| Fugitive leachate | 2,398 | 30 | 71 | 0.9 |

The amount of leachate generated is the highest during the filling/operational phase (no cover, daily cover and intermediate cover) of the landfill and mounts up to 31.8 % (= 2,545 m3/ha.y = precipitation - evapotranspiration - run-off from Table 3.1.46 and Table 3.1.47) of the initial precipitation (7,999 m3/ha.y).  The use of a final cover with composite liner reduces the total amount of leachate significantly to 0.2 % (= 16 m3/ha.y). In the absence of a composite liner in either the top or bottom barrier the amount of leachate produced is still substantial (2,506 m3/ha.y cfr Table 3.1.48 = 7,999 -39 - 5,454). From the results presented above it is clear that the net release of leachate into the environment (i.e. fugitive leachate) is dependent on the presence and efficiency of a leachate collection system and subsequent treatment. In case the final cover and the bottom layer only consists of a single compacted clay liner  2,398 m3/ha.y of fugitive leachate is produced (96 % of the total volume leachate = 2,506 m3 produced). In case only the final top cover consists of a composite liner only approximately 0.6 % (16 m3/ha) of the total volume leachate generated results in fugitive leachate. In the ideal case where both the bottom barrier and the top cover is comprised of a composite liner only 0.25 m3/ha.y of fugitive leachate is produced which is negligible.

In order to cover all landfill types two landfill profiles are further considered in the local assessment

- Landfill profile 1: landfill with bottom liner and final top layer consisting of a single compacted clay liner

- Landfill profile 2: landfill with bottom liner and final top liner consisting of a single composite liner

For the latter scenario the ageing of the geomembrane have been into account. It is assumed that the geomembrane will remain effective during the operational and post closure phase (= 45 years in total). While the top cover can be renewed, the renewal of the bottom liner is less feasible. Therefore it is assumed that after 45 years the bottom liner will only consist of a single compacted clay liner.

Taking into account the leachate volumes of the consecutive life stages of a landfill (see section leachate generation), the cumulated leachate volume expressed as m3 per ha for the different time horizons (20, 100 and 500 years) can be calculated (Table 3.1.49). For the time period of 0-2 years after waste placement, the landfill cells are assumed to have no cover or to be covered with a daily top cover. From years 2-5 years after waste placement cells are covered with an intermediate top cover. From years 5-15 after waste placement the cells are for 40 % covered with a final top cover. After year 15 the landfill is assumed to be completely covered with a final top cover.

Table 3.1.49: Amount of leachate generated per ha of landfill over time

| Time since waste placement (years) | Cumulative leachate generation (m3/ha) |
| --- | --- |
|  | Landfill profile 1 | Landfill profile 2 |
| Leachate | Collected | Fugitive | Collected | Fugitive |
| 20 | 2,426 | 47,747 | 23,900 | 791 |
| 100 | 4,001 | 239,607 | 24,129 | 1,697 |
| 500 | / | 1,198,907 | / | 8,263 |

The collection of the landfill leachate is assumed to proceed throughout the active period of the landfill’s operating life and is extended after the closure of a landfill for another 30 years (if a significant quantity of leachate is still being produced that contains high concentrations of contaminants).

The highest volume of leachate collected is in the operational phases of the landfill and decreases with time. For a generic landfill of 20 ha with a composite bottom liner and no top cover  (Table 3.1.45) 111m3/d (= (2,024 m3/ha.y * 20 ha)/365 d.) is collected and has to be treated. If the leachate collection volume is averaged over 20 year and taking into account the different life stages of a landfill approximately 65 m3/d is collected.

For this report the value of 100 m3/d is taken forward in the local exposure calculations (3.1.3.2) as being representative for the amount of leachate collected per day for a generic landfill of 20 hectare. This figure is in the min-max range from the figures in li–erature: 5 - 650 m3/d (Robinson et al, 1995) for landfills of different landfill surface areas.

The cadmium emissions (Table 3.1.50), before treatment, were then calculated for the generic local landfill with a surface area of 20 hectares and assuming a current leachate concentration of 5 µg/L.

Table 3.1.50: Local cadmium emissions to water (in kg) for the generic local landfill (surface area of 20 ha)

|  | Leachate concentration = 5 µg/L |
| --- | --- |
| Time since waste placement (years) | Cumulative cadmium emission (kg) |
|  | Landfill profile 1 | Landfill profile 2 |
| Leachate | Collecteda | Fugitive | Collecteda | Fugitive |
| 20 | 0.2 | 4.8 | 2.4 | 0.1 |
| 100 | 0.4 | 24.0 | 2.4 | 0.2 |
| 500 | / | 120 | / | 0.8 |

a before treatment

From Table 3.1.50 it is clear that the amount of cadmium released in the future from a landfill is limited. The current generic landfill will contain at the end 1,200-2,400 ktonnes (wet wt.) of MSW (= 840-1,680 ktonnes dry wt.) over a if we assume a 15 year filling period (80-160 ktonnes MSW/year). With a total cadmium content of 10 g/tonne dry wt. and emission factors (kg Cd emitted/kg Cd landfilled) between 1.5 10-3 (24.4 kg/16,800 kg) and 1.5 10-4 (2.6 kg/16,800 kg) can be calculated in case the landfill contains 2,400 ktonnes MSW. For comparison Finnveden (1996) reported an emission factor of 5.0 10-4 for the surveyable time period (100 years). This indicates that the largest part of the landfilled cadmium (99.85-99.98 %) remains in the landfill. If 24.4 kg Cd is released over a period of 100 year this means that on average 0.24 kg is released yearly which is a release rate of 0.001 % per year. If only a landfill height of 10 m. is assumed (1,200 ktonnes MSW) the release factor is 0.0028 %. Ehrig (1989) suggested a similar release rate of 0.002 % per year.

Baccini et al (1987) reported that more than 99.9 % of the metals are still found in the residual solids at the end of the intensive reactor phase. It has, however, been suggested that metal concentrations in landfill leachate may rise again (Eggenberger & Waber, 2000). The environmental impact after a hypothetical infinite time period has not been addressed in this report since our knowledge on this issue is insufficient.

Regional emissions of landfilling MSW

The regional emissions of cadmium per year from MSW landfills in the EU can be calculated with the following formula.

Cadmium flux (kg/year) = Landfill surface (ha) x leachate generation (m3/ha.y) x cadmium concentration in the leachate (5.10-6 kg/L)

In this report a concentration of 5 µg Cd/L is taken as a representative value for the average situation in MSW landfill leachate. In the previous section (local emissions landfill) a maximum leachate volume of 2,500m3/ha.y was calculated for an average rainfall of 7,999 m3/ha.y. The only unknown in the equation is the total surface area of the landfills. Reported landfill areas range between < 1 ha to > 10 ha while new established landfills are assumed to be reasonably large (average 20 ha, Hjelmar et al, 1994). However, almost no reliable data on the total number of MSW landfills or their landfill surface were found for most of the Member States. The values that have been reported for operational landfills for some countries are listed in table 3.1.51. The cadmium flux has been calculated with the equation described above.

Table 3.1.51: Cadmium fluxes (kg/year) of operational MSW landfills for some countries.

| Countrya | MSW landfilled (ktonnes) | Number of landfills | ktonne MSW.y per landfill | Average surface area /landfill (ha) | Total surface area (ha) | Calculated cadmium flux (kg/y) | Reference |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Finland | 1,610 | / | / | 9.3 | / | / | Assmuth (1992) |
| Sweden | 1,300 | 270-280 | 4.8 | 10 | 2,800 | 42 | Flyhammar (1995) and RVF (2002) |
| UK | 26,860 | 764 + 796 | 17.2 | 18.9 9.1 | 14,482 + 7,300 | 181 + 91 | Mc. Mellin (2002) |
| Germany | 16,000 | 376 | 42.5 | 10a | 3,760 | 235 | UBA (2001) |
| The Netherlands | 1,136 | 39 | 29 | 30.7 | 1,198 | 14.9 | VVAV (2000) |
| Average |  |  | 23.4 | 14.7 |  |  |  |

a very rough approximation on the average landfill area

The calculated cadmium fluxes range between 14.9 (The Netherlands) and 272 kg/year (UK sum). As stated in the previous sections these fluxes are directly related to the landfill surface area and the yearly precipitation. Since the total landfill surface area for most of the Member States is unknown an indirect approach had to be developed in order to assess the overall cadmium emissions for these countries. Based on the information in Table 3.1.51 an average landfill surface of 14.7 ha can be calculated. Furthermore approximately 23.4 ktonnes MSW (wet wt.) is landfilled per landfill each year based on an average of the data from Sweden, UK, Germany and the Netherlands. The latter information can be used to translate the amount of MSW landfilled (ktonnes) in each year per country (presented in Table 3.1.21) into a number of landfills. Assuming that each landfill has a surface area of 14.7 ha the total landfill surface can be calculated. Finally the cadmium flux is calculated with the equation mentioned above.

As an example the emission for France is calculated as follows:

Amount landfilled each year = 23,352 ktonnes wet wt..

Number of landfills = 23,352/23.4 = 998

Total landfill surface = 998 x 14.7 ha = 14,671 ha

Total cadmium flux (kg/y) = 14,671 x 2,500 m3/ha.y x 5.10-6.kg/L = 183 kg/y

The generated flux (leachate) may either be discharged to an off-site municipal sewage plant, discharged directly to surface water or enter into the groundwater compartment. Collection and discharge to a Sewage Treatment Plant (STP) is by far the most common discharge route for leachates from municipal waste landfills. A smaller proportion of leachate is discharged directly to surface waters. The latter is only allowed if the leachate quality fulfils certain requirements (sometimes pre-treatment, e.g aerated lagoons, is needed). Most often this quality is governed by the presence of increased levels of BOD, COD and ammonium (Table 3.1.52).

Table 3.1.52: Detailed analysis of leachate sample taken at Chapel Farm landfill, Swindon, Wiltshire, 1990-1991 (Robinson, 1995).

| Parameter | Concentration (mg/L) |
| --- | --- |
| COD | 850-10,600 |
| BOD5 | 239-4,100 |
| Ammoniacal-N | 283-531 |
| Chloride | 834-4,670 |
| Cd | < 0.01-0.02 |

Metals have been regarded only as a minor problem in the waste management of leachates and only rarely posed a significant problem in leachates from domestic waste landfills (Robinson, 1995). Discharge criteria to surface water vary from one Member State to another. Landfill effluent requirements for cadmium as prescribed in the legislation of different European countries and reported by Doedens and Theilen (1992) vary between 2-5 µg/L (The Netherlands) to 100 µg/L (Germany, Austria, Switzerland). The highest proportion of landfills discharging directly to surface water is 23 % (Germany) with less than 10 % in other Member States (Hjelmar et al, 1994).

Permitted discharge to groundwater is uncommon for modern MSW landfills but may occur by old landfills or in the framework of an engineered leachate attenuation site (Robinson, 1995).

Since the number of sites designed with bottom liners and on-site leachate treatment plants is currently increasing it is proposed to use the following regional allocation key for assessing the current emissions of landfills operational to date:

- 10 % direct discharge to groundwater (attenuation/dilution sites)

- 10 % direct discharge to surface water (sometimes an on site pre-treatment step is included)

- 80 % collected and discharged via public sewer systems or transported via tankers to a STP. In a STP an overall cadmium removal efficiency of 60 % is assumed (CBS, 2002).

It should be clear that a direct discharge to groundwater or surface water is only possible when the leachate quality is considered suitable. Since for our regional assessment we are working with a cadmium leachate concentration of 5 µ/L this is of suitable quality since according to some legislations we can discharge from 2-5 up to 100 µg/L. Therefore the scenario of direct discharge to surface water is included. If the quality is insufficient a form of pre-treatment is needed

The above regional scenario was validated with the data presented in the extensive report of Robinson (1995). The semi-quantitative and qualitative information on leachate management in the EU reported on a country by country basis also gives support to the aforementioned allocation key (EC Report, 1994). Some further more recent information was received from MSs during the risk assessment process (UBA, 2002; UK, 2002).

An overview of the overall cadmium emissions to groundwater/surface water and sludge (in kg/year) in Europe due to landfilling of MSW is presented in Tables 3.1.53-3.1.54. The overall cadmium flux was calculated with the methodology described in previous paragraphs.

Table 3.1.53 Overall cadmium emissions to groundwater/surface water and sludge (in kg/year) in Europe due to landfilling of MSW (operational landfills only). Current scenario: 75.6 % landfilling

| Country | MSW landfilled (ktonnes wet wt.) | Total cadmium flux (kg/y) | Fugitive emissions to surface water (kg/year) | Fugitive emissions to groundwater (kg/year) | Collected leachate |
| --- | --- | --- | --- | --- | --- |
| Allocation key |  |  | 10 % | 10 % | 80 % |
|  |  |  |  |  | Emissions to surface water (kg/year) after treatment | Sludge (kg/y) |
|  |  |  |  |  | 40 % | 60 % |
| Austria | 1,099 | 9 | 1 | 1 | 3 | 4 |
| Belgium | 1,473 | 12 | 1 | 1 | 4 | 6 |
| Denmark | 361 | 3 | 0.3 | 0.3 | 1 | 1 |
| Finland | 1,610 | 13 | 1 | 1 | 4 | 6 |
| France | 23,352 | 183 | 18 | 18 | 59 | 88 |
| Germany | 16,000 | 235 | 24 | 24 | 75 | 113 |
| Greece | 3,561 | 28 | 3 | 3 | 9 | 13 |
| Ireland | 1,432 | 11 | 1 | 1 | 4 | 5 |
| Italy | 20,768 | 163 | 16 | 16 | 52 | 78 |
| Luxembourg | 62 | 0.5 | 0.05 | 0.05 | 0.2 | 0.2 |
| Netherlands | 1,136 | 15 | 1 | 1 | 5 | 7 |
| Norway | 1,843 | 14 | 1 | 1 | 5 | 7 |
| Portugal | 2,603 | 20 | 2 | 2 | 7 | 10 |
| Spain | 17,477 | 137 | 14 | 14 | 44 | 66 |
| Sweden | 1,300 | 42 | 4 | 4 | 13 | 20 |
| UK | 26,860 | 272 | 27 | 27 | 87 | 131 |
| Total EU-16 | 120,937 | 1,158 | 116 | 116 | 371 | 556 |

The total amount of MSW being landfilled in 1995-2001 for the EU-16 was 120,937 ktonnes wet wt. (84,656 ktonnes dry wt.) on yearly basis corresponding with an overall EU landfilling share of 75.6% (see point 3.1.2.2.5.4). A total yearly cadmium flux of 1,158 kg has been calculated. Based on the calculations above the cadmium emission to the groundwater compartment due to landfilling MSW is 116 kg Cd/year. An additional 487 kg is emitted to surface water and 556 kg of cadmium can be found in the sludge.

Similar to the section on local emissions of landfilling the release rate (%) per year can be calculated. If it is assumed that the landfills have a 15-year filling period then 1,269,838 ktonnes MSW (dry wt.) have been landfilled. With a total cadmium content of 10 g/tonne dry wt. a total of 12,698,380 kg of cadmium is present. If 1,158 kg Cd is released per year a release rate of approximately 0.01 % per year is calculated.

Table 3.1.54: Overall cadmium emissions to groundwater/surface water and sludge (in kg/year) in Europe due to landfilling of MSW (operational landfills only). Scenario: 100%  landfilling

| Country | MSW landfilled (ktonnes wet wt.) | Total cadmium flux (kg/y) | Fugitive emissions to surface water (kg/year) | Fugitive emissions to groundwater (kg/year) | Collected leachate |
| --- | --- | --- | --- | --- | --- |
| Allocation key |  |  | 10 % | 10 % | 80 % |
|  |  |  |  |  | Emissions to surface water (kg/year) after treatment | Sludge (kg/y) |
|  |  |  |  |  | 40 % | 60 % |
| Austria | 1,578 | 12 | 1 | 1 | 4 | 6 |
| Belgium | 2,842 | 22 | 2 | 2 | 7 | 11 |
| Denmark | 2,091 | 16 | 2 | 2 | 5 | 8 |
| Finland | 1,690 | 13 | 1 | 1 | 4 | 6 |
| France | 34,133 | 268 | 27 | 27 | 86 | 129 |
| Germany | 28,000 | 220 | 22 | 22 | 70 | 106 |
| Greece | 3,561 | 28 | 3 | 3 | 9 | 13 |
| Ireland | 1,432 | 11 | 1 | 1 | 4 | 5 |
| Italy | 22,717 | 178 | 18 | 18 | 57 | 86 |
| Luxembourg | 185 | 1 | 0.1 | 0.1 | 0.5 | 1 |
| Netherlands | 4,995 | 39 | 4 | 4 | 13 | 19 |
| Norway | 2,217 | 17 | 2 | 2 | 6 | 8 |
| Portugal | 3,663 | 29 | 3 | 3 | 9 | 14 |
| Spain | 18,804 | 148 | 15 | 15 | 47 | 71 |
| Sweden | 2,700 | 21 | 2 | 2 | 7 | 10 |
| UK | 29,450 | 231 | 23 | 23 | 74 | 111 |
| Total EU-16 | 160,058 | 1,257 | 126 | 126 | 402 | 603 |

Based on the calculations above the cadmium emission in a 100 % landfilling scenario would result in an emission to the groundwater compartment of 126 kg Cd/year. An additional 528 kg is emitted to surface water and 603 kg of cadmium can be found in the sludge.

The allocation of the total EU landfill emissions to the regional scale has been performed with the 10 % rule (Table 3.1.55).

Table 3.1.55: Total annual amount of Cd emissions to groundwater/surface water and sludge within the EU from landfilling MSW

| Scenario | Released amount Cadmium (kg/y) | Continental (90 %) (kg/y) | Regional (10 %) (kg/y) |
| --- | --- | --- | --- |
|  | SURFACE WATER |
| 75.6 % landfilling | 487 | 438 | 49 |
| 100 % landfilling | 528 | 475 | 53 |
|  | GROUNDWATER |
| 75.6 % landfilling | 116 | 104 | 12 |
| 100 % landfilling | 126 | 113 | 13 |
|  | SLUDGE |
| 75.6 % landfilling | 556 | 500 | 56 |
| 100 % landfilling | 603 | 543 | 60 |

Contribution of Ni-Cd  batteries to the overall cadmium emissions of landfilling MSW

With the assumption that Ni-Cd batteries account for 10-50 % of the total MSW cadmium content, the contribution of Ni-Cd batteries can be calculated by multiplying the overall cadmium emissions as presented in Table 3.1.52 by respectively 0.1 and 0.5 (Table 3.1.56 and Table 3.1.57).

Table 3.1.56: Contribution of Ni-Cd batteries to the overall cadmium emissions due to landfilling of MSW

| Scenario | 75.6 % landfilling | 100 % landfilling |
| --- | --- | --- |
| Allocation key | 10% | 50% | 10% | 50% |
| Compartment | Direct emissions (kg/year) |
| Surface water | 49 | 244 | 56 | 264 |
| Groundwater | 12 | 58 | 13 | 63 |
| Sludge | 56 | 278 | 60 | 302 |

Table 3.1.57: Contribution of Ni-Cd batteries to the continental and regional cadmium emissions due to landfilling of MSW.

| Scenario |  | Released amount Cadmium (kg/y) | Continental (90 %) (kg/y) | Regional (10 %) (kg/y) |
| --- | --- | --- | --- | --- |
|  |  | SURFACE WATER |
| 75.6. % landfilling | 0.1 | 49 | 44 | 5 |
|  | 0.5 | 244 | 220 | 24 |
| 100 % landfilling | 0.1 | 56 | 50 | 7 |
|  | 0.5 | 264 | 238 | 26 |
|  |  | GROUNDWATER |
| 75.6 % landfilling | 0.1 | 12 | 11 | 1 |
|  | 0.5 | 58 | 52 | 6 |
| 100 % landfilling | 0.1 | 13 | 12 | 1 |
|  | 0.5 | 63 | 57 | 6 |
|  |  | SLUDGE |
| 75.6 % landfilling | 0.1 | 56 | 50 | 6 |
|  | 0.5 | 278 | 250 | 28 |
| 100 % landfilling | 0.1 | 60 | 54 | 6 |
|  | 0.5 | 302 | 272 | 30 |

###### Sensitivity analysis

The values used in the previous sections to produce the emissions of MSW incinerators and MSW landfills represent average or estimated values. Therefore, a large amount of uncertainty is associated with these numbers. This uncertainty is difficult to take into account explicitly. However, a sensitivity analysis was performed on some of the input parameters used to determine the effect that varying the parameters had on the overall results. The following parameters and ranges were used:

Table 3.1.58: Variation of model parameters used in the sensitivity analysis

| Incinerator |
| --- |
| Model parameter | Unit | Minimum value | Default value | Maximum value | Affected parameter |
| Total Cd content in MSW | g/ton dry wt. | 5 | 10 | 15 | bottom ash and fly ash concentrations Cadmium landfilled |
| Amount of wastewater | m3/ton | 0.6 | 2.5 | 5 | Emissions to water |
| Effluent concentration | mg/L | 0.1 | 0.3 | 1 | Emissions to water |
| Treatment efficiency | % | 90 | 98.8 | 99.9 | Emissions to water |
| Landfill |
| Leachate concentration landfill | µg/L | 0.5 | 5 | 50 | Emissions to water |
| Percolation flux | % | 1 | 10 | 20 | Emissions to water |
| Treatment efficiency STP | % | 40 | 60 | 80 | Emissions to water |
| Allocation key |
| Contribution Ni-Cd batteries | % | 10 | 50 | Emissions to water |

Ranges were chosen in such a way that they covered at least the figures reported in literature. The upper limit for the leachate concentration (50 µg/L that is close to the solubility limit for cadmium carbonate, Ross et al. (2000)) in landfill leachates is added to represent a worst case future leachate concentration as a result of an increasing cadmium content in the MSW. It should be stressed that this seems indeed a worst case since under aerobic conditions predicted solubility limits are around an order higher than measured leachate concentrations suggesting that other mechanisms such as adsorption phenomena are limiting cadmium release.

However, as it has already been indicated in section 3.1.2.2.5.6 the composition of the future leachate cannot be predicted based on current knowledge since there is no direct relationship between the total content of Cd and the leachability of Cd. If the simplified assumption is taken that there would exist a simple direct linear relationship between the cadmium leachate concentration and the cadmium content in the solid mass as has been assumed in other studies (e.g.  Leenaars and Steketee, 1997 (in: van der Poel, 1999) and Camobreco et al (1999)) this could be calculated as followed:

=  x

CdConc Future, leachate = future cadmium concentration in the leachate (µg/L)

CdConc Present, leachate = present cadmium concentration in the leachate (µg/L) =5 µg/L

CdConc Future, MSW = future cadmium concentration  MSW (g) = 24 g

CdConc Present, MSW = present cadmium concentration in MSW (g) = 10 g

The maximum leachate concentration is calculated based on the ratio of the current cadmium concentration in the leachate for one average ton of waste to the total cadmium present in the average ton of waste. The future cadmium concentration in the MSW has been calculated in section 3.1.2.5.3 . The results showed that a maximum steady state concentration in the MSW corresponds to 24 g/tonne dry wt. From these assumptions and using the formula above a worste case future leachate concentration of 12 µg/L can be calculated which is well within the range (0.5-50 µg/L) used in the sensitivity analysis.

The effects of varying the different input parameters (by the values shown in Table 3.1.58) on the overall results are shown in Figures 3.1.9-3.1.10. On the figures, the dark bar shows the effect of the maximum value and the gray bar show the effects of the minimum values.

Figure 3.1.9 Effects of varying input parameters on MSW incinerator emissions

From Figure 3.1.9, varying the different parameters has a significant effect on the overall results:

- Cadmium concentrations in bottom ash and fly ash vary with 50 %: 1.6-25.9 g/ton dry wt. (bottom ash); 82.9-300 g/ton dry wt. (fly ash)

- Emissions to surface water and sludge are the most influenced by the choice of treatment efficiency. A lower treatment efficiency (90 %) will result in a higher emission to water (+ 732 %)

Figure 3.1.10 Effects of varying input parameters on MSW landfill water emissions

From Figure 3.1.10, varying the different parameters has a significant effect on the overall results:

- The choice of the flux to groundwater or surface water has only a minor influence (± 8.5-14 %)

- The choice of the treatment efficiency in the  STP has a moderate influence (± 38 %)

- The choice of leachate concentration has the highest impact and varies between – 998 % to 809 %

Based on the results above it can be concluded that modifying certain default parameters can have a large effect on the overall emissions of the disposal phase. Where possible the effect of changing these parameters has been taken into account in this report. First of all the emissions to the different compartments have been quantified based on the European average situation (24.4 % incineration and 75.6 % landfill) and completed by two scenario’s (100 % landfilling and 100 % incineration). The effect of increased total cadmium content in MSW is covered in the future scenarios (10 and 75 % collection) for MSW incinerators with a cadmium content of respectively 13.2 and 24 g/ton dry wt. The effect of a hypothetical higher landfill leachate concentration of 50 µg/L has also been taken forward as a scenario. Furthermore for landfills the assessment was performed with and without the presence of a STP.

##### Summary: releases to the environment due to battery related life cycle steps

The overall cadmium emission of the disposal phase originating from all products containing cadmium in MSW can be found in tables 3.1.35 (incineration current situation), table 3.1.39 (incineration future situation) and table 3.1.55 (landfills). In Tables 3.1.59-63 only a summary of the cadmium EU emissions from different parts of the life cycle of Ni-Cd batteries taken forward in the analysis is given. It is important to note that a large uncertainty surrounds the figures of the disposal phase (Cfr 3.1.2.2.5.7).

Table 3.1.59:  Summary of the distributions in kg (total in EU) of Cd emissions to different environmental compartments during the total life cycle of Ni-Cd batteries (realistic scenario: 24.4 % incineration and 75.6 % landfilling). Scenario 10 mg/kg dry wt. cadmium.

| Life cycle stages | Emission distribution in kg/year |
| --- | --- |
|  | Air | Water | Urban/ind. soil/agr. soil | Ground-water | Total release |
| 1 Manufacturing of Ni-Cd batteries and/or battery packs | 51 | 65 | 0 | 0 | 116 |
| 2 Incorporation into battery powered devices and applications | 0 | 0 | 0 | 0 | 0 |
| 3 Use, recharging and maintenance by end users | / | / | / | / | / |
| 4 Recycling Collection Processing Recovery | 1.8 | 0.1 | 0 | 0 | 1.9 |
| 5 Disposal (10-50 % Ni-Cd batteries contribution) Incineration (24.4 %) Landfilling (75.6%) | 323-1,617 N/A | 35-176 49-244 | N/A 56-278 | N/A 12-58 | 358-1,793 117-580 |
| Total | 376-1,670 | 149-485 | 56-278 | 12-58 | 593-2,491 |

/ =  no direct emissions. Indirect cadmium emissions  associated with the energy consumption used to recharge the batteries are deemed negligible

N/A = Not applicable

Table 3.1.60:  Summary of the distributions in kg (total in EU) of Cd emissions to different environmental compartments during the total life cycle of Ni-Cd batteries (worst case scenario: 100% incineration). Scenario 10 mg/kg dry wt. cadmium

| Life cycle stages | Emission distribution in kg/year |
| --- | --- |
|  | Air | Water | Urban/ind. soil/agr. soil | Total release |
| 1 Manufacturing of Ni-Cd batteries and/or battery packs | 51 | 65 | 0 | 116 |
| 2 Incorporation into battery powered devices and applications | 0 | 0 | 0 | 0 |
| 3 Use, recharging and maintenance by end users | / | / | / | / |
| 4 Recycling Collection Processing Recovery | 1.8 | 0.1 | 0 | 1.9 |
| 5 Disposal (10-50 % Ni-Cd contribution) Incineration (100%) Landfilling (0%) | 1,402-7,009 N/A | 144-721 N/A | N/A N/A | 1,546-7,730 N/A |
| Total | 1,455-7,062 | 209-786 | 0 | 1,664-7,848 |

/ =  no direct emissions. Indirect cadmium emissions  associated with the energy consumption used to recharge the batteries are deemed negligible

N/A = Not applicable

Table 3.1.61:  Summary of the distributions in kg (total in EU) of Cd emissions to different environmental compartments during the total life cycle of Ni-Cd batteries (worst case scenario: 100% landfilling). Scenario 10 mg/kg dry wt. cadmium

| Life cycle stages | Emission distribution in kg/year |
| --- | --- |
|  | Air | Water | Urban/ind. soil/agr. soil | Ground-water | Total release |
| 1 Manufacturing of Ni-Cd batteries and/or battery packs | 51 | 65 | 0 | 0 | 116 |
| 2 Incorporation into battery powered devices and applications | 0 | 0 | 0 | 0 | 0 |
| 3 Use, recharging and maintenance by end users | / | / | / | / | / |
| 4 Recycling Collection Processing Recovery | 1.8 | 0.1 | 0 | 0 | 1.9 |
| 5 Disposal (10-50 % Ni-Cd contribution) Incineration (0%) Landfilling (100%) | 0 N/A | 0 56-264 | N/A 60-302 | 0 13-63 | 0 129-629 |
| Total | 53 | 121-329 | 60-302 | 13-63 | 247-747 |

/ =  no direct emissions. Indirect cadmium emissions  associated with the energy consumption used to recharge the batteries are deemed negligible

N/A = Not applicable

Table 3.1.62: Summary of the distributions in kg (total in EU) of Cd emissions to different environmental compartments during the total life cycle of a Ni-Cd battery (Future scenario: 100% incineration. Scenario 13.2 mg/kg dry wt.)

| Life cycle stages | Emission distribution in kg/year |
| --- | --- |
|  | Air | Water | Urban/ind. soil/agr. soil | Total release |
| 1 Manufacturing of Ni-Cd batteries and/or battery packs | 51 | 65 | 0 | 116 |
| 2 Incorporation into battery powered devices and applications | 0 | 0 | 0 | 0 |
| 3 Use, recharging and maintenance by end users | / | / | / | / |
| 4 Recycling Collection Processing Recovery | 1.8 | 0.1 | 0 | 1.9 |
| 5. Disposal (32 % Ni-Cd batteries contribution) Incineration (100%) Landfilling (0%) | 4,486 N/A | 615 N/A | N/A N/A | 5,101 N/A |
| Total | 4,539 | 680 | 0 | 5,219 |

/ =  no direct emissions. Indirect cadmium emissions  associated with the energy consumption used to recharge the batteries are deemed negligible

N/A = Not applicable

Table 3.1.63: Summary of the distributions in kg (total in EU) of Cd emissions to different environmental compartments during the total life cycle of a Ni-Cd battery (Future scenario: 100% incineration. Scenario 24 mg/kg dry wt.)

| Life cycle stages | Regional releases in kg/year |
| --- | --- |
|  | Air | Water | Urban/ind. soil/agr. soil | Total release |
| 1 Manufacturing of Ni-Cd batteries and/or battery packs | 51 | 65 | 0 | 116 |
| 2 Incorporation into battery powered devices and applications | 0 | 0 | 0 | 0 |
| 3 Use, recharging and maintenance by end users | / | / | / | / |
| 4 Recycling Collection Processing Recovery | 1.8 | 0.1 | 0 | 1.9 |
| 5. Disposal (63 % Ni-Cd batteries contribution) Incineration (100%) Landfilling (0%) | 8,831 N/A | 2,178 N/A | N/A N/A | 11,009 N/A |
| Total | 8,882 | 2,243 | 0 | 11,125 |

/ =  no direct emissions. Indirect cadmium emissions  associated with the energy consumption used to recharge the batteries are deemed negligible

N/A = Not applicable

#### Releases based on update site-specific exposure data (reference year 2002)

##### Cadmium metal and cadmium oxide production

As described in section 2.1.2, the number of companies still manufacturing cadmium metal is reduced to three. Only one plant is still producing cadmium oxide.

An overview of Cd emissions to water and air from Cd metal and CdO production is presented in -Table 3.1.64 – Table 3.1.65 and - Table 3.1.66 – Table 3.1.67 respectively (Reference year 2002). Information on waste for these sectors is presented in Table 3.1.68-Table 3.1.69. These data are extracted from plant information recently submitted by the remaining Cd metal/CdO producing plants in the EU-16 (Industry questionnaire 2004).

Cadmium metal production

- The three remaining cadmium metal producing plants all reported information on emissions to water (emission factors varying between 1.10 and 277 g/ton). The total Cd emission to the aquatic environment from the three existing Cd metal producing plants (plant 1, 6, 7) in 2002 is 70.5 kg/y. Water emission data for the year 2004 are reported for Cd metal production plant 7. The total yearly Cd emission to water is reduced by a factor of 1.6; the emission factor is reduced with 16% (i.e. 232 g/ton versus 277 g/ton). As mentioned in the se–tion below -on changes in emission reduction measures- substantial changes have taken place at this site in the collection and treatment of waste water in the period 2002-2004, resulting in a reduction of water emissions.

- All companies presented information on air emissions (stack emissions) (emission factors varying between 23.8 and 259 g/ton). The total EU emission to the air compartment from cadmium metal producers is 94.6 kg Cd/year.

- For all sites fugitive emissions are included in the reported stack emissions. One site reports that fugitive emissions amount to 60-70% of total air emissions.

- Number of emission days to water and air is 365 days for all sites.

- Measured effluent concentrations (annual mean), effluent discharge rates and type of receiving surface water (ditch, tide influenced river, sea) are reported for all companies.

- For two out of three companies, detailed information with respect to on site treatment of waste water in a WWTP is submitted. There are two physico-chemical treatment plants in use on site 7; one central water treatment plant and one weak acid treatment plant. In the central water treatment plant; lime (CaO) and sodium sulphide (Na2S) are used as the main precipitation agents. The main reaction is precipitation of the metals as hydroxides in the pH range of 8.3-8.5. In order to control the Cd concentration in the effluent, some sodium sulphide is added before the water enters a thickener in which the hydroxides/sulfides are settled. The effluent/overflow from the thickener is polished in sand filters. The water treatment plant is continuously controlled (24 hours a day: pH, flow and other parameters). The waste water from Cd metal production site 1 is purified in an on site waste water treatment plant using a bacteriological process in which metal sulphates are converted into metal sulphides. In the first step of this process –Biological DeSulfurisation (BDS) stage- process water containing a high sulphate concentration is treated. The BDS-process consists of an initial chemical pre-purification step (separation of metals (solids) and fluoride from the waste water) followed by a bacteriological purification stage (conversion of sulphate to sulphides). The sludges (metal-sulphates, solids) arising from previous treatment steps are recycled to the main production process. The effluent from the BDS water purification step is further purified in the next step, the SRB (Sulphate Reducing Bacteria) water purification process (capacity of 400 m3/h). The SRB water purification plant is fed with waste water containing low concentrations of metals and sulphate, i.e. the effluent from the BDS process and water from the geohydrological control system. In an UASB (‘upflow anaerobic sludge blanket’) reactor bacteria –fed by ethanol- convert sulphates to sulphides. The excess of formed sulphide is converted by bacteria to sulphur in a fixed film reactor. The sludge of metal sulphides is recycled to the main zinc production process. This technique is known as BAT. The purified water is discharged to a ditch. The effluent from the water purification plant of site 1 is controlled 52 times a year by taking flow proportional samples; the analytical method is according to national standard 6426; the detection limit is 0.3 µg/l. Site 6 mentions that the waste water is treated in an on site water treatment plant; the effluents from this site are treated together with discharges from another metal producing site (distribution 50:50). There are no details on the treatment steps available.

- Waste is not generated during Cd metal production (dross, sludge, solid waste is recycled in the production).

- The flow of the receiving surface water –necessary to calculate a site specific dilution factor- is available for 2 companies (site 1, 6). Site 7 discharges its waste water to a sea environment for which a default dilution factor of 100 is applied.

Significant changes in production/emission reduction measures since 1996 are reported as follows:

- Site 1: in 2000, change of raw material (Century concentrate). Due to new national regulation entering into force, and the fact that Century concentrate was dustier than the concentrates worked up before, a lot of actions were taken: closed conveyor system, closed storage bins with underpressure and baghouse, house keeping etc. Cadmium concentration in Century concentrate is lower as in the concentrates used till 2000. So several Cd emissions (related to diffuse concentrate/calcine emissions) are proportional lower. Former concentrate till 2000: 0.19% Cd, after 2001: 0.12% Cd. Cd produc tion in 1997: 745  tonnes, 2004: 549 tonnes. Cd emission is only for a small part related to the Cd plant, most of the Cd emissions are related to the zinc production. Since 2002 further remediation actions took place: formerly untreated historically contaminated water from  the plant area is now also treated in the WWTP (see also the footnote of Table 3.1.64).

- Site 6: none reported.

- Site 7: 2001-2003. Collecting and treating/reuse of approximatey 90% diffuse emissions and storm/runoff waters from the industrial site. A containment basin was built under the industrial site to collect surface and storm water. 2003. Modernising the central water treatment plant. 2003-2004. Construction of a new quay to reduce pollution/runoff due to spill during unloading of raw materials. 1995-to date: installation of abatement systems in stacks in the leaching plant.

Cadmium oxide production

- The only remaining Cd oxide production plant reports that no waste water discharges from the site occur since the production of cadmium oxide is a totally dry process.

- Very recently an update of the air emission data is provided. Total Cd emission to the atmosphere amounts to 6.6 kg/year (in-house methods; predicted; year 2005 stack measurements: 53-55 µg Cd/m3, average flow rate: 10000 m3/h; number of emission hours: 6000 h/year , 2 stacks). Please note that for the year 2004 the total Cd emission to the air is reported as 11.7 kg/year (independent laboratory) (based on an average Cd concentration of 97 µg/m3 (two stacks), average flow rate: 10000 m3/h; number of emission hours: 6000 h/year). Both emission values will be taken forward to the exposure assessment and risk characterisation.

- Number of emission days to air is 256 days.

- Information on waste is not available.

Release to water

Table 3.1.64: Aquatic emissions from Cd metal producing plants in the EU-16.

| plant N° | production volume | production emission¶ | emission factor | conc.I effluent(c) | number of emission days | concentration in effluent(a) | effluent flow(a) | Low flow receiving water(b) | year |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | ton y-1 | kg y-1 | g ton-1 |  |  | mg l-1 | m³ d-1 | m³ d-1 |  |
| 1 | 485 | 12.0(d) (f) | 25 | M (T) | 365 | 0.004 (g) | 9060 | 12000 | 2002 |
| 6 | 420 | 0.50(d) | 1.10 | M (T) | 365 | 0.0007(h) | 1169 | 13 106 | 2002 |
| 7* | 209 | 58(e) | 277 | M (T) | 365 | 0.05 | 3200 | -* | 2002 |
| 7* | 155 | 36(e) | 232 | M (T) | 365 | 0.030 | 3200 | -* | 2004 |

(a) mean annual; (b) 10th percentile of flow rate or 1/3 of annual mean flow rate (TGD, 2003); (c) M: measured value, E: estimated value, D: dissolved concentration, T: total concentration; (d) emission of Cd from Zn or Zn and Pb production;  (e): only process discharges, no diffuse discharges (surface/storm water etc) included (f) the total emission in 2002 consists of discharge of effluent from water purification plant and discharge of other water from the plant area (historic contaminated). Since 2005, the discharge from water from the plant area has been stopped; since then all waste water is treated in the purification plant. (g) the effluent concentration of 4 µg/l is a weighted average Cd concentration for both types of water discharges (effluent: avg conc. 1.5 µg/l, P90: 2.3 µg/l; discharge: 2,736,115 m3/year; other plant area water: avg concentration: 13.6 µg/l; total discharge: 571,334 m3/year). ¶annual averages; *emission to the sea; (h) measured by supervision authority.

Table 3.1.65: Aquatic emissions from Cd oxide producing plants in the EU-16.

| Plant N° | production volume | production emission¶ | emission factor | conc. In effluent© | number of emission days | concentration in effluent(a) | effluent flow(a) | Low flow receiving water (b) | year |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | ton y-1 | kg y-1 | g ton-1 |  |  | mg l-1 | m³ d-1 | m³ d-1 |  |
| 12 | 4498 | 0(d) | 0 | 0 | 2 | 0 | 0 | 0 | 2002 |

a) mean annual; (b) 10th percentile of flow rate or 1/3 of annual mean flow rate (TGD, 2003); (c) M: measured value, E: estimated value, D: dissolved concentration, T: total concentration; (d) no emissions to water; thermal/dry process  ¶annual averages.

Release to air

Table 3.1.66: Atmospheric emissions from Cd metal producing plants in the EU-16.

| Plant N° | production volume | Production emission amount¶ | emission factor | year |
| --- | --- | --- | --- | --- |
|  | ton y-1 | kg y-1 | g ton-1 |  |
| 1 | 485 | 30.4(a)(b) | 62.7 | 2002 |
| 6 | 420 | 10.0(a) (c) | 23.8 | 2002 |
| 7 | 209 | 54.2(a) (d) | 259 | 2002 |

¶annual averages; (a) Cd emission from whole plant (including Zn and/or Pb production) (b) total emissions: stack + diffuse emissions; diffuse emissions: 60-70% of total; stack emissions: 30-40% of total emissions. (c) All emissions from point sources and fugitive emissions from roof openings for the whole zinc production process (extensive monitoring programme 2001/2002). Emissions from cadmium production are difficult to separate. (d) Total emissions from the zinc smelter; approx. 90 emission points to air. Approximately 90% of the emission comes from 20% of the emission points which all are equipped with abatement systems (demisters or scrubbers).

Table 3.1.67: Atmospheric emissions from Cd oxide producing plants in the EU-16.

| Plant N° | production volume | Production emission amount¶ | emission factor | year |
| --- | --- | --- | --- | --- |
|  | ton y-1 | kg y-1 | g ton-1 |  |
| 12(a) | n.d. | 6.6(a) | n.d. | 2005 |
| 12 | n.d. | 11.7(b) | n.d. | 2004 |

¶annual averages; (a) Cd in stack emissions is recently measured (year 2005): average Cd concentration: 55 µg/m3 (punctual measurement, in-house methods; no further information available); (b) Cd in stack emissions measured by external laboratory (year 2004; no further information available); average Cd concentration : 97 µg/m3; n.d.: no data available.

Waste

Table 3.1.68: Waste information for Cd metal producing plants in the EU-16.

| Plant N° | Type of waste produced | Quantity of waste | Cd content | Waste disposal type | year |
| --- | --- | --- | --- | --- | --- |
|  |  | (t/year) | % |  |  |
| 1 | No waste produced Recycling of liquids directly into the leaching process. Recycling of solid wastes (scalings) by the residue recycling. Sludge out off the water purification is used as secondary raw material. | Not applicable n.d. | Not applicable n.d. | Internal recycling Internal recycling | 2002 2002 |
| 6 | No waste related to cadmium production | Not applicable | Not applicable | Not applicable | 2002 |
| 7 | Normally no waste is produced during production of Cd metal. The Cd is a by product from the hydrometallurgical Zn metal production from Zn concentrates. In the Cd foundry some dross is produced but the material is recycled to the production. Sludges from the water treatment plants are deposited in mountain cavern deposits together with the other process wastes, however, the metal containing hydroxide cake from the weak acid treatment plant is recycled to the zinc process. | Not applicable | Not applicable | Internal recycling | 2002 |

n.d.: no data available

Table3.1.69: Waste information for Cd oxide producing plants in the EU-16.

| Plant N° | Type of waste produced | Quantity of waste | Cd content | Waste disposal type | year |
| --- | --- | --- | --- | --- | --- |
|  |  | (t/year) | % |  |  |
| 12 | n.d. | n.d. | n.d. | n.d. | 2002 |

n.d.: no data available

##### Release during processing and use

###### Ni-Cd batteries’ production and recycling

As described in section 2.2.1.1; the number of companies producing Ni-Cd batteries has further decreased in recent years. Five Ni-Cd battery producers and three Ni-Cd battery recyclers are still in operation. At present, updates on environmental emissions to water and air have been submitted by 3 Ni-Cd battery producers and 3 recyclers (year 2002). Please note that the previous update of exposure information for these sectors was 1999/2000. The data are summarised in Table 3.1.70, Table 3.1.71 and Table 3.1.72, Table 3.1.73. Waste information was collected from battery manufacturing and recycling plants. The data are presented in Table 3.1.74 and Table 3.1.75.

Production of Ni-Cd batteries

- Three out of five remaining Ni-Cd battery producing plants submitted information on emissions to water (site 2, 3, 4). It should be noted however that emissions from site 2 include emissions from battery manufacturing as well as Cd recyling. The site is involved in both activities and wastewater emissions cannot be split between two factories. The total Cd emission to the aquatic environment from Ni-Cd battery producing plants is 49.1 kg/y. It should be noted as well that the updated emissions are derived on the basis of annual average effluent concentrations, as opposed to the emissions given in the original TRAR document (see current section 3.1.2.2.1) in which P90’s values were calculated on monthly average effluent concentrations.

- Two companies (site 2, 4) provided information on air emissions (stack emissions). The total Cd emission to the air compartment from this sector is 8.5 kg/year. As mentioned before, site 2 is both a Ni-Cd battery producing and Cd recycling site. The reported emission figure of 5 kg/year is originating from battery manufacturing only. For site 3 no information is provided since air emissons are not monitored. According to the company, there are no requirements for air monitoring in the permit since the plant runs a wet process (most emissions are to water).

- Fugitive emissions are not monitored.

- Number of emission days to water and air varies between 330 and 344 days.

- Measured effluent concentrations (annual mean), effluent discharge rates and type of receiving surface water (tide influenced river, sea, river) are reported for all companies.

- New information with respect to on site treatment of waste water in a WWTP is not submitted. It is assumed that all waste waters are treated in an on site WWTP/municipal STP before being discharged into surface waters.

- The following Cd containing waste arises from battery production: old batteries, powders, sludge, plates, other. In general all materials are recycled (external recycling in Cd recycling plants). In some cases sludge can also be landfilled.

- The flow of the receiving surface water –necessary to calculate a site specific dilution factor- is available for 3 companies (site 2, 3, 4).

Recycling of Ni-Cd batteries

- Three Ni-Cd battery recycling plants (site 1, 2, 2bis) reported information on emissions to water. Site 1 reports very low emissions to water for the year 2002 i.e. 0.13 kg/y. Moreover, wastewater emissions -and emission factors- from this site are further reduced in 2003/2004 (0.06 kg/y) due to efforts to conform to ISO 14000, for which the site has been certified in February 2005 (details are included in the section below: ‘significant changes in emission reduction measures’). The information for site 2bis is already included in the Ni-Cd battery producing section, since waste water emissions could not be split between NiCd-battery manufacturing and recycling plant. Site 2 states that no site emissions are discharged to surface water. All waste waters are collected and treated off-site in an external waste water treatment plant (total volume of waste water: 100 m3/year, no further update data available) (1996 data: 35 tonnes fluid waste per year; Cd content: 20 ppm (total Cd); effluent concentration of off-site STP: 0.2 mg/l).

- Three Cd recycling plants (site 1, 2, 2bis) provided information on air emissions (stack emissions). Site 1 reports air emissions of 3.97 kg Cd/y for the year 2002. In analogy with water emissions, air emissions –and emission factors- are further reduced in 2003/2004 i.e. to 0.91 kg/y as a result of measures taken to obtain an ISO 14000 certificate (building coverage, aspiration devices) (details are included in the section below: ‘significant changes in emission reduction measures’). The total Cd emission to the air compartment from the site 2bis is 0.85 kg/year. Please note that the reported figure for this site –Ni-Cd battery manufacturing and Cd recyling plant- is related to recycling only. The very low emission of 0.002 kg Cd/year for site 2 is validated on the basis of the submitted air measurements’ report (IUTA-Prüfbericht, 2004). The low emission figure is a result of very low Cd concentrations detected in the stack emissions (Cd conc. 2.5 µg/m3) combined with a low gas flow rate (78 m3/h max).

- 	Fugitive emissions are not monitored.

- Number of emission days to water and air is 330-360 days.

- Since for site 2 wastewater is not discharged locally (near the site), but collected and treated off-site, other water related emission information for this site (effluent discharge rate, type of receiving water, flow rate of surface water,…) is not relevant. The information relevant for site 2bis is reported in the section on Ni-Cd battery manufacturing. Measured effluent concentrations (90P value/annual mean), effluent discharge rate and type and flow (low flow rate) of receiving surface water (river) are reported for site 1.

- Waste arising from the recycling of Ni-Cd batteries e.g. batteries plastic boxes, metallic boxes, concentrated electrolytes, Fe/Cd electrodes… is recycled or landfilled. Waste arising from the treatment of stack (air) emissions and waste water (dust filters, sludges) is recycled.

Significant changes in production/emission reduction measures since 1999/2000 are reported as follows:

- Ni-Cd battery manufacturing plants: not available

- Cd recycling site 1: Invested improvements in building coverage and investment of aspiration device with a capacity of 60,000 m3/h to prevent diffuse emissions to air (since 2002). Improvements are ongoing in 2005. Wastewater and air emissions: efforts to conform to ISO 14000, for which the site has been certified in February 2005. The main changes that took place at the level of waste water emissions are the following: a) Because of the negative impact of the presence of cooling liquid -originating from electric vehicles batteries- and hydrocarbons -sometimes present in the electrolyte from batteries- on the WWTP efficiency, it was decided to collect the cooling liquid –during the batteries dismantlement- separately and send it for recycling. The electrolyte collecting system was modified by adding a hydrocarbon separator. The following actions were undertaken to reduce air emissions: a) high efficiency systems were modified: i.e. two rows of filters were installed instead of one; in this manner maintenance operations are secured, peaks are avoided and Cd emissions are reduced. b) Furthermore, work was done on the empowerment of the operators using these air treatment systems by setting up luminous devices, which indicate the state of sealing. The use of these ‘warnings’ improved the follow up of the installations as well as immediately reduced the delays due to maintenance intervention.

- Cd recycling site 2: Installation of active carbon filter between furnaces and chimney (installed between 2002 and today).

Release to water

Table 3.1.70: Aquatic emissions from Ni-Cd batteries producing plants in the EU-16.

| plant N° | consumption volume (expressed as Cd) | emission¶ | emission factor | coI in effluent(c) | number of emission days | concentration in effluent(a) | effluent flow(a) | Low flow receiving water (b) | year |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | ton y-1 | kg y-1 | g ton-1 |  |  | mg l-1 | m³ d-1 | m³ d-1 |  |
| 2*/2bis | 453 | 11.5(d)* | 25.4 | M (T) | 330 | 0.11 | 326 | 432,000* | 2002 |
| 3 | 454 | 13.7 | 30.2 | M (T) | 330 | 0.06 | 655 | 17 106 | 2002 |
| 4 | 771 | 23.9 | 31.0 | M (T) | 344 | 0.10 | 673 | 1,244,160 | 2002 |
| 6 | No update data | No update data |  |  |  |  |  |  |  |
| 7 | No update data | No up data |  |  |  |  |  |  |  |

(a) mean annual; (b) 10th percentile of flow rate or 1/3 of annual mean flow rate (TGD, 2003); (c) M: measured value, E: estimated value, D: dissolved concentration, T: total concentration; (d): emissions from battery manufacturing plant and Cd recyling plant combined, emissions cannot be split between two factories; ¶annual averages; *emission to the sea.

Table 3.1.71: Aquatic emissions from Ni-Cd batteries recycling plants in the EU-16.

| plant N° | production volume (expressed as Cd) | emission¶ | emission factor | Inc. in effluent(c) | number of emission days | concentration in effluent(a) | effluent flow(a) | Low flow receiving water (b) | year |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | ton y-1 | kg y-1 | g ton-1 |  |  | mg l-1 | m³ d-1 | m³ d-1 |  |
| 1 | 853 | 0.13 | 0.15 | M (T) | 191 | 0.37 (90P) 0.16 (avg) | 4.2 | 11,232 | 2002 |
| 1 | 816 | 0.06 | 0.07 | M (T) | 177 | 0.24 (90P) 0.1 (avg) | 3.3 | 11,232 | 2004 |
| 2 | 62 | 0(d) | 0 | 0 | 360 | 0 | 0 | 0 | 2002 |
| 2bis | See data on site is in Table 3.7 |

(a) mean annual effluent flow for the year 2002 is 4.2 m³ d-1 and for 2004 is 3.3 m³ d-1; (b) 10th percentile of flow rate or 1/3 of annual mean flow rate (TGD, 2003); (c) M: measured value, E: estimated value, D: dissolved concentration, T: total concentration; ¶annual averages; (d) No site emission to water. Cleaning water as well as processing water are collected internal (about 100 m3/year) and send to an external waste water treatment plant.

Release to air

Table 3.1.72: Atmospheric emissions from Ni-Cd batteries producing plants in the EU-16.

| Plant N° | consumption volume (expressed as Cd) | Production emission amount¶ | emission factor | year |
| --- | --- | --- | --- | --- |
|  | ton y-1 | kg y-1 | g ton-1 |  |
| 2 | 453 | 5.0(a) | 11.04 | 2002 |
| 3 | 454 | n.d.(b) | n.d. | 2002 |
| 4 | 771 | 3.5 | 4.54 | 2002 |
| 6 | No update data | No update data |  |  |
| 7 | No update data | No update data |  |  |

¶annual averages; n.d.: no data available (a) Emission from battery manufacturing only; air emissions are broken down between two plants; battery manufacturing and Cd recycling; (b) Air emissons are not monitored. No requirement in the permit since the plant runs a wet process, therefore most emissions are releases in the water.

Table 3.1.73: Atmospheric emissions from Ni-Cd batteries recycling plants in the EU-16.

| Plant N° | production volume (expressed as Cd) | Production emission amount¶ | emission factor | year |
| --- | --- | --- | --- | --- |
|  | ton y-1 | kg y-1 | g ton-1 |  |
| 1 | 853 | 3.97 | 4.55 | 2002 |
| 1 | 816 | 0.91 | 1.10 | 2004 |
| 2 | 771 | 0.0019 (a) | 0.00002 | 2002 |
| 2bis | 453 | 0.85 (b) | 8.30 | 2002 |

¶annual averages; (a) Submitted air emissions are checked versus the analysis report and proved to be correct. Air emissions are that low due to the fact that in air emission no considerable amount of Cd can be found (conc. 2.5 µg/m3) and the fact that the gas stream is very low due to technical reasons (78 m3/h max); analysis performed by external laboratory. (b) Emissions from Cd recycling unit on the site of battery manufacturing plant 2.

Waste

Table 3.1.74: Waste information for Ni-Cd batteries producing plants in the EU-16.

| Plant N° | Type of waste produced | Quantity of waste | Cd content | Waste disposal type | year |
| --- | --- | --- | --- | --- | --- |
|  |  | (t/year) | % |  |  |
| 2 | Old batteries Powders (from sludge recycling) Plates Other (filters,…) | 20.6 25 38 6 | 7% 95% 27% 5% | Recycling plant Recycling plant Recycling plant Incineration | 2002 |
| 3 | Old batteries Sludge (filtercakes) Plates Others (filters,…) | 72 218 51 17 | 7-10% 57% water, 4% Cd on dry weight 48% 20% | External recycling plant Special (CET1) landfill External recycling plant | 2002 |
| 4 | Old batteries Sludge (filtercakes) Plates Others (filters,…) | 185 187 117 1 | 13% 50% water, 9.7% Cd on dry weight 18% 5% | External recycling plant External recycling plant External recycling plant | 2002 |
| 6 | No update data | No update data |  |  |  |
| 7 | No update data | No update data |  |  |  |

Table 3.1.75: Waste information for Ni-Cd batteries recycling plants in the EU-16.

| Plant N° | Type of waste produced | Quantity of waste | Cd content | Waste disposal type | year |
| --- | --- | --- | --- | --- | --- |
|  |  | (t/year) | % |  |  |
| 1 | Batteries plastic boxes Batteries metallic boxes Fe/Cd electrodes after treatment; Concentrated electrolytes Process slag, air treatment dust, used filters, rainwater sludges. | 256 169.5 262.7 186.2 | 0.33 mg/kg 0.1 mg/kg 0.5 mg/kg 4.2 mg/kg. | Industrial landfill Recycling Industrial landfill Neutralisation Internal treatment. | 2002 |
| 2 | n.a. | n.a. | n.a. | n.a. | 2002 |
| 2bis | Old batteries Powders Plates | 1024 25 38 | 9% 95% 27% | Recycling | 2002 |

###### Production of Cd containing pigments

Compiled updated emission information for the three remaining Cd pigments producers was submitted (year 2003). A summary of releases to water and air is given in  Table 3.1.76 and Table 3.1.77respectively. Waste information is presented in Table 3.1.78.

- The three remaining Cd pigments producing plants (site A, B, C) reported information on emissions to water (emission factors not available). The total Cd emission to the aquatic environment in 2003 is 10.9 kg/y. Please note that year 2004 waste water emission data have been provided by site C; Cd emission from this site amounts to 4.4 kg/year (as opposed to 6.9 kg/year for the year 2003).

- All companies presented information on air emissions (stack emissions) (site-specific emission factors not available). The total EU emission to the air compartment from cadmium pigments producers is 11.0 kg Cd/year.

- Information on fugitive emissions is not provided.

- The number of emission days to water and air varies between 318-365 days.

- Measured effluent concentrations (annual mean), effluent discharge rates and type of receiving surface water (river) are reported for all companies. The effluent from site C is analysed daily (usually a 24 hours composite sample). Effluent samples are analysed by Atomic Absorption using either ‘flame’ or ‘graphite furnace’. The laboratory participates in the Aquacheck scheme (Water Proficiency Testing and Laboratory Performance Monitoring) as a means of ensuring accurate results for metals in aqueous effluents.

- New information with respect to the on site treatment of waste water in a WWTP is submitted for all sites. For Cd pigments producing sites in general, the on site treatment of aqueous effluent is an integral part of the production process. The treatment of the aqueous effluent is a chemical/physical process involving pH change to precipitate Cd, followed by filtration to remove Cd carbonate. For site C specifically, all aqueous waste is collected and treated by raising the pH to 9 using sodium carbonate solution in a stirred treatment vessel. This precipitates the soluble Cd as carbonate. The resultant suspension is filtered through a filter press to remove suspended solids. The filtrate is tested for suspended solids, refiltered and then passed to a (settling) ‘pool’ that allows a continuous discharge of effluent to the receiving river over 365 days/year.

- Sludge from the treatment of waste water and other solid wastes are landfilled.

- The flow of the receiving surface water –necessary to calculate a site specific dilution factor- is available for all companies.

Significant changes in production/emission reduction measures since 1996 are reported as follows:

- The most significant changes are for losses to solid wastes. Figures submitted for the previous draft of the RAR were lower because at that time waste solids from treatment of production waste water were sent to zinc refiners for recovery of zinc and cadmium. Environmental pressures have forced the closure of the relevant zinc refiners, and the waste solids now have to be sent to landfill.

Release to water

Table 3.1.76: Aquatic emissions from Cd pigments producing Plants in the EU-16.

| plant N° | Production/ consumption volume | Processing emission¶ | emission factor | conc. in effluent(c) | number of emission days | concentration in effluent(a) | effluent flow(a) | Low flow receiving water (b) | year |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | ton y-1 | kg y-1 | g ton-1 |  |  | mg l-1 | m³ d-1 | m³ d-1 |  |
| A | n.d. | 1.0 | n.d. | M(T) | 365 | 0.02 | 145 | 3333 | 2003 |
| B | n.d. | 3.0 | n.d. | M(T) | 318 | 0.02(f) | 498 | 1681920 | 2003 |
| C | n.d. | 6.9 (d) | n.d. | M(T) | 365 | 0.12(e) | 156 | 45000 | 2003 |
| C | n.d. | 4.4 | n.d. | M(T) | 365 | 0.08 (90P) 0.05 (avg) | 240 | 45000 | 2004 |

(a) mean annual; (b) 10th percentile of flow rate or 1/3 of annual mean flow rate (TGD, 2003); (c) M: measured value, E: estimated value, D: dissolved concentration, (d): waste water consists of process waste water and rainwater collected from buildings and exterior storage areas. (e): average Cd concentration in effluent for the year 2004 is 0.05 mg/l; 90P value: 0.08 mg/l. Total discharge: 87480 m3/d. T: total concentration; (f): P90 in effluent for the year 2004: 0.054 mg/l; ¶annual averages;  n.d.: no data available

Release to air

Table 3.1.77: Atmospheric emissions from Cd pigments producing plants in the EU-16.

| Plant N° | production/consumption volume | Processing emission ¶ | emission factor | year |
| --- | --- | --- | --- | --- |
|  | ton y-1 | kg y-1 | g ton-1 |  |
| A | n.d. | 2.50 | n.d. | 2003 |
| B | n.d. | 5.60 | n.d. | 2003 |
| C | n.d. | 2.90 | n.d. | 2003 |

¶annual averages; n.d.: no data available

Waste

Table 3.1.78: Waste information for Cd pigments producing plants in the EU-16.

| Plant N° | Type of waste produced | Quantity of waste | Cd content | Waste disposal type | year |
| --- | --- | --- | --- | --- | --- |
|  |  | (t/year) | % |  |  |
| A | Solid waste and sludge | 15 | n.d. | landfill | 2002 |
| B | Solid waste and sludge | 6.8 | n.d. | landfill | 2002 |
| C | Solid waste and sludge | 7.3 | n.d. | landfill | 2002 |

n.d.: no data available

###### Production of Cd containing stabilisers

As a result of the Vinyl 2010 commitment the number of producers in the EU-16 dropped to only a few. Currently only 2 companies acknowledged to the Rapporteur that some production still took place at their sites located in Italy. Emission data are summarised in Table 3.1.79 and Table 3.1.80. Waste information is presented in Table 3.1.81.

- The two remaining Cd stabiliser producing plants (site X, Y) reported information on emissions to water (emission factors <9.0-<41.0 g/ton). The total Cd emission to the aquatic environment in 2002 is <1.4 kg/y.

- All companies presented information on air emissions (stack emissions) (emission factors <1.3-38 g/ton). The total EU emission to the air compartment from cadmium stabiliser producers is <0.74 kg Cd/year. The analytical method used to measure Cd in air emissions from site Y is the following: MIP P-PRO-101 rev 2, 2003.

- Information on fugitive emissions is not provided.

- Depending the site, the number of emission days to water varies between 220-365 days. The number of emission days to air varies between 50-220 days. The number of production days for site Y is 40-60 days.

- Measured effluent concentrations (annual mean), effluent discharge rates and type of receiving surface water (municipal STP, river, canal) are reported for both companies. For site Y, the analysis of waste water (ICP, dl: 5 µg/l) is done every 15 days on an average sample collected during this period with an automatic sampling system (internal laboratory). Two times per year the analysis is performed by an accreditated external laboratory on punctual sampling (EPA 200.8, 1994; dl: 1 µg/l).

- New information with respect to on site treatment of waste water in a WWTP is submitted by company Y. This site has a physico-chemical treatment plant (comprising the following main units: homogenisation basin (600m3), additivation, flocculation, sedimentation, filter press for sludges and sand filters for treated water) followed by active carbon filters.. For site X, wastewaters are treated in an on site WWTP(type is unknown) before being discharged to a municipal STP.

- Solid waste is landfilled.

- The flow of the receiving surface water –necessary to calculate a site specific dilution factor- is available for both companies.

Release to water

Table 3.1.79: Aquatic emissions from Cd stabiliser producing plants in the EU-16.

| plant N° | Production/ consumption volume | Production emission amount¶ | emission factor | conc. in effluent(c) | number of emission days | concentration in effluent(a) | effluent flow(a) | Low flow receiving water (b) | year |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | Ton y-1 | kg y-1 | g ton-1 |  |  | mg l-1 | m³ d-1 | m³ d-1 |  |
| X | 17 | <0.70(d) | <41 | M (T) | 220 | On site WWTP : <0.005 Municipal STP : <0.00037(e) | 370 | 831050 | 2002 |
| Y | 77 | <0.69 | <9.0 | M (T) | 365 | <0.005(f) | 352 | 86400 | 2002 |
| Y | 77 | <0.69 | <9.0 | M (T) | 365 | <0.001(g) | 352 | 86400 | 2002 |

a) mean annual; (b) 10th percentile of flow rate or 1/3 of annual mean flow rate (TGD, 2003); (c) M: measured value, E: estimated value, D: dissolved concentration, T: total concentration; (d) Emission to municipal STP (e) Cd concentration in effluent from municipal STP; calculated from Cd concentration in effluent from on site WWTP; taking into account removal at STP: 60%; extra dilution: 2000 m3/d/370 m3/d = 5.4.;  ¶annual averages; (f) analysis performed by internal laboratory (two times a month) method MIP-P-PRO-101 rev 2 year 2003; (g) analysis performed by accreditated external laboratory (two times a year), method EPA 200.8 (1994),

Release to air

Table 3.1.80: Atmospheric emissions from Cd stabiliser producing plants in the EU-16.

| Plant N° | production/consumption volume | Production emission amount¶ | emission factor | year |
| --- | --- | --- | --- | --- |
|  | ton y-1 | kg y-1 | g ton-1 |  |
| X | 17 | 0.64 | 38.0 | 2002 |
| Y | 77 | <0.10(a) | <1.3 | 2002 |

¶annual averages (a) analysis performed by internal laboratory

Waste

Table 3.1.81: Waste information for Cd stabiliser producing plants in the EU-16.

| Plant N° | Type of waste produced | Quantity of waste | Cd content | Waste disposal type | year |
| --- | --- | --- | --- | --- | --- |
|  |  | (t/year) | % |  |  |
| X | Solid waste | 37 kg Cd | 37 kg Cd | offsite inertisation and landfilling | 2002 |
| Y | n.d. | n.d. | n.d. | n.d. | 2002 |

n.d.: no data available

###### Use of Cd/CdO in alloys, plating and other uses

For these uses, no site-specific update information was submitted to the Rapporteur.

##### Releases during the production of other non-ferrous metals

In this section, the Cd releases from four sites that stopped Cd metal production and that submitted emission information are briefly discussed. An overview of Cd emissions to water and air for each of the four non-ferrous metal producing sites is presented in Annex VI.

From this information, it can be concluded that, although the production of Cd metal stopped, Cd emissions to water and air can still be substantial -up to 427 kg Cd/year to water and 56.6 kg Cd/year to air respectively. The Cd emissions arise from the production of other non-ferrous metals (i.e. Zn and Pb). No production volumes related to other non-ferrous metals were submitted, so no corresponding emission factors could be calculated.

### Predicted environmental concentrations (PEC)

#### Local exposure assessment: in production, processing and use scenarios excluding those related to batteries

Point sources have a major impact on the environmental concentration on a local scale.

Local exposure concentrations are calculated from emission data submitted by Industry (Industry Questionnaire, 1997) according to the EU-Technical Guidelines Document (TGD,1996). Calculated values are compared with measured concentrations near Cd emitting plants (Ind. Questionnaire, 1997) and where large differences occur, results are analysed and evaluated.

##### Aquatic compartment

# Calculated local concentrations

Calculation of local PEC-values for the aquatic compartment is performed according to the method described in the TGD (1996). On a local scale it is assumed that wastewater will pass through a STP before being discharged into the environment. Once discharged, complete mixing of the effluent in the surface water is assumed. The calculation involves several sequential steps: it includes the calculation of the discharge concentration (if not available) of a STP to a water body, the dilution effect and the removal from the aqueous medium by adsorption to suspended matter. Volatilisation and degradation are ignored because these processes are not applicable for Cd. Local sedimentation of Cd is ignored. Input data were submitted via the Industrial Questionnaire (1997).

The first step in the assessment of the local PEC values in the aquatic environment is the determination of the site-specific effluent concentration. If not available, it was calculated from reported daily releases to surface water (kg d-1) and the local effluent flow rate (m3 d-1).

# EMISSIONlocal

CeffluentSTP  =   --------------------------------- .103

EFFLUENTlocalSTP

EMISSIONlocal:		local emission amount from point source (kg d-1)

EFFLUENTlocalSTP: 	effluent discharge rate of STP (m³ d-1)

CeffluentSTP: 		Cd concentration in effluent of STP (mg L-1).

If no effluent discharge rate was submitted, a default value of 2000 m³ d-1 (TGD, 1996) was used.

In the second step, the concentration in the receiving surface water is calculated. Complete mixing of the effluent with the receiving water is assumed. The calculation of the dilution factor is based on the given flow rate of the receiving waterbody (or default: 18000 m3 d-1) and on the given discharge rate of the industrial STP (or default: 2000 m3 d-1). In the absence of both data, a default dilution factor of 10 is used for emissions to freshwater. A default dilution factor of 100 is used for emissions to the sea.

# EFFLUENTlocalSTP + FLOW

D =   ——————————————

EFFLUENTlocalSTP

# D: 			dilution factor

EFFLUENTlocalSTP:		effluent discharge rate of local STP (m³ d-1)

FLOW:		flow rate of the receiving water (m³ d-1)

The local available concentration of Cd in water is estimated taking into account the fraction of chemical that is adsorbed to suspended matter (TGD, 1996). The local concentration in the receiving surface water during the emission period is then calculated with the equation:

# CeffluentSTP * 1000

Clocalwater =          ————————————

(1 + Kp * Csusp * 10-6) *D

Clocalwater : 			local concentration in surface water

during emission period ((g L-1)

CeffluentSTP: 		Cd-concentration in local STP effluent ((g L-1)

Kp  : 			solids-water partition coefficient of suspended

matter (130000 L  kg-1).

Csusp : 		concentration of suspended matter in

watercourse (default = 15 mg L-1)

D: 			dilution factor (default 10)

The value of Kp can be derived from the ratio of dissolved to total Cd concentrations in waterbodies. The dissolved fraction is generally the fraction passing a 0.45 µm membrane filter. The Kp-value varies with environmental conditions. Factors having a large influence on the actual Kp-value are the pH, the total metal concentration, the water hardness and the nature and concentration of complexing agents. A range of measured Kp values is presented in Table 3.1.4. In the calculations presented here, a European average value of Kp = 130 103 L kg-1 is used.

Table 3.1.82: the solid- water partition coefficient of suspended matter (Kp) in different freshwaters.

| Location | Kp (L kg-1) average | Kp (L kg-1) min | Kp (L kg-1) max | Source |
| --- | --- | --- | --- | --- |
| Flanders | 17 103 | 0.28 103 | 280 103 | VMM, 1997 |
| the Rhine, Meuse and Schelde rivers in The Netherlands | n.a. | 30 103 | 300 103 | Ros&Slooff, 1990 |
| 4 locations in the Netherlands 1983-1986 | 129 103 | n.a. | n.a. | Crommentuijn et al., 1997a |
| 7 locations in the Netherlands 1988-1992 | 151 103 | n.a. | n.a. | Crommentuijn et al., 1997a |
| 3 locations in the Netherlands 1992-1994 | 224 103 | n.a. | n.a. | Crommentuijn et al., 1997a |
| St Lawrence River basin 1991-1992 | 100 103 | 7.9 103 | 794 103 | Quemerais and Lum, 1997 |

n.a.: not available

The calculated surface water concentrations are actual contributions to the receiving water. The local PEC values are obtained by adding the regional PEC value for water to the calculated local concentration in surface water.

# PEClocalwater = Clocalwater + PECregionalwater

# PEClocalwater: 		predicted environmental concentration during

emission episode ((g L-1)

Clocalwater: 			local concentration in surface water during

emission episode ((g L-1)

PECregionalwater: 	regional concentration in surface

water (0.11 (g L-1 Table 3.1.157)

The local PEC values of Cd in surface water are presented in Table 3.1.83. The local PEC values range from 0.11 to 5.54 µg L-1 for Cd/CdO-producing plants and from 0.11 to 2.86 µg L-1 for Cd/CdO-processing plants.

Table 3.1.83: the local PECwater (dissolved fraction) for Cd-producing and -processing plants in the EU-16.  PEc’s include background Cd.

| use- | N° | production emission¶ | processing emission¶ | dilution Factor | Clocalwater | PEClocalwater | year |
| --- | --- | --- | --- | --- | --- | --- | --- |
| category |  | kg y-1 | kg y-1 |  | µg L-1 | µg L-1 |  |
| Cd-production | 1 | 23.9 |  | 12 | 1.26 | 1.37 | 1996 |
|  | 2 | 614 |  | 320 | 0.47 | 0.58 | 1996 |
|  | 3* | 15.7 |  | 100(a)* | 0.03* | 0.14* | 1996 |
|  | 4* | 21.6 |  | 100(a)* | 0.41* | 0.52* | 1996 |
|  | 5 | 77.8 |  | 10(a) | 5.4 | 5.5 | 1996 |
|  | 6 | 0.18 |  | 29500 | 7.8 10-6 | 0.11 | 1996 |
|  | 7* | 70 |  | 100(a)* | 0.20* | 0.31* | 1996 |
|  | 8 | 11 |  | 930 | 0.01 | 0.12 | 1996 |
|  | 9* | 17.4 |  | 100(a)* | 0.02* | 0.13* | 1999 |
|  | 10 | 0(1) |  | 0(1) | 0(1) | 0.11 | 1996 |
|  | 11 | 0(2) |  | 0(2) | 0(2) | 0.11 | 1996 |
|  | 13* | 372 |  | 100(a)* | 0.58* | 0.69* | 1996 |
| CdO-producers | 11 |  | 0(2) | 0(2) | 0(2) | 0.11 | 1996 |
|  | 12 |  | 0(2) | 0(2) | 0(2) | 0.11 | 1993 |
| Cd-stabilisers | F |  | 0.03 | 500 | 0.0007 | 0.11 | 1996 |
|  | G |  | 0.5 | 25 | 0.18 | 0.29 | 1996 |
|  | H |  | 0.78 | 100 | 0.027 | 0.14 | 1996 |
|  | I |  | 0.1 | 10 | 0.01 | 0.12 | 1996 |
|  | J |  | 0 | 0 | 0 | 0.11 | 1996 |
|  | K |  | 4.1 | 10 | 0.58 | 0.69 | 1996 |
|  | L |  | 0 | 0 | 0 | 0.11 | 1996 |
|  | M |  | 0 | 0 | 0 | 0.11 | 1996 |
|  | windows manufacturer |  | 0 | 0 | 0 | 0.11 | 1996 |
| Cd-pigments | A |  | 0.6 | 50 | 0.14 | 0.25 | 1996 |
|  | B |  | 4.02 | 1000 | 0.001 | 0.11 | 1996 |
|  | C |  | 5.9 | 700 | 0.04 | 0.15 | 1996 |
|  | D |  | 0.9 | 250 | 0.03 | 0.14 | 1996 |
|  | E |  | 13.4 | 24800 | 0.001 | 0.11 | 1996 |
| Cd-plating | EU |  | 250 | 10(a) | 2.75 | 2.9 | 1996 |
| Cd-alloys | EU |  | 61.3 | 10(a) | 1.7 | 1.81 | 1996 |

*Emission to the sea; ¶annual averages; n.a.: not available; (1) No water emissions: waste waters are recycled; (2) no water emissions: dry process; (a) default value: 10 (freshwater), 100 (sea water)

# Measured local concentrations

Monitoring data from Cd-producing plants were submitted via the Industrial Questionnaire (1997). In general, most of these plants have implemented a monitoring program to control the effluent concentrations and the concentrations in the receiving water flow at and around the point of discharge. In Table 3.1.84 measured and calculated data are presented as dissolved concentrations. Submitted measured values are generally total concentrations and are often limited to one value per site rather than ranges. Moreover, measurements do not always refer to the same year as the one for which PEC values are calculated (e.g. site 2). In order to be able to compare measured and calculated values, total measured values are converted to dissolved values assuming a dissolved fraction of 33% of the total measured Cd concentration (dissolved fraction = 1/((1+Kp*Csusp*10-6) with Kp = 130 103 L kg-1, Csusp = 15 mg L-1; TGD, 1996).  Measured concentrations range from <0.1 µg L-1 to 10 µg L-1. At some plants measurements were performed at different locations and Cd-concentrations were found to decrease with distance from the point of discharge.

Only few comparisons between predicted and measured concentrations can be made. Model predictions fit observations except for the plants that emit their effluents to the sea. Environmental characteristics of both receiving water and effluent water have a very important influence on the final dissolved Cd concentrations in the receiving waterbody. Dilution factors of 1.0 to 3.4 do not seem realistic when effluents are emitted to the sea. Factors influencing the final dissolved exposure concentration are the amount and composition of suspended matter, water hardness, pH and Cd concentration of the receiving water before the point of discharge. Predictions of local concentrations can only be improved if local conditions are assessed in detail.

Table 3.1.84: the measured local Cd concentrations in the effluent receiving water and the local PECwater concentrations for Cd-producing and -processing plants in the EU-16.

| use- | plant N° | production | Processing | PEClocalwater |  | year |
| --- | --- | --- | --- | --- | --- | --- |
| category |  | emission amount | Emission amount | calculated | measured(2) |  |
|  |  | kg y-1 | kg y-1 | µg L-1 | µg L-1 |  |
| Cd-production | 1 | 23.9 |  | 1.37 | 1.0 | 1996 |
|  | 2 | 614 |  | 0.59 | 0.1 (1994) | 1996 |
|  | 3* | 15.7 |  | 0.15* | 1.5-10 (500m-1km) | 1996 |
|  | 4* | 21.6 |  | 0.52* | 1.6 (10m, 1995) | 1996 |
|  | 5 | 77.8 |  | 5.5 | 5 | 1996 |
|  | 6 | 0.18 |  | 0.11 | 0.15 | 1996 |
|  | 7* | 70 |  | 0.32* | 0.03 (1997)(a) | 1996 |
|  | 8 | 11 |  | 0.12 | n.a. | 1996 |
|  | 9* | 17.4 |  | 0.13 | <0.05 (2000) | 1999 |
|  | 10 | 0(1) |  | 0.11 | n.a. | 1996 |
|  | 11 | 0(1) |  | 0.11 | n.a. | 1996 |
|  | 13* | 372 |  | 0.69* | 3 (50m) | 1996 |
| CdO-producers | 11 |  | 0(1) | 0.11 | n.a. | 1996 |
|  | 12 |  | 0(1) | 0.11 | n.a. | 1993 |
| Cd-stabilisers | F |  | 0.03 | 0.11 | n.a. | 1996 |
|  | G |  | 0.5 | 0.29 | n.a. | 1996 |
|  | H |  | 0.78 | 0.14 | n.a. | 1996 |
|  | I |  | 0.1 | 0.13 | n.a. | 1996 |
|  | J |  | 0 | 0.11 | n.a. | 1996 |
|  | K |  | 4.1 | 0.69 | n.a. | 1996 |
|  | L |  | 0 | 0.11 | n.a. | 1996 |
|  | M |  | 0 | 0.11 | n.a. | 1996 |
|  | window manufacturer |  | 0 | 0.11 | n.a. | 1996 |
| Cd-pigments | A |  | 0.6 | 0.25 | n.a. | 1996 |
|  | B |  | 4.02 | 0.11 | n.a. | 1996 |
|  | C |  | 5.9 | 0.15 | n.a. | 1996 |
|  | D |  | 0.9 | 0.14 | n.a. | 1996 |
|  | E |  | 13.4 | 0.11 | n.a. | 1996 |
| Cd-plating | EU |  | 250 | 2.9 | n.a. | 1996 |
| Cd-alloys | EU |  | 61.3 | 1.81 | n.a. | 1996 |

*Emission to the sea; n.a.: not available; (1) No water emissions: dry process or waste waters are recycled; (2) If total concentrations are measured, dissolved concentrations are estimated to be 33% of total Cd concentration (Kp = 130 103 L kg-1, Csusp = 15 mg L-1); (a)Measured at 40 m depth (emission at 30 m depth), several km away from the emission point

##### The sediment

Following the standard approach as laid down in the TGD, the local concentration in the sediment is predicted based on the local concentrations in the water as

# PEClocalsediment= Kp PEClocal water. 10-3

in which the Kp (L kg-1dw) equals the solid- water partition coefficient of suspended matter. The average Kp value for suspended matter (130000 Lkg-1dw) however strongly overpredicts sediment concentrations. As an example, the average Cd concentrations in surface water in Europe is about 0.14 µg Cd L-1 and the average sediment Cd concentration is 1.32 mg Cd kg-1dw. The predicted average sediment concentration using the average Kp of suspended matter is 0.14 *130000/1000 = 18.2 mg Cd kg-1dw and which is about 14-fold above the average measured concentrations. As an alternative, one could use the ‘best fit’ Kp of sediments, defined as the ratio of the average sediment to average water Cd concentrations. This ‘best fit’ Kp yields 10000 L kg-1dw (=1.32/0.14*1000). Another alternative is to use a measured regional PEC for the sediment to which a local added fraction is added, formally

PEClocalsediment = PECregionalsediment + Kp Clocal water. 10-3

in which the Kp (L kg-1dw) equals the solid- water partition coefficient of suspended matter. This option has been preferred because (i) of the preference for measured rather than predicted sediment concentrations and (ii) because the contribution of the local discharge to the sediment concentrations is taken into account via suspended matter Kp in line with the TGD.

The measured PEC regional is taken as an average of 90th percentiles of surveys: 2.66 mg Cd kg-1dw (Table 3.1.189).

The local PECsediment  are readily calculated from the data in Table 3.1.83 and the above-mentioned equation and  presented in table 3.1.85. The Clocalsediment (Kp Clocal water. 10-3) is included to illustrate the contribution of the local discharge onto the sediment PEC.

The local PECsediment range from 2.7 to 707.8 mg kg-1dw for Cd-producing plants and from 2.7 to 359.6 mg kg-1 for Cd-processing plants.

Table 3.1.85: the local PECsediment for Cd-producing and –processing plants in the EU-16. The PEC’s include background Cd. All values are expressed as total Cd concentrations and thus not corrected for bioavailability.

| use category | plant n° | production emission¶ | processing emission¶ | Clocalsediment | PEClocalsediment | year |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | kg y-1 | kg y-1 | mg kg-1dw | mg kg-1dw |  |
| Cd-producers(e) | 1 | 23.9 |  | 163.7 | 166.4 | 1996 |
|  | 2 | 614 |  | 61.4 | 64.1 | 1996 |
|  | 3* | 15.7 |  | 4.4 | 7.1 | 1996 |
|  | 4* | 21.6 |  | 52.9 | 55.6 | 1996 |
|  | 5 | 77.8 |  | 705.1 | 707.8 | 1996 |
|  | 6 | 0.18 |  | 0.0 | 2.7 | 1996 |
|  | 7*£ | 70 |  | 26.4 | 29.1 | 1996 |
|  | 8 | 11 |  | 1.4 | 4.1 | 1996 |
|  | 9* | 17.4 |  | 1.8 | 4.5 | 1999 |
|  | 10 | 0(1) |  | 0.0 | 2.7 | 1996 |
|  | 11 | 0(1) |  | 0.0 | 2.7 | 1996 |
|  | 13* | 372 |  | 74.9 | 77.6 | 1996 |
| CdO-producers | 11 |  | 0(1) | 0.0 | 2.7 | 1996 |
|  | 12 |  | 0(1) | 0.0 | 2.7 | 1993 |
| Cd-stabilisers | F |  | 0.03 | 0.1 | 2.8 | 1996 |
|  | G |  | 0.5 | 22.9 | 25.6 | 1996 |
|  | H |  | 0.78 | 3.5 | 6.2 | 1996 |
|  | I |  | 0.1 | 1.7 | 4.4 | 1996 |
|  | J |  | 0 | 0.0 | 2.7 | 1996 |
|  | K |  | 4.1 | 75.3 | 78.0 | 1996 |
|  | L |  | 0 | 0.0 | 2.7 | 1996 |
|  | M |  | 0 | 0.0 | 2.7 | 1996 |
|  | window manufacturer |  | 0 | 0.0 | 2.7 | 1996 |
| Cd-pigments | A |  | 0.6 | 18.8 | 21.5 | 1996 |
|  | B |  | 4.02 | 0.1 | 2.8 | 1996 |
|  | C |  | 5.9 | 5.2 | 7.9 | 1996 |
|  | D |  | 0.9 | 3.8 | 6.5 | 1996 |
|  | E |  | 13.4 | 0.1 | 2.8 | 1996 |
| Cd-plating | EU |  | 250 | 356.9 | 359.6 | 1996 |
| Cd-alloys | EU |  | 61.3 | 220.4 | 223 | 1996 |

*emission to the sea; ¶annual averages; n.a.: not available; (1) no water emissions: waste waters are recycled; (2) no water emission: dry process; £: based on 1996 monitoring results (sediment analyses 0-3cm), the value of 1.9 mg Cd/kg dwt is proposed for the local exposure assessment by the company (Industry/company data submission, Aug. 2004)

##### Atmospheric compartment

# Calculated local concentrations

Local PEC-values for the atmospheric compartment are calculated according to the OPS model proposed in the TGD (1996) for a general standard environment. The PEC values are represented as an average concentration at 100 m from the source. In general the atmospheric compartment receives its input from direct emission to air. Local Cd concentrations in the air are assessed by calculating the amount emitted to the air by the Cd producing and processing plants:

# Clocalair = Elocalair * Cstdair

# Elocalair : 		local direct emission rate to air during emission

period (kg d-1)

Cstdair : 		concentration in air at source strength of 1 kg d-1

(ng m-³) default: 278 (TGD, 1996)

Temission : 		number of days per year that emission takes

place (d y-1)

Clocalair : 	local concentration in air during emission period

(ng m-³)

Clocalair, ann : 		annual average concentration in air, 100 m from

point source (ng m-³)

Input data are the total daily emissions of the individual Cd-producing plants and EU emission data of industry processing Cd in alloys (ERL, 1990) and plating (WS Atkins, 1998).

The calculated concentrations in air are actual contributions to the receiving atmosphere. The local PEC values are obtained by adding the regional PEC values for air to the calculated local concentration in the atmosphere.

# PEClocalair,ann = Clocalair, ann + PECregionalair

# PEClocalair,ann: 		annual average predicted environmental

concentration in air  (ng m-3)

PECregionalair: 		regional concentration in the air

(0.55 ng m-3; table 3.1.157)

The results of the predicted local atmospheric Cd concentrations at 100 m from the point sources are listed in Table 3.1.86. Calculated local PEC values range from 0.8 to 1282 ng m-³ with the highest values emitted by Cd producing pyrometallurgical plants. For the Cd processing industry, a very high value was found for the processing of Cd in alloys. Since information on site specific or EU level was not available, it is based on estimated EU-emission amounts. Site-specific information is needed to validate the results.

Table 3.1.86: calculated local PECair concentrations for Cd-producing and processing plants in EU-16.

| use- | plant N° | production | processing | number of | annual average | PEClocalair,ann | Year |
| --- | --- | --- | --- | --- | --- | --- | --- |
| category |  | emission amount¶ | emission amount¶ | emission days(1) | air concentration |  |  |
|  |  | kg y-1 | kg y-1 |  | (100 m) ng m-³ | (100 m) ng m-³ |  |
| Cd-production | 1 | 54 |  | 365 | 41 | 42 | 1996 |
|  | 2 | 1683 |  | 365 | 1282 | 1282 | 1996 |
|  | 3 | 800 |  | 70 | 609 | 610 | 1996 |
|  | 4 | 3.03 |  | 15 | 2.3 | 2.9 | 1996 |
|  | 5 | 946 |  | 243 | 721 | 721 | 1996 |
|  | 6 | 6.24 |  | 105 | 4.8 | 5.3 | 1996 |
|  | 7 | 200 |  | 365 | 152 | 153 | 1996 |
|  | 8 | 28.6 |  | 151 | 21.8 | 22 | 1996 |
|  | 9 | 110 |  | 365 | 83.8 | 84 | 1996 |
|  | 10 | 3.32 |  | 316 | 2.5 | 3.1 | 1996 |
|  | 11 | 1.61 |  | 32 | 1.2 | 1.8 | 1996 |
|  | 13 | 24.6 |  | 123 | 18.7 | 19 | 1996 |
| CdO-producers | 11 |  | 0.30 | 251 | 0.228 | 0.8 | 1996 |
|  | 12 |  | 0.31 | 256 | 0.236 | 0.8 | 1993 |
| Cd-stabilisers | F |  | 0.09 | 20 | 0.069 | 0.6 | 1996 |
|  | G |  | 0.8 | 48 | 0.609 | 1.2 | 1996 |
|  | H |  | 0.5 | 60 | 0.381 | 0.9 | 1996 |
|  | I |  | 0.1 | 13 | 0.076 | 0.6 | 1996 |
|  | J |  | 0.7 | 13 | 0.533 | 1.1 | 1996 |
|  | K |  | 0.04 | 12 | 0.030 | 0.6 | 1996 |
|  | L |  | n.a. | 155 | n.a. | 0.6 | 1996 |
|  | M |  | 0 | 155 | 0 | 0.6 | 1996 |
|  | window manufacturer |  | n.a. | 350 | n.a. | 0.6 | 1996 |
| Cd-pigments | A |  | 1.15 | 230 | 0.876 | 1.4 | 1996 |
|  | B |  | 2.37 | 231 | 1.8 | 2.4 | 1996 |
|  | C |  | 3.6 | 276 | 2.7 | 3.3 | 1996 |
|  | D |  | 5.8 | 230 | 4.4 | 5.0 | 1996 |
|  | E |  | 0.2 | 85 | 0.152 | 0.7 | 1996 |
| Cd-plating | EU |  | 0 | 155 | 0 | 0.6 | 1996 |
| Cd-alloys | EU |  | 770 | 62 | 586 | 587 | 1996 |

n.a.: not available; ¶annual averages; (1) B-Tables, TGD (1996) when data not available

# Measured local concentrations

Measured atmospheric concentrations in the surroundings of the production sites are available and are presented in Table 3.1.87. Concentrations in the air vary according to the distance from the emission point and the prevailing wind direction. Measured data range from 0.23 ng m-³ to 78 ng m-³. Distances from the point source range from 100 m to 2400 m. Calculated values of these sites vary from 0.6 to 1300 ng m-³ at a distance of 100m from the point source. They are the sum of the calculated local atmospheric concentration, due to plant emission, and the background concentration, which is, according to the TGD (1996), the regional PEC value (0.561 ng m-3, Table 3.1.157). Due to the difference in distance between the measured and calculated values, comparison of both values for each site is not possible. Trends in the measured Cd concentrations over the last decade are presented in Annex 3.1.2.

Table 3.1.87: calculated and measured local PECair concentrations for Cd-producing and processing plants in EU-16.

| use- | N° | production emission | processing emission | PEClocalair | measured ann.avg. air concentration | year |
| --- | --- | --- | --- | --- | --- | --- |
| category |  | amount | amount | (100 m) |  |  |
|  |  | kg y-1 | kg y-1 | ng m-³ | ng m-³ |  |
| Cd-producers | 1 | 54 |  | 42 | 44 (300m, 1993) | 1996 |
|  | 2 | 1683 |  | 1282 | 78 (600m) | 1996 |
|  | 3 | 800 |  | 610 | n.a. | 1996 |
|  | 4 | 3.03 |  | 2.9 | 4 (1000m,1994) | 1996 |
|  | 5 | 946 |  | 721 | 30 (1200 m) | 1996 |
|  | 6 | 6.24 |  | 5.3 | 1 (2400m) | 1996 |
|  | 7£ | 200 |  | 153 | 11 (4000m) | 1996 |
|  | 8 | 28.6 |  | 22 | 11 (300m, 1996) | 1996 |
|  | 9 | 110 |  | 84 | 0.23(2000m,1993) | 1996 |
|  | 10 | 3.32 |  | 3.1 | <40 (100m) | 1996 |
|  | 11 | 1.61 |  | 1.8 | n.a. |  |
|  | 13 | 24.6 |  | 19 | n.a. | 1996 |
| CdO-producers | 11 |  | 0.30 | 0.8 | n.a. | 1996 |
|  | 12 |  | 0.31 | 0.8 | 5.4 (150m, 1994) | 1993 |
| Cd- stabilisers | F |  | 0.09 | 0.6 | n.a. | 1996 |
|  | G |  | 0.8 | 1.2 | n.a. | 1996 |
|  | H |  | 0.5 | 0.9 | n.a. | 1996 |
|  | I |  | 0.1 | 0.6 | n.a. | 1996 |
|  | J |  | 0.7 | 1.1 | n.a. | 1996 |
|  | K |  | 0.04 | 0.6 | n.a. | 1996 |
|  | L |  | n.a. | 0.6 | n.a. | 1996 |
|  | M |  | 0 | 0.6 | n.a. | 1996 |
|  | window manufacturer |  | n.a. | 0.6 | n.a. | 1996 |
| Cd- pigments | A |  | 1.15 | 1.4 | n.a. | 1996 |
|  | B |  | 2.37 | 2.4 | n.a. | 1996 |
|  | C |  | 3.6 | 3.3 | n.a. | 1996 |
|  | D |  | 5.8 | 5.0 | 8 (200 m) | 1996 |
|  | E |  | 0.2 | 0.7 | n.a. | 1996 |
| Cd-plating | EU |  | 0 | 0.6 | n.a. | 1996 |
| Cd-alloys | EU |  | 770 | 587 | n.a. | 1996 |

n.a.=not available; £: the results of recent measurements during February-May 2003 indicate figures of 0.7 to 8.50 ng Cd/m3 (3 month average) (Industry/company data subsmission, Aug. 2004)

##### Terrestrial compartment

# Calculated local concentrations

According to the TGD, the local PECsoil is calculated as an average concentration over a certain time period in agricultural soil, fertilised yearly with sludge from a STP and receiving continuous aerial deposition (dry and wet) from a nearby point source, for a period of 10 years. For the terrestrial ecosystem, the concentration is calculated for a depth of 0.2 m. Sludge from Cd producing plants is however not applied to agricultural land but is recycled internally or by an external plant (IZA-Europe, pers. communication). Application of sludge from processing sites/scenarios is unlikely to take place but may occur if the Cd is emitted via a sewer to a municipal sewage treatment plant. This route of emission is taken into account in the regional assessment as diffuse Cd flux (see section 3.1.3.4.2). Therefore, the Cd input to soil through sludge from the Cd producing plants is omitted in these local calculations and atmospheric deposition is the only source of Cd input into the terrestrial compartment. Atmospheric deposition of Cd is calculated assuming that all Cd is deposited within an area of 100 km2 around the source and that the deposition occurs in a continuous flux.

The PEClocal is the sum of the regional Cd concentration in soil (PECregional) and the atmospheric deposition minus the leaching losses. The PEClocal is solved from the dynamic Cd balance in the 0-0.2 top layer of the soil as:

where

Dair = aerial deposition flux per kg of soil (mg kg-1 d-1)

t = time (3650 d)

k = first order rate constant for removal from top soil (d-1)

PECregionalsoil=the regional Cd concentration in soil (0.36 mg kg-1ww; Table 3.1.157) and which is calculated for an agricultural scenario assuming a realistic worst case Cd input scenario.

The aerial deposition flux is

# DEPtotalann

Dair = —————————

DEPTHsoil * RHOsoil

DEPtotalann = annual average total deposition flux (mg m-2 d-1)

DEPTHsoil = mixing depth of soil (0.20 m)

RHOsoil = bulk density of soil (1700 kg m-3)

Dair = aerial deposition flux per kg of soil (mg kg-1 d-1)

# DEPtotalann = 0.01 (Elocalair + Estpair) * Temission/365

Elocalair = local direct emission rate to air during emission episode (kg d-1)

Estpair = local indirect emission to air from STP during episode (0 kg d-1)

Temission = number of days per year that the emission takes place

DEPtotalann = annual average total deposition flux (mg m-2 d-1)

The factor 0.01 is used in the previous calculation to convert the source strength (kg d-1) to deposition (mg m-2 d-1) assuming a deposition area of 100 km2 (TGD, 1996, p. 300).

Removal from the top soil is by leaching only and the first order rate constant is given as

# Finfsoil * RAINrate/365

k =  ———————————

KD * DEPTHsoil* RHOsoil

Finfsoil = fraction of rain water that infiltrates into soil (0.25)

RAINrate = rate of wet precipitation (700 mm y-1)

KD = solid:liquid Cd distribution in soil (280 L kg-1, see below)

k = pseudo first-order rate constant for leaching from soil layer (d-1)

The solid-liquid Cd distribution coefficient (KD; L kg-1) in soil is defined as

in which [Cd]s represents the Cd concentration in the solid phase of the soil ((g kg-1) and [Cd]l the Cd concentration in pore water (µg L-1) . The Cd KD values vary strongly with soil properties. The Cd KD values have been measured in different soils. Table 3.1.10 lists a number of these studies and shows regression equations between the KD values and soil properties. The KD values are generally obtained from Cd adsorption studies in soil suspensions. Main methodological differences between studies are the type and concentration of the background electrolyte, the solid:liquid ratio and the equilibration time. A variation of about two orders of magnitude of the KD of Cd between different soil types was found. The soil pH is a dominant factor controlling mobility of Cd. From the regression lines between the KD and soil properties (Table 3.1.88) it can be predicted that the KD decreases between 3.2 and 5.1 fold per unit pH decrease. Some studies show that the KD significantly increases if the soil organic matter content increases (Table 3.1.88).

The McBride model was based on data of Gerritse and Van Driel (1984), who measured KD values of Cd for 33 temperate soils, at three different ionic strengths of soils extractants (water extract, dilute salt extract of ionic strength (IS) 0.011M and dilute salt extract of IS 0.11M). The relationship between logKD and pH that was derived for the salt extract of intermediate IS (0.011M) - which best matches the IS of many soil solutions - was in best agreement with the log KD-pH relationships derived by Römkens and Salomons (1998) and Smolders et al. (unpublished) for in situ KD values (Table 3.1.88).  The KD values in the water extract were higher than in the dilute salt extracts, which can be ascribed to a general ionic strength effect. Due to this effect, Cd concentrations in water extracts tend to underestimate the Cd concentrations in the soil solution as the IS is usually lower in a water extract than in the soil solution. It was found for 18 (contaminated) topsoils that the concentration in a water extract was on average 2.4 times lower than the Cd concentration in the pore water (Degryse F, personal communication). As McBride et al. (1997) used the water extract data of Gerritse and Van Driel (1984), their model probably overestimates in situ Kd values and hence underestimates Cd concentrations in the soil solution.

The best estimates on leaching losses are probably made using in situ pore water concentrations, and not using the soluble Cd concentrations in suspension studies. However, no large data sets on in situ KD values are available. In this model KD was assumed 280 L kg-1 which is a typical value for a soil with pH 6.5 and 2% organic matter (the average predicted KD for these characteristics is 500 L kg-1 based on all equations in Table 3.1.88, and 320 L kg-1 without the McBride equation).

Table 3.1.88: the solid-liquid Cd distribution coefficient (KD) in different topsoils†

| KD (L kg-1) | notes | source |
| --- | --- | --- |
| logKD=-1.00+0.51pH+0.51log(%OM) | adsorption KD measured in 0.001M CaCl2, n=63 (Danish agricultural soils, subsoils included) | Christensen, 1989 |
| logKD=0.89+log(%OM/100)+0.52pH | adsorption KD in NaNO3 0.01M, n=15 (soils from New Jersey) | Lee et al. 1996 |
| logKD =-1.8+log(%OM)+0.59pH | adsorption KD in 0.005N salts; n=33 (Dutch, French and British soils, some polluted soils included) | Gerritse and Van Driel, 1984 |
| logKD=-1.16+0.56pH | in situ (pore-water based) KD, n=100 (unpolluted agricultural and forest soils from the Netherlands) | Römkens and Salomons, 1998 |
| log[Cd]S=3.62-0.50pH-0.45log(%OM*10)+0.96log[Cd]Tot | metal concentration in water extract; n=33 (contaminated soils from various sources) | McBride et al., 1997 |
| logKD=-1.34+0.64pH | in situ (pore-water based) KD, n=28 (unpolluted grassland soils from Belgium) | Smolders et al. (unpublished) |
| logKD=-2.09+0.61pH+0.936log(%C) | adsorption KD in CaCl2 0.010M n=58 (unpolluted grassland soils from Belgium) | Smolders et al. (unpublished) |

† the study of Römkens and Salomons (1998) include subsurface horizons.

%OM= percentage organic matter; %C=percentage carbon, [Cd]S=metal concentration in water extract (µg l-1), [Cd]Tot=total metal concentration in soil (mg kg-1)

Results of the calculations are presented in Table 3.1.89. The PECsoil values range from 0.36 mg kgww-1 to 0.85 mg kgww-1.

Table 3.1.89 Calculated total local PECsoil for Cd-producing and processing plants in EU-16. PEC’s include background Cd.

| Use- | Plant N° | Emission | number of | PEClocal soil | Year |
| --- | --- | --- | --- | --- | --- |
| Category |  | to air¶ | emission days(1) |  |  |
|  |  | kg d-1 |  | mg kgww-1 |  |
| Cd-production | 1 | 0.15 | 365 | 0.37 | 1996 |
|  | 2 | 4.6 | 365 | 0.85 | 1996 |
|  | 3 | 11.4 | 70 | 0.59 | 1996 |
|  | 4 | 0.2 | 15 | 0.36 | 1996 |
|  | 5 | 3.9 | 243 | 0.63 | 1996 |
|  | 6 | 0.06 | 105 | 0.36 | 1996 |
|  | 7 | 0.5 | 365 | 0.41 | 1996 |
|  | 8 | 0.2 | 151 | 0.36 | 1996 |
|  | 9 | 0.3 | 365 | 0.39 | 1996 |
|  | 10 | 0.01 | 316 | 0.36 | 1996 |
|  | 11 | 0.05 | 32 | 0.36 | 1996 |
|  | 13 | 0.2 | 123 | 0.36 | 1996 |
| CdO-producers | 11 | 0.001 | 251 | 0.36 | 1996 |
|  | 12 | 0.001 | 256 | 0.36 | 1993 |
| Cd recycling | 1 | 0.02 | 260 | 0.36 | 1996 |
|  | 2 | 0 | 230 | 0.36 | 1997 |
| Cd-stabilisers | F | 0.005 | 20 | 0.36 | 1996 |
|  | G | 0.02 | 48 | 0.36 | 1996 |
|  | H | 0.008 | 60 | 0.36 | 1996 |
|  | I | 0.008 | 13 | 0.36 | 1996 |
|  | J | 0.1 | 13 | 0.36 | 1996 |
|  | K | 0.003 | 12 | 0.36 | 1996 |
|  | L | n.a. | 155 | 0.36 | 1996 |
|  | M | 0 | 155 | 0.36 | 1996 |
|  | window manufacturer | n.a. | 350 | 0.36 | 1996 |
| Cd-pigments | A | 0.01 | 230 | 0.36 | 1996 |
|  | B | 0.01 | 231 | 0.36 | 1996 |
|  | C | 0.01 | 276 | 0.36 | 1996 |
|  | D | 0.03 | 230 | 0.36 | 1996 |
|  | E | 0.002 | 85 | 0.36 | 1996 |
| Cd-plating | EU | 0 | 155 | 0.36 | 1996 |
| Cd-alloys | EU | 12.4 | 62 | 0.58 | 1996 |

n.a.: not available; ¶annual averages; B-Tables (TGD, 1996) when data not available

# Measured local concentrations

At this moment, there are no measured local soil concentrations submitted by the Cd producing- or processing industries.

#### Local exposure assessment: batteries’ related scenarios

Point sources can have a major impact on the environmental concentration on a local scale. Local exposure concentrations are calculated from emission data submitted by Industry (Industry Questionnaires, 2000/2001) according to the EU-Technical Guidelines Document. (TGD, 1996). In this report local PECs are calculated for life cycle stages 1 (Ni-Cd batteries producers) and 4 (Cd recyclers) of the life cycle of Ni-Cd batteries. Local exposure during production of battery raw materials is not considered in this section but is addressed in the section 3.1.3.1. Calculated values will be compared with measured concentrations near Cd emitting plants (Industry Questionnaires, 2000/2001) and where large differences occur, results are analysed and re-evaluated. For the disposal life cycle stage a generic exposure assessment is performed for incineration.

##### Aquatic compartment

- Calculated local concentrations

Input data were submitted via Industry Questionnaires (2000/2001).

Calculation of local PEC-values for the aquatic compartment is performed according to the method described in the TGD (2003). The general lines are the same as those given in the TGD (1996, see section 3.1.3.1.1). However, application of the revised TGD implies a number of changes. These are:

The calculation of the dilution factor is based on the given low-flow rate (or 10th percentile) of the receiving water body and on the given effluent discharge rate. Where only average river flows are available, the flow for dilution purposes should be estimated as one third of this average (EC, 2003). In the absence of both data, a default dilution factor of 10 is used for emissions to freshwater. A default dilution factor of 100 is used for emissions to the sea.

It must be noted that with the assumption of complete mixing of the effluent in the surface water no account is taken of the fact that in reality in the mixing zone higher concentrations will occur. For situations with relatively low dilution factors this mixing zone effect can be accepted. For situations with very high dilution factors, however, the mixing zones may be very long and the overall area that is impacted by the effluent before it is completely mixed can be very substantial. Therefore, in case of site-specific assessments the dilution factor that is applied for calculation of the local concentration in surface water should not be greater than 1000 (EC, 2003).

In short:

The calculated surface water concentrations are actual contributions to the receiving water. The local PEC values are obtained by adding the regional PEC value for water (modelled value) to the calculated local concentration in surface water.

PEClocalwater = Clocalwater + PECregionalwater

PEClocalwater: predicted environmental concentration during emission episode ((g/L )

Clocalwater: local concentration in surface water during emission episode ((g/L)

PECregionalwater: regional concentration in surface water (0.11µg/L, calculated value, no changes made cfr Table 3.157)

In the calculations, a European average value of suspended matter partitioning coefficient: Kp = 130,000 l/kg is used.

The local PEC values of Cd in surface water are presented in Table 3.1.90 and Table 3.1.91.

Table 3.1.90 :	local PECwater for Ni-Cd batteries producing plants and Cd recycling plants in the EU emitting to the surface water after on site WWTP.

| Use category | N° | Production/ processing emission (average) | Ceffluent | Dilution factor Site-specific | Clocal water Site-specific | PEClocalwater Site-specific | Max. Dilution factor (revised TGD) | Clocal water D=1,000 | PEClocalwater D=1,000 | year |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Ni-Cd batteries |  | kg/y | mg/L | - | µg/L | µg/L | - | µg/L | µg/L |  |
|  | 2a | 7.3 | 0.12 | 1,178 | 0.034 | 0.15 | 1,000 | 0.041 | 0.15 | 2000 |
|  | 3 | 30.5 (36,29) | 0.12 | 13,542 | 0.0030 | 0.12 | 1,000 | 0.041 | 0.15 | 2000 |
|  | 4 | 21.9 (31.88) | 0.13 | 771 | 0.06 | 0.18 | N.A. | N.A. | N.A. | 2000 |
|  | 6b | No emissions to water (recycled) | N.A. | N.A. | N.A. | N.A | N.A. | N.A. | N.A. | 1999 |
|  | 7c | No emissions to water (recycled) | N.A. | N.A. | N.A. | N.A. | N.A. | N.A. | N.A. | 1999 |
| Cd recyclersd |  |  |  |  |  |  |  |  |  |  |
|  | 1 | 0.126 | 0.45 | 1,889 | 0.08 | 0.19 | 1,000 | 0.153 | 0.27 | 2000 |
|  | 2d | N.A. | N.A. | N.A. | N.A. | N.A. | N.A. | N.A. | N.A. | 1999 |

N.A:  not applicable

a Company 2 emits to the marine environment.

b All process wastewater is collected and sent to recycling company

c emissions to water from cleaning operations are disposed in alkaline solution and externally recycled

d Only two recyclers (instead of three) have been listed under Cd-recyclers. The reason is that one company is both recycler and producer. A further breakdown in the submitted figures between the producing process and the recycling process was not feasible. For this reason this company have been listed with the other producers.

e No “open” treatment steps; no emissions to air. The wastewater is collected and treated off site. No further information was available. The sludge from the treatment is landfilled.

Plant 1 and plant 5 discharge their effluent after on-site treatment into the public sewer system (STP). These discharges will undergo a dilution step in the STP. The corresponding dilution factor is calculated based on the effluent flow rate and a default sewage flow of 2,000 m3/d. In addition to the dilution factor the cadmium removal efficiency of the STP has to be taken into account. According to CBS (2002) a removal efficiency of 60 % can be used. The final site specific dilution factor is obtained using the site specific flow rate of the receiving surface water and the effluent flow of the STP. The results of the calculations are presented in table 3.1.91.

Table 3.1.91: local PECwater for Ni-Cd batteries producing plants in the EU emitting to the surface water after on site WWTP and followed by STP

| Input | Plant N° 1 | Plant N° 5 |
| --- | --- | --- |
| Reference year |  | 2000 |
| Processing emission (kg/y) | 4.9 | 59.7 |
| Effluent flow (m3/d) | 127 | 5 |
| Conc. effluent (mg/L) | 0.43 | 0.03 |
| Size of STP (m3/d) | 2,000 | 2,000 |
| Removal of cadmium in STP (%) | 60 | 60 |
| Flow rate receiving water (m3/d) | 1.9.106 | 2.2.106 |
| Output |  |  |
| Calculated dilution factor in STP | 16.7 | 401 |
| Calculated conc. effluent STP (mg/L) | 0.010 | 0.00003 |
| Calculated site specific dilution factor in receiving water | 894 | 1,101 |
| Clocal water site specific (µg/L) | 0.0037 | 0.00001 |
| PEClocal water site specific | 0.12 | 0.114 |
| Clocal water (D = 1,000) | N/A. | 0.00001 |
| PEClocal water site (D = 1,000) | N/A | 0.114 |

N/A = not applicab–e.

The local PEC values -calculated on the basis of site-specific dilution factors- range from 0.11 to 0.18 µg L-1 for Ni-Cd batteries producing plants and 0.19 µg L-1 for Cd recycling plants. It should be noted that the 0.11 µg/L value -for Ni-Cd batteries producing plant 5 - equals the regional PEC. The draft revised TGD (2002) states that in case of site-specific assessments the dilution factor that is applied for calculation of the local concentration in surface water should not be greater than 1,000 (assumption of complete mixing, mixing zones). Therefore, for Ni-Cd producing plants 2, 3 and Cd recycling plant 1 a local concentration in surface water is calculated based on the maximum dilution factor of 1,000. The results from this exercise indicate that for these plants the PEC values in surface water equals 0.15 µg/L for the NiCd batteries producing plants and 0.27 µg/L for the Cd recycling plant.

- Measured local concentrations

Monitoring data from Cd-producing plants were submitted via the Industrial Questionnaire (2000/2001). In general, most of these plants have implemented a monitoring program to control the effluent concentrations. Only a limited number of measured Cd concentrations are available in the receiving surface water of the plants. Submitted measured values are generally total concentrations. In order to be able to compare measured and calculated values, total measured values are converted to dissolved values assuming a dissolved fraction of 33% of the total measured Cd concentration. In Table 3.1.92 measured and calculated data are presented as dissolved concentrations.

Table 3.1.92: Measured local Cd concentrations in the effluent receiving water and the local PECwater concentrations for Cd-producing and processing plants in EU.

| Use- | plant N° | Production | Processing | PEClocalwater |  | Year |
| --- | --- | --- | --- | --- | --- | --- |
| category |  | Emission amount | Emission amount | calculated | measured |  |
|  |  | kg/y | kg/y | µg/L | µg/L |  |
| Ni-Cd-batteries | 1g |  | 4.9 | 0.12 | N.A. | 1999 |
|  | 2a |  | 7.3 | 0.15 | 0.153 (P90 downstream of discharge) | 2000 |
|  | 3 |  | 30.5 | 0.15 | N.A. | 2000 |
|  | 4 |  | 21.9 | 0.17 | N.A. | 2000 |
|  | 5 |  | 0.07 | 0.11 | N.A. | 1999 |
|  | 6b |  | No emissions to water (recycled) | N/A | N.A. | 1999 |
|  | 7c |  | No emissions to water (recycled) | N/A | N.A. | 1999 |
| Cd recyclingd | 1 | 0.126 |  | 0.16 | upstream: 75.9 µg/Lf (20 m before emission point) downstream: 85.8 µg/L (80 m after emission point) | 2000 |
|  | 2e | 0 |  | N/A | N.A. | 1999 |

N.A. not available; N/A not applicable

a Company 2  emits to the marine environment.. Measured data from the harbour.

b All process wastewater is collected and sent to recycling company

c emissions to water from cleaning operations are disposed in alkaline solution and externally recycled

d Only two recyclers (instead of three) have been listed under Cd-recyclers. The reason is that one company is both recycler and producer. A further breakdown in the submitted figures between the producing process and the recycling process was not feasible. For this reason this company have been listed with the other producers.

e No “open” treatment steps; no emissions to air. The wastewater is collected and treated off site. No further information was available. The sludge from the treatment is landfilled.

f It should be noted that the river already has high Cd levels (see upstream from discharge) probably due to pollution from old metallic slag heaps.

g company stopped Ni-Cd production

Most of the plants did not have measured data. For plant 2, emitting to the marine environment, measured data were reported. From these data the 90th percentile was taken resulting in a Cd concentration of 0.153 µg/L which is in concordance with the modelled concentration. Recycling plant 1 reported measured Cd concentrations in surface water upstream and downstream from the plant for several years. Although the cadmium concentration downstream increases significantly it is highly unlikely that this increase is caused by a plant emitting 0.126 kg/y with an average effluent flow of 5 m3/d. It is more likely that the elevated cadmium concentrations in the river are due the input from contaminated groundwater and/or run-off water originating from historical metallurgical slag heaps present at the industrial site of the former zinc processing plant.  This hypothesis is supported by the increase in zinc concentration in the same order as cadmium, while the recycling plant does not emit zinc.

MSW incinerator: current situation (24.4% incineration)

Since the collection of site-specific data on MSW incinerators was outside the scope of this report a local scenario have been developed for a hypothetical incinerator based on the information provided in Tables 3.1.25 and  3.1.33. On, average 25 incinerators are present in one region incinerating 2,794 ktonnes of MSW per year which result in an average capacity of 111,760 tonnes MSW/plant.year. The amount of wastewater generated is of the order of 0.5-2.5 m3 per tonne of municipal waste incinerated (Williams, 1998). Reimann (2002) reported a water consumption of 1.1 m3/tonne for the FGCS and 0.25 m3 per tonne boiler water. Stubenvoll et al (2002) reported amounts of waste water between 0.3-0.4 m3 /tonne. If it is assumed that an incinerator is in operation for 330 days per year a daily emission between 169 and 846 m3 can be calculated ((111,760*2.5 (or 0.5)) /330. Using these two values  and assuming a default river flowrate of  18,000 m3/d (TGD default) a generic dilution factor between 22 (=18,846/846) and 107 (= 18,169/169) can be calculated.

Although it was impossible to gather site-specific information for every incinerator in Europe, for some incinerators site-specific information on type of receiving water and flow rate was available  (Table 3.1.93). The dilution factors provided in this table were calculated using the minimum effluent flow of 169 m3/ and the maximum flowrate of 846 m3/d., respectively.

Table 3.1.93: Calculated site specific dilution factors for some MSW incinerators in the EU

| Incinerator | Receiving water | flow rate m³/d | 846 m³/d | 169 m³/d |
| --- | --- | --- | --- | --- |
|  |  |  | Dilution factor |
| United Kingdom |
| Edmonton Incinerator London Waste Ltd | Thames | 5,702,400 | 6,740 | 33,743 |
| Lewisham Incinerator London | Thames | 5,702,400 | 6,740 | 33,743 |
| Stoke on Trent Incinerator MES Environmental Ltd | Trent | 54,432 | 64 | 323 |
| Nottingham Incinerator Waste Recycling Group | Trent | 5,814,000 | 6,872 | 34,403 |
| France |
| Brive | Corrèze | 864,000 | 1,021 | 5,113 |
| Chartres | Eure | 432,000 | 511 | 2,557 |
| Toulouse | Garonne | 17,280,000 | 20,426 | 102,250 |
| Bordeaux | Garonne | 60,480,000 | 71,489 | 357,871 |
| Pau | Gave de Pau | > 57,888 | > 68 | 344 |
| Orléans | Loire | 73,008,000 | 86,298 | 432,001 |
| Angers | Maine | 11,059,200 | 13,072 | 65,440 |
| Chaumont (close to the source) | Marne | 17,280 | 20 | 103 |
| Créteil | Marne (at mouth in Seine) | 4,242,240 – 8,320,320 | 5,014 – 9,835 | 25,103 – 49,234 |
| Caen | Orne | 2,790,720 | 3,299 | 16,514 |
| Maubeuge | Sambre | 43,200 – 259,200 | 51 – 306 | 257 – 1,534 |
| Strasbourg | Rhine | 9,936,000 | 11,745 | 58,794 |
| Lyon Sud | Rhone | 40,262,400 – 49,334,400 | 47,591 – 58,315 | 238,240 – 291,921 |
| Bellegarde | Rhone | 31,104,000 | 36,766 | 184,048 |
| Lyon Nord | Saone | 27,993,600 – 31,795,200 | 33,089 – 37,583 | 165,644 – 188,138 |
| Le Mans | Sarthe | 2,937,600 (à Spay, 5 km van Le Mans) | 3,472 | 17,383 |
| St. Thibault des Vignes Carrières/S. Guerville Issy les Moul. St Ouen Ivry Argenteuil | Seine | 27,648,000 | 32,681 | 1 63,599 |

From the previous table it is clear that a lot of incinerators are discharging their effluents into large rivers frequently resulting in a dilution factor larger than 1,000. In order to obtain both a realistic worst case dilution factor and a typical dilution factor the cumulative distribution function of dilution factors have been elaborated and the 10th percentile and the 50th percentile are taken respectively.

Figure 3.1.11: Cumulative distribution function of dilution factor based on reported flowrates.

From the Figure above it can be calculated that the realistic worst case dilution factors (10th P) range between 93 and 459. Typical dilution factors (50th P) range between 7,370 and 36,840.

In order to take this variation in dilution factors over to the risk characterization phase two scenarios are withheld:

- Realistic worst case dilution factor of 100

- Typical dilution factor of 1,000

As effluent concentration for the local PEC calculations the 90th P value has been chosen of the measured influent concentration and a removal efficiency of  98.8 %.

Effluent concentration  =  0.47 mg Cd/L (90th influent) x (1-0.988) = 0.0056 mg Cd/L

In scenario 1 (DF = 100), the amount of waste water generated is 846 m3/tonne.d With an effluent concentration of 0.0056 mg/L and 330 operating days a yearly load of 1.6 kg can be calculated (846 m3/d x 330 d/y x 0.0056 mg/L = 1.6 kg Cd/y). In a similar way the cadmium load associated with 169 m3 of waste water per day (scenario 2  with DF = 1,000) can be calculated (169 m3/d x 330 d/y x 0.0056 mg/L = 0.3 kg Cd/y).

Table 3.1.94: local PEC water (total cadmium) for MSW incineration plants in the EU

|  | Emission | Ceffluent | Dilution factora | Clocal water | PEClocal water |
| --- | --- | --- | --- | --- | --- |
|  | kg/y | mg/L | - | µg/L | µg/L |
| Scenario 1 | 10h percentile measured dilution factors |
|  | 1.6 | 0.0056 | 100 | 0.019 | 0.13 |
| Scenario 2 | 50th percentile measured dilution factors |
|  | 0.3 | 0.0056 | 1,000 | 0.0019 | 0.12 |

The Cd emissions and the calculated PEClocalwater in Table 3.1.94 represent the impact of all cadmium containing sources in the MSW and not Ni-Cd batteries only. PEClocal surface water of 0.12 µg/L (total cadmium) is calculated for a reasonable worst case scenario (90th P Cd concentration) with a  typical dilution factor of 1,000. This value is very close to the regional background of 0.114 µg/L.. If the calculations are performed with the realistic worst case dilution factor (i.e. 100) PEClocalwater is 0.13 which is only slightly above the regional PEC value (0.114 µg/L),

In order to evaluate if having Ni-Cd batteries in the MSW stream or not significantly influences the PEClocalwater values, these PEClocalwaters have been recalculated assuming in the first scenario that Ni-Cd batteries only contributed 10 % to the overall cadmium content of the waste and in a second scenario it was assumed that Cd from Ni-Cd batteries accounted for 50 % of the total Cd load observed in MSW (Table 3.1.95).

Table 3.1.95: local PEC water (total cadmium without the Ni-Cd contribution) for MSW incineration plants in the EU

|  | Dilution factora | Clocal water | PEClocal water | Dilution factora | Clocal water | PEClocal water |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | µg/L | µg/L | - | µg/L | µg/L |
|  | Assumption Ni-Cd contribution: 10 % of the total Cd load |
| Scenario 1/2 | 100 | 0.017 | 0.13 | 1,000 | 0.002 | 0.11 |
|  | Assumption Ni-Cd contribution: 50 % of the total Cd load |
| Scenario 1/2 | 100 | 0.009 | 0.12 | 1,000 | 0.0009 | 0.11 |

From Table 3.1.95 it is clear that removing the Ni-Cd battery fraction from the MSW does not significantly reduce the PEClocal water. This is not surprisingly since on average 95 % of the PEClocal water is coming from the regional background concentration, which is 0.114 µg/L on a calculated basis.

MSW incinerator scenario sensitivity analysis (effluent concentration = 0.009 mg/L)

As part of the sensitivity analysis (3.1.2.2.5.7) a scenario of a incinerator with a effluent concentration of 0.009 mg/L (derived from the maximum reported influent concentration of 0.76 mg/L and assuming a removal efficiency of 98.8 %) is included (Table 3.1.96).

Effluent concentration  =  0.76 mg Cd/L (max con. influent) x (1-0.988) = 0.009 mg Cd/L

In scenario 1 (DF = 100), the amount of waste water generated is 846 m3/tonne.d With an effluent concentration of 0.009 mg/L and 330 operating days a yearly load of 2.5 kg can be calculated (846 m3/d x 330 d/y x 0.009 mg/L = 2.5 kg Cd/y). In a similar way the cadmium load associated with 169 m3 of waste water per day (scenario 2  with DF = 1,000) can be calculated (169 m3/d x 330 d/y x 0.009 mg/L = 0.5 kg Cd/y).

Table 3.1.96: local PEC water (total cadmium) for MSW incineration plants in the EU

|  | Emission | Ceffluent | Dilution factora | Clocal water | PEClocal water |
| --- | --- | --- | --- | --- | --- |
|  | kg/y | mg/L | - | µg/L | µg/L |
| Scenario 1 | 10h percentile measured dilution factors |
|  | 2.5 | 0.009 | 100 | 0.03 | 0.14 |
| Scenario 2 | 50th percentile measured dilution factors |
|  | 0.5 | 0.009 | 1,000 | 0.003 | 0.12 |

PEClocal surface water of 0.12 µg/L (total cadmium) is calculated for a worst case scenario (max Cd concentration) with a  typical dilution factor of 1,000. This value is very close to the regional background of 0.114 µg/L.. If the calculations are performed with the realistic worst case dilution factor (i.e. 100) PEClocalwater is 0.14 which is only slightly above the regional PEC value (0.114 µg/L),

MSW incinerator: future situation (100 % incineration)

In a similar way the cadmium emission to surface water from future incinerators can be calculated. The assumption has been made that due to expected higher cadmium content in the MSW a higher effluent concentration is expected to occur (this is the case if the removal efficiency will be kept at 98.8 %).  For the two future scenarios the following effluent concentrations have been used to perform the calculations (based on Table 3.1.37):

- For the scenario with 10 % batteries’ collection efficiency the following overall cadmium effluent concentration has been used:  0.0135 mg Cd/L ( = 1.13 * 0.012)

- For the scenario with 75% collection efficiency the following overall cadmium effluent concentration has been used: 0.007 mg Cd/L (= 0.62 * 0.012)

In scenario 1 (DF = 100) for the 10 % collection scenario, the amount of waste water generated is 846 m3/tonne.d With an effluent concentration of 0.0135 mg/L and 330 operating days a yearly load of 3.75 kg can be calculated (846 m3/d x 330 d/y x 0.0135 mg/L = 3.75 kg Cd/y). In a similar way the cadmium load associated with 169 m3 of waste water per day (scenario 2  with DF = 1,000) can be calculated (169 m3/d x 330 d/y x 0.0135 mg/L = 0.75 kg Cd/y).

In scenario 1 (DF = 100) for the 75 % collection scenario, the amount of waste water generated is 846 m3/tonne.d With an effluent concentration of 0.007 mg/L and 330 operating days a yearly load of 1.9 kg can be calculated (846 m3/d x 330 d/y x 0.007 mg/L = 3.75 kg Cd/y). In a similar way the cadmium load associated with 169 m3 of waste water per day (scenario 2  with DF = 1,000) can be calculated (169 m3/d x 330 d/y x 0.0135 mg/L = 0.75 kg Cd/y).

Table 3.1.97 Local PECwater for MSW incineration plants in the EU. Future scenarios:      collection rate: 10 % and 75% (total cadmium )

| Use category | Emission | Ceffluent | Dilution factor | Clocal water | PEClocalwater |
| --- | --- | --- | --- | --- | --- |
|  | kg/y | mg/L | - | µg/L | µg/L |
| MSW Incineration plant (10% collection; total cadmium) | 3.75 | 0.0135 | 100 | 0.045 | 0.16 |
|  | 0.75 | 0.0135 | 1,000 | 0.0046 | 0.12 |
| MSW Incineration plant (75% collection; total cadmium) | 1.9 | 0.007 | 100 | 0.023 | 0.14 |
|  | 0.4 | 0.007 | 1,000 | 0.0023 | 0.12 |

A PEClocal surface water28 of 0.12 µg/L (total cadmium) under a collection scenario of 10 %. And 75 % is calculated for a scenario in which a dilution factor of 1,000 is relevant. For the realistic worst case (DF = 100) PEC local water varies between 0.14 and 0.16 µg/L for the respective scenarios of 75 % collection and 10 % collection.

In case the Ni-Cd batteries would be completely removed from the MSW stream (for the 10 % collection scenario the contribution of Ni-Cd batteries is 63 % and for the 75 % collection scenario a contribution of 32 % is assumed) similar PEClocal water values as presented in Table 3.1.89, for the assumption that Ni-Cd batteries contributed in the current situation only 10 % of the total cadmium load, are obtained.

Landfill current situation (leachate concentration = 5 µg/L)

In the following paragraph the results from the local exposure assessment for a generic landfill (life cycle stage 5: disposal; landfills Table 3.1.50) are presented. Since the collection of site specific data on landfills was out of the scope of this report, local PEC values have been calculated for two hypothetical sites:

- Scenario 1: a landfill where the collected landfill leachate is discharged directly in the surface water

- Scenario 2: a landfill where the collected landfill leachate is discharged into a municipal STP before going into the surface water

The contamination of the groundwater compartment (PEC groundwater, added) due to fugitive emissions of landfills has not been quantified on a local scale in this report since no guidance is available to perform these calculations.

In the case of scenario 1 (direct discharge to surface water) a generic dilution factor can be calculated from the leachate volume generated daily (100 m3/d see section 3.1.2.2.5.6) and the default flowing rate of a river being 18,000 m3/d resulting in a dilution factor of 180.

In scenario 2 the landfill leachate is discharged in the public sewer system (STP). These discharges will undergo a dilution step in the STP. The corresponding dilution factor is calculated based on the landfill effluent flow rate and a default sewage flow of 2,000 m3/d. In addition to the dilution factor the cadmium removal efficiency of the STP has to be taken into account. According to CBS (2002) a removal efficiency of 60 % can be used for STP's. Finally the effluent of the STP is diluted in the receiving water. For the latter a default dilution factor of 10 can be used (based on a default flow rate of the receiving surface water of 18,000 m3/d and a default effluent flow of the STP of 2,000 m3). The results of the calculations are presented in Table 3.1.98.

Table 3.1.98: Local PEC water for MSW landfills emitting directly to the surface water (scenario 1) or indirectly through a STP (scenario 2). Cadmium leachate concentration is 5 µg/L. Current scenario.

| Input | Scenario 1 | Scenario 2 |
| --- | --- | --- |
| Effluent Flow (m3/d) | 100 | 100 |
| Conc. effluent (µg/L) | 5 | 5 |
| Size of STP (m3/d) | N/A | 2,000 |
| Removal of cadmium in STP (%) | N/A | 60 |
| Flow rate receiving water (m3/d) | 18,000 | 18,000 |
| Dilution factor from STP to river | N/A | 10 |
| Output |  |  |
| Calculated dilution factor in STp | N/A | 21 |
| Calculated conc. effluent STP (µg/L) | N/A | 0.095 |
| Calculated generic dilution factor in receiving water | 180 | 10 |
| Clocal water generic (µg/L) | 0.009 | 0.003 |
| PEClocal water generic | 0.12 | 0.12 |

N/A = not applicable.

Table 3.1.99 : 	Local PEC water for MSW landfills emitting directly to the surface water (scenario 1) or indirectly through a STP (scenario 2: STP). Cadmium leachate concentration is 5 µg/L. Total cadmium.

| Use category | Ceffluent | Dilution factora | Clocal water | PEClocalwater |
| --- | --- | --- | --- | --- |
|  | mg/L | - | µg/L | µg/L |
| Scenario 1 (direct discharge, no STP) |  |  |  |  |
| MSW Landfill (total cadmium) | 0.005 | 180 | 0.009 | 0.12 |
| Scenario 2 ( STP) |  |  |  |  |
| MSW Landfill (total cadmium) | 0.005 | 10 | 0.003 | 0.12 |

a  dilution in receiving water

A PEClocal surface water of 0.12 (total cadmium) is calculated for both scenarios which is only slightly above the regional PEC (= 0.11 µg/L).

In case all Ni-Cd batteries would be removed from the MSW the influence on the PEClocal water would be negligible (Table 3.1.100).

Table 3.1.100 : Local PEC water for MSW landfills emitting directly to the surface water (scenario 1) or indirectly through a STP (scenario 2: STP). Cadmium leachate concentration is 5 µg/L. Total cadmium without the Ni-Cd contribution.

| Use category | Ceffluent | Dilution factora | Clocal water | PEClocalwater |
| --- | --- | --- | --- | --- |
|  | mg/L | - | µg/L | µg/L |
| Scenario 1 (direct discharge, no STP) |  |  |  |  |
| MSW Landfill (Ni-Cd batteries contributed for 10 %) | 0.0045 | 180 | 0.008 | 0.12 |
| MSW Landfill (Ni-Cd batteries contributed for 50 %) | 0.003 | 180 | 0.005 | 0.12 |
| Scenario 2 (STP) |  |  |  |  |
| MSW Landfill (Ni-Cd batteries contributed for 10 %) | 0.0045 | 10 | 0.003 | 0.12 |
| MSW Landfill (Ni-Cd batteries contributed for 50 %) | 0.003 | 10 | 0.002 | 0.12 |

a  dilution in receiving water

Landfill  scenario sensitivity analysis (leachate concentration = 50 µg/L)

As part of the sensitivity analysis (3.1.2.2.5.7) a scenario of a landfill with a leachate concentration of 50 µg/L is included. As is the case in the previous paragraph both a landfill with and without a STP is being considered.

Table 3.1.101: local PEC water for landfills emitting directly to the surface water (scenario 1) or indirectly through a STP (scenario 2). Cadmium leachate concentration is 50 µg/L

| Input | Scenario 1 | Scenario 2 |
| --- | --- | --- |
| Effluent Flow (m3/d) | 100 | 100 |
| Conc. effluent (µg/L) | 50 | 50 |
| Size of STP (m3/d) | N/A | 2,000 |
| Removal of cadmium in STP (%) | N/A | 60 |
| Flow rate receiving water (m3/d) | 18,000 | 18,000 |
| Dilution factor from STP to river | N/A | 10 |
| Output |  |  |
| Calculated dilution factor in STp | N/A | 21 |
| Calculated conc. effluent STP (µg/L) | N/A | 0.95 |
| Calculated generic dilution factor in receiving water | 180 | 10 |
| Clocal water generic (µg/L) | 0.094 | 0.032 |
| PEClocal water generic | 0.21 | 0.15 |

N/A = not applicable.

Table 3.1.102 : Local PECwater for MSW landfills emitting directly to the surface water (scenario 1) or indirectly through a STP (scenario 2). Cadmium leachate concentration is 50 µg/L. Total cadmium.

| Use category | Cleachate | Dilution factora | Clocal water | PEClocalwater |
| --- | --- | --- | --- | --- |
|  | mg/L | - | µg/L | µg/L |
| Scenario 1 (direct discharge, no STP) |  |  |  |  |
| MSW Landfill (total cadmium) | 0.05 | 180 | 0.094 | 0.21 |
| Scenario 2 ( STP) |  |  |  |  |
| MSW Landfill (total cadmium) | 0.05 | 10 | 0.032 | 0.15 |

a  dilution in receiving water

A PEClocal surface water of 0.21µg/L (total cadmium) is calculated for landfill sites that discharge directly in surface water. In case the landfill discharged to a STP an overall PEC of 0.15 µg/L is obtained.

In case all Ni-Cd batteries would be removed from the MSW the influence on the PEClocal water would be negligible at the exception of the case where Ni-Cd batteries as to their Cd content contribute to 50% of the MSW (Table 3.1.103). In the latter case, direct discharge of leachate from MSW landfills would no longer result in risk.

Table 3.1.103 : Local PECwater for MSW landfills emitting directly to the surface water (scenario 1) or indirectly through a STP (scenario 2). Cadmium leachate concentration is 50 µg/L. Total cadmium without the Ni-Cd contribution.

| Use category | Cleachate | Dilution factora | Clocal water | PEClocalwater |
| --- | --- | --- | --- | --- |
|  | mg/L | - | µg/L | µg/L |
| Scenario 1 (direct discharge, no STP) |  |  |  |  |
| MSW Landfill (Ni-Cd batteries contributed for 10 %) | 0.045 | 180 | 0.085 | 0.20 |
| MSW (Ni-Cd batteries contributed for 50 %) | 0.025 | 180 | 0.047 | 0.16 |
| Scenario 2 ( STP) |  |  |  |  |
| MSW Landfill (Ni-Cd batteries contributed for 10 %) | 0.045 | 10 | 0.028 | 0.14 |
| MSW Landfill MSW (Ni-Cd batteries contributed for 50 %) | 0.025 | 10 | 0.016 | 0.13 |

a  dilution in receiving water

##### Sediment compartment

The PEClocalsediment is calculated according to the formula presented below (see section 3.1.3.1.2):

PEClocalsediment = PECregionalsediment + Kp Clocal water. 10-3

in which the Kp (L kg-1dw) equals the solid- water partition coefficient of suspended matter (Kp = 130,000 L kg-1dw).

The measured PEC regional as mentioned in section 3.1.3.4.3 is taken as an average of 90th percentiles of different surveys (Flanders, France, The Netherlands, Spain and Sweden) and is 2.66 mg/kg dry wt. (Table 3.1.189). This value represents a realistic worst case for the EU ambient Cd concentrations in sediment (natural Cd + historical Cd) and is used as the PECregional in the risk characterisation.

The local PECsediment  are readily calculated from the data in Table 3.1.90 and the aforementioned equation and  presented in Table 3.1.104. The Clocalsediment (Kp Clocal water. 10-3) is included to illustrate the contribution of the local discharge onto the sediment PEC.

The local PECsediment range from 2.66 (i.e. the PECregional) to 10.46 mg/kg dry wt. for Ni-Cd batteries-producing plants and is 22.6 mg/kg dry wt. for one Cd-recycling plant. Local sediment concentrations calculated for plants 2, 3 and recycler 1 are on the basis of the maximum dilution factor of 1,000.

Table 3.1.104 : local PECsediment for Ni-Cd batteries producing plants and Cd recycling plants in the EU (without correction for bioavailability)

| Use category | N° | Production emission | Processing emission | Clocal sediment D=1,000 or site specific | PEClocalsediment D=1,000 or site specific | year |
| --- | --- | --- | --- | --- | --- | --- |
| NiCd batteries |  | kg/y | kg/y | mg/kg dry wt | mg/kg dry wt. |  |
|  | 1 |  | 4.9 | 0.5 | 3.16 | 1999 |
|  | 2a |  | 7.3 | 5.3 | 7.96 | 2000 |
|  | 3 |  | 30.5 | 5.3 | 7.96 | 2000 |
|  | 4 |  | 21.9 | 7.8 | 10.46 | 2000 |
|  | 5 |  | 0.07 | 0.003 | 2.66 | 1999 |
|  | 6b |  | No emissions to water (recycled) | N/A | N/A | 1999 |
|  | 7c |  | No emissions to water (recycled) | N.A | N/A | 1999 |
| Cd recyclersd | 1 | 0.126 |  | 19.9 | 22.6 | 2000 |
|  | 2e | 0 |  | N/A | N/A | 1999 |

N.A. not available, N/A not applicable

a Company 2 emits to the marine environment.

b All process wastewater is collected and sent to recycling company.

c emissions to water from cleaning operations are disposed in alkaline solution and externally recycled

d Only two recyclers (instead of three) have been listed under Cd-recyclers. The reason is that one company is both recycler and producer. A further breakdown in the submitted figures between the producing process and the recycling process was not feasible. For this reason this company have been listed with the other producers.

e No “open” treatment steps; no emissions to air. The wastewater is collected and treated off site. No further information was available. The sludge from the treatment is landfilled.

MSW incinerator: current situation

The local PEC sediment was calculated for two scenarios (dilution factor 100 and 1,000) (Table 3.1.105)

Table 3.1.105: local PECsediment for MSW incineration plants in the EU (without  correction for bioavailability)

|  | Emission | Dilution factor | Clocal water | Clocal sediment | PEClocal sediment |
| --- | --- | --- | --- | --- | --- |
|  | kg/y |  | µg/L | mg/kg dry wt. | mg/kg dry wt. |
| Scenario 1 | 10h percentile measured dilution factors |
|  | 1.6 | 100 | 0.019 | 2.53 | 5.19 |
| Scenario 2 | 50th percentile measured dilution factors |
|  | 0.3 | 1,000 | 0.0019 | 0.25 | 2.91 |

The Cd emissions and the calculated PEClocal sediment in Table 3.1.105 represent the impact of all cadmium containing sources in the MSW and not Ni-Cd batteries only. PEClocal sediment value  of 2.91 mg/kg. dry wt (total cadmium) is calculated for the typical  scenario (dilution factor of 1,000) which is very close to the regional background of 2.66 mg/kg dry wt. If the calculations are performed with the realistic worst case dilution factor (i.e. 100) PEClocal sediment is 5.19 mg/kg dry wt.

Similar to the aquatic compartment the PEClocalsediment has also been calculated for the assumption that all Ni-Cd batteries would be removed from the MSW waste stream (Table 3.1.106).

Table 3.1.106: Local PEC sediment (total cadmium without the Ni-Cd contribution) for MSW incineration plants in the EU (without correction for bioavailability)

|  | Dilution factora | Clocal sediment | PEClocal sediment | Dilution factora | Clocal sediment | PEClocal sediment |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | mg/kg dry wt. | mg/Kg dry wt. | - | mg/kg dry wt. | mg/kg dry wt. |
|  | Assumption Ni-Cd contribution: 10 % of the total Cd load |
| Scenario 1/2 | 100 | 2.21 | 4.87 | 1,000 | 0.03 | 2.69 |
|  | Assumption Ni-Cd contribution: 50 % of the total Cd load |
| Scenario 1/2 | 100 | 1.17 | 3.93 | 1,000 | 0.13 | 2.79 |

From Table 3.1.106 it is clear that removing the Ni-Cd battery fraction from the MSW does not have a large impact on the calculated PEC sediment values. For those scenarios with a dilution factor of 1,000 the cadmium sediment concentrations are similar (2.69-2.79). If a dilution factor of 100 is applied the calculated sediment concentration is only slightly lower (3.93 vs 4.87)  when is is assumed that Ni-Cd batteries contribute for 50 % of  the total cadmium load.

MSW incinerator scenario sensitivity analysis (effluent concentration = 0.009 mg/L)

The local PEC sediment was also calculated for the scenario developed with the maximum effluent concentration (i.e. 0.009 mg/L) (Table 3.1.107) as part of the sensitivity analysis.

Table 3.1.107: local PECsediment (without correction for bioavailability) for MSW incineration plants in the EU

|  | Emission | Dilution factor | Clocal water | Clocal sediment | PEClocal sediment |
| --- | --- | --- | --- | --- | --- |
|  | kg/y |  | µg/L | mg/kg dry wt. | mg/kg dry wt. |
| Scenario 1 | 10h percentile measured dilution factors |
|  | 2.5 | 100 | 0.03 | 3.95 | 6.6 |
| Scenario 2 | 50th percentile measured dilution factors |
|  | 0.5 | 1,000 | 0.003 | 0.39 | 3.1 |

PEClocal sediment value of 3.1 mg/kg. dry wt (total cadmium) is calculated for the typical  scenario (dilution factor of 1,000) which is very close to the regional background of 2.66 mg/kg dry wt. If the calculations are performed with the realistic worst case dilution factor (i.e. 100) PEClocal sediment is 6.6 mg/kg dry wt.

MSW incinerator: future situation

Table 3.1.108: Local PECsediment (without correction for bioavailability) for a generic MSW incineration plant in the EU. Future scenarios: collection rate: 10 and 75%. Total cadmium

| Use category | Emission | Dilution factor | Clocal water | Clocal sediment | PEClocal sediment |
| --- | --- | --- | --- | --- | --- |
|  | kg/y | - | µg/L | mg/kg dry wt | mg/kg.dry wt |
| MSW Incineration plant (10% collection; total cadmium) | 3.75 | 100 | 0.0455 | 5.9 | 8.6 |
|  | 0.75 | 1,000 | 0.0046 | 0.6 | 3.3 |
| MSW Incineration plant (75% collection; total cadmium) | 1.9 | 100 | 0.023 | 4.2 | 6.8 |
|  | 0.4 | 1,000 | 0.0023 | 0.3 | 3.0 |

The results from the local exposure assessment for MSW incineration plants predict a PEClocal sediment of 3.0-3.3 mg/kg dry wt. (total cadmium) for the different future scenarios (collection rate: 75% and 10 % respectively) if a dilution factor of 1,000 is relevant. In case only a dilution factor of 100 can be applied PEClocal sediment varies between 6.8 and 8.6 mg/kg dry wt.

In case the Ni-Cd batteries would be completely removed from the MSW stream (for the 10 % collection scenario the contribution of Ni-Cd batteries is 63 % and for the 75 % collection scenario a contribution of 32 % is assumed) similar  PEClocal sediment values as presented in Table 3.1.106, for the assumption that Ni-Cd batteries contributed in the current situation only 10 % of the total cadmium load, are obtained.

Landfill current situation

Table 3.1.109: Local PEC sediment (without correction for bioavailability) for MSW landfills emitting directly to the surface water (scenario 1) or indirectly through a STP (scenario 2: STP). Cadmium leachate concentration is 5 µg/L.

| Use category | Dilution factora | Clocal water | Clocal sediment | PEClocal sediment |
| --- | --- | --- | --- | --- |
|  | - |  | mg/kg dry wt. | mg/kg dry wt. |
| Scenario 1 (direct discharge, no STP) MSW Landfill (total cadmium) | 180 | 0.009 | 1.17 | 3.8 |
| Scenario 2 (STP) MSW Landfill (total cadmium) | 10 | 0.003 | 0.39 | 3.1 |

a  dilution in receiving water

The results from the local exposure assessment for MSW landfills show a PEClocal sediment of 3.1  mg/kg.dry wt. (total cadmium) if the leachate is sent to an STP and 3.8 mg/kg dry wt. if there is no STP.

In case all Ni-Cd batteries would be removed from the MSW the influence on the PEClocal sediment would be negligible (Table 3.1.110).

Table 3.1.110 : Local PEC sediment (without correction for bioavailability) for MSW landfills emitting directly to the surface water (scenario 1) or indirectly through a STP (scenario 2: STP). Cadmium leachate concentration is 5 µg/L. Total cadmium without the Ni-Cd contribution.

| Use category | Dilution factora | Clocal water | Clocal sediment | PEClocal sediment |
| --- | --- | --- | --- | --- |
|  | - | µg/L | mg/kg dry wt | mg/kg dry wt |
| Scenario 1 (direct discharge, no STP) |  |  |  |  |
| MSW Landfill (Ni-Cd batteries contributed for 10 %) | 180 | 0.008 | 1 | 3.7 |
| MSW Landfill (Ni-Cd batteries contributed for 50 %) | 180 | 0.005 | 0.65 | 3.3 |
| Scenario 2 (STP) |  |  |  |  |
| MSW Landfill (Ni-Cd batteries contributed for 10 %) | 10 | 0.003 | 0.39 | 3.1 |
| MSW Landfill (Ni-Cd batteries contributed for 50 %) | 10 | 0.002 | 0.26 | 2.9 |

a  dilution in receiving water

Landfill  scenario sensitivity analysis (leachate concentration = 50 µg/L)

As part of the sensitivity analysis (3.1.2.2.5.7) a scenario of a landfill with a leachate concentration of 50 µg/L is included. As is the case in the previous paragraph both a landfill with and without a STP is being considered.

Table 3.1.111 : Local PECsediment (without correction for bioavailability) for MSW landfills emitting directly to the surface water (scenario 1) or indirectly through a STP (scenario 2). Cadmium leachate concentration is 50 µg/L. Total cadmium.

| Use category | Dilution factora | Clocal water | Clocal sediment | PEClocal sediment |
| --- | --- | --- | --- | --- |
|  | - | µg/L | mg/kg dry wt. | mg/kg dry wt. |
| Scenario 1 (direct discharge, no STP) MSW Landfill (total cadmium) | 180 | 0.094 | 12.2 | 14.9 |
| Scenario 2 (STP) MSW Landfill (total cadmium) | 10 | 0.032 | 4.2 | 6.8 |

a  dilution in receiving water

The results from the local exposure assessment for MSW landfills with a leachate concentration of 50 µg Cd/L show a PEClocal sediment of 6.8 mg/kg dry wt. (all waste) if the leachate is sent to an STP and 14.9 mg/kg dry wt. if there is no STP.

Table 3.1.112 : Local PEC sediment (without correction for bioavailability) for MSW landfills emitting directly to the surface water (scenario 1) or indirectly through a STP (scenario 2: STP). Cadmium leachate concentration is 50 µg/L. All cadmium without the Ni-Cd contribution.

| Use category | Dilution factora | Clocal water | Clocal sediment | PEClocal sediment |
| --- | --- | --- | --- | --- |
|  | - | µg/L | mg/kg dry wt | mg/kg dry wt |
| Scenario 1 (direct discharge, no STP) |  |  |  |  |
| MSW Landfill (Ni-Cd batteries contributed for 10 %) | 180 | 0.085 | 11.1 | 13.7 |
| MSW Landfill (Ni-Cd batteries contributed for 50 %) | 180 | 0.047 | 6.1 | 8.8 |
| Scenario 2 (STP) |  |  |  |  |
| MSW Landfill (Ni-Cd batteries contributed for 10 %) | 10 | 0.028 | 3.6 | 6.3 |
| MSW Landfill (Ni-Cd batteries contributed for 50 %) | 10 | 0.016 | 2.1 | 4.7 |

a  dilution in receiving water

For the scenario with a direct discharge of a leachate cadmium concentration of 50 µg/L the PEClocal sediment originating from cadmium emitting sources other than Ni-Cd batteries is predicted to range between 8.8 and 13.7 mg/kg dry wt. If the landfill leachate is sent to an STP for treatment the local sediment concentrations range between 4.7-6.3 mg/kg dry wt.

##### Atmospheric compartment

- Calculated local concentrations

Local PEC-values for the atmospheric compartment are calculated according to the OPS model proposed in the TGD (1996) for a general standard environment (see section 3.1.3.1.3).

Input data are the total daily emissions of the individual Ni-Cd batteries-producing plants and Cd recycling plants (Industry questionnaires 1999/2000). The calculated concentrations in air are actual contributions to the receiving atmosphere. The local PEC values are obtained by adding the regional PEC values for air to the calculated local concentration in the atmosphere.

PEClocalair = Clocalair + PECregionalair

PEClocalair: 	predicted environmental concentration in air during emission episode (ng/m3)

Clocalair: 	local concentration in the air during emission episode (ng/m3)

PECregionalair: 	regional concentration in the air (0.561 ng/m3)

The results of the predicted local atmospheric Cd concentrations at 100 m from the point sources are listed in Table 3.1.113 Reported data are based on new emission data from Industry Questionnaire, 2000/2001. Calculated local PEC values range from 0.561 to 22.6 ng/m³ for Ni-Cd batteries producers and from 0.561 to 1.91 ng/m3 for Cd recycling plants. It should be noted that for producing company 1 and 3 it was stated that emissions to air were negligible and mainly through effluents. Recycler 2 also declared that there are no “open treatment” steps in its procedure, so there are no stack emissions to air.

Table 3.1.113: Calculated local PECair concentrations for Ni-Cd batteries producing plants and Cd recycling plants in the EU

| Use category | Plant n° | Production emission amount (kg/y) | Processing emission amount (kg/y) | Number of emission days (d) | Annual average air concentration (100 m) ng/m3 | PEClocal air (100 m) ng/m3 | Year |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Ni-Cd batteries |  |  |  |  |  |  |  |
|  | 1 |  | N.A. | 225 | N.A. | 0.561 | 1999 |
|  | 2a |  | 1.6 | 330 | 1.22 | 1.78 | 2000 |
|  | 3b |  | N.A. | 315 | N.A. | 0.561 | 2000 |
|  | 4 |  | 13.5 | 330 | 10.28 | 10.9 | 2000 |
|  | 5 |  | 7 | 230 | 5.3 | 5.9 | 1999 |
|  | 6 |  | 0.036 | 250 | 0.03 | 0.64 | 1999 |
|  | 7 |  | 28.99 | 300 | 22.1 | 22.64 | 1999 |
| Cd recyclersc |  |  |  |  |  |  |  |
|  | 1 | 1.77 |  | 350 | 1.35 | 1.91 | 2000 |
|  | 2 d | 0 |  | 240 | 0 | 0.561 | 1999 |
| Total |  |  | > 53 |  |  |  |  |

N.A. not available

a Company 2 emits to the marine environment.

b wet processes. Mainly emissions to effluents.

e Only two recyclers (instead of three) have been listed under Cd-recyclers. The reason is that one company is both recycler and producer. A further breakdown in the submitted figures between the producing process and the recycling process was not feasible. For this reason this company have been listed with the other producers.

dNo “open” treatment steps; no emissions to air.

- Measured local concentrations

Measured atmospheric concentrations in the surroundings of the production sites are scarce and are presented in Table 3.1.114.

From this table it can be concluded that the measured data at a distance of 100 from the point source for plant 4 and plant 6 are in the same order of magnitude as the calculated data (4 ng/m3 versus 10.9 ng/m3 and 0.7 ng/m3 versus 0.64 ng/m3 respectively).

Table 3.1.114: Calculated and measured local PECair concentrations for Ni-Cd producing             and Cd recycling plants in EU.

| use- | N° | production emission | processing emission | PEClocalair | measured ann.avg. air concentration | year |
| --- | --- | --- | --- | --- | --- | --- |
| category |  | amount | amount |  |  |  |
|  |  | kg/y | kg /-1 | (100 m) ng/m³ | ng/m³ |  |
| NiCd-batteries | 1 |  | N.A. | 0.56 | N.A. | 1999 |
|  | 2a |  | 1.6 | 1.78 | N.A | 2000 |
|  | 3b |  | N.A. | 0.56 | N.A. | 2000 |
|  | 4 |  | 13.5 | 10.9 | 4 (100 m from plant) | 2000 |
|  | 5 |  | 7 | 5.9 | N.A. | 1999 |
|  | 6 |  | 0.036 | 0.64 | 0.7 (0.2-2.5) (100 m from plant) | 1999 |
|  | 7 |  | 28.99 | 22.64 | N.A. | 1999 |
| Cd recyclingc | 1 | 1.77 |  | 1.91 | N.A. | 2000 |
|  | 2d | 0 |  | 0.56 | N.A. | 1999 |

N.A. not available

a Company 2 emits to the marine environment.

b wet processes. Mainly emissions to effluents.

c Only two recyclers (instead of three) have been listed under Cd-recyclers. The reason is that one company is both recycler and producer. A further breakdown in the submitted figures between the producing process and the recycling process was not feasible. For this reason this company have been listed with the other producers.

d No “open” treatment steps; no emissions to air.

MSW incinerator: current situation

In the following section the results from the local exposure assessment for MSW incineration plants (life cycle stage 5: disposal; incineration) is presented. The local air emission for incineration plants is calculated using an allocation key based on the number of incinerators in each country and the country specific air emission amounts. The results presented below are based on emission data for incineration scenario 24.4 % only (realistic case); it is assumed that for incineration scenario 100% (worst case), taking into account a proportional increase in incineration plants over Europe, analogous results can be expected.

Table 3.1.115: Calculated local PECair concentration for MSW incineration plant in the EU). Current situation. Total cadmium

| Country | Emission amount | Number of emissions days | Annual average air concentration (100 m) | PEClocal air (100m) |
| --- | --- | --- | --- | --- |
|  | kg/y | d | ng/m3 | ng/m3 |
| Austria | 1.4c | 330 | 1.07 | 1.63 |
| Belgium | 3.5 | 330 | 2.7 | 3.2 |
| Denmark | 9.7 | 330 | 7.4 | 8.0 |
| Finland | 14 | 330 | 10.7 | 11.2 |
| Francea | 16.4 | 330 | 12.5 | 13.1 |
| Franceb | 36.7 | 330 | 27.95 | 28.5 |
| Germany | 5 | 330 | 3.8 | 4.4 |
| Italy | 5.7 | 330 | 4.3 | 4.9 |
| Luxembourg | 22 | 330 | 16.8 | 17.3 |
| Netherlands | 4.8 | 330 | 3.7 | 4..2 |
| Norway | 5.1 | 330 | 3.9 | 4.5 |
| Portugal | 1.6 | 330 | 1.2 | 1.8 |
| Spain | 6.8 | 330 | 5.2 | 5.7 |
| Sweden | 0.2 | 330 | 0.2 | 0.7 |
| UK | 1.5 | 330 | 1.1 | 1.7 |
| EU 10% scenario | 9.1 | 330 | 6.9 | 7.5 |

a generic scenario

b based on P90 measured data

c according to the latest information (Stubenvoll et al., 2002) total Cd emissions in Austria from incinerators amount to 4.2 kg. Since there is a total of 3 plants, on average, 1.4 kg per plant is emitted

From this table it can be concluded that the PEClocal in air at a distance of 100 from the point source of the incineration plant range between 0.7 and 28.5 ng/m3 (7.5 ng/m3 for the average EU situation). It should be noted that this concentration is valid for all MSW incinerated (not exclusively batteries). The influence of removing the Ni-Cd batteries on the overall emissions is given in Table 3.1.116.

Table 3.1.116: Calculated local PECair concentration for MSW incineration plant in the EU). Current situation. Total cadmium without the Ni-Cd contribution.

| Country | Emission amount | Number of emissions days | Annual average air concentration (100 m) | PEClocal air (100m) |
| --- | --- | --- | --- | --- |
|  | kg/y | d | ng/m3 | ng/m3 |
|  | Assumption Ni-Cd contribution: 10 % of the total Cd load |
| Austria | 1.26 | 330 | 1.0 | 1.5 |
| Belgium | 3.2 | 330 | 2.4 | 3.0 |
| Denmark | 8.7 | 330 | 6.3 | 7.2 |
| Finland | 12.6 | 330 | 9.6 | 10.2 |
| Francea | 14.7 | 330 | 11.2 | 11.8 |
| Franceb | 33 | 330 | 25.1 | 25.7 |
| Germany | 4.5 | 330 | 3.4 | 4.0 |
| Italy | 5.1 | 330 | 3.9 | 4.5 |
| Luxembourg | 19.8 | 330 | 15.1 | 15.6 |
| Netherlands | 4.3 | 330 | 3.3 | 3.8 |
| Norway | 4.6 | 330 | 3.5 | 4.1 |
| Portugal | 1.4 | 330 | 1.1 | 1.6 |
| Spain | 6.1 | 330 | 4.7 | 5.2 |
| Sweden | 0.18 | 330 | 0.14 | 0.7 |
| UK | 1.4 | 330 | 1.1 | 1.6 |
| EU 10% scenario | 8.2 | 330 | 6.3 | 6.8 |
|  | Assumption Ni-Cd contribution: 50 % of the total Cd load |
| Country | Emission amount | Number of emissions days | Annual average air concentration (100 m) | PEClocal air (100m) |
|  | kg/y | d | ng/m3 | ng/m3 |
| Austria | 0.7 | 330 | 1.07 | 1.63 |
| Belgium | 1.8 | 330 | 1.4 | 1.9 |
| Denmark | 4.9 | 330 | 3.7 | 4.2 |
| Finland | 7 | 330 | 5.4 | 5.9 |
| Francea | 8.3 | 330 | 6.3 | 6.8 |
| Franceb | 18.4 | 330 | 14 | 14.6 |
| Germany | 2.5 | 330 | 1.9 | 2.4 |
| Italy | 2.9 | 330 | 2.2 | 2.7 |
| Luxembourg | 11 | 330 | 8.4 | 8.9 |
| Netherlands | 2.4 | 330 | 1.9 | 2.4 |
| Norway | 2.5 | 330 | 2.0 | 2.5 |
| Portugal | 0.8 | 330 | 0.6 | 1.1 |
| Spain | 3.4 | 330 | 2.6 | 3.1 |
| Sweden | 0.1 | 330 | 0.1 | 0.6 |
| UK | 0.8 | 330 | 0.6 | 1.1 |
| EU 10% scenario | 4.5 | 330 | 3.5 | 4.0 |

a generic scenario

b based on P90 measured data

Removing  the contribution from Ni-Cd batteries to the MSW (10-50 %), PEC local in air range between 0.6 and 25.7 ng/m3.

For the future and the 100 % incineration scenarios it is assumed that the number of incineration plants is proportionally increased to the amount of MSW to incinerate. And since higher local air emissions due to higher cadmium content of the MSW are not expected to occur when the FGCS are working well (shift of the cadmium to incineration residues) Table 3.1.111 can also be used for these scenarios.

##### Terrestrial compartment

- Calculated local concentrations

According to the TGD, the local PECsoil is calculated as an average concentration over a certain time period in agricultural soil, fertilised yearly with sludge from a STP and receiving continuous aerial deposition (dry and wet) from a nearby point source, for a period of 10 years.

For the terrestrial ecosystem, the concentration is calculated for a depth of 0.2 m. Sludge from Cd producing plants is however not applied to agricultural land but is recycled internally or by an external plant (IZA-Europe, pers. communication). Application of sludge from processing sites/scenarios is unlikely to take place but may occur if the Cd is emitted via a sewer to a municipal sewage treatment plant. This route of emission is taken into account in the regional assessment as diffuse Cd flux (no changes made, see section 3.1.3.4.2). Therefore, the Cd input to soil through sludge from the Cd producing plants is omitted in these calculations and atmospheric deposition is the only source of Cd input into the terrestrial compartment. The fate of sludge from Cd processors is unknown. Atmospheric deposition of Cd is calculated assuming that all Cd is deposited within an area of 100 km2 around the source and that the deposition occurs in a continuous flux.

The PEClocal is the sum of the regional Cd concentration in soil (PECregional) and the atmospheric deposition minus the leaching losses. The PEClocal is solved from the dynamic Cd balance in the 0-0.2 top layer of the soil as (see section 3.1.3.4.2):

where

Dair = aerial deposition flux per kg of soil (mg/kg d)

t = time (3,650 d)

k = first order rate constant for removal from top soil (d-1)

PECregionalsoil=the regional Cd concentration in soil (0.36 mg/kg wet wt) and which is calculated for an agricultural scenario assuming a realistic worst case Cd input scenario.

Results of the calculations are presented in Table 3.1.117. The PECsoil values are 0.363-mg/ kg wet wt.-0.37 mg/kg wet wt.. PECsoil values for Ni-Cd batteries producers and Cd recyclers are very similar and are mainly determined by the PECregional value for soil of 0.363 mg/kg wet wt.. Since atmospheric deposition is the only source of Cd input to the terrestrial compartment (sludge is recycled or landfilled) and emissions to air are relatively low (0.0014-0.10 kg/d; emission days: 225-350 d)), this emission route is of minor importance in comparison to the regional Cd concentration in soil. Referring to the scenarios of production, processing and use (reference year: 1996) in section 3.1.3.1.4, local PECsoil values for Cd producing plants (with higher air emissions) of 0.36-0.85 mg/kg wet wt. were calculated.

Table 3.1.117: Calculated local PECsoil for Ni-Cd producing plants and Cd recycling plants

| Use category | Plant n° | Emission to air | Number of emission days | PEClocal soil | Year |
| --- | --- | --- | --- | --- | --- |
|  |  | kg/d |  | mg/kg wet wt |  |
| Ni-Cd batteries |  |  |  |  |  |
|  | 1 | N.A. | 225 | 0.36 | 1999 |
|  | 2a | 0.005 | 330 | 0.36 | 2000 |
|  | 3b | N.A. | 315 | 0.36 | 2000 |
|  | 4 | 0.04 | 330 | 0.37 | 2000 |
|  | 5 | 0.03 | 230 | 0.37 | 1999 |
|  | 6 | 0.00014 | 250 | 0.36 | 1999 |
|  | 7 | 0.097 | 300 | 0.37 | 1999 |
| Cd recyclersc | 1 | 0.01 | 350 | 0.36 | 2000 |
|  | 2d | 0 | 240 | 0.36 | 1999 |

N.A.. not available

a Company 2  emits to the marine environment.

b wet processes; no emissions to air. Mainly emissions to effluents.

e Only two recyclers (instead of three) have been listed under Cd-recyclers. The reason is that one company is both recycler and producer. A further breakdown in the submitted figures between the producing process and the recycling process was not feasible. For this reason this company have been listed with the other producers.

d No “open” treatment steps; no emissions to air.

- Measured local concentrations

At this moment, only company 3 reported measured local soil concentrations of <12 mg/kg dry wt.

MSW incinerator: current situation

In the following section the results from the local exposure assessment for the terrestrial compartment for MSW incineration plants (life cycle stage 5: disposal; incineration) are presented. The only route of exposure for the terrestrial compartment is aerial deposition since it is assumed that the sludge from the on-site wastewater treatment plant is landfilled. As mentioned previously the local air emission for incineration plants is calculated using an allocation key based on the number of incinerators in each country and the country specific air emission amounts.

From Table 3.1.118 it can be concluded that the local PEC soil surrounding incineration plants in the EU  range from 0.363 mg/kg wet wt to 0.374  mg/kg wet wt. (total cadmium) which is almost similar to the regional PEC soil concentration of 0.363 mg/kg wet wt. Removing Ni-Cd batteries in the MSW will not significantly reduce the cadmium soil concentration (calculations not shown).

Table 3.1.118: Calculated total local PECsoil for MSW incineration plants

| Country | Emission amount | Number of emissions days | Clocalsoil | PEClocal soil |
| --- | --- | --- | --- | --- |
|  | kg/y | d | mg/kg w.wt | mg/kg wwt. |
| Austria | 1.4c | 330 | 0.00041 | 0.363 |
| Belgium | 3.5 | 330 | 0.0012 | 0.364 |
| Denmark | 9.7 | 330 | 0.0028 | 0.366 |
| Finland | 14 | 330 | 0.0041 | 0.367 |
| Francea | 16.4 | 330 | 0.0048 | 0.368 |
| Franceb | 36.7 | 330 | 0.0107 | 0.374 |
| Germany | 5 | 330 | 0.0015 | 0.365 |
| Italy | 5.7 | 330 | 0.0017 | 0.363 |
| Luxembourg | 22 | 330 | 0.0064 | 0.369 |
| Netherlands | 4.8 | 330 | 0.0014 | 0.364 |
| Norway | 5.1 | 330 | 0.0015 | 0.364 |
| Portugal | 1.6 | 330 | 0.0005 | 0.363 |
| Spain | 6.8 | 330 | 0.0020 | 0.365 |
| Sweden | 0.2 | 330 | 0.00006 | 0.363 |
| UK | 1.5 | 330 | 0.0004 | 0.363 |
| EU 10% scenario | 9.1 | 330 | 0.0027 | 0.366 |

a generic scenario

b based on P90 measured data

c according to the latest information (Stubenvoll et al., 2002) total Cd emissions in Austria from incinerators amount to 4.2 kg. Since there is a total of 3 plants, on average 1.4 kg per plant is emitted

Landfills

The leachate from landfills may be treated in municipal treatment plants from which sludge may be applied to land. Figures for the amounts going to agricultural land have been added to the tables in the assessment, but no calculations of soil concentrations have been included (there is no calculation of soil levels related to landfill, as there are no air emissions).

Regulations on the metals content of sludges for agriculture come into play here (cfr section 2.3).  Moreover, as the case in [the ‘global’ RAR related] section 3.1.3.1.4, the TRAR/batteries’ related sections does not include local ‘sludge application scenario’. Only diffuse emissions (averaged over whole EU) are considered in the assessment. The contribution of sludge application to (arable) land is considered and included in the PEC, reg, soil cfr section 3.1.3.4.2.

#### Local exposure: all scenarios: update data (reference year 2002)

##### Aquatic compartment: calculated PECs

###### Surface water

Introduction

Calculation of local PEC-values for the aquatic compartment is performed according to the method described in the TGD (2003; see also section 3.1.3.2.1). Input data were submitted via the Industry Questionnaire (2004).

Cd metal and Cd oxide production

Cd metal production

An overview of the calculated local Cd concentrations in surface water is presented in Table 3.1.119. From this table it can be concluded that for Cd metal producers in Europe:

- Daily emissions to surface water vary between 0.001 kg Cd/d (site 6) and 0.16 kg Cd/d (site 7; year 2002).

- Update information for on site WWTP cadmium removal efficiency is not provided.

- Total Cd concentrations in on site WWTP effluent vary between 0.0007 mg/l (annual mean site 6, direct discharge to large tide influenced river) and 0.05 mg/l (annual mean site 7, discharge to the sea; year 2002).

- Dilution factors vary between 2.3 (site specific dilution factor ditch, site 1) and 1000 (maximum site specific dilution factor large river, site 6). Site specific dilution factors were derived for 2 sites. Production site 7 discharges its wastewater to a marine environment for which a default dilution factor of 100 is applied.

- Local dissolved Cd concentrations in water vary between 0.0002 µg/l (site 6, large tidal river, maximum dilution factor of 1000) and 0.53 µg/l (site 1, ditch, very small dilution factor).

- Calculated PECtotal levels in surface water vary between 0.11 µg/l (calculated regional backgroundtotal = 0.11 µg/l) and 0.64 µg/l.

Table 3.1.119: The local PECwater (dissolved fraction) for Cd metal producing plants in the EU-16. PEC’s include background Cd.

| N° | production emission¶ | concentration in effluent | Type of receiving water | dilution Factor | Clocalwater | PEClocalwater | year |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | kg d-1 | mg l-1 |  |  | µg L-1 | µg L-1 |  |
| 1 | 0.03(c) | 0.004 | ditch | 2.3 | 0.53 | 0.64 | 2002 |
| 6 | 0.001 | 0.0007 | Tide influenced river | 1000(b) (ss: 11087) | 0.0002 | 0.11 | 2002 |
| 7* | 0.16* | 0.05 | sea | 100(a)* | 0.17* | 0.28* | 2002 |
| 7* | 0.10* | 0.03 | sea | 100(a)* | 0.10* | 0.21* | 2004 |

(a) default dilution factor: 10(freshwater), 100 (sea water) (b) site specific dilution factor restricted to a maximum of 1000 (revised TGD, 2003); (c) the total emission in 2002 consists of discharge of effluent from water purification plant and discharge of other water from the plant area (historic contaminated). Since 2005, the discharge from water from the plant area has been stopped; since then all waste water is treated In the purification plant. ss: site specific dilution factor; *: emission to the sea: values are only indicative; no assessment is done for the marine environment; ¶ annual averages.

Cd oxide production

An overview of the calculated local Cd concentrations in surface water is presented in Table 3.1.120. From this table it can be concluded that for Cd oxide producers in Europe:

- Due to the fact that the production of cadmium oxide is a totally dry process; discharge of waste water from the site does not take place.

- As a result the PEClocal in surface water is 0.11 µg/l (calculated regional background).

Table 3.1.120: The local PECwater (dissolved fraction) for Cd oxide producing plants in the EU-16. PEC’s include background Cd.

| N° | production emission¶ | concentration in effluent | Type of receiving water | dilution Factor | Clocalwater | PEClocalwater | year |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | kg d-1 | mg l-1 |  |  | µg L-1 | µg L-1 |  |
| 12 | 0(a) | 0 | n.a. | n.a. | 0 | 0.11 | 2002 |

¶ annual averages;n.a.: not applicable (a) No emission to water; thermal/dry process

Production and recycling of Ni-Cd batteries

Production of Ni-Cd batteries

An overview of the calculated local Cd concentrations in surface water is presented in Table 3.1.121. From this table it can be concluded that for Ni-Cd battery producers in Europe:

- Daily emissions to surface water vary between 0.03 kg Cd/d (site 2) and 0.07 kg Cd/d (site 4).

- Update information for on site WWTP cadmium removal efficiency is not provided.

- Total Cd concentrations in on site WWTP effluent vary between 0.06 mg/l (annual mean site 3, direct discharge to large river) and 0.11 mg/l (annual mean site 2, discharge to the sea).

- Dilution factors are set to 1000 (maximum site specific dilution factor, site 2, 3, 4). Site specific dilution factors were derived for 3 sites.

- Local dissolved Cd concentrations in water vary between 0.02 µg/l (site 3, river, maximum dilution factor of 1000) and 0.04 µg/l (site 2, sea, maximum dilution factor of 1000).

- Calculated PECtotal levels in surface water vary between 0.13 µg/l (calculated regional backgroundtotal = 0.11 µg/l) and 0.15 µg/l. Please note that in this update, annual mean effluent concentrations -as provided by industry- are used for PEClocal water derivation, as opposed to the original TRAR on Ni-Cd batteries (see current section 3.1.3.2.1), in which P90 effluent concentrations were calculated based on monthly average concentrations.

Table3.1.121: The local PECwater (dissolved fraction) for Ni-Cd batteries producing plants in the EU-16. PEC’s include background Cd.

| N° | production emission¶ | concentration in effluent | Type of receiving water | dilution Factor | Clocalwater | PEClocalwater | year |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | kg d-1 | mg l-1 |  |  | µg L-1 | µg L-1 |  |
| 2*/2bis | 0.03* | 0.11 | sea | 1000(b) (ss: 1326)* | 0.04 | 0.15 | 2002 |
| 3 | 0.04 | 0.06 | Tide influenced river | 1000(b) (ss: 25951) | 0.02 | 0.13 | 2002 |
| 4 | 0.07 | 0.10 | river | 1000(b) (ss: 1850) | 0.03 | 0.14 | 2002 |
| 6 | No update data |  |  |  |  |  |  |
| 7 | No update data |  |  |  |  |  |  |

*: emission to the sea: values are only indicative; no assessment is done for the marine environment; ¶ annual averages; (b) site specific dilution factor restricted to a maximum of 1000 (revised TGD, 2003); ss: site specific dilution factor

Recycling of Ni-Cd batteries

An overview of the calculated local Cd concentrations in surface water is presented in Table 3.1.122. From this table it can be concluded that for Ni-Cd battery recyclers in Europe:

- Daily emissions to surface water vary between 0 kg Cd/d (Cd recycling plant 2; off-site treatment of waste water) and 0.0007 kg Cd/d (site 1, year 2002 value). All waste waters from site 2 are collected and treated off-site in an external waste water treatment plant. Recent -year 2004- measurements for site 1 indicate that waste water emissions are reduced by a factor two due to various measures taken to conform to ISO 14000. Please note that emission information and PEC localwater for site 2bis is already included in the Ni-Cd battery producing section since waste water emissions could not be split between the NiCd-battery manufacturing and the recycling plant.

- Update information for on site WWTP cadmium removal efficiency is not provided.

- Total Cd concentrations in on site WWTP effluent vary between 0 mg/l (site 2) and 0.37 mg/l (90P site 1, year 2002, discharge to river). Please note that the 90P Cd concentration in the effluent of site 1 is reduced to 0.24 mg/l in the year 2004.

- The dilution factor for site 1 is set to 1,000 (maximum site specific dilution factor; TGD, 2003). Site specific dilution factors were derived for this site (site 1).

- Calculated PECtotal levels in surface water vary between 0.11 µg/l (site 2, calculated regional backgroundtotal = 0.11 µg/l) and 0.24 µg/l (site 1, year 2002 data). On the basis of year 2004 information for site 1, a PEClocalwater of 0.19 µg/l is calculated.

Table 3.1.122: The local PECwater (dissolved fraction) for Ni-Cd batteries recycling plants in the EU-16. PEC’s include background Cd.

| N° | production emission¶ | concentration in effluent | Type of receiving water | dilution Factor | Clocalwater | PEClocalwater | year |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | kg d-1 | mg l-1 |  |  | µg L-1 | µg L-1 |  |
| 1 | 0.0007 | 0.37 (90P) 0.16 (avg) | river | 1,000(b) (ss: 2,672) | 0.13 | 0.24 | 2002 |
| 1 | 0.0003 | 0.24 (90P) 0.1 (avg) | river | 1,000(b) (ss: 3,443) | 0.08 | 0.19 | 2004 |
| 2 | 0(a) | 0 | n.a. | n.a. | 0 | 0.11 | 2002 |
| 2bis | See data on site 2/2bis in table 3.21 |

¶ annual averages; n.a.: not applicable; (a) No site emission to water. Cleaning water as well as processing water are collected internal (about 100 m3/year) and send to an external waste water treatment plant; (b) site specific dilution factor restricted to a maximum of 1000 (revised TGD, 2003); ss: site specific dilution factor

Production of Cd containing pigments

An overview of the calculated local Cd concentrations in surface water is presented in Table 3.1.123. From this table it can be concluded that for Cd pigment producers in Europe:

- Daily emissions to surface water vary between 0.003 kg Cd/d (site A) and 0.02 kg Cd/d (site C). Please note that for site C year 2004 data have also been provided; emission to surface water is 0.01 kg/d (as opposed to 0.02 kg/d for year 2003).

- Update information for on site WWTP cadmium removal efficiency is not provided.

- Total Cd concentrations in on site WWTP effluent vary between 0.02 mg/l (annual mean for the sites A and B, direct discharge to river) and 0.12 mg/l (annual mean site C, direct discharge to river). Site C reports a 90P effluent concentration of 0.08 mg/l for the year 2004.

- Dilution factors vary between 24 (site specific factor river, site A) and 1000 (maximum site specific dilution factor river, site B). Site specific dilution factors were derived for all sites.

- Local dissolved Cd concentrations in water vary between 0.01 µg/l (site B, river, maximum dilution factor of 1000) and 0.27 µg/l (site A, river, site specific dilution factor). Note that for site Clocalwater for the year 2003 and 2004 are similar; i.e. 0.14 µg/l. Different dilution factors have been calculated for both years due to the large difference in effluent discharge rates: year 2003: 156 m3/d; year 2004: 240 m3/d. Since for the year 2004 a higher effluent discharge is reported, the subsequent dilution in the receiving water is smaller.

- Calculated PECtotal levels in surface water vary between 0.12 µg/l (calculated regional backgroundtotal = 0.11 µg/l) and 0.38 µg/l.

Table 3.1.123: The local PECwater (dissolved fraction) for Cd pigments production plants in the EU-16. PEC’s include background Cd.

| N° | processing emission¶ | concentration in effluent | Type of receiving water | dilution Factor | Clocalwater | PEClocalwater | year |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | kg d-1 | mg l-1 |  |  | µg L-1 | µg L-1 |  |
| A | 0.003 | 0.02 | river | 24 | 0.27 | 0.38 | 2003 |
| B | 0.01 | 0.02 | river | 1000(b) (ss: 3378) | 0.01 | 0.12 | 2003 |
| C | 0.02 | 0.12 | river | 289 | 0.14 | 0.25 | 2003 |
| C | 0.01 | 0.08 (90P) 0.05 (avg) | river | 189 | 0.14 | 0.25 | 2004 |

¶ annual averages; (b) site specific dilution factor restricted to a maximum of 1000 (revised TGD, 2003); ss: site specific dilution factor

Production of Cd containing stabilisers

An overview of the calculated local Cd concentrations in surface water is presented in  Table 3.1.124. From this table it can be concluded that for Cd stabiliser producers in Europe:

- Daily emissions to surface water vary between 0.003 kg Cd/d (site X) and 0.01 kg Cd/d (site Y).

- Update information for on site WWTP cadmium removal efficiency is not provided.

- Total Cd concentrations in on site WWTP effluent  vary between <0.001 mg/l (max. value, site Y, discharge to canal, external laboratory detection limit) and <0.005 mg/l (max. value, site X, discharge to municipal STP). Taking into account a second treatment step for site X (STP: 60% removal) and extra dilution of 5.4 in a municipal STP lowers the Cd concentration from <0.005 mg/l to <0.00037 mg/l.

- Dilution factors vary between 246 (site specific factor river, site Y) and 417 (site specific dilution factor river, site X). Site specific dilution factors were derived for 2 sites.

- Local dissolved Cd concentrations in water vary between 0.0003 µg/l (site X, river after STP, site specific dilution factor) and 0.007 µg/l (site Y, canal, site-specific dilution factor, based on detection limit internal laboratory).

- Calculated PECtotal levels in surface water vary between 0.11 µg/l (calculated regional backgroundtotal = 0.11 µg/l) and 0.12 µg/l.

Table 3.1.124: The local PECwater (dissolved fraction) for Cd stabilisers production plants in the EU-16. PEC’s include background Cd.

| N° | production emission¶ | concentration in effluent | Type of receiving water | dilution Factor | Clocalwater | PEClocalwater | year |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | kg d-1 | mg l-1 |  |  | µg L-1 | µg L-1 |  |
| X | 0.003 | On site WWTP : <0.005 Municipal STP : <0.00037(a) | river after municipal STP | 417 | 0.0003 | 0.11 | 2002 |
| Y | 0.01 | <0.005(b) | canal | 246 | 0.007 | 0.12 | 2002 |
| Y | 0.01 | <0.001(c) | canal | 246 | 0.001 | 0.11 | 2002 |

¶ annual averages; (a) Cd concentration in effluent from municipal STP; calculated from Cd concentration in effluent from on site WWTP; taking into account removal at STP: 60%; extra dilution= 5.4 (ratio of effluent discharge rate STP: default 2000 m3/d and on site WWTP discharge rate: 370 m3/d); (b) analysis performed by internal laboratory (two times a month) method MIP-P-PRO-101 rev 2 year 2003; (c) analysis performed by accreditated external laboratory (two times a year), method EPA 200.8 (1994).

Use of Cd/CdO in alloys, plating and other uses

For these uses, no update information was submitted to the Rapporteur.

###### Calculation of Predicted Environmental Concentration for Sewage Treatment Plants (PECstp)

The first step in the assessment of the local PEC values in the aquatic environment is the determination of the site-specific effluent concentration after on site WWTP treatment. If not available, it is calculated from reported daily releases to surface water and local effluent discharge rate.

Clocaleffluent: concentration in effluent water (mg/l)

EMISSIONlocalwater: local emission rate to water (kg/d)

EFFLUENTlocalSTP: effluent discharge rate of local STP (l/d)

If no effluent discharge rate is submitted, a default value of 2000 m3/d is used.

In case measured Cd concentrations in WWTP effluent are available, 90th percentile values are preferably used to account for a realistic worst case situation. If not available, annual means are used.

Additional removal of Cd needs to be considered if the industrial waste water undergoes an additional treatment in a municipal STP.

Since site specific information on type of WWTP, removal efficiency, Cd concentration in sludge and destination of sludge is not provided in the recently submitted industry questionnaires (2004), the paragraph extracted from section 3.1.2.2.1 is still considered as valid for Cd metal/CdO producing and processing plants (see below).

“Wastewater treatment at Cd-producing and -processing plants involves filtration and precipitation. Liquid effluents from the different stages during production and processing of Cd are collected and treated with sodium carbonate at alkaline pH to precipitate Cd.  Filtration aids and flocculating agents are added. The sludge is then filtered from the solution. The filtrate is neutralised prior to discharge to the environment. At industrial non-ferrous metal producing sites and waste water treatment plants (WWTP) a cadmium removal efficiency of at least 90% is reported based on physico-chemical techniques only, to achieve total cadmium concentrations within the range 1 – 0.1 mg/l (IPPC report, 2000). EUSES calculations give a corroborating removal rate (WS Atkins, 1998 and RPA, 2001): the Simple Treat model run with the Kp value of 130 000 l/kg yields the following distribution in the waste water treatment plant: 90% in sludge and 10% in water.

However, for municipal STP in practice, the average removal efficiency can vary widely from >80% (based on measurements of influent and effluent cadmium concentrations and the water flows; VMM, pers. com. 2002) to 60% (CUWVO, 1986; in: CBS/Milieucompendium, 2000). The latter, lower figure will be used in this report”.

Calculation of the STP concentration for evaluation inhibition to microorganisms (EC, 2003)

The removal of a chemical in the STP is computed from a simple mass balance. For the aeration tank, this implies that the inflow of sewage (raw or settled, depending on the equipment with a primary sedimentation tank) is balanced by the following removal processes: degradation, volatilization and outflow of activated sludge into the secondary settler. Activated sludge flowing out of the aeration tank contains the chemical at a concentration similar to the aeration tank, which is the consequence of complete mixing. It consists of two phases: water, which is virtually equal to effluent flowing out of the solids-liquid separator (this is called the effluent of the STP), and suspended particles, which largely settle to be recycled into the aeration tank. Assuming steady state and complete mixing in all tanks (also the aeration tank), the effluent concentration approximates the really dissolved concentration in activated sludge. It is assumed that only the dissolved concentration is bioavailable, i.e. the actual concentration to which the microorganisms in activated sludge are exposed. For the risk characterization of a substance upon microorganisms in the STP, it can therefore be assumed that homogeneous mixing in the aeration tank occurs which implies that the dissolved concentration of a substance is equal to the effluent concentration:

Clocaleffluent: total concentration of substance in STP effluent (mg/l)

PECstp: PEC for microorganisms in the STP (mg/l)

Cd metal production

An overview of PECWWTP/STP is given in Table 3.1.125. From this table it can be concluded that the PECWWTP for Cd metal producing plants varies between 0.7 µg/l and 50 µg/l (dissolved fraction).

Table 3.1.125: The local PECWWTP/STP (total fraction) for Cd metal producing plants in the EU-16.

| N° | production emission¶ | On site WWTP Off site municipal STP | Removal efficiency | PECWWTP/ PECSTP (dissolved fraction) | year |
| --- | --- | --- | --- | --- | --- |
|  | kg d-1 |  | % | µg L-1 |  |
| 1 | 0.03 | On site WWTP (physico-chemical as pre-treatment, biological BDS and SRB as polishing) (a) | n.d. | 3.6 | 2002 |
| 6 | 0.001 | On site WWTP | n.d. | 0.7 | 2002 |
| 7* | 0.16* | On site WWTP | n.d. | 50 | 2002 |
| 7* | 0.10* | ite WWTP | n.d. | 30 | 2004 |

(a) wwtp with physico-chemical pre-treatment followed by biological process based on fully adapted, specialised and dedicated micro-organisms. Cannot be compared with STPs based on ‘standard’ micro-organisms communities.*: emission to the sea; ¶ annual averages, n.d.: no data available

Cd oxide production

Since the production of cadmium oxide is a totally dry process; discharge of waste water from the site does not take place.

Table 3.1.126: The local PECWWTP/STP (total fraction) for Cd oxide producing plants in the EU-16.

| N° | production emission¶ | On site WWTP Off site municipal STP | Removal efficiency | PECWWTP/ PECSTP (dissolved fraction) | year |
| --- | --- | --- | --- | --- | --- |
|  | kg d-1 |  | % | µg L-1 |  |
| 12 | 0(a) | n.a. | n.a. | 0 | 2002 |

¶ annual averages, n;a.: not applicable. (a) No emission to water; thermal/dry process

Production of Ni-Cd batteries

An overview of PECWWTP/STP is given in Table 3.1.127. From this table it can be concluded that the PECWWTP for Ni-Cd battery producing plants vary between 63 µg/l and 107 µg/l (dissolved fraction).

Table 3.1.127: The local PECWWTP/STP (total fraction) for Ni-Cd batteries producing plants in the EU-16.

| N° | production emission¶ | On site WWTP Off site municipal STP | Removal efficiency | PECWWTP/ PECSTP (dissolved fraction) | year |
| --- | --- | --- | --- | --- | --- |
|  | kg d-1 |  | % | µg L-1 |  |
| 2*/2bis | 0.03 | On site WWTP | n.d. | 107 | 2002 |
| 3 | 0.04 | On site WWTP | n.d. | 63 | 2002 |
| 4 | 0.07 | On site WWTP | n.d. | 103 | 2002 |
| 6 | No update data |  |  |  |  |
| 7 | No update data |  |  |  |  |

*: emission to the sea; ¶ annual averages, n.d.: no data available

Recycling of Ni-Cd batteries

An overview of PECWWTP/STP is given in Table 3.1.128. Update data are available for site 1 and site 2. For the latter site, the waste waters are collected and transported to be treated in an external waste water treatment plant. Therefore no site emissions occur. For site 1, the PECWWTP is 370 µg/l (90P, year 2002). For the year 2004, a lower PECWWTP of 240 µg/l (90P) is reported.

Table 3.1.128: The local PECWWTP/STP (total fraction) for Ni-Cd batteries recycling plants in the EU-16.

| N° | production emission¶ | On site WWTP Off site municipal STP | Removal efficiency | PECWWTP/ PECSTP (dissolved fraction) | year |
| --- | --- | --- | --- | --- | --- |
|  | kg d-1 |  | % | µg L-1 |  |
| 1 | 0.0004 | On site WWTP | n.d. | 370 (90P) | 2002 |
| 1 | 0.0002 | On site WWTP | n.d. | 240 (90P) | 2004 |
| 2 | 0(a) | n.a. | n.a. | 0 | 2002 |
| 2bis | See data on site 2/2bis in Table 3.1.127 |

¶ annual averages; n.d.: no data available; n.a.: not applicable; (a) No site emission to water. Cleaning water as well as processing water are collected internal (about 100 m3/year) and send to an external waste water treatment plant.

Production of Cd containing pigments

An overview of PECWWTP/STP is given in Table 3.1.129. From this table it can be concluded that the PECWWTP for Cd pigments producing plants vary between 19 µg/l and 121 µg/l (dissolved fraction).

Table 3.1.129: The local PECWWTP/STP (total fraction) for Cd pigments producing plants in the EU-16.

| N° | processing emission¶ | On site WWTP Off site municipal STP | Removal efficiency | PECWWTP/ PECSTP (dissolved fraction) | year |
| --- | --- | --- | --- | --- | --- |
|  | kg d-1 |  | % | µg L-1 |  |
| A | 0.003 | On site WWTP | n.d. | 19 | 2003 |
| B | 0.01 | On site WWTP | n.d. | 19 | 2003 |
| C | 0.02 | On site WWTP | n.d. | 121 | 2003 |
| C | 0.01 | On site WWTP | n.d. | 80 | 2004 |

¶ annual averages, n.d.: no data available

Production of Cd containing stabilisers

An overview of PECWWTP/STP is given in Table 3.1.130. From this table it can be concluded that the PECWWTP for Cd stabiliser producing plants vary between 5 µg/l and 19 µg/l (dissolved fraction). The PECSTP for stabiliser plant X –discharging to a municipal STP- is 0.4 µg/l.

Table 3.1.130: The local PECWWTP/STP (total fraction) for Cd stabiliser producing plants in the EU-16.

| N° | production emission¶ | On site WWTP Off site municipal STP | Removal efficiency | PECWWTP/ PECSTP (dissolved fraction) | year |
| --- | --- | --- | --- | --- | --- |
|  | kg d-1 |  | % | µg L-1 |  |
| X | 0.003 | On site WWTP | n.d. | 5 | 2002 |
| X |  | Off site municipal STP | 60 | 0.4(a) | 2002 |
| Y | 0.01 | On site WWTP | n.d. | <5(b) | 2002 |
| I.01 | On site WWTP | n.d. | <1(c) | 2002 |

¶ annual averages, n.d.: no data available (a): PECSTP calculated taking into account 60% removal at STP and extra dilution at municipal STP of 5.4 (ratio of effluent discharge rate STP: default 2000 m3/d and on site WWTP discharge rate: 370 m3/d).; (b) effluent analysis performed by internal laboratory (two times a month) method MIP-P-PRO-101 rev 2 year 2003; (c) effluent analysis performed by accreditated external laboratory (two times a year), method EPA 200.8 (1994).

Use of Cd/CdO in alloys, plating and other uses

For these uses, no update information was submitted to the Rapporteur.

###### Calculation of PECsediment

The PEClocalsediment is calculated according to the formula presented below (see section 3.1.3.1.2):

PEClocalsediment = PECregionalsediment + Kp Clocal water. 10-3

in which the Kp (L kg-1dw) equals the solid- water partition coefficient of suspended matter (Kp =130,000 l/kg).

The measured PEC regional is taken as an average of 90th percentiles of surveys: 2.66 mg Cd kg-1dw (no changes made; Table 3.1.189, value not corrected for bioavailability).

The local PECsediment are readily calculated from the data in  Table 3.1.119- Table 3.1.124 and the above-mentioned equation and presented in Table3.1.131- Table 3.1.136. The Clocalsediment (Kp Clocal water. 10-3) is included to illustrate the contribution of the local discharge onto the sediment PEC.

Cd metal production

- Local Cd concentrations in sediment vary between 0.03 mg/kg dw (site 6, tide influenced river, max. dilution 1000) and 68.8 mg/kg dw (site 1, ditch). Elevated Cd concentrations in surface water lead to high concentrations in sediment due to the methodology used to calculate the Csediment (cfr. partitioning on the basis of Csurface water cfr. section 3.1.3.3.1.3).

- Calculated PECtotal levels in sediment vary between 2.7 mg/kg dw (measured regional backgroundtotal = 2.66 mg/kg dw) and 71.5 mg/kg dw.

Table 3.1.131: The local PECsediment (without correction for bioavailability) for Cd metal producing plants in the EU-16. PEC’s include background Cd

| N° | production emission¶ | Clocalwater | Clocalsediment | PEClocalsediment | year |
| --- | --- | --- | --- | --- | --- |
|  | kg d-1 | µg L-1 | mg kg-1dw | mg kg-1dw |  |
| 1 | 0.03 | 0.53 | 68.8 | 71.5 | 2002 |
| 6(b) | 0.001 | 0.0002 | 0.03 | 2.7 | 2002 |
| 7*(a) | 0.16 | 0.17* | 21.9 | 24.5 | 2002 |
| 7*(a) | 0.10 | 0.10* | 13.6 | 16.2 | 2004 |

(a) default dilution factor: 10 (freshwater), 100 (sea water;) (b) site specific dilution factor restricted to a maximum of 1000 (revised TGD, 2003);  *: emission to the sea: values are only indicative; no assessment is done for the marine environment; ¶ annual averages.

Cd oxide production

- Since no emissions to water take place at the CdO producing plant, the Clocal sediment and PEClocal sediment is 0 mg/kg dw and 2.7 mg/kg dw respectively.

Table 3.1.132: local PECsediment (without correction for bioavailability) for Cd oxide producing plants in the EU-16. PEC’s include background Cd.

| N° | production emission¶ | Clocalwater | Clocalsediment | PEClocalsediment | year |
| --- | --- | --- | --- | --- | --- |
|  | kg d-1 | µg L-1 | mg kg-1dw | mg kg-1dw |  |
| 12 | 0(a) | 0 | 0 | 2.7 | 2002 |

¶ annual averages. (a) No emission to water; thermal/dry process

Production of Ni-Cd batteries

- Local Cd concentrations in sediment vary between 2.8 mg/kg dw (site 3, tide influenced river, max. dilution 1000) and 4.7 mg/kg dw (site 2, sea, max. dilution 1000).

- Calculated PECtotal levels in sediment vary between 5.5 mg/kg dw (measured regional backgroundtotal = 2.66 mg/kg dw) and 7.4 mg/kg dw. Please note that site 2 is involved in both production and recycling of Ni-Cd batteries. No split in aquatic emissions could be done. Please note that in this update document, annual mean effluent concentrations -as provided by industry- are used for PEClocal water derivation, and consequently also the derivation of PEClocal sediment, as opposed to the original TRAR on Ni-Cd batteries (see current section 3.1.3.2.1), in which P90 effluent concentrations were calculated based on montly average concentrations.

Table 3.1.133: The local PECsediment  (without bioavailability correction) for Ni-Cd batteries producing plants in the EU-16. PEC’s include background Cd

| N° | production emission¶ | Clocalwater | Clocalsediment | PEClocalsediment | year |
| --- | --- | --- | --- | --- | --- |
|  | kg d-1 | µg L-1 | mg kg-1dw | mg kg-1dw |  |
| 2*(b)/2bis | 0.03* | 0.04 | 4.7 | 7.4 | 2002 |
| 3(b) | 0.04 | 0.02 | 2.8 | 5.5 | 2002 |
| 4 | 0.07 | 0.03 | 4.5 | 7.2 | 2002 |
| 6 | No update data |  |  |  |  |
| 7 | No update data |  |  |  |  |

*: emission to the sea: values are only indicative; no assessment is done for the marine environment; ¶ annual averages; (b) site specific dilution factor restricted to a maximum of 1000 (revised TGD, 2003)

Recycling of Ni-Cd batteries

- Local Cd concentrations in sediment vary between 0 mg/kg dw (site 2, no direct, local on-site emissions to water) and 16.3 mg/kg dw (site 1, river, max. dilution 1,000, year 2002 data).

- Calculated PECtotal levels in sediment vary between 2.66 mg/kg dw (measured regional backgroundtotal = 2.66 mg/kg dw) and 19.0 mg/kg dw.

Table 3.1.134: The local PECsediment  (without correction for bioavailability) for Ni-Cd batteries recycling plants in the EU-16. PEC’s include background Cd.

| N° | production emission¶ | Clocalwater | Clocalsediment | PEClocalsediment | year |
| --- | --- | --- | --- | --- | --- |
|  | kg d-1 | µg L-1 | mg kg-1dw | mg kg-1dw |  |
| 1 | 0.0007 | 0.13 | 16.3 | 19.0 | 2002 |
| 1 | 0.0003 | 0.08 | 10.6 | 13.2 | 2004 |
| 2(a) | 0 | 0 | 0 | 2.7 | 2002 |
| 2bis | See data on site 2/2bis in Table 3.1.133 |

¶ annual averages. (a) No site emission to water. Cleaning water as well as processing water are collected internal (about 100 m3/year) and send to an external waste water treatment plant.

Production of Cd containing pigments

- Local Cd concentrations in sediment vary between 0.8 mg/kg dw (site B, river, max. dilution 1000) and 34.7 mg/kg dw (site A, river). Please note that update emission information (90P) submitted for site C for the year 2004 gives similar results for Clocalsediment: 18.7 mg/kg dw as opposed to 18.4 mg/kg dw.

- Calculated PECtotal levels in sediment vary between 3.5 mg/kg dw (measured regional backgroundtotal = 2.66 mg/kg dw) and 37.4 mg/kg dw.

Table 3.1.135: The local PECsediment  (without correction for bioavailability) for Cd pigments production plants in the EU-16. PEC’s include background Cd.

| N° | processing emission¶ | Clocalwater | Clocalsediment | PEClocalsediment | year |
| --- | --- | --- | --- | --- | --- |
|  | kg d-1 | µg L-1 | mg kg-1dw | mg kg-1dw |  |
| A | 0.003 | 0.27 | 34.7 | 37.4 | 2003 |
| B(b) | 0.01 | 0.01 | 0.8 | 3.5 | 2003 |
| C | 0.02 | 0.14 | 18.4 | 21.0 | 2003 |
| C | 0.01 | 0.14 | 18.7 | 21.3 | 2004 |

¶ annual averages; (b) site specific dilution factor restricted to a maximum of 1000 (revised TGD, 2003)

Production of Cd containing stabilisers

- Local Cd concentrations in sediment vary between 0.04 mg/kg dw (site X, river after STP, site specific dilution factor) and 0.9 mg/kg dw (site Y, canal).

- Calculated PECtotal levels in sediment vary between 2.7 mg/kg dw (measured regional backgroundtotal = 2.66 mg/kg dw) and 3.6 mg/kg dw.

Table 3.1.136: The local PECsediment   (without correction for bioavailability) for Cd stabilisers production plants in the EU-16. PEC’s include background Cd.

| N° | production emission¶ | Clocalwater | Clocalsediment | PEClocalsediment | year |
| --- | --- | --- | --- | --- | --- |
|  | kg d-1 | µg L-1 | mg kg-1dw | mg kg-1dw |  |
| X(a) | 0.003 | 0.0003 | 0.04 | 2.7 | 2002 |
| Y | 0.01 | 0.007(b) | 0.9 | 3.6 | 2002 |
| Y | 0.01 | 0.001(c) | 0.2 | 2.8 | 2002 |

¶ annual averages; (a) Cd concentration in effluent from municipal STP; calculated from Cd concentration in effluent from on site WWTP; taking into account removal at STP: 60%; extra dilution: 2000 m3/d/370 m3/d = 5.4; (b) effluent analysis performed by internal laboratory (two times a month) method MIP-P-PRO-101 rev 2 year 2003; (c) effluent analysis performed by accreditated external laboratory (two times a year), method EPA 200.8 (1994).

Use of Cd/CdO in alloys, plating and other uses

For these uses, no update information was submitted to the Rapporteur.

###### Summary of calculated PECs for surface water

In  Table 3.1.137 a summary is given of the calculated Clocal and PECs in WWTP/STP, surface water and sediment for Cd metal and CdO producing and processing sectors. A detailed description of the results for each sector is provided in sections 3.1.3.3.1.1-3.1.3.3.1.3 of this document.

Table 3.1.137: Summary of calculated PECs in surface water for Cd/CdO producing/processing sectors. Clocalsediment and PEClocalsediment are not corrected for bioavailability.

| N° | PECWWTP/ PECSTP (total fraction) | Clocalwater | PEClocalwater | Clocalsediment | PEClocalsediment |
| --- | --- | --- | --- | --- | --- |
|  | µg L-1 | µg L-1 | µg L-1 | mg kg-1dw | mg kg-1dw |
| Cd metal production |  |  |  |  |  |
| 1 | 3.6© | 0.53 | 0.64 | 68.8 | 71.5 |
| 6 | 0.7 | 0.0002 | 0.11 | 0.03 | 2.7 |
| 7* | 50 | 0.17* | 0.28* | 21.9 | 24.5 |
| 7* (year 2004 data) | 30 | 0.10* | 0.21* | 13.6 | 16.2 |
| Cd oxide production |  |  |  |  |  |
| 12(a) | 0 | 0 | 0.11 | 0 | 2.7 |
| Ni-Cd battery production |  |  |  |  |  |
| 2*/2bis | 107 | 0.04 | 0.15 | 4.7 | 7.4 |
| 3 | 63 | 0.02 | 0.13 | 2.8 | 5.5 |
| 4 | 103 | 0.03 | 0.14 | 4.5 | 7.2 |
| 6 | No update data | No update data | No update data | No update data | No update data |
| 7 | No update data | No update data | No update data | No update data | No update data |
| Ni-Cd battery recyling |  |  |  |  |  |
| 1 | 370 | 0.13 | 0.24 | 16.3 | 19.0 |
| 1 (year 2004 data) | 240 | 0.08 | 0.19 | 10.6 | 13.2 |
| 2(b) | 0 | 0 | 0.11 | 0 | 2.7 |
| 2bis | See data on site 2/2bis under Ni-Cd battery production |
| Cd pigments production |  |  |  |  |  |
| A | 19 | 0.27 | 0.38 | 34.7 | 37.4 |
| B | 19 | 0.01 | 0.12 | 0.8 | 3.5 |
| C | 121 | 0.14 | 0.25 | 18.4 | 21.0 |
| C (year 2004 data, 90P) | 80 | 0.14 | 0.25 | 18.7 | 21.3 |
| Cd stabiliser producton |  |  |  |  |  |
| X WWTP | 5 |  |  |  |  |
| X STP | 0.4 | 0.0003 | 0.11 | 0.04 | 2.7 |
| Y | <5(d) | 0.007 | 0.12 | 0.9 | 3.6 |
| Y | <1(e) | 0.001 | 0.11 | 0.18 | 2.8 |

*Emission to the sea: values are only indicative; no assessment is done for the marine environment;(a) No emission to water; thermal/dry process; (b) No site emission to water. Cleaning water as well as processing water are collected internal (about 100 m3/year) and send to an external waste water treatment plant. (c) effluent concentration from biological based wastewater purification system contains fully adapted, specialised and dedicated micro-organisms. Cannot be compared with STPs based on ‘standard’ micro-organisms communities; (d) effluent analysis performed by internal laboratory (two times a month) method MIP-P-PRO-101 rev 2 year 2003; (e) effluent analysis performed by accreditated external laboratory (two times a year), method EPA 200.8 (1994).

###### Measured data in the aquatic compartment

Surface water

Table 3.1.138: Summary of calculated versus measured levels in surface water for Cd/CdO producing/processing sectors.

| N° | Emission amount | PEClocalwater Calculated Dissolved Cd | measured(1) (estimated dissolved Cd unless stated differently) | remarks | year |
| --- | --- | --- | --- | --- | --- |
|  | kg d-1 | µg L-1 | µg L-1 |  |  |
| Cd metal production |  |  |  |  |  |
| 1 | 0.03 | 0.64 | 1.0 | 25 m downstream from discharge point; spot sampling: 3 times/week, analytical method NEN 6426, Ditch is influenced by historical contamination, pH: 7.7-7.9 | 2002-2003 |
| 6 | 0.001 | 0.11 | n.a. |  |  |
| 7* | 0.16* | 0.28 | 0.1-1.65 µg/l (total Cd) 0.08-1.3 µg/l (estimated dissolved fraction in seawater) | different sampling points nearest to the outlets of the WWTPs, year 2002, concentration of suspended matter in seawater: 0.5-4 mg/l (avg 2 mg/l), dissolved concentration is estimated to be 79% of total concentration (Kp=130000 l/kg, Csusp=2 mg/l) (external laboratory data, NIVA). | 2002 |
| 7* | 0.10* | 0.21 | 0.16-0.36 µg/l (total Cd) 0.13-0.28 µg/l (estimated dissolved fraction in seawater) | different sampling points nearest to the outlets of the WWTPs, year 2004, concentration of suspended matter in seawater: 0.5-4 mg/l (avg 2 mg/l), dissolved concentration is estimated to be 79% of total concentration (Kp=130000 l/kg, Csusp=2 mg/l) (external laboratory data, NIVA). | 2004 |
| Cd oxide production |  |  |  |  |  |
| 12(a) | 0 | 0.11 | n.d.. |  | 2002 |
| Ni-Cd battery production |  |  |  |  |  |
| 2*/2bis | 0.03* | 0.15 | n.d.. |  | 2002 |
| 3 | 0.04 | 0.13 | n.d.. |  | 2002 |
| 4 | 0.07 | 0.14 | n.d.. |  | 2002 |
| 6 | No update data |  |  |  |  |
| 7 | No update data |  |  |  |  |
| Ni-Cd battery recyling |  |  |  |  |  |
| 1 | 0.0007 | 0.24 | 19.8 | 200 m downstream from discharge point, year 2002, River is influenced by contamination; i.e. infiltration and run-off waters from old metallurgical slag heaps. Upstream conc: 9.9 µg dissolved Cd/l; 200 m upstream from discharge point. | 2002 |
| 1 | 0.0003 | 0.19 | 10.6 | 200 m downstream from discharge point, year 2004, River is influenced by contamination; i.e. infiltration and run-off waters from old metallurgical slag heaps. Upstream conc: 13.9 µg dissolved Cd/l; 200 m upstream from discharge point. | 2004 |
| 2(b) | 0 | 0.11 | n.d.. |  | 2002 |
| 2bis | See data on site 2/2bis under Ni-Cd battery production |
| Cd pigments production |  |  |  |  |  |
| A | 0.003 | 0.38 | n.d.. |  | 2003 |
| B | 0.01 | 0.12 | n.d.. |  | 2003 |
| C | 0.02 | 0.25 | n.d.. |  | 2003 |
| Cd stabiliser producton |  |  |  |  |  |
| X WWTP | 0.003 |  |  |  |  |
| X STP |  | 0.11 | n.d.. |  | 2002 |
| Y | 0.01 | 0.12(b) | <1.65 µg/l | upstream and downstream value, < 5 µg total Cd/l = dl, ICP, pH: 7.9; hardness: 120-123 mg CaCO3/l; DOC: 7-11 mg/l | 2002 |
| Y | 0.01 | 0.11(c) | <1.65 µg/l | upstream and downstream value, < 5 µg total Cd/l = dl, ICP, pH: 7.9; hardness: 120-123 mg CaCO3/l; DOC: 7-11 mg/l | 2002 |

*Emission to the sea: values are only indicative; no assessment is done for the marine environment; n.a.: not available; (1) If total concentrations are measured, dissolved concentrations are estimated to be 33% of total Cd concentration (Kp = 130 103 L kg-1, Csusp = 15 mg L-1); (a) No emission to water; thermal/dry process; (b) No site emission to water. Cleaning water as well as processing water are collected internal (about 100 m3/year) and send to an external waste water treatment plant; (b) effluent analysis performed by internal laboratory (two times a month) method MIP-P-PRO-101 rev 2 year 2003; (c) effluent analysis performed by accreditated external laboratory (two times a year), method EPA 200.8 (1994).

Sediment

Table 3.1.139: Summary of calculated versus measured levels in sediment for Cd/CdO producing/processing sectors (without correction for bioavailability).

| N° | Emission amount | PEClocalsediment calculated | measured | remarks | year |
| --- | --- | --- | --- | --- | --- |
|  | kg d-1 | mg kg-1dw | mg kg-1dw |  |  |
| Cd metal production |  |  |  |  |  |
| 1 | 0.03 | 71.5 | upstream: 5 mg/kg dw At discharge point: 1.6 mg/kg dw | (Recent) dredging occurred downstream of the discharge point. Ditch is influenced by historical contamination. TOC: <1% AVS: U: 23.7 µmol/g dw D: 2.6 µmol/g dw (sampling: 25.11.2002, 100m upstream and downstream discharge point) (EURAS, 2003; external laboratory) | 2002-2003 |
| 6 | 0.001 | 2.7 | 0.64 mg/kg dw (300 m upstream) 1.14 mg/kg dw (1800 m downstream | n.a. | 2002 |
| 7* | 0.16* | 24.5 | At discharge point: 1.1 mg/kg dw; further in the open sea: 2.1-3.2 mg/kg dw | jarosite discharge prior to 1986; since deposition in mountain caverns, significant decrease in top 1-cm sediment concentrations (external laboratory data, NIVA). | 1996 (measured data) 2002 (calculated PEC) |
| 7* | 0.10* | 16.2 | At discharge point: 1.1 mg/kg dw; further in the open sea: 2.1-3.2 mg/kg dw | jarosite discharge prior to 1986; since deposition in mountain caverns, significant decrease in top 1-cm sediment concentrations (external laboratory data, NIVA). | 1996 (measured data) 2002 (calculated PEC) |
| Cd oxide production |  |  |  |  |  |
| 12(a) | 0 | 2.7 | n.d.. | n.d.. | 2002 |
| Ni-Cd battery production |  |  |  |  |  |
| 2*/2bis | 0.03* | 7.4 | n.d.. | The sediments of the harbour are heavily contaminated by industrial activity in the vicinity of the harbour. The total amount of metals present in the sediments is estimated to 1000 tons. No relationship between the present metal emissions and the metal content of the harbour sediments can be established. | 2002 |
| 3 | 0.04 | 5.5 | n.d.. | n.. | 2002 |
| 4 | 0.07 | 7.2 | 4.6 | 3 km downstream from discharge point, year 2001 data 3.3 mg/kg dw; 100 m upstream from discharge point; year 2001 data. | 2002 |
| 6 | No update data |  |  |  |  |
| 7 | No update data |  |  |  |  |
| Ni-Cd battery recyling |  |  |  |  |  |
| 1 | 0.0007 | 19.0 | 133 | 200 m downstream from discharge point, year 2002 River is influenced by contamination; i.e. infiltration and run-off waters from old metallurgical slag heaps. Upstream conc: 55 mg/kg dw; 200 m upstream from discharge point. | 2002 |
| 1 | 0.0003 | 13.2 | 224 | 200 m downstream from discharge point, year 2002 River is influenced by contamination; i.e. infiltration and run-off waters from old metallurgical slag heaps. Upstream conc: 88 mg/kg dw; 200 m upstream from discharge point. | 2004 |
| 2(b) | 0 | 2.7 | n.d.. | n.d.. | 2002 |
| 2bis | See data on site 2 under Ni-Cd battery production |
| Cd pigments production |  |  |  |  |  |
| A | 0.003 | 37.4 | n.d.. | n.d.. | 2003 |
| B | 0.01 | 3.5 | n.d.. | n.d.. | 2003 |
| C | 0.02 | 21.0 | n.d.. | n.d.. | 2003 |
| Cd stabiliser producton |  |  |  |  |  |
| X WWTP | 0.003 |  |  |  |  |
| X STP |  | 2.7 | n.d.. | Id.. | 2002 |
| Y | 0.01 | 3.6(c) | n.d.. | n.d.. | 2002 |
| Y | 0.01 | 2.8(d) | n.d. | n.d. | 2002 |

*emission to the sea: values are only indicative; no assessment is done for the marine environment; ¶ annual averages; n.a.: not available; TOC: total organic carbon; AVS: acid volatile sulfides; U: upstream; D: downstream; (a) No emission to water; thermal/dry process; (b) No site emission to water. Cleaning water as well as processing water are collected internal (about 100 m3/year) and send to an external waste water treatment plant; (c) effluent analysis performed by internal laboratory (two times a month) method MIP-P-PRO-101 rev 2 year 2003; (d) effluent analysis performed by accreditated external laboratory (two times a year), method EPA 200.8 (1994).

Comparison of PECs with measured data

Measured Cd concentrations in surface water –presented in Table 3.1.138- are available for Cd metal production site 1 and 7, Cd recycling site 1 and Cd stiliser production site Y.

-	The dissolved Cd concentration of 1 µg/l measured in the ditch downstream from the discharge point of Cd metal production site 1 is in the same range as the predicted concentration of 0.64 µg/l. The measured data should however be treated with caution due to the ‘large influence of historic contamination in the ditch surrounding thisite’ (company statement).

-	Measured Cd concentrations in the receiving marine environment are available for Cd metal production site 7. Measurements are performed at several locations: nearby the discharge point and some kilometres away from the emissions point in the open sea. Total Cd concentrations varying between 0.1 µg/l and 1.65 µg/l are reported. The concentration of suspended solids in the seawater is on average 2 mg/l (0.5-4 mg/l). On the basis of this information, dissolved concentrations can be estimated from total concentrations as 79% of total Cd concentration (Kp = 130 103 L kg-1, Csusp = 2 mg L-1). Dissolved Cd concentrations varying between 0.08 µg/l and 1.3 µg/l are calculated. The maximum measured dissolved Cd concentration of 1.3 µg/l is situated a factor of five above the PEClocalwater derived for this site of 0.28 µg/l (dissolved fraction).

-	Cd recycler site 1 reports measured total Cd concentrations in the receiving river 200 m downstream from the discharge point of 60 µg total Cd/l (i.e. 19.8 µg dissolved Cd/l) (year 2002). The site reports that these data are influenced by historical contamination; i.e. infiltration and run-off waters from old metallurgical slag heaps in front of the plant. Therefore they should be treated with caution. The measured dissolved Cd concentration in the river of 19.8 µg/l is eighty fold the calculated PECwater (0.24 µg/l). Data for the year 2004 indicate that although there is a decline in Cd concentrations in the receiving river i.e. 10.6 µg/l, the measured value is still a factor of 60 above the modelled PEC of 0.19 µg/l. It should be noted however that the upstream measurement for this site is 13.9 µg Cd/l which is in the same order of magnitude –s the downstream measurement.

-	Cd stabiliser site Y reports measured total Cd concentrations in the receiving river of <5 µg/l (5 µg/l being the detection limit). This value corresponds to <1.65 µg dissolved Cd/l. The calculated PEClocalwater of 0.12 µg/l is situated a factor of 14 below the measured Cd concentration of 1.65 µg/l. It should be noted however that the measured value is a maximum.

In conclusion, it can be noted that only limited measured information is (made) available.

Moreover, submitted measured data are stated by the companies to be (heavily) influenced by other sources (incl. historic contamination e.g. by infiltration from deposited waste).

In general measured Cd concentrations in surface water are situated above the modelled local values for the receiving surface water.

It should be noticed that in general the analytical methods (detection limit > 0.10 µg/l) used are not adequate to accurately and reliably measure (very low) concentrations in the environment.

The measured (estimated dissolved) concentrations, including ‘background’ concentrations, range from 0.08 to 1.3 µg/l for cadmium production sites. The range of calculated local Cwater and PEC values in water is respectively 0.00026 – 0.53 (g/l and 0.11-0.64 µg/l (the latter figures including the calculated 0.11 µg/l regional background level). Comparison of these local measured data for sites emitting to surface water with the calculated local PECwater values of the corresponding sites shows good corroboration (the difference is maximum a factor 3.5 lower to factor 4.6 higher.

The measured data for NiCd battery recycler (site 1; for 2002 and 2004 resp.) 19.8 - 10.6 µg/l are two orders of magnitude higher as the corresponding calculated Clocalwater and PEC values for this site are 0.13 - 0.08 µg/l and 0.24 – 0.19 µg/l (factors up to 152 - 132 difference).

For other sectors/plants no comparison is possible due to lack of measured data.

Both calculated and measured values will be taken forward to the risk characterisation bearing however in mind the limitations of these values.

Measured Cd concentrations in sediment (without correction for bioavailability) –presented in Table 3.1.139 - are available for Cd metal production site 1, 6 and 7, Ni-Cd battery manufacturing site 4 and Cd recycling site 1.

- For Cd metal production site 1, the measured Cd concentration in sediment sampled upstream and at the discharge point is 5 mg/kg dw and 1.6 mg/kg dw respectively. Measured Cd concentrations are situated a factor of 14-45 below the PEClocalsediment of 71.5 mg/kg dw. This site also submitted information on AVS and organic carbon content of the sediments. Using these data, the exposure assessment could further be refined. As the methodology to perform the bioavailability correction for Cd is still under development, the correction will be performed in a next phase of the update RA process.

- Cd metal production site 6 provides recent upstream and downstream measurements in sediments of 0.64 mg Cd/kg dw and 1.14 mg Cd/kg dw respectively (year 2002). As for site 1, the measured Cd concentrations are 2.4-4.2 times below the calculated PEClocalsediment of  2.7 mg/kg dw.

- For Cd metal production site 7, discharging to a marine environment, Cd concentrations in sediment are reported near the discharge point for the year 1996: 1.1 mg/kg dw and in the open sea: 2.1-3.2 mg/kg dw. The same observation is made as for the other Cd metal producing plants. Measured Cd concentrations are situated 7.7-22.3 times below the modelled sediment concentration i.e. 24.5 mg/kg dw.

- Ni-Cd battery manufacturing site 4 provides recent upstream and downstream measurements in sediments of 3.3 mg/kg dw and 4.6 mg/kg dw respectively (year 2001). The measured Cd concentrations are situated below, but in the same order of magnitude as the calculated PEClocal sediment of 7.2 mg/kg dw. Please note that the downstream sample is situated 3 km from the discharge point.

- Cd recycling site 1 provides recent upstream and downstream measurements in sediments of 55 mg/kg dw and 133 mg/kg dw respectively (year 2002). The measured Cd concentrations are 3-7 fold the calculated PEClocal sediment of 19.0 mg/kg dw. Please note that the measured data are influenced by historical contamination (infiltration and run-off waters from old metallurgical slag heaps). The sediment data for the year 2004 show an increase in Cd concentrations: upstream concentration: 88 mg/kg dw; downstream value 224 mg/kg dw. These data are 7-17 fold the modelled value of 13.2 mg/kg dw.

In conclusion, it is noted that only limited measured information is (made) available.

Moreover, it is stated by the companies that submitted measured data are (heavily) influenced by other sources (incl. historic contamination e.g. by infiltration from deposited waste).

In general, measured values are situated below the corresponding modelled PEClocalsediment.

This may be due to the fact that the calculated PECsediment –derived using the partitioning methodology and Kpsuspended solids- overestimates the real situation.

The measured concentrations in sediment (in the range 1.1 to 5 mg/kg dw) are for the Cd metal producers a factor 4.2 to 22.3 lower than the calculated values (range 2.7 to 71.5 mg/kg dw). Clocal sediment varies between 0.03 and 68.8 mg/kg dw. Only for one site (site 1): more detailed information on AVS and SEM concentrations on Cd, Cu and Pb are available.

For NiCd battery producers no comparison is possible due to lack of representative measured data (i.e. data for site 4 are not considered valid/useful given the distance from the discharge point).

For the NiCd recyclers site 1 measured data are a factor 7 to 17 higher than the calculated values. Clocalsediment is 10.6 to 16.3 mg/kg dw. Measurements only relate to Cd concentration in sediment. No data are available on AVS and SEMs on other metals, neither the sampling date(s).

For other sectors/plants no comparison is possible due to lack of measured data.

Both calculated and measured data will be taken forward to the risk characterisation bearing however in mind the limitations of these values.

##### Terrestrial compartment

###### Calculated PEC for soil

Calculations are made following the equations given in section 3.1.3.1.4.

The local PECsoil are readily calculated from the release data and the above-mentioned equation and are presented in Table 3.1.140-Table 3.1.145.

Cd metal production

- Daily stack emissions to air vary between 0.03 kg Cd/d (site 6) and 0.15 kg Cd/d (site 7).

- Calculated annual average deposition rates vary between 2.74x10-4 mg/m2.d and 1.48x10-3 mg/m2.d

- The main exposure route is aerial deposition for Cd metal producers; sludge from the on site waste water treatment system is not applied to agricultural land but is recycled or landfilled (industry information).

- Calculated added local concentrations in soil vary between 0.003 mg/kg ww (site 6) and 0.02 mg/kg ww (site 7).

- Calculated PEClocal in soil vary between 0.36 mg/kg ww (calculated regional background soil = 0.36 mg/kg ww) and 0.38 mg/kg ww (based on calculated aerial deposition rates). For site 7, the selected measured annual average aerial deposition rate of 0.008 mg/m2.d was used for PECsoil derivation. The PECsoil level –on the basis of measured deposition rates- for this site is 0.45 mg/kg ww. Please note that using measured deposition rates for PEClocalsoil derivation addresses a reasonable worst case situation. Measured deposition data are influenced by blown up dust and other undefined inputs.

Table 3.1.140: Calculated total local PECsoil for Cd-metal producing plants in EU-16. PEC’s include background Cd.

| N° | Emission to air¶ | Number of emission days | Clocalsoil | PEClocal soil (modelled aerial deposition rates) | PEClocalsoil (measured aerial deposition rates) | year |
| --- | --- | --- | --- | --- | --- | --- |
|  | kg d-1 |  | mg kgww-1 | mg kgww-1 |  |  |
| 1 | 0.08(a)(b) | 365 | 0.01 | 0.37 | - | 2002 |
| 6 | 0.03(a)(c) | 365 | 0.003 | 0.36 | - | 2002 |
| 7 | 0.15(a)(d) | 365 | 0.02 | 0.38 | 0.45 | 2002 |

¶ annual averages; (a) Cd emission from whole plant (including Zn and/or Pb production) (b) total emissions: stack + diffuse emissions; diffuse emissions: 60-70% of total; stack emissions: 30-40% of total emissions. (c) All emissions from point sources and fugitive emissions from roof openings for the whole zinc production process. Emissions from cadmium production are difficult to separate. (d) Total emissions from the zinc smelter; approx. 90 emission points to air. Approximately 90% of the emission comes from 20% of the emission points which all are equipped with abatement systems (demisters or scrubbers).

Cd oxide production

- Daily stack emission to air is 0.026 kg Cd/d (year 2005; in-house methods) and 0.045 kg/d (year 2004; stack air measurements performed by external laboratory).

- The calculated annual average deposition rate is 1.81x10-4 mg/m2.d (year 2005) and 3.19x10-4 mg/m2.d (year 2004)

- The main exposure route is aerial deposition for Cd oxide producers.

- Calculated added local concentration in soil is 0.002 mg/kg ww (year 2005) and and 0.003 mg/kg ww (year 2004).

- Calculated PEClocal in soil is 0.36 mg/kg ww (calculated regional background soil = 0.36 mg/kg ww).

Table 3.1.141: Calculated total local PECsoil for Cd-oxide producing plants in EU-16. PEC’s include background Cd (0.36 mg/kg ww).

| N° | Emission to air¶ | Number of emission days | Clocalsoil | PEClocal soil | year |
| --- | --- | --- | --- | --- | --- |
|  | kg d-1 |  | mg kgww-1 | mg kgww-1 |  |
| 12 | 0.026(a) | 256 | 0.002 | 0.36 | 2005 |
| 12 | 0.045(b) | 256 | 0.003 | 0.36 | 2004 |

¶ annual averages;  (a) Cd in stack emissions is recently measured (year 2005); average Cd concentration: 55 µg/m3 (punctual measurement; in-house methods); (b) Cd in stack emissions measured by external laboratory (year 2004); average Cd concentration : 97 µg/m3.

Production of Ni-Cd batteries

- Daily stack emissions to air vary between 0.01 (site 4) and 0.02 kg Cd/d (site 2, battery manufacturing plant only). Site 3 did not provide any emission information, since air emissions are not monitored (not obliged in permit).

- The calculated annual average deposition rates vary between 9.59x10-5 (site 4) and 1.37x10-4 mg/m2.d (site 2)

- The main exposure route is aerial deposition for Ni-Cd battery producers; sludge from the on site waste water treatment system is not applied to agricultural land but is recycled or landfilled (industry information).

- Calculated added local concentration in soil is 0.001 mg/kg ww (site 2, 4).

- Calculated PEClocal in soil is 0.36 mg/kg ww (calculated regional background soil = 0.36 mg/kg ww) (site 2, 4).

Table 3.1.142: Calculated total local PECsoil for Ni-Cd batteries producing plants in EU-16. PEC’s include background Cd .

| N° | Emission to air¶ | Number of emission days | Clocalsoil | PEClocal soil | year |
| --- | --- | --- | --- | --- | --- |
|  | kg d-1 |  | mg kgww-1 | mg kgww-1 |  |
| 2 | 0.02(a) | 330 | 0.001 | 0.36 | 2002 |
| 3 | n.d.(b) | 330 | n.d. | n.d. | 2002 |
| 4 | 0.01 | 344 | 0.001 | 0.36 | 2002 |
| 6 | No update data |  |  |  |  |
| 7 | No update data |  |  |  |  |

¶annual averages; n.d.: no data available; (a) Emission from battery manufacturing only; air emissions are broken down between two plants; battery manufacturing and Cd recycling; (b) Air emissons are not monitored. No requirement in the permit since the plant runs a wet process, therefore most emissions are releases in the water.

Recycling of Ni-Cd batteries

- Daily stack emissions to air vary between 5.3x10-6 kg Cd/d (site 2) and 0.01 kg Cd/d (site 1, year 2002 data).

- Calculated annual average deposition rates vary between 5.21x10-8 mg/m2.d and 1.09x10-4 mg/m2.d

- The main exposure route is aerial deposition for Cd recyclers; sludge from the on site waste water treatment system is not applied to agricultural land but is recycled or landfilled (industry information).

- Calculated added local concentrations in soil vary between 5.6x10-7 mg/kg ww (site 2) and 0.0012 mg/kg ww (site 1, year 2002 data).

- Calculated PEClocal in soil is 0.36 mg/kg ww (calculated regional background soil = 0.36 mg/kg ww).

Table 3.1.143: Calculated total local PECsoil for Ni-Cd batteries recycling plants in EU-16. PEC’s include background Cd.

| N° | Emission to air¶ | Number of emission days | Clocalsoil | PEClocal soil | year |
| --- | --- | --- | --- | --- | --- |
|  | kg d-1 |  | mg kgww-1 | mg kgww-1 |  |
| 1 | 0.01 | 355 | 0.0012 | 0.36 | 2002 |
| 1 | 0.003 | 336 | 0.0003 | 0.36 | 2004 |
| 2 | 5.3x10-6(a) | 360 | 5.6x10-7 | 0.36 | 2002 |
| 2bis | 0.003(b) | 330 | 0.0003 | 0.36 | 2002 |

¶annual averages; (a) Submitted air emissions are checked versus the analysis report and proved to be correct. Air emissions are that low due to the fact that in air emission no considerable amount of Cd can be found (conc. 2.5 µg/m3) and the fact that the gas stream is very low due to technical reasons (78 m3/h max). (b) Emissions from Cd recycling unit on the site of battery manufacturing plant 2.

Production of Cd containing pigments

- Daily stack emissions to air vary between 0.01 kg Cd/d (site A, C) and 0.02 kg Cd/d (site B).

- Calculated annual average deposition rates vary between 6.85x10-5 mg/m2.d and 1.53x10-4 mg/m2.d

- The main exposure route is aerial deposition for Cd pigments producers. Sludge from the treatment of waste water is landfilled.

- Calculated added local concentrations in soil vary between 0.0007 mg/kg ww (site A) and 0.002 mg/kg ww (site B).

- Calculated PEClocal in soil is 0.36 mg/kg ww (calculated regional background soil = 0.36 mg/kg ww).

Table 3.1.144: Calculated total local PECsoil for Cd pigments producing plants in EU-16. PEC’s include background Cd.

| N° | Emission to air¶ | Number of emission days | Clocalsoil | PEClocal soil | year |
| --- | --- | --- | --- | --- | --- |
|  | kg d-1 |  | mg kgww-1 | mg kgww-1 |  |
| A | 0.01 | 230 | 0.0007 | 0.36 | 2003 |
| B | 0.02 | 318 | 0.002 | 0.36 | 2003 |
| C | 0.01 | 250 | 0.0008 | 0.36 | 2003 |

¶annual averagesProduction of Cd containing stabilisers

- Daily stack emissions to air vary between 0.002 kg Cd/d (site Y) and 0.003 kg Cd/d (site X).

- Calculated annual average deposition rates vary between 2.74x10-6 mg/m2.d and 1.75x10-5 mg/m2.d

- The main exposure route is aerial deposition for Cd stabiliser producers. Although site X discharges its waste water to a municipal STP; the sludge is not applied to agricultural soil (see section 3.1.3.3.2.1). Site-specific information on the destination of sludge is not available.

- Calculated added local concentrations in soil vary between 2.9x10-5 mg/kg ww (site Y) and 0.0002 mg/kg ww (site X).

- Calculated PEClocal in soil is 0.36 mg/kg ww (calculated regional background soil = 0.36 mg/kg ww).

Table 3.1.145: Calculated total local PECsoil for Cd stabiliser producing plants in EU-16. PEC’s include background Cd.

| N° | Emission to air¶ | Number of emission days | Clocalsoil | PEClocal soil | year |
| --- | --- | --- | --- | --- | --- |
|  | kg d-1 |  | mg kgww-1 | mg kgww-1 |  |
| X | 0.003 | 220 | 0.0002 | 0.36 | 2002 |
| Y | 0.002 | 50 | 2.9x10-5 | 0.36 | 2002 |

¶annual averages

Use of Cd/CdO in alloys, plating and other uses

For these uses, no update information was submitted to the Rapporteur.

###### Measured levels in soil

There are no measured local soil concentrations submitted by the Cd/CdO producing- or processing industries.

Measured aerial deposition rates are available for the Cd metal producing sites. A comparison between calculated and measured deposition levels is provided in Table 3.1.153 (section 3.1.3.3.3.2).

##### Atmospheric compartment

###### Calculation of PEClocalair

Local PEC-values for the atmospheric compartment are calculated according to the OPS model proposed in the TGD (2003) for a general standard environment.

Input data are the total daily emissions of the individual Cd-producing and processing plants (Industry questionnaires, 2004).

The calculated concentrations in air are actual contributions to the receiving atmosphere. The local PEC values are obtained by adding the regional PEC values for air to the calculated local concentration in the atmosphere.

PEClocalair,ann = Clocalair, ann + PECregionalair

PEClocalair,ann: 		annual average predicted environmental concentration in air  (ng m-3)

PECregionalair: 		regional concentration in the air (0.55 ng m-3; table 3.1.157)

The results of the predicted local atmospheric Cd concentrations at 100 m from the point sources are listed in Table 3.1.146 -Table 3.1.149.

Cd metal production

- Daily stack emissions to air vary between 0.03 kg Cd/d (site 6) and 0.15 kg Cd/d (site 7). Please note that in general for the Cd metal production sites the total emissions are reported i.e. emissions from stack and diffuse sources. Moreover, emissions due to to refining/production of other non-ferro metals may be included (to different extent from site to site).

- Calculated annual average Cd concentrations at a distance of 100 m from the point source vary between 7.6 ng/m3 (site 6) and 41.3 ng/m3 (site 7).

- Calculated PEClocalair values vary between 8.2 and 41.8 ng/m3 (calculated regional background = 0.55 ng/m3).

Table 3.1.146: Calculated total local PECair for Cd-metal producing plants in EU-16. PEC’s include background Cd.

| N° | Emission to air | Number of emission days | annual average air concentration | PEClocalair,ann | year |
| --- | --- | --- | --- | --- | --- |
|  | kg d-1 |  | (100 m) ng m-³ | (100 m) ng m-³ |  |
| 1 | 0.08(a)(b) | 365 | 23.2 | 23.7 | 2002 |
| 6 | 0.03(a)(c) | 365 | 7.6 | 8.2 | 2002 |
| 7 | 0.15(a)(d) | 365 | 41.3 | 41.8 | 2002 |

¶annual averages; (a) Cd emission from whole plant (including Zn and/or Pb production) (b) total emissions: stack + diffuse emissions; diffuse emissions: 60-70% of total; stack emissions: 30-40% of total emissions. (c) All emissions from point sources and fugitive emissions from roof openings for the whole zinc production process. Emissions from cadmium production are difficult to separate. (d) Total emissions from the zinc smelter; approx. 90 emission points to air. Approximately 90% of the emission comes from 20% of the emission points which all are equipped with abatement systems (demisters or scrubbers).

Cd oxide production

- The daily stack emissions to air for CdO production site 12 amount to 0.026 kg/d (year 2005, in house methods). On the basis of Cd measurements in the stacks, performed by an external laboratory, an emission amount of 0.045 kg/d could be calculated for the year 2004.

- The calculated annual average Cd concentration at a distance of 100 m from the point source is 5.0 ng/m3 (year 2005) and 8.9 ng/m3 (year 2004) respectively.

- The calculated PEClocal air is 5.6 ng/m3 (year 2005) and 9.4 ng/m3 (year 2004).

Table 3.1.147: Calculated total local PECair for Cd-oxide producing plants in EU-16. PEC’s include background Cd.

| N° | Emission to air | Number of emission days | annual average air concentration | PEClocalair,ann | year |
| --- | --- | --- | --- | --- | --- |
|  | kg d-1 |  | (100 m) ng m-³ | (100 m) ng m-³ |  |
| 12(a) | 0.026 | 256 | 5.0 | 5.6 | 2005 |
| 12(b) | 0.045 | 256 | 8.9 | 9.4 | 2004 |

¶annual averages; (a) Cd in stack emissions is recently measured (year 2005); average Cd concentration: 55 µg/m3 (punctual measurement, in-house methods); (b) Cd in stack emissions measured by external laboratory (year 2004); average Cd concentration: 97 µg/m3.

Production of Ni-Cd batteries

- Daily stack emissions to air vary between 0.01 kg Cd/d (site 4) and 0.02 kg Cd/d (site 2, battery manufacturing plant only). Data are not available for site 3 since there is no requirement to monitor air emissions.

- The calculated annual average Cd concentration at a distance of 100 m from the point source vary between 2.7 ng/m3 (site 4) and 3.8 ng/m3 (site 2).

- Calculated PEClocalair varies between 3.2 ng/m3 and 4.4 ng/m3 (calculated regional background = 0.55 ng/m3).

Table 3.1.148: Calculated total local PECair for Ni-Cd battery producing plants in EU-16. PEC’s include background Cd.

| N° | Emission to air | Number of emission days | annual average air concentration | PEClocalair,ann | year |
| --- | --- | --- | --- | --- | --- |
|  | kg d-1 |  | (100 m) ng m-³ | (100 m) ng m-³ |  |
| 2 | 0.02(a) | 330 | 3.8 | 4.4 | 2002 |
| 3 | n.d.(b) | 330 | n.d. | n.d. |  |
| 4 | 0.01 | 344 | 2.7 | 3.2 | 2002 |
| 6 | No update data |  |  |  |  |
| 7 | No update data |  |  |  |  |

¶annual averages; n.d.: no data available; (a) Emission from battery manufacturing only; air emissions are broken down between two plants; battery manufacturing and Cd recycling; (b) Air emissons are not monitored. No requirement in the permit since the plant runs a wet process, therefore most emissions are releases in the water.

Recycling of Ni-Cd batteries

- Daily stack emissions to air vary between 5.3x10-6 kg Cd/d (site 2) and 0.01 kg Cd/d (site 1, year 2002 data). Year 2004 data for site 1 show a significant reduction in air emissions -i.e. 0.003 kg Cd/y- as a result of measures taken to obtain an ISO 14000 certificate (building coverage, aspiration devices). The reported very low air emissions of site 2 are verified and proved to be correct (very low Cd concentrations and gas flow rate; analysis done by extern laboratory).

- The calculated annual average Cd concentrations at a distance of 100 m from the point source vary between 0.001 ng/m3 (site 2) and 3.0 ng/m3 (site 1).

- Calculated PEClocalair vary between 0.6 ng/m3 and 3.6 ng/m3 (calculated regional background = 0.55 ng/m3).

Table 3.1.149: Calculated total local PECair for Ni-Cd battery recycling plants in EU-16. PEC’s include background Cd.

| N° | Emission to air¶ | Number of emission days | annual average air concentration | PEClocalair,ann | year |
| --- | --- | --- | --- | --- | --- |
|  | kg d-1 |  | (100 m) ng m-³ | (100 m) ng m-³ |  |
| 1 | 0.01 | 355 | 3.0 | 3.6 | 2002 |
| 1 | 0.003 | 336 | 0.69 | 1.2 | 2004 |
| 2 | 5.3x10-6(a) | 360 | 0.001 | 0.6 | 2002 |
| 2bis | 0.003(b) | 330 | 0.6 | 1.2 | 2002 |

¶annual averages; (a) Submitted air emissions are checked versus the analysis report and proved to be correct. Air emissions are that low due to the fact that in air emission no considerable amount of Cd can be found (conc. 2.5 µg/m3) and the fact that the gas stream is very low due to technical reasons (78 m3/h max). (b) Emissions from Cd recycling unit on the site of battery manufacturing plant 2.

Production of Cd containing pigments

- Daily stack emissions to air vary between 0.01 kg Cd/d (site A, C) and 0.02 kg Cd/d (site B).

- Calculated annual average Cd concentrations at a distance of 100 m from the point source vary between 1.9 ng/m3 (site A, C) and 4.3 ng/m3 (site B).

- Calculated PEClocalair values vary between 2.5 and 4.8 ng/m3 (calculated regional background = 0.55 ng/m3).

Table 3.1.150: Calculated total local PECair for Cd pigment producing plants in EU-16. PEC’s include background Cd.

| N° | Emission to air ¶ | Number of emission days | annual average air concentration | PEClocalair,ann | year |
| --- | --- | --- | --- | --- | --- |
|  | kg d-1 |  | (100 m) ng m-³ | (100 m) ng m-³ |  |
| A | 0.01 | 230 | 1.9 | 2.5 | 2002 |
| B | 0.02 | 318 | 4.3 | 4.8 | 2002 |
| C | 0.01 | 250 | 2.2 | 2.8 | 2002 |

¶annual averagesProduction of Cd containing stabilisers

- Daily stack emissions to air vary between 0.002 kg Cd/d (site Y) and 0.003 kg Cd/d (site X).

- Calculated annual average Cd concentrations at a distance of 100 m from the point source vary between 0.08 ng/m3 (site Y) and 0.5 ng/m3 (site X).

- Calculated PEClocalair values vary between 0.6 and 1.0 ng/m3 (calculated regional background = 0.55 ng/m3).

Table 3.1.151: Calculated total local PECair for Cd stabiliser producing plants in EU-16. PEC’s include background Cd.

| N° | Emission to air ¶ | Number of emission days | annual average air concentration | PEClocalair,ann | year |
| --- | --- | --- | --- | --- | --- |
|  | kg d-1 |  | (100 m) ng m-³ | (100 m) ng m-³ |  |
| X | 0.003 | 220 | 0.5 | 1.0 | 2002 |
| Y | 0.002 | 50 | 0.08 | 0.6 | 2002 |

¶annual averages

Use of Cd/CdO in alloys, plating and other uses

For these uses, no site-specific update information was submitted in time to the Rapporteur.

###### Measured levels

Table 3.1.152: Summary of calculated versus measured levels in air for Cd/CdO producing/processing sectors.

| N° | Emission amount | PEClocalair Calculated (100 m) | measured ann.avg. air concentration | remarks | year |
| --- | --- | --- | --- | --- | --- |
|  | kg d-1 | ng m-³ | ng m-³ |  |  |
| Cd metal production |  |  |  |  |  |
| 1 | 0.08 | 23.7 | 5.6 | 300 m from emission point, measured with pourbaix (isokinetic) low volume sampler, year 2003 data. | 2003: measured 2002: modelled |
| 6 | 0.03 | 8.2 | 1.8 | 300 m NNW of Cd refinery (border of the site). Sampling device: DIGITEL DHA-80 (Riemer Messtechnik), high volume sampler, 500 l/min, 24 hours; pore size: 5µm (in-house analysis). Data are influenced by neighbouring harbour and industrial activities. | 2002 |
| 7 | 0.15 | 41.8 | 8.5 (± 14.94 st.dev.) (450 m NNW) 0.97 (± 1.06 st. dev.) (626 m SW) | 3 month period; 4 sampling points; 14 measurements per point; ICP-MS, NILU method U-22, Norwegian Institute of Air research (NILU), year 2003 data (external laboratory) | 2003: measured 2002: modelled |
| Cd oxide production |  |  |  |  |  |
| 12 | 0.026 | 5.6 | n.d.. | n.d.. | 2005 |
| 12 | 0.045 | 9.4 | n.d. | n.d. | 2004 |
| Ni-Cd battery production |  |  |  |  |  |
| 2 | 0.02 | 4.4 | n.d.. | n.d.. | 2002 |
| 3 | No data | No data | 4 | 200 m from stack, downwind. Measurements are carried out according to NFX 43.261 and NFX 43.006. |  |
| 4 | 0.01 | 3.2 | 0.3 | 50 m from property line to the NW; in direction of prevailing wind | 2002 |
| 6 | No update data |  |  |  |  |
| 7 | No update data |  |  |  |  |
| Ni-Cd battery recyling |  |  |  |  |  |
| 1 | 0.01 | 3.6 | 126(300 m N) 37 (300 m S) wind direction: from N or from S | Cd in PM 10; Sampling apparatus: High Volume System (Digitel DA 80); flow rate: 500 l/mn, 24 hours/day, more than 350 d/y. Analytical method: ICP, spectrophotometer. | 2002 |
| 1 | 0.003 | 1.2 | 21 (300m N)* 15 (300m S) wind direction: from N or from S | Cd in PM 10; Sampling apparatus: High Volume System (Digitel DA 80); flow rate: 500 l/mn, 24 hours/day, more than 350 d/y. Analytical method: ICP, spectrophotometer | 2004 |
| 2 | 5.3x10-6 | 0.6 | n.d.. | n.d.. | 2002 |
| 2bis | 0.003 | 1.2 | n.d.. | n.d.. | 2002 |
| Cd pigments production |  |  |  |  |  |
| A | 0.01 | 2.5 | n.d.. | n.d.. | 2003 |
| B | 0.02 | 4.8 | n.d.. | n.d.. | 2003 |
| C | 0.01 | 2.8 | n.d.. | n.d.. | 2003 |
| Cd stabiliser producton |  |  |  |  |  |
| X | 0.003 | 1.0 | n.d.. | Cd concentration in air of the surroundings of the plant is considered to be negligible or very close to zero. | 2002 |
| Y | 0.002 | 0.6 | n.d.. | n.d.. | 2002 |

n.d.: no data available; *: the reduction in air concentrations in 2004 –as compared to 2002- is a result of the measures taken to reduce point and diffuse air emissions from the site (improvement in building coverage/aspiration device and improved air treatment systems (two rows of filters) (ISO 14000 certificate)).

Reduction in emission data of 2002 (and possibly later year(s)) compared to previously reported and assessed data of 1996 should be seen in the light of the information given under section 3.1.2.3 and per sector in the paragraph starting with ‘significant changes in production/emission reduction measures’.

Table 3.1.153: Summary of calculated versus measured aerial deposition levels for Cd/CdO producing/processing sectors.

| N° | Emission amount | Aerial deposition calculated | Aerial deposition measured | remarks | year |
| --- | --- | --- | --- | --- | --- |
|  | kg d-1 | mg/m2.d | mg/m2.d |  |  |
| Cd metal production |  |  |  |  |  |
| 1 | 0.08 | 8.33x10-4 | 0.1 | average of 8 sampling points, average distance 1 km, deposition measurements with Bergerhoff collecting measurements, year 1996-1998). No individual data for points provided. The data are influenced by excavation activities on the plant area. | 2002-2003 |
| 6 | 0.03 | 2.74x10-4 | 6.4 mg/m2.d (300 m NNW) 4.5 mg/m2.d (1.2 km ENE) 2.4 mg/m2.d (750 m S) 2.7 mg/m2.d (1 km WNW) 1.7 mg/m2.d (1.2 km SW) | sampling in accordance with VDI 2119, Bergerhoff system, duration 1 month. Data are influenced by neighbouring harbour and industrial activities. | 2002 |
| 7 | 0.15 | 0.0015 | 0.008 | location: 500 m NNW, NILU, method ISO/DIS 4222.2 standard, n=12 | 2002 |
| Cd oxide production |  |  |  |  |  |
| 12 | 0.026 | 1.81x10-4 | n.d. |  | 2005 |
| 12 | 0.045 | 3.19x10-4 | n.d. |  | 2004 |
| Ni-Cd battery production |  |  |  |  |  |
| 2 | 0.02 | 1.37x10-4 | n.d. |  | 2002 |
| 3 | n.d. | n.d. | n.d. |  | 2002 |
| 4 | 0.01 | 9.59x10-5 | n.d. |  | 2002 |
| 6 | No update data |  |  |  |  |
| 7 | No update data |  |  |  |  |
| Ni-Cd battery recyling |  |  |  |  |  |
| 1 | 0.01 | 1.09x10-4 | n.d. |  | 2002 |
| 1 | 0.003 | 2.49x10-5 | n.d. |  | 2004 |
| 2 | 5.3x10-6 | 5.21x10-8 | n.d. |  | 2002 |
| 2bis | 0.003 | 2.33x10-5 | n.d. |  |  |
| Cd pigments production |  |  |  |  |  |
| A | 0.01 | 6.85x10-5 | n.d. |  | 2003 |
| B | 0.02 | 1.53x10-4 | n.d. |  | 2003 |
| C | 0.01 | 7.95x10-5 | n.d. |  | 2003 |
| Cd stabiliser producton |  |  |  |  |  |
| X | 0.003 | 1.75x10-5 | n.d. |  | 2002 |
| Y | 0.002 | 2.74x10-6 | n.d. |  | 2002 |

n.d: no data available

###### Comparison of PECs with measured data

Measured Cd concentrations in air –presented in Table 3.1.152 - are available for Cd metal production site 1, 6 and 7; Ni-Cd battery producing site 3, 4 and Cd recycling site 1.

- For metal production site 1, the measured annual average Cd concentration in air at a distance of 300 m from the emission point is 5.6 ng/m3. The sampling is performed with a pourbaix low volume sampler (year 2003 data). The measured value is a factor of 4 below the modelled air concentration determined at 100 m from the emission point – i.e. 23.7 ng/m3.

- Metal production site 6 reports measured annual average air concentration at a distance of 300 m NNW of the border of the site of 1.8 ng/m3 (sampling device used: high volume sampler; 500 l/min, 24h, pore size: 5 µm). The measured value is situated a factor of 4.6 below the modelled PECair of 8.2 ng/m3 (100 m from site). Please note that these data are influenced by neighbouring industrial activities.

- Measured Cd concentrations in the surrounding air compartment are available for Cd metal production site 7. Measurements are performed at two different locations: 450 m NNW of site: 8.5 ± 14.9 ng/m3 and 626 m SW of the site: 0.97 ± 1.06 ng/m3 (year 2003 data). The highest measured concentrations are situated a factor of 4.9 below the modelled PECs. Measurements are performed according to NILU method U-22; and analysed by ICP-MS (National Environment Institute, 2003).

- Although Ni-Cd battery producer 3 reports that there are no air emission data available (not required); measured Cd concentrations at a distance of 200 m from the stack are reported: 4 ng/m3 (measurements carried out according to National standards NFX 43.261 and NFX 43.006).

- Battery manufacturing site 4 reports a measured annual Cd concentration in air of 0.3 ng/m3 at a distance of 50 m from the property line in the prevailing wind direction. The measured value is a factor of 10 below the modelled PECair at 100 m from the site of 3.2 ng/m3.

- Measured Cd concentrations in the surrounding air compartment are available for Ni-Cd battery recycling site 1. Measurements are performed at two different locations: 300 m N of site: 126 ng/m3 and 300 m S of the site: 37 ng/m3 (year 2002). The wind direction is from North or South. The sampling is performed with a high volume sampler, flow rate: 500 l/min, 24 h/d, >350d/y; analytical method: ICP, spectrophotometer, Cd in PM10. The highest measured concentration is situated a factor of 35 above the modelled PEC of 3.6 ng/m3. The lowest concentration is situated a factor of 10 above the modelled PECair. Year 2004 data indicate that Cd concentrations in air are reduced in comparison with previous years: 21 ng/m3 (300 m N) and 15 ng/m3 (300 m S) respectively. These values are situated a factor of 12.5-17.5 above the modelled air concentrations. The plant indicates that impact from other industrial sources is probable (but cannot be quantified).

In conclusion, only limited measured information is (made) available.

Moreover, measured data are stated by the companies to be (very probably) influenced by other sources (e.g. other industrial sources, traffic,…). However, only for one site, Cd metal producer site 7, the identification and approximate contribution of these other sources could be made based on the results of an extensive air monitoring programme. For recycler site 1 similar investigations are in preparation in collaboration with the national authority.

In general, the measured annual air concentration at a certain distance from the site is situated below the modelled PEClocalair. This may be due to the different distances from the source (the calculated assumes 100 m whereas the measured were at 300 – 450 m) or different reference years (e.g. 2003 measured versus 2002 for the calculated).

For the three production companies of cadmium metal, measured concentrations, including ‘background’ concentrations, range from 1.8 to 8.6 ng/m3. The range of calculated local Cair and PEC values in air is 8.2 - 41.8 ng/m3. For corresponding sites a comparison of these local monitoring data with the calculated local Cair values shows that the calculated Cair  is a factor 4 to 5 higher than the measured concentration at the respective site.

For battery producers some comparison is only possible for site 4 where the calculated value 3.2 ng/m3 is a factor 10.6 higher than the (limitedly documented) measured data (0.3 ng/m3).

The measured cadmium concentrations in air near the NiCd recyclers (site 1), ranging from 37 to 126 ng/m3 (2002) and from 15 to 21 ng/m3 (2004) are a factor 17.5 to 35 higher than the calculated local Cair for this site (0.6 to 3 ng/m3).

Both calculated and measured data will be taken forward to risk characterisation bearing however in mind the limitations of these values.

Measured aerial deposition rates –presented in Table 3.1.153 - are available for Cd metal production site 1, 6 and 7.

- For metal production site 1, the measured annual average deposition rates at a distance of 1 km from the emission point is 0.1 mg/m2.d (year 1996-1998 data). The measured data are situated two orders of magnitude above the modelled deposition rates of 8.33x10-4 mg/m2.d (year 2002 data, based on stack emissions only). The sampling is performed at 8 different sampling poins, located on average 1 km from the site. Bergerhoff collection methods are used to perform the sampling. It should be noted that the measured data are influenced by excavation activities in the plant area.

- Metal production site 6 reports measured annual average deposition rates at different locations: 6.4 mg/m2.d (300 m NNW); 4.5 mg/m2.d (1.2 km ENE); 2.4 mg/m2.d (750 m S); 2.7 mg/m2.d (1 km WNW) and 1.7 mg/m2.d (1.2 km SW). Relevant values (1.7-4.5 mg/m2.d; within 1000 m range as described in the TGD) are situated three orders of magnitude above the modelled aerial deposition value for the site of 2.74 x10-3 mg/m2.d. The sampling is performed in accordance with national guidelines VDI 2119 using Bergerhoff system, duration: 1 month. Please note that the deposition monitoring data are influenced by neighbouring harbour and industrial activities.

- Metal production site 7 reports a measured annual average deposition rate of 0.008 mg/m2.d measured at 500 m NNW of the site. The measured Cd deposition rate is five fold the deposition rate modelled by EUSES (i.e. 0.0015 mg/m2.d). The sampling is performed in accordance with ISO/DIS 4222.2 standard.

In conclusion, since metal production sites 1 and 6 indicate that:

- the reported measured deposition rates are influenced by excavation activities on the plant area (site 1) and neighouring harbour and industrial activities (site 6);

- fugitive emissions from both sites are reported to be minor in comparison with stack emissions (site 1) or are already included in the stack air emission estimation (site 6);

- the data from site 1 are rather outdated (1996-1998) (and in the meantime: excavation activities at the site are stopped),

it is judged that the measured aerial deposition rates for sites 1 and 6 do not fulfil the reliability and relevance criteria for further use of the data in PEClocalsoil modelling. Hence only the average aerial deposition rate reported for site 7 is taken forward for modeling purposes.

##### Non compartment specific effects relevant for the food chain

(Secondary poisoning)

No changes made.

#### Regional and continental exposure assessment

##### Regional and continental concentrations calculated according to the TGD

Calculation of the regional environmental exposure concentration is based on both point and diffuse sources over a wider (regional) area. The regional PEC also provides the Cd background concentration (anthropogenic+natural) that is incorporated in the calculation of the local PEC.

The point Cd emissions are rather well documented (e.g. 3.1.3.1). Some diffuse Cd emissions can also be rather well quantified such as Cd input from fertilisers or the total losses to the air based on deposition data (Tables 3.1.178 and 3.1.180). Total Cd emissions during use and from disposal of Cd containing products are more difficult to quantify.  Emissions of Cd from waste incineration and landfilling have been estimated in the TRAR/batteries’ related sections.

Data of the OECD 1995 questionnaire (Pearse, 1996) and, for The Netherlands, the RIVM 1997 data are used for calculating the regional and continental PEC values in the various environmental compartments. These data were not complete and the missing data were completed with emission data that were estimated by ERL (ERL, 1990), or other sources as indicated in Tables 3.1.154, 3.1.155 and 3.1.156.

Annual atmospheric emissions in the EU-16 amount to at least 124 ton Cd (Table 3.1.154). This value does not include natural sources of Cd emission (15 ton y-1, ERL 1990) such as emissions from mount Etna, sea spray, forest fires, weathering of Cd rich soils, etc. The contribution of the natural sources is included in the background which is added to the continental PEC’s (see 3.1.1).  The emission of the EU non-ferrous metal producers and of Cd processors is 14.4 ton Cd. This value corresponds well with the sum of the emissions of these industries estimated in each country. The major sources of atmospheric Cd emissions in the environment are oil/coal combustion (43%) and iron and steel production (24.7%). Large differences are noticed in estimated Cd emissions from oil/coal combustion. As an example ERL estimates 7.1 ton Cd emission from oil/coal combustion for the UK whereas the OECD data estimate 48.2 ton Cd emission for the UK (Pearse, 1996) and Berdowski et al. (1998) 4.5 ton Cd per year. Total Cd emission in the EU from oil/coal combustion is 49.3 ton (ERL, 1990) or 54 (table 3.1.154, data of Berdowski et al. (1998) and ERL (1990)). A roughly estimated EU average value of measured deposition is 1 g Cd g ha-1 y –1 (Table 3.1.180). This is equivalent to 356 ton Cd on the EU wide area. This value indiactes that the atmospheric Cd emissions (including natural) are about 2 fold underestimated. On the other hand, net deposition may also be overestimated because even wet-only deposition data can include Cd that is resuspended from soil. Analytical quality of measured data is also a major issue in this assessment. The EU average Cd deposition rate is predicted about 0.4 g Cd ha-1 y –1 (Table 3.1.180) and which is equivalent to 0.06 µg Cd L-1 in collected rain water (assume 700 mm rainfall y-1). Limits of quantification of Cd in water samples are often about 0.05 µg Cd L-1 in monitoring programmes.

Annual emissions in water are at least 39 ton Cd (Table 3.1.155). The available data are not comparable between EU countries since not all emissions were taken into account in each country. As an example, the Swedish Cd emission from municipal wastewater is 0.3 ton Cd/year. An extrapolation of this number to the EU on population basis, yields 12.7 ton Cd/year. It is unknown to what extent this value reflects a net emission to water. Waste water contains natural Cd (e.g. surface water contains 0.05µg L-1, dissolved natural Cd section 3.1.3.4.3) and carry Cd that is recycled within the environment (dust, organic matter, etc.). Data on Cd emission from waste water treatment plants in the different EU countries are scarcely available. The older data provided by ERL (ERL, 1990) estimated Cd emissions from non ferrous metal producers and Cd processors as large as 72 ton Cd/y. The updated data (Pearse, 1996) yield estimated emissions of only 11.1 ton Cd/y (table 3.1.155, all data refer to emissions after the STP). Stormwater and combined sewer overflows may not be entirely covered. Emissions to water through runoff from soil are not accounted in Table 3.1.155. The anthropogenic part of these emissions is, however, included in the PECwater calculations because the model (EUSES 1.0) assumes that a fraction of the emissions to soil is released to water. The natural part of these processes is included via the background Cd concentration that is added to the predicted added concentrations (section 3.1.1. Emissions of Cd to water from natural processes are estimated to be of the same order of magnitude or even larger than the anthropogenic emissions. The natural background of Cd (dissolved fraction only) is estimated 0.05 µg/l for the entire of Europe. At default values of water volumes in the European continent (320 109 m3) and the mean residence time of 166 days, this natural flux is equivalent to 35 ton Cd year-1 (dissolved Cd) or about 100 ton Cd year-1 (total). Natural Cd in water is obviously not all derived from runoff and erosion because other biogeochemical processes, such as fluxes of natural organic transfer, introduce metals into freshwater bodies.

Fertiliser Cd and atmospheric deposition are the major sources of Cd in agricultural soils. Soils receive a considerable fraction of total Cd emitted to the atmosphere.  The fraction surface area that is agricultural soil in EU is 0.27, therefore 0.27 x 124 ton Cd (34 ton Cd) emitted annually ends up in agricultural soils.  Fertiliser Cd is estimated to be 231 ton per year in the EU. The amount of Cd used in agriculture through sludge application is at least 13.6 ton y-1 (table 3.1.156).

The Cd released to natural and industrial soil is assumed to consist of atmospheric deposition only.  The fraction natural soil (surface based) is 0.6 and the fraction industrial soil is 0.1.  Emissions to the natural soils are therefore 0.6 x 124 =74 ton Cd/y and to industrial soil 0.1 x 126 = 12.4 ton Cd/y.

Table 3.1.154: direct atmospheric Cd emission in the EU-16 (ton Cd/y). Data combined from different source documents as indicated in footnotes. Note that EU totals of the non-ferrous metals producers do not match the sum of the emissions of each country. The EU totals are the most recent data and are based on confidential questionnaires.

|  | Cd alloys5 & batteries production & recycling12 | Cd/CdO production | other non-ferrous metals | production of iron and steel | oil/coal combustion | processing phosphates | municipal incineration13 | wood/peat combustion | other (cement, glass prod., traffic…) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Austria | 05 | 0.14,11 | 0.14,11 | 2.011 |  | 0.086 | 1.44 | 2.911 |
| Belgium | 05 | 24,11 | 1.911 | 311 | 0.14 | 0.063 |  | 0.811 |
| Denmark | 0.025 | 09 | 0.2 | 0.4511 |  | 0.300 |  | 1.411 |
| Finland | n.d.5 | 0.411 | 0.74 | 0.911 | n.d. | 0.014 |  | 1.611 |
| France | 0.245 | 0.2311 | 3.95,11 | 7.411 | 0.0311 | 1.92 |  | 0.024 |
| Germany | 0.185 | 5.311 | 10.511 | 14.2311 |  | 0.300 |  | 1.411 |
| UK | 0.265 | 6.711 | 2.911 | 4.4711 | 0.034 | 0.019 |  | 1.411 |
| Greece | 05 | 0.0211 | 0.711 | 1.611 |  | 05 |  | 2.2511 |
| Ireland | 05 | 0.0511 | 0.2311 | 0.611 |  | 05 |  | 0.711 |
| Italy | 0.045 | 2.25 | 4.65 | 6.35 |  | 0.351 |  | > 0.45,11 |
| Luxemburg |  |  | 0.911 | 0.2411 |  | 0.022 |  |  |
| Netherlands | 0.015 | 0.856,8 | 0.311 |  | 0.053 |  | 0.711 |
| Norway | n.d. | 0.2611 | 0.2811 | 0.1311 | n.d. | 0.041 | n.d. | 1.511 |
| Portugal | 05 | 0.0211 | 0.3411 | 1.411 |  | 0.003 |  | 1.211 |
| Spain | 0.015 | 0.0411 | 2.3411 | 10.511 | 0.5711 | 0.054 |  | > 2.85,11 |
| Sweden | n.d. | 1.44,11 | 1.211 | 0.411 |  | 0.005 | 0.34 |  |
| EU total | 0.8535, 12 | 3.92 | 9.73 | 31 | 54 | 0.7 | 3.2 | 1.7 | > 19 | TOTAL |
| % of total | 0.6% | 3.1% | 7.7% | 24.7% | 43.0% | 0.6% | 2.6%¶ | 1.4% | 15.1% | > 124 |

n.d.: no data; 1Norwegian Zn producer’s data (1994-1996); 2industry questionnaire of 1997; 3industry update based on 1995-1996 data and subtracting the emissions from Cd/CdO industry (Van Assche, 1998); 4OECD Cd questionnaire, 1995 (Pearse, 1996); 5emission data by ERL (1990); 6RIVM, 1997; 7data from 1991 and given by Pearse (1996); 8this value is estimated to consist of 0.05 ton Cd from non-ferrous industry and 0.8 ton Cd from iron and steel production; 9no non-ferrous metals producing industry in DK; 10Cd-Bilanz 1994 (Umweldbundesamt, 1996); 11Berdowsky et al., 1998; 12 & 13 measured and modelled emissions (see TRAR/batteries’ related sections)

Table 3.1.155: Cd emissions in the EU-16 to water (ton Cd/y). Data combined from different source documents as indicated in footnotes. Note that EU totals of the non-ferrous metals producers and of country totals do not match the sum of the emissions of each country. The EU totals are the most recent data and are based on confidential questionnaires.

|  | Cd plating12 & batteries production & recycling15 | Cd/CdO production | other non-ferrous metals | production of iron and steel | oil/coal combustion/ traffic | processing phosphates | municipal incineration 13 | MSW operational landfills 14 | metal mining | other (chem. industry, municipal wastewater) | TOTAL |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Austria |  |  | n.d. |  |  | 0.004 | 0.004 | 0 |  | 0.008 |
| Belgium |  | 0.54 | 0.44 |  | 1.84 | 0.012 | 0.0074 | 0 |  | 2.7 |
| Denmark |  | 09 | 0.15 |  |  | 0.016 | 0.001 | 0 |  | 0.1 |
| Finland |  | 0.14 | n.d. | n.d. | n.d. | 0.001 | 0.007 | n.d. |  | 0.1 |
| France |  | 2.44 | 0.14 |  | 7.34 | 0.097 | 0.096 |  |  | 9.8 |
| Germany |  | 0.210 | 6.35 |  |  | 0.108 | 0.99 |  |  | 6.5 |
| UK |  | 0.61 | 3.05 |  |  | 0.023 | 0.114 |  |  | 3.6 |
| Greece |  | 0.15 | 0.15 | -5 | -5 | 0 | 0.014 | n.d. | -5 | 0.2 |
| Ireland |  | 05 | <0.05 | -5 | -5 | 0 | 0.006 | n.d. | -5 | <0.05 |
| Italy |  | 0.0251 | 3.65 |  |  | 0.018 | 0.085 |  |  | 3.6 |
| Netherlands |  | 0.46 | 0.16 | x11 | 0.035 | 0.006 | 0 | 0.86 | 1.3 |
| Norway |  | 0.91 | n.d. |  |  | 0.003 | 0.008 | 0 |  | 0.9 |
| Portugal |  | 0.15 | 0.15 | -5 | -5 | 0.003 | 0.011 | n.d. |  | 0.2 |
| Spain |  | >2.5 | 1.85 | -5 | -5 | 0.012 | 0.072 | n.d. |  | >4.3 |
| Sweden |  | 0.14 | 0.14 | -4 | -4 | 0.013 | 0.017 | 1.14 | 0.34 | 1.6 |
| EU total | 0.212+0.06515 | 1.22 | 9.73 | >15.6 | >0.1 | 9.1 | 0.354 | 0.55 | >1.1 | >1.2 | >39.2 |

n.d.: no data; 1Zn producer’s data of these countries(1994-1996); 2industry questionnaire of 1997; 3industry update based on 1995-1996 data and subtracting the emissions from Cd/CdO industry (Van Assche, 1998); 4OECD Cd questionnaire, 1995 (Pearse, 1996); 5emission data by ERL (1990); 6Milieucompendium, 2001; 7data from 1988 and given by Pearse (1996); 8this value is estimated to consist of 0.05 ton Cd from non-ferrous industry and 0.8 ton Cd from iron and steel production; 9no non-ferrous metals producing industry in DK; 10Cd-Bilanz 1994 (Umweldbundesamt, 1996); 11gypsum waste from the P fertiliser industry (15 ton Cd in 1985), this is expected to decrease to 1.2 ton in 1994 and 0 ton in 2000 (Speed, 1993) ; 12WS Atkins (1998); 13, 14 and 15: data from the TRAR/batteries’ related sections.

Table 3.1.156: annual Cd input into agricultural soils from phosphate fertilisers and sludge in European countries. Underlined values are used when different values were available for the same country

|  | Cd from phosphate fertilisers | Cd from sludge3 |
| --- | --- | --- |
|  | ton y-1 | ton y-1 |
| Austria | 2.91 | 0.1 |
| Belgium | 1.56 | >6 |
| Denmark | 0.7076 | 0.12 |
| Finland | 0.21 | 0.07 |
| Finland |  | 0.0425 |
| France | 922 | 1.58 |
| Germany |  | 1.27 |
| Germany | 20.41 | 2.41 |
| Germany¶ | 22.14 | 3.24 |
| Greece | 102 |  |
| Ireland | 7.46 | 0.01 |
| Italy | 442 |  |
| Netherlands | 31 | 0.4 |
| Norway | 0.0726 |  |
| Portugal | 52 |  |
| Spain | 302 |  |
| Sweden | 1.11 | 0.1 |
| Sweden |  | 0.13 (1996) |
| UK | 11.31 | 1.88 (1996) |
| EU total | 231 | >13.6 |

1data based on the OECD questionnaire (Pearse, 1996) 2Landner et al. (1996), data from 1990;3 Source: report from the commission to the council and the European Parliament on the implementation of community waste legislation Directive 86/278/EEC on sewage sludge for the period 1995-1997, data from 1997 unless otherwise stated; 4Kiene (1999); 5Finnish Environment Institute (1997); 6Hutton et al. (2001)

Computations of continental exposure concentrations are made by means of multimedia fate models based on the fugacity concept. These models are box models, consisting of a number of compartments - air, water, sediment and soil- which are considered homogeneous and well mixed. A chemical released into the model is distributed between the compartments according to the properties of both the chemical and the model environment. For metals the following types of fate processes are distinguished in the continental assessment:

- emission direct and indirect (STP)

- advective transport: deposition, run-off, and erosion.

The input of chemicals is regarded in the model as continuous and equivalent to continuous diffuse emission. For metals, all individual compounds are assumed to transform into the ionic species. The results from the models are steady-state concentrations, which can be regarded as estimates of long-term average exposure levels (TGD, 1996).

In the continental model, it is assumed that all Cd emissions enter into the continental environment. It is also assumed that no inflow of air and water across the boundaries of the continent occurs. Continental exposure concentrations are calculated based on the combined anthropogenic Cd emissions from all EU-16 countries (Tables 3.1.154 to 3.1.156) and on the background of Cd

PECcontinental = C_continental + background Cd

The C_contintental is the Cd concentration at continental scale that is related to Cd emissions by man (EUSES 1.0 calculations, see below). Background Cd is, by definition, the natural background for surface water and air and is the ambient Cd concentration measured in areas away from point source for soils and sediments (see 3.1.1).

Regional calculations are performed using a similar box model for a generic regional environment. This environment is not an actual region, but a hypothetical site with predefined environmental characteristics, the so-called 'standard environment'. A general standard region is represented by a typical densely populated area with an area of 200x200 km² and 20 million inhabitants, located in the margin of Western Europe (sum of EU Member States = continental scale). By default, it is assumed that 10% of the European production and use of Cd takes place within this area. Therefore

continental emission = 90% of total European emission

regional emission = 10% of total European emission

The PECregional is calculated from

PECregional= C_regional + PECcontinental

The C_regional is the Cd concentration at regional scale that is related to Cd emissions by man (EUSES 1.0 calculations, see below).

For the soil compartment, however, a second model was used in which country specific Cd emission data were used (section 3.1.3.4.2).

C_continental and C_regional are calculated with EUSES 1.0 (1997). The output of the model gives in fact the predicted added environmental concentrations at continental and regional scale (PECcon,add and PECreg,add). Therefore C_continental is considered as the calculated PECcon,add, and C_regional is calculated as the difference between PECreg,add and PECcon,add.

In the model calculations, the use of the physico-chemical properties of Cd are not appropriate, and estimated partition coefficients for soil, sediments and suspended matter are used instead (TGD Appendix VIII, 1996). The solid/liquid distribution coefficient in soil, KD, was set to 280 L kg-1 (see 3.1.3.1.4), the solid/water partition coefficient, Kp, of sediment and suspended matter were both set at 130 10³ L kg-1 (see 3.1.3.1.1, European average). The sensitivity of PECwater and PECsed to the choice of Kp is tested with additional model calculations, assuming the Kp of sediment and suspended matter equal to 17 103 L kg-1 or 224 103 L kg-1. The concentration of suspended solids was set to 15 mg L-1 in each scenario, both for the continental and the regional compartment.

Volatilisation is ignored for Cd, therefore the Henry-coefficient was set to 0 Pa m³ mol-1. Most of the Cd present in the atmosphere will be bound to aerosols. The vapour pressure was set to 10-10 Pa to ensure that the metal fraction associated to aerosols was equal to one. Biotic and abiotic degradation rates were considered not to be relevant and set to zero.

Two models are used to estimate the Cd concentration in agricultural soil. The first method follows the procedure of the TGD (1996) and is calculated by EUSES 1.0 (1997). The second model is based on the mass balance of Cd including detailed Cd immision onto soil (country based) from fertilisers, sludge and atmospheric deposition and including output through leaching and plant uptake. This model is described in detail section 3.1.3.4.2.

In the TGD model (Model I for soil), input sources for soil contamination include direct emission to soil, deposition from the atmosphere and emission of sewage sludge to agricultural soil. Three types of soil are distinguished: agricultural, natural and industrial. The Cd emissions from agricultural practice (fertilisers) are assumed not to affect natural or industrial soil. The diffuse Cd emissions from atmospheric deposition, traffic etc. are distributed between these 3 types of soil proportionally to the surface areas of the three types of soil. According to the TGD (1996) the fraction of surface area that is agricultural soils is 0.27, the fraction natural soil 0.6, and the fraction industrial soil 0.1.

The continental and calculated regional emission data and resulting regional PEC values are presented in Table 3.1.157 (details cfr Annex 3.1.1). The calculated values are averages for a general regional and general continental environment.

Table 3.1.157 : emission values, total concentration and total PEC values for the regional And continental environment.

| input continental (anthropogenic): |
| --- |
| amount released to air | 111.6 ton y-1 |
| amount released to surface water | 35.2 ton y-1 |
| amount released to agricultural soil (1) | 207.9 ton y-1 + 12.2 ton y-1 (sludge application) |
| amount released to natural soil(1) | 0 ton y-1 |
| amount released to industrial soil(1) | 0 ton y-1 |
| input regional (anthropogenic): |
| amount released to air | 12.4 ton y-1 |
| amount released to surface water | 3.9 ton y-1 |
| amount released to agricultural soil(1) | 23.1 ton y-1 + 1.4 ton y-1 (sludge application) |
| amount released to natural soil(1) | 0 ton y-1 |
| amount released to industrial soil(1) | 0 ton y-1 |
| results: | C_continental concentration | background(2) | C_regional |
| Concentration in air | ng m-³ | 0.15 | 0 | 0.40 |
| Concentration in agricultural soil | mg kgwwt -1 | 0.175 | 0.266 | 1.43 (not used)* |
| Concentration in natural soil | mg kgwwt -1 | 0.018 | 0.266 | 0.048 (not used)* |
| Concentration in industrial soil | mg kgwwt -1 | 0.018 | 0.266 | 0.048 (not used)* |
| Kp sediment/suspended matter = 130 103 L kg-1 |  |  |  |
| Concentration in surface water | µg L-1 | 0.01 | 0.05 | 0.05 |
| Concentration in sediment | mg kgwwt -1 | 0.48 | 0.77 | 2.64 |
| Kp sediment/suspended matter = 17 103 L kg-1 |  |  |
| Concentration in surface water | µg L-1 | 0.06 | 0.05 | 0.24 |
| Concentration in sediment | mg kgwwt -1 | 0.39 | 0.77 | 1.54 |
| Kp sediment/suspended matter = 224 103 L kg-1 |  |  |
| Concentration in surface water | µg L-1 | 0.006 | 0.05 | 0.03 |
| Concentration in sediment | mg kgwwt -1 | 0.48 | 0.77 | 2.76 |
| PEC values | PEC continental | PEC regional |
| PEC air | ng m-³ | 0.15 | 0.55 |
| PEC agricultural soil | mg kg-1wwt-1 | 0.441 | 0.363 (model 2)* |
| PEC natural soil | mg kgwwt -1 | 0.284 | 0.322 |
| PEC industrial soil | mg kgwwt -1 | 0.284 | 0.322 |
| Kp sediment/suspended matter = 130 103 L kg-1 |  |  |  |
| PEC surface water (dissolved fraction) | µg L-1 | 0.06 (selected) | 0.11 (selected) |
| PEC sediment | mg kgwwt -1 | 1.25 (selected) | 3.88 (selected) |
| Kp sediment/suspended matter = 17 103 L kg-1 |  |  |
| PEC surface water (dissolved fraction) | µg L-1 | 0.11 | 0.35 |
| PEC sediment | mg kgwwt -1 | 1.16 | 2.70 |
| Kp sediment/suspended matter = 224 103 L kg-1 |  |  |
| PEC surface water (dissolved fraction) | µg L-1 | 0.06 | 0.09 |
| PEC sediment | mg kgwwt -1 | 1.25 | 4.01 |

*See note in text for discussion; (1) not including atmospheric deposition; (2) natural (water and air) or ambient (soil and sediment) background Cd, section 3.1.3.4.3.

The estimated Cregional for agricultural soils is high and exceeds ambient Cd concentrations (see 3.1.3.4.4). The PEC’s calculated by EUSES 1.0 refer to the ‘steady state’ concentrations in the environment. Cadmium has a very long residence time in soil (elimination half-life is about 380 years with default parameters) and, therefore, steady state may not be achieved within the next centuries. The assumption in the model is that 10% of the continental emissions take place within the area of a standard regional system, i.e. 10% of the continental emissions (mainly diffuse emissions) are deposited in only 1% of the total European area. Fertiliser application is the dominant source of Cd in agricultural soils (Tables 3.1.156 and 3.1.157) and are 231 ton Cd y-1.  The fraction of surface area that is agricultural is 0.27, therefore the area of agricultural soil in that region is 0.27*4 104 km2 = 1.08 104 km2.  The predicted emission of Cd trough fertiliser at the regional scale is 10% of 231 ton/year or the flux is 23.1 ton/(1.08 104 km2)= 25.5 g Cd ha y-1.  This is about tenfold higher than the emission data found for most European countries (Table 3.1.178). The parameter values in EUSES could be adjusted but there are a number of reasons to use alternative (existing) soil mass balances (3.1.3.4.2) rather than EUSES (e.g. modelling the transient state rather than the steady state, modelling Cd losses from background Cd due to crop offtake and leaching, etc.). Input and output parameters of the alternative model will be selected to represent different land use (agricultural) scenario’s in EU.  Therefore, PECregionalsoil for agricultural soils will be calculated with an alternative model and the outcome of this model (=0.36 mg Cd kg-1ww) will be used instead of the values given in Table 3.1.15. The PECregionalsoil, calculated with the alternative model  is lower than the PECcontinentalsoil.that is calculated with EUSES (Table 3.1.157). This is unusual but is inherent to the EUSES assumption that Cd output from soil (leaching) is calculated for the added Cd only, i.e. it assumes that ambient Cd in soil cannot be removed from soil. This is incorrect as the availability of added and ambient Cd is not strongly different (see 3.2.2) and ambient Cd in soil is the major source of Cd in leachates and crop Cd. The alternative model (3.1.3.4.2) assumes that all Cd in soil (natural background+ historic additions+current additions) can be equally lost from soil by leaching or crop offtake, leading to higher Cd output than estimated by EUSES. The EUSES calculations, will, however be used to estimate the PECregionalsoil for natural soils and industrial soils because the alternative model has not been used to derive specific values for such soils. No fertiliser emissions take place on these soils, i.e. the regional emissions for natural and industrial soils in EUSES may represent realistic values in contrast with agricultural soils (see above). Even though the EUSES predicted values refer to steady state conditions for the industrial and natural soils (i.e. concentration in a far future), these choices will not affect the conclusion of this risk assessment as will be shown in section 3.3.

Increasing the Kp value of suspended matter and sediment by a factor 13, from 17 103 l kg-1 to 224 103 l kg-1, decreases the predicted regional Cd concentration in surface water by a factor 4, from 0.35 µg L-1 to 0.09 µg L-1, which corresponds to the background concentration. The PECsediment only increases by a factor 1.5. At lower Kp, more Cd remains in solution (higher Cd concentration in dissolved fraction) and less Cd will be sorbed on particles (lower Cd concentration in sediment/suspended matter).

Varying the the solid-liquid Cd distribution coefficient (KD) in soil tenfold above or below the selected value strongly affects the PECsoil values as calculated with EUSES, but affects the PECwater by maximally 20%. The PECsoil values predicted with EUSES are sensitive to the KD because EUSES predicts concentrations at steady stades which are reached after varying periods depending on the KD (which control the output). In other words, PECsoils compared for different KD values are compared at different times after contamination.

Cadmium disposal scenarios have been calculated in the Targeted Risk Assessment Report on batteries (see batteries’ related sections).

###### Contribution of batteries’ related life-cycle steps

In order to compare the global regional Cd emissions with the regional/continental Cd emissions during the life cycle of Ni-Cd batteries an overview of these releases is given in Tables 3.1.158-3.1.167. The regional/continental cadmium emission of the disposal phase originating from all products containing cadmium in MSW can be found in Table 3.1.35 (incineration current situation), Table 3.1.39 (incineration future situation) and Table 3.1.55 (landfills).

Table 3.1.158: Summary of regional releases in kg/year of Cd to different environmental compartments during the total life cycle of a Ni-Cd battery (realistic scenario: 24.4 % incineration and 75.6 % landfilling. Scenario 10 mg/kg dry wt.)

| Life cycle stages | Regional releases in kg/year |
| --- | --- |
|  | Air | Water | Urban/ind. soil/agr. soil | Ground-water | Total release |
| 1 Manufacturing of Ni-Cd batteries and/or battery packs | 29 | 35.4 | 0 | 0 | 64.4 |
| 2 Incorporation into battery powered devices and applications | 0 | 0 | 0 | 0 | 0 |
| 3 Use, recharging and maintenance by end users | / | / | / | / | / |
| 4 Recycling Collection Processing Recovery | 1.8 | 0.1 | 0 | 0 | 1.9 |
| 5. Disposal (10-50% Ni-Cd batteries contribution) Incineration (24.4 %) Landfilling (75.6 %) | 32-162 N/A | 4-18 5-24 | N/A 6-28 | N/A 1-6 | 36-180 12-62 |
| Total | 63-193 | 45-78 | 6-28 | 1-6 | 115-308 |

/ =  no direct emissions. Indirect cadmium emissions  associated with the energy consumption used to recharge the

batteries are deemed negligible

N/A = Not applicable

Table 3.1.159: Summary of regional releases in kg/year of Cd to different environmental compartments during the total life cycle of a Ni-Cd battery (worst case scenario: 100% incineration. Scenario 10 mg/kg dry wt.)

| Life cycle stages | Regional releases in kg/year |
| --- | --- |
|  | Air | Water | Urban/ind. soil/agr. soil | Total release |
| 1 Manufacturing of Ni-Cd batteries and/or battery packs | 29 | 35.4 | 0 | 64.4 |
| 2 Incorporation into battery powered devices and applications | 0 | 0 | 0 | 0 |
| 3 Use, recharging and maintenance by end users | / | / | / | / |
| 4 Recycling Collection Processing Recovery | 1.8 | 0.1 | 0 | 1.9 |
| 5. Disposal (10-50% Ni-Cd batteries contribution) Incineration (100%) Landfilling (0%) | 140-701 N/A | 14-72 N/A | N/A N/A | 154-773 N/A |
| Total | 171-730 | 50-108 | 0 | 220-839 |

/ =  no direct emissions. Indirect cadmium emissions  associated with the energy consumption used to recharge the

batteries are deemed negligible

N/A = Not applicable

Table 3.1.160: Summary of regional releases in kg/year of Cd to different environmental compartments during the total life cycle of a Ni-Cd battery (worst case scenario: 100% landfilling. Scenario 10 mg/kg dry wt.)

| Life cycle stages | Regional releases in kg/year |
| --- | --- |
|  | Air | Water | Urban/ind. soil/agr. soil | Ground-water | Total release |
| 1 Manufacturing of Ni-Cd batteries and/or battery packs | 29 | 35.4 | 0 | 0 | 64.4 |
| 2 Incorporation into battery powered devices and applications | 0 | 0 | 0 | 0 | 0 |
| 3 Use, recharging and maintenance by end users | / | / | / | / | / |
| 4 Recycling Collection Processing Recovery | 1.8 | 0.1 | 0 | 0 | 1.9 |
| 5. Disposal (10-50% Ni-Cd batteries contribution) Incineration (0%) Landfilling (100%) | N/A N/A | N/A 7-26 | N/A 6-30 | N/A 1-6 | N/A 14-62 |
| Total | 31 | 43-62 | 6-30 | 1-6 | 81-129 |

/ =  no direct emissions. Indirect cadmium emissions  associated with the energy consumption used to recharge the

batteries are deemed negligible

N/A = Not applicable

Table 3.1.161: Summary of regional releases in kg/year of Cd to different environmental compartments during the total life cycle of a Ni-Cd battery (Future scenario: 100% incineration. Scenario 13.2 mg/kg dry wt.)

| Life cycle stages | Regional releases in kg/year |
| --- | --- |
|  | Air | Water | Urban/ind. soil/agr. soil | Total release |
| 1 Manufacturing of Ni-Cd batteries and/or battery packs | 29 | 35.4 | 0 | 64.4 |
| 2 Incorporation into battery powered devices and applications | 0 | 0 | 0 | 0 |
| 3 Use, recharging and maintenance by end users | / | / | / | / |
| 4 Recycling Collection Processing Recovery | 1.8 | 0.1 | 0 | 1.9 |
| 5. Disposal (32 % Ni-Cd batteries contribution) Incineration (100%) Landfilling (0%) | 449 N/A | 62 N/A | N/A N/A | 511 N/A |
| Total | 480 | 98 | 0 | 577 |

/ =  no direct emissions. Indirect cadmium emissions  associated with the energy consumption used to recharge the

batteries are deemed negligible

N/A = Not applicable

Table 3.1.162: Summary of regional releases in kg/year of Cd to different environmental compartments during the total life cycle of a Ni-Cd battery (Future scenario: 100% incineration. Scenario 24 mg/kg dry wt.)

| Life cycle stages | Regional releases in kg/year |
| --- | --- |
|  | Air | Water | Urban/ind. soil/agr. soil | Total release |
| 1 Manufacturing of Ni-Cd batteries and/or battery packs | 29 | 35.4 | 0 | 64.4 |
| 2 Incorporation into battery powered devices and applications | 0 | 0 | 0 | 0 |
| 3 Use, recharging and maintenance by end users | / | / | / | / |
| 4 Recycling Collection Processing Recovery | 1.8 | 0.1 | 0 | 1.9 |
| 5. Disposal (63 % Ni-Cd batteries contribution) Incineration (100%) Landfilling (0%) | 883 N/A | 218 N/A | N/A N/A | 1,101 N/A |
| Total | 914 | 254 | 0 | 1,167 |

/ =  no direct emissions. Indirect cadmium emissions  associated with the energy consumption used to recharge the

batteries are deemed negligible

N/A = Not applicable

Table 3.1.63: Summary of continental releases in kg/year of Cd to different environmental compartments during the total life cycle of a Ni-Cd battery (realistic scenario: 24.4 % incineration and 75.6 % landfilling. Scenario 10 mg/kg dry wt.)

| Life cycle stages | Continental releases in kg/year |
| --- | --- |
|  | Air | Water | Urban/ind. soil/agr. soil | Ground-water | Total release |
| 1 Manufacturing of Ni-Cd batteries and/or battery packs | 22 | 29.6 | 0 | 0 | 51.6 |
| 2 Incorporation into battery powered devices and applications | 0 | 0 | 0 | 0 | 0 |
| 3 Use, recharging and maintenance by end users | / | / | / | / | / |
| 4 Recycling Collection Processing Recovery | 0 | 0 | 0 | 0 | 0 |
| 5 Disposal (10-60% Ni-Cd batteries contribution) Incineration (24.4 %) Landfilling (75.6 %) | 291-1,455 N/A | 32-158 44-220 | N/A 50-250 | N/A 11-52 | 323-1,613 105-522 |
| Total | 313-1,477 | 106-408 | 50-250 | 11-52 | 479-2,187 |

/ =  no direct emissions. Indirect cadmium emissions  associated with the energy consumption used to recharge the

batteries are deemed negligible

N/A = Not applicable

Table 3.1.164: Summary of continental releases in kg/year of Cd to different environmental compartments during the total life cycle of a Ni-Cd battery (worst case: 100% incineration- Scenario 10 mg/kg dry wt.)

| Life cycle stages | Continental releases in kg/year |
| --- | --- |
|  | Air | Water | Urban/ind. soil/agr. soil | Total release |
| 1 Manufacturing of Ni-Cd batteries and/or battery packs | 22 | 29.9 | 0 | 51.6 |
| 2 Incorporation into battery powered devices and applications | 0 | 0 | 0 | 0 |
| 3 Use, recharging and maintenance by end users | / | / | / | / |
| 4 Recycling Collection Processing Recovery | 0 | 0 | 0 | 0 |
| 5 Disposal (10-50% Ni-Cd batteries contribution) Incineration (100%) Landfilling (0%) | 1,262-6,308 N/A | 130-649 N/A | N/A N/A | 1,392-6,957 N/A |
| Total | 1,284-6,330 | 160-679 | 0 | 1,444-7,009 |

/ =  no direct emissions. Indirect cadmium emissions  associated with the energy consumption used to recharge the

batteries are deemed negligible

N/A = Not applicable

Table 3.1.165: Summary of continental releases in kg/year of Cd to different environmental compartments during the total life cycle of a Ni-Cd battery (worst case scenario: 100% landfilling-Scenario 10 mg/kg dry wt.)

| Life cycle stages | Continental releases in kg/year |
| --- | --- |
|  | Air | Water | Urban/ind. soil/agr. soil | Ground-water | Total release |
| 1 Manufacturing of Ni-Cd batteries and/or battery packs | 22 | 29.6 | 0 | 0 | 51.6 |
| 2 Incorporation into battery powered devices and applications | 0 | 0 | 0 | 0 | 0 |
| 3 Use, recharging and maintenance by end users | / | / | / | / | / |
| 4 Recycling Collection Processing Recovery | 0 | 0 | 0 | 0 | 0 |
| 5 Disposal (10-50 % Ni-Cd batteries contribution) Incineration (0%) Landfilling (100%) | N/A N/A | N/A 50-238 | N/A 54-272 | N/A 12-57 | N/A 116-567 |
| Total | 22 | 80-268 | 54-272 | 12-57 | 168-619 |

/ =  no direct emissions. Indirect cadmium emissions  associated with the energy consumption used to recharge the

batteries are deemed negligible

N/A = Not applicable

Table 3.1.166: Summary of continental releases in kg/year of Cd to different environmental compartments during the total life cycle of a Ni-Cd battery (Future scenario: 100% incineration. Scenario 13.2 mg/kg dry wt.)

| Life cycle stages | Continental releases in kg/year |
| --- | --- |
|  | Air | Water | Urban/ind. soil/agr. soil | Total release |
| 1 Manufacturing of Ni-Cd batteries and/or battery packs | 22 | 29.6 | 0 | 51.6 |
| 2 Incorporation into battery powered devices and applications | 0 | 0 | 0 | 0 |
| 3 Use, recharging and maintenance by end users | / | / | / | / |
| 4 Recycling Collection Processing Recovery | 0 | 0 | 0 | 0 |
| 5 Disposal (32 % Ni-Cd batteries contribution) Incineration (100%) Landfilling (0%) | 4,037 N/A | 554 N/A | N/A N/A | 4,591 N/A |
| Total | 4,059 | 584 | 0 | 4,643 |

/ =  no direct emissions. Indirect cadmium emissions  associated with the energy consumption used to recharge the

batteries are deemed negligible

N/A = Not applicable

Table 3.1.167: Summary of continental releases in kg/year of Cd to different environmental compartments during the total life cycle of a Ni-Cd battery (Future scenario: 100% incineration. Scenario 24 mg/kg dry wt.)

| Life cycle stages | Continental releases in kg/year |
| --- | --- |
|  | Air | Water | Urban/ind. soil/agr. soil | Total release |
| 1 Manufacturing of Ni-Cd batteries and/or battery packs | 22 | 29.6 | 0 | 51.6 |
| 2 Incorporation into battery powered devices and applications | 0 | 0 | 0 | 0 |
| 3 Use, recharging and maintenance by end users | / | / | / | / |
| 4 Recycling Collection Processing Recovery | 0 | 0 | 0 | 0 |
| 5 Disposal (54 % Ni-Cd batteries contribution) Incineration (100%) Landfilling (0%) | 7,948 N/A | 1,960 N/A | N/A N/A | 9,908 N/A |
| Total | 7,970 | 1,990 | 0 | 9,960 |

/ =  no direct emissions. Indirect cadmium emissions  associated with the energy consumption used to recharge the

batteries are deemed negligible

N/A = Not applicable

The C_continental and C_regional for the Ni-Cd battery life cycle are calculated with EUSES 1.0. Three different scenarios are considered (realistic case: 24.4 % incineration; 75.6 % landfilling, worst case incineration: 100% incineration, 0% landfilling and worst case landfilling: 100% landfilling, 0% incineration). The contribution from the Ni-Cd batteries to MSW varies between 0.1 and 0.5 for the current scenarios. In addition the future scenarios with a battery contribution of 32 % and 63 % have also been calculated The output of the model gives in fact the predicted added environmental concentrations at continental and regional scale (PECcon, add and PECreg, add). Therefore C_continental is considered as the calculated PECcon, add, and C_regional is calculated as the difference between PECreg, add and PECcon, add.

The results are presented in the Tables 3.1.168-3.1.176.

Current situation

It can be concluded that for all scenarios investigated the added regional/continental concentrations calculated on the basis of the emissions from the Ni-Cd batteries life cycle only (indicated in bold) are very small. Due to the rather high Cd background concentrations for some environmental compartments (soil, sediment, surface water) the resulting PECregional and PECcontinental for these compartments are comparable to the overall regional/continental PECs (cfr Table 3.1.157).

Table 3.1.168:	Contribution of Ni-Cd batteries (fraction 0.1) to the overall Cd emissionvalues, total concentration and total PEC values for the regional and continental environment (incineration 24.4 %; landfilling 75.6 %). Scenario 10 mg/kg dry wt.

| input continental (anthropogenic): |
| --- |
| amount released to air | 313 kg/year |
| amount released to surface water | 106 kg/year |
| amount released to agricultural soil | 50 (sludge from STP landfill) |
| amount released to natural soil | 0 |
| amount released to industrial soil | 0 |
| input regional (anthropogenic): |
| amount released to air | 63 kg/year |
| amount released to surface water | 45 kg/year |
| amount released to agricultural soil(1) | 6 (sludge from STP landfill) |
| amount released to natural soil(1) | 0 |
| amount released to industrial soil(1) | 0 |
| results: | C_continental concentration | background(2) | C_regional |
| Concentration in air | ng m-³ | 3.8 x 10-13 | 0 | 6.8 x 10-12 |
| Concentration in agricultural soil | mg kgwwt -1 | 0.0001 | 0.266 | 0.00137 |
| Concentration in natural soil | mg kgwwt -1 | 0.00006 | 0.266 | 0.0011 |
| Concentration in industrial soil | mg kgwwt -1 | 0.00006 | 0.266 | 0.0011 |
| Kp sediment/suspended matter = 130 103 L kg-1 |  |  |  |
| Concentration in surface water | µg L-1 | 1.5 x 10-5 | 0.05 | 0.00024 |
| Concentration in sediment | mg kgwwt -1 | 0.0007 | 0.77 | 0.0122 |
| PEC values | PEC continental | PEC regional |
| PEC air | ng m-³ | 3.8 x 10-13 | 7.8 x 10-12 |
| PEC agricultural soil | mg kg-1wwt-1 | 0.266 | 0.267 |
| PEC natural soil | mg kgwwt -1 | 0.266 | 0.267 |
| PEC industrial soil | mg kgwwt -1 | 0.266 | 0.267 |
| Kp sediment/suspended matter = 130 103 L kg-1 |  |  |  |
| PEC surface water (dissolved fraction) | µg L-1 | 0.05 | 0.050 |
| PEC sediment | mg kgwwt -1 | 0.77 | 0.78 |

(1) not including atmospheric deposition; (2) natural or ambient background Cd, section 3.1.3.4.3.

Table 3.1.169:	Contribution of Ni-Cd batteries (fraction 0.5) to the overall Cd emission values, total concentration and total PEC values for the regional and continental environment (incineration 24.4 %, landfilling 75.6 %). Scenario 10 mg/kg dry wt.

| input continental (anthropogenic): |
| --- |
| amount released to air | 1,477 kg/year |
| amount released to surface water | 408 kg/year |
| amount released to agricultural soil | 250 (sludge from STP landfill) |
| amount released to natural soil | 0 |
| amount released to industrial soil | 0 |
| input regional (anthropogenic): |
| amount released to air | 193 kg/year |
| amount released to surface water | 78 kg/year |
| amount released to agricultural soil(1) | 28 (sludge from STP landfill) |
| amount released to natural soil(1) | 0 |
| amount released to industrial soil(1) | 0 |
| results: | C_continental concentration | background(2) | C_regional |
| Concentration in air | ng m-³ | 1.81 x 10-12 | 0 | 2.1 x 10-11 |
| Concentration in agricultural soil | mg kgwwt -1 | 0.00046 | 0.266 | 0.005 |
| Concentration in natural soil | mg kgwwt -1 | 0.00028 | 0.266 | 0.003 |
| Concentration in industrial soil | mg kgwwt -1 | 0.00028 | 0.266 | 0.003 |
| Kp sediment/suspended matter = 130 103 L kg-1 |  |  |  |
| Concentration in surface water | µg L-1 | 6.5 x 10-5 | 0.05 | 0.0006 |
| Concentration in sediment | mg kgwwt -1 | 0.0032 | 0.77 | 0.03 |
| PEC values | PEC continental | PEC regional |
| PEC air | ng m-³ | 1.81 x 10-12 | 2.3 x 10-11 |
| PEC agricultural soil | mg kg-1wwt-1 | 0.266 | 0.27 |
| PEC natural soil | mg kgwwt -1 | 0.266 | 0.27 |
| PEC industrial soil | mg kgwwt -1 | 0.266 | 0.27 |
| Kp sediment/suspended matter = 130 103 L kg-1 |  |  |  |
| PEC surface water (dissolved fraction) | µg L-1 | 0.05 | 0.051 |
| PEC sediment | mg kgwwt -1 | 0.773 | 0.80 |

(1) not including atmospheric deposition; (2) natural or ambient background Cd, section 3.1.3.4.3.

Table 3.1.170:	Contribution of Ni-Cd batteries (fraction 0.1) to the overall Cd emission values, total concentration and total PEC values for the regional and continental environment (incineration 100%, landfilling 0%). Scenario 10 mg/kg dry wt.

| input continental (anthropogenic): |
| --- |
| amount released to air | 1,284 kg/year |
| amount released to surface water | 160 kg/year |
| amount released to agricultural soil (1) | 0 (sludge from STP is landfilled) |
| amount released to natural soil(1) | 0 |
| amount released to industrial soil(1) | 0 |
| input regional (anthropogenic): |
| amount released to air | 171 kg/year |
| amount released to surface water | 50 kg/year |
| amount released to agricultural soil | 0 |
| amount released to natural soil | 0 |
| amount released to industrial soil | 0 |
| results: | C_continental concentration | background(2) | C_regional |
| Concentration in air | ng m-³ | 1.57 x 10-12 | 0 | 1.84 x 10-11 |
| Concentration in agricultural soil | mg kgwwt -1 | 0.00024 | 0.266 | 0.0028 |
| Concentration in natural soil | mg kgwwt -1 | 0.00025 | 0.266 | 0.0029 |
| Concentration in industrial soil | mg kgwwt -1 | 0.00025 | 0.266 | 0.0029 |
| Kp sediment/suspended matter = 130 103 L kg-1 |  |  |  |
| Concentration in surface water | µg L-1 | 0.00004 | 0.05 | 0.0004 |
| Concentration in sediment | mg kgwwt -1 | 0.002 | 0.77 | 0.02 |
| PEC values | PEC continental | PEC regional |
| PEC air | ng m-³ | 1.57 x 10-12 | 2 x 10-11 |
| PEC agricultural soil | mg kg-1wwt-1 | 0.266 | 0.269 |
| PEC natural soil | mg kgwwt -1 | 0.266 | 0.269 |
| PEC industrial soil | mg kgwwt -1 | 0.266 | 0.269 |
| Kp sediment/suspended matter = 130 103 L kg-1 |  |  |  |
| PEC surface water (dissolved fraction) | µg L-1 | 0.050 | 0.050 |
| PEC sediment | mg kgwwt -1 | 0.772 | 0.79 |

(1) not including atmospheric deposition; (2) natural or ambient background Cd, section 3.1.3.4.3.

Table 3.1.171:	Contribution of Ni-Cd batteries (fraction 0.5) to the overall Cd emission values, total concentration and total PEC values for the regional and continental environment (incineration 100%, landfilling 0%). Scenario 10 mg/kg dry wt.

| input continental (anthropogenic): |
| --- |
| amount released to air | 6,330 kg/year |
| amount released to surface water | 679 kg/year |
| amount released to agricultural soil (1) | 0 (sludge from WWTP is landfilled) |
| amount released to natural soil(1) | 0 |
| amount released to industrial soil(1) | 0 |
| input regional (anthropogenic): |
| amount released to air | 730 kg/year |
| amount released to surface water | 108 kg/year |
| amount released to agricultural soil | 0 |
| amount released to natural soil | 0 |
| amount released to industrial soil | 0 |
| results: | C_continental concentration | background(2) | C_regional |
| Concentration in air | ng m-³ | 7.8 x 10-12 | 0 | 7.9 x 10-11 |
| Concentration in agricultural soil | mg kgwwt -1 | 0.0012 | 0.266 | 0.012 |
| Concentration in natural soil | mg kgwwt -1 | 0.0012 | 0.266 | 0.012 |
| Concentration in industrial soil | mg kgwwt -1 | 0.0012 | 0.266 | 0.012 |
| Kp sediment/suspended matter = 130 103 L kg-1 |  |  |  |
| Concentration in surface water | µg L-1 | 0.00019 | 0.05 | 0.0015 |
| Concentration in sediment | mg kgwwt -1 | 0.0096 | 0.77 | 0.074 |
| PEC values | PEC continental | PEC regional |
| PEC air | ng m-³ | 7.8 x 10-12 | 8.7 x 10-11 |
| PEC agricultural soil | mg kg-1wwt-1 | 0.27 | 0.28 |
| PEC natural soil | mg kgwwt -1 | 0.27 | 0.28 |
| PEC industrial soil | mg kgwwt -1 | 0.27 | 0.28 |
| Kp sediment/suspended matter = 130 103 L kg-1 |  |  |  |
| PEC surface water (dissolved fraction) | µg L-1 | 0.05 | 0.052 |
| PEC sediment | mg kgwwt -1 | 0.78 | 0.85 |

(1) not including atmospheric deposition; (2) natural or ambient background Cd, section 3.1.3.4.3.

Table 3.1.172:	Contribution of Ni-Cd batteries (fraction 0.1) to the overall Cd emission values, total concentration and total PEC values for the regional and continental environment (landfilling 100%, incineration 0%). Scenario 10 mg/kg dry wt.

| input continental (anthropogenic): |
| --- |
| amount released to air | 22 kg/year |
| amount released to surface water | 80 kg/year |
| amount released to agricultural soil (1) | 54 (sludge from STP landfill) |
| amount released to natural soil(1) | 0 |
| amount released to industrial soil(1) | 0 |
| input regional (anthropogenic): |
| amount released to air | 31 kg/year |
| amount released to surface water | 43 kg/year |
| amount released to agricultural soil | 6 kg/year (sludge from STP (landfill) |
| amount released to natural soil | 0 |
| amount released to industrial soil | 0 |
| results: | C_continental concentration | background(2) | C_regional |
| Concentration in air | ng m-³ | 2.7 x 10-14 | 0 | 3.3 x 10-12 |
| Concentration in agricultural soil | mg kgwwt -1 | 5 x 10-5 | 0.266 | 0.00098 |
| Concentration in natural soil | mg kgwwt -1 | 4.2 x 10-6 | 0.266 | 0.00052 |
| Concentration in industrial soil | mg kgwwt -1 | 4.2 x 10-6 | 0.266 | 0.00052 |
| Kp sediment/suspended matter = 130 103 L kg-1 |  |  |  |
| Concentration in surface water | µg L-1 | 6.4 x 10-6 | 0.05 | 0.00019 |
| Concentration in sediment | mg kgwwt -1 | 0.00032 | 0.77 | 0.0093 |
| PEC values | PEC continental | PEC regional |
| PEC air | ng m-³ | 2.7 x 10-14 | 3.3x 10-12 |
| PEC agricultural soil | mg kg-1wwt-1 | 0.266 | 0.267 |
| PEC natural soil | mg kgwwt -1 | 0.266 | 0.267 |
| PEC industrial soil | mg kgwwt -1 | 0.266 | 0.267 |
| Kp sediment/suspended matter = 130 103 L kg-1 |  |  |  |
| PEC surface water (dissolved fraction) | µg L-1 | 0.050 | 0.05 |
| PEC sediment | mg kgwwt -1 | 0.770 | 0.78 |

(1) not including atmospheric deposition; (2) natural or ambient background Cd, section 3.1.3.4.3.

Table 3.1.173:	Contribution of Ni-Cd batteries (fraction 0.5) to the overall Cd emission values, total concentration and total PEC values for the regional and continental environment (landfilling 100%, incineration 0%). Scenario 10 mg/kg dry wt.

| input continental (anthropogenic): |
| --- |
| amount released to air | 22 kg/year |
| amount released to surface water | 268 kg/year |
| amount released to agricultural soil (1) | 272 (sludge from STP landfill) |
| amount released to natural soil(1) | 0 |
| amount released to industrial soil(1) | 0 |
| input regional (anthropogenic): |
| amount released to air | 31 kg/year |
| amount released to surface water | 62 kg/year |
| amount released to agricultural soil | 30kg/year (sludge from STP (landfill) |
| amount released to natural soil | 0 |
| amount released to industrial soil | 0 |
| results: | C_continental concentration | background(2) | C_regional |
| Concentration in air | ng m-³ | 2.7 x 10-14 | 0 | 3.3 x 10-12 |
| Concentration in agricultural soil | mg kgwwt -1 | 0.00023 | 0.266 | 0.0028 |
| Concentration in natural soil | mg kgwwt -1 | 4.2 x 10-6 | 0.266 | 5.2 x 10-4 |
| Concentration in industrial soil | mg kgwwt -1 | 4.2 x 10-6 | 0.266 | 5.2 x 10-4 |
| Kp sediment/suspended matter = 130 103 L kg-1 |  |  |  |
| Concentration in surface water | µg L-1 | 2.43 x 10-5 | 0.05 | 3.11 x 10-4 |
| Concentration in sediment | mg kgwwt -1 | 0.0012 | 0.77 | 0.0156 |
| PEC values | PEC continental | PEC regional |
| PEC air | ng m-³ | 2.7 x 10-14 | 3.3 x 10-12 |
| PEC agricultural soil | mg kg-1wwt-1 | 0.266 | 0.296 |
| PEC natural soil | mg kgwwt -1 | 0.266 | 0.267 |
| PEC industrial soil | mg kgwwt -1 | 0.266 | 0.267 |
| Kp sediment/suspended matter = 130 103 L kg-1 |  |  |  |
| PEC surface water (dissolved fraction) | µg L-1 | 0.05 | 0.05 |
| PEC sediment | mg kgwwt -1 | 0.77 | 0.79 |

(1) not including atmospheric deposition; (2) natural or ambient background Cd, section 3.1.3.4.3.

Future situation (incineration only)

The overall effect of a future possible increase in the total cadmium content of the MSW up to 24 mg/kg dry wt. is represented in Table 3.1.174.

Table 3.1.174 Contribution of all MSW waste to the overall Cd emission values, total concentration and total PEC values for the regional and continental environment (Future scenario 100%  incineration). Scenario 24 mg/kg dry wt.

| input continental (anthropogenic): |
| --- |
| amount released to air | 12,638 kg/year |
| amount released to surface water | 3,140.6 kg/year |
| amount released to agricultural soil (1) | 0 |
| amount released to natural soil(1) | 0 |
| amount released to industrial soil(1) | 0 |
| input regional (anthropogenic): |
| amount released to air | 1,433 kg/year |
| amount released to surface water | 381.5 kg/year |
| amount released to agricultural soil | 0 |
| amount released to natural soil | 0 |
| amount released to industrial soil | 0 |
| results: | C_continental concentration | background(2) | C_regional |
| Concentration in air | ng m-³ | 1.55 x 10-11 | 0 | 1.55 x 10-10 |
| Concentration in agricultural soil | mg kgwwt -1 | 0.0023 | 0.266 | 0.023 |
| Concentration in natural soil | mg kgwwt -1 | 0.0024 | 0.266 | 0.024 |
| Concentration in industrial soil | mg kgwwt -1 | 0.0024 | 0.266 | 0.024 |
| Kp sediment/suspended matter = 130 103 L kg-1 |  |  |  |
| Concentration in surface water | µg L-1 | 0.00047 | 0.05 | 0.0034 |
| Concentration in sediment | mg kgwwt -1 | 0.023 | 0.77 | 0.17 |
| PEC values | PEC continental | PEC regional |
| PEC air | ng m-³ | 1.55 x 10-11 | 1.7 x 10-10 |
| PEC agricultural soil | mg kg-1wwt-1 | 0.268 | 0.29 |
| PEC natural soil | mg kgwwt -1 | 0.268 | 0.29 |
| PEC industrial soil | mg kgwwt -1 | 0.268 | 0.29 |
| Kp sediment/suspended matter = 130 103 L kg-1 |  |  |  |
| PEC surface water (dissolved fraction) | µg L-1 | 0.050 | 0.054 |
| PEC sediment | mg kgwwt -1 | 0.79 | 0.97 |

(1) not including atmospheric deposition; (2) natural or ambient background Cd, section 3.1.3.4.3.

It can be concluded that the effect of an increase in MSW cadmium content up to 24 mg/kg dry wt. will have only a minor influence on the currently derived PECs regional for air, water and soil.  Therefore there is no need to revise the current PEC reg, water and the PEC reg, air in order to derive the PEC values for the future situation (3.1.3.2). The specific future contribution of Ni-Cd batteries to the overall PEC is given in Table 3.1.175-3.1.176 and is overall low.

Table 3.1.175	Contribution of Ni-Cd batteries (fraction 0.32) to the overall Cd emission values, total concentration and total PEC values for the regional and continental environment (Future scenario 100% incineration). Scenario 13.2 mg/kg dry wt.

| input continental (anthropogenic): |
| --- |
| amount released to air | 4,059 kg/year |
| amount released to surface water | 584 kg/year |
| amount released to agricultural soil (1) | 0 |
| amount released to natural soil(1) | 0 |
| amount released to industrial soil(1) | 0 |
| input regional (anthropogenic): |
| amount released to air | 480kg/year |
| amount released to surface water | 98 kg/year |
| amount released to agricultural soil | 0 |
| amount released to natural soil | 0 |
| amount released to industrial soil | 0 |
| results: | C_continental concentration | background(2) | C_regional |
| Concentration in air | ng m-³ | 4.97 x 10-12 | 0 | 5.2 x 10-11 |
| Concentration in agricultural soil | mg kgwwt -1 | 0.00074 | 0.266 | 0.0077 |
| Concentration in natural soil | mg kgwwt -1 | 0.00077 | 0.266 | 0.0081 |
| Concentration in industrial soil | mg kgwwt -1 | 0.00077 | 0.266 | 0.0081 |
| Kp sediment/suspended matter = 130 103 L kg-1 |  |  |  |
| Concentration in surface water | µg L-1 | 0.00013 | 0.05 | 0.001 |
| Concentration in sediment | mg kgwwt -1 | 0.0065 | 0.77 | 0.053 |
| PEC values | PEC continental | PEC regional |
| PEC air | ng m-³ | 4.97 x 10-12 | 5.7 x 10-11 |
| PEC agricultural soil | mg kg-1wwt-1 | 0.267 | 0.274 |
| PEC natural soil | mg kgwwt -1 | 0.267 | 0.275 |
| PEC industrial soil | mg kgwwt -1 | 0.267 | 0.275 |
| Kp sediment/suspended matter = 130 103 L kg-1 |  |  |  |
| PEC surface water (dissolved fraction) | µg L-1 | 0.050 | 0.051 |
| PEC sediment | mg kgwwt -1 | 0.777 | 0.83 |

(1) not including atmospheric deposition; (2) natural or ambient background Cd, section 3.1.3.4.3.

Table 3.1.176	Contribution of Ni-Cd batteries (fraction 0.63) to the overall Cd emission values, total concentration and total PEC values for the regional and continental environment (Future scenario 100%  incineration). Scenario 24 mg/kg dry wt.

| input continental (anthropogenic): |
| --- |
| amount released to air | 7,970 kg/year |
| amount released to surface water | 1,990 kg/year |
| amount released to agricultural soil (1) | 0 |
| amount released to natural soil(1) | 0 |
| amount released to industrial soil(1) | 0 |
| input regional (anthropogenic): |
| amount released to air | 914 kg/year |
| amount released to surface water | 254 kg/year |
| amount released to agricultural soil | 0 |
| amount released to natural soil | 0 |
| amount released to industrial soil | 0 |
| results: | C_continental concentration | background(2) | C_regional |
| Concentration in air | ng m-³ | 9.77 x 10-12 | 0 | 9.86 x 10-11 |
| Concentration in agricultural soil | mg kgwwt -1 | 0.0015 | 0.266 | 0.015 |
| Concentration in natural soil | mg kgwwt -1 | 0.0015 | 0.266 | 0.015 |
| Concentration in industrial soil | mg kgwwt -1 | 0.0015 | 0.266 | 0.015 |
| Kp sediment/suspended matter = 130 103 L kg-1 |  |  |  |
| Concentration in surface water | µg L-1 | 0.00030 | 0.05 | 0.0022 |
| Concentration in sediment | mg kgwwt -1 | 0.015 | 0.77 | 0.11 |
| PEC values | PEC continental | PEC regional |
| PEC air | ng m-³ | 9.77 x 10-12 | 1.1 x 10-10 |
| PEC agricultural soil | mg kg-1wwt-1 | 0.268 | 0.28 |
| PEC natural soil | mg kgwwt -1 | 0.268 | 0.28 |
| PEC industrial soil | mg kgwwt -1 | 0.268 | 0.28 |
| Kp sediment/suspended matter = 130 103 L kg-1 |  |  |  |
| PEC surface water (dissolved fraction) | µg L-1 | 0.050 | 0.053 |
| PEC sediment | mg kgwwt -1 | 0.79 | 0.90 |

(1) not including atmospheric deposition; (2) natural or ambient background Cd, section 3.1.3.4.3.

##### An alternative model predicting regional and continental concentrations in agricultural soils

# Model description

The predicted environmental Cd concentration in soil (PECsoil) is a critical parameter in the risk assessment of Cd. The Cd exposure to the general population is predominantly controlled by dietary intake of Cd (section 4.1.1.4: see RAR on Cd/CdO human part, in separate document) and, hence, by Cd in crops used for food production. Food Cd concentrations are related to soil Cd and increasing trends in soil Cd may result in increasing trends in dietary intake. It is known that Cd availability is not greatly reduced upon ageing in soil and, therefore, a reduced Cd input in soil does not warrant reduced crop Cd concentrations if soil Cd input still exceeds the Cd losses from the soil (Smolders et al., 1999 and references therein). Whereas Cd in air and in the aquatic compartments have reduced since the late 70’s in Europe, soil Cd concentrations may still increase with time (section 4.1.1.4.7: see RAR human part, in separate document). The relationship between Cd input in the agricultural environment and the resulting Cd concentrations in soil is discussed in this section.

A wealth of information exists on Cd balances in agricultural soils and this information will be used in an alternative soil Cd model. The alternative model is based on the Cd mass balance in the plough layer. The mass balance model calculates trends in soil Cd concentrations from the annual input-output balance and the existing Cd in soil. Cadmium mass balances in agricultural soils have been described before (Tjell and Christensen, 1992, Jensen and Bro-Rasmussen, 1992, Moolenaar and Lexmond, 1998, Hellstrand and Landner, 1998, Kiene, 1999) and are reproduced here with small modifications and updated information. The Cd mass balance offers distinct advantages over the EUSES 1.0 model for predicting soil Cd since the former (i) includes the main pathways of cadmium to and from agricultural soils and (ii) uses local Cd input rates that are measured and (iii) predicts future soil Cd concentrations at any time after t=0 in contrast with the EUSES predictions which are steady state concentrations that may only be reached after several decades. No distinction will be made between regional or continental scales, and the balances will be constructed for a number of conditions that are relevant in European agriculture.

The Cd mass balance is presented graphically in Figure 3.1.12. The Cd input in the agricultural soils mainly originates from the atmospheric deposition, from the fertilisation with phosphate fertilisers and from the application of manure or sludge. The main Cd fluxes out of the plough layer are leaching losses and removal of Cd with the harvested crop (=crop offtake). The input of Cd through manure or sludge application recycles some of the Cd that was previously removed from soil by crop offtake (see below).

It can be discussed that the Cd mass balance should be made on the whole rooting zone (i.e. 1 m) rather than on the plough layer. Losses of Cd by leaching out of the plough layer may indeed not be a reduction of risk for crop uptake as Cd may be retained in deeper horizons where it is still available for root uptake. However, because information on soil properties of deeper horizons is often lacking (e.g. total Cd, pore water concentrations, net water flux out of the rooting zone, rooting depth) it was preferred to focus on the plough layer only.

Fig. 3.1.12 The Cd input-output balance in agricultural soils

The Cd concentration in the topsoil at year i (Cdsoil,i, mg kg-1dw) is calculated from the net Cd balance (input-output, g ha-1 y-1) in year i-1 and the soil Cd concentration in year i-1 as

Cdsoil,i = Cdsoil,i-1 + (input-output)/(1000*Wsoil)

in which Wsoil represents the soil weight of the plough layer (kgdw ha-1). In all calculations presented below, Wsoil is assumed to be 3 106 kgdw (i.e., 0.23 m ploughing depth and 1300 kgdw m-3 bulk density). All data are calculated on dry soil weight basis. No data were found for Cd losses by erosion and it is furthermore assumed that these Cd losses are marginal. This model does not assume that a fraction of the wet deposition is lost to The aquatic environment (cfr. assumption in the EUSES 1.0 model). Input and output of Cd are discussed in detail below before predicting future trends in soil Cd.

Input of Cd in agricultural soil

Fertilisers

Phosphate fertilisers contain appreciable levels of Cd. The phosphate rock is the source of Cd and only a limited fraction of Cd is lost to the by-products during manufacture of high analysis fertiliser. As a result, the final Cd content in fertilisers, expressed on a unit P basis, is not very different from that in the rock phosphate, and the Cd:P ratio in the rock phosphate determines the fertiliser Cd content (McLaughlin et al., 1996). The Cd:P concentration ratio in rock phosphate varies from 1 to 640 mg Cd kg-1P. Typical low Cd rock phosphates (<100 mg Cd kg-1P) are those from Florida and Russia (Kola). Many rock phosphates from Africa (Morocco, Togo) contain average to high Cd levels (100-350 mg Cd kg-1P). More details on Cd levels in rock phosphates can be found in the compilation made by McLaughlin et al. (1996). The fertiliser industry has developed a process to remove cadmium from the phosphoric acid, which is used in the production of many phosphate fertilisers. However, this process has not been incorporated at industrial scale (IFA, 1998).

Based on data from 1990, the annual Cd input from phosphate fertilisers in the EEC countries was estimated to be 275-ton (Landner et al., 1996). This number was obtained from phosphate fertiliser consumption data and Cd concentration in these fertilisers ranging between 128 and 176 mg Cd kg-1P in different European countries. Current annual Cd input from phosphate fertiliser is somewhat reduced because of lower fertiliser consumption and because the Cd content in fertiliser is restricted (231 ton/y, Table 3.1.156 and 3.1.178). Between 1990 and 1995, annual consumption of phosphate fertilisers in West Europe has reduced from 4.5 million tons P205 to 3.6 million tons P205 (Statistics of the International Fertiliser Industry Association, Paris). During the last decade, several countries adopted limits of Cd content in fertilisers (Table 3.1.177). Table 3.1.178 lists input of Cd to agricultural soils from phosphate fertilisers in Europe. Most of the data are based on the OECD questionnaire (Pearse, 1996). The total Cd load in those EU-16 countries that responded to the 1995 questionnaire is about half of the value that was estimated based on the 1990 data (details not shown). The 1990 data are given for those EU countries that did not respond to the OECD questionnaire.

The annual Cd flux to agricultural soils from phosphate application varies from <0.1g ha-1 (Finland) to 4.5g ha-1 (The Netherlands). Most of the data are calculated from total P consumption per country, the Cd concentrations in fertilisers and the total arable surface in that country. Since these fluxes are country averages, they do not reflect the variance that exists between cropping systems. The highest Cd flux (The Netherlands) is a local value for an experimental arable farm using only mineral fertilisers (Moolenaar and Lexmond, 1998). The high flux of 3.2 g Cd ha-1y-1 in France is based on data from the late '80s. The present use of phosphate rock fertiliser in agriculture is further declining in Europe mainly due to the high production of manure and compost.

Table 3.1.177: maximum permissible and currently applied Cd concentrations P fertilisers in European countries (sources: International Fertiliser Industry Association, pers. comm.; Hutton et al., 2001 and references therein); value of Germany is based on a personal communication for the Umweltbundesamt, 2002.

| country | limit (mg Cd kg-1P) | from | Currently applied (mg Cd kg-1P) |
| --- | --- | --- | --- |
| Austria | 170 (max 20 g Cd ha-12y-1 on arable land, max 10 g Cd ha-12y-1 on grassland) | 1994 | 57 |
| Belgium | 210(voluntary) | 1994 | 75 |
| Denmark | 110 | 1995 | 34 |
| Finland | 50 | 1992 | 2.5 |
| Germany | 90 (voluntary) | 1984 | 80 |
| Norway | 100 | 1992 | 5.3 |
| Sweden | 100, above 5 mg kg-1 P, an environmental fee is raised of 30 SEK per g Cd | 1994 | < 20 |
| UK |  |  | 34 |

Other fertilisers than P fertilisers contain low and negligible Cd concentrations with the exception of trace element fertilisers (McLaughlin et al., 1996). The general impact of these fertilisers on total Cd input in agricultural soils is most likely low.  Lime may contain elevated Cd levels where it is a by-product of industrial processing.  KEMI (1996) reports Cd levels in Danish lime around 1 mg Cd kg-1.  An annual lime application of 300 kg is then equivalent to 0.3 g Cd ha-1. In Sweden, lime applications are estimated to import 0.02 g ha-1 y-1 (Hellstrand and Landner, 1998).

Table 3.1.178: annual Cd input into agricultural soils from phosphate fertilisers in European countries

| country | Cd input | source* |
| --- | --- | --- |
|  | ton | g ha-1 |  |
| Austria | 2.9 | 1.1 | 1 |
| Austria |  | 0.8 | 7 |
| Belgium | 1.5 | 0.59-1.40 | 7 |
| Denmark | 0.707 | 0.79-1.44 | 7 |
| France | 92 | 3.2 | 2 |
| Finland | 0.2 | <0.1 | 1 |
| Finland |  | 0.02-0.1 | 2 |
| Finland | 0.052 | 0.03 | 5 |
| Finland |  | 0.025 | 7 |
| Germany | 20.4 | 1.7 | 1 |
| Germany¶ | 22.1 | 1.28 | 6 |
| Greece | 10 | 2.8 | 2 |
| Ireland | 9 | 1.8 | 2 |
| Ireland | 7.4 | 1.67 | 7 |
| Italy | 44 | 3.0 | 2 |
| The Netherlands | 3 | 1.5 | 1 |
| The Netherlands |  | 4.5 | 3 |
| Norway | 0.072 | 0.12-0.21 | 7 |
| Portugal | 5 | 1.4 | 2 |
| Spain | 30 | 1.5 | 2 |
| Sweden | 1.1 | 0.5 | 1 |
| Sweden |  | 0.8 | 2 |
| Sweden |  | 0.20 | 4 |
| United Kingdom | 11.3 | 0.9 | 1 |
| United Kingdom |  | 1.0-2.1 | 7 |
| EEC (1990) | 231 | 2.5 | 2 |

*source: 1Pearse, 1996, data based on the OECD questionnaire (1995), conversion to Cd flux (g ha-1 y-1) made by Landner et al., 1995;2Landner et al., 1996, data from 1990;3Moolenaar and Lexmond, 1998; 4Hellstrand and Landner, 1998; 5Finnish Environment Institute, 1997; 6Kiene, 1999; 7 Hutton et al., 2001

Manure, compost and sludge

The Cd input into agricultural soil by application of animal manure recycles some of the Cd that was previously taken up by crops. Therefore, Cd input from manure is only a net input into agricultural soil at a continental scale if there is a net import of animal feed crops. No data were found on the net total Cd import in Europe by this pathway. In Sweden, it was estimated that a total of 155 kg Cd is imported annually through animal feeds to farms with animal production. This corresponds to a Cd influx of 0.05g Cd ha-1 y-1 at the national level (Hellstrand and Landner, 1998). Moolenaar and Lexmond (1998) estimated the average net Cd influx from imported animal feed (feed concentrates) as 0.05 g Cd ha-1 y-1 for a mixed farming system in The Netherlands. Kiene (1999) calculated the total Cd input via slurry and dung (gross input, no net input) to be 13 ton y-1 in Germany, equivalent to 0.76 g Cd ha-1y-1. Since these values are much lower than the total Cd load from P fertilisers, it is unlikely that manure application is an important net source of Cd in agriculture at the European level. A similar reasoning is made for compost.

Table 3.1.18 shows the Cd input into agricultural soils from manure application. The country average fluxes range from 0.4-2.1 g Cd ha-1 y-1. In The Netherlands, the Cd input from application of manure and compost is higher than that from the use of mineral fertilisers. This reflects the importance of the intensive livestock industry in that country (Pearse, 1996).

It should be noted that the Cd:P ratio in manure is lower than that in most mineral fertilisers. Moolenaar and Lexmond (1998) report Cd:P ratios of 18 mg Cd kg-1P in poultry manure and 47 mg Cd kg-1P in cattle manure. Manure samples from Belgium were found to contain 70 mg Cd kg-1P (cattle) or 43 mg Cd kg-1P (pig, Landner et al., 1996). Therefore, lower Cd input values are found in these farming systems where P from mineral fertiliser is (partly) replaced by P from manure. Local excesses in areas of intensive livestock industry have resulted in almost zero P-fertiliser consumption in some areas (e.g. Flanders, Belgium). In Sweden, more than 50 % of total P fertilisation was applied as manure-P in 1994-1995 (Hellstrand and Landner, 1998).

The application of sludge is an important source of Cd where it is applied. In the European countries listed in table 3.1.179, sewage sludge Cd load is estimated to be lower than fertiliser Cd load (exception: Belgium, Table 3.1.179). The country average fluxes of Cd from sewage sludge application are below 0.2 g ha-1 y-1 for those countries for which data were found. However, it must be stressed that these fluxes are country averages (i.e. total load divided by the area of arable land for each country) and are not reflecting the much higher flux where it is applied. These fluxes vary widely and depend on local restrictions on the use of sludge in agriculture. Legislation in EU-16 countries is either based on maximal Cd concentrations in sludge (i.e. 1.2-10 mg Cd kg-1) or maximum Cd fluxes (e.g. 3-15 g ha-1y-1). Some countries restrict a cumulative load (OECD, 1994).  Total Cd input from sludge in the EU-16 is estimated to be at least 11.6 ton y-1 (Table 3.1.156).

Table 3.1.179: annual Cd input into agricultural soils from manure, sludge, lime and compost in European countries. All flux data are country averages, i.e. total load divided by area of arable land and, hence, do not reflect The flux where it is applied.

| country | manure+compost | Sludge | lime | source |
| --- | --- | --- | --- | --- |
|  | ton | g ha-1 | ton | g ha-1 | g ha-1 |  |
| Austria | 1.3 |  | 0.1 | 0.04 |  | 1, 3 |
| Austria |  | 0.95 |  |  |  | 2 |
| Belgium |  | 1.7 | >6 |  |  | 1, 3 |
| Belgium |  | 0.78-2.66 |  | <0.01 |  | 5 |
| Denmark |  |  | 0.12 | 0.06 |  | 3 |
| Denmark |  |  |  | 1.45 | 0.4 | 5 |
| Finland | 0.2 |  | 0.07 | 0.02-0.05 |  | 3 |
| Finland |  | 0.322 |  |  | 0.035 | 5 |
| Germany |  |  | 1.27 |  |  | 3 |
| Germany |  |  | 2.4 |  |  | 1 |
| Germany¶ | 14.1 | 0.82 | 3.2 | 0.19 |  | 4 |
| Netherlands | 4.2 | 2.1 | 0.4 | 0.2 |  | 1, 3 |
| Norway |  |  |  |  | 0.02 | 5 |
| Sweden | 0.6-0.7 | 0.05(5) | 0.1 |  |  | 1 |
| Sweden |  |  | 0.13 |  |  | 3 |
| UK |  | 0.4 | 2.3 |  | 0.375-0.503 | 1 |

* source: 1 Pearse, 1996, data based on the OECD questionnaire (1995), conversion to Cd flux (g ha-1 y-1) made by Landner et al., 1996; 2Dachler and Kernmaeyr, 1997; 3Source: report from the commission to the council and the European Parliament on the implementation of community waste legislation Directive 86/278/EEC on sewage sludge for the period 1995-1997, data from 1997; 4Kiene (1999); 5Hutton et al. (2001)

Atmospheric deposition

The atmospheric deposition has been a major source of Cd in European agricultural soils in the past. As a result of increased emission control, atmospheric Cd deposition notably decreased over the last decades (see also section 3.1.3.4.3). Therefore, only more recent data (>1985) are included in this section. Total atmospheric deposition includes wet and dry deposition. It can be argued that the dry Cd deposition is not completely a net Cd input into soil on a regional or larger scale. Dry deposition contains Cd that was previously removed from other locations. Total deposition in rural areas is, however, dominated by wet deposition (CCRX, 1991).

Table 3.1.180 shows the measured atmospheric Cd deposition in rural areas of different EU-16 countries. The deposition values range between 0.15 and 4 g ha-1 y-1, depending on country and on sampling method. The deposition values generally decrease from North- to Central Europe. No deposition data for southern European countries were found. The EU-16 average is calculated based on total atmospheric emission data at EU-16 scale (Table 3.1.154) and an area of 3.56 106 km². The calculated EU-16 average is 0.4 g ha-1 y –1 and is lower than most measured data (e.g. Dutch averages, about 1 g ha-1 y –1). It is unknown if the net deposition is overestimated (even wet-only deposition data can include Cd that is resuspended from soil) or if the estimated total Cd emission is underestimated.

Table 3.1.180: atmospheric Cd deposition in rural areas of European countries (measured, Eu-16 average is calculated).

| country | Cd deposition g ha-1 y-1 | comments | source |
| --- | --- | --- | --- |
| Austria | 2.61 | Lower Austria (1987) | BFL, 1997 |
| Austria | 0.4-0.62 | original reference from 1994 | BFL, 1997 |
| Austria | 2.1 | National mean (wet+dry deposition) | Hutton et al., 2001 |
| Belgium | 3.63 | 1 rural site at Belgian coast; 1995-1997 | VMM, 1999 |
| Belgium | 1.15 |  | Landner et al., 1995 |
| Denmark | 1.53 |  | Jensen and Bro-Rasmussen, 1992 |
| Denmark | 1.15 |  | Landner et al., 1995 |
| Denmark | 0.41 | bulk deposition (wet deposition) | Hutton et al., 2001 |
| Finland | 0.2-0.41 | original reference from 1995 | Landner et al., 1995 |
| Finland | 0.09-0.35 | gradually from north to south Finland | Hutton et al., 2001 |
| France | 24 | southern France, 1985-1986 | Jensen and Bro-Rasmussen, 1992 |
| Germany | 1.4-4.0 | field measurements ("wet only" and "bulk") | Bachmann et al., 1998 |
| Germany | 4 | wet only measurements | Kiene, 1999 |
| Netherlands | 1.24 | average of 14 sampling points in 1992 | CCRX, 1994 |
| Netherlands | 0.95 |  | Landner et al., 1995 |
| Norway | 0.2-1.2 | north -south, 1985-1986 | Jensen and Bro-Rasmussen, 1992 |
| Norway | 0.37 | average value for Norway | Hutton et al., 2001 |
| Sweden | 0.6-1.12 | two districts in Sweden, original reference from 1994 | Eriksson et al., 1996 |
| Sweden | 0.15-0.64 | north -south, 1996 | Hellstrand and Landner, 1998 |
| Sweden | 0.4-1.55 |  | Landner et al., 1995 |
| UK | 25 |  | Landner et al., 1995 |
| UK | 1.8 | median value of 29 rural sites | Hutton et al., 2001 |
| EU-16-average predicted | 0.4 | 126 ton y-1 deposited over 3.56 106 km2 | this study |

1methodology unknown; 2deposition calculated from Cd in moss;3total deposition;4wet deposition; 5based on OECD questionnaire (Pearse, 1996) with recalculations made in Landner et al., 1995.

Output of Cd from agricultural soils

Leaching

The Cd losses by leaching out of the plough layer are difficult to quantify in agricultural soils. The estimated losses of Cd from the plough layer are generally smaller than 1 % per year (Landner et al., 1995). Therefore, downward movement of Cd is only detectable in long-term observations.

Detailed Cd leaching studies at the field scale have been performed for a number of polluted soils (e.g. Streck and Richter, 1997 and references therein). No such studies or model predictions were found for agricultural soils at an ambient Cd concentration. Therefore, Cd losses by leaching are estimated here based on a simplified model that is commonly used in Cd mass balance studies. The annual leaching losses L (g Cd ha-1y-1) is estimated as the Cd concentrations in pore water multiplied by the annual net water flux (also called the precipitation excess), formally:

in which [Cd]l represents the Cd concentration in the liquid ((g L-1) and F is the annual precipitation excess (m). A typical values for F in temperate regions is 0.2 m y-1. The concentration of Cd in pore water is calculated from the solid-liquid distribution coefficient KD (L/kg) and the soil Cd concentration (section 3.1.3.1.4).

Despite a high correlation between KD and soil properties (Table 3.1.88, section 3.1.3.1.4), large systematic variations in predicted KD values exist among the different studies. As an examples, for a typical arable soil of the temperate regions with pH 6.5 and 2 % OM (1.2%C), predicted KD values range between 90 and 1560 L kg-1 depending on the regression equations. Effectively, the uncertainty in the KD results in an equal uncertainty in the predicted annual Cd losses per unit of excess precipitation.

Table 3.1.181 shows the predicted Cd leaching from an agricultural soil at an ambient Cd concentration for different soil properties. This table shows that the predicted Cd leaching strongly depends on the soil pH and on the type of regression equation. As will be shown below, this uncertainty will imply that it is impossible to predict if Cd will accumulate in soil or not in low Cd input cropping systems. Therefore, we feel that more accurately estimating average Cd losses by leaching is critical for predicting future trends in average soil Cd in Europe.

There is little experimental evidence that could be used to validate the model that estimates Cd leaching losses. The predicted annual Cd losses from the plough layer (0.3-26 g ha-1 y-1) are generally higher than those estimated in most other soil Cd balances (typically <2 g ha-1 y-1, Tjell and Christensen, 1992, Jensen and Bro-Rasmussen, 1992, Moolenaar and Lexmond, 1998, Hellstrand and Landner, 1998). Nicholson et al., (1996) estimated Cd leaching from the unlimed long-term park grass soils of Rothamsted (UK) using the Cd mass balance. The increase of Cd in the 0-22.5 cm horizon during 1913-1983 was compared with the Cd input by atmospheric deposition (estimated) and by phosphate fertilisers (based on analysis). After accounting for a small (measured) Cd loss by crop offtake, the leaching losses were found to vary between 0.7-3.1 g ha-1 y-1(untreated) and 2.4-4.9 g ha-1 y-1 (P-treated). The authors estimated a range for the atmospheric Cd input from the average and maximum net annual increase of Cd in 4 different untreated plots of the Rothamsted long-term trials (Jones et al., 1987). Obviously, even the maximum net Cd accumulation in these plots (i.e. 5.4 g ha-1 y-1) is likely lower than the atmospheric Cd input because of Cd losses from these plots. Therefore, the highest estimated Cd leaching from the park grass plots (i.e. 3.1-4.9 g ha-1 y-1) may still be conservative values. Using our model, we calculated the average annual Cd losses from the P treated plots from the soil properties (soil pH values as given in Nicholson et al., 1994), 0.2 m annual water flux out of the topsoil and the KD estimated with the model of Römkens and Salomons, 1998. Our model predicted 7.1 g ha-1 y-1 for the P treated plots, i.e. not too much higher than the 4.9 g ha-1 y-1 estimated by Nicholson et al., 1996.

Table 3.1.181: the annual Cd leaching from the plough layer (L, in g ha-1y-1). The Cd leaching is calculated for a soil with 0.3 mg kg-1 total Cd (background concentration) and an annual net water flux out of the plough layer of 0.2 m. The different models used for estimating the KD of Cd in soil are referred to in the Table 3.1.88.

| soil pH | %OM | KD model | L g ha-1 y-1 |
| --- | --- | --- | --- |
| 6.5 6.5 5.5 | 2 4 2 | Christensen, 1989 | 2.0 1.4 6.6 |
| 6.5 6.5 5.5 | 2 4 2 | Lee et al. 1996 | 1.6 0.8 5.3 |
| 6.5 6.5 5.5 | 2 4 2 | Gerritse and Van Driel, 1984 | 2.8 1.4 10.8 |
| 6.5 6.5 5.5 | 2 4 2 | Römkens and Salomons, 1998 | 2.0 2.0 7.2 |
| 6.5 6.5 5.5 | 2 4 2 | McBride et al., 1997 | 0.4 0.3 1.2 |
| 6.5 6.5 5.5 | 2 4 2 | Smolders et al. (in situ data, unpublished) | 0.9 0.9 4.0 |
| 6.5 6.5 5.5 | 2 4 2 | Smolders et al. (adsorption data, unpublished) | 6.6 3.4 26 |

Crop offtake

Crop offtake of Cd is the amount of Cd that is removed from the soil with the harvested part of the plant. The crop offtake of Cd is generally small in agricultural conditions and does not largely influence the soil Cd balance. The crop offtake in three different crop rotation systems in agricultural districts of Sweden varied from 0.17 to 0.62 g Cd ha-1 y-1 (averages for each rotation, Eriksson et al., 1996).  The crops included in the rotations were carrots, potatoes, barley, oil seed, oat and winter wheat.  Detailed farm-gate and field-scale Cd balances were calculated for arable, dairy and mixed farming systems at two locations in The Netherlands (Moolenaar and Lexmond, 1998).  On the arable farm, crop offtake varied from 0.6-0.9 g Cd ha-1 y-1 (averages for a rotation including potato, sugar beets, chicory and onion, winter wheat and spring barley). Crop offtake in grassland was 1.4 g Cd ha-1 y-1 but most of this returns to the soil as manure. The farm-gate balance of the mixed-farming system showed that the net Cd loss with milk and meat/animal was less than 0.01 g Cd ha-1 y-1. The crop offtake can also be calculated from typical yields and crop Cd concentrations. Table 3.1.182 shows such estimates for wheat grain and potatoes in several European countries. It can be deducted from the table that harvesting wheat grain removes, on average, 0.4 g ha-1.  A potato yield removes around 1.2 g Cd ha-1

Table 3.1.182: the Cd content in selected agricultural crops and the estimated annual crop offtake

| crop | crop Cd† (g kg-1 | comment | typical yield (tons) | crop offtake g ha-1 |
| --- | --- | --- | --- | --- |
| wheat grain | 38 (M) 58 (M) 70 (M) 40-69 (M) 56 (M) | UK2, n=393 France3, n=16 The Netherlands4, n=84 Sweden1, n=354, averages of three data sets Germany5, n=886 | 7.7 6.5 8.8 6.0 6.9 | 0.29 0.38 0.62 0.24-.0.41 0.39 |
| potato tuber | 51 (M) 30 (M) | Sweden1, n=69 The Netherlands4, n=94 | 30 35 | 1.53 1.05 |

† M = mean, m = median.  Source 1Eriksson et a l., 1996;2Chaudri et  al., 1995;3Mench et a l., 1997;4Wiersma et al., 1986;5Weigert et al., 1984

For modelling purposes, crop offtake is assumed proportional to soil Cd and, hence, future crop offtake values are changed proportionally to the change in soil Cd. No changes in crop offtake are assumed with long-term changes in soil properties (e.g. soil pH).

Future trends in soil Cd: the regional PECsoil  in 8 different  scenarios

The Cd mass balance in the plough layer will be calcu’ated for a number of scenario's representative of European agriculture. These scenarios are indicative for average conditions.

Three different input scenarios are combined with a low or high output scenario each. The difference in output scenario is mainly based on a different soil pH, either pH 6.8 (low output) or pH 5.8 (high output). Leaching losses are calculated with the KD model of Römkens and Salomons (1998) and assuming 0.2 m annual water flux out of the plough layer and 2% organic matter.  The soil Cd concentration at t=0 is derived from measured Cd concentrations in areas well away from point sources (Table 3.1.190).  The Cd content in soil at t=0 refers to natural Cd (from geological origin) and some Cd that was added in the past (fertiliser Cd and Cd from atmospheric deposition).

The low input scenario's 1&2 represent agricultural conditions of northern Europe (Sweden, Finland and Denmark) and Cd input/offtake and soil Cd data were selected to correspond with preceding tables. Scenario 3 and 4 represent central European agricultural conditions (e.g. UK, France, The Netherlands, Germany) using average Cd fluxes from P fertilisers and atmospheric deposition in these countries. The offtake values were selected from Moolenaar and Lexmond, 1998 (either mixed farming or arable farming) and a typical soil Cd concentration was selected for these countries. Scenario 5 and 6 represents high input farming systems, which may be found in e.g. wheat/corn rotations. Applications of P in these systems are typically 30 kg P ha-1 (i.e. data of France, Italy and Germany, Harris, 1998) and it is assumed that the P fertiliser contains 150 mg Cd kg-1 P.  The atmospheric deposition (3 g Cd ha-1 y-1) represents a high value for European rural areas (see above). The offtake is low and represents farming systems with high Cd recycling (i.e. corn used for roughage). A worst case scenario 7 is included: this scenario may represent land use in some mediteranean agricultural areas where very low output prevails. The Mediterranean biogeographical region comprises up to 9% of the Pan- European area (Roekaerts, 2002). This region can be charachterized by a limited excess drainage (0.05m/year rather than 0.2 m/year; note default value of TGD is 0.175 m/year) and a large Kd value (calcareous soils which prevail in Mediterranean areas, pH 7.5). The scenario is considered as worst case because the very low output is coupled with high input as described above. High input of fertiliser is unusual for these areas because of lower crop yields (unless combined with irrigation, for which the low excess drainage may not be realistic). Data of Cd deposition in these areas are not available, and a realistic worst case assumption of 3 g/ha/year was made.   The scenario 8 is an attempt to represent an average for the whole of Europe. Average Cd inputs are derived from the tables given above and the EU-16 average Cd deposition is based on the net immision at the regional scale (see Table 3.1.180). The average Cd input from fertiliser may be based on the 1990 data and, as discussed above, this value may overestimate current input of Cd from fertilisers.  The average Cd output is difficult to estimate. The leaching losses are based on a soil pH of 6.5 and the crop offtake is an average for scenario's 1-6.

The soil Cd is predicted to increase in 6 scenarios (between 2.8 and 46 %) and decrease in two scenarios (11 and 19 %) after 60 years of exposure to current inputs. At the EU scale (average), soil Cd is predicted to increase by 6 % after 60 years. This increase is lower than the historical increasing trends in soil Cd in Europe (see Table 4.1.3.3, in RAR human part, see separate document). The (realistic) worst case of scenario (5) predicts soil Cd concentration = 0.411 mg Cd kg-1dw. This is equivalent to 0.363 mg Cd kg-1ww (standard environment characteristics, TGD) and is used as the PECregionalsoil.

The soil Cd concentration at t=0 has a major impact on the PECsoil. This is obviously related to the fact that the amount of background Cd in soil is several fold higher than the annual Cd addition. For example, the 90th percentile of the Cd concentrations in cultivated soils in France is 0.8 mg kg-1 (Baize, 1999; see Table 3.1.190). This concentration would increase to 0.875 mg Cd kg-1dw after 60 years, assuming a high input/low output scenario as in scenario 5. However, we do not prefer to use upper percentiles (=local situation) as a realistic worst case for PECregional since the risk scenarios in soil (section 3.3) are mainly important for human foodchain contamination (regional/continental) and food items are not grown in one location in this scenario (4.1.1.4.8, in RAR human part, see separate document). The upper percentiles of background Cd in soil are certainly more relevant for local exposure to Cd but the PEClocalsoil should then be contrasted to PNEC values derived for these scenario’s (e.g. human diets dominated by home-grown food, section 4.1.1.4.8, in RAR human part, see separate document). The PEClocalsoil values obviously span a wider range than the PECregionalsoil values in Table 3.1.183. It can be shown that the risk characterisation of diffuse Cd emissions in agricultural scenario’s (fertiliser Cd, atmospheric deposition) is controlled by the regional and continental assessment and not by local risk assessment, even if the local Cd background is 3-4 fold larger than assumed in Table 3.1.183.  Moreover, soils with high natural background Cd are usually soils that have large clay content and have a high pH, both factors known to reduce risk of Cd for foodchain contamination (4.1.1.4.8, in RAR human part, see separate document) or secondary poisoning (3.2.6.4.2) and which are the critical pathways of Cd in soil.

In the context of the continued review, under the Fertilisers Directive (76/116/EEC), of risks posed to human health and the environment by cadmium in fertilisers, Member States were encouraged to perform national risk assessments during summer/autumn 2000. To ensure conformity, a suggested template of procedures had been established. Eight Member states (Austria, Belgium, Denmark, Finland, Greece, Ireland, Sweden and the United Kingdom) and Norway submitted risk assessments. These were analysed and summarised in a consultants report to the Commission (Hutton et al) in January 2001.

Compared to the accumulation calculations performed within this report, a longer time horizon, 100 years, was chosen by most Member States. The time period (60 or 100 years) only weakly affects the PECsoil.  As an example, the EU average PECsoil (60 years) = 0.318 mg Cd/kg dw whereas the PECsoi (100 years) = 0.329 mg  Cd/kg d.w. Different algorithms for KD were chosen based on national soil properties. Also, a majority of the MS modelled scenarios with different cadmium concentration in fertilisers, e.g. “low”, national average” and “high/EU average”. Finally, many MS chose to use different input values for cadmium via fertilisers in order to assess the importance of crop rotation or regional agriculture practices.

Predictions of PECsoil after 60 or 100 years, performed by Austria, Belgium, Denmark, Finland, Norway, Sweden and the UK are given as an illustration in Table 3.1.22. Ireland presented a risk assessment using default input parameters, while the input and output values in the Greek risk assessment are difficult to comprehend. Therefore the results of these assessments are not integrated in Table 3.1.183.

Despite the differences in input values, the consultant found the following consistent trends in the various assessments, based on current fertiliser input levels:

- for low fertiliser cadmium concentrations (between 2.5 to 40 mg Cd/kg P), cadmium in soil tends to accumulate relatively slowly, or decreases after 100 years of application due to net removal rates (leaching, crop uptake) exceeding inputs

- for fertilisers with Cd concentrations of 60 mg/kg P and above, accumulation in agricultural soils over 100 years is more pronounced (between 17 and 43 % increase after 100 years).

The future soil Cd content might be slightly overpredicted by some countries because they included animal manure as a net input in soil. Cadmium input from manure is, however, only a net input at the country level if there is a net import of minerals added to animal feed. The Cd input in soil from animal feed is low compared to the input from P-fertilisers (Table 3.1.183). The soil Cd content in some Belgian regions is predicted to increase by more than a factor two over 60 years. These values are based on Cd deposition data near former industrial sites (atmospheric deposition 36 g ha-1 y-1) where resuspension is a possible source of atmospheric Cd.

Low Cd input values through fertiliser addition are currently applied in northern European countries (Sweden, Finland and Denmark). As seen from Table 3.1.177, these countries introduced maximum permissible Cd concentrations in the mid 1990's. The calculations represent the present day situation, where risk reduction measures strongly influence the Cd input by fertilisers, and not a worst case scenario.

Some countries have predicted steady state soil Cd concentrations which are significantly above those calculated by the alternative model for the 6 regions (e.g. Austria: soil Cd at steady state = 1.13 mg Cd/kg dw).  But steady state concentrations are only reached after very long periods (e.g. about 930 years, recalculated for Austrian data) during which soil properties (pH !) land use (crop offtake) may change and that undoubtedly affect the soil Cd balance. In other words, the assumption of constant parameter values in predicting soil Cd concentrations in the very far future is highly questionable.

It is difficult to judge if the Cd balance in European soils is at a steady state or not. Current European Cd inputs in agricultural soil (2-3 g ha-1 y-1) have strongly reduced from historical inputs (e.g. 7-9 g ha-1 y-1 in Denmark between 1923-1980, Tjell and Christensen, 1985; at least 8-10 g ha-1 y-1 in UK, P treated park grass soils 1913-1983, Nicholson et al., 1996). In the low input scenario's, predicted trends are extremely sensitive to changes in soil pH. Lowering the soil pH increases predicted Cd leaching and results in a predicted downward trend of soil Cd. No other soil Cd balance has predicted a reduction in soil Cd.

It can be concluded that the current Cd input in European agricultural soils is reduced from historical input and that the European soil Cd concentration is predicted to change by between a 19% decrease to a 46% increase in 60 years. However, there is always uncertainty in the input-output data and it now appears that estimating Cd leaching losses is critical for drawing firm conclusions. An average steady state obviously does not preclude that a strong increase in soil Cd is found in local areas. The steady state in soil Cd may not be reached in agricultural systems that have characteristics as given in scenario 5, 6 and 7. These systems have a high Cd input from fertilisers, even where fertiliser Cd is below the legal limits of e.g. Germany and Belgium.

Predicting future trends in crop Cd is even more difficult than predicting future trends in soil Cd. It is very likely, for example, that soil acidification may have more effect on crop Cd concentrations than the slow changes in soil Cd. Trends in crop Cd concentrations are not included in this report because annual variations in crop Cd can be higher than changes over long periods of time. Andersson and Bingefors (1985) found an increase of a factor two in grain Cd content (winter wheat) between 1918 and 1980, while the annual variations in the grain Cd content were up to a factor five. Large annual variations in crop Cd are also observed by Kjellstrom et al. (1975) (see also section 4.1.1.4.7, in RAR human part, see separate document). Soil Cd typically explains a minor part of the variance in crop Cd. As an example: Swedish field data show that soil Cd only explains 3-19% of the variability of crop Cd concentrations (Eriksson et al., 1996).

Table 3.1.183: the predicted environmental concentration of Cd in agricultural soil (PECsoil, -plough layer only) after 60 years of exposure to current Cd influx in agricultural soils. Seven scenario's are selected that may be representative for European agriculture. Predictions are made using the Cd mass balance approach described in the text. The full description of the scenarios is given in the text.

| scenario | Cd input (g ha-1 y-1) | Cd output (g ha-1 y-1) at t=0 | net Cd balance | Cd soil at t=0 | PECsoil after 60 years |
| --- | --- | --- | --- | --- | --- |
|  | P fertiliser | atmospheric deposition | animal feed | total | crop offtake | leaching | total | g ha-1y-1 | mg kg-1dw |
| 1. low input-low output | 1.1 | 0.6 | 0.05 | 1.75 | 0.3 | 1.1 | 1.4 | +0.35 | 0.250 | 0.257 |
| 2. low input-high output | 1.1 | 0.6 | 0.05 | 1.75 | 0.5 | 4.1 | 4.6 | -2.85 | 0.250 | 0.203 |
| 3. average input-low output | 2.0 | 2.0 | 0.1 | 4.1 | 0.66 | 1.6 | 2.26 | +1.84 | 0.350 | 0.385 |
| 4. average input-high output | 2.0 | 2.0 | 0.1 | 4.1 | 0.8 | 5.7 | 6.5 | -—4 | 0.350 | 0.310 |
| 5. high input--low output | 4.5 | 3.0 | - | 7.5 | 0.3 | 1.3 | 1.6 | +5.9 | 0.300 | 0.411 |
| 6. high input-high output | 4.5 | 3.0 | - | 7.5 | 0.3 | 4.9 | 5.2 | +2.3 | 0.300 | 0.339 |
| 7. high input-very low output (worst case Mediterranean) | 4.5 | 3.0 | - | 7.5 | 0.3 | 0.1 | 0.4 | +7.4 | 0.300 | 0.439 |
| 8. EU average | 2.5 | 0.4(1) | 0.05 | 2.95 | 0.5 | 2.0 | 2.5 | +0.45 | 0.300 | 0.318 |
| Predicted environmental concentrations in agricultural soils as calculated(3) in the Risk assessments on Cd in fertilisers performed by EU Member States and Norway (Hutton et al., 2001) at current Cd application rates through fertilisers (Table 3.1.177) |
|  | Current Cd concentration in the soil | PECsoil after 60 years (mg kg-1dw) | PECsoil after 100 years (mg kg-1dw) |
| UK | 0.23 | - | 0.27 |
| Austria | 0.242 | - | 0.345 |
| Belgium | 0.22-0.35 | 0.114-0.772(2) | - |
| Denmark | 0.144-0.249 | - | 0.076-0.273 |
| Finland | 0.21 | - | 0.145-0.228 |
| Sweden | 0.23 (wheat + potatoes) 0.33 (carrots) | - | 0.20-0.30 (wheat + potatoes)(4) 0.30-0.35 (carrots) |
| Norway | 0.24 | - | 0.19-0.21 |

(1) 126 ton y-1deposited over 3.56 106 km² = 0.4 g ha-1 y-1; (2)Based on Cd deposition data near former industrial sites (atmospheric deposition 36 g ha-1 y-1) where resuspension is a possible source of atmospheric Cd; (3) Calculations are based on net Cd inputs from different sources (P-fertilisers, atmospheric deposition, manure, sludge application and/or liming). Cadmium output is based on Cd offtake by several crops and leaching estimated by different KD models. (4) Calculations based on the algorithm of McBride et al. (1997).

##### Measured regional data in the environment

# Aquatic systems

Cadmium enters rivers and lakes because of both natural and anthropogenic factors. Weathering and erosion processes may wash Cd from geological sources into rivers. Industrial and municipal effluents are discharged into rivers and lakes. There is direct deposition of atmospheric Cd onto surface waters as well as run-off of Cd-bearing water from the soil and from landfills. Acidification of soil and water may increase the mobilisation of Cd in the environment which would otherwise remain adsorbed to rock and soil particles (Pearse, 1996). Measured Cd concentrations in freshwaters and in suspended matter are presented in Tables 3.1.184, 3.1.185 and 3.1.186. Measured Cd concentrations in freshwater sediments are presented in Tables 3.1.187.

Most of the data presented in these tables originate from national or regional monitoring programs. The following data treatment was applied to derive statistics (e.g. 90th percentiles) from the data in the following consecutive steps:

- Data are sorted per country as a surrogate for region

- When measurements were reported as being smaller than the detection limit (DL), a value of half the DL was assigned to this measurement.

- Outliers: a statistical approach was used for defining outliers in an attempt to exclude the contribution of local emissions from diffuse emissions. The uncertainty related to either including or excluding outliers will be taken forward to the risk characterization where the effect of outlier analysis on the risk factors will be compared. In this section, however, percentiles only refer to the database obtained after outlier exclusion. Outliers are selected based on the TGD (2002) using the equation: log(Xi) > log(P75) + K(log(P75) - log(P25)) where Xi is the concentration above which a measured value may be considered an outlier, Pi is the value of the ith percentile of the statistic and K is a scaling factor. This filtering of data with a scaling factor K = 1.5 is used in most statistical packages, but the factor can be subject dependent. A value of 1.5 was chosen in this report. Outliers are detected by calculating the P75 and P25 statistics on the entire dataset, i.e. not per sampling site. Outlier calculation per sampling site detects measurement errors.

- Derivation of statistics: the revised TGD (2002) recommends to calculate the PECregional as the mean of 90th percentiles within a region. The 90th percentiles refer to observations at one sampling site. Almost all data referred to below do not give data organized per sampling site but rather list data without reference to a site. In order of preference we calculated the statistics as: xth percentile= mean of xth percentiles within the region; if this was not possible, then xth percentile= xth percentile of the data within the dataset. The P90 value is calculated from the rank in the observed frequency distribution and not from the rank in a curve fitted to the frequency distribution. This means that the P90 is not affected by the exact values of data at lower percentiles

- Data are presented as dissolved (D) concentrations. If the original data refer to total concentrations, then dissolved concentrations are estimated (ED) assuming that the dissolved Cd concentration in freshwater is 33% of the total Cd concentration in water (see section 3.1.2.3.1: dissolved fraction = 1/((1+Kp*Csusp*10-6) with Kp = 130 103 L kg-1, Csusp = 15 mg L-1; TGD, 1996). In Swedish oligotrophic lakes, about 60-100% of the Cd is dissolved (<2.4 nm) at pH 4.5-6.0 and about 10-60% at pH 6-7 (Parkman et al., 1998). Fractionation is unknown (U) for the large Scandinavian database of Skjelkvåle et al. (1999). For all these data, the dissolved fraction is set at 100%. As will be shown in the risk characterisation, this conservative assumption does not affect the conclusion for regional risk.

Priority is given to the most recent data for risk characterization. All data below are drawn from the original databases and secondary information about regional averages (or 90P values) are not used if the background information (i.e. detection or reporting limit¶) is missing. The data of surface water are classified in reliability classes (RI1: most reliable, RI4,  least reliable) to aid the risk characterization. The detection limit (DL) is most critical. As the PNECwater is 0.19 µg/L (see 3.2), we propose that a dataset with DL≥0.1 µg L-1 (dissolved) is less reliable within the risk characterisation.

RI 1:	the detection limit is <0.1 µg L-1 (dissolved), the Cd fractionation is known as dissolved or estimated dissolved and water hardness data are known. This allows the risk characterization to be corrected for water hardness.

RI 2:	the detection limit is <0.1 µg L-1 (dissolved), the Cd fractionation is known as dissolved or estimated dissolved; hardness is unknown and no correction for hardness can be made.

RI 3:	the detection limit is <0.1 µg L-1 (dissolved), the Cd fractionation is known as dissolved, estimated dissolved or is assumed as dissolved when no information regarding the Cd fractionation was given.

RI 4:	the detection limit ≥0.1 µg L-1 (dissolved) and data are considered on a case-by-case basis because the detection limit is too large.

In what follows the datasets of various European countries are described and discussed. Several databases contain series with different detection limits and a specific data analysis was performed, discussed below, to allow classification in the above-mentioned reliability classes Data are presented in table 3.1.184-3.1.187 The underlined values are taken forward to the risk characterization and are summarised in Tables 3.1.185 and 3.1.188 in which the average of 90th percentiles are calculated per region. .

- Belgium

Flanders region: Monitoring data of total cadmium were obtained from the Flemish Environment Agency (VMM; http://www.vmm.be).For the purpose of this risk assessment, data for the years 2000-2002 are used. After analysis of the dataset and exclusion of the outliers, the dataset contained 3591 measurements. The DL ranges from 0.1 to 1.2µg/L. Only 6% of the data were above the detection limit. This means that the 90-percentile of that dataset, 0.5µg/L (total) i.e. 0.17 µg/L (estimated dissolved) is unreliable.

Additionally, a qualitative description of the data-set was provided by VMM (pers. com., 2004). The monitoring network in Flanders contains a large number of sampling locations distributed over various types of surface waters in Flanders (834 sampling points in 2002). Total cadmium levels have been analysed and the data show that most higher cadmium levels are concentrated in the Kempen (i.e. the results of Dommel, Molse Neet and the Scheppelijke Neet are conspicuous). In 1997, 24 % of the measurements were above the detection limit (mainly 0,2 and 1 µg/l). In 2002, 13 % of the results were above the detection limit (between 0,1 and 1,2 µg/l). Calculation of the average of 90-percentiles on the datasets of 1997 and 2002 separately and without any data exclusion and by setting data lower than detection limit at half the detection limit, yields a 90-percentile (total cadmium) of 1.0µg/L in 1997 as well as in 2002 (VMM, pers. com., 2005). Given however that these P90’s are within the range of the DL, these cannot be considered as reliable for the risk characterisation.

The monitoring data for the Walloon region were generated and reported by the Scientific Institute for Public Services (ISSeP). The dataset contains 690 values for the dissolved Cd content and 39 for the total Cd content of Walloon surface waters. The DL is reported to range from 0.1 to 0.3 µg/L for the dissolved Cd content and is equal to 1 µg/L for the total Cd concentration. The reporting limit exceeds the critical value of this report, however the P90-value is still useful as it  exceeds the critical reporting limits (notice that all values below the reporting limit have been set to half the reporting limit). After excluding the outliers following the procedure mentioned above a dataset of 659 values remained ranging from 0.05 to 1.53 µg/L. Statistics were calculated once for the entire dataset.

Recently more (detailed) data for the Walloon region (years 2000, 2002 and 2004) were submitted via Industry’s commentary file (ICdA, 2005) but could not be taken into account in this assessment

- Denmark

For Denmark, data concerning Cd concentrations in surface waters were found in a survey of the national lakes for the Nordic Council of Ministers by Skjelkvåle et al. (1999). Measurements were performed in the year 1995 with the ICP-MS method. 0.03 µg/L was reported as the DL. The method was subjected to quality control. The statistics of the report for Denmark are based on 19 not-statistically selected lakes, and are therefore only indicative of the general levels of Cd in Danish lakes. For this reason, Skjelkvåle et al. (1999) only reported the 50th percentile. The maximum measured concentration is 0.266 µg/L, the lowest reported value is below the DL.

- Finland

A first dataset was found in the survey of the national lakes for the Nordic Council of Ministers by Skjelkvåle et al. (1999). Measurements were performed in the year 1995 with the ICP-MS method. 0.03 µg/L was reported as the DL. The method was subjected to quality control. 464 lakes were selected at random keeping in mind basic requirements concerning size and location. The data can be considered to represent the entire country.

A second dataset was obtained from the cooperation project “Ecogeochemical mapping of Eastern Barents region 1999-2000” (Salminen et al., 2004). The dataset reports the dissolved cadmium content of 339 measurements. The lowest reported value is 0.005 µg/L, the highest 0.48 µg/L. No DL is indicated.

- France

A number of monitoring data (52 in total), representative for the Rhône-mediterranean basin, were gathered from the “Réseau des Données sur l’eau du Bassin Rhône-Méditerranée-Corse”(RNB-eauRMC). This dataset for the region of the Rhône-Méditerranée for the year 2001 contains no actual measured data for Cadmium. All data are reported as smaller than the DL of 0.5 µg/L.

Data for the Seine were gathered from the Réseau National de Donnéés sur l’Eau (RNDE) and can be consulted on the web at http://www.rnde.tm.fr/ . The dataset contains 9 values for the years 1998 to 2000. No DL is indicated and values range from 0.025 to 0.073 µg/L.

Data for the Rhine-Meuse basin are reported by the Office International de l’Eau (1999) for the years 1995 to 1999. Data were obtained from 104 measurements. No information regarding the method of detection or DL is reported.

The datasets for France were designated RI 4. The reporting limits are unknown or exceed 0.1 µg L-1 or the dataset is not considered representative for a region.

- Germany

The dataset from the Elbe for the year 2000 originates from the Wassergütestelle Elbe (Hamburg). It reports the total Cd concentrations and consists of 114 measurements. The DL is reported as 0.05 µg/L and values range from 0.05 to 0.7 µg/L for total Cd concentrations. 111 values are reported as higher than the DL. Statistics were calculated once for the entire dataset.

A large dataset was obtained from the “Hessisches Landesamt für Umwelt und Geologie”(HLUG), containing recent information (2001) on cadmium concentrations in a large number of rivers in Germany (26 in total).  The data can be presumed to represent the entire country. The dataset consists of 531 measurements. The fractionation of the measured cadmium is not indicated. The lowest reported values range from 0.1 to 0.5 µg/L, the highest is 64.2 µg/L. One measuring site was excluded, however, according to the aforementioned selection procedure. This resulted in a dataset of 520 values with a range of 0.1 – 0.98 µg/L. No DL is reported. Statistics were calculated by averaging over the different measuring sites, following the TGD, revised 2002 procedure.The reliability of the database is, overall, low because the fractionation is unknown, the detection limit is unknown and the majority of the data within a site are reported as a constant value (e.g. 0.5 µg/L), suggesting that this is the reporting limit. Because of lack of information on DL’s, it was considered unreliable to divide the lowest values by 2. This database will not be taken forward to the Risk Characterisation because of all these uncertainties.

A third dataset for the year 1998 was obtained from the “Joint Water Commission of the Federal Länder (LAWA), Federal institute of Hydrology, Berlin. This dataset contains 2614 measurements of 89 rivers. Data for different measurement points are available for some of these rivers. The 90th percentiles for some of the major rivers are given here. If 90th percentiles of different measuring points for a river are available, only the average of these 90th percentiles is indicated. Cadmium concentrations are reported for the total cadmium concentration and the DL ranges from 0.05 to 0.5 µg/L.

In addition, data concerning the Cd content of German surface waters were extracted from the COMMPS database (Combined Monitoring-based and Modelling-based Priority Setting scheme) of the European Commission (European Commission, 1999). This smaller dataset contains 33 values for the year 1996. Measurements were performed for the dissolved cadmium content and range from 0.02 to 0.21 µg/L. No DL is reported. Statistics were calculated once for the entire dataset.

- Greece

Data concerning the Cd content of Greek surface waters were extracted from the COMMPS database (Combined Monitoring-based and Modeling-based Priority Setting scheme) of the European Commission (European Commission, 1999). This dataset contains 39 values for the year 1998. Data refer to total concentrations (Dr. Lekkas, personal communication) and no DL is given. The reported values range from 0.06 to 1.89 µg/L. Statistics were calculated once for the entire dataset.For reference: Estrela et al. (2000) report an average value for the Axios river of 0.25 µg/L. No information regarding the original dataset, method of detection or DL is given.

- Italy

Data concerning the Cd content of Italian surface waters were extracted from the COMMPS database (Combined Monitoring-based and Modelling-based Priority Setting scheme) of the European Commission (European Commission, 1999). This dataset contains 6 values for the year 1996. The fractionation of the measured Cd content is not indicated and no DL is given. The reported values range from 0.5 to 2 µg/L. No information is available about the location of sampling. Statistics were calculated once for the entire dataset.

Because of the small amount of data for the year 1996, data for the year 1995 from the same database are also given. Notice the large difference in measured values between the 2 years. Questions can be raised regarding the representative ness of this dataset for the entire country. Statistics were calculated once for the entire dataset.

For reference: Breder (1988) reported dissolved Cd concentrations in Italian rivers to range from 0.004 to 0.113 µg/L in the years 1980 – 1982.  Furthermore, Breder (1988) reports values in the Po river to range from 0.028 to 0.19 µg/L in the year 1983 with an average of 0.065 µg/L and the Cd content of Italian lakes to range from 0.004 to 0.013 µg/L. Jensen and Bro-Rasmussen (1992) report the average Cd content in the Tiber as 0.015 µg/L and in the Arno 0.1 µg/L.Because of the large difference between the dataset and the literature date, the dataset should not be taken forward to the risk analysis (RI 4).

- The Netherlands

Monitoring data for the Netherlands were gathered by the Rijkswaterstaat (RWS; executive organization of the Dutch Ministry of Transport, Public Works and Water Management). The dataset presented here contains 333 values for the measured total Cd content of Dutch surface waters for the year 2002. Data are obtained from the “Waterstat” database on the internet to be found on http://www.actuelewaterdata.nl/.  The data can be presumed to represent the entire country (data from 27 sampling sites). The DL is reported as 0.05 µg/L. Statistics were calculated by averaging the 90th percentiles of measurements at each sampling point, following the TGD, revised 2002 procedure.

A second dataset for regional waters was obtained, containing 1692 data from 242 sampling points. Total Cd concentrations are reported. The reporting limit varies from 0.01 to 0.3 µg/L total Cd depending on the regional water management authority. Data were screened according to the aforementioned selection procedures (i.e. excluding data from regional water management authorities with RI 4 and excluding outlier data). This resulted in a dataset of 1492 values from 228 sampling points, with total Cd concentrations ranging from 0.005 to 0.56 µg/L (RL 0.01-0.24 µg/L). Including outlier data, total Cd concentrations range from 0.005 to 21 µg/L. Statistics were calculated by averaging the 90th percentiles of measurements at each sampling point, following the TGD, revised 2002 procedure. The analysis by the responsible Dutch Water Authorities for these waters yielded a P90 of 0.73 µg/L (total) or 0.24 µg/L (estimated dissolved) which is about 3-fold above the P90 value calculated here and which was mainly related to the either or not including data with large detection limits. The MSR has returned this data analysis to the responsible Dutch Water Authorities but no further comments were received.

An additional dataset on total Cd content of Dutch surface waters for the year 1997 can be extracted from the COMMPS database (Combined Monitoring-based and Modeling-based Priority Setting scheme) of the European Commission (European Commission, 1999). However, in the presence of more recent datasets, NL proposed to base the risk characterization on the latter and preferred not to use the older COMMPS dataset to this aim (COM302+303_env_NL4, 19.11.04).

For reference:

Crommentuijn et al. (1997a) report a background concentration for the 90th percentile of dissolved Cd in the Netherlands of 0.08 µg/L.

Ros and Slooff (1990) report values for the dissolved Cd concentration of 0.18 - 0.026 and 0.34 - 0.059 µg/L for the Rhine (near Lobith) respectively the Meuse (near Eysden) in the years 1983 to 1986.

The “Coordinatie-Commissie voor de metingen van Radioactiviteit en Xenobiotische stoffen” (CCRX, 1994) reports the following 90th percentiles for the Cd content in the year 1992: 0.1, 0.8, 0.38, 0.2, 0.15, 0.09 and 0.2 µg/L for the Rhine (near Lobith), the Meuse (near Eysden), the Westerscheldt Schaar van Ouden Doel, the Nieuwe Waterweg Maassluis, the Nieuwe Waterweg Haringvlietsluizen, the Netherlands IJ23 and the Netherlands NZK KM2 respectively. The fractionation of the measured Cd is not given.

Pearse (1996) reports the following 90th percentiles for the Cd content of the year 1993: 0.1 and 0.6 µg/L for the Rhine (near Lobith) and the Meuse (near Eysden) respectively. The fractionation of the measured Cd is not reported.

- Norway

A first dataset was found in the survey of the national lakes for the Nordic Council of Ministers by Skjelkvåle et al. (1999). Measurements were performed in the year 1995 with the ICP-MS method. 0.02 µg/L was reported as the DL. The method was subjected to quality control. 985 lakes were selected at random keeping in mind basic requirements concerning size and location. The data can be considered to represent the entire country.

- Portugal

Data for Portugal were found in the Portuguese Database for Water (the National Information System for Water, to be found on the web at http://snirh.inag.pt). Values are presented here for the total Cd content of Portuguese surface waters in the year 2002. Detection limits vary per region from 0.1 to 5 µg/L total Cd or from 0.03 to 1.7 µg/L estimated dissolved Cd. In the whole dataset, 84% of the measurements are smaller than the DL, but for some of the surface waters more than 90% of the data are below the DL. As such, the DL strongly determines the statistics derived from this dataset. The dataset for Portugal, although very extensive, will not be fully included in the risk characterization, because the detection limits exceed 0.1 µg/L. Statistics were calculated by averaging over the different regions, following the TGD, revised 2002 procedure.

- Spain

A dataset was found for one region of Spain: Andalusia. Data originate from the “Consejeria de medio ambiente en Andalusia” and were reported on the web by the Spanish Ministry of Environment. (http://www.mma.es). The database consists of 330 measurements of the cadmium concentrations of Spanish surface waters for the year 1994. The fractionation of the measured Cd is not indicated. The DL was 0.3 µg/L. Reported concentrations range from <0.3 to 68 µg/L with 39% of the dataset being smaller than the DL. High values are encountered because of a historical contamination of the Guadalquivir. The results can, therefore, not be considered to represent ambient Cd concentrations of Spanish waters. Statistics were calculated once for the entire dataset but the data are not taken forward to the risk characterisation in this report because of the influnce of data with historical contamination.

Recent data for Spain were submitted (Ministerio de medio ambiente, 2005) but could not be taken into account in this assessment.

Additional data were extracted from the COMMPS database (Combined Monitoring-based and Modeling-based Priority Setting scheme) of the European Commission (European Commission, 1999). This dataset contains 11 values for the year 1996. The fractionation of the measured Cd content is not indicated and no DL is given, but the reporting limit, as well all the values in the dataset, equal 0.1 µg L-1. Therefore, the COMMPS dataset for Spain will not be included in the risk characterisation (RI 4). Statistics were calculated once for the entire dataset.

Notice the large difference between the 2 datasets. Keeping in mind the overall measured concentrations in Europe, one is inclined to rely stronger on the dataset from the COMMPS database.

For reference: Jensen and Bro-Rasmussen (1992) report the Cd concentrations of the Ebro as  0.12 µg/L. No additional information is provided.

- Sweden

Data were gathered by the Swedish University of Agricultural Sciences and can be consulted on the web at http://info1.ma.slu.se/. Data are presented for the year 2000 for lakes and for the years 1995 – 2001 for rivers. DLs vary but all cover the very low range of encountered values. Reported values range from 0.002 to 2.03 µg/L for rivers and from 0.001 to 4.46 µg/L for lakes. Statistics were calculated for the 2 datasets separately by averaging over the different regions, following the TGD, revised 2002 procedure.

A second dataset was found in the survey of the national lakes for the Nordic Council of Ministers by Skjelkvåle et al. (1999). Measurements were performed in the year 1995 with the ICP-MS method. 0.003 µg/L was reported as the DL. The method was subjected to quality control. 820 lakes were selected at random keeping in mind basic requirements concerning size and location.

- The United Kingdom

Data for the Cd content of British surface waters were gathered by the U.K Environmental Change Network (ECN) and can be found on the web at http://www.ecn.ac.uk/index.html  Data are presented for the year 1995 and consist of 10 measurements. The fractionation of the measured Cd is not indicated. The DL is reported as 0.02 µg/L. Reported values range from <0.02 to 0.46 µg/L with 30% of the values reported as smaller than the DL. Statistics were calculated once for the entire dataset.

Data were also extracted from the COMMPS database (Combined Monitoring-based and Modeling-based Priority Setting scheme) of the European Commission (European Commission, 1999). This dataset contains 1363 values for the year 1996. Measurements were performed on the dissolved Cd content and the lowest reported values range from 0.02 to 0.2 µg/L. No DL was indicated. Measured concentrations range from 0.02 µg/L to 346 µg/L. After excluding the outliers a dataset was obtained with 1244 values ranging from 0.02 to 1.38 µg/L. Statistics were calculated once for the entire dataset.

A 3rd database (WIMS) was received from the Environment Agency and contains 7108 Cd measurements in freshwater for the year 2003. Measurements were performed on the dissolved Cd content. The detection limit varies from 0.01 to 1 µg/L. Sampling points with DL > 0.1 µg/L and sampling points with only one measurement were rejected. This resulted in a dataset of 6905 values from 728 sampling points, with dissolved Cd concentrations ranging from 0.005 to 158 µg/L. Of these values, 5388 are reported as ‘<0.1 µg/L’. Because of the high number of measurements found under the DL, an outlier analysis on the full dataset was not useful because it resulted in a limit value at the DL.  Therefore, it is proposed here to make an outlier analysis on the sub-dataset of measurements found above the DL.  It should be noted that this results in a very conservative outlier analysis and only 20 P90 values of the 729 were rejected.  Statistics were calculated by averaging the 90th percentiles of measurements at each sampling point, following the TGD, revised 2002 procedure.

Table 3.1.184: measured or estimated dissolved Cd concentrations in surface water. Underlined data are used for risk characterization.

| Location (source/database) | Cd fractionation1 | Sampling period | n | Reporting limits [µg L-1] | 90th percentile [µg L-1] | 50th percentile [µg L-1] | 10th percentile [µg L-1] | Statistics2 | RI |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Belgium |
| Flanders (VMM) | ED | 2000-2002 | 3591 | 0.03 - 0.4 | (0.17: unreliable, only 6% of data>DL) | - | - | * | 4 |
| Walloon (ISSeP) | D | 1999-2000 | 681 | 0.1 – 0.3 | 0.66 | 0.10 | 0.05 | ** | 4 |
| Denmark |
| Denmark (Skjelkvåle et al., 1999) | U | 1995 | 19 | 0.03 | - | 0.05 | - | *** | - |
| Finland |
| Finland (Skjelkvåle et al.,1999) | U | 1995 | 464 | 0.030 | 0.03 | <0.03 | <0.03 | *** | 2 |
| Eastern Barents Region (Salminen et al., 2004) | D | 1999-2000 | 339 | 0.005 | 0.085 | 0.020 | 0.005 | ** | 2 |
| France |
| Rhône-Méditerranée (RNB-eauRMC) | U | 2001 | 52 | 0.5 | 0.25 | 0.25 | 0.25 | ** | 4 |
| Seine (RNDE) | D | 1998 -2000 | 9 | 0.025 | 0.06 | 0.03 | 0.03 | ** | 4 |
| Rhine-Meuse (Office International de l’eau) | U | 1995-1999 | 104 | - | 0.85 | - | 0.05 | *** | 4 |
| Germany |
| Elbe (Wassergütestelle Elbe) | ED | 2000 | 114 | 0.02 | 0.12 | 0.07 | 0.07 | ** | 2 |
| Germany (HLUG) | U | 2001 | 520 | 0.1 - 0.5 | 0.46 | 0.45 | 0.44 | * | 4 |
| Danube (LAWA) | ED | 1998 | 52 | 0.03 - 0.07 | 0.03 | - | - | * | 2 |

–

| –Main (LAWA) | ED | 1998 | 100 | 0.03 - 0.1 | 0.04 | - | - | * | 4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Mosel (LAWA) | ED | 1998 | 26 | 0.02 - 0.03 | 0.03 | - | - | * | 2 |
| Oder (LAWA) | ED | 1998 | 52 | 0.07 | 0.10 | - | - | * | 2 |
| R–hein (LAWA) | ED | 1998 | 194 | 0.02 - 0.07 | 0.03 | - | - | * | 2 |
| Ruhr (LAWA) | ED | 1998 | 22 | 0.07 | 0.11 | - | - | * | 2 |
| Saar (LAWA) | ED | 1998 | 76 | 0.03 | 0.03 | - | - | * | 2 |
| Weser (LAWA) | ED | 1998 | 67 | 0.02 - 0.13 | 0.09 | - | - | * | 4 |
| Germany (COMMPS) | D | 1996 | 33 | 0.02 | 0.11 | 0.05 | 0.02 | ** | 2 |
| Greece |
| Greece (COMMPS) | ED | 1998 | 39 | 0.02 | 0.18 | 0.08 | 0.03 | ** | 3 |
| Italy |
| Italy (COMMPS) | U | 1996 | 6 | 0.5 | 1.74 | 0.75 | 0.52 | ** | 4 |
| Italy (COMMPS) | U | 1995 | 7 | 0.5 | 11.42 | 2.86 | 0.56 | ** | 4 |
| The Netherlands |
| The Netherlands (RWS) | ED | 2002 | 333 (27 sampling sites) | 0.02 | 0.07 | 0.03 | - | * | 2 |
| The Netherlands (regionale wateren) | ED | 2002 | 1492 (228 sampling sites) | 0.003-0.08 | 0.06 | - | - | * | 2 |
| Norway |
| Norway (Skjelkvåle et al., 1999) | U | 1995 | 985 | 0.02 | 0.055 | <0.02 | <0.02 | *** | 2 |
| Portugal |
| Arade (SNIRH) | ED | 2002 | 6 | 0.33 | - | 0.17 | - | ** | 4 |
| Ave/ Leca (SNIRH) | ED | 2002 | 22 | 0.33 | 0.17 | 0.17 | 0.17 | ** | 4 |
| Cavado/rib Costeiras (SNIRH) | ED | 2002 | 39 | 0.33 | 0.17 | 0.17 | 0.17 | ** | 4 |
| Douro (SNIRH) | ED | 2002 | 219 | 0.17 - 0.33 | 0.17 | 0.17 | 0.08 | ** | 4 |
| Guadiana (SNIRH) | ED | 2002 | 35 | 1.7 | 0.83 | 0.83 | 0.83 | ** | 4 |
| Lima/ Neiva (SNIRH) | ED | 2002 | 24 | 0.33 | 0.17 | 0.17 | 0.17 | ** | 4 |
| Lis/rib. Costa (SNIRH) | ED | 2002 | 92 | 0.17 | 0.43 | 0.08 | 0.08 | ** | 4 |
| Minho/ Ancora (SNIRH) | ED | 2002 | 41 | 0.33 | 0.17 | 0.17 | 0.17 | ** | 4 |
| Mira (SNIRH) | ED | 2002 | 4 | 1.7 | - | 0.83 | - | ** | 4 |
| Mondego (SNIRH) | ED | 2002 | 193 | 0.17 | 0.21 | 0.08 | 0.08 | ** | 4 |
| Rib. Algarve (SNIRH) | ED | 2002 | 8 | 0.33 | 0.17 | 0.17 | 0.17 | ** | 4 |
| rib. Oeste (SNIRH) | ED | 2002 | 57 | 0.03 | 0.02 | 0.02 | 0.02 | ** | 3 |
| Sado (SNIRH) | ED | 2002 | 27 | 1.7 | 0.83 | 0.83 | 0.83 | ** | 4 |
| Tejo (SNIRH) | ED | 2002 | 280 | 0.03 -1.7 | 0.83 | 0.83 | 0.02 | ** | 4 |
| Vouga/ rib. Costeiras (SNIRH) | ED | 2002 | 127 | 0.17 | 0.28 | 0.08 | 0.08 | ** | 4 |
| Spain |
| Andalusia (MMA) | U | 1994 | 330 | 0.3 | 7 | 1 | 0.1 | ** | 4 |
| Spain (COMMPS) | U | 1997 | 11 | 0.1 | 0.1 | 0.1 | 0.1 | ** | 4 |
| Sweden |
| Sweden - rivers (SLU) | U | 1995-2001 | 6975 | 0.002 | 0.052 | 0.023 | 0.007 | * | 1 |
| Sweden - lakes (SLU) | U | 2000 | 1204 | 0.001 | 0.027 | 0.011 | 0.006 | * | 1 |
| Sweden (Skjelkvåle et al., 1999) | ED | 1995 | 820 | 0.003 | 0.052 | 0.01 | 0.003 | *** | 2 |
| The United Kingdom |
| The UK (ECN) | U | 1995 | 10 | 0.02 | 0.31 | 0.10 | 0.01 | ** | 3 |
| The UK (COMMPS) | D | 1996 | 1244 | 0.02 – 0.2 | 0.43 | 0.17 | 0.10 | ** | 4 |
| The UK (WIMS) | D | 2003 | 6905 (728 sampling sites) | 0.01-0.1 | 0.15 | 0.10 | 0.08 | * | 2 |

1Cd fractionation: 	D: dissolved Cd; ED: estimated dissolved Cd. If total concentrations are measured, dissolved concentrations are estimated to be 33% of the total Cd concentration (see 3.1.3.1.1); U: unknown Cd (presumed as 100% dissolved).

2Statistics:	*: the statistics (=percentiles) are averages of corresponding values of the different sampling sites per region (TGD, revised 2002);**: the statistics are the percentiles of the entire dataset due to a lack of geographically-referenced data;	***: statistics are reported by the author of the respective dataset.

Reported average Cd concentrations in European surface waters range from 0.03 µg/L (Sweden) to 0.14 µg/l (U.K; Table 3.1.185). Notice that reported Cd concentrations increase.as the uncertainty (RI) increases.  We propose to use the data of RI 3 as a trade off between data richness and quality. Countries from northern, western and southern Europe are included and as such a general view of the ambient Cd concentration in European surface waters is obtained. The dataset for the Seine (France; n=9, P90= 0.06 µg/L) is not included as it comprises a very limited area and, as such, does not represent the entire region. If included, the effect on the resulting statistics would be minimal.

The average of the average 90th percentiles per region is 0.12 µg/L and is a first approximation of a PECregional. This value is slightly above the 90th percentile obtained in the EU-wide systematic survey of FOREGS study (0.10 µg/L, see below). The statistics of the datasets with RI 4 are not summarized as the uncertainty regarding these data is too large.

It is most likely that all surface waters contain some Cd that is emitted by man.  Natural background Cd in surface water can therefore only be estimated indirectly.  Scandinavian rivers and lakes probably contain minor quantities of Cd added by man since atmospheric Cd deposition data are lowest in the Scandinavian countries (Table 3.1.180).  The median Cd concentration in Scandinavian lakes is 0.01 µg Cd L-1 (Skjellkvåle et al., 1999).  This value may not be representative for natural Cd in other regions since weathering of natural Cd from minerals may certainly vary between regions.  Surface sediments in EU lakes contain 3.6-30-fold higher Cd concentrations than deeper sediments (see below: sediment data).  These enrichment factors could be combined with actual Cd concentrations in the lakes to calculate pre-industrial Cd concentrations. An overall view of Cd concentrations in European aquatic systems is provided by the FOREGS Geochemical Baseline Program (FGBP). This program has been initiated to provide high quality environmental geochemical baseline data for Europe. The data presented here are based on samples of stream water collected throughout Europe. High quality and consistency of the obtained data are ensured by using standardized sampling methods and by treating and analyzing all samples in the same laboratories. The FGBP is authorized by the directors of the Geological Surveys within FOREGS (Forum of European Geological Surveys) and can be found on the web at http://www.eurogeosurveys.org/foregs/ .The cadmium concentration was measured using the ICP-MS method with a DL of 0.002 µg/L. 807 samples were taken randomly throughout Europe to obtain an overall view of the Cd concentration. The survey yielded a median concentration of 0.01 µg/L and a 90th percentile of 0.10 µg/L.

We propose a (high) estimate of 0.05 (g L-1 as a general natural background Cd in freshwater (dissolved fraction).  This value is used as the natural background concentration in the calculation of PECcontinentalwater. A high estimate of the natural background can be considered as a conservative choice because it is added to the calculated concentrations. The choice of this background is, however, not very relevant for local risk characterisation since the PNEC is about 4-fold higher than the natural background.  The risk characterisation at regional scale is performed with measured data.

Table 3.1.185: measured Cd concentrations in surface water classified per reliability index (RI)  taken forward to the risk characterization . The statistics (90th percentile and average) are the averages of corresponding values of the regional data from Table 3.1.184 which meet the crtiteria of reliability*. Datasets with RI=4 were discussed on a case-by-case basis above. Datasets with RI>1 include also data of classes with lower RI index (i.e. cumulative number of data).

|  | RI* | Region | n | 90th percentile [µg L-1] | Average [µg L-1] |
| --- | --- | --- | --- | --- | --- |
|  | 1 | Sweden | 8179 | 0.0395 | 0.03 |
|  | 2 | Finland | 803 | 0.057 | - |
|  |  | Germany | 608 | 0.07 | - |
|  |  | Norway | 985 | 0.055 | - |
|  |  | Sweden | 8999 | 0.044 | 0.03 |
|  |  | The Netherlands | 1825 | 0.07 | 0.04 |
|  |  | Greece | 39 | 0.18 | 0.12 |
|  | 3 | Finland | 803 | 0.06 | - |
|  |  | Germany | 608 | 0.07 | - |
|  |  | Greece | 39 | 0.18 | 0.12 |
|  |  | The Netherlands | 1825 | 0.07 | 0.04 |
|  |  | Norway | 985 | 0.06 | - |
|  |  | Sweden | 8999 | 0.04 | 0.03 |
|  |  | UK (ECN) | 10 | 0.31 | 0.14 |
|  |  | U.K. (WIMS) | 6905 | 0.15 |  |
|  | 4 | Belgium | 4272 | - | - |
|  |  | Finland | 803 | - | - |
|  |  | France | 165 | - | - |
|  |  | Germany | 1295 | - | - |
|  |  | Italy | 13 | - | - |
|  |  | The Netherlands | 405 | - | - |
|  |  | Norway | 985 | - | - |
|  |  | Portugal | 1174 | - | - |
|  |  | Spain | 11 | - | - |
|  |  | Sweden | 3353 | - | - |
|  |  | UK(COMMPS) | 1244 | - | - |

*RI 1: DL<0.1 µg/L, Cd fractionation: D or ED (D: dissolved Cd; ED: estimated dissolved Cd ) and water hardness known;RI 2: DL<0.1  µg/L, Cd fractionation: D or ED; RI 3: DL<0.1  µg/L, Cd fractionation: D, ED or U (Unknown=assumed dissolved); RI 4: all data.

n: number of values in the dataset.

An important fraction of total Cd in freshwater is adsorbed on suspended matter. The Cd concentrations in suspended matter typically range between 1 and 10 mg kg-1dw (Table 3.1.186). Higher values are typically recorded in the river Maas that carries Zn ore particles. The dissolved fraction Cd ranges 10-40% in the rivers Rhine, Meuse and Schelde (Ros and Slooff, 1990), about 50% in the rivers Rhine and Arno (Breder, 1988) and 30-40 % in Tiber and Elbe (Breder 1988). In lake Constance and Zurich, the percentage dissolved Cd is 80 and 84% respectively. High dissolved fractions are found in acid waters, in which total concentrations are also elevated.

The Cd concentrations in EU freshwater generally decrease since the end of the 1970s. Breder (1988) noticed the largest drop in dissolved Cd concentration in the lower course of the Rhine between 1977 and 1984.  Ros and Slooff (1990) demonstrated that Cd concentrations in great Dutch rivers (total and dissolved and on suspended matter) decreased 4-fold from 1983 to 1986. Since 1990, the decrease in Cd is generally less pronounced (Milieucompendium, 2001; see also Annex 3.1.2). The total Cd concentration in the Schelde at the border Belgium-Netherlands decreased from 3.5 (g L-1 in 1975 to about 0.4 (g L-1 in 1988 (no further trend).

Seasonal changes in Cd concentrations occur in lakes. Borg (1987) investigated 59 forest lakes in northern Sweden. The Cd concentrations are 2.4 fold higher in winter than in than in summer. During summer, there is higher production of phytoplankton and the higher input of particulate matter from the watershed. Therefore, more metal becomes particle bound and settles to the lake sediment.

A negative correlation between Cd concentrations and pH is observed in Swedish rivers and in lakes. Cadmium concentrations in Swedish surface waters increase from north to south along with acidification and air-born Cd.  Different fractions of Cd in five soft water forest lakes with differing pH (average 4.85-6.61) in southern Sweden were measured. Most of the Cd in water was in dialysable form, especially in the more acidic lakes. This Cd form increases with decreasing pH, resulting in increased total Cd levels (Parkman et al., 1998).

Table 3.1.186: measured cadmium concentrations in suspended matter

| location | concentration (mg kg-1dw) | moment | year | Source |
| --- | --- | --- | --- | --- |
| Germany Danube, Jochenstein | 0.41 0.32-0.50 | average (n=2) min-max | 1998 | LAWA database1 |
| Germany Danube | 0.82 | average of 90 percentiles | 1998 | LAWA database1, 2 |
| Germany Elbe, Grauerort | 1.81 0.73-5.10 | average (n=12) min-max | 1998 | LAWA database1 |
| Germany Elbe | 7.11 | average of 90 percentiles | 1998 | LAWA database1, 2 |
| Germany Mosel, Koblenz | 0.94 0.43-1.34 | average (n=13) min-max | 1998 | LAWA database1 |
| Germany Mosel | 1.09 | average of 90 percentiles | 1998 | LAWA database1, 2 |
| Germany Rhine, Koblenz | 0.76 0.39-1.18 | average (n=26) min-max | 1998 | LAWA database1 |
| Germany Rhine | 0.94 | average of 90 percentiles | 1998 | LAWA database1, 2 |
| Germany Weser, Bremen | 3.60 1.60-5.00 | average (n=14) min-max | 1998 | LAWA database1 |
| Germany Weser | 3.65 | average of 90 percentiles | 1998 | LAWA database1, 2 |
| France: basin Artoie, Picardie | 11.83 | average (n=10) | 1995-1999 | Office International de l’Eau, 1999 |
| France: basin Rhin-Meuse | 1.33 | average (n=10) | 1995-1999 | Office International de l’Eau, 1999 |
| France: basin Seine, Normandie | 2.56 | average (n=10) | 1995-1999 | Office International de l’Eau, 1999 |
| France: basin Loire, Bretagne | 3.73 | average (n=10) | 1995-1999 | Office International de l’Eau, 1999 |
| France: basin Rhône-Méditeranée-Corse | 1.09 | average (n=10) | 1995-1999 | Office International de l’Eau, 1999 |
| Netherlands: Rhine Lobith | 6.3 2.3 | n.a. | 1983 1986 | Ros and Slooff, 1990 |
| Netherlands: Rhine Lobith | 3.0 3.5 3.0 | n.a. | 1988 1989 1990 | CCRX, 1991 |
| Netherlands Rhine Lobith Netherlands Maas Eysden Netherlands Westerschelde Schaar van Ouden Doel Netherlands Nieuwe Waterweg Maassluis Netherlands Nieuwe Waterweg Haringvlietsluizen Netherlands IJ 23 Netherlands NZK KM2 | 4 34 1 7.5 6.5 2 2.2 | 90 percentile | 1992 | CCRX, 1994 |
| Netherlands: Rhine | 7.5 | 90 percentile | 2000 | Milieucompendium, 2001 |
| Netherlands: Maas | 19.1 | 90 percentile | 2000 | Milieucompendium, 2001 |
| Netherlands: Schelde | 8.1 | 90 percentile | 2000 | Milieucompendium, 2001 |
| Netherlands: Rijkswateren | 8.5 | 90 percentile | 2000 | Milieucompendium, 2001 |
| Netherlands: IJsselmeer | 1.9 | 90 percentile | 2000 | Milieucompendium, 2001 |
| Netherlands: Maas Eysden | 29 11 | n.a. | 1983 1986 | Ros and Slooff, 1990 |
| Netherlands: Maas Eysden | 133 19 32 | n.a. | 1988 1989 1990 | CCRX, 1991 |
| Netherlands: Schelde Schaar van Ouden Doel | 17 9 | n.a. | 1983 1986 | Ros and Slooff, 1990 |

n.a.= information not available; 1Source: Joint Water Commission of the Federal Länder (LAWA), Federal Institute of Hydrology, Berlin; 2The LAWA database contains 2614 measurements of 89 rivers. Data for different measurement points are available for some of these rivers. The 90th percentiles for some of the major rivers are indicated as an example in this table. If 90th percentiles of different measurement points for a river are available, only the average of these 90th percentiles is indicated.

# Sediment

The datasets of various European countries are described and discussed below. Data are presented in table 3.1.187. Older (literature) data are summarised in Table 3.1.25bis. The averages of percentiles per region are summarised in Table 3.1.25tris. It should be noted that these measured data in the sediment refer to total cadmium concentrations and are thus not corrected for bioavailability.

A statistical approach was used for defining outliers in an attempt to exclude the contribution of local emission sources from diffuse emission sources. The uncertainty related to either including or excluding outliers will be taken forward to the risk characterization where the effect of outlier analysis on the risk factors will be compared. In this section, however, percentiles only refer to the database obtained after outlier exclusion. Outliers are selected based on the TGD (2002) using the equation: log(Xi) > log(P75) + K(log(P75) - log(P25)) where Xi is the concentration above which a measured value may be considered an outlier, Pi is the value of the ith percentile of the statistic and K is a scaling factor. This filtering of data with a scaling factor K = 1.5 is used in most statistical packages, but the factor can be subject dependent. A value of 1.5 was chosen in this report. Outliers are detected by calculating the P75 and P25 statistics on the entire dataset, i.e. not per sampling site. Outlier calculation per sampling site detects measurement errors.

- Belgium

Monitoring data of cadmium concentrations in Flemish sediments (Belgium) were obtained from the Flemish Environment Agency (VMM). Data can also be consulted at the website (http://www.vmm.be). After exclusion of the outliers (8), the dataset contained 512 values of the year 2001. Data range from 0.02 to 7.4 mg/kgdw. Data were aggregated to obtain the statistics presented below as not enough data were available to calculate site-specific statistics.

Additional data were extracted from the COMMPS database. 20 values for the year 1995 yield the statistics presented below. The values range from 1.48 to 31.33 mg/kgdw. Samples were taken in rivers burdened by a high historical pollution load, however, and the data are therefore not taken forward in this report.

For reference: Plasman and Verreet (1992) report Cd concentrations in the sediment of the Dijle river to range from 0.1 to 3 mg/kgdw.

- France

Data were obtained of the Cd concentration of the sediment for the year 2001 from the Réseau National de Donnéés sur l’Eau (RNDE) and can be consulted on the web at http://www.rnde.tm.fr/ . Data were selected for 2 regions: Artois-Picardie (n = 126) and Rhône-Méditerranée (n = 66). For Artois-Picardie it was possible to calculate river-specific statistics. For the Rhône-Méditerranée only the main rivers and tributaries were included in the database. For the latter region, all individual data were used to calculate region-specific statistics.

Additional data were found in the COMMPS database and consist of 123 values for the year 1996 (after excluding the outliers). The measured Cd concentration ranges from 1 to 20 mg/kgdw.

For reference, averaged data per basin reported by the Office International de l’Eau are included in the table. In addition Breder (1988) reports values of 2 mountain lakes of Dauphiné to range from 0.15 to 2.5 mg/kgdw, which are not incorporated in the risk assessment, however.

- The Netherlands

Monitoring data for the Netherlands were gathered by the Rijkswaterstaat (RWS; executive organisation of the Dutch Ministry of Transport, Public Works and Water Management). The dataset presented here contains 12 values of 12 different points for the measured Cd concentration of sediments for the year 2000. Data are obtained from the “Waterstat” database to be found on http://www.actuelewaterdata.nl/. The reported values range from 0.05 to 4.89 mg/kgdw.

Data for the year 1997 were found in the COMMPS database. It contains 6 values with a range of 0.63 to 4.68 mg/kgdw (after excluding one outlier).

For reference: Breder (1988) reports a Cd concentration in the sediment of the Ijsselmeer of 3 mg/kgdw and in the Ketelmeer of 34 mg/kgdw. Crommentuijn et al. (1997a) report a background Cd concentration of Dutch sediments of 0.8 mg/kgdw. Pearse (1996) reports Cd concentrations in Maas sediments to range from <0.6 to 15 mg/kgdw for the year 1994.

- Spain

One dataset of 9 values was found for Spain in the COMMPS database. Values represent Cd concentration in the sediment for the year 1997 and range from 0.1 to 17.2 mg/kgdw. The highest measurement was rejected however, considered as being an outlier, resulting in a dataset of 8 values with a range of 0.1 – 0.52 mg/kgdw.

- Sweden

Data for the Cd concentration of Swedish sediments was gathered by the Swedish University of Agricultural Sciences (SLU) and can be consulted on the web at http://info1.ma.slu.se/. Data for the years 1998 – 2000 are presented here. The dataset consists of a total of 297 values measured in 99 distinct locations. As such, it can be considered to represent the entire country. Values range from 0.12 to 7.64 mg/kgdw.

For reference: Pearse (1996) reports Cd concentrations in pre-industrial sediments of lake bed deposits to range from 0.3 to 0.6 mg/kgdw. Jensen and Bro-Rasmussen (1992) report for northern Sweden background Cd concentrations in lake sediments of 0.1 to 0.4 mg/kgdw and Cd concentrations in the upper cm of the lake sediments to range from 0.1 to 2 mg/kgdw. Parkman et al. (1998) reports Cd concentrations in the surface sediment of forest lakes in south-west Sweden to range from 1 to 6 mg/kgdw in the year 1977 and in central and northern Sweden to range from 0.4 to 2.4 mg/kgdw in the year 1979.

Table 3.1.187: measured Cd concentrations in sediments. Underlined data are used for risk characterization. All values are expressed as total Cd concentrations and thus not corrected for bioavailability.

| Location (source) | Sampling period | n | Range [mg kg-1dw] | 90th percentile [mg kg-1dw] | 50th percentile [mg kg-1dw] | 10th percentile [mg kg-1dw] | Average [mg kg-1dw] | Statistics1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Belgium |
| Flanders (VMM) | 2001 | 512 | 0.02 – 7.4 | 1.59 | 0.27 | 0.03 | 0.68 | ** |
| Belgium (COMMPS) | 1995 | 20 | 1.48 – 31.33 | 14.83 | 7.89 | 2.88 | 8.58 | ** |
| France |
| AA-delta (Artois-Picardie) (RNDE) | 2001 | 13 | 0.1 - 6.1 | 4.66 | 1 | 0.54 | 1.78 | ** |
| Boulonnais (Artois-Picardie) (RNDE) | 2001 | 4 | 0.2 - 0.4 | 0.34 | 0.2 | 0.2 | 0.25 | ** |
| Bresle (Artois-Picardie) (RNDE) | 2001 | 2 | 0.2 – 0.5 | 0.47 | 0.35 | 0.23 | 0.35 | ** |
| Canche (Artois-Picardie) (RNDE) | 2001 | 7 | 0.1 – 1.1 | 0.68 | 0.2 | 0.1 | 0.34 | ** |
| Deule (Artois-Picardie) (RNDE) | 2001 | 14 | 0.8 – 7.8 | 7.74 | 2.9 | 0.86 | 3.91 | ** |
| Lys (Artois-Picardie) (RNDE) | 2001 | 13 | 0.2 – 0.9 | 0.9 | 0.5 | 0.2 | 0.55 | ** |
| Samber (Artois-Picardie) (RNDE) | 2001 | 13 | 0.3 – 1.2 | 0.8 | 0.4 | 0.3 | 0.53 | ** |
| Scarpe (Artois-Picardie) (RNDE) | 2001 | 15 | 0.4 – 9.7 | 3.84 | 1.8 | 0.42 | 2.4 | ** |
| Scheldt (Artois-Picardie) (RNDE) | 2001 | 20 | 0.2 – 12 | 1.41 | 0.35 | 0.29 | 1.15 | ** |
| Somme (Artois-Picardie) (RNDE) | 2001 | 23 | 0.2 – 4.3 | 1.32 | 0.4 | 0.2 | 0.71 | ** |
| Yser (Artois-Picardie) (RNDE) | 2001 | 2 | 0.3 – 0.4 | 0.39 | 0.35 | 0.31 | 0.35 | ** |
| Artois-Picardie (RNDE) | 2001 | 126 | 0.1 - 12 | 2.05 | 0.77 | 0.35 | 1.12 | ** |
| Rhône-Méditerranée (RNDE) | 2001 | 66 | 0.01 – 4.2 | 0.93 | 0.12 | 0.01 | 0.37 | ** |
| France (COMMPS) | 1996 | 123 | 1 - 20 | 5.6 | 2 | 1 | 2.91 | ** |
| Rhine-Meuse (Office International de l’eau) | 1995-1999 | 135 | - | - | - | - | 1.23 | ** |
| Seine, Normandie (Office International de l’eau) | 1995-1996 | 260 | - | - | - | - | 2.16 | ** |
| Loire, Bretagne (Office International de l’eau) | 1995-1996 | 97 | - | - | - | - | 8.32 | ** |
| Adour, Garonne (Office International de l’eau) | 1995-1996 | 365 | - | - | - | - | 2.38 | ** |
| Rhone-Méditerrannée-Corse (Office International de l’eau) | 1995-1996 | 431 | - | - | - | - | 1.55 | ** |
| The Netherlands |
| The Netherlands (RWS) | 2000 | 12 | 0.05 – 4.89 | 3.75 | 1.49 | 0.08 | 1.92 | ** |
| The Netherlands (COMMPS) | 1997 | 6 | 0.63 – 4.68 | 3.63 | 1.74 | 0.83 | 2.07 | ** |
| Spain |
| Spain (COMMPS) | 1997 | 8 | 0.1 – 6.13 | 2.20 | 0.34 | 0.18 | 1.05 | ** |
| Sweden |
| Sweden (SLU) | 1998-2000 | 297 | 0.12 –7.64 | 2.97 | 1.07 | 0.3848 | 1.4168956 | ** |

1Statistics:		**: the statistics are the Xth percentile of the entire dataset.

Table 3.1.188: literature data on the Cd concentrations in European sediments. All values are expressed as total Cd concentrations and thus not corrected for bioavailability.

| Location | Concentration [mg kg-1dw] | Moment | Year | Source |
| --- | --- | --- | --- | --- |
| Germany: 12 lakes in southern Bavaria | 0.4-5.9 | max |  | Breder, 1988 |
| Germany: 12 lakes in southern Bavaria | 0.1-0.95 | min |  | Breder, 1988 |
| Lower+middle Rhine(*) | 12.8, 16.1, 5.1 |  | 1972, 1979, 1985 | Jensen and Bro-Rasmussen, 1992 |
| European rivers: the lower Rhine | 11.8 | max |  | KEMI, 1997 |
| Upper Rhine(*) | 5.3, 3.1, 2.1 |  | 1972, 1979, 1985 | Jensen and Bro-Rasmussen, 1992 |
| Elbe(*) | 17, 11.8 |  | 1972, 1985 | Jensen and Bro-Rasmussen, 1992 |
| Danube(*) | 19.8, 2.1 |  | 1972, 1985 | Jensen and Bro-Rasmussen, 1992 |
| Weser(*) | 13.6, 2.6 |  | 1972, 1985 | Jensen and Bro-Rasmussen, 1992 |
| Ems(*) | 10.4, 1.7 |  | 1972, 1985 | Jensen and Bro-Rasmussen, 1992 |
| Main(*) | 12, 3.9 |  | 1972, 1985 | Jensen and Bro-Rasmussen, 1992 |
| Neckar(*) | 37.3, 11.9, 2.4 |  | 1972, 1979, 1985 | Jensen and Bro-Rasmussen, 1992 |
| N-Italy: lake Como | 1.1 |  |  | Breder, 1998 |
| N-Italy: lake Maggiore | 0.25-2.5 |  |  | Breder, 1998 |
| Italy: rivers, natural background | 0.2-0.3 |  |  | Breder, 1998 |
| Italy: rivers, surface sediment | 0.6-1.8 |  |  | Breder, 1998 |
| Lake Zürich, background | 0.2 |  |  | Breder, 1988 |
| Lake Zürich, surface | 6 |  |  | Breder, 1988 |

The ambient Cd concentration in surface sediments away from point sources ranges between 0.1-34 mg Cd kg-1dw with most values in the 1-10 mg Cd kg-1dw range (0.38-3.8 mg Cd kg-1ww). All data from Table 3.1.187 are taken forward to the risk characterization and are summarised in table 3.1.189. Countries from northern, western and southern Europe are included and as such a general view of the ambient Cd concentration in European sediments is obtained. The total average Cd concentration of European sediments is 1.32 mg Cd kg-1dw. 10% of the sediments contains Cd concentrations exceeding 2.66 mg kg-1dw.

Table 3.1.189: measured Cd concentrations in sediments taken foward to the risk characterization. The statistics (90th percentile and average) are the averages of corresponding values of the regional data from table 3.1.187. All values are expressed as total Cd concentrations and thus not corrected for bioavailability.

| PEC regional | n | 90th percentile [mg kg-1dw] | Average [mg kg-1dw] |
| --- | --- | --- | --- |
| Flanders | 512 | 1.59 | 0.68 |
| France | 315 | 2.86 | 1.47 |
| The Netherlands | 18 | 3.69 | 2.00 |
| Spain | 8 | 2.20 | 1.05 |
| Sweden | 297 | 2.97 | 1.42 |

The average of 90th percentiles of measured Cd concentrations in various countries is 2.66 mg kg-1dw.  This value represents a realistic worst case for the EU ambient Cd concentrations in sediment (natural Cd + historical Cd) and is used as the PECregional  in the risk characterization. The modelled PEC values for sediment are calculated from regional emission to sediments and a background concentration that is typical for EU (i.e. no realistic worst case). That typical ambient background concentration away from point sources is derived here as the median of the averages reported in table 3.1.189 and 3.1.188 to encompass more countries. The resultant typical ambient background sediment Cd concentration is 2 mg Cd kg-1dw (=0.77 mg Cd kg-1ww).  This value is used in Table 3.1.157 to calculate modelled PEC values.

The Cd concentrations in the deeper layers of sediments in lakes range between 0.1 - 0.8 mg kg-1dw (0.04-0.3 mg Cd kg-1ww). These concentrations may be representative for natural background.  In lakes in SW Sweden concentrations in pre-industrial sediment layers, below 20 cm depth, are 0.3 - 0.6 mg kg-1dw and 0.1 - 0.4 in middle and N-Sweden (Johansson, 1989 cited in KEMI, 1997). A generalised background concentration of 0.4 mg kg-1dw was therefore proposed for Swedish lake sediments (Pearse, 1996). Surface sediments (0 - 20 cm) are enriched with Cd compared to deeper layers. Results from Swedish lakes show a gradient significantly decreasing from south to north and an enrichment factor of about 7, referring to the background in southern areas of Sweden. The enrichment factor in Lake Zurich is 30 (Breder, 1988). Concentrations in river sediments show a 3-6 fold enrichment compared with background concentrations in Italian rivers (Breder, 1988).  However, in many non-polluted lakes of northern Europe a decrease in Cd concentration of surface sediments is found compared to concentrations in deeper sediment layers deposited during less acidic conditions. Borg et al (1989) found Cd in the sediment to decrease at pH below 5. Decreasing pH values in the sediment pore water may also cause leakage of Cd from the sediments to the water phase. In acid forest lakes, Johansson (1980) found lower Cd concentrations in surface sediments (0-1cm) compared to in subsurface layers (1-3cm). Furthermore he found that the fixation of Cd to sediment decreased at pH<5, increasing the residence time for Cd in the water phase.

In general, Cd concentrations of surface sediments show downward trends. Breder (1988) demonstrated for the river Rhine a decrease from 1977 to 1983 from 38.6 mg kg-1dw to 21.9 mg kg-1dw at the most contaminated site. At other locations of the river Rhine, a 2- to 5-fold decrease was recorded.

Terrestrial compartment

Measured Cd concentrations in soil are presented in Table 3.1.190. Little data were found for southern European countries. The soil Cd concentrations in areas away from point sources range between 0.05 and 14 mg kg-1dw and most concentrations are found in the 0.1-1.8         mg kg-1dw range. Figure 3.1.4 illustrates the concentration ranges that are listed in the table 3.1.190.

Figure 3.1.13: Measured concentrations of Cd in soils in Europe. Points are averages, medians or geometric means (of min-max) or 90th percentiles of all European surveys listed in Table 3.1.190. Full points are the means of corresponding ranges. Observations near point sources and industrial activities are excluded and only the most recent data are included when data were reported for various periods.

The data from Table 3.1.190 can be subdivided in different regions as a tool for the risk characterisation. Regional ambient Cd concentrations can be derived for the different countries/regions according to two different methodologies:

- method 1: ambient Cd concentration = 90th percentile of all data from a single country/region (TGD, 1996);

- method 2: ambient Cd concentration = average of the 90th percentiles that have been derived for the different sites within the region of interest   (TGD, revised 2002)

However, it is difficult to combine the data of all soils within a country because of the large differences between soils (e.g. sandy versus clay soils). Ideally, averages of 90th percentiles should be calculated per soil type within a country or region.

An attempt was made to average the 90th percentiles of German sand, löss and clay soils. The data were identified (wherever possible), selected and compiled from the data set “Hintergrundwerte für anorganische und organische Stoffe in Böden” (LABO, 1998). In this selection only the data related to the for this risk assessment most relevant ‘soil-use’ and ‘soil-exposure’ categories i.e. the data of the so-called ‘Typ 0’ (“ohne Gebietsdifferenzierung”) and ‘Type II’ (“verdichtete Raume”) are included:

- average P90 for sandy soils: 0.56 mg kg-1dw

- average P90 for löss (loamy) soils: 0.67 mg kg-1dw

- average P90 for clay soils: 0.89 mg kg-1dw

All data from Table 3.1.191 are taken forward To the risk characterization. as is presented in Table 3.3.7. Reported P90 values are averaged per country as a surrogate for region. No attempt was made to differ between soil classes. 10% of the soils contain Cd concentrations exceeding 0.86  mg kg-1. Recent data for Spain are reported (Ministerio de medio ambiente, 2005) but could not be taken into account in this assessment.

A typical average Cd concentration (ambient Cd concentration) in soils located away from point sources is 0.30 mg kg-1dw (0.26 mg kg-1ww).  This concentration is close to the average soil Cd concentrations of the different surveys.  This concentrations is used as the ambient background concentration that is included in the PECsoil. The Cd concentration in the soil depends on the parent material of the soil, the localisation and the land use. Districts associated with Cambrian bedrock, have enhanced Cd concentrations in the soils. Shales and sandstone are important components of the Cambrian formation and have generally high Cd-concentrations. Marine clays in western Sweden and the coarser textured sediments in the middle of Sweden generally have lower-than-average contents (KEMI, 1998).  Little information is available to estimate the natural background of Cd.  The archived soil collection of Rothamsted shows that soil Cd has increased about 0.1-0.2 mg Cd kg-1 between about 1850 and 1980 (Jones et al., 1987, see Table 3.1.190).  A more detailed analysis of this trend is described in section 4.1.1.4.7 (cfr RAR human part, in separate document).

Influence of atmospheric deposition in areas around industrial point sources is well demonstrated in the Shipman area in the UK. Shipman was the centre of Zn mining from the middle of the 17th until the middle of the 19th century. Very high Cd concentrations have been found in these soils. Atmospheric deposition is the dominant source of cadmium in forest soils (Pearse, 1996). In Sweden, concentrations of Cd in the mor layer (the top layer of podzolic soils, 5-8 cm thick, rich in organic matter) of forest soils increased threefold since the pre-industrial era (Pearse, 1996). The mor layer absorbs heavy metals very effectively, and metal concentrations reflect the historical deposition over many decades (Pearse, 1996). The enrichment factor decreases to the north, but even in the northern-most part of Sweden the soil content is somewhat affected by long-range atmospheric transport and deposition of Cd. The concentrations showed a large-scale pattern with the highest values in the south of Sweden and decreasing concentrations towards the north. Regional average Cd concentrations in the mor layer ranged from 1 mg kg-1dw in the south to 0.4 mg kg-1dw in the north. About 2 mg kg-1 has been measured in surface layers (0-20 cm) of peatlands (Hellstrand and Landner, 1998). Locally enhanced Cd concentrations in forest soils are attributed to larger point sources, such as the Rönnskär smelters. The concentrations in the mor layer are > 5 mg kg-1, within a distance of 15 km from the Rönnskär smelter (Hellstrand and Landner, 1998).  There are indications of enriched concentrations also in the B-horizon of the soils (15-25 cm below surface), in southern Sweden (Hellstrand and Landner, 1998).  Recent data indicate that Cd concentrations in the mor layer of Swedish forest soils are presently decreasing in most areas. In northern Sweden, decreasing concentrations in the mor layer are probably a result of the decreasing atmospheric deposition. In southern Sweden, acidification has caused increased leakage rates of Cd from soil surface layers which, together with decreased deposition, result in net outflow of Cd from the mor layers. This indicates that Cd is leaching from surface soils to deeper soil layers, and finally to the runoff water (Hellstrand and Landner, 1998).

Table 3.1.190: total cadmium concentrations in soils. Values underlined are used for risk characterization.

| location | concentration (mg kg-1dw) | moment | year | Source |
| --- | --- | --- | --- | --- |
| Natural soils |  |  |  |  |
| Sweden: concentration in forest mor layer | 0.35 0.64 1.27 | 5 percentiles 50 percentiles 95 percentiles |  | Pearse, 1996 |
| Netherlands: natural areas | 0.05 - 1.8 |  |  | Ros and Slooff, 1990 |
| Germany: Niedersachsen (country area) sandy soils loamy soils | 0.16 0.24 0.19 0.30 | median (n=3379) 90 percentile median (n=1833) 90 percentile |  | LABO, 1994 |
| Germany: forest soil on sand | <0.3 0.7 | Median (n=164) 90 percentile |  | Hindel et al., 1997; LABO, 1998 |
| Germany: forest soil on sandloam | <0.3 0.4 | Median (n=20) 90 percentile |  | Hindel et al., 1997; LABO, 1998 |
| Agricultural soils |  |  |  |  |
| Sweden: background concentration in agricultural soil | 0.15 |  |  | SEPA, 1987 |
| Swedish agricultural soil | 0.26 0.22 0.11-0.49 | average median 5 -95 percentiles |  | Pearse, 1996 |
| Finland: normal agricultural topsoil | 0.06 | average |  | KEMI, 1997 |
| Finland agricultural soil | 0.2 | average |  | Pearse, 1996 |
| Denmark: arable soil | 0.22 0.25 | median average (n=44) | 1966 | Tjell and Hovmand, 1978 |
| UK: Rothamsted agricultural soils soils under permanent grassland | 0.51-0.77 0.33-0.43 0.27-0.42 0.37-0.47 0.19-0.27 | averages | 1846-1980 1881-1983 1882-1982 1870-1983 1876-1984 | Jones et al., 1987 |
| Netherlands: agricultural soils | < 0.1 - 1.6 |  |  | Pearse, 1996 |
| Netherlands: agricultural soils | 0.30 - 0.87 |  |  | Ros and Slooff, 1990 |
| Netherlands: arable soils | 0.5 0.4 0.04-14 | average (n=708) median min-max |  | Wiersma et al., 1986 |
| Belgium: agricultural soils in Flanders sandy soil sandy loam soil loam soil clay soil | 0.25 0.37 0.3 0.4 0.32 0.46 0.27 0.31 | median (n=222) 90 percentile median (n=270) 90 percentile median (n=120) 90 percentile median (n=19) 90 percentile | 1994-1995 | De Temmerman et al., 2000 |
| France plough layer of agricultural soils | 0.01 0.30 0.39 0.69 | min median average (n=10634) 90 percentile | 1995-1999 | Baize, 1999 |
| France: cultivated soils | 0.02 0.25 0.41 0.80 | min median average (n=1063) 90 percentile | 1995-1999 | Baize, 1999 |
| France: all soils (surface and deep soils, agricultural and forest) | <0.02 0.16 0.46 1.06 | min average (n=768) median 90 percentile | 1995-1999 | Baize, 1999 |
| Germany: agricultural soil on sand | <0.3 0.6 | median 90 percentile |  | Hindel et al., 1997; LABO, 1998 |
| Germany: agricultural soil on loam | <0.3 0.7 | median 90 percentile |  | Hindel et al., 1997; LABO, 1998 |
| Germany: agricultural soil on sandloam | <0.3 0.7 | median 90 percentile |  | Hindel et al., 1997; LABO, 1998 |
| Germany: agricultural soils (Südoldenburg) | 0.31 1.59 | median (n=269) 90 percentile |  | Leinweber, 1996 |
| Soils near point sources |  |  |  |  |
| UK: Shipman (n=329) | 97 2 - 360 | average range |  | Jensen and Bro-Rasmussen, 1992 |
| Germany: Hamburg region | 1.2 <0.1-27.8 | average min-max |  | Lux et al., 1988 |
| Netherlands organic matter layer of forest soils and borders of highway Netherlands subsoil of forest soils and borders of highway | 1.13-4.91 <0.35 |  |  | CCRX, 1994 |
| unknown land use |  |  |  |  |
| Sweden | 0.22 0.03-2.3 | average min-max |  | Jensen and Bro-Rasmussen, 1992 |
| N-Sweden: top soils | 0.17-0.28 | averages |  | KEMI, 1998 |
| S-Sweden: top soils | 0.23-0.31 | averages |  | KEMI, 1998 |
| Middle of-Sweden: top soils | 0.22-0.28 | averages |  | KEMI, 1998 |
| Sweden (north, south and middle), top soils | 0.26 0.40 | average 90 percentile |  | KEMI, 1998 |
| Denmark | 0.17 0.11-0.32 | average min-max |  | Jensen and Bro-Rasmussen, 1992 |
| Netherlands | 0.4 | average |  | Jensen and Bro-Rasmussen, 1992 |
| Netherlands: background concentrations | 0.01 - 0.3 |  |  | Ros and Slooff, 1990 |
| Netherlands: calculated background conc. for a standard soil with 10% OM and 25% clay. | 0.8 |  |  | Crommentuijn et al., 1997a |
| Netherlands: Kempen (0 - 25 cm) | 0.3 - 2.7 |  |  | Ros and Slooff, 1990 |
| Netherlands: Kempen (0 - 2 cm) | 0.2 - 100 |  |  | Ros and Slooff, 1990 |
| Netherlands: clay soils sandy soils | 0.5 0.3 | average (n=248) average (n=63) |  | Van Driel and Smilde (1982) |
| Belgium | 0.28 | average |  | Jensen and Bro-Rasmussen, 1992 |
| Belgium: background concentration in Flanders | 0.5 0.4-1.0 1.0 | average (n=470) 25-75 percentile 90 percentile |  | Cornelis et al., 1993 |
| France | 0.2 | average |  | Jensen and Bro-Rasmussen, 1992 |
| UK | 0.5 | average |  | Jensen and Bro-Rasmussen, 1992 |
| UK (England+Wales) | 0.2, 0.7, 1.4 | 10,50,90 percentiles |  | McGrath and Loveland, 1992. |
| UK | 0.49 0.3 11.2 | mean median max | 2000 | Black et al., 2002 |
| UK | 0.44 0.29 2.39 | mean median max |  | Ross et al. (draft) |
| Germany | 0.3 | average |  | Jensen and Bro-Rasmussen, 1992 |
| Germany | 0.44 | average |  | Crössman and Wüstermann, 1992 |
| Germany: Hessen | 0.12 0.1-2.4 | average min-max |  | Jensen and Bro-Rasmussen, 1992 |
| Sweden, top soil (0-20 cm) | 0.23 0.37 | average (n=3067) 90 percentile |  | Eriksson et al., 1997 |
| Netherlands, top soil, all land uses (n=4094) | 0.3 0.83 | 50 percentile 90 percentile | 1993-1998 | Brus et al., 2002 |

Table 3.1.191: measured Cd concentrations in soils taken foward to the risk characterization. The statistics (90th percentile) are  the averages of corresponding values of the regional data from table 3.1.190.

| Location | 90th percentile [µg kg-1] |
| --- | --- |
| Belgium | 0.51 |
| France | 0.85 |
| Germany | 0.65 |
| Sweden | 0.39 |
| The Netherlands | 0.83 |
| The United Kingdom | 1.40 |

Atmospheric compartment

Important sources of Cd in the atmosphere are natural sources, industrial point sources and the combustion of fuel and coal. Atmospheric Cd concentrations measured in various sites in the EU, are shown in Table 3.1.192.

The air Cd concentrations in remote areas are about 0.1 ng m-³. Such values are found in northern Norway in 1978 and in southern Norway in 1985 (Jensen & Bro-Rasmussen, 1992). Recent levels in European rural areas vary from 0.1 to 0.5 ng m-³, averaging 0.5 ng m-³ in Germany and the Netherlands.  The natural background of Cd in air (pre-industrial background) is most likely lower than the ranges now found in rural areas.  The estimated emissions of Cd due to natural processes is 15 ton y-1 (sea spray, mount Etna, forest fires,…ERL, 1990) whereas the current anthropogenic emissions are 126 ton y-1.  Therefore, natural background of Cd in air is probably 10 fold lower than the 0.1-0.5 ng m-³ range of rural areas.  Because air Cd concentrations below 0.1 ng m-³ are hardly detectable and have no meaning in terms of risk, we choose to select a zero Cd concentration as the natural background.

Dutch measurements in 1982/83 demonstrate a decrease in the concentrations from south to north caused by Belgian emissions. A Norwegian study demonstrated, that the long-range Cd transport from Western Europe has decreased from 1978/79 to 1985, whereas transport from eastern Europe has not changed. In Germany, the mean concentration of Cd in the air decreased between 1979 and 1994 from 0.97 ng m-3 to 0.22 ng m-3 (Bieber, 1995) because of a decreasing content of total dust as well as a decreasing Cd content in dust.  In The Netherlands, average concentrations ranged from 0.7 - 2 ng m-³ (Ros and Slooff, 1990). The Cd concentrations decreased from south to north. Since 1990, the average Cd concentration in The Netherlands decreased from 0.5 to 0.2 ng m-3 in 2000 (Milieucompendium, 2001). In general, no large differences are measured between industrial areas and rural area, but higher values are recorded around metal-processing industries. The air Cd in Belgium is generally higher than in other countries. This may reflect resuspension of historic polluted particles although it is possible that the detection limit is higher than 1 ng m-³ (no data were reported below 10 ng m-³). More details on recent time trends in air Cd are given in section 4.1.1.4.7 (cfr RAR on Cd/CdO human part, in separate document).

More recent measured cadmium concentrations in air for the Belgian region, Flanders, can be found in VMM (2004). Air monitoring data of remote/rural areas for EU-countries for more recent years (till 2003) are reported in EMEP (2004).

Table 3.1.192: measured cadmium concentrations in air

| location | Cd concentration (ng m-³) | moment | year | source |
| --- | --- | --- | --- | --- |
| Sweden background concentrations | 0.1 |  |  | SEPA, 1987 |
| N-Norway | 0.1 |  | 1978 | Jensen and Bro-Rasmussen, 1992 |
| S-Norway | 0.3 |  | 1978/1979 | Jensen and Bro-Rasmussen, 1992 |
| S-Norway | 0.1 |  | 1985 | Jensen and Bro-Rasmussen, 1992 |
| Netherlands: Witteveen | 5 |  |  | Hutton, 1982 |
| Netherlands: background concentrations | 3-6 |  |  | Ros and Slooff, 1990 |
| Netherlands: Rekken: background area | 1, 4, 11 | 50,75,98 percentiles |  | Ros and Slooff, 1990 |
| Netherlands: 17 locations | 1 - 11 | average | 1981-1983 | Ros and Slooff, 1990 |
| Netherlands: 17 locations | 1 - 10 | 50 percentile | 1981-1983 | Ros and Slooff, 1990 |

–

| Netherlands: 17 locations | 4 - 21 | 95 percentile | 1981-1983 | Ros and Slooff, 1990 |
| --- | --- | --- | --- | --- |
| Netherlands: 17 locations | 5 - 59 | 98 percentile | 1981-1983 | Ros and Slooff, 1990 |
| Netherlands: 17 locations | 10 - 73 | max | 1981-1983 | Ros and Slooff, 1990 |
| Netherlands: 5 locations | 0.71 - 1.27 | min | 1982-1983 | Ros and Slooff, 1990 |
| Netherlands: 5 locations | 2.9 - 11.6 | max | 1982-1983 | Ros and Slooff, 1990 |
| Netherlands | 0.5 |  | 1982-83 | Jensen and Bro-Rasmussen, 1992 |
| Netherlands: 4 locations | 1.1 0.71 1.3 0.71 1.7 0.53 0.35 | average | 1982-1983 1992 1982-1983 1992 1982-1983 1992 1992 | CCRX, 1994 |
| Belgium:– Botrange | 4 - 6 | average | 1972 - 77 | Hutton, 1982 |
| Belgium, 1984/88 | < 10 |  |  | Jensen and Bro-Rasmussen, 1992 |
| Belgium: rural areas | 10 |  | 1985-1995 | VMM, 1997 |
| Western Germany (5 sampling sites) | 0.97 0.22 |  | 1979 1994 | Bieber, 1995 |
| Germany, Corviglia | 2.1 |  |  | Hutton, 1982 |
| Germany | 1 - 0.4 |  | 1979-1987 | Jensen and Bro-Rasmussen, 1992 |
| The Netherlands | 0.5-0.2 | n.a. | 1990-2000 | Milieucompendium, 2001 |
| UK: 7 rural sites | 1 - 2.7 | average |  | Hutton, 1982 |
| Wales | 0.4 - 0.1 |  | 1984-1987 | Jensen and Bro-Rasmussen, 1992 |
| France, Corsica | 0.66 |  | 1986 | Jensen and Bro-Rasmussen, 1992 |
| Mediterranean Sea | 0.36 |  | 1984 | Jensen and Bro-Rasmussen, 1992 |
| Central Europe: rural areas | 0.1 - 0.8 |  | late 1980s | KEMI, 1997 |
| EU: annual, rural | 0.1-4 |  |  | OECD, 1994 |
| EU: rural annual mean | <1 - 5 |  |  | KEMI, 1997 |
| Near point sources |  |  |  |  |
| Belgium: area around non-ferro plants | 10, 27, 50 |  | 1992-1993 | Ecolas, 1995 |
| Belgium: area around non-ferro plants | 10, 57, 120 |  | 1993-1994 | Ecolas, 1995 |
| Belgium: urban areas | 10-20 |  | 1985-1995 | VMM, 1997 |
| Belgium: non-ferro industrial areas | 10-100 |  | 1985-1995 | VMM, 1997 |
| Belgium: ferro industrial areas | 10-20 |  | 1985-1995 | VMM, 1997 |
| Belgium: other industrial areas | 10-20 |  | 1985-1995 | VMM, 1997 |
| at the edge of a lead smelter in Belgium at the edge of a lead smelter in Germany | 60 29 | max |  | OECD, 1994 |
| EU: annual, urban areas | 2-150 |  |  | OECD, 1994 |
| EU: urban annual mean | 5 - 15 |  |  | KEMI, 1997 |
| EU: industrial annual mean | 15 -50 |  |  | KEMI, 1997 |

##### Comparison of measured and calculated data

Table 3.1.193 summarises the typical regional Cd concentration in surface water, sediments, soils and air and shows regional and continental PEC’s in these various compartments.

Both calculated regional and continental PEC’s of freshwater are found in the typical range of measured Cd concentrations.  The calculated regional PEC is close to the 90th percentile of Cd concentration in the dissolved fraction.

The modelled regional PEC’s of the sediment are about 8 fold higher than the average Cd concentrations although the continental PEC is still in the typical range. Regional and continental PEC’s are calculated for ‘steady state’ conditions with EUSES for the sediment. Steady state conditions in the environment can only be achieved after a very long period, presumably several centuries (see section 3.1.3.4.1). Regional sediment Cd concentrations may exceed actual ambient concentrations because the indirect input via runoff from soil with steady state Cd concentrations is much larger than the actual input via runoff. The regional steady state soil Cd concentrations (EUSES predictions) were 4-5 fold above ambient soil Cd concentrations  (section 3.1.3.4.1).  Regional PEC’s can also be above the typical Cd concentrations because of the assumption that only 1% of the total EU sediment volume collects Cd from 10% of the EU Cd releases into surface water.

The PEC’s of soil, calculated with the alternative model, are close to the measured Cd concentrations.  This correspondence is related to the fact that the model II predicts on average only 14% change in soil Cd in 60 years with current Cd emissions.

Air Cd is remarkably well predicted.  Typical Cd concentrations in air are, however, only valid for rural areas.

Table 3.1.193 Typical measured regional Cd concentrations in the environment (away from point sources and remote areas = ambient Cd concentrations) and the regional and continental predicted environmental concentrations (PEC’s). The measured concentrations and natural background are derived from compilations given in Tables 3.1.184-3.1.192 as discussed in the previous section.  PEC’s are derived from Table 3.1.157.

| compartment | measured Cd | natural background | PECcontinental | PECregional |
| --- | --- | --- | --- | --- |
|  | typical range | average concentration (90th percentile) |  |  |  |
| freshwater µg L-1 (dissolved fraction) | 0.02-0.27 | 0.12$ | <0.05 | 0.06 | 0.11 |
| aq. sediment mg kg-1ww aq. sediment mg kg-1dw | 0.38-3.8 1-10 | 0.51 (1.01) 1.3 (2.6) | 0.04-0.3 0.1-0.8 | 1.25 3.2 | 3.88 10 |
| soil mg kg-1ww soil mg kg-1dw | 0.1-1.6 0.11-1.81 | 0.26 0.29 | unknown | 0.28-0.44 0.32-0.50 | 0.36 0.41 |
| air ng Cd m-3 | 0.1-0.5 | ~0.5 | ~0 | 0.15 | 0.55 |

$ average of regionally averaged P90 values

## Effects Assessment

### Methods and definitions

#### Data quality

A wealth of information is available on the ecotoxicity of Cd.  The data quality of that information varies between source documents.  Not all source documents provide complete background information of the toxicity test.  A Reliability Index (RI, score 1-4) was given to each test result based on a number of quality criteria. These criteria are described in the introduction of the sections on the terrestrial and aquatic compartments. In this way, the risk assessments can be made for various levels of data quality.

Not all data that were incorporated in the tables, have been used in the effect assessment (e.g. derivation of the Predicted No Effect Concentrations –PNEC's-).  A first selection was made based on the RI values of the test results. Secondly, some test results were not taken into account to avoid overrepresentation of similar data. As an example, some tests provide data at different exposure times. In these conditions, only the data at the highest exposure time were selected.  If various endpoints are derived from one test (i.e. reproduction, growth and mortality), only the most sensitive endpoint was included.  Similar toxicity tests are reported in different source documents (i.e. using the same organism, endpoint, soil or water and test conditions). For these cases, the lowest value is selected or a geometric mean value is calculated. All data selected for the effects assessment (PNEC calculation and summarising graphs and tables) are underlined in the tables presenting toxicity data.

#### Definitions of critical concentrations

A number of critical concentrations are derived from the dose response relationship of each test result. Based on guidelines of the TGD (TGD 1996, part II, p. 327), these concentrations are defined as:

No Observed Effect Concentration - NOEC. In order of preference, the NOEC is derived as:

Category 1: the NOEC is the highest tested concentration at which the endpoint is not significantly different from the control treatment at the 5% level of significance, or at which the endpoint shows ( 10% significant adverse effect.

Category 2: if the test shows a significant toxic effect at the lowest concentration tested, the NOEC is defined as LOEC/2 if the inhibition is ( 20 %.

The statistical analysis in the source document is used to identify NOEC's of category 1 and 2.

Category 3: if no statistics are provided in the source document, the NOEC is determined as the highest concentration at which inhibition is ( 10 %.

Category 4: if no statistics are provided in the source document and there is more than 10% inhibition at the lowest tested concentration, the NOEC is determined as half the highest concentration at which the inhibition is ( 10 % but ( 20 %.

There has to be a concentration-effect relationship to derive a NOEC, i.e. no NOEC is defined if the test does not show a toxic effect up to the highest concentration tested. If the % inhibition is ( 20 % at the lowest tested concentration, no NOEC can be derived.

Category 5: the NOEC is defined as the EC10, the concentration at which 10 % inhibition is found, as given in the source document. This value is often found by intra- or extrapolation.

Lowest Observed Effect Concentration (LOEC), the lowest tested concentration at which ( 10 % inhibition is found. The toxic effect must be statistically significant at the 5% level. The statistical analysis in the source document is used to find that concentration. If no statistics are provided in the source document but if there is a dose-effect relationship, the LOEC value is derived as the lowest concentration at which the inhibition is ( 20 % but ( 30 %. In some exceptional cases, an insignificant toxic effect (or, when no statistics are provided,  ( 20 % inhibition) can be found at concentrations higher than the LOEC as defined above. In these cases, LOEC's are re-defined as the lowest concentration at which and above which significant toxicity (or, when no statistics were provided, ( 20 % inhibition) is found.

Along with the LOEC value, the % effect (inhibition) relative to the control is given. If the LOEC is found at the Lowest concentration Tested, this is given in the table (LT). Along the same lines, NOEC values found at the Highest concentration Tested (HT) are indicated. NOEC or LOEC data have not been included if they were found by extrapolation outside the test range, i.e. below the lowest or above the highest Cd application rate.

The ECx(50 (LCx(50) is the concentration at which at least 50 % inhibition (mortality) is found. This value is calculated from the response curve given in the source document or is defined as the concentration at which the toxicity is 50 % or more. The % effect is indicated in the tables.

The definitions of NOEC and LOEC are essential for a consistent approach. Some information is, however, lost using these definitions. Insensitive tests are not included in the effect assessment if the test failed to detect any toxic effect (no NOEC can be defined). Sensitive tests do not affect the derivation of the PNEC if the test showed 20 % or more inhibition at the lowest concentration tested (no NOEC can be derived).

### Aquatic compartment

#### General

##### Data quality: definitions of Reliability Indices (RI’s)

A reliability index (RI) is given for each test based on a number of criteria. These criteria are given below and the IUCLID contains the information which criteria were not met by each test.

RI 1: standard test (OECD approved tests) and performed according to the standard procedures.

RI 2: no standard test but complete background information is given, i.e. the following information is present:

- water hardness (either measured or calculated from Ca and Mg concentrations)

- pH

- the background Cd concentration in the test medium for all data < 1 (g L-1

- measured Cd concentrations or indications that nominal concentrations are close to measured concentrations

- information that actual Cd concentrations were maintained during the test

- statistical analysis of the dose-response relationship

- no varying metal contamination along with increasing Cd application

- the control must be tested along with at least two Cd concentrations above the control

- information about the origin of the test organisms

- information on the test concentration range

RI 3: no standard test and one or more of the following information from the above-mentioned list is missing as background information: b), d), e), f), i), or j). All other information from that list is present.

RI 4: no standard test and one or more of the following information from the above-mentioned list is missing as background information: a), c), g) or h).

The requirement c) is critical since some tests have reported toxic effects below 1 (g L-1 nominal Cd concentrations. Background Cd concentrations in filtered water typically range between 0.05 and 0.2 (g L-1 and the lack of reporting the background concentration may underestimate the Cd concentration at which the first toxic effects are found. Some tests were included that did not show Cd toxicity up to the highest Cd concentration tested. These tests cannot be used for risk assessment (no NOEC can be found) and were considered unreliable (RI4) but were quoted in the tables for illustration.

##### Source of data and its limitations for risk assessment

A wealth of information is available on the toxicity of Cd to aquatic organisms. In this section, a compilation is made of different studies, which provide data of Cd toxicity to different species.  Most of the tests were performed in laboratory conditions where Cd was added to the solution as soluble Cd2+ salts. Four tests on the toxicity of the CdO powder were found. The tests were performed using the filtrate of a dispersion of CdO powder.  These tests are the OECD 203 fish acute toxicity test (Janssen Pharmaceutica, 1993b), the OECD 202 acute immobilisation test with Daphnia sp. (Janssen Pharmaceutica, 1993d) and the OECD 201 algae growth inhibition test (Janssen Pharmaceutica, 1993f, Lisec 1998b).  The test results were reported as measured concentrations in the filtrates. It is most likely that Cd in the soluble fraction of the dispersion has the same speciation as that in a corresponding solution where Cd is added as soluble Cd2+ salts. Therefore, the toxicity tests using the filtrates of the CdO dispersion are treated equally as tests performed using soluble Cd2+ salts.

The CdO powder is only slightly soluble in water. The solubility decreases with increasing solution pH.  Details of the dissolution test are given in 1.4.1.2.

It is assumed that the dissolved fraction of a CdO dispersion represents the toxic Cd compound. The dissolved fraction of CdO has most likely the same speciation as the soluble Cd2+salts dissolved in the same medium. It is therefore assumed that the toxicity of CdO can be assessed based on studies with Cd2+salts, providing that the assessments are based on the dissolved fractions.  Both the effect and exposure assessments of CdO in the aquatic environment are being made based on soluble fraction, as far as possible.

Cadmium toxicity in the aquatic environment can as well be overestimated or underestimated based on the laboratory data for various reasons. The major factors limiting a proper risk assessment are the unknown Cd speciation in environmental samples, the joint toxic actions of different pollutants, the process of long-term acclimation of organisms/populations to Cd and the general lack of information about the most toxic pathways of the higher trophic levels. A short discussion of these factors is given below.

# Speciation

Cadmium can be present in an aquatic environment as inorganic species, including the free metal ion Cd2+, as soluble complexes or sorbed on suspended particles. The free metal ion is considered as the most toxic species. Evidence for this concept was found in studies where metal speciation was altered by varying Cl concentration, affecting the concentration of CdCln2-n species (Sunda et al., 1978) or where synthetic chelates were added to the test solution (Allen et al., 1980). Other evidence on limited Cd toxicity of Cd complexed by dissolved organic matter is illustrated by the data of Giesy et al. (1977) discussed in section 3.2.1.3. The toxicity of cadmium sorbed on suspended particles is far less than that of soluble Cd (see e.g. Van Leeuwen et al. 1985 discussed in 3.2.1.2). Soluble Cd is traditionally distinguished from insoluble forms by membrane (0.45 µm) filtration. Soluble cadmium in freshwater can be lower than 10 % of total cadmium as discussed in the exposure section. Certainly, membrane filtered water samples should be used in risk analysis when concentrations are compared with toxic concentrations given in this compilation.

Data on Cd speciation in the soluble fraction of freshwater samples are limited. Complexation of Cd2+ by inorganic ligands is not pronounced in freshwater systems. Concentrations of inorganic ligands such as Cl-, CO32- and SO42- are generally below 0.001 M in freshwaters (Stumm and Morgan, 1996).  The computed fraction of Cd2+ to the total dissolved inorganic Cd species is about 0.5 (Stumm and Morgan, 1996). In exceptional cases, freshwaters may contain higher concentrations of ligands and lower free metal fractions. An example is the Lake IJssel in The Netherlands that was used for toxicity tests described below (Van Leeuwen et al., 1985). Lake IJssel is an artificial freshwater basin containing salts originating from the sea which was previously at that place. Complexation of Cd by dissolved organic ligands cannot be calculated unequivocally. Complexation is high at high concentrations of dissolved organic carbon and at low water hardness. Solution speciation of Cd undoubtedly affects toxicity but it is striking to note that the free metal ion is very rarely an order of magnitude smaller than the total concentration. Borg et al. (1989) studied Cd speciation in five soft water forest lakes in southern Sweden. Cadmium was predominantly in the soluble form in all of the lakes. In the circumneutral lakes, 35 to 82% of the soluble Cd was present in free ionic form, as inorganic complexes or as low molecular weight organic complexes. In the more acidic lakes, 83 to 100% of the soluble Cd was present in these forms. No data are available at the regional scale to account for Cd speciation in the dissolved fraction for risk assessment.  In view of the much larger uncertainty of a toxic threshold concentration, we conclude that ignoring Cd speciation on the dissolved fraction will not cause large errors in risk assessment of Cd at a regional scale.

# Mixed pollution

In the data compilation given below, only tests with single Cd contamination are included. However, elevated Cd levels in the environment are often associated with elevated Zn levels. The interaction between Zn and Cd can be antagonistic (Zn protecting Cd to become toxic) at moderate Zn levels. At Zn concentrations reaching toxic levels, Cd toxicity is more readily observed. In addition to simultaneous Zn pollution, in many environments other toxic substances exist that may affect Cd toxicity. A widespread approach to account for combined metal toxicity is to use the sum of the toxic unit of each pollutant (the concentration of a pollutant divided by its EC50) as a gross toxicity indicator. In this approach it is assumed that the toxic actions of each contaminant are additive. The validity of such an approach was confirmed in a mesocosm experiment (Jak et al., 1996). The EC50 values of combined toxicity of 7 different heavy metals (including Cd) and arsenic on several plankton species were found between 0.53 and 0.98 ‘sum of toxic units’ (Jak et al., 1996).

# Acclimation

Populations previously exposed to Cd are more tolerant to elevated Cd than previously unexposed populations. An example of this process is found in a laboratory study with algae (Lawrence et al.1989) reported in section 3.2.1.4 and with slugs (Lam, 1996) reported in section 3.2.1.3

# Toxic pathways for higher trophic levels

Most studies report single species tests where Cd was added as Cd2+ salts. Cadmium toxicity in multi-species systems is certainly more complex because of altered food availability in toxic conditions and because of Cd exposure in various ways to higher trophic levels. The first process is illustrated in section 3.2.1.3 by two studies reporting that the toxic action of Cd can decrease some populations and rise other populations in a multi-species system (Lawrence et al., 1989, DeNoyelles et al., 1980, Marshall and Mellinger, 1980). The question whether Cd in the diet or in water is the most toxic source is difficult to answer. Sörensen (1991) reports that in less contaminated environments, water rather than dietary uptake is the major route of Cd uptake. In contrast, as aquatic ecosystems become progressively more contaminated with Cd, the gastrointestinal route of Cd uptake becomes more important than the gill route (Sörensen, 1991). It must be stressed that this conclusion refers to Cd uptake and not to Cd toxicity. The importance of the food route on Cd toxicity can be indirectly found in data on Cd toxicity found in Sweden at very low Cd concentrations. In a field study in the River Emån (Sweden), sublethal toxicity was found in perch (Perca fluviatilis) collected downstream from a source of Cd pollution that ceased its discharge in the river in 1976 (Sjöbeck et al., 1984). The Cd concentrations downstream from the source were 0.1-0.2 µg L-1 while upstream from the source the Cd concentrations were around 0.05 µg L-1 (probably detection limit). The Cd concentrations in the liver of female downstream fish were 6-8 times higher than in those of upstream fish. Based on solution levels, no such large difference in liver Cd should be expected. Before 1976, solution Cd was however higher (about 1 µg L-1) and it is likely that the downstream river sediment and benthic organisms had a high Cd burden at the time of fish and solution sampling (1981). The higher Cd load in the food rather than in solution may be the reason for increased liver Cd and Cd toxicity in the downstream fish compared to the upstream fish. This example indicates that a solution based risk assessment could underestimate exposure on sites with historical pollution.

#### Acute and chronic toxicity to fish/amphibians

Table 3.2.1: selected data with RI 1-3 for acute and chronic Cd toxicity to fish/amphibians. Sixty-three tests were reviewed from 27 source documents and 51 tests were selected.

|  | min | median | max | n |
| --- | --- | --- | --- | --- |
| acute tests |
| E(L)Cx(50 ((g L-1) | 0.9 | 1500 | 40200 | 31 |
| chronic tests |
| NOEC ((g L-1) | 0.47 | 4.2 | 62 | 19 |
| LOEC ((g L-1) | 0.78 | 11 | 132 | 20 |
| E(L)Cx(50 ((g L-1) | 3.4 | 20 | 650 | 7 |

Results of cadmium toxicity studies with fish reveal that toxic concentrations vary from the sub µg L-1 range to over 10 mg L-1 (Table 3.2.1). Larger values are less relevant as many of the organisms in the environment exposed to such cadmium concentrations are already affected (see below 3.2.1.1).  The variability in toxicity among tests can be attributed to varying water quality (e.g. hardness, pH and organic load), life stage investigated, species differences, exposure time and acclimation of the test organisms.

The marked effects of water hardness on cadmium toxicity have been studied extensively. Toxicity test results of Canton and Slooff (1982) demonstrate that cadmium toxicity decreases as water hardness increases. For Oryzias latipes a NOEC value of 30 µg L-1 was recorded after 18 days exposure at a hardness of 200 mg CaCO3/L. This value was fivefold lower in water with hardness of 100 mg CaCO3/L. The effect of hardness became only significant after 4 days. McCarty et al. (1978) compared Cd toxicity to Carassius auratus in water with hardness 20 and 140 mg CaCO3/L. A 20-fold lower LC50-value was recorded in soft test water. The effects of water hardness on the LC50 values are confounded by precipitation reactions that occur at the very high Cd concentrations. Pickering and Henderson (1966) also found changes in pH and acidity of the test water when cadmium salts were added to hard water. The water became milky, insoluble hydroxide and/or basic salts of cadmium were precipitated and lowered the pH of the test water. Carroll et al. (1979) compared cadmium toxicity in the presence of either Ca, Mg en Na salts at equal total salt concentrations. Calcium salts were most efficient in reducing the toxic action of Cd. Hall et al. (1986) compared Cd toxicity to Pimephales promelas in synthetic water with hardness 120 mg CaCO3/L with that in well water with hardness 200 mg CaCO3/L. The LC50 values were statistically not different in both media.

Toxicity values smaller then < 1 µg L-1 are found in very soft waters. Rombough and Garside (1982) tested Cd toxicity for alevins of Salmo salar in soft water with hardness ranging between 19 and 28 mg CaCO3/L.  Biomass production per female, an endpoint combining reproduction, survival of alevins and their growth, was significantly reduced at a Cd concentration of 0.78 µg L-1.  Chapman (1978) tested mortality of different juvenile stages of Oncorhynchus tsahwytscha in soft well water with hardness 23 mg CaCO3/L. After 8.3 days, LC50 values of parr and smolts stages were found at Cd concentration of 0.9 and 1.6 µg Cd/L respectively. Benoit et al.(1976) exposed three generations of Salvelinus fontinalis to several concentrations of Cd in Lake Superior water (H 42-47 mg CaCO3/L) . The total weight of young produced per female of the second generation was significantly reduced at a Cd concentration of 1.7 µg L-1. No effect was found at a concentration of 0.9 µg Cd/L. Sjöbeck et al. (1984) studied Cd toxicity to Perca fluviatilis in a field investigation of river Emån (Sweden, H 40-50 mg CaCO3/L). Downstream from a former source of Cd pollution, an activated immune defence system was found in perch compared to reference perch living in the same river upstream of the contamination source. Upstream of the source, Cd concentration is below 0.05 µg L-1 and downstream Cd concentrations are 0.1-0.2 µg L-1. This test calls for a detailed analysis because it shows the lowest LOEC value in the entire data set of reviewed tests. The test is, however, excluded in the current risk assessment (RI 4) for various reasons.  First of all, only two test concentrations (upstream/downstream) were studied. Secondly, the statistics of the experimental design are questionable, as only one reference site but three contaminated sites were studied (confounding factors cannot be excluded). Thirdly, the river was contaminated in the past with both Cd and Ni and it is unknown how these two metals interact. A fourth remark is that the uptake of food with elevated Cd (benthic organisms dwelling in the sediment with elevated Cd due to the historical pollution) might have been an important Cd exposure in this investigation (see also above in section 3.2.1.1.2). This implies that the solution LOEC does not reflect the risk.  Last of all, the authors note that it is difficult to evaluate the ecological significance of the sublethal endpoint (Sjöbeck et al. 1984).

Canton and Slooff (1982) illustrate to what extent sensitivity to Cd varies among several species. The LC50 values vary from 30 to 3800 (g L-1 at water hardness H= 100 mg CaCO3 L-1 and from 20 to 11100 (g L-1 at H= 200 mg CaCO3 L-1 between 6 fish species. Phipps and Holcombe (1985) studied acute cadmium toxicity to 6 fish species and recorded a fish sensitivity factor (highest fish 96h LC50/lowest fish 96h LC50) of about 9. Dave et al. (1981) found rainbow trout to be more sensitive than zebrafish during their embryo-larval stage. Eaton et al. (1978) found greater sensitivity of two salmonid species, whereas Chapman (1978) noticed that steelhead was consistently more sensitive to cadmium than chinook salmon. Pickering and Henderson (1966) found that 96h LC50 values for fathead minnows were significantly lower than those for bluegills. The LC50 values for fathead minnows were also lower than those for goldfish.

Different toxicity tests studied cadmium sensitivity at different life stages. Chapman (1978) found newly hatched alevins of both chinook salmon and brook trout to be much more tolerant than later juvenile forms. Toxic Cd concentration were very low (lowest LC50 value was found at 0.9µg L-1) but it should be noted that tests were performed in very soft well water of only 23 mg CaCO3/L. The toxicity tests of Eaton et al. (1978) indicated that larvae or juveniles were in all cases more sensitive than embryos. In contrast, Spehar (1976) demonstrated that stages of spawning and embryo production were the most sensitive for Jordanella floridae. Benoit et al. (1976) found males of brook trout to be more sensitive than females. At a cadmium concentration of 3.4 µg L-1, both pre-exposed and not pre-exposed males became extremely hyperactive during spawning and suddenly died. Weights (growth) of 16-week old juveniles were also significantly less than weights of control fish. Hatch and survival of brook trout through the juvenile stage were not affected at 6.4 µg L-1. Pickering and Gast (1972) found a statistically significant effect of cadmium toxicity at 27 µg Cd/L on hatchability of Pimephales promelas. At lower cadmium concentrations they also noticed a sudden increase in the number of eggs produced. Rombough and Garside (1982) found Atlantic salmon alevins to be considerably more sensitive to cadmium than the embryos. Alevins became substantially more sensitive near the completion of yolk absorption.

Increasing exposure time generally increases the Cd concentration in target organs, resulting in an increasing severity of observed effects (Pickering and Henderson 1966, Eaton et al., 1978, Spehar, 1976, Carroll et al., 1979, Phipps and Holcombe, 1985, McCarty et al., 1978). Carroll et al. (1979) recorded a 2- to 5-fold decrease in the LC50 value for Salvelinus fontinalis from 24 to 96h. McCarty et al. (1978) found a 2-fold reduction in the LC50-value for Carassius auratus from 2 to 10 days.

Besides growth, reproduction and survival, other parameters have been studied when assessing toxicity of cadmium to fish. Muramoto (1981) observed vertebral column damage of Cyprinus carpio during 47 days. Bishop and McIntosh (1981) evaluated the use of ventilation rate and cough rate to predict the chronic toxicity of cadmium to bluegill. At cadmium concentrations lower than 1 % of the LC50 value of bluegill, the ventilation rate and cough rate of bluegill were increased. Changes in cough rate were correlated with cadmium exposure. This test has not been selected for the risk assessment since it is an acute test.  Arillo et al. (1984) investigated the biochemical responses to low cadmium concentrations in Salmo gairdneri. Blood, liver and mitochondrial enzymes are sensitive to cadmium and their activity was altered when exposed to 10 µg Cd/L. The activity of the enzymes antioxidase and lipid peroxidase was only reduced at a Cd concentration of 620 µg Cd/L. This test was neither selected because of unknown ecological relevance of the test results.  Venugopal et al. (1997) found a reduction of more than 50% at this concentration. Karlsson-Norrgren et al. (1985) recorded a change in gill morphology at 10 µg Cd/L after 6 weeks of exposure. Lowe-Jinde and Niimi (1984) found short- and long-term effects of cadmium on glycogen reserves and liver size of rainbow trout.

In conclusion, lowest effect concentrations for fish were found at 0.8 µg L-1. Toxicity is most pronounced in soft water. One reliable EC50 and one LOEC value were found below 1 µg L-1. These values refer to tests performed at water hardness < 50 mg CaCO3/L. Reproduction parameters are most sensitively affected by Cd.

Table 3.2.2: toxicity to fish/amphibians. All underlined data are selected to discuss the critical concentrations (table 3.2.1). Bold data are used to estimate the HC5 (table 3.2.10). Data with reliability index 4 are given as supporting information but they are not used in the effects assessment.

| test substance | organism | medium | test conditions | Nominal/ Measured | Dura tion (d) | Acute/ chronic | endpoint | NOEC (µg L-1) | Cat.* | LOEC (µg L-1) (%effect) | EC50 (µg L-1) (%effect) | LC50 (µg L-1) (%effect) | references | R.I. |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| CdCl2 | Salmo salar | municipal water charcoal filtered and UV sterilised; BC 0.13 µg Cd/L; pH 6.5-7.3; T 5-10; DO 11.1-12.5; Al 14-17; H 19-28 | semi-static | M | 24 46 | A C | mortality total biomass | 0.47 | 1 | 0.78(28) |  | 34 | Rombough and Garside, 1982 | 2 2 |
| CdCl2 | Catostomus commersoni | sand filtered Lake Superior Water; continuous flow; DO 10.3; H 45; Al 41; Ac 3; pH 7.6 | T 18.1 | M | 30 | C | standing crop (biomass) | 4.2 | 1 | 12 |  |  | Eaton et al., 1978 | 2 |
|  | Esox lucius |  | T 15.9 |  | 28 | C | biomass | 4.2 | 1 | 12.9 |  |  |  | 2 |
|  | Oncorhynchus kisutch (sac fry |  | T 10.1 |  | 27 | C | biomass | 1.3 | 1 | 3.4 |  |  |  | 2 |
|  | Oncorhynchus kisutch |  | T 9.7 |  | 27 | C | biomass | 4.1 | 1 | 12.5 |  |  |  | 2 |
|  | Salvelinus namaycush |  | T 9.6 |  | 31 | C | biomass | 4.4 | 1 | 12.3 |  |  |  | 2 |
|  | Salvelinus fontinalis |  | T 9.7 |  | 126 | C | biomass | 1.1 | 1 | 3.8 |  |  |  | 2 |
|  | Salmo trutta |  | T 9.7 |  | 60 | C | biomass | 3.8 | 1 | 11.7 |  |  |  | 2 |
|  | Salmo trutta (late eyed eggs) |  | T 10 |  | 61 | C | biomass | 1.1 | 1 | 3.7 |  |  |  | 2 |
| CdCl2 | Salvelinus fontinalis | sterilised Lake Superior water; H 42-47; pH 7-8; Al 38-46; Ac 1-10; DO 4-12; T 9-15 | continuous flow | M | 3 years | C C C C | mortality growth (weight) of 16 week old juveniles total weight of young /female of the 2nd generation reproduction | 1.7 1.7 0.9 6.4 | 1 1 1 1 | 1.7(31) | 3.4(56) | 3.4 | Benoit et al, 1976 | 2 2 2 2 |
| CdCl2 | Jordanella floridae | untreated Lake Superior water; T 25; DO 8.3; H 44; Al 42; Ac 2.4; pH 7.1-7.8 | continuous flow | M | 4 100 | A C C C | mortality mortality growth reproduction | 8.1 8.1 4.1 | 1 1 1 | 16(27) | 8.1(52) | 2500 16(72) | Spehar, 1976 | 2 2 2 2 |
| CdCl2 | Salmo gairdneri | aerated well water; T 10; O2 7.5; H 375-390; pH 8-8.6 | continuous flow | M | 84 | C | mortality | 12 | 1 | 36 (10) HT |  |  | Lowe-Jinde and Niimi, 1984 | 2 |
| Cd | Salvelinus fontinalis | reconstituted soft water: T 14-16°C; DO 9.3-11.4 mg/L; Cd(BG) <0.2 µg/L; pH 6.3-7.6; H 20 river water: T 14-16°C; DO 8.7-12.2 mg/L; Cd(BG) <4 µg/L; pH 6.6-7.4; H 16-28 | static renewal static renewal | M M | 10 10 | C C C | survival growth survival | 8 18 62 | 1 1 1 | 18 132 |  |  | Jop et al., 1995 | 2 2 2 |
| CdCl2 | Lepomis macrochirus | dechlorinated, carbon-filtered tap water | Static; T 22; DO 8.5; H 18; Al 16; pH 7.4-7.7 | M | 4 | A | mortality |  |  |  |  | 2300 | Bishop and McIntosh, 1981 | 2 |
| CdCl2 | Pimephales promelas Carassius auratus Ictalurus punctatus Lepomis macrochirus( juv) | lake water; T 22.5; DO 7. 5; H 44.4; Al 45.4; pH 7.1-7.8 | continuous flow | M | 4 4 4 4 | A A A A | mortality mortality |  |  |  |  | 1500 748 4480 6470 | Phipps and Holcombe, 1985 | 2 2 2 2 |
| CdCl2 | Barytelphusa guerini | tap water; pH 7.2-7.4; DO 7.8-8 mg L-1, Al 102; H 112; male fish | semi-static | N | 4 | A | mortality |  |  |  |  | 1820 | Venugopal et al., 1997 | 2 |
| Cd-solution | Oncorhynchus tsahwytscha Salmo gairdneri | continuous flow; aerated UV sterilised well water; T 11.6-12.8; Al 22; H 23; DO 10.2; pH 7.1; Cd < 0.2 µg L-1 | newly hatched alevins swim-up alevins 5-8m old parr smolts newly hatched alevins swim-up alevins 5-8m old parr smolts newly hatched alevins swim-up alevins 5-8m old parr smolts newly hatched alevins swim-up alevins 5-8m old parr smolts | M | 4 8.3 4 8.3 | A A A A A A A A A A A A A A A A | mortality |  |  |  |  | > 27 1.3 1.0 > 2.9 > 27 1.3 0.9 1.6 > 26 1.8 3.5 > 2.9 > 26 1.6 2.0 2.3 | Chapman, 1978 | 3 3 3 3 3 3 3 3 3 3 3 3 3 3 3 3 |
| CdCl2 | Brachydanio rerio | synthetic water (changed ISO) ; T 24; DO >80%; H 100; pH 7.2 | semi-static; adults larvae | N | 4 24 36 | A C C | mortality reproduction reproduction | 1 | 1 | 10(35) |  | 3500 | Bresch ., 1982 | 3 |
| CdCl2 | Brachydanio rerio Oryzias latipes Poecilia reticulata Oryzias latipes | tap water; continuous flow; T 20 synthetic water (Dutch standard water); semi-static; T 24 synthetic water (Dutch standard water); semi-static; T 24 tap water; continuous flow; T 20 | H 170 H 200 H 100 H 200 H 100 H 200 H 100 H 200 H 100 | M | 1 2 1 2 3 4 1 2 3 4 1 2 3 4 1 2 3 4 1 2 3 4 1 2 3 4 1 2 3 4 1 2 3 4 18 18 | A A A A A A A A A A A A A A A A A A A A A A A A A A A A A A A A A A C C C C | mortality mortality mortality and abn. behaviour mortality mortality and abn. behaviour mortality mortality and abn. behaviour mortality mortality and abn. behaviour mortality mortality and abn. behaviour | 30 6 6 3 | 1 1 1 1 | 35(25) 23(25) 7(25) 13(25) |  | 7000 4200 >2600 1800 170 130 >2600 470 160 70 >2800 350 350 >2800 320 120 70 33000 20500 14400 11100 31000 19500 12100 11100 10400 5700 4300 3800 7100 5900 3700 3400 50 40 20 30 | Canton and Slooff, 1982 | 3 |
|  | Xenopus laevis | tap water; continuous flow; T 20 | H 170 |  | 1 2 100 | A A C | mortality mortality inhibition of larvae development body weight | 30 9 30 | 1 1 1 |  | 650 | 4000 3200 1500 |  |  |
| CdSO4 | Brachydanio rerio Salmo gairdneri | synthetic water (ISO 1977) ; T 25; pH 8.3; H 100 | static; juvenile fish (0.25g each) semi-static; T 8; embryo-larva | N | 1 4 6 48 | A A A C | mortality median survival time | 4 | 1 | 5(15) |  | 2400 1700 1700 | Dave et al., 1981 | 3 3 3 3 |
| CdSO4 | Pimephaless promelas | pond water diluted with carbon filtered demineralised tap water; H 201-204; DO 6.5-6.6; pH 7.6-7.7; Al 145-161; Ac 8-12; T 16-27 | continuous flow; pond fish continuous flow; 3 week old fry from laboratory static continuous flow | M | 60 104 60 30 4 4 | C C C C C C C C A A | survival of developing embryos hatchability of eggs growth reproduction mortality survival of developing embryos reproduction growth mortality | 37 37 350 13 27 14 110 | 1 1 1 1 1 1 1 | 57(26) 57 37(26) 57(22) 27(24) |  | 68 30000 2000 | Pickering and Gast, 1972 | 3 3 3 3 3 3 3 3 3 3 |
| CdCl2 | Brachydanio rerio | synthetic water; T 25; pH 6.9-7.2; H 12.4 | continuous flow | N | 42 | C | mortality |  |  | 3 (40)LT |  | 10 (60) | Karlsson-Norrgren et al., 1985 | 3 |
| CdCl2 | Cyprinus carpio | tap water; T 18-19; pH 6.8; Al 14.8; H 18, BC 0.001 mg L-1; food < 0.05 µg L-1 | semi-static | N | 47 | C | vertebral column damage |  |  | 10LT |  |  | Muramoto, 1981 | 3 |
| CdSO4 | Salvelinus fontinalis | synthetic soft water (EPA); pH 7.3 - 7.7; T 12 | + 3.10-3 M CaCO3 H 340 - 344; Al 327-332 + 3.10-3 M CaSO4 H 332 - 348; Al 28-30 + 3.10-3 M MgCO3 H 348 - 360; Al 314-324 + 3.10-3 M MgSO4 H 324 - 336; Al 27-32 + 3.10-3 M Na2SO4 H 44 -46; Al 27-34 | N | 4 | A A A A A | mortality |  |  |  |  | 26 29 3.8 4.4 2.4 | Carroll et al., 1979 | 3 3 3 3 3 |
| CdCl2 | Pimephales promelas | well water; pH 7.7; H 200; Al 140; T 22; BC negligible | static | N | 2 4 | A A | mortality |  |  |  |  | 100 90 | Hall et al., 1986 | 3 |
| Cd(NO3)2 | Gambusia affinis | 0.15µm filtered pond water rich in TOC; continuous flow; DO > 90%; Al 4; H 10; pH 5.6; Cd 0.02 µg L-1 0.15 µm filtered well water pour in TOC; continuous flow; ; DO > 90%; Al 9.7; H 11.1; pH 6.5; Cd 0.023 µg L-1 | T 30.2 T 30.7 T 28 T 30.2 T 28 | N | 4 | A A A A A | mortality |  |  |  |  | 1300 1500 2600 900 2200 | Giesy et al., 1977 | 3 3 3 3 3 |
| CdCl2 | Carassius auratus | aerated dechlorinated and aged city water; T 22-25; Cd < 10 µg L-1; Al 14-18; DO 90% | static; H 20 H 140 | N | 2 4 10 2 4 10 | A A A A A A | mortality |  |  |  |  | 2760 2130 1780 46900 46800 40200 | McCarty et al., 1978 | 3 3 3 3 3 3 |
| Supporting data |  |  |  |  |
| CdCl2 | Salmo gairdneri | water; T 15; pH 7.4; DO 90%; H 320 | continuous flow | N | 4 months | C C C C C | activity of: liver enzymes blood enzymes mitochondrial enz gill sialic acid content mucus lysozyme | 1 1 1 1 10 | 1 1 1 1 1 | 10(10) 10(36) 10(20) | 10(75) |  | Arillo et al., 1984 | 4 4 4 4 4 |
| CdSO4 | Brachydanio rerio | synthetic water (ISO 1977) ; T 25; pH 8.3; H 100 | semi-static; embryo-larva | N | 10 | C | median survival | 50(HT) |  |  |  |  | Dave et al., 1981 | 4 |
| Cd | Brachydanio rerio | OECD-203-test water; T 22; pH 7.42; DO 9.3; H 233.4 | static | M | 4 | A | mortality |  |  | 320(20) |  |  | Janssen Pharmaceutica, 1993a | 4 |
| CdO | Brachydanio rerio | OECD-203-test water; T 22; pH 7.82; DO 9.5; H 243.6 | static | M | 4 | A | mortality | 1600 (HT) |  |  |  |  | Janssen Pharmaceutica, 1993b | 4 |
| Cd | Salvelinus fontinalis | river water: T 14-16°C; DO 8.7-12.2 mg/L; Cd(BG) <4 µg/L; pH 6.6-7.4; H 16-28 | static renewal | M | 10 | C | growth | 132 (HT) |  |  |  |  | Jop et al., 1995 | 4 |
| CdCl2 | Lepomis macrochirus | dechlorinated, carbon-filtered tap water | continuous flow; T 14.5-16; pH 7.8-8.2; DO 6.2-8.1; H 340-360; Al 248-264; Cd < 1 µg L-1 | N | 3 | A | cough rate |  |  | 50(35)LT |  |  | Bishop and McIntosh, 1981 | 4 |
| CdCl2 | Barytelphusa guerini | tap water; pH 7.2-7.4; DO 7.8-8 mg L-1, Al 102; H 112; male fish | semi-static | N | 30 | C C | activity of antioxidase lipid peroxidase |  |  |  | 620(80) 620(52) |  | Venugopal et al., 1997 | 4 4 |
| CdCl2 | Pimephales promelas Lepomis macrochirus Carassius auratus Lebistes reticulatus Lepomis cyanellus Pimephales promelas Lepomis cyanellus | synthetic water (5% natural limestone spring water + 95% deionised water); static hard limestone spring water | T 25; DO 7.8; pH 7.5; Al 18; H 20 T 25; DO 7.8; pH 8.2; Al 300; H 360 | N | 4 | A A A A A A A | mortality |  |  |  |  | 630-1050 1940 2340 1270 2840 72600-73500 66000 | Pickering and Henderson, 1966 | 4 4 4 4 4 4 4 |
| Soluble Cd | Perca fluviatilis | River Emån water; T 20-22; H 40-50; pH 6.7; female fish | field study | M | whole life | C | immune defence |  |  |  | 0.1-0.2(45-100)LT |  | Sjöbeck et al., 1984 | 4 |

T = temperature (°C); H = hardness (as mg CaCO3/L); DO = dissolved oxygen (mg O2/L); Al = alkalinity (mg CaCO3/L); Ac = acidity (mg CaCO3/L); *NOEC classification (see section 3.2.0.2); ** days of exposure of embryos and larvae-juveniles

#### Acute and chronic toxicity to aquatic invertebrates

Table 3.2.3: selected data with RI 1-3 for acute and chronic Cd toxicity to aquatic invertebrates. One hundred and two tests were reviewed from 42 source documents and 97 tests were selected.

|  | min | median | max | n |
| --- | --- | --- | --- | --- |
| acute tests |
| E(L)Cx(50 ((g L-1) | 7 | 166 | 74000 | 61 |
| chronic tests |
| NOEC ((g L-1) | 0.16 | 2.0 | 11 | 22 |
| LOEC ((g L-1) | 0.28 | 1.9 | 25 | 19 |
| E(L)Cx(50 ((g L-1) | 1 | 5 | 32 | 14 |

A large number of acute tests were found for invertebrates. Only few chronic studies met all criteria for classification as RI 2.  Certain invertebrates e.g. Daphnia and Ceriodaphnia, appear to be particularly sensitive to cadmium. Most chronic LOEC values of Daphnia range between 1 and 10 µg L-1. The lowest LOEC value is found in well water (H 103 mg CaCO3 L-1, background Cd 0.08 µg L-1, Chapman et al., 1980). The mean number of young per adult after 21 days exposure was reduced at only 0.29 µg L-1 (measured concentration). The NOEC in this test was 0.16 µg L-1.

Toxicity of CdO powder was tested in the 48h acute test with Daphnia magna.  The filtrate of a CdO dispersion was diluted in several series (57-750 (g Cd L-1).  There were no toxic effects up to 250 (g Cd L-1 and there was 70 % mortality at 750 (g Cd L-1).

A wide range of concentrations at which cadmium is toxic to freshwater invertebrates (Table 3.2.3) is found. The acute E(L)Cx(50  values vary from 5 µg L-1 to 74 103 µg L-1.  Canton and Slooff (1982) found a lower LC50 value of 0.67 µg Cd/L and a NOEC value of 0.37 µg Cd/L.  Both values are, however, unreliable because the authors state that it is an extrapolated value below the lowest test concentration (tested concentration range not reported). The extrapolation is based on concentration measurements with flame atomic absorption spectrophotometry (detection limit ~20 µg L-1) does therefore not warrant reliable data.  Differences in species, life stage, exposure time, type of flow system in which experiments were performed, changes in water quality -hardness, pH, alkalinity, temperature and organic fractions- impact cadmium toxicity.

Van Leeuwen et al. (1985) compared both mortality and reproduction characteristics in synthetic water and 50 µm filtered and sterilised IJssel water. The LC50 and LOEC values were both 7 times higher in natural water than in synthetic water. They explain the differences found by differences in speciation of cadmium. In natural water bioavailability of cadmium is reduced through sorption on suspended particles so that biological responses occur at higher cadmium levels. Giesy et al. (1977) also report the influence of particles on bioavailability of cadmium. They compare cadmium toxicity in soft well water containing low organic carbon concentrations to toxicity in soft surface waters containing high concentrations of naturally occurring organic compounds. Toxicity of cadmium was significantly smaller in the organic surface water than in the well water (LC50 values were 35 µg L-1 and 7 µg L-1 respectively). Different molecular organic fractions of this surface water were isolated by ultracentrifugation and were added to the well water. Addition of these fractions resulted in a decrease in Cd toxicity (an increase of the LC50 value from 7 µg L-1 to 16.5 µg L-1). Adding the smallest fraction (<0.9 nm) however increased Cd toxicity.  Both effects of cadmium sorption to suspended particles and cadmium complexation by dissolved organic carbon confirm the free ion theory as described above (3.2.1, introduction). Schuytema et al. (1984) compared Cd toxicity in soft well water with toxicity in a water-sediment system. In well water toxic concentrations were expressed as total measured concentrations, in the sediment-water system as dissolved measured concentrations. They found similar LC50 values in both systems demonstrating that the dissolved fraction in sediment-water systems is the bioavailable fraction. Hall et al. (1986) tested cadmium toxicity on different water flea species in both synthetic and well water. They report that the different water types did not affect the cadmium toxicity to the different species tested.

Acclimation of a species or a population generally decreases the sensitivity to toxic compounds. Lam (1996) collected adolescent Brotia hainanensis (snails) from sites either upstream or downstream of a Cd polluting source. The downstream snails were more tolerant to cadmium than upstream snails even after laboratory acclimation for one week. Similar interpopulation differences persisted in the first generation (F1) juveniles (< 2d olds) which were descendants of laboratory-cultured snails. These differences in metal tolerance in the F1 juveniles disappeared after the juveniles had been cultured under identical laboratory conditions for one week. Bodar et al. (1990) found Daphnia magna pre-exposed to sublethal Cd concentrations to become more resistant to cadmium.

Cadmium toxicity generally increases with increasing exposure time. Van Leeuwen et al. (1985) report a gradual decline in the LC50 values for daphnids with time from 10 µg L-1 to 2 µg L-1 in synthetic water until a constant level was reached after about 2 weeks. In 50 µm filtered Lake IJssel water the LC50 declined from 24 µg L-1 after 14 days to 14 µg L-1 after 21 days. Attar and Maly (1982) obtained LC50 values, which varied between 204 µg L-1 if calculated at 36h and 5 µg L-1 if calculated at 96h. Biesinger and Christensen (1972) found a fourteen-fold decrease of the LC50 value for Daphnia magna, in filtered Lake Superior water, from exposure day 2 to 21. Canton and Slooff (1982) performed a similar test in synthetic water and found an even bigger decrease of the LC50 value, from 30 µg Cd/L to 0.67 µg Cd/L. In the same test the NOEC data for mortality showed a similar trend. The background Cd of the test medium and test concentration range is unknown. Furthermore, it is not known if thresholds below 1 µg L-1 are calculated by extrapolation outside the tested concentration range. Therefore, these data are considered as unreliable. Spehar et al. (1978) record an eleven-fold decrease of the LC50 value for snails between 7 days and 28 days. For mayfly no significant effects on mortality were observed until the fourth week of exposure at which 3 µg L-1 caused 70% mortality.

The marked effects of increasing water hardness reducing cadmium toxicity are extensively reported (see also 3.2.1.6.4).

The importance of species differences -over and within different trophic levels- is illustrated by the experiments of Canton and Slooff (1982), Baudouin and Scoppa (1974), Warnick and Bell (1969), Williams et al. (1985), Winner (1988), Fennikoh et al. (1978), Hall et al. (1986) and Ingersoll and Kemble (2000). Canton and Slooff (1982) studied short- and long-term toxicity of cadmium to different freshwater organisms of different trophic levels. Bacteria, algae, crustaceans, fishes and amphibians were studied. In both short- and long-term studies, Daphnia magna was the most sensitive organism. Baudouin and Scoppa (1974) compared cadmium toxicity to three most representative freshwater zooplankton (Cyclops abyssorum prealpinus, Eudiaptomus padanus padanus, Daphnia hyalina) of Lake Monate -an unpolluted subalpine lake of Italy- and also found Daphnia sp. to be the most sensitive. Williams et al. (1985) studied cadmium toxicity on ten freshwater macroinvertebrates. Results indicated a wide range of species sensitivity. Members of the crustacean (Gammarus sp.) appear the most sensitive (LC50 20 µg L-1) whilst insect species of the orders Plecoptera and Trichoptera exhibit high short-period tolerance to cadmium poisoning (LC50 520 103 µg L-1). Warnick and Bell (1969) studied 3 aquatic insects from which mayfly (Ephemerella subvaria) is the most sensitive. Hall et al. (1986) compared the sensitivity of different water flea species to cadmium. No difference in species sensitivity was reported. Ingersoll and Kemble (2000) compared Cd toxicity to Hyalella azteca and Chironomus tentans in well water. They found Hyalella azteca to be the most sensitive.

Different toxicity tests demonstrate cadmium sensitivity to be depended on life stages. Wier and Walter (1976) found mature Physa gyrina to be much more tolerant than immature snails. Nebeker et al. (1986a) noted new-born Daphnia's to be more resistant to Cd than test organisms of several days old. Sensitivity to Cd was also found to be dependent on the size of the neonates. Enserink et al. (1990) demonstrated larger neonates to be more resistant than smaller neonates.

Several reproduction parameters are used as toxic endpoints. Van Leeuwen et al (1985) tested the effects of Cd on the number of offspring and the delay in the reproduction. Both parameters are based on individuals. From a 3-week life table study the authors calculated ‘the intrinsic rate of natural reproduction’ which integrates both age-specific survival and reproduction and found this a better test parameter. Bertram and Hart (1979) investigated the effect of cadmium on survival and reproduction capacity of Daphnia pulex. Cadmium at 5 µg L-1 reduced the average longevity. Reproduction parameters such as the number of broods per adult, the number of young per brood, the number of progeny per adult, the intrinsic rate of natural increase or the mean generation time were already affected at 1 µg L-1.  Elnabarawy et al. (1986) also found reproduction to be more sensitive to Cd than mortality for several daphnids. Both LOEC- and NOEC-values were below 1 µg L-1. The same conclusion is drawn for the very low effect values on reproduction and growth found by Biesinger and Christensen (1972). A LOEC value of 0.17 µg Cd L-1 for reproduction was found by extrapolation beyond the test concentrations. Bodar et al. (1988a) note the change in the reproduction strategy of Daphnia magna which produce larger broods with smaller neonates at low cadmium concentrations (< 5 µg L-1). At higher cadmium concentrations (> 5 µg L-1) brood size and body size decline and the average number of days to the first brood increases.

Sublethal endpoints of Daphnia can be very sensitive to Cd. The haemoglobin content decreased by 20 % when Daphnia was exposed to only 0.1 µg L-1 Cd for 16 days (Berglind, 1985). However, at Cd exposure between 0.2-1.6 µg L-1, no differences with the control value were found. Bodar et al. (1988b) found a decrease of 60% in the chlorella consumption rate of Daphnia magna at a cadmium concentration of 5 µg L-1.

In conclusion, Cd can effect primary consumers in the µg L-1 range and below. Reproduction was found to be the most sensitive endpoint. Different effect data smaller than 1 µg L-1 were found. However, several of those values are considered unreliable because they were obtained by extrapolation, or because they are expressed as nominal concentrations without information on background Cd concentration in the test medium.

Table 3.2.4: toxicity to aquatic invertebrates. All underlined data are selected to discuss the critical concentrations (table 3.2.3). Bold data are used to estimate the HC5 (table 3.2.10). Data with reliability index 4 are given as supporting information but they are not used in the effect assessment.

| test substance | Organism | medium | test conditions | Nominal/ Measured | Duration (d) | acute/ chronic | endpoint | NOEC (µg L-1) | Cat.* | LOEC (µg L-1) (%effect) | EC50 (µg L-1) (%effect) | LC50 (µg L-1) (%effect) | references | RI |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Cd (filtrate of dispersion) | Daphnia magna | OECD 202-test medium; pH 7.76; DO 9.6; H 274; T 20.2 | static | M | 2 | A | mortality |  |  | 40(30) |  | 110(70) | Janssen Pharmaceutica, 1993c | 1 2 |
| CdCl2 | Daphnia magna | synthetic water; T 25; pH 8; H 11; DO 69% | semi-static | M | 1 21 | A C | mortality reproduction | 0.6 | 1 | 1.9 | 1900 |  | Kühn et al., 1989 | 2 2 |
| CdCl2 | Daphnia magna | aerated well water; DO >70%; pH 8; T 22; H 300; Al 250 | continuous | M | 21 | C C | mortality reproduction | 4.3 0.8 | 1 1 |  | 2.1(54) | 7.2 (100) | Knowles and McKee, 1987 | 2 2 |
| CdCl2 | Aplexa hypnorum mature immature | Lake Superior water; DO 7.5; T 24 | continuous flow H 44.8; Al 40.7; pH 7.4-7.5; H 45.3; Al 40.3; pH 7.3-7.6 | M | 4 26 | A C C | mortality growth mortality+hatchability | 4.41 4.41 | 1 1 |  | 4.79(47) 4.79(62) | 93 | Holcombe et al., 1984 | 2 2 2 |
| CdCl2 | Physa integra Ephemerella sp. | untreated Lake Superior water; pH 7.1-7.7; T 15; DO 10-11; H 44-48; Al 40-44; Ac 1.9-3 | semi-static | M | 21 28 28 | C C C | mortality | 8.3 | 1 |  |  | 10.4 3(70) | Spehar et al., 1978 | 2 2 2 |
| CdO (filtrate of dispersion) | Daphnia magna | OECD 202-test medium; pH 8.05; DO 9.3; H 226; T 19.1 | static | M | 2 | A | mortality |  |  |  |  | 750(70) | Janssen Pharmaceutica, 1993d | 2 |
| CdCl2 | Daphnia magna | dechlorinated Montreal city water; pH 6.95; T 20; Al 80; H 130; Cd 1µg L-1 | continuous flow | N | 1.5 2 2.5 3 4 | A A A A A | mortality |  |  |  |  | 203.8 58.16 15.8 8.88 5 | Attar and Maly, 1982 | 2 2 2 2 2 |
| CdCl2 | Daphnia magna Daphnia pulex | synthetic water; static; pH 8-8.5 | H 160-180; T 20 H 80-100; T 20 | N | 2 | A | mortality |  |  |  |  | 38 42 | Lewis and Horning, 1991 | 2 2 |
| CdCl2 | Daphnia magna | soft well water; H 26-32; Al 30; T 20; DO 7.5-9; pH 6.6-7.8 slurry; T 20; H 15-23; Al 10-15; DO 7.5-9; pH 6.1-7.1 (LC50 expressed on dissolved fraction) | static continuous 100 mg L-1 total solids, static continuous 1000 mg L-1 total solids, static continuous | M | 2 | A A A A A A | mortality |  |  |  |  | 36 49 39 144 44 97 | Schuytema et al., 1984 | 2 2 2 2 2 2 |
| Cd | Ceriodaphnia dubia | reconstituted soft water: T 14-16°C; DO 9.3-11.4 mg/L; Cd(BG) <0.2 µg/L; pH 6.3-7.6; H 20 river water: T 14-16°C; DO 8.7-12.2 mg/L; Cd(BG) <4 µg/L; pH 6.6-7.4; H 16-28 | static renewal static renewal | M M | 7 7 | C C C | survival reproduction survival reproduction | 19 10 19 11 | 1 1 1 1 | 41 19 39 19 |  |  | Jop et al., 1995 | 2 2 2 2 |
| CdCl2 | Daphnia magna | well water: T 20±2°C; DO 4.9-7.9; Cd(BG) 0.08 pH 7.5, H 53 pH 7.9, H 103 pH 8.2, H 209 | static renewal | M | 21 | C | reproduction (mean number of young per adult) | 0.16 0.21 | 3 3 | 0.29 0.28 0.91 |  |  | Chapman et al., 1980 | 3 3 3 |
| Cd | Hyalella azteca Chironomus tentans | well water: T 23°C; pH 7.8; H 280 | flow-through | M M | 42 20 | C C | survival reproduction weight biomass %emergence %hatch | 0.51 1.9 5.8 5.8 5.8 5.8 | 1 1 1 1 1 1 | 1.9 3.2 17.4 17.4 17.4 17.4 |  |  | Ingersoll and Kemble, 2000 | 3 3 3 3 3 3 |
| CdCl2 | Daphnia magna Daphnia pulex Ceriodaphnia reticulata Daphnia magna Daphnia pulex | unchlorinated, carbon filtered well water, aerated to saturation; H 240; Al 230; pH 8; DO >5; T 23; Cd < 0.01 µg Cd/L | static semi-static | N | 2 14 | A A A C C | mortality reproductive impairment | 2.5 7.5 | 1 1 | 25 (32) | 7.5 (75) | 178 319 184 | Elnabarawy et al., 1986 | 3 3 3 3 3 |
|  | Ceriodaphnia reticulata |  |  |  | 7 | C |  | 0.25 | 1 | 0.75 (20) |  |  |  | 3 |
| CdCl2 | Daphnia magna | 20 µm cloth filtered Lake Superior water; pH 7.7; H 45.3; Al 42.3; DO 9; T 18; | semi-continuous flow; without food with food | N | 2 21 | A C C C C | mortality mortality weight/animal protein conc./animal GOT activity/animal | 1 1 | 3 3 | 1(15) |  | 65 5 | Biesinger and Christensen, 1972 | 3 3 3 3 3 |
| CdCl2 | Daphnia pulex | Whatman N° 1 filtered Lake Champlain water; pH 7.7; Al 42.4; H 65; Cd < 1µg L-1 | static semi-continuous flow | N | 3 4 104 | A A C C C | mortality mortality longevity brood size generation time in days | 1 | 3 | 1(37)LT 1(19)LT | 5(57) | 62 47 | Bertram and Hart, 1979 | 3 3 3 3 3 |
| CdCl2 | Daphnia magna | Dutch standard water; T 19 | semi-static H 200 H 100 | M(>20µg L-1) | 2 2 | A A | mortality mortality |  |  |  |  | 30 30 | Canton and Slooff, 1982 | 3 3 |
| CdSO4 | Ceriodaphnia dubia Daphnia magna | Synthetic water; H 90; Al 65; T 25 | static | N | 7 | C C | mortality reproduction | 1.5 2 | 1 1 | 2(40) 3(30) |  | 3(70) | Winner, 1988 | 3 3 |
| CdCl2 | Daphnia magna | NPR synthetic water; pH 8.4; T 20; H 200 50 µm filtered and sterilised Lake IJssel water; pH 8.1; T 20; H 224 | semi-static semi-continuous flow semi-static | N M N | 21 21 21 | C C C C | intrinsic rate of natural increase mortality yield intrinsic rate of natural increase | 1 1 3.2 | 1 1 1 | 1.8(32.5) 1.8 (17) 0.3(36)LT 10 (14.5) | 32(100) 32 (100) | 3.2 (88) | Van Leeuwen et al., 1985 | 3 3 3 3 |
| CdCl2 | Daphnia galeata mendotae | 10 µm filtered Lake Michigan water; T 18.5 H 120 | semi-continuous flow | N | 154 | C C C C C C C C | carrying capacity number of individuals average biomass average birth rate average death rate brood size dry weight life expectancy | 2 2 2 2 2 4 | 1 1 1 1 1 1 | 4(23) 4(9) 4(36) | 7.7(50) 8(58) 4(71) 4(70) 5(54) 8(71) 5(50) |  | Marshall, 1978 | 3 3 3 3 3 3 3 3 |
| CdCl2 | Daphnia magna | culture medium; pH8.4; H 150; T 20 | semi-continuous flow | N | 25 | C C C | mortality biomass production/female intrinsic rate of natural increase | 2.5 2.5 5 | 4 4 3 | 10(34) | 10(71) 20(72) | 10(60) | Bodar et al., 1988a | 3 3 3 |
| CdCl2 | Simocephalus serrulatus Gammarus pseudolimnaeus Daphnia magna Ceriodaphnia reticulata Simocephalus vetulus Simocephalus serrulatus Gammarus pseudolimnaeus Hyalella azteca Paraleptophlebia praepedita | synthetic water; H 39-48; Al 26-42; Ac 1.9-5.7; pH 7-7.9 unfiltered river water; static; H 55-79 Ac 2-4.2; Al 41-65; pH 7.2-7.8 | static T 20; <1d old T 17; 0.1g T 20; <1d old T 20; <1d old T 20; <1d old T 20; <1d old T 17; 0.1g T 7; 1µg T 12; 2µg | M | 2 4 2 2 9 2 2 4 4 4 | A A A A C A A A A A | mortality reproduction mortality | 3.4 | 1 | 7.2 |  | 24.5 68.3 166 129 89.3 123 54.4 285 449 | Spehar and Carlson, 1984 | 3 3 3 3 3 3 3 3 3 3 |
| CdCl2 | Dugesia sp. Cyclops sp. Cypridopsis sp. Hyalella sp. Procambarus sp. | non aerated spring water; T 23; H 20 | static | N | 4 | A A A A A | mortality |  |  |  |  | 4900 340 190 85 5000 | Fennikoh et al., 1978 | 3 3 3 3 3 |
| CdCl2 | Daphnia magna | Dutch Standard water NPR 6503 (1980); pH 8.4; H 150; T 20 | semi-continuous flow | N | 2 | A | mean survival time of embryos |  |  | 1000(37) (LT) | 10000(87) |  | Bodar et al., 1989 | 3 |
| CdCl2 | Daphnia magna | Dutch Standard water NPR 6503 (1980); pH 8.4; H 150; T 20 | semi-continuous flow | N | 14 | C C | body weight consumption rate | 1 | 1 |  | 1(56) 5(60) |  | Bodar et al., 1988b | 3 3 |
| CdSO4 | Tubifex tubifex | dilution water for BOD without phosphate buffer dilution water for BOD with phosphate buffer: drinking water | pH 6.85; H 34.2; Al 1.5 pH 6.85; H 34.2; Al 22.5 pH 7.32; H 261; Al 234; T 20 | N | 2 | A A A | mortality |  |  |  |  | 31 45 720 | Brkovic-Popovic and Popovic, 1977 | 3 3 3 |
| Cd(NO3)2 | Simocephalus serrulatus | filtered (0.15µm ) well water; Cd 0.023 µg L-1; pH 6.5; H 11.1; Al 9.7; T 22; DO >80% Skinface pond water; filtered through 0.15µm; Cd 0.02 µg L-1; pH 5.6; H 10; Al 4; T 22; DO >80% | filtered well water filtered well water + F1** filtered well water + F2** filtered well water + F3** filtered well water + F4** | N | 2 | A A A A A A | mortality |  |  |  |  | 7 8.6 12 16.5 3.6 35 | Giesy et al., 1977 | 3 3 3 3 3 3 |
| Cd-solution | Gammarus pulex Asellus aquaticus Baetis rhodani Physa fontinalis Limnodrilus hoffmeisteri Ephemerella ignita Leuctra inermis Polycelis tenius Chironomus riparius Hydropsyche angustipennis | dechlorinated tap water; pH 7.7; T 12; H 152; DO >96% | continuous flow | M | 4 | A A A A A A A A A A | mortality |  |  |  |  | 20 600 500 800 2400 13000 32000 74000 30000 52000 | Williams et al., 1985 | 3 3 3 3 3 3 3 3 3 3 |
| CdCl2 | Daphnia magna | well water; T 19.5; H 32-76; Al 31-69; pH 6.8-7.8 | semi-static <4h old <24h old 1d old 2d old 3d old 4d old 5d old 6d old | M | 2 | A A A A A A A A | mortality |  |  |  |  | 109 46 48 164 63 82 49 23 | Nebeker et al., 1986a | 3 3 3 3 3 3 3 3 |
| CdCl2 | Daphnia pulex Daphnia magna Ceriodaphnia reticulata Daphnia pulex Daphnia magna Ceriodaphnia reticulata | synthetic water; pH 7.8; T 22 well water; pH 7.7; T 22 | static; H 120; Al 110 static; H 200; Al 140; | N | 2 2 | A A A A A A | mortality |  |  |  |  | 90 35 110 90 65 80 | Hall et al., 1986 | 3 3 3 3 3 3 |
| CdSO4 | Daphnia magna | synthetic water (ISO 1977); pH 7.8; H 200; T 20-23 | static | N | 1 2 3 | A A A | mortality |  |  |  |  | 309 69 40 | Dave et al., 1981 | 3 3 3 |
| CdSO4 | Cyclops abyssorum prealpinus Eudiaptomus padanus padanus Daphnia hyalina | 5µm filtered Lake Monate water; pH 7.2; H 40.7; T 10 |  | N | 2 | A A A | mortality |  |  |  |  | 3800 550 55 | Baudouin and Scoppa, 1974 | 3 3 3 |
| CdCl2 | Daphnia magna | synthetic water; T 20; pH 8.3; H 250 | semi-static; small neonates large neonates | N | 2 | A A | mortality |  |  |  |  | 98 294 | Enserink et al., 1990 | 3 3 |
| CdCl2 | Daphnia magna | synthetic water; T 20; pH 8.4; H 150 | static; pre-exposed to control pre-exposed to 1µg Cd/L pre-exposed to 5 µg Cd/L | N | 2 2 2 | A A A | mortality |  |  |  |  | 320 391 424 | Bodar et al., 1990 | 3 3 3 |
| Cd-solution | Physa gyrina mature immature | synthetic water; T 20-22; DO 10-14; H 200; Al 130; pH 6.73; Cd < 0.5µg L-1 | static | N | 1 2 4 9.5 2 4 | A A A A A A | mortality |  |  |  |  | 7600 4250 1370 830 690 410 | Wier and Walter, 1976 | 3 3 3 3 3 3 |
| CdCl2 | Brotia hainanensis | aerated artificial pond water; T 20: pH 7.4;H 200 | upstream adolescents downstream adolescents upstr. juv. <2d downstr. juv. <2d upstr. juv. >7d downstr. juv. >7d | N | 4 | A A A A A A | mortality |  |  |  |  | 15210 35940 770 1090 1180 1220 | Lam, 1996 | 3 3 3 3 3 3 |
| CdSO4 | Daphnia magna | filtered aerated tubewell hard water; H 240, T 13; pH 7.6; DO 5.6; Al 400 | static | M | 2 | A | mortality |  |  |  |  | 1880 | Khangarot and Ray, 1989 | 3 |
| CdSO4 | Acroneuria lycorias Ephemerella subvaria Hydropsyche betteni | carbon filtered Lake Superior tap water; pH 7-7.3; T 18.5; DO 8; Al 54-60; Ac 6-12; H 52-56 |  | N | 14 4 10 | A A A | mortality |  |  |  |  | 32000 2000 32000 | Warnick and Bell, 1969 | 3 3 3 |
| Supporting data |
| CdCl2 | Pteronarcys dorsata Hydropsyche betteni | untreated Lake Superior water; pH 7.1-7.7; T 15; DO 10-11; H 44-48; Al 40-44; Ac 1.9-3 | semi-static | M | 28 28 | C C | mortality | 238 (HT) 238 (HT) |  |  |  |  | Spehar et al., 1978 | 4 4 |
| CdCl2 | Daphnia magna Daphnia pulex Ceriodaphnia reticulata | unchlorinated, carbon filtered well water, aerated to saturation; H 240; Al 230; pH 8; DO >5; T 23; Cd < 0.01 µg/L | semi-static | N | 14 7 | C C C | mortality | 25(HT) 25(HT) 25(HT) |  |  |  |  | Elnabarawy et al., 1986 | 4 4 4 |
| CdCl2 | Daphnia magna | 20 µm cloth filtered Lake Superior water; pH 7.7; H 45.3; Al 42.3; DO 9; T 18; | semi-continuous flow | N | 21 | C | reproductive impairment |  |  | 0.17 (16) | 0.7 |  | Biesinger and Christensen, 1972 | 4 |
| CdCl2 | Daphnia magna | Dutch standard water; T 19 | semi-static H200 | M(>20µg L-1) | 20 20 | C C | mortality reproduction | 0.37 0.5 | 5 1 |  | 4.2 | 0.67 | Canton and Slooff, 1982 | 4 4/3 |
| Cd | Hyalella azteca Chironomus tentans | well water: T 23°C; pH 7.8; H 280 | flow-through | M M | 42 20 | C C | length weight biomass survival number of eggs | 3.2 (HT) 3.2 (HT) 3.2 (HT) 17.4 (HT) 17.4 (HT) |  |  |  |  | Ingersoll and Kemble, 2000 | 4 4 4 4 4 |
| CdSO4 | Daphnia magna Ceriodaphnia dubia | synthetic water; H 90; Al 65; T 25 | static | N | 7 | C C | mortality reproduction | 3(HT) 0.5 | 2 | 1(45) |  |  | Winner, 1988 | 4 4/3 |
| CdCl2 | Daphnia magna | hard synthetic water; H 250; T 20; DO 66-100%; pH 7.2-8.2 | semi-static | N | 16 | C | growth | 1.6(HT) |  |  |  |  | Berglind, 1985 | 4 |
| CdCl2 | Tetrahymena sp. | Osterhouts medium |  | N | 15 min. | A | ciliate chemotactic response inhibition |  |  | 250 | 475 |  | Berk et al., 1985 | 4 |

T = temperature (°C); H = hardness (as mg CaCO3/L); DO = dissolved oxygen (mg O2/L); Al = alkalinity (mg CaCO3/L); Ac = acidity (mg CaCO3/L); *NOEC classification (see section 3.2.0.2); **organic fractions F1: > 0.0183 µm; F2: 0.0183 - 0.0032 µm; F3: 0.0032 - 0.0009 µm; F4: < 0.0009 µm; GOT: glutamic oxalacetic transaminase;

#### Toxicity to primary producers.

Table 3.2.5: selected data with RI 1-3 for Cd toxicity to primary producers. Twenty-nine tests were reviewed from 21 source documents and 20 tests were selected. All tests were considered to represent chronic exposure to Cd.

|  | min | median | max | n |
| --- | --- | --- | --- | --- |
| NOEC ((g L-1) | 0.85 | 6.9 | 31 | 8 |
| LOEC ((g L-1) | 1.9 | 18 | 100 | 9 |
| E(L)Cx(50 ((g L-1) | 6.1 | 59 | 1000 | 12 |

Various studies reveal the toxicity of Cd, added as soluble salts, on algae, diatomic species, floating weeds and bacteria (Table 3.2.5). Two studies are dealing with toxicity of CdO following the OECD-201 protocol for testing growth inhibition of algae (Janssen Pharmaceutica, 1993f, LISEC 1998b).  These tests were performed in filtrates (0.1 µm or 0.45 µm pore size) of a CdO dispersion made up in the test medium.  The metal oxide was dispersed in the test medium and membrane filtered. The Cd concentration in the filtrate was analysed and dilutions of the filtrate in test solution were inoculated with algae cells. Growth rate of Selenastrum capricornutum was reduced by 50% at Cd concentrations between 80-120 µg L-1 with CdO as test substance (LISEC 1998b, Janssen Pharmaceutica 1993f). A similar test was performed with filtrates of a dispersion of metallic Cd powder (LISEC 1998a, Janssen Pharmaceutica 1993e).  The EC50 values for growth were 70-89 µg L-1 with Cd as test substance, similar to the values obtained with the CdO filtrates. This indicates that the filtrates of the CdO and metallic Cd dispersions have the same Cd speciation, i.e. predominantly Cd2+ ions.

Most reported LOEC values for algae or diatomic species range between 10 and 50 µg L-1 with some exceptions. Four effect concentrations were noted below that range. In general terms, metal toxicity to algae increases with decreasing nutrient supply, decreasing cell density and with decreasing concentrations of chelating agents (Chen and Lin, 1997). Those studies in which synthetic chelates have been used in solution are omitted from this review except when these concentrations are low enough to warrant little Cd complexation. It appears that Cd toxicity is far more pronounced in flow through systems compared to static experiments (Chen and Lin, 1997). The type of Cd2+ salts (Cl, NO3-, acetate or carbonate) was found not to affect Cd2+ toxicity (Wong et al., 1979).

Wong and co-workers (1979) followed growth (as cell number) in static conditions of Ankistrodesmus falcatus during 10 days after applying Cd2+ salts to a synthetic medium. The cell number was reduced to 60 % of the control after 6 days exposure to 1000 µg L-1. At 500 µg L-1, no toxic effect was yet clear.  A NOEC of Cd at 500 µg L-1 is rather high compared to that of other studies (see Table 3.2.6). This could be attributed to a species effect: in a further comparative study on photosynthetic activity (14CO2 uptake) of four algae species (Ankistrodesmus falcatus, Chlorella vulgaris, Scenedesmus quadricauda, Chlorella pyrenoidosa) it was found that A. falcatus and C. vulgaris are rather tolerant to Cd (EC50 values at 700 and 600 µg L-1 resp.) whereas S. quadricauda or C. pyrenoidosa are sensitive species (EC50 values below 20 and at 100 µg L-1 resp., Wong et al. 1979). Another factor that may explain the high NOEC in this test is the cell density.  Metal toxicity often reduces at higher cell density because an increasing amount of metal becomes immobilised in the algal cell wall. A maximal initial cell density of 10000 cells mL-1 is defined in the OECD-201 algal growth inhibition tests. The initial cell density in the test A. falcatus is about 20 fold above this limit (190000 cells mL-1). Therefore, we chose to define this test as uncreliable. Klass et al. (1974) and Bringmann and Kühn (1980) also illustrate the sensitivity of Scenedesmus quadricauda to Cd. In the study of Klass et al., cell number was reduced to 48 % of control at 6.1 µg L-1. In this static experiment, cell density was rather low (ca. 105 cells/mL) and water hardness also low (25 mg L-1), both factors contributing to high sensitivity. A drawback in the data interpretation of the test results is that average cell number (between 2-16 days after exposure) of the growing population is used as endpoint rather than cell number at one occasion.  Bringmann and Kühn (1980) report a toxicity threshold concentration of Cd to Scenedesmus quadricauda of 31 µg L-1. The effect at that concentration is very low (3 %) and is considered as a NOEC here. Another Scenedesmus species (S. subspicatus) is affected by Cd concentrations around 30 µg L-1 (EC10 values in this case, Kühn and Pattard, 1990).

Toxicity of Cd to Chlorella vulgaris in static tests was reported by Wong et al. (1979), see above, Rosko and Rachlin (1977), Jouany et al. (1983) and Kosakowska et al. (1988). The study of Rosko and Rachlin reports an EC50 value for growth at 60 µg L-1 after 33 days of exposure. Neither pH (which increased from 7.5 to 9.5) nor Cd concentrations were monitored during growth in this static test. In the tests of Jouany et al. (1983) EC50 values for growth are 550-1220 µg L-1. In these tests, cell density was about two orders of magnitude higher than in the test of Rosko and Rachlin (1977). The test systems of Jouany et al. (1983) were either static or pseudodynamic (periodic addition of fresh medium). The Cd toxicity in the latter system was twofold higher (EC50 value twofold lower) than in the static system. In the tests of Kosakowska et al. (1988), the chlorophyll a content of the static system reduced by 77 % compared to control in the presence of 393 µg L-1 Cd, the only concentration tested.

A very high sensitivity to Cd was reported for the diatomic species Asterionella formosa by Conway (1978). The test system was dynamic (continuous culture system, also called chemostat) in which the Cd addition starts when steady state conditions are reached, i.e. when algae growth rate matches the dilution rate. In an artificial medium matching the Lake Michigan composition, Cd reduced growth rate by an order of magnitude when measured steady state Cd concentration reached 2 µg L-1.  Unfortunately, the authors did not include a zero Cd treatment to show that steady state conditions were maintained during a further 9 days after initial steady state conditions. Therefore, these data are not included here. Nevertheless, static studies with the same diatomic species in (almost) the same medium revealed that significant inhibition of growth by 17 % is reached at 4.1 µg L-1 after 24 hours (Conway and Williams, 1979). Another diatomic species, Fragilaria crotonensis, was unaffected by Cd up to 8.5 µg L-1, the highest concentration tested.

The alga Selenastrum capricornutum is used in various standard algae tests (U.S. EPA, 1985, OECD, 1984). The static studies reported by Bartlett et al. (1974), Turbak et al. (1986), Lin et al. (1996), Chen and Lin (1997), Janssen Pharmaceutica (1993e&f) and LISEC (1998a,b) yield EC50 values for that species ranging between 18 and 341 µg L-1.   Lin et al. (1996) indicated that most standard tests have high P concentrations (>0.1 mg L-1) and showed that sensitivity to Cd increases tenfold under P limiting conditions. Chen and Lin (1997) compared Cd toxicity to Selenastrum capricornutum between a continuous system and the U.S. EPA static test. In an artificial medium, the growth rate declined to 50 % of control at 13 µg L-1 in the continuous system within 24 hours. In the static experiment, the EC50 value for growth was 341 µg L-1. The medium composition differed in the concentrations of NaNO3, KH2PO4 and Na2EDTA. The EDTA concentrations in both systems were low enough (below 1 µM) to ensure that almost no Cd is complexed by EDTA. Solution speciation calculation revealed that the difference in EC50 values between static and continuous systems is similar, whether based on total Cd concentration or on free metal (Cd2+) concentration.

Lawrence et al. (1989) used a serial construction of two continuous systems. In the first continuous system, the green alga Chlamydomonas reinhardii was grown and that suspension was pumped into the second where the protozoan Tetrahymena vorax was grown. Once steady state cell numbers were reached in both continuous systems, Cd was added at various concentrations. LOEC’s on cell number after 7 days were 10 µg L-1 and it appeared that the algae were a bit more sensitive to Cd than the protozoa. As a result of reduced grazing, the cell number of algae temporarily increased in the second continuous system at 40 µg L-1 Cd.  Acclimation of the algae to 20 µg L-1 allowed the population to respond less drastically to 40 µg L-1 than increasing Cd from 0 to 40 µg L-1 in one step. It is unclear why the authors deliberately omitted Zn from the artificial solutions. It is likely that in Zn deficient conditions, Cd toxicity will be more pronounced.  In a continuous in situ culture, shifts in populations of phytoplankton were observed upon Cd exposure. At Cd concentrations ranging between 2.9 and 4.2 µg L-1 (measured concentrations, almost all Cd soluble), cell densities of two Dinobryon species were reduced to less than 10 % of control values. The densities of other plankton species (Elakatothrix sp. and Rhabdoderma gorskii) were increased significantly above those in the control systems (DeNoyelles et al., 1980). Since only one concentration was tested above the background, the data of this experiment cannot be used for the current risk assessment.

Varying solution pH between 4.3 and 6.2 marginally affected Cd toxicity to the green alga Coelastrum proboscideum. LOEC values were found at 27 µg L-1 (Müller and Payer, 1979).

Effects of Cd to duckweed (Lemna paucicostata) was assessed in three artificial media at varying pH (Nasu and Kugimoto, 1981). Toxic effects on the number of fronds after 1 week of growth started at 10 µg L-1 Cd and Cd toxicity was generally higher at higher pH.

In conclusion, Cd can affect primary producers in the 1-10 µg L-1 range but no tests showed toxicity below 1 µg L-1. At nutrient limiting conditions and low cell density, species are likely to be most sensitive to Cd. With one exception, all tests were performed in artificial media, some of which had very similar composition as freshwater samples.

Table 3.2.6: toxicity to aquatic primary producers. All underlined data are selected to discuss the critical concentrations (table 3.2.5). Bold data are used to estimate the HC5 (table 3.2.10). Data with reliability index 4 are given as supporting information but they are not used in the effects assessment.

| test substance | organism | medium | test conditions | nominal/ measured | duration (d) | endpoint | NOEC (µg L-1) | Cat.* | LOEC (µg L-1) (%effect) | EC50 (µg L-1) (%effect) | references | RI |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Cd filtrate of dispersion | Selenastrum capricornutum | modified ISO 6341 medium; 0.2 µm filtered; T 20.3-25.6; pH 7.7-10.4 H 49 | static | M | 3 | cell number growth rate | 2.4 9.0 | 1 4 | 5(11) | 23 89 | LISEC, 1998a | 1 1 |
| CdO filtrate of dispersion | Selenastrum capricornutum | modified ISO 6341 medium; 0.2 µm filtered; H 49;pH 7-10 |  | M | 3 | cell number growth rate | 10.9 | 1 | 9.5(37)LT 48(39) | 18 79 | LISEC, 1998b | 1 1 |
| Cd filtrate of dispersion | Selenastrum capricornutum | AM; H 23; pH 7-9 |  | M | 3 | growth rate | 15 | 4 | 60(46) | 70 | Janssen Pharmaceutica, 1993e | 1 |
| CdO filtrate of dispersion | Selenastrum capricornutum | AM H 23; pH 7-8 |  | M | 3 | growth rate | 50 | 1 |  | 120 | Janssen Pharmaceutica, 1993f | 1 |
| CdSO4 | Coelastrum proboscideum | AM;H 32;T 31;pH 5.3; | static | M | 1 | biomass | 6.3 | 1 | 27(36) |  | Müller and Payer 1979 | 2 |
| CdCl2 | Asterionella formosa | AM; pH 8; H 121 | static | M | 1 | growth rate | 0.85 | 2 | 1.9(18)LT |  | Conway and Williams 1979 | 2 |
| CdCl2 | Chlamydomonas reinhardii | AM;H 42;pH 6.7; T 20 | continuous | N | 7 | steady state cell number | 7.5 | 1 | 10(22) |  | Lawrence et al. 1989 | 3 |
| CdCl2 | Scenedesmus subspicatus | AM;H 60;T 24; pH 8 | static | N | 3 | biomass growth rate (0-3d) |  |  |  | 62 136 | Kühn and Pattard 1990 | 3 3 |
| Cd(NO3)2 | Scenedesmus quadricauda | AM; pH 7 | static; T 27; H 55 | N | 7 | biomass (OD) | 31 | 1 |  |  | Bringmann and Kühn, 1980 | 3 |
| CdCl2 | Lemna paucicostata | AM; T 25 | static; pH > 6; H 120 pH 5.1; H 120 pH 5.1; H 700 | N | 7 | number of fronds | 5 10 10 | 2 3 3 | 10(19) 100(35) 50(20) |  | Nasu and Kugimoto, 1981 | 3 3 3 |
| Cd(NO3)2 | Chlorella vulgaris Scenedesmus quadricauda Chlorella pyrenoidosa | AM; H=34;T=20 AM; H=34;T=20 AM; H=34;T=20 AM; H=34;T=20 | static static static static | N | 1 1 1 1 | 14CO2 uptake |  |  |  | 600(50) 700(50) 20(80)LT 100(50) | Wong et al., 1979 | 3 3 3 3 |
| CdCl2 | Selenastrum capricornutum | AM;H=15;pH=7.1;T=24 | static | N | 4 | biomass |  |  | 50(32)LT |  | Bartlett et al. 1974 | 3 |
| CdCl2 | Selenastrum capricornutum | AM; pH 7.6; H 15; T 24 | continuous static | N | 1 1 | growth rate growth rate |  |  |  | 13 341 | Chen and Lin, 1997 | 3 3 |
| CdCl2 | Selenastrum capricornutum | AM; pH 7.5; H 15;T24; | static | N | 1 | growth rate |  |  |  | 32 | Lin et al., 1996 | 3 |
| CdCl2 | Selenastrum capricornutum | AM;H=15;pH=7.1 | static | N | 14-21 | biomass |  |  |  | 57 | Turbak et al., 1986 | 3 |
| Supporting data |
| CdCl2 | Scenedesmus quadricauda | AM; H 28; T 21-30 | static | N | 2-16 | average cell number | 0.6 | 1 |  | 6.1(52%) | Klass et al., 1974 | 4/3 |
| CdCl2 | Fragilaria crotonensis | AM; pH 8; H 121 | static | M | 1 | growth rate | 8.5HT |  |  |  | Conway and Williams 1979 | 4 |
| Cd(NO3)2 | Ankistrodesmus falcatus | AM; H=34;T=20 | static | N | 6 | cell number | 500 | 3 |  | 1000(60%) | Wong et al., 1979 | 4/3 |
| CdCl2 | Chlorella vulgaris | AM;H=82;T=21 | static | N | 33 | cell number | 0.75 | 3 | 18(28) | 60(50) | Rosko and Rachlin, 1977 | 4/3/3 |
| Cd(NO3)2 | Chlorella vulgaris | AM Lefevre Czarda; T 20 | static pseudo-dynamic | N | 4 4 | biomass (OD) |  |  |  | 1220 550 | Jouany et al., 1983 | 4 4 |
| Cd-salt | Dinobryon bavaricum Dinobryon sertularia Elakatothrix sp Rhabdoderma gorskii | lake water | in situ continuous; epilimnion | M | 12 | cell density cell density |  |  | 3.5(+80%) 3.5(+40%) | 3.5(>90) 3.5(>90) | DeNoyelles F. et al., 1980 | 4 4 4 4 |
| CdCl2 | Chlorella vulgaris Anabaena variabilis | AM;H33;T 28 | static | N | 7 | chlorophyll a content |  |  |  | 393(77)LT 393(79)LT | Kosakowska et al. 1988 | 4 |

T = temperature (°C); H= water hardness (mg CaCO3/L); AM, artificial medium; OD, optical density; *NOEC classification (see section 3.2.0.2)

#### Discussion.

Table 3.2.7 lists all toxicity data of primary producers, aquatic invertebrates and fish/amphibians. This data set contains all individual data (i.e. no species means) that were underlined in Tables 3.2.2, 3.2.4 and 3.2.6.  This selection is based on data quality, i.e. data with RI 1-3 only. The selected data are retrieved from 168 different tests. This selection of results is used in this section to identify the factors that affect Cd toxicity, i.e. type of organism and environmental conditions.

Table 3.2.7: summary of selected Cd toxicity data ((g Cd L-1). All data have RI(3 and are underlined in Tables 3.2.2, 3.2.4 and 3.2.6.

|  | NOEC (chronic tests only) |
| --- | --- |
|  | min | 5th perc. | median | max | n |
| fish/amphibians | 0.47 | 0.86 | 4.2 | 62 | 19 |
| aquat. invertebrates | 0.16 | 0.21 | 2.0 | 11 | 22 |
| primary producers | 0.85 | 1.4 | 6.9 | 31 | 8 |
|  | LOEC (chronic tests only) |
|  | min | 5th perc. | median | max | n |
| fish/amphibians | 0.78 | 1.7 | 11 | 132 | 20 |
| aquat. invertebrates | 0.28 | 0.29 | 1.9 | 25 | 19 |
| primary producers | 1.9 | 3.1 | 18 | 100 | 9 |
|  | E-LCx(50 (chronic tests only) |
|  | min | 5th perc. | median | max | n |
| fish/amphibians | 3.4 | 4.8 | 20 | 650 | 7 |
| aquat. invertebrates | 1 | 1.7 | 5 | 32 | 14 |
| primary producers | 6.1 | 9.9 | 59 | 1000 | 12 |
|  | E-LCx(50 (acute tests only) |
|  | min | 5th perc. | median | max | n |
| fish/amphibians | 0.9 | 2 | 1500 | 40200 | 31 |
| aquat. invertebrates | 7 | 24.5 | 166 | 74000 | 61 |

The summary of selected data from chronic Cd tests reveal that the sensitivity to Cd decreases as:

aquatic invertebrates > fish/amphibians> primary producers.

The LOEC values indicate a considerably lower sensitivity of algae towards Cd than invertebrates or fish/amphibians. However, many of the tests with algae are performed in static (batch) conditions where high LOEC/NOEC values are associated with high cell densities. The much higher sensitivity obtained in the continuous systems (chemostats) indicates that algae may indeed be sensitively affected in the µg L-1 range (Conway, 1978; Chen and Lin, 1997).

The toxic effects of Cd become pronounced above 1 µg L-1. In the selected data set with RI (3, only 6 of the 48 LOEC values and 1 of the 125 E(L)C50 values can be found below 1 (g L-1. Two of these data refer to tests on fish in soft water (<28 mg CaCO3/L). In the data with RI 4, at least three more effect concentrations are found below 1 µg L-1. These data were considered as not reliable, mainly because Cd background concentrations were unknown. Detecting Cd in solution below about 0.5 µg L-1 is intricate with conventional methods (i.e. flameless atomic absorption spectrometry, detection limit ( 0.1µg L-1). The source document of Rombough and Garside (1982) is the only that mentions details on pre-concentration steps. These authors found a LOEC at 0.78 µg L-1, significantly above the background of 0.13 µg L-1. More information should be gathered using more sensitive techniques such as Inductively Coupled Plasma- Mass Spectrometry (ICP-MS detection limits around 0.05 µg L-1) to assess possible toxic effects of Cd in the < 0.5 µg L-1 range. Some authors however stressed that threshold toxic Cd effects may not be found in chronic studies with Cd (Marshall, 1978; Van Leeuwen et al., 1985).

#### The PNECwater.

##### The NOEC data

Different species sensitivity distributions (SSD's) can be calculated for different selections of the data since the NOEC values have attached information such as data quality (the Reliability Index, RI) and properties of the test (species, water characteristics and endpoint). All data with RI = 4 (unreliable) were not included because critical information of the test was lacking.  Statistical properties of the selected NOEC data are given in Table 3.2.8. The selected NOEC data are summarised in table 3.2.9A.

Table 3.2.8: summary of the NOEC values ((g Cd L-1) of chronic tests in the aquatic compartment for various levels of reliability (RI, defined in the introduction of 3.2.1.).

|  | NOEC |
| --- | --- |
|  | min | 5th perc. of NOEC data | median | max | n |
| RI 1-3 | 0.16 | 0.34 | 3.4 | 62 | 49 |
| RI 1-2 | 0.47 | 0.60 | 4.2 | 62 | 21 |
| RI 1 |  |  | 2.4 |  | 1 |

##### Species sensitivity distributions at different levels of data quality

There are enough data from all three trophic levels to calculate the PNECwater by the assessment factor method (AFM) using the lowest assessment factor 10 (TGD, 1996, p. 330). The lowest NOEC value with a RI (3 is 0.16  µg L-1. This would yield a PNECwater = 0.016µg L-1 (table 3.2.10). Rather than making a risk assessment based on one single NOEC value, it is possible to use the statistical extrapolation method (TGD, 1996, p. 469) if enough NOEC data are available. This condition is certainly met in the case of Cd and is preferred over the assessment factor method. The PNECwater, derived with the assessment factor method, is in the range of background concentrations of membrane filtered freshwaters. The Cd toxicity has not been tested in that range. Moreover, Cd concentrations below 0.1-0.2 µg L-1 are difficult to measure with conventional methods (see also section 3.2.1.4.).

To evaluate the toxicity data, the statistical extrapolation method is used (Aldenberg and Slob, 1993). The fifth percentile (HC5), with 50% confidence, of a species sensitivity distribution is calculated using the software package ETX 1.3a (RIVM, Bilthoven, The Netherlands). The HC5 is calculated for 4 different approaches of data selection. The first approach is by using all the data (Table 3.2.9A), without calculation of species geometric mean values. The second method is by calculating 'geometric mean' NOEC values for each species, resulting in one NOEC per species (Table 3.2.9B). The third approach is by calculating 'geometric mean' NOEC's on a case-by-case basis (Table 3.2.9C). At a special workshop, held in January 2001, in the framework of the EU Existing Substances programme, it was agreed that "for comparable data on the same endpoint and species the geometric mean should be used as the input value for the calculation using the SSD. If this is not thought to be possible, perhaps because results that are considered valid, are too variable, then consider grouping and combining the values, e.g. by pH ranges, and using reduced numbers of values. The full data set could also be used if necessary". Geometric mean NOEC's are thus calculated for the same species and the same endpoint, tested in similar media¶. This approach does not result in one NOEC per species. The fourth approach is by selecting the lowest NOEC for each species, resulting in one NOEC per species (Table 3.2.9D).

Table 3.2.9A: selected NOEC data of effects of Cd in freshwater. Data derived from tables 3.2.2, 3.2.4 and 3.2.6 within quality class RI 1-3.

| organism | phylum/class | order | family | medium | H | Nominal/ Measured | Dura tion (d) | endpoint | NOEC (µg L-1) | references | R.I. |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Salmo gairdneri | Chordata | Salmoniformes | Salmonidae | aerated well water; T 10; O2 7.5; pH 8-8.6 | 375-390 | M | 84 | mortality | 12 | Lowe-Jinde and Niimi, 1984 | 2 |
| Salmo gairdneri | Chordata | Salmoniformes | Salmonidae | synthetic water (ISO 1977) ; T 25; pH 8.3 | 100 | N | 50 | median survival time | 4 | Dave et al., 1981 | 3 |
| Oncorhynchus kisutch | Chordata | Salmoniformes | Salmonidae | sand filtered Lake Superior Water; continuous flow; DO 10.3; Al 41; Ac 3; pH 7.6 | 45 | M | 27 | biomass | 1.3 | Eaton et al., 1978 | 2 |
| Salvelinus fontinalis | Chordata | Salmoniformes | Salmonidae | sand filtered Lake Superior Water; continuous flow; DO 10.3; Al 41; Ac 3; pH 7.6 | 45 | M | 126 | biomass | 1.1 | Eaton et al., 1978 | 2 |
| Salvelinus fontinalis | Chordata | Salmoniformes | Salmonidae | sterilised Lake Superior water; pH 7-8; Al 38-46; Ac 1-10; DO 4-12; T 9-15 | 42-47 | M | 3 years | total weight of young /female of the 2nd generation | 0.9 | Benoit et al, 1976 | 2 |
| Salvelinus fontinalis | Chordata | Salmoniformes | Salmonidae | reconstituted soft water: T 14-16°C; DO 9.3-11.4 mg/L; Cd(BG) <0.2 µg/L; pH 6.3-7.6; H 20 | 20 | M | 10 | survival | 8 | Jop et al., 1995 | 2 |
| Salvelinus fontinalis | Chordata | Salmoniformes | Salmonidae | river water: T 14-16°C; DO 8.7-12.2 mg/L; Cd(BG) <4 µg/L; pH 6.6-7.4; H 16-28 | 16-28 | M | 10 | survival | 62 | Jop et al., 1995 | 2 |
| Salmo salar | Chordata | Salmoniformes | Salmonidae | municipal water charcoal filtered and UV sterilised; BC 0.13 µg Cd/L; pH 6.5-7.3; T 5-10; DO 11.1-12.5; Al 14-17 | 19-28 | M | 46 | total biomass | 0.47 | Rombough and Garside, 1982 | 2 |
| Catostomus commersoni Esox lucius Salvelinus namaycush Salmo trutta (late eyed eggs) | Chordata Chordata Chordata Chordata | Cypriniformes Esociformes Salmoniformes Salmoniformes | Catostomidae Esocidae Salmonidae Salmonidae | sand filtered Lake Superior Water; continuous flow; DO 10.3; Al 41; Ac 3; pH 7.6 | 45 | M | 30 28 31 61 | standing crop (biomass) biomass | 4.2 4.2 4.4 1.1 | Eaton et al., 1978 | 2 2 2 2 |
| Jordanella floridae | Chordata | Cyprinodontiformes | Cyprinodontidae | untreated Lake Superior water; T 25; DO 8.3; Al 42; Ac 2.4; pH 7.1-7.8 | 44 | M | 100 | reproduction | 4.1 | Spehar, 1976 | 2 |
| Brachydanio rerio | Chordata | Cypriniformes | Cyprinidae | synthetic water (changed ISO) ; T 24; DO >80%; pH 7.2 | 100 | N | 36 | reproduction | 1 | Bresch ., 1982 | 3 |
| Oryzias latipes | Chordata | Beloniformes | Adrianichthyidae | tap water; continuous flow; T 20 | 200 100 | M | 18 | mortality and abn. behaviour | 6 3 | Canton and Slooff, 1982 | 3 |
| Xenopus laevis | Chordata | Anura | Pipidae | tap water; continuous flow; T 20 | 170 |  | 100 | inhibition of larvae development | 9 |  | 3 |
| Pimephaless promelas | Chordata | Cypriniformes | Cyprinidae | pond water diluted with carbon filtered demineralised tap water; DO 6.5-6.6; pH 7.6-7.7; Al 145-161; Ac 8-12; T 16-27 | 201-204 | M | 60 60 | reproduction (pond fish) reproduction (laboratory fry) | 13 14 | Pickering and Gast, 1972 | 3 3 |
| Daphnia magna | Arthropoda | Cladocera | Daphnidae | 50 µm filtered and sterilised Lake IJssel water; pH 8.1; T 20; H 224 | 224 | N | 21 | intrinsic rate of natural increase | 3.2 | Van Leeuwen et al., 1985 | 3 |
| Daphnia magna | Arthropoda | Cladocera | Daphnidae | NPR synthetic water; pH 8.4; T 20 | 200 | N | 21 | mortality | 1 | Van Leeuwen et al., 1985 | 3 |
| Daphnia magna | Arthropoda | Cladocera | Daphnidae | synthetic water; T 25; pH 8; DO 69% | 11 | M | 21 | reproduction | 0.6 | Kühn et al., 1989 | 2 |
| Daphnia magna | Arthropoda | Cladocera | Daphnidae | Synthetic water; Al 65; T 25 | 90 | N | 7 | reproduction | 2 | Winner, 1988 | 3 |
| Daphnia magna | Arthropoda | Cladocera | Daphnidae | well water: T 20(2°C; DO 4.9-7.9; Cd(BG) 0.08; pH 7.9 | 103 | M | 21 | reproduction | 0.16 | Chapman et al., 1980 | 3 |
| Daphnia magna | Arthropoda | Cladocera | Daphnidae | well water: T 20(2°C; DO 4.9-7.9; Cd(BG) 0.08; pH 8.2 | 209 | M | 21 | reproduction | 0.21 | Chapman et al., 1980 | 3 |
| Daphnia magna | Arthropoda | Cladocera | Daphnidae | unchlorinated, carbon filtered well water, aerated to saturation; Al 230; pH 8; DO >5; T 23; Cd < 0.01 µg Cd/L | 240 | N | 14 | reproductive impairment | 2.5 | Elnabarawy et al., 1986 | 3 |
| Daphnia magna | Arthropoda | Cladocera | Daphnidae | aerated well water; DO >70%; pH 8; T 22; Al 250 | 300 | M | 21 | reproduction | 0.8 | Knowles and McKee, 1987 | 2 |
| Daphnia magna | Arthropoda | Cladocera | Daphnidae | culture medium; pH8.4; T 20 | 150 | N | 25 | biomass production/female | 2.5 | Bodar et al., 1988a | 3 |
| Daphnia magna | Arthropoda | Cladocera | Daphnidae | 20 µm cloth filtered Lake Superior water; pH 7.7; Al 42.3; DO 9; T 18 | 45.3 | N | 21 | weight/animal | 1 | Biesinger and Christensen, 1972 | 3 |
| Daphnia pulex | Arthropoda | Cladocera | Daphnidae | Whatman N° 1 filtered Lake Champlain water; pH 7.7; Al 42.4; Cd < 1µg L-1 | 65 | N | 104 | longevity | 1 | Bertram and Hart, 1979 | 3 |
| Daphnia pulex | Arthropoda | Cladocera | Daphnidae | unchlorinated, carbon filtered well water, aerated to saturation; Al 230; pH 8; DO >5; T 23; Cd < 0.01 µg Cd/L | 240 | N | 14 | reproductive impairment | 7.5 | Elnabarawy et al., 1986 | 3 |
| Aplexa hypnorum: immature | Mollusca | Basommotophora | Physidae | Lake Superior water; DO 7.5; T 24 |  | M | 26 | growth | 4.41 | Holcombe et al., 1984 | 2 |
| Physa integra | Mollusca | Basommotophora | Physidae | untreated Lake Superior water; pH 7.1-7.7; T 15; DO 10-11; Al 40-44; Ac 1.9-3 | 44-48 | M | 21 | mortality | 8.3 | Spehar et al., 1978 | 2 |
| Daphnia galeata mendotae | Arthropoda | Cladocera | Daphnidae | 10 µm filtered Lake Michigan water; T 18.5 | 120 | N | 154 | number of individuals | 2 | Marshall, 1978 | 3 |
| Ceriodaphnia reticulata | Arthropoda | Cladocera | Daphnidae | unfiltered river water; static; Ac 2-4.2; Al 41-65; pH 7.2-7.8 | 55-79 | M | 9 | reproduction | 3.4 | Spehar and Carlson, 1984 | 3 |
| Ceriodaphnia reticulata | Arthropoda | Cladocera | Daphnidae | unchlorinated, carbon filtered well water, aerated to saturation; Al 230; pH 8; DO >5; T 23; Cd < 0.01 µg/L | 240 | N | 7 | reproductive impairment | 0.25 | Elnabarawy et al., 1986 | 3 |
| Ceriodaphnia dubia | Arthropoda | Cladocera | Daphnidae | Synthetic water; Al 65; T 25 | 90 | N | 7 | mortality | 1.5 | Winner, 1988 | 3 |
| Ceriodaphnia dubia | Arthropoda | Cladocera | Daphnidae | reconstituted soft water: T 14-16°C; DO 9.3-11.4 mg/L; Cd(BG) <0.2 µg/L; pH 6.3-7.6; H 20 | 20 | M | 7 | reproduction | 10 | Jop et al., 1995 | 2 |
| Ceriodaphnia dubia | Arthropoda | Cladocera | Daphnidae | river water: T 14-16°C; DO 8.7-12.2 mg/L; Cd(BG) <4 µg/L; pH 6.6-7.4; H 16-28 | 16-28 | M | 7 | reproduction | 11 | Jop et al., 1995 | 2 |
| Hyalella azteca | Arthropoda | Amphipoda | Hyalellidae | well water: T 23; pH 7.8 | 280 | M | 42 | Survival | 0.51 | Ingersoll and Kemble, 2000 | 3 |
| Chironomus tentans | Arthropoda | Diptera | Chironomidae | well water: T 23; pH 7.8 | 280 | M | 20 | weight | 5.8 | Ingersoll and Kemble, 2000 | 3 |
| Selenastrum capricornutum | Chlorophyceae | Chlorococcales | Scenedesmaceae | modified ISO 6341 medium; 0.2 µm filtered; T 20.3-25.6; pH 7.7-10.4 | 49 | M | 3 | cell number | 2.4 | LISEC, 1998a | 1 |
| Coelastrum proboscideum | Chlorophyceae | Chlorococcales | Coelastraceae | AM;T 31;pH 5.3; | 32 | M | 1 | biomass | 6.3 | Müller and Payer 1979 | 2 |
| Asterionella formosa | Bacillariophyceae | Pennales | Diatomaceae | AM; pH 8 | 121 | M | 1 | growth rate | 0.85 | Conway and Williams 1979 | 2 |
| Chlamydomonas reinhardii | Chlorophyceae | Volvocales | Chlamydomonaceae | AM; pH 6.7; T 20 | 42 | N | 7 | steady state cell number | 7.5 | Lawrence et al. 1989 | 3 |
| Scenedesmus quadricauda | Chlorophyceae | Chlorococcales | Scenedesmaceae | AM; pH 7 |  | N | 7 | biomass (OD) | 31 | Bringmann and Kühn, 1980 | 3 |
| Lemna paucicostata | Liliopsida | Arales | Lemnaceae | AM; T 25 pH>6 pH 5.1 pH 5.1 | 120 120 700 | N | 7 | number of fronds | 5 10 10 | Nasu and Kugimoto, 1981 | 3 3 3 |

T = temperature (°C); H = hardness (as mg CaCO3/L); DO = dissolved oxygen (mg O2/L); Al = alkalinity (mg CaCO3/L); Ac = acidity (mg CaCO3/L); AM, artificial medium.

Table 3.2.9B: 'One species, one NOEC': selected NOEC data of effects of Cd in freshwater and calculation of 'geometric mean NOEC's. Data derived from table 3.2.9A.

| organism | phylum/class | order | family | NOEC (µg L-1) |  |
| --- | --- | --- | --- | --- | --- |
| Salmo gairdneri | Chordata | Salmoniformes | Salmonidae | 6.9 | geometric mean of 4 and 12 |
| Oncorhynchus kisutch | Chordata | Salmoniformes | Salmonidae | 1.3 |  |
| Salvelinus fontinalis | Chordata | Salmoniformes | Salmonidae | 4.7 | geometric mean of 0.9, 1.1, 8 and 62 |
| Salmo salar | Chordata | Salmoniformes | Salmonidae | 0.47 |  |
| Catostomus commersoni Esox lucius Salvelinus namaycush Salmo trutta (late eyed eggs) | Chordata Chordata Chordata Chordata | Cypriniformes Esociformes Salmoniformes Salmoniformes | Catostomidae Esocidae Salmonidae Salmonidae | 4.2 4.2 4.4 1.1 |  |
| Jordanella floridae | Chordata | Cyprinodontiformes | Cyprinodontidae | 4.1 |  |
| Brachydanio rerio | Chordata | Cypriniformes | Cyprinidae | 1 |  |
| Oryzias latipes | Chordata | Beloniformes | Adrianichthyidae | 4.2 | geometric mean of 3 and 6 |
| Xenopus laevis | Chordata | Anura | Pipidae | 9 |  |
| Pimephaless promelas | Chordata | Cypriniformes | Cyprinidae | 13.5 | geometric mean of 13 and 14 |
| Daphnia magna | Arthropoda | Cladocera | Daphnidae | 1.0 | geometric mean of 0.16, 0.21, 0.6, 0.8, 1, 1, 2, 2.5, 2.5 and 3.2 |
| Daphnia pulex | Arthropoda | Cladocera | Daphnidae | 2.7 | geometric mean of 1 and 7.5 |
| Aplexa hypnorum: immature | Mollusca | Basommotophora | Physidae | 4.41 |  |
| Physa integra | Mollusca | Basommotophora | Physidae | 8.3 |  |
| Daphnia galeata mendotae | Arthropoda | Cladocera | Daphnidae | 2 |  |
| Ceriodaphnia reticulata | Arthropoda | Cladocera | Daphnidae | 0.9 | geometric mean of 0.25 and 3.4 |
| Ceriodaphnia dubia | Arthropoda | Cladocera | Daphnidae | 5.5 | geometric mean of 1.5, 10 and 11 |
| Hyalella azteca | Arthropoda | Amphipoda | Hyalellidae | 0.51 |  |
| Chironomus tentans | Arthropoda | Diptera | Chironomidae | 5.8 |  |
| Selenastrum capricornutum | Chlorophyceae | Chlorococcales | Scenedesmaceae | 2.4 |  |
| Coelastrum proboscideum | Chlorophyceae | Chlorococcales | Coelastraceae | 6.3 |  |
| Asterionella formosa | Bacillariophyceae | Pennales | Diatomaceae | 0.85 |  |
| Chlamydomonas reinhardii | Chlorophyceae | Volvocales | Chlamydomonaceae | 7.5 |  |
| Scenedesmus quadricauda | Chlorophyceae | Chlorococcales | Scenedesmaceae | 31 |  |
| Lemna paucicostata | Liliopsida | Arales | Lemnaceae | 7.9 | geometric mean of 5, 10 and 10 |

Table 3.2.9C: 'Case-by-case selection': selected NOEC data of effects of Cd in freshwater and case-by-case calculation of 'geometric mean NOEC's. Bold, underlined data are selected for the HC5 calculation. Data derived from table 3.2.9A.

| organism | medium | H | endpoint | NOEC (µg L-1) |  | references |
| --- | --- | --- | --- | --- | --- | --- |
| Salmo gairdneri | aerated well water; T 10; O2 7.5; pH 8-8.6 | 375-390 | mortality | 12 | S. gairdneri: no geometric mean calculation: different test medium | Lowe-Jinde and Niimi, 1984 |
| Salmo gairdneri | synthetic water (ISO 1977) ; T 25; pH 8.3 | 100 | median survival time | 4 |  | Dave et al., 1981 |
| Oncorhynchus kisutch | sand filtered Lake Superior Water; continuous flow; DO 10.3; Al 41; Ac 3; pH 7.6 | 45 | biomass | 1.3 |  | Eaton et al., 1978 |
| Salvelinus fontinalis | sand filtered Lake Superior Water; continuous flow; DO 10.3; Al 41; Ac 3; pH 7.6 | 45 | biomass | 1.1 | S. fontinalis: geometric mean calculation: same test medium, same endpoint (biomass) | Eaton et al., 1978 |
| Salvelinus fontinalis | sterilised Lake Superior water; pH 7-8; Al 38-46; Ac 1-10; DO 4-12; T 9-15 | 42-47 | total weight of young /female of the 2nd generation | 0.9 | geometric mean = 1.0 | Benoit et al, 1976 |
| Salvelinus fontinalis | reconstituted soft water: T 14-16°C; DO 9.3-11.4 mg/L; Cd(BG) <0.2 µg/L; pH 6.3-7.6; H 20 | 20 | survival | 8 | S. fontinalis: geometric mean calculation: similar test medium, same endpoint (survival) | Jop et al., 1995 |
| Salvelinus fontinalis | river water: T 14-16°C; DO 8.7-12.2 mg/L; Cd(BG) <4 µg/L; pH 6.6-7.4; H 16-28 | 16-28 | survival | 62 | geometric mean = 22 | Jop et al., 1995 |
| Salmo salar | municipal water charcoal filtered and UV sterilised; BC 0.13 µg Cd/L; pH 6.5-7.3; T 5-10; DO 11.1-12.5; Al 14-17 | 19-28 | total biomass | 0.47 |  | Rombough and Garside, 1982 |
| Catostomus commersoni Esox lucius Salvelinus namaycush Salmo trutta (late eyed eggs) | sand filtered Lake Superior Water; continuous flow; DO 10.3; Al 41; Ac 3; pH 7.6 | 45 | standing crop (biomass) biomass | 4.2 4.2 4.4 1.1 |  | Eaton et al., 1978 |
| Jordanella floridae | untreated Lake Superior water; T 25; DO 8.3; Al 42; Ac 2.4; pH 7.1-7.8 | 44 | reproduction | 4.1 |  | Spehar, 1976 |
| Brachydanio rerio | synthetic water (changed ISO) ; T 24; DO >80%; pH 7.2 | 100 | reproduction | 1 |  | Bresch ., 1982 |
| Oryzias latipes | tap water; continuous flow; T 20 | 200 100 | mortality and abn. behaviour | 6 3 | O. latipes: no geometric mean calculation: different test medium | Canton and Slooff, 1982 |
| Xenopus laevis | tap water; continuous flow; T 20 | 170 | inhibition of larvae development | 9 |  | Canton and Slooff, 1982 |
| Pimephaless promelas | pond water diluted with carbon filtered demineralised tap water; DO 6.5-6.6; pH 7.6-7.7; Al 145-161; Ac 8-12; T 16-27 | 201-204 | reproduction (pond fish) reproduction (laboratory fry) | 13 14 | P. promelas: geometric mean calculation: same test medium, same endpoint (reproduction) geometric mean = 13.5 | Pickering and Gast, 1972 |
| Daphnia magna | 50 µm filtered and sterilised Lake IJssel water; pH 8.1; T 20; H 224 | 224 | intrinsic rate of natural increase | 3.2 | D. magna: no geometric mean calculation: different endpoints | Van Leeuwen et al., 1985 |
| Daphnia magna | NPR synthetic water; pH 8.4; T 20 | 200 | mortality | 1 |  | Van Leeuwen et al., 1985 |
| Daphnia magna | synthetic water; T 25; pH 8; DO 69% | 11 | reproduction | 0.6 | D. magna: no geometric mean calculation: different medium | Kühn et al., 1989 |
| Daphnia magna | Synthetic water; Al 65; T 25 | 90 | reproduction | 2 | D. magna: geometric mean calculation: similar medium, same endpoint (reproduction) | Winner, 1988 |
| Daphnia magna | well water: T 20(2°C; DO 4.9-7.9; Cd(BG) 0.08; pH 7.9 | 103 | reproduction | 0.16 | geometric mean = 0.6 | Chapman et al., 1980 |
| Daphnia magna | well water: T 20(2°C; DO 4.9-7.9; Cd(BG) 0.08; pH 8.2 | 209 | reproduction | 0.21 | D. magna: no geometric mean calculation: different medium | Chapman et al., 1980t |
| Daphnia magna | unchlorinated, carbon filtered well water, aerated to saturation; Al 230; pH 8; DO >5; T 23; Cd < 0.01 µg Cd/L | 240 | reproductive impairment | 2.5 |  | Elnabarawy et al., 1986 |
| Daphnia magna | aerated well water; DO >70%; pH 8; T 22; Al 250 | 300 | reproduction | 0.8 |  | Knowles and McKee, 1987 |
| Daphnia magna | culture medium; pH8.4; T 20 | 150 | biomass production/female | 2.5 | D. magna: no geometric mean calculation: different medium | Bodar et al., 1988a |
| Daphnia magna | 20 µm cloth filtered Lake Superior water; pH 7.7; Al 42.3; DO 9; T 18 | 45.3 | weight/animal | 1 |  | Biesinger and Christensen, 1972 |
| Daphnia pulex | Whatman N° 1 filtered Lake Champlain water; pH 7.7; Al 42.4; Cd < 1µg L-1 | 65 | longevity | 1 | D. pulex: no geometric mean calculation: different medium | Bertram and Hart, 1979 |
| Daphnia pulex | unchlorinated, carbon filtered well water, aerated to saturation; Al 230; pH 8; DO >5; T 23; Cd < 0.01 µg Cd/L | 240 | reproductive impairment | 7.5 |  | Elnabarawy et al., 1986 |
| Aplexa hypnorum: immature | Lake Superior water; DO 7.5; T 24 |  | growth | 4.41 |  | Holcombe et al., 1984 |
| Physa integra | untreated Lake Superior water; pH 7.1-7.7; T 15; DO 10-11; Al 40-44; Ac 1.9-3 | 44-48 | mortality | 8.3 |  | Spehar et al., 1978 |
| Daphnia galeata mendotae | 10 µm filtered Lake Michigan water; T 18.5 | 120 | number of individuals | 2 |  | Marshall, 1978 |
| Ceriodaphnia reticulata | unfiltered river water; static; Ac 2-4.2; Al 41-65; pH 7.2-7.8 | 55-79 | reproduction | 3.4 | C. reticulata: no geometric mean calculation: different medium | Spehar and Carlson, 1984 |
| Ceriodaphnia reticulata | unchlorinated, carbon filtered well water, aerated to saturation; Al 230; pH 8; DO >5; T 23; Cd < 0.01 µg/L | 240 | reproductive impairment | 0.25 |  | Elnabarawy et al., 1986 |
| Ceriodaphnia dubia | Synthetic water; Al 65; T 25 | 90 | mortality | 1.5 | C. dubia: no geometric mean calculation: different medium, different endpoint | Winner, 1988 |
| Ceriodaphnia dubia | reconstituted soft water: T 14-16°C; DO 9.3-11.4 mg/L; Cd(BG) <0.2 µg/L; pH 6.3-7.6; H 20 | 20 | reproduction | 10 | C. dubia: geometric mean calculation: similar medium, same endpoint (reproduction) | Jop et al., 1995 |
| Ceriodaphnia dubia | river water: T 14-16°C; DO 8.7-12.2 mg/L; Cd(BG) <4 µg/L; pH 6.6-7.4; H 16-28 | 16-28 | reproduction | 11 | geometric mean = 10.5 | Jop et al., 1995 |
| Hyalella azteca | well water: T 23; pH 7.8 | 280 | Survival | 0.51 |  | Ingersoll and Kemble, 2000 |
| Chironomus tentans | well water: T 23; pH 7.8 | 280 | weight | 5.8 |  | Ingersoll and Kemble, 2000 |
| Selenastrum capricornutum | modified ISO 6341 medium; 0.2 µm filtered; T 20.3-25.6; pH 7.7-10.4 | 49 | cell number | 2.4 |  | LISEC, 1998a |
| Coelastrum proboscideum | AM;T 31;pH 5.3; | 32 | biomass | 6.3 |  | Müller and Payer 1979 |
| Asterionella formosa | AM; pH 8 | 121 | growth rate | 0.85 |  | Conway and Williams 1979 |
| Chlamydomonas reinhardii | AM; pH 6.7; T 20 | 42 | steady state cell number | 7.5 |  | Lawrence et al. 1989 |
| Scenedesmus quadricauda | AM; pH 7 |  | biomass (OD) | 31 |  | Bringmann and Kühn, 1980 |
| Lemna paucicostata | AM; T 25 pH>6 pH 5.1 pH 5.1 | 120 120 700 | number of fronds | 5 10 10 | L. paucicostata: no geometric mean calculation: different medium | Nasu and Kugimoto, 1981 |

T = temperature (°C); H = hardness (as mg CaCO3/L); DO = dissolved oxygen (mg O2/L); Al = alkalinity (mg CaCO3/L); Ac = acidity (mg CaCO3/L); AM, artificial medium.

Table 3.2.9D: 'One species, one NOEC': lowest NOEC selection. Data derived from Table 3.2.9A.

| organism | phylum/class | order | family | NOEC (µg L-1) |
| --- | --- | --- | --- | --- |
| Salmo gairdneri | Chordata | Salmoniformes | Salmonidae | 4 |
| Oncorhynchus kisutch | Chordata | Salmoniformes | Salmonidae | 1.3 |
| Salvelinus fontinalis | Chordata | Salmoniformes | Salmonidae | 0.9 |
| Salmo salar | Chordata | Salmoniformes | Salmonidae | 0.47 |
| Catostomus commersoni Esox lucius Salvelinus namaycush Salmo trutta (late eyed eggs) | Chordata Chordata Chordata Chordata | Cypriniformes Esociformes Salmoniformes Salmoniformes | Catostomidae Esocidae Salmonidae Salmonidae | 4.2 4.2 4.4 1.1 |
| Jordanella floridae | Chordata | Cyprinodontiformes | Cyprinodontidae | 4.1 |
| Brachydanio rerio | Chordata | Cypriniformes | Cyprinidae | 1 |
| Oryzias latipes | Chordata | Beloniformes | Adrianichthyidae | 3 |
| Xenopus laevis | Chordata | Anura | Pipidae | 9 |
| Pimephaless promelas | Chordata | Cypriniformes | Cyprinidae | 13 |
| Daphnia magna | Arthropoda | Cladocera | Daphnidae | 0.16 |
| Daphnia pulex | Arthropoda | Cladocera | Daphnidae | 1 |
| Aplexa hypnorum: immature | Mollusca | Basommotophora | Physidae | 4.41 |
| Physa integra | Mollusca | Basommotophora | Physidae | 8.3 |
| Daphnia galeata mendotae | Arthropoda | Cladocera | Daphnidae | 2 |
| Ceriodaphnia reticulata | Arthropoda | Cladocera | Daphnidae | 0.25 |
| Ceriodaphnia dubia | Arthropoda | Cladocera | Daphnidae | 1.5 |
| Hyalella azteca | Arthropoda | Amphipoda | Hyalellidae | 0.51 |
| Chironomus tentans | Arthropoda | Diptera | Chironomidae | 5.8 |
| Selenastrum capricornutum | Chlorophyceae | Chlorococcales | Scenedesmaceae | 2.4 |
| Coelastrum proboscideum | Chlorophyceae | Chlorococcales | Coelastraceae | 6.3 |
| Asterionella formosa | Bacillariophyceae | Pennales | Diatomaceae | 0.85 |
| Chlamydomonas reinhardii | Chlorophyceae | Volvocales | Chlamydomonaceae | 7.5 |
| Scenedesmus quadricauda | Chlorophyceae | Chlorococcales | Scenedesmaceae | 31 |
| Lemna paucicostata | Liliopsida | Arales | Lemnaceae | 5 |

The statistical extrapolation method (SEM, Aldenberg and Slob, 1993) was applied to the NOEC data (some grouped per species, see previous section), calculating the median 5th percentile (HC5) of both the log-logistic and the log-normal distribution with the software package ETX 1.3a RIVM, Bilthoven, The Netherlands) (table 3.2.10).

Table 3.2.10: calculation of critical concentrations ((g L-1) using the assessment factor method (AFM) or the statistical extrapolation method (SEM, Aldenberg and Slob, 1993) for various levels of data quality.

| data quality group | AFM: NOEC/AF (g Cd L-1 |
| --- | --- |
|  | AF=10 |
| RI 1-3 | 0.016 |
| RI 1-2 | 0.047 |
|  | SEM: HC5 at 50% (and 95%) confidence (g Cd L-1 |
|  | logistic distribution | normal distribution |
| Selection of all data, RI 1-2 (Table 3.2.9A); n = 21 | 0.39 (0.15) | 0.40 (0.16) |
| Selection of all data, RI 1-3 (Table 3.2.9A); n = 49 | 0.35 (0.19) | 0.34 (0.20) |
| One species, ’ne value: geometric mean NOEC's (Table 3.2.9B); n = 28 | 0.59 (0.30) | 0.59 (0.32) |
| Case-by-case geometric mean calculation (Table 3.2.9C); n = 44 | 0.38 (0.21) | 0.38 (0.22) |
| One species, one value: lowest NOEC selection (Table 3.2.9D); n = 28 | 0.31 (0.14) | 0.31 (0.15) |

Selection on data quality does affect the value of HC5 between groups RI 1-3 and RI 1-2. The NOEC data with RI 1-3 yield a smaller HC5 than those with RI 1-2. The group with RI 1-2 has obviously a higher quality label than the group RI 1-3. The latter group of data is, on the other hand, derived based on 28 species whereas the former is derived on 16 species (Table 3.2.9).  Many test results are classified as RI 3 mainly because the source document did not give statistical data analysis or because only nominal concentrations were given.  These tests are still considered to be reliable (no critical information is missing).  The choice between these two data groups is therefore a trade off between complete background information on tests with fewer species or more species with less complete background information.  The latter is preferred here because the statistical extrapolation is based on the modelling of the species sensitivity distribution.

The choice of SSD (log-logistic or log-normal) does not affect the HC5 (table 3.2.10). The choice of data selection (geometric mean calculation or not, lowest NOEC selection or not) influences the HC5 by a factor two. The lowest HC5 (0.31 µg L-1) is calculated when only the lowest NOEC value is selected for each species. The highest HC5 (0.59 µg L-1) is calculated when the geometric mean NOEC is calculated for each species. The main drawback of both approaches is that they reduce information from the database. The lowest NOEC values are often found at low water hardness, in synthetic water or carbon filtered water. Selecting only these values creates a bias in the database which should be avoided for a generic risk assessment. However, hardness correction of the data may be used to set standards that vary by region (section 3.2.1.6.4). Selecting a geometric mean NOEC for each species may not protective for that species in all conditions. As an example, the geometric mean NOEC of D. magna is 1 µg Cd L-1 whereas several LOEC’s of that species have been detected below 1 µg Cd L-1 (see Table 3.2.4). The alternatives for data selection are therefore using all RI 1-3 data or data of RI 1-3 with case-by-case averaging Some species might be overrepresented compared to others when all data are selected to calculate the HC5. This is partly overcome by calculating geometric mean NOEC values on a ’case-by-case basis, where NOEC's are only averaged for the same species tested on the same endpoint in the same or a similar medium.  As a trade-off between the last 2 alternatives, we propose to use the HC5 of the largest group (RI 1-3), calculated based on case-by-case selected (geometric mean) NOEC values, i.e.

# HC5 = 0.38 (g L-1

# The frequency distribution and HC5 are illustrated in Fig. 3.2.1.

Fig. 3.2.1: the cumulative frequency distribution of the NOEC values of Cd toxicity tests of data quality group and RI 1-3 used to calculate the HC5 (case-by-case geometric mean calculation; n = 44). Selected data and logistic distribution curve fitted on the data.

Fig. 3.2.2 gives the cumulative number of the LOEC values of data quality group RI 1-3. LOEC values are found at higher Cd concentrations than NOEC ’alues (not shown). Three LOEC's are found below the HC5.  Yield of a Daphnia population was reduced by 36 % at 0.3 µg L-1 (measured concentration) after 21 days exposure in Lake IJssel water (Van Leeuwen et al., 1985).  There was no statistical evaluation of the data and no NOEC value could be derived from that test (the LOEC was found at the lowest concentration tested). Furthermore, reproduction Daphnia magna was also significantly affected at 0.28 an 0.29 µg L-1 in well water at a hardness of 53 and 103 mg CaCO3 L-1 (Chapman et al., 1980).

A small number of other chronic tests has also demonstrated Cd toxicity at solution Cd concentrations below 0.5 (g Cd L-1 (e.g. Biesinger and Christensen, 1972; Sjöbeck et al, 1984,). These data are less reliable as discussed in the sections 3.2.1.2 and 3.2.1.3. Nevertheless, this review of toxicity data indicates that a toxicity threshold Cd concentration in freshwater, if detectable, may be very close to background Cd concentrations (typically 0.05-0.2 (g Cd L-1 in filtered freshwater). The number of ecological processes affected in the 0.1-0.5 (g Cd L-1 is, however, small as indicated by the LOEC frequency distribution.

The  HC5 is likely not overestimated due to speciation of Cd in the test media that would reduce Cd toxicity in the tests. One NOEC value of 0.8 µg L-1 was found in unfiltered well water (Knowles and McKee, 1987). All other data (both NOEC or effect data) at concentrations below 1 µg L-1 were found in either synthetic media or in filtered environmental samples.  Therefore, almost no Cd in these solutions has reduced availability due to sorption on suspended solids.  This again justifies the use of filtered solutions in risk assessment of Cd in aquatic systems (see exposure section).

Fig. 3.2.2: the cumulative number of LOEC values of selected tests of data quality group RI 1-3.

##### Calculation of the generic PNECwater

The EU workshop on statistical extrapolation (17-18 January, 2001) proposed that the statistical extrapolation technique can be applied to derive a PNEC, but that an additional assessment factor should be applied to the HC5.  In order to derive a PNEC, this extra assessment factor should be between 5 and 1,  to be judged on a case by case basis, and should remove uncertainty in extrapolating the PNEC to the field situation.

The data on which the HC5 i’ calculated are selected’NOEC's or geometric mean NOEC's, calculated on a case-by-case basis (Table 3.2.9C). The diversity of the data (44 NOEC values from 28 species and 16 different families, including warm and cold water fish, amphibians, crustaceans, algae and higher plants) is large enough to use the statistical extrapolation method to calculate the PNEC. Many of the tests are performed in synthetic water resulting in a lower degree of Cd complexation than in natural conditions.

All NOEC data are derived from real chronic studies. Test durations are between 7 days and 3 years, except for some algae tests, which should cover different life stages. ’he goodness-of-fit of the SSD's is tested with the Kolmogorov-Smirnov test. It indicated that the log-logistic distribution is accepted at the 1-5% and the log-normal distribution at the 1-10% significance levels whe’ applied on the selected NOEC's.

Field data on Cd can hardly be used to derive threshold values for Cd in the environment because of the usual mixed metal pollution where Cd is found at high concentrations.  Microcosm (model) ecosystems offer an alternative way of testing effects of Cd in field conditions.  Results from such multi-species studies should be evaluated regarding their reliability, reproducibility, representativeness and relevance. Furthermore, the evaluation should include consideration of the reported endpoints, species and/or indices, including the statistical power of the test design. Table 3.2.11 gives an overview of the description and results of nine multi-species (MS) studies. Using the US-EPA hardness correction (see next section), the NOEC and LOEC values of these MS studies can be compared to the HC5 of single species NOECs (table 3.2.12). This reveals that the hardness corrected HC5 values are within the range of the reported MS-NOEC values and below the reported MS-LOEC values, with one exception in the study of Marshall and Mellinger, 1980 That study revealed a significant effect on 1 of the 16 species at 0.2 µg/L (nominal concentration, measured concentrations unknown).

Table 3.2.11: overview of multi-species studies about effects of Cd (added as Cd2+salt) in the aquatic environment.

| reference (chronological order) | test system | replicates | Cd conc. range (µg/l, Nominal or Measured) | water chemistry | period | results | conclusion for Multi-Species study (MS) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1. Giesy et al., 1979 | artificial streams: 91.5 long, 0.3 m depth; mean water retention time = 2h; sediment present | 2 for each treatment | 0, 5, 10 (N) 0.02, 4-5, 8-10 (M) | hardness 11 mg/l as CaCO3; pH = 6.5 | 1 year | at 5 and 10 µg Cd/l significant reductions in macrophytes biomass and periphyton; some invertebrate taxa eliminated, while other taxa increased in density chronic toxicity in crayfish and snails | 5 µg/l is a MS-LOEC a MS- NOEC can not be derived (extrapolation factors > 2 are considered not reliable in Cd/CdO RAR) effects of Cd at 5 µg Cd/l in this very soft water is expected from single species studies |
| 2. Marshall and Mellinger, 1980 | closed 8 l carboys at 3-5 m or 6-8 m depth in Lake Michigan | 2 for each treatment | 0, 0.6, 1.2, 2.5, 5.0 (N, exp.1-4) 0, 0.2, 0.4, 0.8, 1.6 (N, exp. 5-6) | hardness 120 mg/l as CaCO3; background Cd <0.1 µg Cd/l | 3 weeks | for 16 species/categories of crustacean plankton sign. increases in density of 4 categ. at 0.6 or 1.2 µg Cd/l sign. decrease in density of 2 species at 0.6 µg Cd/l, one species sign. affected at 0.2 µg Cd/l lowest LOEC for total zooplankton density at 0.8 µg Cd/l- NOEC’s varying with experiments (0.4-2.5 µg Cd/l) LOEC for 1 species at 0.2 µg/L LOEC for percentage similarity (biodiversity index): 1.2 µg/l (exp. 1&2), 0.6 µg/l (lowest tested conc., exp. 3&4)0.4 µg/l (exp. 5&6) | less reliable because no measured Cd concentrations in the critical Cd concentration range (<1 µg Cd/l) MS-NOEC’s of total zooplankton density: 0.4-2.5 µg/l 1 individual species can be sign. affected at Cd = 0.2 µg/l |
| 3. Marshall and Mellinger, 1980 | 10 m diameter open surface enclosures in L 223 of Canada’s experimental lake area (~2m depth) | no | 0, 1, 3, 10, 30 (N) | background Cd <0.1 µg Cd/l; hardness unknown | 44-87 days | reduction in density of most of the 8 species/categories of custacean plankton at lowest Cd concentration tested increased density of 8 species/categories of rotifers at 1 or 3 µg/l LOEC for percentage similarity (biodiversity index) is 1 µg/l (lowest tested) EC1 of percent similarity is extrapolated from L223 and Lake Michigan enclosure data and is predicted 0.12 added Cd (background not included) | unreliable because no measured Cd concentrations, no replicates and no known water characteristics |
| 4. DeNoyelles et al., 1980 | continuous 5 l culture chambers, retention time 92-110 h, incubated at 1.74 m depth in L 239 of Canada’s experimental lake area | 2 for each treatment | 0, 4 (N) unknown and 2.9-4.2 (M) | background Cd unknown; hardness unknown | 188 h | density of 4 phytoplankton species: increased for 2 species and decreased for 2 other species | MS-NOEC is below 2.9-4.2 µg/l if based on most sensitive species less reliable because water hardness unknown |
| 5. DeNoyelles et al., 1980 | 10 m diameter open surface enclosures in L 223 of Canada’s experimental lake area (~2m depth) | no | 0, 1, 3, 10, 30 (N) measured Cd : declined to half of nominal in 2 weeks (no other details available)² | background Cd <0.1 µg Cd/l; hardness unknown | 2 weeks | density of 3 phytoplankton species: increased for 2 species at Cd = 1 and 3 µg/l, decreased for 1 species at lowest Cd rate and above (LOEC = 1 µg/l) | MS-NOEC is below 1 µg/l if based on most sensitive species unreliable because no measured Cd, hardness unknown and no replicates |
| 6. Niederlehner et al., 1985 | colonisation of barren polyurethane foam substrates by protozoan from a species source (collected on foam in a pond) | 2 per treatment | 0, 0.6, 1.3, 2.5, 5, 10 (N) 0.2, 0.4, 1.4, 2.7, 5.6, 9.5 (M) | dechlorinated tap water; hardness 70 mg/l as CaCO3; background Cd 0.2 µg Cd/l | 28 days | NOEC colonisation tests 0.4 µg/l, LOEC=1.4 µg/l (22% inhibition)² | reliable MS-NOEC=0.4 µg/l |
| 7. Borgmann et al. 1989 | 3400 l indoor ecosystems (4 tanks) inoculated with Daphnia magna and phytoplankton | none at 5 and 15 µg/l, 2 at 1µg/l*, 3 at control* | 0, 1, 5, 15 (N) 0.08-0.2, 1, 4.7, 12 (M) | tap water; hardness 130 mg/l as CaCO3; background Cd < 0.3 µg Cd/l; pH 8.2-8.6 | >10 weeks | no effects at 1 µg Cd/l on Daphnia ash free dry weight or chlorophyll concentration collapse of Daphnia population and Increase in Chlorophyll conc. at 5 µg /L both endpoints affected at 15 µg/l | less reliable MS-NOEC of 1 µg/l because no continuous replicates of control and 1 µg Cd/l treatment |
| 8. Lawrence and Holoka, 1991 | continuous 41 l culture chambers, retention time 2 days, incubated at 2 me depth in L 382, 302,204 of Canada’s experimental lake area | 2 per treatment | paired studies: 0, 0.2 (10 exp.) 0, 0.4 (3 exp) 0, 1 (2 exp) 0, 3 (2 exp) | background Cd in L 382 is < 0.002 µg/l, other lakes unknown; hardness less than about 10 mg/l as CaCO3$ DOC < 1.2 mmol/l | 2 weeks | 6 categories of crustacean species calanoid and cyclopoid copepods: NOEC=1.0 µg/l 2 species: NOEC = 0.2 µg Cd/l 2 species (D. galeata mendotae & Holpedium gibberum): LOEC = 0.2 µg/l (lowest tested, 40% and 38% inhibition) | MS-NOEC below 0.2 µg/l if based on most sensitive species less reliable: no measured Cd concentrations in the critical Cd concentration range (<1 µg Cd/l) |
| 9. Malley and Chang, 1991 | lake 382 of Canada’s experimental lake area | no | 0.002 (pre-contamination years 1985-1986); 0.05-0.08 µg Cd/l (experimental years 1987-1988) | hardness less than about 10 mg/l as CaCO3$ DOC<0.7 mmol/l | 2 years | zooplankton community structure: no adverse effects on composition and population abundances | MS-NOEC = 0.08 µg/l, highest tested (less reliable-no replicates and unbounded, authors have indirect evidence for predicting effects at 0.2 µg Cd/l in soft water lakes) |

*control: 1 continuous control, 2 controls for the period before Cd was added; Cd in 4-th unit (designed as 2-nd continuous control) increased in time to 1 µg Cd/l (contamination ascribed to a welding joint); $ The test reports Ca concentrations of about 2.2 mg/L but data on Mg are lacking, i.e. the hardness cannot be calculated unequivocally. The Ca/Mg molar ratio is typically about 3:1 in freshwater, yielding a hardness of about 7 mg CaCO3/L. We have used a larger estimated Mg concentration (Ca/Mg molar ratio of 1), i.e. hardness of about 10 mg/L.

Table 3.2.12: summarising table for multi-species studies (numbers refer to those in table 3.2.11). The water hardness correction is described in section 3.2.1.6.4. The HC5 at the water hardness of the MS study is calculated based on hardness corrected NOEC data and retransformation with a lower hardness limit of H = 40 mg l-1 as CaCO3). The model for the hardness correction is discussed insection 3.2.1.6.4..

| study number | reliability | MS-NOEC (µg L-1) | MS-LOEC (µg L-1) | Hardness (mg L-1) | HC5 at that hardness (µg L-1) |
| --- | --- | --- | --- | --- | --- |
| 1 | reliable | - | 5 | 11 | 0.16 |
| 2 | less reliable | <0.2 (most sensit. species) 0.4-2.5 (crustacean density) | 0.2 (most sensit. species) (0.8 (crustacean density) | 120 | 0.34 |
| 3 | unreliable | <1 (most sensit species) | 1 (most sensit. species) | no data | - |
| 4 | less reliable | <2.9-4.2 | 2.9-4.2 | no data | - |
| 5 | unreliable | <1 | 1 | no data | - |
| 6 | reliable | 0.4 | 1.4 | 70 | 0.23 |
| 7 | less reliable | 1.0 | 5.0 | 130 | 0.37 |
| 8 | less reliable | <0.2 (most sensit. species) | 0.2 (most sensit. species) | (10 | 0.16 |
| 9 | less reliable | 0.08 | - | (10 | 0.16 |

The database of the 168 reliable tests on single species contains 3 reliable LOEC’s below the HC5 whereas the 9 multi species studies identified 1 LOEC below the hardness corrected HC5.  This suggests that NOEC and LOEC distributions overlap in the lower concentration range and that an additional assessment factor may be necessary.  Therefore, we propose to include a  assessment factor of 2 on the HC5, yielding

# PNECwater = HC5/2 = 0.19 (g L-1

One NOEC from the laboratory toxicity tests (RI 1-3) and one NOEC from the multi-species studies are below this PNECwater. No LOEC’s of the reliable single species or multi species studies is found below this PNECwater.  However, this generic PNECwater might not be protective for water with a very low water hardness (see section 3.2.1.6.4).  Finally, we note that the PNECwater derived with the Assessment Factor (AF) method is 4-14-fold below the value proposed above. This is related to the emphasis on the lowest NOEC value (with AF=10) with the AF methodwhereas the Statistcal Extrapolation method uses the weight of evidence.

##### PNECwater as a function of water characteristics

Water characteristics affect Cd toxicity. Toxicity of Cd generally increases with reducing water hardness, reducing concentrations of dissolved organic matter and increasing solution pH.  Effects of dissolved organic matter on Cd toxicity cannot be described using the tests that are reviewed here since most tests did not report this water characteristic.

Toxicity of Cd2+ in solution is lower in more acid conditions because of H+/Cd2+ competition at the membrane (e.g. data on Lemna paucicostata, Nasu and Kugimoto, 1981). Acidification leads to higher Cd emissions from catchments into water, but this is an effect on exposure, not on ecotoxicology of soluble Cd. In the presence of soluble Cd complexes (Cd complexed by dissolved organic matter), the situation is more complex because pH has effects on affinity of Cd2+ for the membrane and for the dissolved organic matter. Data suggesting that the effect of acidification is larger on releasing Cd2+ from soluble complexes than the opposite effect of decreasing Cd2+ affinity for the biota, have not been found. However, John et al. (1987) studied 109Cd uptake (not toxicity) at varying pH and aquatic humus concentrations by Salmo salar in water reconstituted from a small marsh area in Oslo. The 109Cd uptake was lowest at lowest pH at all but one DOC-level (Dissolved Organic Carbon). The pH effect was not significant at that DOC-level. The effects of pH on Cd toxicity were not identified in the selected tests of this report: a regression between the log(ECx(50) and pH showed non-significant effects for both the acute as chronic tests (P>0.05 for both regressions). The absence of effects of pH on Cd toxicity in this report might be due to the bias towards higher pH values (pH >7) of the aqeous media used in the selected tests.

Biotic ligand models (BLM’s) have been developed to account for abiotic factors affecting metal toxicity. This model has been constructed and  successfully validated to explain acute Cd toxicity to fish (fathead minnow and rainbow trout). Data for invertebrates (C. dubia) were not reliable enough to allow validation of a BLM and no BLM for algae was constructed (Hydroqual, 2003).. Most of the data with fish show the importance of hardness on Cd toxicity, while effects of pH are of minor importance at pH >6.2. This BLM model can, however not be used in this document because the modifying factors for acute toxicity are not necessarly identical in chronic exposure and because the model is missing for invertebrates which are, most likely, the most sensitive group.

Considerable regional differences in water hardness of surface waters exist within the EU (Table 3.2.13). Half of the surface waters in the northern European countries have a water hardness below 10 mg CaCO3 L-1, while in the western European countries almost 50% of the surface waters have a hardness above 200 mg CaCO3 L-1. Therefore, a water hardness correction of the PNECwater for risk characterisation at a local or regional scale might be useful.

Table 3.2.13: water hardness (in mg CaCO3 L-1) distribution of surface waters in some EU countries.

|  | 10th percentile | 25th percentile | 50th percentile | 90th percentile |
| --- | --- | --- | --- | --- |
| Finland(a) | 6.5 | 9 | 12 | 25 |
| Sweden(b) | 5 | 8 | 14 | 107 |
| Norway(a) | 0.7 | 1.7 | 4 | 18 |
| Denmark(a) | 14 | 86 | 155 | 272 |
| France | 48 | 83(e) | 217 | 335 |
| Belgium (Flanders)(c) | 109 | - | 240 | 500 |
| G ermany(d) | 30 | 105 | 210 |  |

(a) Source: Skjelkvåle et al. (2001); (b) Source: Swedish University of agriculture; (c) Source: VMM; (d) water hardness of groundwater instead of surface water (Hannappel et al., 2000); (e) 20th percentile

The effect of water hardness (H) on Cd toxicity has been quantified by the US-EPA (US-EPA, 2001). For Daphnia magna, Pimephales promelas and Salmo trutta an increasing trend of chronic values with increasing water hardness was observed (Table 3.2.14). The chronic value is the geometric mean of the NOEC and LOEC value for a given endpoint. To account for the apparent relationship of Cd chronic toxicity to hardness, an analysis of covariance was performed to calculate the pooled slope for hardness using the natural logarithm of the chronic value as the dependent variable, species as the treatment or grouping variable and the natural logarithm of hardness as the covariate or independent variable. This analysis was fit to the data of the 3 species for which chronic values are available over a range of hardness such that the highest hardness is at least 3 times the lowest, and the highest is also 100 mg L-1 higher than the lowest. Regression of the natural logarithm of the chronic value against the natural logarithm of water hardness gave a slope of 0.7712 for D. magna, 1.0034 for P. promelas and 0.5212 for S. trutta. The pooled slope for the three species is 0.7409, with 95% confidence limits of 0.3359 and 1.1459. The slope of 0.7409 was then used to adjust a range of chronic values to a reference hardness of 50 mg CaCO3 L-1 following

(3.2.1)

The water hardness correction covers a hardness range of 44-209 mg CaCO3 L-1.

Table 3.2.14: Chronic values as a function of water hardness as reported by US-EPA (2001).

| Species | hardness (mg L-1 as CaCO3) | Chronic value (µg L-1) |
| --- | --- | --- |
| Daphnia magna | 53 | 0.152 |
| Daphnia magna | 103 | 0.212 |
| Daphnia magna | 209 | 0.437 |
| Salmo trutta | 44 | 6.668 |
| Salmo trutta | 250 | 16.49 |
| Pimephales promelas | 44 | 10.0 |
| Pimephales promelas | 201 | 45.92 |

The effect of water hardness on Cd toxicity can also be observed in the current database.  It has been frequently described in sections 3.2.1.2-3.2.1.4 that water hardness is an important factor influencing Cd toxicity in water.  Lowest LOEC or ECx(50 values are often found in soft waters. The intrinsic variability of NOEC’s across different studies limits the identification of the underlying relationship between hardness and toxicity in a meta-analysis in this report.  Therefore, it is preferred to use the mean slope as used by US-EPA for the water hardness correction.

The water hardness correction equation of the U.S. EPA (US EPA, 2001; see above) is used to calculate the HC5 as a function of water hardness. All NOEC values at hardness H are converted to NOEC values at a reference hardness of 50 mg CaCO3 L-1 (NOECH=50) following

(3.2.2)

Geometric mean values are calculated on the same data as in Table 3.2.9C after normalisation of the data. The software package ETX 1.3a (RIVM, Bilthoven, The Netherlands) is used to calculate the HC5 at the reference hardness of 50 mg CaCO3 L-1,  assuming a log-logistic distribution. This HC5 value is then divided by a assessment factor of 2 to yield a PNECwater, regional that is valid for waters with hardness of 50 mg CaCO3 L-1. The arguments to include a assessment factor 2 to convert a HC5 to PNEC were given in the previous paragraph. Finally, equation 3.2.2 is used again to recalculate the PNECwater,regional at different values of water hardness as

PNECwater,regional = 0.09 (H/50)0.7409						(3.2.3)

It is proposed that this equation is not extrapolated below H = 40 mg CaCO3 L-1, i.e. the PNECwater,regional for H<40 mg CaCO3 L-1 = 0.08 µg Cd L-1. The PNECwater,regional is graphically represented in Fig 3.2.3.

The extrapolation of the hardness correction below H = 40 mg CaCO3 L-1 is not proposed because this equation has not been tested in that hardness range. The PNECwater,regional = 0.08 µg Cd/L should then be evaluated for soft water. It is observed that:

- none of the 37 Cd toxicity tests in the database of the Cd RAR (including data with lower quality) that were performed between H = 7-101 and H=40 mg CaCO3/L have identified adverse effects below the threshold of 0.08 µg Cd/L

- there are 2 multi-species studies (Table 3.2.11) carried out in soft water lakes of Canada and which were designed to study fate and effects of Cd at low concentrations (0.05-0.2 µg Cd/L). The chemical properties of these waters (Ca = 2.2 mg/L, neutral pH, DOC about 8 mg C/L) are similar to that of soft water lakes in Scandinavian countries. The tests allow to conclude that 0.08 µg Cd/L is protective whereas adverse effects are found at about 0.20 µg Cd/L.

- We conclude that down to a water hardness of 7-10 mg CaCO3/l there is no indication of Cd toxicity below 0.08 µg Cd/l.

- There are no data for the very soft waters (H below about 10 mg CaCO3/L) and these areas may be unprotected by the proposed PNECwater for soft water.

Table 3.2.15: the PNECwater,regional ((g L-1) for different values of water hardness (H, mg CaCO3/L). The NOEC data were all first normalised to H=50 from which the HC5 at a reference hardness was found. The PNECwater at that hardness contains a assessment factor of 2.  The normalisation was then used to calculate the PNECwater,regional values at other values of H.

|  | N | min. NOEC | median NOEC | PNECwater |
| --- | --- | --- | --- | --- |
| Data normalised to H 50 (method 2) | 34 | 0.07 |  | 0.09 |
| retransformed PNECwater = 0.09 (H/50)0.7409 |  |  |  |  |
| H 40 |  |  |  | 0.08 |
| H50 |  |  |  | 0.09 |
| H100 |  |  |  | 0.15 |
| H200 |  |  |  | 0.25 |

Fig 3.2.3: NOEC values of the laboratory studies , LOEC of multi-species studies (1 NOEC), water hardness corrected PNECwater and the US-EPA chronic criterion (US-EPA, 2001) as a function of water hardness. The dashed lines indicate the range of water hardness for which the US EPA (2001) hardness correction was derived.

The water hardness correction method yields a PNECwater,regional at H = 50 mg CaCO3/L, of 0.09 µg Cd L-1 for the whole data setpproachrwater,regional that is tranformed to other water hardness using the slope of 0.7409, increases more than threefold between H = 40 and H = 200 (Fig. 3.2.3). We note that the US-EPA Cd criterion continuous concentration is very close to the regional PNECwater.

Sorption of Cd2+ on suspended particles is higher in soft water than in hard water. As a result, the difference in HC5 values between soft and hard water becomes smaller if the concentrations are based on total concentrations (dissolved + sorbed).

Although there is a relationship between Cd toxicity and water hardness, no correction of the PNECwater will be made to derive the generic PNECwater. However, we suggest that for risk characterisation on a local/regional scale, PNECwater should be corrected to water hardness in order to better correspond to local/regional environmental conditions.

#### Conclusion

The PNECwater of Cd is derived from the median HC5 value (Aldenberg and Slob, 1993) from 44 chronic NOEC values, some of which are geometric species means. These data are derived from 19 tests with fish/amphibians, 22 tests with aquatic invertebrates and 8 tests with primary producers, and represent 28 species in total. All these tests belong to data quality group RI 1-3. The NOEC values were obtained from laboratory based, single species studies and refer to the dissolved fraction. An assessment factor of two is applied on the HC5. The PNECwater is

# PNECwater = 0.19 µg Cd L-1

No adverse effect of Cd below this PNEC was found in the 168 tests with RI 1-3 that have been reviewed.  There is a trend that dissolved Cd is more toxic at lower water hardness.  A correction of the PNEC for water hardness has been proposed that may be useful for local or regional risk characterisation.  Multi-species NOEC’s have been reported between 0.08 and 4.2 µg Cd L-1. The lowest NOEC was found at a very low water hardness. The hardness corrected PNECwater was within the range of MS ’OEC values and below all MS LOEC's. This indicates that the HC5 method is protective for ecosystem structure in case of Cd. No data were, however, found for very soft waters, i.e. at water hardness below about 10 mg CaCO3/L. Current data suggest that a significant number of freshwaters in Norway, Finland and Sweden have water hardness below this threshold. So, a conclusion i) is reached because there is a need for better information regarding the toxic effects of cadmium to aquatic organisms under low water hardness conditions (Cd toxicity testing in very soft waters).

### Terrestrial compartment.

#### General

##### Data quality: definitions of Reliability Indices (RI’s)

For each test, a RI is given according to the following criteria:

RI 1: standard test. Two such test included are the OECD 207 acute toxicity test with Eisenia fetida in OECD-soil and the ISO 1994: soil quality effects of soil pollutants on Collembolla (Folsomia candida): method for the determination of effects on reproduction.

RI 2: no standard test but complete background information is given, i.e. the following information is present:

- soil pH

- soil organic matter or carbon content

- texture (class or texture fractions)

- total Cd content of the soil at zero Cd application if the NOEC or LOEC value is below 2(g g-1

- equilibration time after soil contamination and prior to the test

- statistical analysis of the dose-response relationship

- no varying metal contamination along with increasing Cd application

- the control soil must be tested along with at least two Cd concentrations above the background concentration

- the soil must be homogeneously mixed with the metal prior to the test

RI 3: no standard test and one or more of the following information from the above-mentioned list is missing as background information: b), c), e) or f). All other information from that list is present.

RI 4: no standard test and one or more of the following information from the above-mentioned list is missing as background information: a), d), g), h) or i). The requirement d) is critical since some tests reporting LOEC values < 2 (g g-1 are considered unreliable. Background Cd concentrations in soil typically range between 0.1 and 0.5 (g g-1 and the lack of reporting the background concentration may underestimate the total Cd concentration in soil at which the first toxic effects are found. Some tests were included that did not show Cd toxicity up to the highest Cd concentration tested. These tests cannot be used for risk assessment (no NOEC can be found) and were considered unreliable (RI4) but were quoted in the tables for illustration.

Tests performed in substrates that were judged as not representative for soils (e.g. pure quartz sand or farmyard manure) were not included in this effects assessment.

##### Source of data and its limitations for risk assessment

The original HEDSET contained no toxicity data for terrestrial organisms. A literature review was made on Cd toxicity to soil or litter microflora, soil fauna and higher plants.

Almost no tests have been made on the toxicity of CdO in soil. Many tests have however been performed with soluble Cd2+ salts. The relevance of soil toxicity tests with metal salts for a risk assessment of the metal oxide is discussed below. The tests with mixed metal pollution or with sludge are generally avoided in this review in order to avoid confounding factors for assessing the dose-response relationship.  Mixed metal pollution is, however, more often found in the environment than single metal pollution. Other metals may have a synergistic or antagonistic effect on Cd toxicity.  Increasing soil zinc is known to reduce Cd availability to plants. It has been advocated that plant Cd uptake studies at soil Cd:Zn ratio’s that are strongly different from the usual 1:100 weight ratio are not relevant (Chaney et al. 1996). Antagonistic effects of Zn on Cd toxicity were shown for growth of the collemobollan Folsomia candida in artificial soil (Van Gestel and Hensbergen, 1997). The EC50 for growth was found at 1.5 of toxic units of Cd and Zn.  The effects of Zn on Cd toxicity to reproduction were, however, only additive.  Due to the lack of information on Cd:Zn interactions in Cd toxicity to soil microflora, soil fauna or higher plants, no predictions can be made to what extent single Cd toxicity studies may overestimate the Cd related toxicity at sites with moderate Cd-Zn metal contamination.

# Toxicity of Cd2+ salts versus toxicity of CdO

Only one reliable study was found in which the toxicity of CdO was tested (Khan and Frankland, 1983). All other data are derived from studies using soluble Cd2+ salts in soil.

The toxicity of CdO in soil can be overestimated based on studies with soluble Cd2+ salts. Depending on the conditions prevailing in the soil, CdO transforms in soil to Cd2+ that sorbs to the soil sorption sites. In this way, Cd derived from CdO becomes equally available as soluble Cd2+ salts after a certain equilibration time.

In order to quantify the transformation rate of CdO in soil, an experiment was set up in which 2 soils were amended with CdO at 50 (g Cd g-1 (Smolders et al., unpublished). The soil solution Cd concentration was monitored during a 3 month incubation period. The soil solution Cd concentrations were compared with these in soils that were amended with a Cd2+-salt at an equivalent total Cd application. The Cd concentrations in the CdO treated soil were between 71and 86 % of those in soil applied with the Cd2+-salt after 3 months incubation. Both soils were acids (pH CaCl2 4.4 and 5.4) which may have contributed to the rapid transformation.

Other evidence on the fate of CdO in soil can be found in studies on comparative toxicity of CdO versus Cd2+ salts and in isotopic exchange of Cd in soils contaminated with CdO.  Calculations with MINTEQA2 (Allison et al., 1991) can provide the equilibrium speciation of CdO in soils but no model has yet been developed predicting its reaction rate.

Table 3.2.16: the Cd concentrations in membrane filtered soil solution of soils amended with CdO. The solution Cd concentrations are expressed as a percentage of the Cd concentration in the soil solution of the Cd(N03)2 treated soil for corresponding soil types and equilibration times. Data in brackets at 99 days incubation are standard deviations (Smolders et al., unpublished).

|  | soil solution Cd (% of Cd-salt treated soil) |
| --- | --- |
| Cd source | sandy pH 4.4 | clayey sand, pH 5.4 |
|  | 8 days | 33 days | 99 days | 8 days | 33 days | 99 days |
| untreated | 0.3 | 0.2 | 0.6(0.1) | 0.6 | 0.5 | 0.1(<0.1) |
| CdO | 103 | 76 | 71(12) | 56 | 77 | 86(4) |

In the study of Khan and Frankland (1983), a loamy sand soil (pH 4.6) was incubated for 15 days after contaminating with 10, 50, 100 and 500 µg g-1 Cd as CdCl2 or with 100, 500 and 1000 µg g-1 Cd as CdO.  Yield of 42-day-old radish plants decreased consistently with increasing Cd rate. From the curves fitted to the shoot yield responses to both Cd compounds, the EC50 was predicted to be 70 µg g-1 for Cd added as CdCl2 and 190 µg g-1 for the Cd added as CdO.  Muramoto et al. (1991) measured Cd uptake in unpolished rice after applying various soluble and insoluble Cd forms. Cd application rates were 10 and 50 (g g-1. The yield of rice (16 weeks) was reduced by 17 % at the highest rate using CdCl2 and by 8 % using CdO. The Cd concentration in rice was not significantly different between CdCl2 or CdO treated plants at the highest application rate. Webber (1973) compared Cd uptake in different plants from compost (pH 6.1) treated with various rates  (0-500 (g g-1) of Cd added as CdO or CdSO4. The author concluded that CdO was at least as phytotoxic as CdCl2. The Cd concentrations in the plant supplied with CdO were even higher than in those treated with CdSO4.

Isotopic exchange using 109Cd2+ is a method allowing to calculate the fraction of the Cd in soils contributing to Cd2+ sorption/desorption reactions within defined conditions of time, solution composition and pH. A radiolabile fraction of 100 % of total Cd in soil effectively means that all Cd in soil is equally available as recently added Cd2+. In 33 polluted soils from U.K., Nakhone and Young (1993) found that this fraction varies from 6 % to 102 %. Many of these soils were contaminated by mine spoils and were characterised by a low fraction of radiolabile Cd. In the soils where the majority of Cd originated from sludge or from smelter fumes (Cd/CdO), the Cd labile pool varied from 29-102 % (average 55 %).  In 10 Belgian soils with both background as elevated Cd levels, the radiolabile Cd pool was found to vary from 62-90 % of aqua regia soluble Cd (Smolders et al., 1999). In a sandy soil sampled in the vicinity of a former Zn smelter in Northern Belgium and which has been polluted through atmospheric deposition with mainly CdO, all aqua regia soluble Cd (10 µg g-1) was found to be radiolabile (Vlassak V., personal communication).

Equilibrium calculations with MINTEQA2 (Allison et al., 1991) confirm that CdO is labile in soil and that Cd2+ becomes adsorbed. Effectively this prediction means that all Cd derived from CdO has the same speciation as Cd derived from soluble Cd salts. Table 3.2.17 shows that in a soil contaminated with 50 (g g-1 Cd, added as CdO, almost all Cd is adsorbed and than all CdO has dissolved. This is surprising since CdO is considered as an insoluble product. In aqueous systems, CdO is indeed insoluble since the pH increases as the product dissolves, thereby reducing the solubility of the product. In soils, however, the pH is buffered and almost unaffected upon the dissolution of CdO.

All evidence gathered above indicates that, in the short term, CdO is less available than soluble Cd2+ salts but that the differences in availability between both Cd2+ forms are not very pronounced.  For these reasons, a soil risk assessment for CdO based on soluble salt studies seems to be justified.

Table 3.2.17: equilibrium speciation in soil contaminated with 50 (g g-1 Cd added as CdO. The speciation is predicted with MINTEQA2 (Allison et al., 1991). The logK value of the reaction Cd2+ + H20 (CdO (Monteponite) +2H+ is –15.12 (database of MINTEQA2). Input parameters: soil moisture content = 0.2 g g-1; soil solution composition Ca(NO3)2 5 mM. Sorption of Cd2+ was assumed to occur on an infinite number of sites. At each soil pH, a solid:liquid concentration ratio KD (solution Cd2+ activity based) was selected that represents a typical value (see Table 3.1.88).

| speciation | Soil pH 5 Kd 50L/kg | Soil pH 6 Kd 200L/kg | Soil pH 7 Kd 800L/kg |
| --- | --- | --- | --- |
| CdO (% of total) | 0.0 | 0.0 | 0.0 |
| Cd2+ sorbed on soil solid (% of total) | 99.3 | 99.8 | 99.9 |
| Cd in soil solution (% of total) | 0.7 | 0.2 | <0.1 |
| Soil solution Cd2+ ((M) Cd(NO3)+ ((M) | 14.4 0.2 | 3.61 0.05 | 0.9 <0.01 |

Influence of soil properties on Cd toxicity

Soil properties influence Cd toxicity. This is illustrated in this review in several tests that have been performed on a series of different soils. A general trend emerges that toxicity increases in soil when mobility of Cd is higher, i.e. soil toxicity increases as soil pH, or soil organic matter decrease. Exceptions to this rule have also been found (Mahler et al., 1978, see section 3.2.2.4.).

The toxicity data were not converted to a standard soil in contrast with suggestions of the Technical Guidance Document (TGD, 1996, p.338).  The suggested conversion corrects the data to a soil with a standard organic matter content of 3.4 %.  Whereas this conversion may be relevant for hydrophobic compounds, no information was found that bioavailability of metals in soil is predominantly related to soil organic matter content. Other normalisation equations that are used for defining maximum permissible concentrations in soils in Flanders-Belgium (Vlarebo, 1996) or in the Netherlands (Lexmond et al., 1986) are merely corrections for variance in background concentrations with soil properties. Since most LOEC data are substantially higher than background concentrations, no such normalisation equation can be advocated. We are not aware of any experimentally obtained relationship between soil properties and soil toxicity for Cd.  Sauvé et al. (1998) demonstrated that toxicity of Pb and Cu on plants or on microbial processes correlates better with soil solution metal activity than with total concentrations. This indicates that soil solution metal activities represent the toxic dose in the soil. If this is the case, then soil toxicity data could be normalised based on e.g. soil properties that affect solid-liquid distribution of Cd. Crommentuijn et al. (1997b) however demonstrated that variation in Cd EC50 values for growth of the collembollan Folsomia candida increased when effects were expressed Cd concentrations instead of total concentrations. The collembollan were exposed to Cd in artificial soils varying in pH and organic matter content, and hence, varying in Cd2+ sorption. It is unclear if the same is true for plants or soil microbial processes.

#### Toxicity to soil microflora

Table 3.2.18: selected data for Cd toxicity to soil microflora. Fifty tests were reviewed from 18 source documents and 36 tests were selected.

|  | min | median | max | n |
| --- | --- | --- | --- | --- |
| NOEC ((g g-1) | 3.6 | 50 | 3000 | 21 |
| LOEC ((g g-1) | 7.1 | 100 | 8000 | 21 |
| E(L)Cx(50 ((g g-1) | 7.1 | 283 | 5264 | 20 |

The soil microflora cycle C, N, P and S compounds in soil. Toxicity to some essential pathways in these cycles may result in plant nutrient deficiencies or unacceptable losses of nutrients to the environment.

Respiration is a process which is performed by a suite of soil organisms with varying sensitivities to soil contamination. Bond et al. (1976) measured respiration in a forest soil and litter microcosm for 24 days following soil contamination with 0, 0.01 and 10 µg g-1 Cd. The respiration rate between day 6-24 at the highest Cd rate was decreased by 36% compared with the control. No information was given on soil properties. Similar respiration studies with forest soil (0-4.5 cm) microcosms contaminated with 0, 0.6 and 6 µg g-1 Cd could not detect significant toxic effects on respiration rates followed over 23 days after contamination (Chaney et al., 1978). Interestingly, respiration rate decreased faster during incubation in control microcosms than in the Cd treated ones, resulting in significant higher respiration rates at 23 days in the Cd treated soils. To overcome the problems with high variability between the replicates, respiration of each microcosm was expressed as a percentage of that rate just prior to the treatment. Expressed this way, respiration was not significantly reduced by Cd up to the highest application rate at either 1.5 or 23 day's incubation. However, in treatments with 47 µg g-1 Zn added, Cd addition at the highest dose reduced respiration rate faster than in the control soils at 36 hours after contamination. The added amount of Cd was not mixed in the microcosms (applied as a solution on the top layer) and, therefore, this test is not selected for effects assessment.  Cornfield (1977) found evidence for increasing Cd toxicity with time on soil respiration. The respiration was followed for 8 weeks after contaminating the acid sandy soil with either 10 or 100 µg g-1 Cd. No toxic effects were noted for the 0-2 weeks incubation whereas respiration significantly reduced by 17 % at the lowest rate tested for the 0-8 weeks incubation. Saviozzi et al. (1997) found no Cd effects up to 50 (g g-1 on total respiration (28 days) in an inceptisol. Walter and Stadelman (1979) measured soil respiration for 24 hours in loamy sand previously grown for 14 weeks by maize plants. The soils were contaminated with Cd at 5 rates between 0 and 58 µg g-1 before plant growth. The LOEC was found at 29.1 µg g-1 at which respiration was 36 % lower than in the nil treatment. Doelman and Haanstra (1984) compared toxic effects on respiration between five different soils amended with various Cd rates between 55 and 8000 µg g-1. Respiration rate was followed during approximately 18 months after contamination. In one soil (sandy soil) toxicity markedly reduced by ageing whereas no such clear trend was found in the other soils. The respiration rates at the end of the incubation period were insignificantly affected by Cd concentrations up to concentrations ranging from 150 to 3000 µg g-1. Increasing clay content and organic matter content reduced Cd toxicity in soil (Doelman and Haanstra, 1984). It is unclear why NOEC values in this study are much higher than the LOEC values for respiration from the studies cited above.  In another study by the same authors (Haanstra and Doelman, 1984), glutamic acid (GLU) induced respiration was followed on the same soils (one soil not included). The time to reach a peak in respiration rate was chosen as the endpoint. The soils were all measured 18 months after Cd addition. Elevated Cd reduced GLU decomposition rate. In the sandy soil, a small but significant decrease in decomposition rate was already found at 55 µg g-1 (lowest concentration tested). In the other 4 soils, an inhibitory effect was only found at higher concentrations or not found (peat soil). A similar study on substrate (glucose+GLU) induced respiration was made on three different soils amended with various Cd rates between 1.8 and 229 µg g-1 (Reber 1989). In this study, the respiration rate of the treated soils was measured at the time where respiration rate increased maximally in the control soils. This endpoint proved to be very sensitive and statistically significant toxic effects (6 % inhibition) were already found at Cd levels of 2.7-7.8 µg g-1.  More than 10 % inhibition was found at 7-29 µg g-1 (LOEC values).  It should be stressed that this endpoint should not be compared with, for example, cumulative respiration, an endpoint that is far less sensitive as can be derived from the studies cited above. Khan and Frankland (1984) measured toxic effects of Cd on cellulolytic activity in a loamy sand soil. The cellulolytic activity was measured using the dye release from a dyed cellophane film, encased in a nylon mesh and placed for 30 days in the soil. The soil was contaminated with various Cd rates between 0 and 100 µg Cd and incubated for 15 days prior to the test. The dye release was measured in a pot with or without growing plants. In the uncropped soils, the LOEC was 50 µg g-1 at which cellulolytic activity was 17 % below that of the control. In the presence of plants, cellulolytic activity was more sensitive to Cd and the LOEC with oat plants was found at 10 µg g-1 (lowest concentration tested) where the inhibition was already 34 %.

The N-cycle provides various pathways on which toxic effects can be monitored. Liang and Tabatabai (1978) measured NH4+-N induced nitrification as NO3-+NO2- accumulation after 10 days of incubation. Three soil types were contaminated with only one Cd application rate (560 µg g-1). Nitrification decreased by between 67% and 94% compared with the nil treated soils. Bewley and Stotzky (1983) followed mineralisation and nitrification for 35 days after adding glycine to soils contaminated with 50, 100, 500 and 1000 µg g-1 Cd.  Nitrate accumulated at a lower rate in the Cd treated soil columns compared with the control. After 4 days, nitrate accumulation was 23 % lower at the lowest Cd concentration tested (50 µg g-1). After 35 days incubation, significant effects on nitrate accumulation were only found at the highest concentration tested.  The Cd application was not well mixed in the soil columns and, therefore, these data were not selected for the effects assessment. Dušek (1995) measured ammonification and nitrification in two soils with and without NH4+ addition. Both soils were contaminated with 0, 10, 100 and 500 µg g-1 Cd. The LOEC’s on maximum nitrate production rate were found at 100 µg g-1 or above. Walter and Stadelman (1979) measured ammonification on the same soil sample on which respiration was measured (see above). The ammonium accumulated after 50 days incubation was not sensitively affected up to the highest concentration tested (58 µg g-1). Denitrification of nitrate in anaerobic conditions in a helium atmosphere was followed for a silt loam soil contaminated with various Cd rates between 0 and 500 µg g-1 (Bollag and Barabasz, 1979). Some samples were autoclaved and subsequently inoculated with Pseudomonas. Because of unknown effect of autoclaving soils on Cd availability, only the data obtained with the native soil microflora in unautoclaved soils are reported here. The various N forms (NO3-, NO2-, N2O and N2) were followed during 3 weeks of incubation.  Removal of nitrate was slower and accumulation of the intermediates (NO2-, N2O) was higher in the Cd treated soils. The presence of the intermediate N2O (a greenhouse gas) was already higher at the lowest concentration tested (10 µg g-1) after two or three weeks incubation. At a Cd level of 100 µg g-1, the remaining quantities of NO3- + N2O in the systems were about twice as high as in the control soil after 2 weeks incubation.

Toxic effects on soil enzymes are often used in soil toxicology, perhaps because of the ease of measurement. The enzymes reported here, urease, phosphatase and arylsulphatase, represent responsible parts of the N, P and S cycle respectively.  Doelman and Haanstra (1986, 1989) and Haanstra and Doelman (1991) reported effects of Cd addition on enzyme activities in the five soils which were also used for the respiration studies (Doelman and Haanstra, 1984). The enzyme activities were recorded at a saturating substrate concentration in soils either 6 weeks or 18 months after Cd addition. Cd rates varied from 55 to 8000 µg g-1.  The inhibition of the enzyme activity was plotted to the log of the added Cd concentration. A logistic response curve was plotted to the data and an EC50 was calculated by interpolation where curve fitting was possible. The EC50 values are given in Table 3.2.19. Toxicity of Cd increased with time (decrease of EC50) for all combinations of soil and type of enzymes where response curves could be fitted. In all soils, except the peat soil, response curves were significant at 18 months after incubation and this incubation time was chosen for discussion below. The toxic effects of Cd were in general terms most pronounced in the sandy soil. Among the three enzyme, the urease activity was generally most sensitive to Cd (lowest EC50 values) except in the silty loam at pH 7.7.  The EC50 value of urease in the sandy loam was 30 µg g-1 and is below the lowest concentration tested. The authors also reported the EC10 which were calculated with the experimental curves. These EC10 values range from <1 to 280 µg g-1 for urease, from 16 to 8000 µg g-1 for phosphatase and from 3.4 to 5880 µg g-1 for arylsulphatase. Ten of the 14 EC10 values however fall below the lowest concentration tested (55 µg g-1) and, hence, their statistical significance is questionable. The LOEC’s were unfortunately not given in the original papers.

Biological N2 fixation  (either by free living cyanobacteria or as symbiotic associations) is very sensitive to soil pollution (Brookes, 1995). Toxic effects are found in soils treated with sewage sludge where, of course, multiple metal contamination is found. The LOEC values on yield of clover or on population of Rhizobium leguminosarum biovar trifolii are 0.8 µg g-1, 1.0 µg g-1 and 6.0 µg g-1 Cd in three European long-term sludge treated plots (McGrath et al., 1995). The Zn levels on these sites are 130 µg g-1, 200 µg g-1 and 180 µg g-1 respectively. All three Zn levels are below current limits of sludge treated soils in the EC.  Effects of single metals on survival of Rhizobium leguminosarum biovar trifolii in soil was reported by Chaudri et al. (1992). This survival study used a farmyard manure treated plot of the Woburn Experimental Farm (U.K.). Two month after CdSO4 application, no toxic effects were found on survival of the Rhizobium strains. After 18 months, however, the cell number was decreased in all soils and this decrease was most pronounced in the metal applied samples. The Cd NOEC was 4 (g g-1 and at 7.1 (g g-1 no more cells of the Rhizobium strains were detected. The nitrogen content in white clover plants grown on these soils decreased with increasing soil Cd content with a LOEC of 7.1 (g g-1. In N-fertilised samples, no such decrease in plant N-content was found confirming toxicity on N2-fixation. The evidence of metal toxicity on N2-fixation which has been gathered in the last decade is however conflicting. NOEC values on N2-fixation in sludge treated soils are often higher than the LOEC values given above (e.g. Ibekwe et al, 1995)

The toxicity tests for soil microflora lack standardisation that complicates mutual comparison of the tests described above. Toxicity of Cd generally decreases with increasing clay content, pH and organic matter content. The data compilation shows that N2-fixation is probably the most sensitive soil microbial process. Toxic effects on N2-fixation have been found at moderate Cd pollution, both in metal salt applied soils as in sludge treated soils.

Table 3.2.19: toxicity to soil microflora. All underlined data are selected to discuss the critical concentrations (table 3.2.18). Bold data are used to estimate the HC5 (table 3.2.26). Data with reliability index 4 are given as supporting information but they are not used in the effects assessment.

| test substance | organism | medium | pHa | %OCb | % clay | Equil. Period (d) | duration (d) | endpoint | NOEC (µg g-1) | Cat.* | LOEC (µg g-1) (%effect) | ECx(50 (µg g-1) (%effect) | references | R.I. |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| CdOAc. | native soil microflora | phaeosem | 6.9 | 1.3 | 21 | >1 week | 84(min.) | substrate induced respiration rate | 3.6 | 1 | 7.1(15) | 60 | Reber, 1989 | 2 |
|  |  | neutral sandy hortisol | 7 | 1.5 | 3 |  | 84(min.) | substrate induced respiration rate | 3.6 | 1 | 7.1(15) | 70 |  | 2 |
|  |  | acidic cambisol | 5.6 | 1 | 7 |  | 84(min.) | substrate induced respiration rate | 14.3 | 1 | 28.6(18) | >228(HT) |  | 2 |
| CdCl2 | native soil microflora | grassland soil | 7.4 | 5.7 | 24 | 0 | 33 | nitrification: NO3- production rate -NH4+substrate | 50 | 2 | 100(19) |  | Dušek, 1995 | 2 |
|  |  |  |  |  |  |  |  | +NH4+substrate | 10 | 1 | 100(13) | 500(60) |  |  |
|  |  |  | 7.6 | 2.9 | 19 |  | 33 | nitrification: NO3- production rate -NH4+substrate | 50 | 2 | 100(12) |  |  |  |
|  |  |  |  |  |  |  |  | +NH4+substrate | 100 | 1 | 500 (45) |  |  |  |
| Cd(NO3)2 | native soil microflora | loamy sand | 5.8 | 2.7 | 16 | >98 | 1 | 24h respiration | 14.6 | 1 | 29.1(36) |  | Walter and Stadelman, 1979 | 2 |
| CdCl2 | native soil microflora | sand silty loam | 7 7.7 | 1.1 2.6 | 2 19 | 560 560 | 1-2 1-2 | glutamic acid decomposition time glutamic acid decomposition time | 55 | 1 | 150(15) | 150(56) | Haanstra and Doelman, 1984 | 2 2 |
|  |  | clay | 7.5 | 3.4 | 60 | 560 | 1-2 | glutamic acid decomposition time | 150 | 1 | 400(10) |  |  | 2 |
| CdCl2 | native soil microflora | sand | 7 | 1.1 | 2 | 490 | 42-70 | respiration | 150 | 3 | 400(23) |  | Doelman and Haanstra, 1984 | 3 |
|  |  | sandy loam | 6 | 6.1 | 9 | 301 | 42-70 | respiration | 150 | 1 | 400(20) |  |  | 2 |
|  |  | silty loam | 7.7 | 2.6 | 19 | 630 | 42-70 | respiration | 150 | 1 | 400(17) |  |  | 2 |
|  |  | clay | 7.5 | 3.4 | 60 | 560 | 42-70 | respiration | 3000 | 1 | 8000(34) |  |  | 2 |
|  |  | peat | 4.5 | 13.6 | 5 | 574 | 42-70 | respiration | 400 | 1 | 1000(19) |  |  | 2 |
| CdCl2 | native soil microflora | sandy soil | 7 | 1.1 | 2 | 42 560 | 5h 5h | urease activity urease activity |  |  |  | 340 120 | Haanstra and Doelman, 1991 | 2 |
|  |  |  |  |  |  | 42 | 1h | phosphatase activity |  |  |  | 840 |  |  |
|  |  |  |  |  |  | 560 | 1h | phosphatase activity |  |  |  | 330 |  |  |
|  |  |  |  |  |  | 42 | 2h | arylsulphatase activity |  |  |  | 2206 |  |  |
|  |  |  |  |  |  | 560 | 2h | arylsulphatase activity |  |  |  | 121 |  |  |
|  |  | sandy loam | 6 | 6.1 | 9 | 42 | 5h | urease activity |  |  |  | >8000 |  |  |
|  |  |  |  |  |  | 42 | 1h | phosphatase activity |  |  |  |  |  |  |
|  |  |  |  |  |  | 42 | 2h | arylsulphatase activity |  |  |  | >8000 |  |  |
|  |  |  |  |  |  | 560 | 2h | arylsulphatase activity |  |  |  | 1792 |  | 2 |
|  |  | silty loam | 7.7 | 2.6 | 19 | 42 | 5h | urease activity |  |  |  | 970 |  |  |
|  |  |  |  |  |  | 560 | 5h | urease activity |  |  |  | 520 |  |  |
|  |  |  |  |  |  | 42 | 1h | phosphatase activity |  |  |  | 5488 |  |  |
|  |  |  |  |  |  | 560 | 1h | phosphatase activity |  |  |  | 235 |  |  |
|  |  |  |  |  |  | 42 | 2h | arylsulphatase activity |  |  |  | 1882 |  |  |
|  |  |  |  |  |  | 560 | 2h | arylsulphatase activity |  |  |  | 137 |  |  |
|  |  | clay | 7.5 | 3.4 | 60 | 42 | 5h | urease activity |  |  |  | 4460 |  |  |
|  |  |  |  |  |  | 560 | 5h | urease activity |  |  |  | 520 |  |  |
|  |  |  |  |  |  | 42 | 1h | phosphatase activity |  |  |  | 9744 |  |  |
|  |  |  |  |  |  | 560 | 1h | phosphatase activity |  |  |  | 5264 |  |  |
|  |  |  |  |  |  | 42 | 2h | arylsulphatase activity |  |  |  | 9486 |  |  |
|  |  |  |  |  |  | 560 | 2h | arylsulphatase activity |  |  |  | 1016 |  |  |
|  |  | peat | 4.5 | 13.6 | 5 | 42 | 5h | urease activity |  |  |  | 3260 |  |  |
|  |  |  |  |  |  | 560 | 5h | urease activity |  |  |  | 490 |  |  |
|  |  |  |  |  |  | 42 | 2h | arylsulphatase activity |  |  |  | 3181 |  |  |
| CdSO4 | native soil microflora | sandy soil | 4.9 | 2.2 | 5.2 | 0 | 56 | respiration | 5 | 2 | 10(17) |  | Cornfield 1977 | 3 |
| CdsO4 | Rhizobium leguminoasorum bv. trifolii | sandy loam | 6.5 | / | 9 |  | 540 | cell number (survival) | 4 | 3 |  | 7.1(100) | Chaudri et al., 1992 | 3 |
| CdCl2 | native soil microflora | brown earth loamy sand | 4.6 | 1-20** | 0-15** | 15 | 45 | cellulolytic activity: unplanted soil oat grown soil | 10 | 1 | 50(17) 10(34)LT |  | Khan and Frankland, 1984 | 3 3 |
|  |  |  |  |  |  |  |  | wheat grown soil |  |  | 50(43)LT |  |  | 3 |
| CdSO4 | native soil microflora | organic soil sandy-loam | 4.5 7.8 | 47 2.6 |  | 180 180 | 180 180 | respiration rate ATP content ATP content | 60 112 112 | 3 3 3 |  | 1574 2810 708 | Frostegård et al., 1993 | 3 3 3 |
| CdCl2 | native soil microflora | inceptisol | 5.2 | 1.4 | 8 | 0 | 28 | substrate induced respiration | 50 | 3 | 250(27) |  | Saviozzi et al. 1997 | 3 |
| Cd(NO3)2 | native soil microflora | silt loam | 6.7 | 1.9 | 28 | 0 | 14 | denitrification |  |  | 10LT | 100 | Bollag and Barabasz, 1979 | 3 |
| Supporting data |
| CdSO4 | native soil microflora | sandy soil | 4.9 | 2.2 | 5.2 | 0 | 14 | respiration | 100HT |  |  |  | Cornfield 1977 | 4 |
| CdCl2 | native soil microflora | forest soil (0-4.5cm) loamy sand | 4.8 | 1.1 | 0-15** | 0 | 1.5 23 | respiration rate: 47ppm Zn added no Zn added with or without Zn added | 1.3 6.7HT 6.7HT |  | 6.7(28) |  | Chaney et al., 1978 | 4 4 4 |
| Cd(NO3)2 | native soil microflora | loamy sand | 5.8 | 2.7 | 16 | >98 | 50 | ammonification: NH4+ found after 50 days incubation | 58HT |  |  |  | Walter and Stadelman, 1979 | 4 |
| CdCl2 | native soil microflora | Peat | 4.5 | 13.6 | 5 | 560 | 1-2 | glutamic acid decomposition time | 1000HT |  |  |  | Haanstra and Doelman, 1984 | 4 |
| CdSO4 | native soil microflora | surface soil | 4.8 | 3.8 | 9 | 0 | 4 | nitrification: % NO3- of total N |  |  | 50(30)LT | 1000(54) | Bewley and Stotzky, 1983 | 4 |
| CdSO4 | native soil microflora | surface soil | 5.8 | 2.8 | 23 | 0 | 10 | nitrification: NO3- + NO2- accumulation after 10 days with addition of NH4+ |  |  |  | 560(94)LT | Liang and Tabatabai, 1978 | 4 |
|  |  |  | 7.8 | 3.9 | 30 |  | 10 | nitrification: NO3- + NO2- accumulation after 10 days with addition of NH4+ |  |  |  | 560 (70)LT |  |  |
|  |  |  | 7.4 | 5.7 | 34 |  | 10 | nitrification: NO3- + NO2- accumulation after 10 days with addition of NH4+ |  |  |  | 560(67)LT |  |  |
| CdSO4 | native soil microflora | Lösslehm Lösslehm degr Lösslehm + kalk Auengleye Auenboden | 6.10 3.25 7.25 7.50 7.20 | 1.56 3.45 1.47 2.91 1.95 |  |  | 30 52 30 30 38 30 37 30 37 | microbial biomass nitrification microbial biomass microbial biomass nitrification microbial biomass nitrification microbial biomass nitrification | 30(HT) 33(HT) 30(HT) 30(HT) 30(HT) 30(HT) 33(HT) 30(HT) 33(HT) |  |  |  | Beck, 1981 | 4 4 4 4 4 4 4 4 4 |
| CdCl2 | native soil microflora | forest soil |  |  |  | 0 | 24 | respiration | 0.01 | 2 | 10(36) |  | Bond et al., 1976 | 4 |

a pH-water ;b% OC= %OM/1.7; LT: Lowest Tested concentration; HT: Highest Tested concentration; *NOEC classification (see –ection 3.2.0.2); **estimated OC - clay content

#### Toxicity to soil fauna

Table 3.2.20: selected data for Cd toxicity to soil fauna. Forty tests were reviewed from 22 source documents and 37 tests were selected.

|  | Min | median | max | n |
| --- | --- | --- | --- | --- |
| NOEC ((g g-1) | 5 | 32 | 320 | 13 |
| LOEC ((g g-1) | 5 | 59 | 326 | 12 |
| E(L)Cx(50 ((g g-1) | 27 | 102 | 3680 | 28 |

The potential hazards of environmental pollutants to soil invertebrates have been assessed in acute and chronic toxicity tests. The toxicity of Cd (Cd2+ salts) has been tested with standard tests: the 14-day LC50 test using the earthworm Eisenia fetida (OECD 1984, EEC 1985) and the ISO test (ISO, 1994) with the collembolan Folsomia candida.

Table 3.2.20 summarises the reviewed literature data. Reproduction parameters are generally more sensitive to Cd than growth or survival. Spurgeon et al. (1994) grew adult E. fetida in contaminated OECD artificial soil (pH 6.3) for 8 weeks to test the effects of Cd [as Cd(NO3)2] on survival and cocoon production. Soil contamination ranged from 10 to 300 µg g-1. The calculated LC50 was greater than 300 µg Cd/g soil (highest concentration tested).  Cocoon production was unaffected at 5 (g g-1 but was reduced by 80 % at 20 (g g-1. The NOEC value for cocoon production in this soil is the lowest NOEC value for soil fauna found in this literature review. It was however noted by the authors (Spurgeon et al., 1994) that worms in all treatments lost weight after two weeks in the experiment. Using the same artificial soil, the EC50 of the growth of E. fetida was 33 µg Cd/g soil and there was no observed effect at 18 µg Cd/g soil (Van Gestel et al., 1991).  Sexual development of E. fetida was inhibited at 10 µg Cd/g soil (lowest concentration tested) and a 50% effect was found at 27 µg Cd/g soil. The LC50 was 253 µg Cd/g soil.  In studies by van Gestel et al. (1993) it was found that reproduction of Eisenia was more sensitive than growth.  Khalil et al. (1996b) re–orted a LOEC of 10 µg Cd/g soil –the lowest concentration tested - and an EC50 of 35 µg Cd/g soil for cocoon production of the earthworm Aporrectodea caliginosa in natural soil 56 days after Cd addition. The LC50 was found at 540 µg Cd/g. Growth of this earthworm in that soil was reduced by 50% at 68 µg Cd/g (Khalil et al, 1996a).

Increasing exposure time generally increases toxicity in the laboratory tests. Van Gestel and van Dis (1988) recorded an increase in mortality with increasing exposure time, using the 14-day OECD test. Khalil et al. (1996b) and van Gestel et al. (1991) extended the exposure time of the earthworm to 8 and 12 weeks respectively. Both authors found a significant decrease of more than 50% of the LC50 during the exposure period. A short exposure time may therefore explain the higher LC50 values found by Neuhauser et al. (1985) in an artificial soil. An LC50 value of 1843 (g g-1 was recorded in 2 weeks of exposure.

Fitzpatrick et al. (1996) compared the sensitivity to Cd in an artificial OECD-soil between two earthworm species. The LC50 of Lumbricus terrestris was lower than that of Eisenia fetida (256 versus 374 µg g-1 soil).

Soil characteristics influence Cd sorption and therefore its bioavailability and toxicity. Van Gestel and van Dis (1988) investigated the influence of pH on the toxicity of Cd to earthworms. Toxicity was assessed in a sandy soil limed from pH 4.1 to pH 7.0. The LC50 value at pH 4.1 was at least 3 to 4-fold lower than at pH 7.0. Bengtsson et al. (1986) studied the combined effects of Cd pollution and acidification of the soil on the earthworm Dendrobaena rubida. Tests were performed at pH 4.5, 5.5 and 6.5 in the C horizon of a sandy coniferous forest soil mixed with well decomposed cattle dung. Cocoon production was lower at pH 4.5 than at higher pH values in the nil treated soils. Cadmium significantly reduced cocoon production at pH 4.5. At pH 5.5 and 6.5 however, 10 µg Cd/g increased cocoon production whereas 100 µg Cd/g significantly decreased this productions at pH 5.5 only. Similar conclusions were made about effects of pH and Cd on success of hatching of the cocoons. No toxic effects of Cd on growth were found. At pH 6.5, growth was even increased by 100 µg Cd/g compared to control. Crommentuijn et al. (1997b) investigated the effects of pH and organic matter content on toxicity of Cd on growth and reproduction of the springtail Folsomia candida. The difference in soil properties affected the performance of the test organisms. Soluble Cd concentrations increased when pH or organic matter decreased in soil. The variation in Cd EC50 values for growth increased when effects were expressed as soluble Cd concentrations instead of total concentrations.

Kammenga et al. (1996), Korthals et al. (1996) and Parmelee et al. (1997) studied the effect of Cd pollution on nematodes. Korthals et al (1996) recorded a NOEC value of 160 µg Cd/g (highest concentration tested) for survival of the natural nematode community in a sandy soil. Parmelee et al. (1997) found a comparable NOEC value of 200 µg g-1 (highest concentration tested) for survival in a forest topsoil. Kammenga et al. (1996) found a NOEC value for the juvenile/adult ratio of the nematode Plectus acuminatus of 32 µg g-1 in an artificial OECD-soil.

This data compilation seems to indicate that soil fauna are less sensitive to Cd than soil microflora. The LOEC values obtained with soil fauna are all higher than or equal to 5 µg g-1 whereas Cd toxicity to soil microbial processes or plants has been shown at lower Cd concentrations (section 3.2.2.2 and 3.2.2.4). Soil fauna could indeed be more resistant to Cd but it is striking to note that sensitive endpoints (e.g. reproduction) have rarely been tested in the 1-10 µg g-1 range. Some LOEC values of 10 (g g-1 are found at the lowest concentration tested for reproduction parameters of Eisenia andrei (van Gestel et al., 1991&1993).  Three tests were found where Cd toxicity was measured below 10 µg g-1 (Khalil et al., 1996a, Spurgeon et al., 1994 and Parmelee et al., 1997).  One of these tests showed Cd toxicity at 5 (g g-1  (Khalil et al, 1996a).

Table 3.2.21: toxicity to soil fauna. All underlined data are selected to discuss the critical concentrations (table 3.2.20). Bold data are used to estimate the HC5 (table 3.2.26). Data with reliability index 4 are given as supporting information but they are not used in the effects assessment.

| test substance | organism | medium | pHa | %OCb | clay | Equil. Period (d) | duration (d) | endpoint | NOEC (µg g-1) | Cat.* | LOEC (µg g-1) (%effect) | ECx(50 (µg g-1) (%effect) | LCx(50 (µg g-1) (%effect) | references | R.I. |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| CdCl2 | Folsomia candida | OECD-soil | 6.1$ | 5.9 | 20 |  | 42 | fresh weight reproduction | 50 22 | 1 5 |  | 322 51 |  | van Gestel and Hensbergen, 1997 | 1 |
| CdCl2 | Eisenia fetida | OECD soil | 7$ | 5.9 | 10.4 | 0 |  | mortality |  |  |  |  | >1000HT | Van Gestel & van Dis, 1988 | 1 |
| CdCl2 | Folsomia candida | OECD soil | 6.6 | 5.9 | 20 | 0 | 35 | mortality growth number of juveniles population increase |  |  |  | 633 153 152 | 972 | Crommentuijn et al., 1995 | 1 |
| Cd(NO3)2 | Eisenia fetida | OECD-soil | 6.5 | 5.8 | 20 | 0 | 14 | mortality |  |  |  |  | 374 | Fitzpatrick et al., 1996 | 1 |
| Cd(NO3)2 | Dendrobaena rubida | C-horizon of sandy coniferous forest soil+well decomposed cattle dung | 4.5 5.5 6.5 5.5 | 4.5-6.9 |  | 4 weeks | 110 270 | cocoon production cocoon production hatching success embryonic development | 10 10 | 1 1 | 100(47) 10LT | 100(72%) 100(78%) |  | Bengtsson et al., 1986 | 2 2 2 2 |
| CdCl2 | Lumbricus rubellus | sandy loam soil | 7.3 | 4.7 | 17 | 0 | 42 | mortality weight | 150 150 | 3 3 |  |  | 1000(100) | Ma, 1982 | 3 |
| CdCl2 | Folsomia candida | OECD-soil | 6.3$ | 5.9 | 20 | 0 | 42 | mortality at 25% MC 45%MC 55%MC fresh weight at 25%MC 35%MC 45%MC 55%MC reproduction at 25%MC 35%MC 45%MC 55%MC | 160 320 80 160 | 3 1 3 3 | 320(72) 160(43) 320(29) | 523 640(73) 253 481 80(56)LT 80(57)LT 80(46)LT 80(43)LT | 1275 868 617 | van Gestel and van Diepen, 1997 | 3 3 2 3 3 3 |
| CdCl2 | Eisenia fetida | sandy soil | 4.1$ | 1 | 4.3 | 0 | 14 | mortality |  |  |  |  | 320-560 | Van Gestel & van Dis, 1988 | 2 |
| CdCl2 | Folsomia candida | OECD soil; T 20; 50% WHC | 5.4-5.9$ 5.4$ 5.7$ 5.9$ 5.9$ 5.8$ 3.1$ 3.7$ 4.3$ 5.7$ 7$ 7.3 | 1.2 2.1 3.1 4 4.9 5.9 5.9 5.9 5.9 5.9 5.9 5.9 | 20 | 0 | 35 | growth reproduction mortality growth reproduction mortality growth reproduction mortality growth reproduction mortality growth reproduction mortality growth reproduction mortality growth reproduction mortality growth reproduction mortality growth reproduction mortality growth reproduction growth reproduction growth reproduction |  |  |  | 246 125 356 44 389 82 651 193 615 130 824 193 302 102 316 102 542 164 697 177 583 113 601 306 | 323 684 758 940 890 1261 743 1276 | Crommentuijn et al., 1997b | 2 |
| CdCl2 | Folsomia candida | OECD soil | 6 | 5.9 | 20 | 0 | 19 | mortality number of offspring growth | 326 148 | 1 1 | 707 326 | / 448 | 917 | Crommentuijn et al., 1993 | 2 2 |
|  |  |  |  |  |  |  | 23 | mortality number of offspring growth | 326 71 148 | 1 1 1 | 707 148 326 | 159 376 | 778 |  | 2 2 2 |
|  |  |  |  |  |  |  | 26 | mortality number of offspring growth | 326 71 326 | 1 1 1 | 707 148 | 204 707 | 822 |  | 2 2 2 |
|  |  |  |  |  |  |  | 30 | mortality number of offspring growth | 326 71 148 | 1 1 1 | 707 148 326 | 227 541 | 893 |  | 2 2 2 |
|  |  |  |  |  |  |  | 35 | mortality number of offspring growth | 326 148 326 | 1 1 1 | 326 707 | 807 | 854 |  | 2 2 2 |
| Cd(NO3)2 | Eisenia fetida | OECD soil | 6 | 5.9 | 20 | 0 | 14 | mortality |  |  |  |  | 1843 | Neuhauser et al., 1985 | 2 |
| Cd(NO3)2 | Eisenia fetida | OECD soil | 6.3 | 5.9 | 20 |  | 56 | cocoon production | 5 | 1 |  | 46 |  | Spurgeon et al, 1994 | 3 |
| CdCl2 | Eisenia andrei | OECD soil | 6.3 | 5.9 | 20 | 7 | 21 | cocoon production juvenile/adult ratio | 10 | 3 | 10(LT) 18(38) |  |  | Van Gestel et al., 1993 | 3 3 |
| CdSO4 | Aporrectodea caliginosa | natural forest soil | 7.05 | 12.5 |  | 0 | 42 | growth |  |  | 5(40)LT) | 68 |  | Khalil et al., 1996a | 3 |
| CdSO4 | Aporrectodea caliginosa | natural forest soil | 7.05 | 12.7 |  | 0 | 56 | mortality cocoon production |  |  | 10(28)LT | 35 | 540 | Khalil et al., 1996b | 3 3 |
| CdCl2 | Eisenia andrei | OECD soil | 6.7 | 5.9 | 20 |  | 84 | growth mortality sexual development | 18 | 1 | 10(37)LT | 33 27 | 253 | van Gestel et al., 1991 | 3 3 3 |
| CdCl2 | Plectus acuminatus | OECD soil | 5.5 | 5.9 | 20 | 5h | 21 | juvenile/adult ratio | 32 | 1 | 100(24) | 321 |  | Kammenga et al., 1996 | 3 |
| Cd(NO3)2 | Lumbricus terrestris | OECD-soil | 6.5 | 5.8 | 20 | 0 | 14 | mortality |  |  |  |  | 256 | Fitzpatrick et al., 1996 | 3 |
| CdCl2 | Enchytraeus albidus | OECD-soil | 6.5 | 5.9 | 20 | 0 | 28 | mortality |  |  |  |  | 3680 | Römbke, 1989 | 3 |
| Supporting data |
| Cd(NO3)2 | Eisenia fetida | OECD soil | 6.3 | 5.9 | 20 |  | 56 | mortality | 300HT |  |  |  |  | Spurgeon et al, 1994 | 4 |
| CdCl2 | Eisenia andrei | OECD soil | 6.3 | 5.9 | 20 | 7 | 21 | growth | 100HT |  |  |  |  | Van Gestel et al., 1993 | 4 |
| CdSO4 | nematode community | top 10cm of an arable field on a sandy soil | 4.1 | 1.9 | 4 |  | 14 | mortality | 160HT |  |  |  |  | Korthals et al. , 1996 | 4 |
| CdSO4 | trophic groups of nematode and microanthropod communities | top 10cm of A-horizon of mature oak-beech forest soil | 3.8$ | 3.4 | 11 | 0 | 7 | mortality | 200HT |  |  |  |  | Parmelee et al., 1997 | 4 |
| Cd(NO3)2 | Lumbricus terrestris | artificial-soil |  |  |  | 0 | 16 | sperm-count |  |  |  | 100 |  | Cikutovic et al., 1993 | 4 |

a pH-water; $pH-KCl; b OM = OC*1.7; LT: Lowest Tested concentration; HT: Highest Tested concentration; MC: moisture content; *NOEC classification (see section 3.2.0.2)

#### Toxicity to higher plants

Table 3.2.22: selected data for Cd toxicity to higher plants. Seventy-six tests were reviewed from 15 source documents and 54 tests were selected.

|  | min | median | max | n |
| --- | --- | --- | --- | --- |
| NOEC ((g g-1) | 1.8 | 10 | 80 | 41 |
| LOEC ((g g-1) | 2.5 | 40 | 160 | 44 |
| E(L)Cx(50 ((g g-1) | 2.8 | 100 | 320 | 34 |

Many studies report effects of Cd salts on plant development in potted soil. Only few studies were found in recent literature. There is currently a consensus that toxicity to plants due to single Cd pollution seldom occurs in the environment. In most cases, Cd pollution is associated with Zn pollution. Zinc is known to be more toxic to plants and plant growth effects in metal polluted areas are often attributed to Zn and not to Cd (Tiller, 1989). As stated above, we only report data that were obtained with single Cd pollution.

A summary of the literature review is given in Table 3.2.22. All data have been obtained using pot trials in greenhouse conditions. In most pot trials, Cd is homogeneously mixed in the whole soil prior to plant growth. In the experiments reported by Miles and Parker (1979) and by Kelly et al. (1979) however, the Cd2+ salts were incorporated by top dressing. These data are reported here but they were not selected for the effects assessment.  Miles and Parker (1979) found that soil Cd in the top 2.5 cm of the pots was about twice as high as the intended average Cd level in soil. Near background Cd concentrations (< 1µg/g) were recorded in the base 2.5 cm of the pots. The strong toxic effects on growth of 3 of the 6 natural species tested at the lowest average concentration tested (10 µg g-1) should therefore be treated with caution.  Many threshold levels for Cd toxicity were obtained by Bingham et al. (1975) and by Mahler et al. (1978) using soils to which 1 % sludge was incorporated. Sludge Cd was not the source for increasing Cd rates in soils (all soils obtained equal sludge rate). Bingham et al. (1975) report that the sludge was low in heavy metals without supplying the data.  Mahler et al. (1978), from the same group of Bingham, report that 1 % sludge application is equivalent to a metal application rate of 0.1 µg g-1 Cd, 6 µg g-1 Cu, 0.4 µg g-1 Ni and 20 µg g-1 Zn. These metal concentrations are all low and should not strongly increase the plant sensitivity to Cd. The data obtained by these two reports are interesting as they allow comparing differences in Cd toxicity between plant types (Bingham et al., 1975) and between soil types (Mahler et al. 1978). The data of Bingham et al. (1975) show that EC25 values vary from 4 µg g-1 to 170 µg g-1 between plant types. The EC25 values of rice were over 640 µg g-1, the highest concentration tested. Mahler et al. (1978) showed that EC50 values vary from 105-320 µg g-1 for chard and from 18-270 µg g-1 for lettuce between the 8 soils. Among these 8 soils, 4 are acid (pH <5.7), and 4 are calcareous (pH>7.4). The Cd toxicity to chard is generally higher in acid soils (lower EC50) than in calcareous soils, as expected based on the effect of pH on Cd sorption. However, Cd toxicity to lettuce is surprisingly generally higher in calcareous soils than in acid soils. Cd uptake in both plants is lower in the calcareous soils than in the acid soils. Why growth sensitivity of lettuce to absorbed Cd is so much higher in lettuce at higher soil pH is unknown. The other tests where Cd toxicity is compared between soil types support the general idea that Cd toxicity in soil is higher if the Cd sorption capacity of the soil is lower, i.e. at low pH, clay content and organic C content (Reber et al. 1989; Miller et al. 1976).

The low values of some LOEC values call for attention. The reliable LOEC values lower or equal to 4 µg g-1 are found by Miller et al. (1977), Reber (1989), Haghiri (1973) and by Bingham et al. (1975-with spinach only). These data generally relate to added Cd concentrations and Cd concentrations of the control soils were not given (generally below 1 µg g-1). The LOEC values from the tests of Haghiri (1973) are derived as EC>20 values without statistical information.

Two more source documents can be quoted here, which show Cd toxicity below 4 µg g-1 but of which data are not included in the table. The first report (Bingham et al. 1986) shows a significant yield reduction of 9 week-old Swiss chard upon adding 1 or 2.5 µg g-1 Cd to an unlimed sandy loam at pH 4. The yield reduction was 33 % and 42 % compared with the ‘control’ soil which was not a nil treatment but a soil supplied with 0.25 µg Cd/g. Because the ‘control’ soil was contaminated, no LOEC could be derived. The second report (Strickland et al., 1979) shows that yield of soybeans is reduced by over 30 % upon adding Cd at 2.5 µg g-1.  The soil in which this effect was observed is, however an artificial substrate (quartz sand with 0.5 % peat moss) wetted with dilute nutrient solution. Since this substrate represents an extreme example of a soil low in Cd sorption properties, we chose not to incorporate it in the table.

Table 3.2.23: toxicity to higher plants. All underlined data are selected to discuss the critical concentrations (table 3.2.22). Bold data are used to estimate the HC5 (table 3.2.26). Data with reliability index 4 are given as supporting information but they are not used in the effects assessment.

| test substance | plant | medium | pHa | %OCb | % clay | Equil. time prior to plant growth (d) | growing period (d) | pot (P) or field (F) trial | endpoint | NOEC (µg g-1) | Cat.* | LOEC (µg g-1) (%effect) | ECx(50 (µg g-1) (%effect) | references | R.I. |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| CdCl2 | Picea sitchensis | peaty gley | 3.3 | 45 | 40-100** | 2 | 100 | P | root length | 1.8 | 1 |  | 2.8(59) | Burton et al, 1984 | 2 |
| CdOAc | Triticum aestivum | phaeosem neutral sandy hortisol acidic cambisol | 6.9 7.0 5.6 | 1.3 1.4 0.9 | 21 3 7 | >84 | 28 | P | shoot dry weight | 7.1 29 | 1 1 | 14.3(15) 57(15) 3.6(11) |  | Reber, 1989 | 2 2 2 |
| CdCl2 | Glycine max | silt loam clay loam | 7.9 6.0 5.5 6.5 6.1 | 1-20** | 0-28** 0-28** 0-28** 0-28** 28-40** | 4 drying and rewetting cycles | 28 | P | shoot dry weight | 10 10 5 10 | 3 3 4 3 | 100(22) 10(26) 10(12) | 100(69) 100(47) 100(66) | Miller et al., 1976 | 3 3 3 3 3 |
| CdCl2 | Zea mays | loamy sand | 6 |  |  | 4 drying and rewetting cycles | 24 | P | shoot dry weight |  |  | 2.5(47)LT |  | Miller et. al, 1977 | 3 |
| CdCl2 CdO | Raphanus sativus | loamy sand | 5.4 | 1-20** | 0-15** | 15 | 42 | P | shoot dry weight | 10 | 1 | 50(30) 100(29)LT | 70 190 | Khan and Frankland, 1983 | 3 3 |
| Cd(NO3)2 | Lactuca sativa | soil | 3.9 | 1.2 | 8 |  | 42 | P | shoot dry weight | 2 | 2 | 32 (30) |  | Jasiewicz,1994 | 3 |
| CdCl2 CdO | Avena sativa Triticum aestivum Triticum aestivum | loamy sand | 5.4 | 1-20** | 0-15** | 15 15 15 | 42 42 42 | P P P | root dry weight root dry weight root dry weight |  |  | 10(24)LT 100(47)LT | 50(61)LT | Khan and Frankland, 1984 | 3 |
| CdCl2 | Lactuca sativa Lycosperisicon esculentum Avena sativa | humic sand loam humic sand loam humic sand loam | 5.1 7.5 5.1 7.5 5.1 7.5 | 2.2 0.8 2.2 0.8 2.2 0.8 |  |  | 14 | P | shoot fresh weight | 32 3.2 32 10 10 | 1 1 1 1 1 |  | 136(50) 33(50) 16(50) 171(50) 97(50) 159(50) | Adema and Henzen, 1989 | 3 3 3 3 3 3 |
| CdSO4 | Phaseolus vulgaris Glycine max Triticum aestivum Zea mays Lycosperisicon esculentum Cucurbita pepo Brassica oleracea Lactuca sativa Lepidium sativum Spinacia oleracea Brassica rapa Raphanus sativus Daucus carota Oryza sativa | silt-loam soil amended with 1% clean sludge | 7.5 |  | 0-28** |  | up to maturity | P | bean dry weight bean dry weight grain weight kernel weight ripe fruit weight fruit weight head weight head weight shoot weight shoot weight tuber weight tuber weight tuber weight grain weight | 20 2.5 20 10 80 80 160(HT) 5 5 1.25 10 40 10 640(HT) | 3 3 3 3 3 3 3 3 3 3 3 | 40 (25) 5 (25) 50 (25) 18 (25) 16(25) 160 (25) 13 (25) 8 (25) 4 (25) 28 (25) 96 (25) 20 (25) |  | Bingham et al., 1975 | 3 3 3 3 3 3 4 3 3 4/3 3 3 3 4 |
| CdSO4 | Lactuca sativa Beta vulgaris Lactuca sativa Beta vulgaris Lactuca sativa Beta vulgaris Lactuca sativa Beta vulgaris Lactuca sativa Beta vulgaris Lactuca sativa Beta vulgaris Lactuca sativa Beta vulgaris Lactuca sativa Beta vulgaris | surface soils amended with 1% clean sludge | 4.8 5.0 5.3 5.7 7.4 7.5 7.7 7.8 | 2.6 3.3 0.9 3.0 1.4 0.6 0.9 0.7 | 8.3 14.6 8.9 37.5 18.7 4.4 40.6 15.2 | 14 >77 14 >77 14 >77 14 >77 14 >77 14 >77 14 >77 14 >77 | 63 | P | shoot dry weight shoot dry weight | 40 20 40 20 10 40 20 40 20 40 2.5 20 5 40 10 80 | 3 3 3 3 3 3 3 3 3 4 4 3 3 3 3 3 | 80(20) 80(35) 160(22) 80(30) 40(35) 80(25) 80(25) 160(40) 80(35) 160(25) 10(25) 80(25) 10(30) 160(35) 40(38) | 260 110 270 135 100 110 160 185 195 320 80 105 18 195 58 320 | Mahler et al., 1978 | 3 3 |
| CdCl2 | Glycine max Triticum aestivum Raphanus sativus Lactuca sativa Capsicum frutescens Apium graveolem | silty clay loam | 6.7 | 2.5 | 28-40** |  | 35 35 26 37 112 117 | P P P P P P | shoot dry weight shoot dry weight root dry weight shoot dry weight pepper dry weight leaf dry weight | 10HT 10HT |  | 2.5(21)LT 2.5(36)LT 2.5(40)LT | 10(50) | Haghiri, 1973 | 3 3 3 3 4 4 |
| Supporting data |
| CdCl2 | Poa pratensis Liatris spicata Rhus radicans Andropgong scoparius Rudbeckia hirta Monarda fistulosa | sandy | 4.8 | 1.1 | 0-15** | 7-10 | 42 | P | shoot dry weight shoot dry weight shoot dry weight shoot dry weight shoot dry weight shoot dry weight | 10 10 10 | 3 3 3 | 10(30) 10(21) | 30(90) 30(63) 10(79) 30(68) | Miles and Parker, 1979 | 4 |
| CdCl2 | Glycine max | silt loam loamy sand | 4.5 6.1 7.0 5.7 | 1-20** | 0-28** 0-28** 0-2**8 0-28** | 4 drying and rewetting cycles | 28 | P | shoot dry weight | 1 1 1 0.5 | 3 3 3 4 | 10(33) 10(33) | 10(52) 100(66) 100(50) 10(77) | Miller et al., 1976 | 4/3 4/3 4/3 4/3 |
| CdCl2 | Pinus strobus Pinus taeda Liriodendron tulipifera Betula alleghaniensis Prunus virginiana | forest soil 0-14cm sandy | 4.8 | 1.1 | 0-15** | several weeks | 120 | P | shoot dry weight shoot dry weight shoot dry weight shoot dry weight shoot dry weight | 15 15 15 15 15 | 1 3 3 1 1 |  | 100(57) 100(55) 100(78) 100(82) 100(62) | Kelly et al., 1979 | 4 |
| Cd(NO3)2 | Nicotinia tabacum Nicotinia rustica Zea mays | sandy clay | 5.3 | 0.9 | 9.4 | 21 | 60 | P | total plant dry weight total plant dry weight total plant dry weight | 5.4(HT) 5.4(HT) 0.4 |  | 5.4(21) |  | Mench et al., 1989 | 4 |

a pH-water; $pH-KCl; b OM = OC*1.7; LT: Lowest Tested concentration; HT: Highest Tested concentration; *NOEC classification (see –ection 3.2.0.2); **estimated OC - clay content

#### Discussion

Table 3.2.24 lists all selected toxicity data of soil microflora, soil fauna and higher plants. This data set contains all data that were underlined in Tables. 3.2.19, 3.2.21 and 3.2.23. This selection is based on data quality, i.e. data with RI 1-3 only, and on an attempt to avoid overrepresentation of data from the same test or the same organism (see introduction of effects assessment section). The selected data are retrieved from 167 different tests. This selection of results is used in this section to identify the factors that affect Cd toxicity, i.e. type of organism and environmental conditions. The data with RI 1-3 are considered to be reliable (no critical information is missing).

Table 3.2.24: summary of selected Cd toxicity data for the terrestrial environment ((g g-1). All data have RI(3 and a data selection was made to avoid overrepresentation of data from the same test or the same organism (see introduction of effects assessment section).

|  | NOEC |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  | min | 5th perc. | median | max | n |
| microflora | 3.6 | 3.6 | 50 | 3000 | 21 |
| higher plants | 1.8 | 2.5 | 10 | 80 | 41 |
| soil fauna | 5 | 8.0 | 32 | 320 | 13 |
|  | LOEC |  |  |  |  |
|  | min | 5th perc. | median | max | n |
| microflora | 7.1 | 7 | 100 | 8000 | 21 |
| higher plants | 2.5 | 2.5 | 40 | 160 | 44 |
| soil fauna | 5 | 7.8 | 59 | 326 | 12 |
|  | E-LCx(50 |  |  |  |  |
|  | min | 5th perc. | median | max | n |
| microflora | 7.1 | 57 | 283 | 5264 | 20 |
| higher plants | 2.8 | 10 | 100 | 320 | 34 |
| soil fauna | 27 | 38 | 102 | 3680 | 28 |

The median and 5th percentiles of the NOEC, LOEC and ECx(50 values of tests with higher plants are lower than corresponding values for microflora and soil fauna.  This may indicate that Cd more sensitively affects higher plants than microbial processes or soil fauna. It must be stressed, however, that the low Cd concentration range (1-10 (g g-1) has been tested in more detail with higher plants than with the other organisms.

#### The PNECsoil

##### Species sensitivity distributions at different levels of data quality

The PNECsoil is calculated from the se’ected NOEC values. Different SSD's can be calculated for different selections of the data since the NOEC values have attached information such as data quality (the Reliability Index, RI) and properties of the test (species, soil characteristics and endpoint). The statistical properties of the NOEC data as a function of data quality is given in table 3.2.25. All data with RI=4 (unreliable) were not included because critical information of the test was lacking. The selected NOEC data are summarised in table 3.2.26A.

Table 3.2.25: the NOEC values ((g g-1) of the terrestrial compartment for various levels of reliability (RI, defined in the introduction of effects assessment section). The selected data are underlined in preceding Tables 3.2.19, 3.2.21 And 3.2.23.

| NOEC |
| --- |
|  | min | 5th perc. of the NOEC data | median | max | n |
| RI 1-3 | 1.8 | 3.0 | 20 | 3000 | 75 |
| RI 1-2 | 1.8 | 3.6 | 40 | 3000 | 22 |
| RI 1 |  |  | 22 |  | 1 |

To evaluate the toxicity data, the statistical extrapolation method is used (Aldenberg and Slob, 1993). The fifth percentile (HC5), with 50% confidence, of a species sensitivity distribution is calculated using the software package ETX 1.3a (RIVM, Bilthoven, The Netherlands). The HC5 is calculated for three different approaches of data selection. The first approach is by using all the data (Table 3.2.26A), without calculation of species geometric mean values. The s‘cond approach ’s by calculating 'geometric mean' NOEC values for each species, resulting in one NOEC per species (Table 3.2.26B). The ‘hird approach ’s by ’alculating 'geometric mean' NOEC's on a case-by-case bas’s (3.2.26C). Geometric mean NOEC's are calculated for the same species and the same endpoint, tested in similar¶ soils. This approach does not result in one NOEC per species. NOEC’s of soil microbial assays have never been averaged across soils because of the intrinsic variability of the microbial population between soils.

Table 3.2.26A: selected data of effects of Cd in soil. Data derived from Tables. 3.2.19, 3.2.21 and 3.2.23 within quality class  RI 1-3.

| organism | phylum/class | order | family | medium | pHa | duration (d) | endpoint | NOEC (µg g-1) | references | R.I. |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| native soil microflora |  |  |  | phaeosem | 6.9 | 84(min.) | substrate induced respiration rate | 3.6 | Reber, 1989 | 2 |
|  |  |  |  | neutral sandy hortisol | 7 | 84(min.) | substrate induced respiration rate | 3.6 |  | 2 |
|  |  |  |  | acidic cambisol | 5.6 | 84(min.) | substrate induced respiration rate | 14.3 |  | 2 |
| native soil microflora |  |  |  | grassland soil | 7.4 | 33 | nitrification: NO3- production rate -NH4+substrate | 50 | Dušek, 1995 | 2 |
|  |  |  |  |  |  |  | +NH4+substrate | 10 |  |  |
|  |  |  |  |  | 7.6 | 33 | nitrification: NO3- production rate -NH4+substrate | 50 |  |  |
|  |  |  |  |  |  |  | +NH4+substrate | 100 |  |  |
| native soil microflora |  |  |  | loamy sand | 5.8 | 1 | 24h respiration | 14.6 | Walter and Stadelman, 1979 | 2 |
| native soil microflora |  |  |  | silty loam | 7.7 | 1-2 | glutamic acid decomposition time | 55 | Haanstra and Doelman, 1984 | 2 |
|  |  |  |  | clay | 7.5 | 1-2 | glutamic acid decomposition time | 150 |  | 2 |
| native soil microflora |  |  |  | sand sandy loam | 7 6 | 42-70 42-70 | respiration respiration | 150 150 | Doelman and Haanstra, 1984 | 3 2 |
|  |  |  |  | silty loam | 7.7 | 42-70 | respiration | 150 |  | 2 |
|  |  |  |  | clay | 7.5 | 42-70 | respiration | 3000 |  | 2 |
|  |  |  |  | peat | 4.5 | 42-70 | respiration | 400 |  | 2 |
| native soil microflora |  |  |  | sandy soil | 4.9 | 56 | respiration | 5 | Cornfield 1977 | 3 |
| Rhizobium leguminoasorum bv. trifolii |  |  |  | sandy loam | 6.5 | 540 | cell number (survival) | 4 | Chaudri et al., 1992 | 3 |
| native soil microflora |  |  |  | brown earth loamy sand | 4.6 | 45 | cellulolytic activity: unplanted soil | 10 | Khan and Frankland, 1984 | 3 |
| native soil microflora |  |  |  | organic soil sandy-loam | 4.5 7.8 | 180 180 | respiration rate ATP content | 60 112 | Frostegård et al., 1993 | 3 3 |
| native soil microflora |  |  |  | inceptisol | 5.2 | 28 | substrate induced respiration | 50 | Saviozzi et al. 1997 | 3 |
| Folsomia candida | Arthropoda | Collembola | Isotomidae | OECD-soil | 6.1$ | 42 | reproduction | 22 | van Gestel and Hensbergen, 1997 | 1 |
| Dendrobaena rubida | Annelida | Haplotaxida | Lumbricidae | C-horizon of sandy coniferous forest soil+well decomposed cattle dung | 4.5 6.5 | 110 270 | cocoon production hatching success | 10 10 | Bengtsson et al., 1986 | 2 2 |
| Lumbricus rubellus | Annelida | Haplotaxida | Lumbricidae | sandy loam soil | 7.3 | 42 | weight | 150 | Ma, 1982 | 3 |
| Folsomia candida | Arthropoda | Collembola | Isotomidae | OECD-soil | 6.3$ | 42 | fresh weight at 25%MC 35%MC 45%MC 55%MC | 160 320 80 160 | van Gestel and van Diepen, 1997 | 3 2 3 3 |
| Folsomia candida | Arthropoda | Collembola | Isotomidae | OECD soil | 6 | 35 | number of offspring | 148 | Crommentuijn et al., 1993 | 2 |
| Eisenia fetida | Annelida | Haplotaxida | Lumbricidae | OECD soil | 6.3 | 56 | cocoon production | 5 | Spurgeon et al, 1994 | 3 |
| Eisenia andrei | Annelida | Haplotaxida | Lumbricidae | OECD soil | 6.3 | 21 | juvenile/adult ratio | 10 | Van Gestel et al., 1993 | 3 |
| Eisenia andrei | Annelida | Haplotaxida | Lumbricidae | OECD soil | 6.7 | 84 | growth | 18 | Van Gestel et al., 1991 | 3 |
| Plectus acuminatus | Nemata | Araeolaimida | Plectidae | OECD soil | 5.5 | 21 | juvenile/adult ratio | 32 | Kammenga et al., 1996 | 3 |
| Picea sitchensis | Pinopsida | Pinales | Pinaceae | peaty gley | 3.3 | 100 | root length | 1.8 | Burton et al, 1984 | 2 |
| Triticum aestivum | Liliopsida | Cyperales | Poaceae | phaeosem neutral sandy hortisol | 6.9 7.0 | 28 | shoot dry weight | 7.1 29 | Reber, 1989 | 2 2 |
| Glycine max | Mafnoliopsida | Fabales | Fabaceae | silt loam clay loam | 7.9 6.0 6.5 6.1 | 28 | shoot dry weight | 10 10 5 10 | Miller et al., 1976 | 3 3 3 3 |
| Raphanus sativus | Mafnoliopsida | Capparales | Brassicaceae | loamy sand | 5.4 | 42 | shoot dry weight | 10 | Khan and Frankland, 1983 | 3 |
| Lactuca sativa | Mafnoliopsida | Asterales | Asteraceae | soil | 3.9 | 42 | shoot dry weight | 2 | Jasiewicz,1994 | 3 |
| Lactuca sativa Lycosperisicon esculentum Avena sativa | Mafnoliopsida Mafnoliopsida Liliopsida | Asterales Solanales Cyperales | Asteraceae Solanaceae Poaceae | humic sand loam loam humic sand loam | 5.1 7.5 7.5 5.1 7.5 | 14 | shoot fresh weight | 32 3.2 32 10 10 | Adema and Henzen, 1989 | 3 3 3 3 3 |
| Phaseolus vulgaris Glycine max Triticum aestivum Zea mays Lycosperisicon esculentum Cucurbita pepo Lactuca sativa Lepidium sativum Brassica rapa Raphanus sativus Daucus carota | Mafnoliopsida Mafnoliopsida Liliopsida Liliopsida Mafnoliopsida Mafnoliopsida Mafnoliopsida Mafnoliopsida Mafnoliopsida Mafnoliopsida Mafnoliopsida | Fabales Fabales Cyperales Cyperales Solanales Violales Asterales Capparales Capparales Capparales Apiales | Fabaceae Fabaceae Poaceae Poaceae Solanaceae Cucurbitaceae Asteraceae Brassicaceae Brassicaceae Brassicaceae Apiaceae | silt-loam soil amended with 1% clean sludge | 7.5 | up to maturity | bean dry weight bean dry weight grain weight kernel weight ripe fruit weight fruit weight head weight shoot weight tuber weight tuber weight tuber weight | 20 2.5 20 10 80 80 5 5 10 40 10 | Bingham et al., 1975 | 3 3 3 3 3 3 3 3 3 3 3 |
| Lactuca sativa Beta vulgaris Lactuca sativa Beta vulgaris Lactuca sativa Beta vulgaris Lactuca sativa Beta vulgaris Lactuca sativa Beta vulgaris Lactuca sativa Beta vulgaris Lactuca sativa Beta vulgaris Lactuca sativa Beta vulgaris | Mafnoliopsida Mafnoliopsida | Asterales Caryophyllales | Asteraceae Chenopodiaceae | surface soils amended with 1% clean sludge | 4.8 5.0 5.3 5.7 7.4 7.5 7.7 7.8 | 63 | shoot dry weight shoot dry weight | 40 20 40 20 10 40 20 40 20 40 2.5 20 5 40 10 80 | Mahler et al., 1978 | 3 3 |

a pH-water; $ pH-KCl; MC: ‘oisture content

Tabl’ 3.2.26B: 'One species, one NOEC': selected NOEC data of effects of Cd in soil on fauna and hi‘her plnants, and ca’culation of 'geometric mean NOEC's. Data derived from table 3.2.26A.

| organism | phylum/class | order | family | endpoint | NOEC (µg g-1) |  |
| --- | --- | --- | --- | --- | --- | --- |
| Dendrobaena rubida | Annelida | Haplotaxida | Lumbricidae |  | 10 | geometric mean of 10 and 10 |
| Lumbricus rubellus | Annelida | Haplotaxida | Lumbricidae |  | 150 |  |
| Folsomia candida | Arthropoda | Collembola | Isotomidae |  | 113 | geometric mean of 22, 80, 148, 160, 160, 320 |
| Eisenia fetida | Annelida | Haplotaxida | Lumbricidae |  | 5 |  |
| Eisenia andrei | Annelida | Haplotaxida | Lumbricidae |  | 13 | geometric mean of 10 znd 18 |
| Plectus acuminatus | Nemata | Araeolaimida | Plectidae |  | 32 |  |
| Avena sativa | Avena sativa | Cyperale | Poaceae |  | 10 | geometric mean of 10 and 10 |
| Picea sitchensis | Pinopsida | Pinales | Pinaceae |  | 1.8 |  |
| Triticum aestivum | Liliopsida | Cyperales | Poaceae |  | 16 | geometric mean of 7.1, 20, 29 |
| Glycine max | Mafnoliopsida | Fabales | Fabaceae |  | 7 | geometric mean of 2.5, 5, 10, 10, 10 |
| Raphanus sativus | Mafnoliopsida | Capparales | Brassicaceae |  | 20 | geometric mean of 10 and 40 |
| Lactuca sativa | Mafnoliopsida | Asterales | Asteraceae |  | 10 | geometric mean of 2, 2.5, 3.2, 5, 5, 10, 10, 20, 20, 32, 40, 40 |
| Lycosperisicon esculentum | Mafnoliopsida | Solanales | Solanaceae |  | 51 | geometric mean of 32 and 80 |
| Phaseolus vulgaris Zea mays Cucurbita pepo Lepidium sativum Brassica rapa Daucus carota | Mafnoliopsida Liliopsida Mafnoliopsida Mafnoliopsida Mafnoliopsida Mafnoliopsida | Fabales Cyperales Violales Capparales Capparales Apiales | Fabaceae Poaceae Cucurbitaceae Brassicaceae Brassicaceae Apiaceae |  | 20 10 80 5 10 10 |  |
| Beta vulgaris | Mafnoliopsida | Caryophyllales | Chenopodiaceae |  | 34 | geometric mean of 20, 20, 20, 40,‘40, 40, 40, 80 |

Table’3.2.26C: 'Case-by-case selection': selected NOEC data of effects of Cd in soil on fauna and higher plants,‘and case-by-case ca’culation of 'geometric mean NOEC's. Bold, underlined data are selected for the HC5 calculation. Data derived from table 3.2.26A.

| organism | medium | pH | %OC | %clay | endpoint | NOEC (µg g-1) |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Dendrobaena rubida | C-horizon of sandy coniferous forest soil+well decomposed cattle dung | 4.5 6.5 | 4.5-6.9 4.5-6.9 |  | cocoon production hatching success | 10 10 | no geometric mean: different endpoints |
| Lumbricus rubellus | sandy loam soil | 7.3 | 4.7 | 17 | weight | 150 |  |
| Folsomia candida | OECD soil | 6 | 5.9 | 20 | reproduction | 148 | geometric mean: similar soil, same endpoint, same species |
| Folsomia candida | OECD-soil | 6.1 | 5.9 | 20 | reproduction | 22 | geometric mean = 57 |
| Folsomia candida | OECD-soil | 6.3 | 5.9 5.9 5.9 5.9 | 20 20 20 20 | fresh weight fresh weight fresh weight fresh weight | 160 320 80 160 | geometric mean: similar soil, same endpoint, same species geometric mean = 160 |
| Eisenia fetida | OECD soil | 6.3 | 5.9 | 20 | cocoon production | 5 |  |
| Eisenia andrei | OECD soil | 6.3 | 5.9 | 20 | juvenile/adult ratio | 10 | no geometric mean: different endpoints |
| Eisenia andrei | OECD soil | 6.7 | 5.9 | 20 | growth | 18 |  |
| Plectus acuminatus | OECD soil | 5.5 | 5.9 | 20 | juvenile/adult ratio | 32 |  |
| Picea sitchensis | peaty gley | 3.3 | 45 |  | root length | 1.8 |  |
| Triticum aestivum Triticum aestivum | phaeosem neutral sandy hortisol | 6.9 7.0 | 1.3 1.4 | 21 3 | shoot dry weight shoot dry weight | 7.1 29 | no geometric mean: different endpoints, different soils |
| Triticum aestivum | silt-loam soil amended with 1% clean sludge | 7.5 |  |  | grain weight | 20 |  |
| Glycine max Glycine max Glycine max Glycine max | silt loam silt loam silt loam clay loam | 7.9 6.0 6.5 6.1 |  |  | shoot dry weight shoot dry weight shoot dry weight shoot dry weight | 10 10 5 10 | no geometric mean: different endpoints, different soils |
| Glycine max | silt-loam soil amended with 1% clean sludge | 7.5 |  |  | bean dry weight | 2.5 |  |
| Raphanus sativus | loamy sand | 5.4 |  |  | shoot dry weight | 10 | no geometric mean: different soils |
| Raphanus sativus | silt-loam soil amended with 1% clean sludge | 7.5 |  |  | tuber weight | 40 |  |
| Lycosperisicon esculentum | loam | 7.5 |  |  | shoot fresh weight | 32 | no geometric mean: different soils |
| Lycosperisicon esculentum | silt-loam soil amended with 1% clean sludge | 7.5 |  |  | ripe fruit weight | 80 |  |
| Avena sativa Avena sativa | humic sand loam | 5.1 7.5 |  |  | shoot fresh weight | 10 10 | no geometric mean: different soils |
| Phaseolus vulgaris Zea mays Cucurbita pepo Lepidium sativum Brassica rapa Daucus carota | silt-loam soil amended with 1% clean sludge | 7.5 |  |  | bean dry weight kernel weight fruit weight shoot weight tuber weight tuber weight | 20 10 80 5 10 10 |  |
| Lactuca sativa | humic sand loam | 5.1 7.5 | 2.2 0.8 |  | shoot fresh weight shoot fresh weight | 32 3.2 | no geometric mean: different soils |
| Lactuca sativa | soil | 3.9 | 1.2 | 8 | shoot dry weight | 2 |  |
| Lactuca sativa Lactuca sativa | surface soils amended with 1% clean sludge | 4.8 5.0 | 2.6 3.3 | 8.3 14.6 | shoot dry weight shoot dry weight | 40 40 | geometric mean: same endpoint, same species, similar soils geometric mean = 40 |
| Lactuca sativa Lactuca sativa | surface soils amended with 1% clean sludge | 5.3 5.7 | 0.9 3.0 | 8.9 37.5 | shoot dry weight shoot dry weight | 10 20 |  |
| Lactuca sativa | surface soils amended with 1% clean sludge | 7.4 | 1.4 | 18.7 | shoot dry weight | 20 | geometric mean: same endpoint, same species, similar soils |
| Lactuca sativa | silt-loam soil amended with 1% clean sludge | 7.5 |  | 14 | shoot weight | 5 | geometric mean = 10 |
| Lactuca sativa | surface soils amended with 1% clean sludge | 7.5 | 0.6 | 4.4 | shoot dry weight | 2.5 | no geometric mean: different soils |
| Lactuca sativa Lactuca sativa | surface soils amended with 1% clean sludge | 7.7 7.8 | 0.9 0.7 | 40.6 15.2 | shoot dry weight shoot dry weight | 5 10 |  |
| Beta vulgaris Beta vulgaris | surface soils amended with 1% clean sludge | 4.8 5.0 | 2.6 3.3 | 8.3 14.6 | shoot dry weight shoot dry weight | 20 20 | geometric mean: same endpoint, same species, similar soils geometric mean = 20 |
| Beta vulgaris Beta vulgaris Beta vulgaris Beta vulgaris Beta vulgaris Beta vulgaris Beta vulgaris Beta vulgaris | surface soils amended with 1% clean sludge | 4.8 5.0 5.3 5.7 7.4 7.5 7.7 7.8 | 2.6 3.3 0.9 3.0 1.4 0.6 0.9 0.7 | 8.3 14.6 8.9 37.5 18.7 4.4 40.6 15.2 | shoot dry weight shoot dry weight shoot dry weight shoot dry weight shoot dry weight shoot dry weight shoot dry weight shoot dry weight | 20 20 40 40 40 20 40 80 | no geometric mean: different soils |

There are enough data from all three trophic levels to calculate the PNECsoil by the assessment factor method (AFM) using the lowest assessment factor 10 (TGD, 1996, p. 339). The lowest NOEC value with a RI (3 is 1.8 (g g-1. This yields a PNECsoil = 1.8/10 µg g-1 or 0.18 µg g-1.  That value is within the range of Cd background concentrations in soil. Rather than making a risk assessment based on one single NOEC value, it is possible to use the statistical extrapolation method (TGD, 1996, p. 469) if enough NOEC data are available. This condition is certainly met in the case of Cd and is preferred because it is based on information from a wide range of species and soil microbial processes. The need for additional assessment factors in that assessment will be discussed in the next section.

The statistical extrapolation method (SEM) was applied to the NOEC data (some geometric mean values, see above), calculating the median 5th percentile (HC5) of both the log-logistic and the log-normal distribution with the software package ETX 1.3a (RIVM, Bilthoven, The Netherlands) (table 3.2.27).

Table 3.2.27: Calculation of critical concentrations  ((g g-1) using the assessment factor method (AFM) or the statistical extrapolation method (SEM; Aldenberg and Slob, 1993) for Various levels of data quality.

| data quality group | AFM: NOEC/AF µg g-1 |
| --- | --- |
|  | AF = 10 |
| RI 1-2: whole data set (n=22) | 0.18 |
| RI 1-3: w hole data set (n=75) | 0.18 |
| RI 1- 3: microflora (n=21) | 0.36 |
| RI 1-3: plants+invertebrates (n=54) | 0.18 |
|  | SEM: HC5 at 50% (and 95%) confidence (g g-1 |
|  | logistic distribution | normal distribution |
| RI 1-2: whole data set (n=22) | 1.8 (0.5) | 1.9 (0.5) |
| RI 1-3: whole data set (n=75) | 2.3 (1.3) | 2.2 (1.4) |
| RI 1-’ microflora |  |  |
| Selection of NOEC's, RI 1-3 (Table 3.2.26A); n = 21 | 2.3 (0.6) | 2.3 (0.7) |
| RI 1-3 higher plants + invert’brates |  |  |
| Selection of all NOEC's, RI 1-3 (Table 3.2.26A); n = 54 | 2.5 (1.5) | 2.5 (1.5) |
| One specie’, one value: geometric mean NOEC's (Table 3.2.26B); n = 20 | 2.5 (1.0) | 2.6 (1.1) |
| Case-by-case geometric mean calculation (Table 3.2.26C); n = 49 | 2.7 (1.6) | 2.6 (1.7) |

Selection on data quality slightly affects the value of HC5 between groups RI 1-3 and RI 1-2 (Table 3.2.27; whole data set), illustrating that the frequency distributions of both data sets overlap (2.3 versus 1.8 (g Cd g-1). The median NOEC is distinctly higher for RI 1-2 than for RI 1-3 (Table 3.2.25), but the higher variance in the former data set results in a larger difference between the 5th percentile and the median. Many plant data are excluded from the group RI 1-2 (only 3 NOEC values of plants in that group) whereas plants seem to be the most sensitive group (see 3.2.2.5).  Several Cd toxicity tests on higher plants are selected from older source documents (1970-1980) and the information on the test, such as statistical treatment, is often not complete in these documents. Statistical data analysis is a prerequisite for a test to enter class RI 2.

The HC5 value of tests with RI 1-2 is based on 14 NOEC’s from 3 different soil microbial processes, 5 NOEC’s from 2 different invertebrate families (2 species), and 3 NOEC’s from 2 different plant families (2 species; Table 3.2.26). The RI 1-3 database consists of 24 NOEC’s from 7 soil microbial processes, 12 NOEC’s from 3 invertebrate families (5 species), and 41 NOEC’s from 9 plant families (16 species). The data with RI 1-2 have a higher quality label, but are derived from a limited number of species (only 4 different species and 3 different soil microbial processes).  The majority of data within group RI 3 lack statistical data analysis to classify them as RI 2 (details not shown).  In consequence, the choice for which data group is based on a preference for either a large diversity in species or for data supplied with statistical analysis of the test result (class 1 and 2 NOEC’s).  The underlying assumption in the statistical extrapolation technique is that the logistic frequency distribution reflects species sensitivity distribution.  Since the class RI 1-2 has limited species, it is proposed to use the class RI 1-3 as the basis for deriving the PNEC.

The terrestrial data set is split in two groups: microbial processes and soil invertebrates + higher plants. The endpoints for microbial processes are relevant at the ecosystem functioning level, while the endpoints for soil fauna and plants are relevant at the species level. The principle of splitting the terrestrial data in two groups is open to criticism: there is no scientific argument (e.g. field validation) for either option.   For both groups, the choice of SSD does not affect the HC5, nor does the choice of data selection (geometric mean calculation or not) for soil invertebrates and higher plants. However, the statistical uncertainty surrounding the HC5 is smaller using the combined dataset. In contrast to the procedure used to derive a PNECwater, the lowest NOEC selection approach was not performed because such a selection would not yield a represenative data set for the terrestrial ecosystem (e.g. all clay soils would be excluded). The HC5 for the microflora furthermore equals the HC5 for soil fauna and plants.

Concluding we propose’to use the HC5 based on all NOEC's of the microflora data set, which is the lowest of all HC5 values is, i.e.

# HC5 = 2.3 µg Cd g-1

# The frequency distribution and HC5 are illustrated in Fig. 3.2.4..

Fig. 3.2.4: the cumulative frequency distribution of the selected NOEC values of Cd toxicity tests of soil microflora, invertebrates and higher plants. Observed data and logistic distribution curve for the whole RI 1-3 data set fitted on the data.

The HC5 for the terrestrial ecosystem, based on all NOEC's of the microflora group and on a logistic distribution, is 2.3 µg g-1. The whole data set of terrestrial tests (including tests with RI = 4) contains no observations where toxicity was found below 2.3 µg g-1 (Fig. 3.2.5). The lowest toxicity data (2.5 µg Cd g-1; 4 values) are classified as RI = 3 and were found on plant growth.

Fig. 3.2.5: the cumulative number of LOEC values of selected tests of data quality group RI 1-3.

##### Calculation of the generic PNECsoil

The EU workshop on statistical extrapolation (17-18 January, 2001) proposed that the statistical extrapolation technique can be applied to derive a PNEC, but that an additional assessment factor should be applied to theHC5, which is estimated as a median 5th percentile of the NOEC distribution.  This assessment factor may be chosen between 5 and 1 and should remove uncertainty in extrapolating the PNEC to the field situation. The uncertainty is related to the limited number of taxa included in the species sensitivity distribution, the unknown long term effects in the field and the possibility that mixed pollution renders cadmium more readily toxic.

Species diversity. 	The HC5 value of the terrestrial ecosystem is derived from 5 different microbial processes. This HC5 almost equals the HC5 values based on the fauna+plant data (49 different tests) and the HC5 of the whole RI 1-3 data set (derived from 65 different tests with 20 different species and 5 different soil microbial processes).  The plants belong to 9 different families and 9 different orders and the invertebrates belong to 3 different families and 3 different orders. This diversity certainly meets the recommendation of the EU workshop (17-18 January, 2001) on statistical extrapolation that the data set should contain at least 8 different taxa for applying the statistical extrapolation technique.  The entire database does, however, not contain community system data and is biased towards agricultural species.

Along the same lines, it can be argued that the data should be based on a diversity of soil properties.  The tests on which the HC5 value is based are performed in soils with pH 3.1-7.9 % carbon 0.6-47 and % clay 2-70.  This range in soil properties covers most of the European topsoils.

Lab to field extrapolation.	There are only limited field data that allow deriving threshold concentrations of Cd in soil at the field scale.  Cadmium is usually associated with other metals in the field and these other metals are more readily toxic than Cd itself.  In most cases, Cd pollution is associated with Zn pollution.  Effects of smelter contamination on plants or on earthworms are often attributed to Zn and not to Cd (Tiller, 1989; Spurgeon and Hopkin, 1995).

Few toxic effects of Cd-salts were found in the field observations (Sajwan et al., 1995, Kádár, 1995). In the former test, the top 7.5 cm of loamy sand microplots were contaminated with Cd up to 6.7 µg g-1 Cd (measured concentration) along with small doses of Ni (11 µg g-1) and Se (0.2 µg g-1). There were no growth effects observed in bush beans compared with the nil treatment where soil Cd was at 0.6 µg g-1 Cd (Sajwan et al., 1995).

A field trial on the effects of metal salts was started in Nagyhörcsök (Hungary) in 1991 by Dr. I. Kádár.  Cadmium (as CdSO4) was applied to the soil at 4 rates above control with threefold replication (Table 3.2.28).  The soil is a calcareous chernozem, characterised by a high cation exchange capacity, high pH and high base saturation.  More details on this field trial are described elsewhere (Kádár, 1995; Kádár et al., 1998).  This type of soil is certainly not a worst case scenario for cationic metals, which are strongly sorbed in that type of soil.  No toxic effect of Cd on plant growth was detected up to the highest rate during the first 4 years.  Toxic effects were very pronounced in 1995 and 1996 in spinach and red beet, both plants belonging to the same family, and, to a lesser extent, in 1997 in wheat grain.  Pot trial studies confirm that spinach is far more sensitive to Cd than corn, wheat or carrots (Bingham et al., 1975, see also Table 3.2.23).  The NOEC’s for spinach and red beet in the field were both 50 (g Cd g-1, i.e. well above the HC5   as derived from the laboratory tests.  The average yield data (Table 3.2.28) show that the average plant yield is already considerably reduced at this NOEC, but that this reduction is not large enough to yield a statistically significant effect.  The intrinsically higher variability in field data biases the comparison of field NOEC’s with laboratory NOEC’s.  Effect concentrations may, therefore, be a better basis for a lab-field comparison for plant growth.  The response of spinach growth to Cd shows that yield is reduced with about 25 % at 18 (g Cd g-1 (Table 3.2.28).  The EC25 of spinach grown in a pot trial s was 4 (g Cd g-1, i.e. more than 4-fold lower in than in the field (Bingham et al., 1975; see also Table 3.2.23 and Fig. 3.2.6). The soil in that pot trial (pH 7.5) has a similar pH as in the field trial (7.3).  No pot trial studies were found with red beet.  The Bingham et al. study also reports the EC25 of Cd on wheat grain as 50 (g Cd g-1 (same soil as with spinach) whereas the highest Cd rate in the field did not even result in 25 % reduction in wheat grain yield.  The highest Cd rate in the field was 810 kg Cd ha-1, equivalent to 456 (g Cd g-1 EDTA extractable Cd (Kádár, 1995).  The total Cd in that soil is most likely similar to EDTA extractable Cd.  Concluding, the phytotoxic effect of Cd in the field trials in the Hungarian calcareous chernozem are found at higher concentration than in the pot trials of Bingham et al. (1975) with a calcareous silt loam.

Fig 3.2.6: Yield of spinach: field data (Hungary; Kádár et al., 1998) and pot trial data (Bingham et al., 1975). The soil pH  was 7.3 in the field experiment and 7.5 in the pot trial.

Another long-term field trial was started in 1988-1990 in Bordeaux (France) by Dr. M. Mench of the INRA Bordeaux.  By 1990, there were 3 nominal Cd rates above control: 10, 20 and 40 (g Cd g-1.  The field has plots with pH 5.3-5.6 and plots with pH 6.7-7.0.  The corn shoot yield data of 2000 are given in Table 3.2.28.  Cadmium was more toxic in the most acid plots and had no significant effect on corn shoot yield up to 7-8 (g Cd g-1.   The LOEC’s at 15 (g Cd g-1 are associated with a 50 % (high pH) and 61 % (low pH) lower shoot yield than the control.  One pot trial with corn is reported in a similar soil as in the acid plots.  Leaf + stem dry weight was reduced by 18 % at 5.4 (g Cd g-1 , the highest concentrations tested (Mench et al., 1989; Fig. 3.2.7).  The field data suggest a similar inhibition of growth of corn by Cd as in the pot trials if the field data between control and the first Cd rate are interpolated.

Fig. 3.2.7: Yield of corn: field data and pot trial data (pot trials with 17 kg soil; Mench et al., 1989)

Concluding, the few field data yield NOEC’s that are well above the HC5 of 2.3 (g Cd g-1.  Toxicity of Cd on plants grown in pot trials is equally or more pronounced than in the field. There is currently no indication of higher toxicity of Cd salts in the field than in the laboratory.

Goodness-of-fit	The goodness-of-fit of the SSD's is tested with the Kolmogorov-Smirnov test. The log-logistic and the log-normal distribution are accepted at the 1-10% significance levels when applied on the microbial data set on which the HC5 is based. The lower 95% confidence level is 0.6 (log-logistic distribution) and 0.7 (log-normal distribution), which is considerably lower than the HC5. The lower 95% confidence level in the combined dataset is 1.5 showing that the statistical uncertainty strongly reduces when combining all terrestrial data.

All these arguments given above suggest that  a assessment factor ranging from 1 to 2 might be appropriate to derive a PNECsoil from the HC5. Therefore we propose

| HC5 | Assessment factor | PNECsoil |
| --- | --- | --- |
| 2.3 µg g-1 | 1 | 2.3 µg g-1 |
| 2.3 µg g-1 | 2 | 1.15 µg g-1 |

It must be recalled that there is no single test in the entire database (including tests with RI 4) at which a toxic effect of Cd was found at or below the PNECsoil = 2.3 (g Cd g-1. Furthermore, the PNECsoil based on secondary poisoning is below 1.15 µg Cd g-1(see section 3.2.6.4.2), and therefore a single value for the PNECsoil based on microbial processes is of no importance on the overall outcome of the risk characterisation for the soil compartment.

Table 3.2.28: phytotoxicity of Cd salts in field trials.

| test substance | soil properties | Results* |  |
| --- | --- | --- | --- |
| CdSO4 | Nagyhörcsök (Hungary): calcareous Chernozem; pH (CaCl2) = 7.3; 3% org. matter; 5%CaCO3; CEC 22 cmolc/kg | 1991: 1single Cd application (kg Cd/ha) 1994: soil Cd ((g) yield (ton FW/ha) 1991: corn 1992: carrot 1993: potato 1994: pea 1995: red beet 1996: spinach 1997: wheat grain | 0 0.3 14.6a 16.3a 6.8a | 30 18 n.s. n.s. n.s. n.s. 7.4a 12.1a n.d. | 90 50 n.s. n.s. n.s. n.s. 9.5a 11.4a 7.3a | 270 162 n.s. n.s. n.s. n.s. 3.7b 9.8b 6.4a | 810 not meas. n.s. n.s. n.s. n.s. 0.7b 3.7b 5.4a | Kádár et al., 1998 |
| Cd(NO3)2 | Borde aux (France) pH (CaCl2) = 5.3-5.6; CEC 10 cmolc/k g | 1988-1990 Cd applications 2000:soil Cd (mg Cd/kg) 2000: corn (g FW/plant) | 1.3 59.9a | 7.2 39.9a | 15 23.3b | 35 18.6b |  | Mench, pers. com. (2000) |
| Cd(NO3)2 | Bordeaux (France) pH (CaCl2) = 6.7-7.0; CEC 15 cmolc/kg | 1988-1990 Cd applications 2000:soil Cd (mg Cd/kg) 2000: corn (g FW/plant) | 1.2 35.6a | 8.3 44.0a | 15 17.9b | 32 16.4b |  | Mench, pers. com. (2000) |

*values in the same row with the same superscript do not differ significantly.

##### PNECsoil in relation to soil properties

Toxicity is well known to vary with soil properties, which justifies deriving PNEC values per soil type. As an example, a very low ECx(50 value (2.8 (g g-1) was found for root growth in a forest soil with pH 3.3 (Burton et al, 1984). Clearly, such soil should not be compared with arable soils at higher pH values for which ECx(50 values are almost one order of magnitude higher. As discussed above, no empirical equation has been developed for Cd to normalise toxicity to a standard soil. In this section, an attempt will be made to calculate the PNEC for different soil classes. All selected NOEC data with RI(3 are used in this calculation. The number of classes is restricted to maintain a sufficient number of degrees of freedom. Two selection methods are tested: one is by pH and one is by soil texture.

The pH of the soil dominates the solid-liquid distribution of Cd in soil (Table 3.1.10).  It is often assumed that the metal concentration in soil solution represents the toxic dose for the ecosystem and, therefore, a correlation between metal toxicity and pH is to be expected.  At higher pH, metal solubility is low and the HC5 could be higher than at low pH where metals are more soluble. A significant correlation between the logNOEC values and soil pH was, however, not found (P>0.05) for the data collated here (Fig. 3.2.8). A positive trend between logNOEC and soil pH emerges up to about pH 6 beyond which there seems to be no further trend.

The data were classified in two groups, data obtained at soil pH lower or equal to 6.0 and data obtained at soil pH above 6.0. Statistical properties of the data are given in Table 3.2.29.  The HC5 was calculated by statistical extrapolation of the log logistic distribution of the NOEC values (ETX 1.3a, RIVM, Bilthoven, The Netherlands). The HC5 value is lower in the group pH>6.0 (Table 3.2.29). The mean logNOEC value is identical for both groups but the standard deviation of the logNOEC values is largest in the group pH>6.0. Therefore, the extrapolated HC5 value is smaller for the group pH>6.0.

No correlation was found between logNOEC values and % clay in soil (details not shown). The NOEC values found in soils with less than 10 % clay are somewhat lower than in soils with more than 10 % clay. The lowest HC5 value is found in soils with less than 10 % clay. The median logNOEC is also lowest in this group, while the standard deviation is identical in both groups.

Fig. 3.2.8: semi log plot of the selected Cd NOEC values in soil (n=72) as a function of soil pH.

Table 3.2.29: the PNECsoil ((g Cd g-1) calculated as the HC5 value using the statistical extrapolation method (Aldenberg and Slob, 1993) on the NOEC data sorted by soil characteristics. The NOEC data were sorted either by soil texture or by soil pH.

|  | n | min. NOEC | median NOEC | HC5 ((g Cd g-1) |
| --- | --- | --- | --- | --- |
| classified by pH |  |  |  |  |
| pH ( 6.0 | 25 | 1.8 | 20 | 2.7 |
| pH > 6.0 | 50 | 2.5 | 20 | 2.0 |
| classified by %clay |  |  |  |  |
| % clay ( 10 | 18 | 2.0 | 17 | 1.5 |
| % clay > 10 | 48 | 1.8 | 20 | 2.4 |

It is striking that the HC5 values vary only slightly with soil properties whereas higher variability in toxicity between soil types is often found in comparative experiments (see e.g. plant data of Miller et al., 1976). That variability is reduced here for several reasons. Firstly, the effect of soil factors on the NOEC data is obscured by all other sources of variance, e.g. variance in sensitivity among species and endpoints. Secondly, a NOEC value relates to the lack of toxicity. Soil properties may, for example, have a more pronounced effect on the concentrations at which toxicity is found (LOEC and ECx(50 values).

An attempt was made to unravel the effect of soil type on Cd toxicity using the effect data (LOEC and ECx(50 values). The % effect was related to neither total soil Cd nor to soluble Cd concentrations. The soluble Cd concentrations are calculated from total concentrations based on a model relating soil properties with the solid-liquid distribution coefficient KD. The model proposed by Römkens and Salomons, 1998 was used (see Table 3.1.10). This model estimates the KD based on soil pH only. Few LOEC data were found for which the % effect was not clear from the data. The % inhibition for these data was assumed to be 30%.

The correlation coefficient between % inhibition and soluble Cd concentrations (R2 = 0.02) is similar as between % inhibition and total soil Cd (R2 = 0.04) and EC50 values seem to span an almost equal order of magnitude variability whether expressed as solubles or totals (Fig. 3.2.9). Other KD models were tested (Table 3.1.10) but none of these models yielded better correlation’s (details not shown). It is concluded that normalisation of terrestrial Cd toxicity data based on the solubility of Cd in soil is still not justified pending experimentally proven models.

#### Conclusion

The PNECsoil of CdO is based on the 5th percentile (HC5) of a log-logistic distribution fitted to 21 NOEC’s of microbial processes (5 different processes). The HC5 of the microbial processes almost equals the HC5 values based on the fauna+plant data (54 different tests) and the HC5 of the whole data set of reliable tests (derived from 75 different tests with 20 different species and 5 different soil microbial processes).  The NOEC data are derived from terrestrial toxicity tests with Cd2+ salts. The HC5 is 2.3 (g g-1. There is currently no justification for higher toxicity of Cd salts in the field then in the laboratory. Therefore, a PNEC can be proposed as the median HC5 with an additional assessment factor ranging from 1 to 2. This yields:

# PNECsoil = 1.15-2.3 (g Cd g-1dw

No adverse effects of Cd were found below 2.3 µg g-1 in the entire data set (including data that were considered unreliable). Soils with less than 10 % clay have a slightly lower PNECsoil  (1.5 (g g-1) than soils with more than 10 % clay (2.0 (g g-1). Normalising the Cd toxicity data to soil solution Cd concentrations does not reduce the variance of toxic Cd concentrations between the tests.

Fig. 3.2.9: the % inhibition of Cd in soil related to the soil total Cd concentrations (top) or to soil solution Cd concentrations (bottom). The soil solution concentrations are estimated from soil Cd concentrations based on soil pH (see main text for details).

### Toxicity to benthic organisms.

The fate of CdO powder in sediments is not documented. In the absence of this information, it is hypothesised that the metal behaves as the Cd2+ salt after equilibration. Only limited relevant data on the toxicity of Cd2+ to freshwater benthic organisms were found. These data refer to tests where uncontaminated sediment was spiked with Cd2+ salts.  Several tests with field-contaminated sediments were found. These tests cannot be used for dose-response analysis because the sediments are contaminated with various other metals and with organic compounds. Some of these tests are nevertheless included as supportive information in the review given below. Tests with marine sediments were not included.

#### Influence of sediment properties on toxicity of Cd

There are 3 potential pathways for contaminants to reach benthic organisms: the sediment (e.g. ingestion), the overlying water and the interstitial (pore) water (e.g. across respiratory surfaces and body walls). The relative importance of each rout– depends on a number of factors -sediment characteristics such as type of organisms and feeding habitat (Power and Chapman, 1996).

The Cd mobility in anaerobic sediments is controlled by he concentration of acid-volatile sulphides (AVS) by the particulate organic carbon (POC) and by the dissolved organic carbon (DOC). In aerobic conditions, in which the AVS are virtually absent, Cd mobility depends on the content of the POC and of Fe and Mn-hydroxides. The toxicity of Cd most likely depends on its mobility in the sediment. Since the beginning of the 90’s the role of AVS on metal toxicity in sediments has been studied intensively (Van den Berg et al., 1998, Pesch et al., 1995, Allen et al., 1993, Zhuang et al., 1994, Di Toro et al., 1992, Carlson et al., 1991). A relationship was found between cadmium toxicity and the AVS normalised Cd content. In general, toxicity was expected to be absent when the ratio of the simultaneously extractable metals (SEM) to the AVS < 1 (molar ratio) and to increase drastically from SEM/AVS (1. Metal toxicity above this value furthermore depend on water hardness, pH and solid phase properties. However, the molar ratio did not seem to be a good predictor of potential effects, because the ratio gives no indication about the absolute amount of SEM present in excess of AVS. Therefore, the molar difference was introduced as a better predictor.  At a molar SEM-AVS difference < 0 no toxic effects are expected while at molar SEM-AVS difference > 0 toxic effects may occur. Recently, Di Toro et al. (2000) suggested another modification to the SEM-AVS procedure that significantly improves the prediction of organism mortality. The indicator of risk is the ratio of [SEM-AVS] to the organic carbon content (oc) of the sediment. The SEM-AVS relationships can, however, only be applied in anaerobic conditions and ignores spatial and temporal variations (Van den Berg et al., 1998, Zhuang et al., 1994).

There are exceptions to the AVS based normalisation for bioavailability of Cd in sediments. Lee et al. (2000) did not find a correlation between metal concentrations in animal tissue of four benthic organisms and metal concentrations in pore water. The metal concentrations in the animal tissue were correlated with the metal concentrations extracted from the sediment, indicating that exposure of these organisms principally occurred through ingestion of particles. Therefore, the AVS-based approach may be appropriate for protecting some, but not all, benthic organisms. One study furthermore identified Cd toxicity at SEM concentrations below the AVS (Hansen et al., 1996b). A marine sediment with an AVS level of about 17 mmol kg-1dw was spiked with CdCl2. Effects were found at 12 mmol SEM kg-1dw on the abundancies of Nematoda and Annelida. Although this effect concentration is found at rather high total metal concentration, it reveals that the AVS normalisation may not be applicable in all cases. The study was, however, carried out in marine sediments, and is therefore not used in our calculation of the PNECsediment.

#### Acute and prolonged toxicity to benthic organisms

Table 3.2.30: selected data with RI 1-3 for Cd toxicity to benthic organisms. Seventeen tests were reviewed from 5 source documents and 14 tests were selected.

|  | min | median | max | n |
| --- | --- | --- | --- | --- |
| NOEC ((g gdw-1) | 115 | 680 | 3390 | 15 |
| LOEC ((g gdw-1) | 334 |  | 1079 | 2 |
| E(L)Cx(50 ((g gdw-1) | 563 | 1400 | 6200 | 13 |

A summary of the literature review is given in Table 3.2.30. The Cd concentrations in the sediment/water systems are either expressed pe– unit sediment dry weight ((g g -1dw) or as the dissolved fraction in the liquid phase (µg L –1).  The main factors influencing toxicity results are physico-chemical characteristics of the test medium, test species (physiological behaviour), life stage of the test organisms, test design and preparation of the test medium. The criteria for defining reliability indices are explained for each source document in the IUCLID document. Data obtained from mixed polluted sediments were considered unreliable (RI 4).

Carlson et al. (1991) and Di Toro et al. (1992) studied the influence of the type of sediment on toxicity of Cd. Carlson et al. (1991)pproachr toxicity to Lumbricus variegatus in two lake sediments and one river sediment.  The sediments were con–aminated with Cd (40-16000 (g g -1dw) by equilibrating the sediment with Cd spiked Lake Superior water. The LC50 –alues varied from 700-6000 (g g -1dw.  The LC50 values were positively related with the AVS—content, i.e. more AVS reduces Cd toxicity.. Similar dose-response curves were obtained for the three sediments if the sediment Cd concentration was normalised per unit AVS. Cadmium was extracted with cold hydrochloric acid ((Cd(SE), simultaneous with AVS.  No toxicity was recorded when (Cd(SE/AVS<1 (molar concentration ratio).  Mortality increased sharply to 100% when (Cd(/AVS(1.  Di Toro et al. (1992) performed similar tests with the same test species and sediments of the same three locations.  They found no unique re–ationship between (Cd(SE (mg kg -1dw) and mortality of the test organisms for the different freshwater sediments. By contrast, a clear mortality-concentration relationship was observed when relating mortality to the (Cd(SE/AVS molar ratio. No mortality in excess of 20% was observed for sediments with (Cd(SE/AVS<1. For sediments with (Cd(SE/AVS>1-3, mortality increased significantly.  Similar results were found by Hansen et al (1996a) for mixed polluted sediments. The simultaneously extractable metals (SEM) however included Cd+Cu+Ni+Zn+Pb. The authors conclude that the AVS is a reactive pool that binds heavy metals and render them unavailable to biota. Hare et al. (1994) studied the in situ colonisation of Cd-spiked freshwater sediments by macroinvertebrates in a chronic field study. Lake sediments below the top 10 cm layer was sampled, spiked with Cd, transferred to 8-L test trays and then installed in the lake bottom at 15 m depth. The mean total abundance for all taxa in the test trays was not significantly related to Cd exposure. Taken individually (at species level), the abundances of most species also did not appear to be related to exposure up to the highest Cd exposure level (563 µg Cd g-1dw). Only the number of Chironomus (salinarius gp) sp., which is one of the most abundant Chironomidae species, was strongly reduced at 563 µg Cd g-1dw. Larvae of this species burrow deep in the sediment and have their guts filled with sediment, indicating a high exposure via sediment intake.

The physiological behaviour of the test species affects their sensitivity to Cd. Carlson et al. (1991), Di Toro et al. (1992) and Francis et al. (1984).pproachr of the worm Lumbricus variegatus and the snail Helisoma sp. was measured in spiked sediments (Carlson et al. 1991, Di Toro et al. 1992). Lumbricus was found to be the most sensitive to Cd in 4 out of the 6 different freshwater sediments. The higher sensitivity of the worms was attributed to the extended exposure of the worms due their life strategy. Lumbricus is usually half buried in the sediment while the other half remains in the overlying water for respiration. The snails however remain on the surface of the sediment, decreasing their contact with Cd in the sediment. Francis et al. (1984) investigated the effect of Cd-enriched sediment on goldfish, leopard frog and largemouth bass in the embryonic and larvae stages. The sediment was contaminated between 1 and 1000 mg kg-1dw. No effects on survival were found up to the highest level for goldfish and frog. There was, however, 14 % mortality at hatching of the bass larvae at the highest Cd level. The authors attribute the higher sensitivity of bass to the extended contact time of embryos and larvae with the contaminated sediment. Eggs of largemouth bass are settled onto the sediment and larvae remain there after hatching. Embryos and larvae of goldfish and leopard frog however remain in the overlying water and are less exposed to Cd in the sediment.

Nebeker et al. (1986b) studied survival of Hyalella azteca in Cd-spiked water and in sediment. Tests were performed in static and flow through conditions. The Cd concentrations in the solutions of the flow through systems were far below those in the static system. In the flow-through test, Cd had no effect on mortality of Hyalella azteca whereas in the static test, effects are found in sediment/wat–r systems containing 20 (g Cd L -1.  The gradient between the pore water and bottom water Cd concentrations is disturbed in flow-through systems. Therefore the pore water and bottom water concentrations decrease and the sediment appears to be less toxic.

Table 3.2.31: toxicity to benthic organisms. All underlined data are selected for the effect assessment

| test substance | organism | medium | test conditions | Nominal/ Measured | Equilibration period (d) | Dura tion (d) | endpoint | NOEC (– g-1dw (g L-1 | Cat* | LOEC (g g -1dw µg L-1 | ECx(50 (g g-1dw µg L-1 | references | R.I. |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | pproachrlisoma sp. Lumbricus variegatus | uncontaminated freshwater sediment from: Pequaywan Lake East River West Bearskin Lake Pequaywan Lake East River West Bearskin Lake | semi-static; sed./water:1:3 (vol) AVS: 42 µmol/g AVS: 8.8 µmol/g AVS: 3.6 µmol/g AVS: 42 µmol/g AVS: 8.8 µmol/g AVS: 3.6 µmol/g | M-total | / | 10 | mortality | 3390 2260 340 3390 680 340 |  | 1 1 1 1 1 1 |  |  | 4520 3340 790 4520 1130 680 |  | Di Toro et al., 1992 | 3 3 3 3 3 3 |
| CdCl2 | Hyalella azteca | n–tural sediment (Soap Creek Pond - Oregon State University); 200 ml spiked natural sediment + 800 ml well water | static; T 19°C; sediment characteristics: 3% organic carbon, 15% sand, 29% silt, 56% clay; water ch–racteristics: pH 7.1, H 54 mg L -1 CaCO3, BC < 0.5 µg L –1. AVS unknown | M (diss.) | 0.5 | 4 | mortality | 167 | 1.1 | 2 | 334(26) | 3.2 |  | 6.6 | Nebeker et al., 1986b | 3 |
| CdCl2 | Micropterus salmoides | natural stream sediment; 250 gdw sediment pproachd-solution or distilled deionized water (control) +350 ml rec–nstituted water | DO 6.6-8.1 mg L -1, T 22.1-22.5 °C, pH 7.9-8–4; sed: OM 2.3%, Cd– 1.02 mg kg -1, ZnT 108.2 mg kg -1, FeT 5.52%; 5.52% sand, 35.4% silt, 12% clay | M | 0.42 | 7 | mortality | 540 | 22 | 2 | 1079 (14) | 44 (14) |  |  | Francis et al., 1984 | 3 |
| CdNO2 | Chironomus (salinarius gp) sp. | natural lake sediment (Lake Tantaré, Canada), sampled below the top 1-10 cm; spiked sediments in test trays replaced in the test location in the lake | field test; water characteristics: pH 5.5-5.6, H 3; sediment characteristics: AVS: 0.5 µmol/gdw | N | / | 14 months | abundance | 115 |  | 1 |  |  | 563 (80) |  | Hare et al., 1994 | 2 |
| CdCl2 | Lumbricus variegatus Helisoma sp. | Pequaywan Lake East River sediment West Bearskin Lake Pequaywan Lake East River sediment West Be arskin Lake | sediment AVS content: 38-32 µmol/g 6.8-7.3 µmol/g 2.8-3.2 µmol/g 38-32 µmol/g 6.8-7.3 µmol/g 2.8-3.2 µmol/g test water: sand filtered Lake Superior water; T–21-22 °C, alkalinity 45–46 mg L -1, hardness 44-45 mg L -1, pH 7.9-8, dissol–ed oxygen concentration >6 mg L -1, continuous flow; T 23°C; 1.5L Cd sol. + 1L sed. | M | 4 | 10 | mortality | 3000 800 380 3000 2300 380 |  | 1 1 1 1 1 1 |  |  | 6000 1400 700 6200 4100 810 |  | Carlson et al., 1991 | 2 |
| Supporting data |
| CdCl2 | Hyalella azteca | contaminated freshwater sediment from Foundry cove | semi -static; sed./w ater:1:3 (vol) AVS: 0.1-47 µmol/g; SEM (Ni+Cd) 0.3-1000 µmol/g | M-total | / |  | mortality |  |  |  |  |  | 17 (100) |  | Di Toro et al., 1992 | 4 |
| CdCl2 | Rana pipiens Carassius auratus | natural stream sediment; 250 gdw sediment pproachd-solution or distilled deionized water (control) +350 ml rec–nstituted water | DO 6.6-8.1 mg L -1, T 22.1-22.5 °C, pH 7.9-8–4; sed: OM 2.3%, Cd– 1.02 mg kg -1, ZnT 108.2 mg kg -1, FeT 5.52%; 5.52% sand, 35.4% silt, 12% clay | M | 0.42 | 7 | mortality | 1074(HT) 1008(HT) | 77 69 |  |  |  |  |  | Francis et al., 1984 | 4 4 |
| Cd2+ | Hyalella azteca | natural sediment: Foundry cove | % total organic carbon: 0.55-16.4 µg/g, total Cd: 0.4-38900 µg/g, total Cu: 18-143 µg/g, total Ni: 18-31500 µg/g, total Pb: 6.1-357 µg/g, total Zn: 65-403 µg/g, sum metals: 2.9-893, SEM: 0.2-779 µmol/g, AVS: 0.4-64.6 µmol/g, SEM/AVS: 0.02-139 | M-total | / | 10 | mortality | 72 |  |  | 363(20) |  |  |  | Hansen et al., 1996a | 4 |

TOC: total organic carbon; AVS: acid volatile sulphides; H: water hardness (mg CaCO3 L-1); *NOEC classification (see section 3.2.0.2)

#### The PNECsediment.

There is only one sediment toxicity test available within the data set that can be considered as a real chronic test (test duration of other tests are 4-10 days and use mortality as endpoint). The statistical extrapolation technique will therefore not be used on the NOEC data and two alternative methods will be proposed.

According to the TGD (TGD 1996, p.335), the PNECsediment may be calculated using the equilibrium partitioning (EP) method in the absence of ecotoxicological data for sediment-dwelling organisms.Based on the equilibrium partitioning, the following formula is applied to calculate PNECsediment (mg kg-1ww):

(3.2.3)

with PNECwater expressed in mg L-1, RHOsediment the bulk density of wet sediment (kg ww m-3), Ksed-water the water-sediment partition coefficient (m³ m-3).

This equation can be transformed to a dry weight based PNECsediment  as

(3.2.4)

in which Kp equals the solid-water partition coefficient of suspended matter, expressed in L kg-1, and PNECwater expressed in µg L-1. This transformation has assumed that the fraction Cd in the pore water can be neglected compared to the total amount of Cd in the sediment. Even at the lowest Kp assumed in the Table below, this fraction is less than 0.01%. The PNECwater equals 0.19 µg L-1 (section 3.2.1.7). The  Kp ranges 17 103 L kg-1- 224 103 L kg-1 (typical value , 130 10³ L kg-1 see 3.1.2.3.1, Table 3.1.4). The TGD stipulates an upper limit of Kp beyond which an additional safety factor of 10 should be included (either in PNEC or in PEC) to take the risk of direct ingestion into account. This upper limit is at Kp of about 2000 L kg-1. This situation is certainly the case for Cd, therefore the PNEC should be lowered by a factor of 10 in all cases, i.e. the PNECsediment should be calculated in this case as

(3.2.5)

This results in:

| Kp (L kg-1) | PNECsediment (mg Cd kg-1dw) |
| --- | --- |
| 17000 | 0.32 |
| 130000 | 2.5 |
| 224000 | 4.3 |

The ‘generic’ PNECsediment derived with the EP method using the typical Kp values of suspended matter is, therefore, 2.5 mg Cd kg-1dw

Another approach to calculate the PNECsediment is using the assessment factor (AF) method. The NOEC of the chronic test (115 mg kg-1) is divided by an AF of 50. The choice of an AF of 50 instead of 100 is justified by the number of acute toxicity data, showing no differences between species. This results in

# PNECsediment = 115 mg kg-1/50 = 2.3 mg Cd kg-1dw

The AF method yields a PNEC that is almost identical as the ‘generic’ PNECsediment derived with the EP method.  The AF method however predicts a PNEC which is even below the background value of the sediment in which the lowest chronic NOEC was  found (2.8 mg Cd kg-1dw , Hare et al., 1994). The separation between the PNEC and effect concentrations (n=15) is higher than 100-fold, and this is large for natural elements. Additional chronic toxicity data (currently not found) could remove this concern by reducing the AF to 10 or below. However, it should be recalled that sediment toxicity tests spiked with Cd have little field relevance because Cd availability can remain low as long as the capacity of free sulphides (AVS) in the sediment is not exceeded. Mixed metal pollution is the rule rather than the exception in the field and the Cd availability in a metal polluted sediment is larger than in a clean sediment. The AVS normalisation method proposed by DiToro et al. (2000) for predicting chronic effects can be a useful alternative, but can hardly be used to set generic sediment criteria (see below).

The rapporteur of the present document has clear reservations against the AF method (see above) but has no other choice than selecting the AF above the EP method for a  pragmatical reason: the EP method that includes the safety factor 10 leads to an enigma that risk is predicted in all local scenario’s, even if emissions are zero and the Cd concentrations in water are within the natural background range. This enigma remains whatever the choice of Kp as will be demonstrated in the next paragraph.

The local risk characterisation method of the TGD uses the risk factor for sediment, defined as PEClocalsed/PNECsediment. The PEClocalsed is calculated from the local water concentrations and the suspended matter-water partitioning coefficient (Eqn. 35 in the TGD). It can be shown that PEClocalsed/PNECsediment effectively eliminates the Kp factor in the nominator and denominator, leading to PEClocalsed/PNECsediment=10*PEClocalwater/PNECwater. In simple terms, this means that the risk is predicted (risk factor above 1.0) when the local water concentration is larger than the PNECwater/10, i.e. risk for the sediment compartments is predicted when the Cd concentrations in the overlying water is above 0.019 µg L-1. The natural background Cd concentration is estimated as 0.050 µg Cd L-1 (section 3.1.2.4.3) which means that risk is predicted even when emissions are zero and where the Cd concentrations in water are background. Different hypothesis can be forwarded to explain this enigma (i) the benthic organisms may be less sensitive to Cd than aquatic organisms; (ii) exposure via the pore water is the dominant route and the safety factor 10 is overly protective; (iii) the Cd concentrations in the pore water of sediment are lower than that in the overlying water in contrast with the TGD method that assumes equal concentrations in local scenarios; formation of metal sulphides that reduce Cd2+ activity in sediments compared to the overlying water can explain such reductions. The  safety factor 10 could be disregarded to avoid the enigma with the EP method, however no consensus was reached at the Technical Meetings and it is proposed to use the AF method.

Concluding, it is proposed to select a PNEC derived with an AF as:

# PNECsediment = 2.3 mg Cd kg-1dw

There seems to be many studies that indicate that the SEM/AVS concept (3.2.3.1) may be used for evaluating site-specific toxicity of metals. There are, however, a number of comments on the SEM/AVS concept, which limits its use for a generic approach. Firstly, Ankley (1996) showed that in some cases there appeared to be a linear accumulation of metals with increasing sediment metal concentration irrespective of the SEM/AVS content. This questions the validity of the assumption that when the SEM/AVS < 1, the metals would not be bioavailable.

Secondly, both the qualities of the SEM-data and the AVS-data are under recent discussion. The experimentally determined SEM values may underestimate the actual concentration of metals (Cooper and Morse, 19998), while the AVS values from pooled sediment samples may overestimate the actual AVS concentration in the top, aerobic sediment layer (Van den Berg et al., 1998).

Thirdly, relative to the SEM/AVS concentrations, sediment guidelines based upon dry weight-normalised concentrations were equally or slightly more accurate in predicting both non-toxic and toxic results in laboratory tests (Long et al., 1998). These latter findings currently limit the value of the SEM/AVS ratio for risk assessment.

Fourthly, further research is required to the proposed SEM/AVS concept to better implement its significance (Ankley et al., 1996; Ankley, 1996; Mayer et al., 1996)

- for benthic organisms that have a habitat at or slightly above the sediment surface  where aerobic conditions prevail, and the AVS-content will be very low;

- to protect aquatic systems from metal release associated with sediment suspension;

- for the transport of metals into the food web either from sediment ingestion or the ingestion of contaminated benthos; and

- for organisms that are capable of actively extracting substances from sediments, such as polychaetes, that may produce ligands for (essential) metals, to accelerate uptake.

Due to the several comments on the SEM/AVS concept, its use for a generic approach is not adopted in the present RAR. However, taking into account AVS in assessing the risk of Cd for site-specific purposes might be possible.

The two-tiered approach as proposed in the Zn RAR (draft version, June 2001; Annex 3.3.2.C) could be followed.

To apply the AVS-approach, the worst case approach should be followed, i.e. the highest SEM concentration, the lowest AVS concentration and the lowest foc value. Furthermore, before applying the AVS-approach, some answers should be found on questions about the representativeness of the studies used to develop the AVS approach, the cut off value of 100 µmol g-1oc, seasonal variations in SEM, AVS and foc and the presence of other metals.

# In conclusion, the PNECsediment is derived by the assessment factor method, i.e.

# PNECsediment = 2.3 mg Cd kg-1dw

will be used for risk characterisation.

Remark: After the TMIV’02 last visit discussion on cadmium in sediment a number of MSs (UK, F, DE) and Industry commented on the sediment assessment (cfr also Risk Characterisation and Conclusions).

For UK and DE comments see Risk Characterisation (section 3.3.2).

F expressed it cannot accept a final conclusion iii) based on PNEC derived from an assessment factor of 50. An additional test for the sediment compartment should be requested, in order to reduce the uncertainty of the hazard assessment of the sediment compartment. So, F suggests a general conclusion i) for the sediment compartment (long-term assay on sediment spiked with cadmium). In addition F supports the proposal made by Industry (F CA, 21.01.03).

Industry proposes a stepwise approach (IZA Europe, ICdA CollectNiCad letter, 6.02.03). The first step is related to the incorporation of the results of the studies dealing with bioavailability of metals performed in the frame of the zinc risk assessment. If needed, a second step, an additional long-term assay on sediment could be performed

### Atmospheric compartment.

# No toxicity data of CdO in the atmospheric compartment were found.

### Toxicity for micro-organisms in a sewage treatment plant (STP)

Toxicity data of Cd to micro-organisms are presented in Table 3.2.32. Two tests on the effect of Cd on sludge respiration were found. Both tests were performed according to the OECD 209-guidelines (respiration inhibition test). The tests were performed using metallic Cd powder and CdO powder.  Accounting for the variability of the test results, it seems that both Cd and CdO have a similar toxic action (similar NOEC and LOEC values) when based on the soluble fraction. Cd only affects sludge respiration at about 1 mg Cd L-1 in the dissolved fraction. This concentration was found at a loading of 100 mg metallic Cd powder or 100 mg CdO powder per litre of sludge suspension.

The LOEC values in the dissolved fraction ((1 mg Cd L-1) are high compared with LOEC values for aquatic species (mostly in the 10-100 (g Cd L-1 range).  This may indicate a high tolerance of bacteria to Cd. Some toxicity tests were found with bacterial cultures. These bacteria are tested in artificial media and a high tolerance to Cd was found for Pseudomonas putida, Zoogloea ramigera and Escherichia coli (Bringman and Kuhn, 1980; Norberg and Molin, 1983; Zwarum 1973). The threshold toxic Cd concentration for Pseudomonas putida is 80 µg L-1 (Bringman and Kuhn, 1980), but this concentration refers to 3 % inhibition and can be considered as a NOEC. Cd only affects the other species above 1 mg L-1 range. It is unknown to what extent the components of the media, in which the bacteria are tested, can reduce Cd toxicity through metal complexation.  Therefore, none of the tests with bacterial cultures have been selected for deriving the PNECmicro-organisms .

A PNECmicro-organisms is derived by dividing the lowest NOEC value of a respiration inhibition by an assessment factor of 10  (TGD, 1996, p.334).

This yields

# PNECmicro-organisms = 20 µg Cd L-1

# This concentration refers to the Cd in the dissolved fraction.

Table 3.2.32: toxicity for micro-organisms in a sewage treatment plant or in artificial media

| test substance | organism | medium | test conditions | Nominal/ Measured | Dura tion (d) | endpoint | NOEC (µg Cd L-1) | LOEC (µg Cd L-1) | EC50 (µg Cd L-1) | references | R.I. |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Cd | 0.5 mm sieved activated domestic sludge | activated domestic sludge (1.6g L-1) fed with synthetic sewage | pH 7.7-7.8; T 18.5-19.2 | M-total (Cd) M-dissolved | 0.125 | respiration rate | 32600 200 | 100000(11) 800 (11) |  | LISEC, 1998c | 1 |
| CdO | 0.5 mm sieved activated domestic sludge | activated domestic sludge (1.6g L-1) fed w ith synthetic sewage | pH 7.59-7.79; T 18.5-19.3 | M-total (Cd) M-dissolved | 0.125 | respiration rate | 27300 353 | 77800(26) 1200(26) |  | LISEC, 1998d | 1 |
| CdCl2 | Escherichia coli | artificial medium; pH 6 | soy pepton 0.01% | N | 1-6h | respiration | 600 | 6000 |  | Zwarum, 1973 | 4 |
| Cd(NO3)2 | Pseudomonas putida | artificial medium; pH 7 | static; T 25; H 80 | N | 0.67 | biomass (OD) | 80 |  |  | Bringmann and Kühn, 1980 | 4 |
| CdCl2 | Zoogloea ramigera | artificial medium; pH 7; H 81; T 26 | static | N | 0.87 | cell number | 1000 |  | 3000 | Norberg and Molin, 1983 | 4 |

H= water hardness (mg CaCO3 L-1); OD=optical density

### Assessment of secondary poisoning

#### Source of data and limitations for risk assessment

Toxicity of Cd through secondary poisoning is assessed based on laboratory studies where organisms are exposed to variable Cd concentrations in their prey. A PNECoral can be calculated from such studies. This PNECoral can be combined with the bioconcentration factors (BCF’s) or bioaccumulation factors (BAF’s) of the prey to assess risks of secondary poisoning of the predator by Cd originating from soil, freshwater or sediment. This protocol is suggested by the TGD (TGD, 1996) and will be discussed together with an alternative approach for mammals and birds in section 3.2.6.4).

The risk of secondary poisoning is focussed on mammals and birds and not on lower organisms.  No or little data were found to calculate the PNECoral for fish or aquatic invertebrates, benthic organisms or lower terrestrial organisms. A short discussion will, however, be given about secondary poisoning in fish or lower terrestrial organisms (sections 3.2.6.1.3 and 3.2.6.2.2).

A wealth of data is available on bioconcentration factors or bioaccumulation factors. Only a selection of the data is given here, merely as an illustration rather than to serve as a complete survey.  The bioconcentration factors soil-plant (the soil-plant transfer factors) are reported separately in section 4.1.1.4.8 as this pathway is important for Cd exposure to the general population.

Some BCF and BAF values are derived from systems with mixed metal pollution. Mixed pollution is an additional factor that affects the Cd availability and, hence, the BCF or BAF.  No reliability indices were given to the studies from which the BCF’s or BAF’s are calculated.

#### The aquatic compartment

##### The bioconcentration factor in water

The ability of an organism to concentrate a substance from the aquatic environment is expressed as the bioconcentration factor (BCF).

BCF-values calculated on the basis of steady-state uptake and depuration rate constants are indicated with an asterisk in the Tables. Most of the BC values were, however simply calculated from the concentration ratio between water and biota.  Many of the BCF’s are calculated on a dry weight basis. The BCF’s on dry weight basis are transformed to the wet weight basis if the dry weight percentage of the organism was given in the source document.

Results of Cd bioconcentration studies in water are presented in Table 3.2.33.

Table 3.2.33: the bioconcentration factor (BCF) of Cd in freshwater organisms. the Cd concentrations in the organisms are the product of BCf and Cd concentration in water.

| test substance | organism | medium | test conditions | nominal/ measured | dura tion (d) | Cd in water µg L-1 | BCF (L kg-1ww or L kg-1dwa) | references | Remark |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| primary producers |
| CdCl2 | periphyton (assembly of algae and detritus on rocks) | natural sediment and water of oligotrophic soft water lakes (Ontario) | field study; alkalinity 98 mg L-1; DOC 601 µm L-1; H 8.3 mg L-1 | M-total | 116 | 0.09 | 130000*a | Stephenson and Turner |  |

pproach

| CdCl2 | Elodea sp. | tap + deionized water (50/50); T 20°C; DOC 0.9 mg L-1; H 88 mg CaCO3 L-1; Cd 0.14 µg L-1; Cu 4 µg L-1; Zn 4 µg L-1; Pb 0.2 µg L-1 | semi-static; pH 6; no aeration | M | 16 14 | 0.5 2 4.3 11 | 60600-151500(a) 4560-11400 89000-300000(a) 6700-22333 100232-310000(a) 7535-23143 1636 | Van Hattum et al., 1989 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| CdSO4 | Chlorella vulgaris | algae medium: H 6.2 mg CaCO3 L-1; Zn 48 µg L-1, Cu 2.54 µg L-1, Co 5.9 µg L-1, Mn 91 µg L-1; T 25°C; aerated with 5% CO2 |  | M | 2.08 | 0.18 | 2222(a) | Khummongkol et al., 1982 |  |
| CdCl2 | Phytium sp. Dictyuchus sterile Scytalidium lignicola Phytium sp. Dictyuchus sterile Scytalidium lignicola | bal Medium A basal Medium B | 5 g glucoseL-1, 4 g casamino acidL-1; pH 6.5; T 25°C 2 g glucoseL-1, 1.8 g casamino acidL-1; pH 6.5; T 25°C | M | 5 7 | 5 | 44000(a) 89000(a) 50000(a) 38000(a) 90000(a) 48000(a) | Duddridge and Wainwright, 1980 |  |
| primary consumers |
| CdCl2 | Daphnia magna | Lake Louhilampi (Finland) Artificial humic-free water | DOC 14.2 mg L-1; pH 6.5; H 6 mg CaCO3 L-1 DOC < 0.2 mg L-1; pH 6.5; H 30 mg CaCO3 L-1 | N | 1 3 1 | 20 20 20 | 994* 625 510* | Penttinen et al., 1995 |  |
| CdCl2 | Daphnia magna | Reconstituted water charcoal and 0.45 µm filtered | H 92 mg L-1; Al 73 mg L-1; pH 8 Without HA +0.5 mg HA L-1 +5 mg HA L-1 +50 mg HA L-1 | N | 4 | 10 | 6240(a) 5520(a) 4690(a) 2200(a) | Stackhouse and Benson, 1989 | no gut clearance |
| CdSO4 | Daphnia magna | Ultrapure water; Alk: 100 mg L-1; pH 8.3-8.8; T 20°C | Soft water: H 58 mg L-1 Hard water: H 230 mg L-1 Soft water: H 58 mg L-1 + 0.75 mg HA L-1 | N | 28 28 20 20 | 7.5 | 7333(a) 6666(a) 4733(a) 5000(a) | Winner and Gauss, 1986 | no gut clearance; no steady state |
| CdSO4 | Daphnia magna | Lake Superior water |  |  | 4 | (dissolved) 0.0225 0.225 1 3.4 10.1 | 3555 2089 1000 735 396 | Poldoski J.E., 1979 | no gut clearance |
| CdCl2 | Pteronarcys dorsata Hydropsyche betteni Physa integra. Pteronarcys dorsata Hydropsyche betteni Physa integra Pteronarcys dorsata Hydropsyche betteni Physa integra Pteronarcys dorsata Hydropsyche betteni Physa integra Pteronarcys dorsata Hydropsyche betteni Physa integra | Untreated Lake Superior water; semi-static; T 15°C; DO 10.1-11 mg L-1; H 44-48 mgCaCO3 L-1; A 40-44 mgCaCO3 L-1; Ac 1.9-3 mgCaCO3 L-1; pH 7.1-7.7; food: birch and aspen leaves and Daphnia for H. Betteni |  | M | 28 | 1 3 8.3 27.5 238 | 1000(a) 2000(a) 9000(a) 2500(a) 33333(a) 12333(a) 3614(a) 21084(a) 5904(a) 1818(a) 7455(a) 5818(a) 546(a) 798(a) 672(a) | Spehar et al., 1978 | no gut clearanc |
|  | pproachAsellus aquaticus | Tap + deionized water (50/50); T 20°C; DOC 0.9 mg L-1; H 88 mg CaCO3 L-1; Cd 0.14 µg L-1; Cu 4 µg L-1; Zn 4 µg L-1; Pb 0.– µg L-1 | continuous flow; pH 5.9 - 7.6; DO 8.5 mg L-1 | M | 30 | 0.87-11.3 | 17560* | Van Hattum et al., 1989 |  |
| secondary consumers |
| CdCl2 | Salmo salar | municipal water charcoal filtered and UV sterilised; BC 0.13 µg CdL-1; pH 6.5-7.3; T 5-10; DO 11. 1-12.5; Al 14-17; H 19-28 | Alevins; T 8.9-9.3 °C | M | 92 | 0.13 0.47 0.78 7.5 8.2 34 79 300 | 1385(a) 1277(a) 1282(a) 213(a) 213(a) 95(a) 60(a) 5(a) | Rombough and Garside, 1982 |  |
| CdCl2 | Gasterosteus aculeatus | Water; T 14.6 °C; pH 8.09; DO 94%; Alk 99.7 mg CaCO3L-1; H 120.6 mg CaCO3L-1 | Semi-static | M | 33.3 16 15.3 16.3 30 22.2 7.6 21.5 13.3 36.8 15.3 2 0.3 | 0.8 2.6 4.5 9 29 50 90 290 910 2970 5180 8670 97500 | 511 172.5 216.3 101.3 34.03 23.14 14.36 14.77 5.24 2.78 2.04 1.27 0.51 | Pascoe and Mattey, 1977 | no gut clearance |
| CdCl2 | Cyprinus carpio | tap water; T 18-19; pH 6.8; Al 14.8; H 18, BC 0.001 mg L-1; food < 0.05 µg L-1 | semi-static; viscera gills vertebrae viscera gills vertebrae viscera gills vertebrae viscera gills vertebrae | N | 100 | 1 10 50 100 | 221(a) 286(a) 122(a) 1620(a) 1300(a) 418(a) 892(a) 236(a) 11500(a) 613(a) 158(a) 59(a) | Muramoto, 1981 |  |
| CdSO4 | Lepomis macrochirus | Water; H 207 mg CaCO3L-1; Ac 11 mg CaCO3L-1; Alk 152 mg CaCO3L-1; pH 7.7; DO 6.6 mg L-1; T 16-29 °C | gill intestine and caecum liver kidney gill intestine and caecum liver kidney gill intestine and caecum liver kidney gill intestine and caecum liver kidney gill intestine and caecum liver kidney gill intestine and caecum liver kidney | M | 330 | 2.3 31 80 239 757 2140 | <2174 <2174 <4348 <4348 1097 2355 6484 6065 363 2188 4175 2313 142 1364 1826 634 53 229 363 165 37 176 206 68 | Eaton, 1974 |  |
| CdCl2 | Salvelinus fontinalis | sterilised Lake Superior water; H 42-47; pH 7-8; Al 38-46; Ac 1-10; DO 4-12; T 9-15 | continuous flow; first generation: kidney gill liver kidney gill liver kidney gill liver gonad spleen muscle red blood cells second generation: kidney gill liver | M | 266 735 | 0.06 0.5 3.4 3.4 | 33333(a) 11666(a) 6666(a) 24000(a) 11000(a) 9000(a) 14118(a) 2206(a) 2941(a) 1912(a) 882(a) 29.4(a) 29.4(a) 12647(a) 2647 1765(a) 1471 4412(a) 2294 | Benoit et al, 1976 |  |

HA: humic acids;*BCF-value calculated on the basis of steady-state uptake and depuration rate constants; DOC: dissolved organic carbon; H: water hardness (as mg CaCO3 L-1)

The BCF’s of Cd are highest for the primary producers and lowest for fish (Table 3.2.34). The BCF’ of algae are obtained by measuring Cd concentration in water and algae. The high BCF’s do not necessarily reflect high Cd intake in algae because a significant proportion of Cd is sorbed in the cell wall.  Several BCF values of the invertebrates might overestimate true intake if the analysis of the Cd content in the organisms was performed without gut clearance. The kidney and liver of fish concentrate most Cd within the fish total body.

Table 3.2.34a: comparison of freshwater BCF (L kg-1) found in this study with data found by Taylor (1983).

|  | this review | Taylor (1983) |
| --- | --- | --- |
|  | min | max | median | min | max |
| algae wet weight dry weight | 1636 2222 | 23143 310000 | 7535 115116 | 10 | 10000 |
| invertebrates wet weight dry weight | 396 546 | 17560 33333 | 994 5000 | 10 | 2000 |
| vertebrates wet weight dry weight | 0.51 5 | 6–84 33333 | 229 233 |  |  |
| vertebrates -total body content- wet weight dry weight | 0.51 5 | 5’1 1385 | 15 80 | 1 | 3000 |

The BCF' of algae, that were selected in this review, are higher than the BCF’s that were reviewed from 40 laboratory studies by Taylor (1983). The reviewed BCF values for freshwater algae range between 10 and 10000 L kg-1ww (Taylor, 1983). This report finds BCF values ranging between 222-31000 L kg-1ww if all dry weigh based data are converted to wet weight data. For this conversion it was assumed that the average dry matter content of is 10 %. The BCF’s for algae, that were collated here, were generally found in soft water. Low water hardness is known to increase availability of soluble metals such as Cd2+. The range in fresh weight based BCF’s of invertebrates is also somewhat above the range found by Taylo’ (1983). The whole-body fish BCF's cover a similar range in both studies.

Most important factors affecting the bioconcentration of Cd by aquatic organisms are the Cd concentration of the water, the hardness, pH, and the presence of complexing agents such as humic acid.

The influence of pH on the bioconcentration of Cd is illustrated by experiments of Lithner et al. (1995). A field study was performed in Swedish brooks. The bryophyte Fontinalis antipyretica was transplanted from a pristine brook to various polluted brooks, in the Rönnskär area, containing 0.12 to 0.29 µg Cd L-1. After an exposure period of 14 days the BCF of the top shoots of the bryophytes was determined. An increase in BCF with increasing pH was observed. In acidified brooks (pH < 6) BCF values up to 10000 L kg-1dw were found. In neutral brooks (pH>6) BCF values of more than 30000 L kg-1dw were recorded.

Increasing water hardness reduces the BCF of Cd. Penttinen et al. (1995) found a significant effect of hardness on bioconcentration of Cd by Daphnia magna. After an exposure period of 1 day in artificial water, the uptake rate constant was 5 times smaller in water with hardness of 30 mg CaCO3 L-1 than in water with hardness 6 mg CaCO3 L-1. However, Winner and Gauss (1986) found no significant change in Cd bioconcentration by Selenastrum capricornutum at water hardness values ranging from 57 to 230 mg CaCO3 L-1.

Humic acids (HA) associate with Cd and reduce the bioavailability and accumulation of Cd by aquatic organisms. The Cd in Daphnia magna decreased from 66 to 50 µg Cd g-1dw when 5 mg HA L-1 was added to the artificial water (Stackhouse and Benson, 1989). Increasing the HA content to 50 mg HA L-1 further decreased the Cd uptake by 65%.

Increasing Cd concentration in water reduce the BCF. Tissue Cd concentrations increase with increasing solution Cd but level off at high Cd concentrations (i.e. > 10 µg L-1). As a result, the BCF’s decrease at high Cd concentrations.  This is well illustrated by the BCF values of fish presented in figure 3.2.10. The decreasing trend was observed in all tissues.

Figure 3.2.10: the BCF values (L kg-1) of fish or fish tissues as a function of the Cd concentration in water (µg L-1). Data collated from experiments where solution Cd was artificially increased (see Table 3.2.33).

This trend was also observed in aquatic invertebrates. Poldoski (1979) increased Cd concentrations from. Cadmium content of Daphnia magna increased from 0.08 to 4 mg/kgww with increasing solution Cd between 0.023 and 10 µg Cd L-1. The bioconcentration factor, however decreased from 3555 to 396 L kg-1ww. The BCF’s of the insects Pteronarcys dorsata, Hydropsyche betteni and the snail P. integra. increased up to Cd concentrations of 10 µg Cd L-1. Further increasing the Cd concentration in water resulted in a decrease of the BCF’s. Van Hattum et al. (1989), however, found increasing BCF values of the isopod Asellus aquaticus with increasing solution Cd concentrations between 0.5 and 4.3 µg Cd L-1.

In conclusion, the restricted survey of BCF’s of aquatic organisms demonstrates that the BCF’s are highest in primary producers and lowest in secondary consumers. Factors affecting the BCF are the water hardness, pH, the Cd concentration and the presence of Cd2+complexing agents.

##### The bioaccumulation factor in water

Whereas bioconcentration is the net uptake due to water exposure only, bioaccumulation includes all routes (air, water, soil and food) (TGD, 1996). Several field studies and one laboratory experiment were found in which the BAF (L kgww-1) was calculated for organisms, mainly invertebrates, exposed by both water and food. Bioaccumulation factors range from 4 to 170000 L kg-1dw. Comparison of bioaccumulation factors and bioconcentration factors of aquatic invertebrates reveals the latter to be significantly lower.

Lithner et al. (1995) calculated BAF values ranging from 24000 to 65000(L kg-1dw) for 4 invertebrates living in Swedish lakes (heavy metal contaminated Rönnskär area). In the same area two fish species were captured to determine the Cd concentration of the liver. A BAF of 27000 L kg-1dw was found for liver of Esox lucius and of 164000 L kg-1dw for liver of Perca fluviatilis. These values are remarkably high but liver is known to concentrate Cd compared to the other tissues (see previous section).  The dry weight based BCF values of whole fish (Table 3.2.34a: 5-1385 L kg-1) seem to span a similar range as field derived BAF values of whole fish (4-2492 L kg-1, Table 3.2.32b).  A similar comment apllies to the wet weight based BAF values (Tables 3.2.32a&b).

Table 3.2.34b: the BAF values for whole body vertebrates (L kg-1).

|  | min | max | median |
| --- | --- | --- | --- |
| vertebrates -total body–content- dry weight vertebrates -total body content- weteight* | 4 1 | 2492 623 | 167 42 |

* calculated assuming a mean dry weight:wet weight ratio of 0.25 for whole fish

Stephenson and Turner (1993) calculated a BAF of 170000 L kg-1dw for the amphipod Hyalella azteca in an oligotrophic Canadian lake containing 0.09 µg Cd L-1. The fraction of body burden Cd derived from food (algae) was calculated to be 58 %. This fraction was calculated based on the difference in Cd uptake rate from food only and from food + water. Munger and Hare (1997) found a BAF of 1345 L kg-1dw for the insect Chaoborus punctipennis in a laboratory test. They also studied the relative importance of water and food as Cd sources to the insect. In artificial lake water, a food chain was simulated, composed of the larvae of the insect, its crustacean prey (’eriodaphnia dubia), and the prey's algae food (Selenastrum capricornutum). Animals were exposed to a Cd concentration of 1.1 µg Cd2+ L-1. Chaoborus punctipennis was exposed to both food and water and to food alone during a 14 day exposure period. Cadmium concentration in food, the crustacean prey, was 77 µg Cd g-1dw and remained stable throughout the experimental period. No significant difference in Cd content of the insect between both scenarios was found. This suggests that Cd uptake via the water is negligible for Chaoborus punctipennis.

From the same test it was possible to study the biomagnification. Selenastrum capricornutum exposed to 1.1 µg Cd2+ L-1 had a Cd content of 1110 (g g-1dw and was the food for Ceriodaphnia dubia. Exposure of the latter to the same Cd2+ concentration in the water and to Cd-enriched algae resulted in a body burden of 77 (g g-1dw. Chaoborus punctipennis contained 16 (g Cd g-1dw when fed by Cd-enriched Ceriodaphnia in water containing 1.1 µg Cd L-1. These results suggest no biomagnification of Cd in the lower aquatic food chain.

##### Secondary poisoning within the aquatic compartment

The freshwater shrimp Gammarus pulex was exposed to Cd contaminated mycelium as a sole nutrient source (Duddridge and Wainwright, 1980). The mycelium was grown in a medium containing 1000 (g Cd L-1 for 4 days prior to the feeding experiment.  The shrimps were maintained in a solution containing background Cd or in a solution containing 7 (g Cd L-1. In the latter case, the mycelium fed to the shrimps was not previously contaminated by Cd. A 4-day LC50 value was recorded when feeding the contaminated mycelium (150-170 mg Cd/kgdw) to the shrimp and all shrimps died after 13 days in that treatment. The shrimps exposed to Cd in solution only, survived the treatment better and 50 % mortality was observed at 12 days. The most toxic pathway (water or food) cannot be derived from this study as the food was contaminated at a higher Cd concentration (1000 (g L-1) than that in the solution of the shrimp feeding experiments (7 (g Cd L-1). Another study with Cd in water only revealed a 4-d LC50 of 20 (g Cd L-1 for Gammarus pulex (Williams et al., 1985).

No PNECoral can be calculated for secondary or primary consumers in the aquatic compartment since no NOEC’s were found from feeding studies. Cd uptake through food intake may be more important than uptake from water for some organisms, such as amphipods and insects (Stephenson and Turner 1993, Munger and Hare 1997).

Table 3.2.35: the bioaccumulation factor (BAF) of Cd in freshwater: the Cd concentrations in the organisms are the product of BAf and Cd concentration in water.

| test substance | Organism | medium | test conditions | nominal/ measured | dura tion (d) | Cd water µg L-1 | BAF (L kg-1ww or L kg-1dwa) | references | remark |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| primary consumers |
| CdCl2 | Hyalella azteca | natural sediment and water of oligotrophic soft water lakes (Ontario) | field study; uptake via water + (periphyton) food; alkalinity 98 mg L-1; DOC 601 µmL-1; H 8.3 mg L-1 | M-total | 116 | 0.09 | 170000(a)* | Stephenson and Turner., 1993 | field study |
| Cd-water | Asellus aquaticus Libellulidae Sialis lutaria | Surface water of lakes (Sweden) | Lakes neutral: pH 6.5; H 19 mg CaCO3L-1: Zn 15.2 µg L-1, Cu 4.6 µg L-1, Cd 0.14 µg L-1, Pb 1.8 µg L-1, As 7 µg L-1; Acidified: pH 5.6; H 14 mg CaCO3L-1: Zn 14.4 µg L-1, Cu 2.4 µg L-1, Cd 0.1 µg L-1, Pb 1.4 µg L-1, As 2.6 µg L-1 | M | whole-life | 0.10-0.14 | 65000(a) 41000(a) 27000(a) | Lithner et al., 1995 | field study/BAF’s are arrhythmic means |
| Cd-water | Chaeroborus punctipennis | Canadian lakes | pH 4.62-7.27; H 7.1-74 mg CaCO3L-1; OC 1.29-14.6 mg L-1; Cd 0.017-0.802 µg L-1; Zn 0.523-2.4 µg L-1 | M | whole life | dissolved 0.033 0.021 0.267 0.043 0.354 0.036 0.552 0.802 0.246 0.035 0.036 0.075 0.017 0.127 0.161 0.061 0.023 0.017 0.028 0.045 0.217 0.134 0.251 | 87272(a) 11429(a) 23483(a) 21860(a) 25113(a) 53889(a) 7228(a) 1783(a) 54065(a) 31714(a) 48889(a) 25067(a) 14118(a) 20475(a) 29814(a) 21967(a) 13913(a) 38235(a) 25714(a) 7778(a) 35806(a) 42687(a) 9841(a) | Hare and Tessier, 1996 | field study |
| 109Cd | Chaeroborus punctipennis | Artificial lake water; | T 10°C, H 11.6 mg CaCO3 L-1; food: Ceriodaphnia dubia; Cd background concentration < 0.023 µg L-1 | M | 14 | 1.1 | 1345(b) | Munger and Hare, 1997 | laboratory experiment |
| secondary consumers |
| Cd-water | Perca fluviatilis Esox lucius | Surface water of lakes (Sweden) | Lakes circumneutral: pH 6.5; H 19 mg CaCO3L-1: Zn 15.2 µg L-1, Cu 4.6 µg L-1, Cd 0.14 µg L-1, Pb 1.8 µg L-1, As 7 µg L-1; Acidified: pH 5.6; H 14 mg CaCO3L-1: Zn 14.4 µg L-1, Cu 2.4 µg L-1, Cd 0.1 µg L-1, Pb 1.4 µg L-1, As 2.6 µg L-1 | M | whole-life | 0.10-0.29 | 164000(a)(liver) 27000 (a)(liver) | Lithner et al., 1995 | field study |
| Cd2+water | Perca fluviatilis | River Eman water | field study; liver; | M | whole life | 0.1-0.2 | 64000-32000(a) | Olsson and Haux, 1986 | field study |
| Cd-water | Lepomis macrohirus L. microlophus L. gulosus Micropterus salmoides Pomoxis nigromaculatus Notemigonus crysoleucas Catostomus commersoni Ictalurus nebulosus Amia calvla | Palestina lake, Indiana (US); H= 275-300 mg CaCO3 L-1); shallow lake (2m); moderately contaminated and contaminated sites | field study; whole fish | M | whole life | 0.9 17 0.9 17 0.9 17 0.9 17 0.9 17 0.9 17 0.9 17 17 17 | 111a 182 a 144 a 470 a 167 a 82 a 135 a 64 a 89 a 33 a 213 a 38 a 133 a 117 a 166 a 3.5 a | Murphy et al., 1978 | field study |
| Cd-water | Lepomis. macrochirus | Skinface pond (South Carolina, US); pH 4.6, 6 mg O2 L-1; uncontaminated | field study, whole fish | M | 499 (after stocking) | 0.17 | 240a | Wiener and Giesy, 1979 | field study |
| Cd-water | Cyprinus carpio Barbus plebejus | Sakarya river basin (Turkey); pH ~7; EC 350-850 µS/cm | field study, whole fish, 4 sampling occasions | M | whole life | 0.06-0.6 0.06-0.6 | 340-2300a 280-2500a | Barlas, 1999 | field study |

Table 3.2.36: secondary poisoning of Cd in freshwater

| test substance | Organism | medium | test conditions | nominal/ measured | dura tion (d) | food mg/kgww | EC50 g/kgww | references |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| CdCl2 | Gammarus pulex | Dechlorinated tap water | Semi-static; T 15°C, constant aeration; fed Phytium mycelium | M | 4 21 | 150-170(a) | 150-170 (50) 150-170 (100) | Duddridge and Wainwright, 1980 |

#### The terrestrial compartment

##### Bioconcentration and bioaccumulation factors in soil

Bioconcentration of Cd in the terrestrial compartment is defined as the net result of the Cd uptake, distribution and elimination in an organism due to exposure to Cd in soil only.

Results of cadmium bioaccumulation studies in soil are presented in Table 3.2.38 and a summary of the bioaccumulation factors is given in Table 3.2.37. All BAF values were calculated from the soil:biota concentration ratio’s. Most organisms are earthworms and the Cd levels are expressed on dry or wet weight basis. All the data on earthworms are obtained from specimens with guts voided prior to analysis.

Table 3.2.37: the bioaccumulation factors (BAF's) of soil dwelling organisms.

|  | min | max | median | 5th percentile | n |
| --- | --- | --- | --- | --- | --- |
| earthworms- wet weight basis (kgdw/kgww) | 4 | 32 | 15 | 5 | 11 |
| earthworms- dry weight basis (kgdw/k–dw) | 1.6 | 151 | 15 | 5 | 85 |
| arthropoda - dry weight basis (kgdw/kgdw) | 0.05 | 18.8 | 1.4 | 0.30 | 45 |

Cadmium is concentrated from the soil into earthworms organisms (BAF values all higher than 1). Most important factors affecting the bioaccumulation of Cd by earthworms are the Cd concentration of the soil, soil type, pH, soil organic matter and CEC.

The influence of the Cd content of the soil on the bioaccumulation of Cd is illustrated in most of the studies. Cadmium concentrations in earthworms increase with increasing Cd levels in a non-proportional way (i.e. Wright and Stringer, 1980; Ma, 1982). As a result, the BAF decreases with increasing soil Cd (Figure 3.2.11). Wright and Stringer (1980) compared Cd content in earthworms and soil from pastures near a large Pb and Zn smelting plant and a control area 9-km away. Cadmium concentrations in the earthworms were several times the value in the soil. For all species, the Cd BAF values however were significantly lower at the contaminated site than at the control site. The soil Cd concentration in the contaminated site was 7-9 fold higher than in the control site. Spurgeon and Hopkin (1996) calculated the BAF of Cd for different earthworm species at 22 locations around a primary smelting plant. For all worm species, body burdens increased with increasing soil Cd levels. No evidence was found for species specific accumulation. The BAF values ranged from 2.59 to 115 kgdw/kgdw. There was an inv’rse relationship between the BAF's for earthworms and the concentration of Cd in soils. In addition, soil  pH and OM were found to affect the BAF of Cd for earthworms. Beyer et al. (1982) examined Cd in earthworms (Lumbricidae) from agricultural sites amended with sewage sludge and from experimental control plots. Earthworms from sludge amended sites contained 12 times more Cd than worms from the control sites. The BAF values were lower in contaminated soil than in the control soils. Liming the soil slightly decreased the Cd body burden of the earthworms and high Zn concentrations in soil substantially reduced Cd in earthworms.  Morgan and Morgan (1988) examined Cd content in worms in 12 heavily polluted soils of non-ferrous metalifferous mines. A significant correlation was found between the Cd in earthworm and total Cd content of the soils.  Gish and Christensen (1973) measured Cd content of topsoil and earthworms near 2 highways (Maryland). Cd contents in both soil and worms decreased with increasing distance from the roadways. Andersen(1979) studied Cd uptake by Allolobophora spp. And Lumbricus terrestris in soil receiving sewage sludge. The sludge application reduced the Cd content in the worms whereas soil Cd concentrations were more than doubled by the sludge application.

The influence of soil type, pH, CEC and the organic matter content of the soil was studied by Ma (1982). The body burden of Cd in earthworms was higher in sandy soils (21-35 mg/kgdw) than in loamy soils (12.2-32 mg/kgdw), although the soil concentration of Cd was higher in the latter. The BAF increased with decreasing the pH, CEC and soil organic matter content. The soil pH was the most important soil factor for the BAF.

Hunter et al. (1987a) performed a field study in the vicinity of a major copper refinery housing copper/cadmium alloying plant. Invertebrates from contaminated and semi-contaminated (1 km from the plant) grasslands all showed significant elevation of total body Cd concentrations relative to the control site. Detrivorous soil macrofauna showed accumulation of Cd (10-20 times) with respect to concentrations in refinery site organic surface soil and plant litter. Herbivorous invertebrates showed body:diet concentration factors of 3-5 times. Biotransfer of Cd to carnivorous invertebrates reveals marked differences in Cd accumulation by predatory beetles and spiders. Seasonal changes in the abundance, species composition and age structure of invertebrate populations caused marked variation in Cd contamination levels throughout the year.

Figure 3.2.11: the bioaccumulation factors (BAF kg kg-1) of earthworms as a function of the Cd concentration in soil (mg kg-1)

Table 3.2.38: bioaccumulation factors in soil. The Cd concentrations in the biota are the product of BAF and soil Cd concentration.

| test substance | organism | medium | test conditions | equilibration period (d) | dura tion (d) | soil mg/kgdw | BAF (kgdw/kgww or kgdw/kgdw(a) ) | references | remark |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Cd-soil | Lumbricus terrestris Allolobophora caliginosa Allolobophora tuberculata Allolobophora chlorotica Allolobophora longa Allolobophora rosea | control soil of orchard (Long Ashton); pH 6.5; average biomass 113.7 g/m²; Cd 1 µg/gdw; Pb 92 µg/gdw; Zn 89 µg/gdw Polluted soil of pasture (Severnside); pH 6.8; average biomass 85.8 g/m²; Cd 10 µg/gdw; Pb 147 µg/gdw; Zn 617 µg/gdw | control soil polluted soil control soil polluted soil control soil polluted soil control soil polluted soil control soil polluted soil control soil polluted soil | / | whole life | 1 10 1 10 1 10 1 10 1 10 1 10 | 14.64 5.58 32.45 6.43 17.55 / 14.91 5.65 16.01 3.99 16.27 6.06 | Wright and Stringer, 1980 | field study |
| Cd-soil | Allalobophera sp. + Lumbricus sp. + Octolasium sp. | soil | Bodine soil Captina soil Clairborne soil Emory soil Linside soil Rarklin soil | / | whole life | 0.32 0.2 0.28 0.8 0.28 0.23 | 22.5a 15.5 a 21.8 a 11.6 a 18.2 a 14.8 a | Van Hook, 1974 | field study |
| Cd-soil | Lumbricus terrestris + Lumbricus rubellus + Lumbricus castaneus + Allolobophora caliginosa + Allolobophora chlorotica + Allolobophora rosea | Polluted soil around a primary smelting place; pH 5.56-7.32; OM 15-29.9% |  | / | whole life | / | 2.59(a) 6.11(a) 3.81(a) 6.53(a) 5.99(a) 4.86(a) 23(a) 10.2(a) 11.4(a) 22.8(a) 64.3(a) 13.2(a) 19.8(a) 9.26(a) 32.6(a) 115(a) | Spurgeon and Hopkin, 1996 | field study |
| Cd-soil | Lumbricadea sp. | Landsdale1 loam Hagerstown silt loam Landsdale2 loam Readingston silt loam | control; pH 5.9-6.3 sludge; pH 5.5-6.2 control; pH 5.4-6.4; CEC 9 meq/100g; OM 3% sludge; pH 4.9-6; CEC 13 meq/100g; OM 4.9% control; pH 4.9-6.4; CEC 8 meq/100g; OM 2.5% Sludge; pH 4.6-6.3; CEC 8 meq/100g; OM 2.8% control; pH 5.3-6.1; CEC 10 meq/100g; OM 2.6% sludge; pH 5.5-6.1; CEC 11 meq/100g; OM 3.8% | / | whole life | 0.06 3.8 0.18 0.91/0.55 0.14/0.05 1.9/1.6 0.09/0.08 8.2/5.7 | 66(a) 13(a) 30(a) 20(a) 62(a) 54(a) 40(a) 14(a) | Beyer et al., 1982 | agricultural soil amended or not with sludge |
| Cd-soil | Lumbricus rubellus Dendrodrilus rubidus | Topsoil of control soil and12 heavily contaminated soils of non-ferrous metalliferous mines; pH 4.3-7.8; OC 1-27%; CEC 8-77 meq/100g | control polluted control polluted | / | whole life | 1 0.1-350 1 0.1-350 | 10(a) 80(a)- 1.6(a) 45(a) 100(a)- 5.1(a) | Morgan and Morgan, 1988 | field study |
| Cd-soil | Lumbricus terrestris + Allolobophora chlorotica + Allolobophora trapezoides + Allolobophora turgida | Topsoil along two highways (Maryland): B-W parkway; silt-clay; pH 6.97; OM 4.96-7.3 US-Highway1 ; pH 6.88-6.96; OM 4.8-6.36 | B-W parkway 3 m 6.1 m 12.2 m 24.4 m 48 8 m US-Highway1 3 m 6.1 m 12.2 m 24.4 m 48 8 m | / | whole life | 1.59 0.78 0.68 0.71 0.74 0.95 0.66 0.76 0.65 0.7 | 7.4(a) 13.2(a) 12.7(a) 10.6(a) 11.5(a) 15.2(a) 11.5(a) 10.1(a) 9.7(a) 8.4(a) | Gish and Christensen, 1973 | field study |
| Cd-soil | Allolobophora longa Allolobophora caliginosa Allolobophora rosea Allolobophora chlorotica Lumbricus terrestris | experimental plots: soil 1: K-fertilised; pH 5.9 soil 2: NPK-fertilised (300 kg N/ha); pH 5.7 soil 3 Vejen sewage sludge (30 T/ha containing 14.6 mg Cd/kgdw); pH 5.8) soil 4: Lundtofte sewage sludge (30 T/ha containing 34.1 mg Cd/kgdw ); pH 6 | soil 1 soil 2 soil 3 soil 4 soil 1 soil 2 soil 3 soil 4 soil 1 soil 2 soil 3 soil 4 soil 3 soil 4 soil 1 soil 3 soil 4 | / | whole life | 0.29 0.14 0.65 0.99 0.29 0.14 0.65 0.99 0.29 0.14 0.65 0.99 0.65 0.99 0.29 0.65 0.99 | 40.7(a) 71.4(a) 8.8(a) 9.3(a) 10.6(a) 11(a) 92.8(a) 151.4(a) 16.8(a) 19.8(a) 16.8(a) 16.4(a) 58.3(a) 25.8(a) 8.88(a) | Andersen, 1979 | micrplots |
| Cd-soil | detrivorous invertebrates Collembola Isopoda Diplopoda Oligochaeta Diptera herbivorous insects Orthoptera Formicidae Hemiptera Lepidoptera (larvae) Curculionidae Carnivorous insects Coleoptera Saphylinidae Carabidae predatory larvae Araneida Lycosidae Linyphiidae Opiliones |  | control 1 km site refinery control 1 km site refinery control 1 km site refinery control 1 km site refinery control 1 km site refinery control 1 km site refinery control 1 km site refinery control 1 km site refinery control 1 km site refinery control 1 km site refinery control 1 km site refinery control 1 km site refinery control 1 km site refinery control 1 km site refinery control 1 km site refinery control 1 km site refinery | / | whole life | 0.8 6.9 15.4 0.8 6.9 15.4 0.8 6.9 15.4 0.8 6.9 15.4 0.8 6.9 15.4 0.8 6.9 15.4 0.8 6.9 15.4 0.8 6.9 15.4 0.8 6.9 15.4 0.8 6.9 15.4 0.8 6.9 15.4 0.8 6.9 15.4 0.8 6.9 15.4 0.8 6.9 15.4 0.8 6.9 15.4 0.8 6.9 15.4 | 2.6(a) 1.7(a) 3.4(a) 18.4(a) 18.8(a) 15.0(a) 7(a) 2.1(a) 1.2(a) 5.1(a) 4.9(a) 6.9(a) 2.8(a) 1.0(a) 1.6(a) 0.24(a) 0.046(a) 0.12(a) 1.5(a) 0.8(a) 2.4(a) 1.0(a) 0.5(a) 0.7(a) 0.8(a) 1.0(a) 1.4(a) 0.8(a) 0.5(a) 1.0(a) 0.8(a) 0.7(a) 0.9(a) 0.9(a) 0.8(a) 1.0(a) 2.8(a) 1.2(a) 1.4(a) 3.3(a) 5.0(a) 6.6(a) 3.0(a) 2.7(a) 5.8(a) 3.5(a) 3.7(a) 6.0(a) | Hunter et al., 1987a | field study |
| CdCl2 Cd-soil | Lumbricus rubellus Allolobophora caliginosa | sandy loam soil marine clay loam; sandy loam; riverine clay loam; peaty sand; sandy podzolized soil; plaggen soil; | 17% clay; OM 8%; pH 7.3; CaCO3 5.5%; ; T 15°C moisture content 35-40%: food: dried alder leaves 30% clay; CEC 26.3 meq/100g; OM 5.8%; pH 7.1; 0 T compost/ha 30% clay; CEC 24.5 meq/100g; OM 6.7%; pH 7; 20 T compost/ha 30% clay; CEC 25.1 meq/100g; 8.4%; pH 6.9; 40 T compost/ha 10% clay; CEC 9.4 meq/100g; OM 2.8%; pH 6.6; 0 T compost/ha 10% clay; CEC 10.5 meq/100g; OM 4%; pH 7; 20 T compost/ha 10% humus CEC 12.3 meq/100g; OM 4.9%; pH 7; 40 T compost/ha 40% humus; CEC 26.4 meq/100g; OM 6.9%; pH 5.3; 0 T compost/ha 40% humus; CEC 28.7 meq/100g; OM 9.2%; pH 5.8; 20 T compost/ha 40% humus; CEC 28.7 meq/100g; OM 9.7%; pH 5.9; 40 T compost/ha 10% humus CEC 20.5 meq/100g; OM 12.4%; pH 4.7; 0 T compost/ha 10% humus CEC 19.2 meq/100g; OM 11.2%; pH 5.2; 20 T compost/ha 10% humus CEC 18.3 meq/100g; OM 13.6%; pH 5.8; 40 T compost/ha 7% humus CEC 13.5 meq/100g; OM 6.4%; pH 5.4; 0 T compost/ha 7% humus CEC 12.7 meq/100g; OM 7.4%; pH 5.4; 20 T compost/ha 7% humus CEC 23.2 meq/100g; OM 8.1%; pH 5.7; 40 T compost/ha 3% humus CEC 5.3 meq/100g; OM 2.8%; pH 4.8; 0 T compost/ha 3% humus CEC 6.1 meq/100g; OM 3.7%; pH 5.5; 20 T compost/ha 3% humus CEC 7.1 meq/100g; OM 4.3%; pH 6; 40 T compost/ha | / up to 1 decade | 84 whole life | 0.5 20 150 1 1.4 1.5 0.6 0.7 1 1.1 1.5 2 0.23 0.57 0.81 0.27 0.56 0.82 0.22 0.54 0.62 | 32(a) 5(a) 2.7(a) 12.3(a) 10.7(a) 11.3(a) 26.2(a) 30.4(a) 17.5(a) 15.3(a) 13.6(a) 15.9(a) 112.2(a) 60.9(a) 40.5(a) 79.6(a) 42.6(a) 30.7(a) 140(a) 59.4(a) 40.5(a) | Ma, 1982 | Laboratory study Field study |

##### Secondary poisoning within the lower terrestrial foodchain

Russell et al. (1981) studied Cd toxicity to Helix aspersa by feeding with Cd-enriched food during 30 days. The Cd concentration in tissue increased with increasing Cd content of the food.  Reproduction was unaffected by the Cd in food up to 10 mg/kgdw (concentration in food). Reproduction was significantly reduced at 25 mg/kgdw.

A case study on Cd bioaccumulation in the lower food chain was made for the plant (wheat)-insect (aphids)-predator (lacewings) pathway (Merrington et al., 2001).  A low Cd soil was fertilised with high Cd P fertiliser and Cd concentrations, resulting in higher Cd in soil and in wheat shoots. Aphids feeding on the wheat plants of the fertilised soil had 3 times higher Cd concentrations than those feeding on the control plants.  However, lacewings showed no significant accumulation of Cd and no differences in larval performance were recorded. This illustrates that this pathway does not lead to Cd bioaccumulation.

No PNECoral will be derived for lower terrestrial organisms due to lack of sufficient data and because secondary poisoning is assessed for organisms of a higher trophic level (mammals and birds).

Table 3.2.39: secondary poisoning in soil.

| test substance | organism | medium | test conditions | endpoint | nominal/ measured | dura tion (d) | NOEC mg/kgdw | LOEC mg/kgdw | ECx(50 mg/kgdw | references |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| CdCl2 | Helix aspersa | moist quartz sand covered by a piece of woven glass towel; food: ground Purina Lab-Chow supplemented with CaCO3; |  | shell growth reproduction | N | 30 | 25 10 | 100 (20) 25 (28) | 300 (95) 50 (69) | Russell et al., 1981 |

#### The sediment compartment

##### Bioaccumulation in sediment

Most of the BAF’s of benthic organism are lower than 1 (either fresh weight based or dry weight based, Table 3.2.40). The BAF’s are smaller for vertebrates than for invertebrates. The BAF’s of benthic organism are generally smaller than BAF’s for soil-invertebrate transfer (Fig. 3.2.11). Data on marine organisms indicate larger BAF values than given here (details not shown). However, BAF values of marine organisms are not used in this risk assessment.

Table 3.2.40: the  BAF values of some benthic organisms

|  | min | max | median |
| --- | --- | --- | --- |
| invertebrates, wet weight (kgdw/kgww) | 0.38 | 0.44 | 0.43 |
| invertebrates, dry weight (kgdw/kgdw) | 0.01 | 1.15 | 0.28 |
| vertebrates, wet weight (kgdw/kgww) | 0.006 | 0.18 | 0.07 |

The body burden Cd generally increases with increasing Cd concentration in the sediment but levels off at higher Cd contents of the sediment (Francis et al, 1984). Low BAF values can therefore be found at high Cd concentrations in the sediment. The Cd concentratipproachr oligochaete Lumbricus variegatus were similar in field contaminated sediments, containing about 5 (g Cd g-1dw, and in sediments spiked up to 750 (g Cd g-1dw (Ankley et al., 1994; Peterson et al, 1996). The BAF values therefore differ by more than one order of magnitude between both systems. These observations were made for two different sediments (one from a pond, the other from a river) and differences in metal immobilisation between the sediments may explain different Cd availability in the sediments.

The influence of contact time in the sediment on the BAF was illustrated by data of Francis et al. (1984). Cd accumulation and toxicity in fish (largemouth bass) and amphibian (leopard frog) was measured in embryo-larval stages. Largemouth bass accumulated, at all sediment concentrations, significantly more Cd than leopard frog. The differences in BAF’s between the species were attributed to differences in contact time of the organisms with the sediment.  Bass eggs and larvae have direct contact with sediment throughout the exposure period whereas goldfish and leopard frog dwell in the water column above the sediment.

The BAF’s collected in this review are based on a maximal exposure time of 50 days and may underestimate longer-term BAF values.

Van Hattum et al. (1993) studied the influence of temperature and pH on the uptake of Cd in Asellus aquaticus. No significant pH effects on Cd uptake were observed. Increasing temperature from 5-20°C, however, significantly increased Cd uptake about fourfold.

Table 3.2.41: bioaccumulation of Cd in benthic organisms

| test substance | organism | medium | test conditions | Nominal/ Measured | Equilibration period (d) | Dura tion (d) | Sediment mg/kgdw | BAF (kgdw/kgww or kgdw/kgdw(a) ) | references |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Cd-sediment | Lumbricus variegatus | contaminated sediment from lower Fox river (Wisconsin) | 40-60gdw sediment + Lake Superior water; T 22°C; semi-static; Cu 64-90 mg/kgdw; Zn 208-347 mg/kgdw; Pb 102-150 mg/kgdw; Cr 71-118 mg/kgdw; no food addition | M-total | 1 | 30 | 5.2 4.1 5.8 | 0.38 0.44 0.43 | Ankley et al., 1994 |
| CdCl2 | Lumbricus variegatus | Cd spiked natural sediment of small mesotrophic pond(Minnesota); 0.74 µmol/gdw SEM and 4.6 µmol S/gdw | org. density 10000 org/m² SEM/AVS = 0.4 SEM/AVS = 0.8 org. density 25000 org/m² SEM/AVS = 0.4 SEM/AVS = 0.8 | M-total | 11 | 14 | 450 754 382 714 | 0.02a 0.03a 0.01a 0.01a | Peterson et al., 1996 |
| Cd-sediment | Asellus aquaticus | natural sediment from the polluted lake Ketelmeer and the uncontaminated lake Oostvaardersplassen (Npproachs) + mixture of tap and deionized water; 100 gww sediment + 400 ml water | semi-static; lake Ketelmeer: 2% OC; 1% clay, 13% silt; Pb 48 mg/kgdw; Cu 27 mg/kgdw; Zn 319 mg/kgdw; Fe 5100 mg/kgdw; T 5°C T 10°C T 20°C pH 5 (T 20°C) pH 8 ( T 20°C) lake Oostvaarders plassen: 5% OC; 8% clay, 70% s ilt; Pb 84 mg/kg dw; Cu 25 mg/kgdw; Zn 221 mg/kgdw; Fe 16400 mg/kgdw; T 5°C T 10°C T 20°C | M-total | 7 | 50 | 5.3 5.3 5.3 5.3 5.3 1.2 1.2 | 0.28 a 1.02 a 1.15 a 1.1 a 1 a 0.25 a 0.5 a 0.5 a | Van Hattum et al., 1993 |
| CdCl2 | Rana pipiens Micropterus salmoides | natural stream sediment; 250 gdw sediment pproachd-solution or distilled deionized water (control) +350 ml reconstituted water | DO 6.6-8.1 mg/L, T 22.1-22.5 °C, pH 7.9-8.4; sed: OM 2.3%, CdT 1.02 mg/kg, ZnT 108.2 mg/kg, HgT 0.052 mg/kg, FeT 5.52%; 5.52% sand, 35.4% silt, 12% clay | M | 0.42 | 7 | 1 10 100 1000 1 10 100 1000 | 0.08 0.034 0.0031 0.013 0.18 0.072 0.15 0.006 | Francis et al., 1984 |

dw: dry weight basis, ww: wet weight basis; a dry weight basis; SEM: simultaneously extractable metals. This is the sum of the metals cadmium, lead, nickel, zinc and copper in the sediment simultaneously extracted with the AVS and is expressed in µmol/gdw.; equilibration period: time of equilibration after spiking the pristine sediments or time of stabilisation after mixing the contaminated sediment and water, prior to exposure’.

#### Toxicity to mammalian and avian organisms

##### Derivation of the PNECoral

The TGD suggested method for risk assessment of secondary poisoning is based on modelling critical pathways such as the soil-worm-bird or water-fish-bird food chains (Romijn et al., 1994).  The PNECoral for mammals and birds is derived from feeding studies with Cd salt spiked diets.  Nine feeding studies have been selected here (Table 3.2.43).  This compilation is based on sub-chronic and chronic studies and has excluded acute studies, mixed metal feeding studies and experiments where Cd was injected in the test animals. Four studies were selected with birds and 5 studies with mammals.

The PNECoral can be calculated from the lowest NOEC using an assessment factor. The assessment factors for the feeding test are based on the TGD (TGD, 1996, p.350) and are 10 for the 90 day feeding test with mallard ducks (reproduction as endpoint) and 10 for the chronic study with monkey. The PNECoral could also be calculated using statistical extrapolation.  The underlying assumption is a log-logistic distribution of species sensitivity to dietary Cd (Table 3.2.42). This approach has been used in the risk assessment of secondary poisoning of Spurgeon and Hopkin (1996) and Smit et al. (2000).  No species mean NOEC’s are calculated from the 2 studies with either rats and mallard ducks.  The 2 studies on rats were performed with very different exposure time and the studies with mallard ducks have different endpoints. Averaging per species increases the HC5 (50 and 95 % confidence) of the mammal+bird data (not shown).

Table 3.2.42: Calculation of PNECoral  (mg kg-1 food) using the assessment factor method (AFM) or the statistical extrapolation method (SEM; Aldenberg and Slob, 1993)

|  | AFM | SEM |
| --- | --- | --- |
|  | NOEC/AF | HC5 at 50% (and 95%) confidence | significance* |
|  | mg kg-1 food |  |
| Mammals (n=5) | 0.30 | 1.9 (0.14) | *** |
| Birds (n=4) | 0.16 | 0.75 (0.007) | *** |
| Combined (n=9) | 0.16 | 1.6 (0.35) | *** |

*goodness of fit, *** is significant at 1% level of significance

- The assessment factor method invariably leads to the lowest PNECoral. There is currently no guideline in the TGD to use the statistical extrapolation method to derive a PNECoral and it is proposed to use the AF method as a first approach to assess secondary poisoning.

The suggested PNECoral is therefore calculated as the lowest NOEC in the database and using and AF of 10, yielding

PNECoral = 0.16 mg/kg fresh weight

and is expressed as the fresh weight based Cd concentration in the food of the predator. Note that this PNEC is situated at the lowest NOEC of this database and which is the NOEC of the feedings studies with mallard ducks discussed above.

Table 3.2.43: mammalian and avian toxicity data from laboratory feeding studies. Concentrations are expressed per unit fresh weight of the food. Bold and underlined NOEC data are used to estimate the HC5.

| test substance | organism | medium | duration (d) | Endpoint | NOEC (mg Cd/kg) | cat* | LOEC (mg Cd /kg) (%effect) | references |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| mammals |
| CdCl2 | 2-5 y old rhesus monkey Macaca mulatta | pelleted food | 3280 (9 y) | growth | 3 | 1 | 10 ((25) | Masaoka et al., 1994 |
| CdCl2 | 8 wk old Yorkshire barrows (pig) Sus scrofa domesticus | diet: mixture of yellow corn, soybean meal, meat and bone meal, dehydrated alfalfa meal, trace minerals and vitamins | 42 | growth | 50 | 1 | 150 (60) | Cousins et al., 1973 |
| CdCl2 | 4 m old lamb Ovis amon aries | diet: mixture of primary corn, cotton seed hulls and soybean oil meal | 191 | growth | 15 | 1 | 30 (20) | Doyle et al., 1974 |
| CdCl2 | rat Rattus norvegicus | basal animal diet: Altromin-R, powdered | 728 (2y) | grth | 10 | 1 | 50 | Löser, 1980 |
| CdCl2 | 5 wk old rat Rattus norvegicus | basal diet: wheat flour, casein, lard, minerals and vitamins | 56 | growth | 15 | 2 | 30 (8) | Groten et al., 1991 |
| birds |
| CdCl2 | first-year adult mallard duck Anas platyrhynchos | commercial duck breeder mash coated with Cd dissolved in propylene glycol | 90 | spermatogenesis | 1.6 | 1 | 15.2 | White et al., 1978 |
| CdCl2 | 1 d old mallard duckling Anas platyrhynchos | food | 84 | kidney lesion haemoglobin concentrations | 10 10 | 1 | 20 20 | Cain et al., 1983 |
| CdSO4 | 6 m old White Leghorn laying hen Gallus dometicus | purified soybean-glucose diet | 28 | egg production | 12 | 1 | 48 (39) | Leach et al., 1978 |
| CdCl2 | Japanese quail (after hatching) Coturnix c. japonica | purified basal diet (35% soybean protein) | 42 | growth | 38 | 2 | 75(15) | Richardson et al. 1974 |

*NOEC classification (see section 3.2.0.2)

The risk of secondary poisoning of fish eating birds by Cd is predicted to be smaller than the direct effects of Cd in the aquatic environment (section 3.3).  This is readily demonstrated using BCF’s of fish in Table 3.2.34.  Cadmium concentrations in whole fish at the proposed PNECwater = 0.19 µg Cd/l (section 3.2.1.7) is predicted to range between 0.0001 and 0.12 mg Cd/kg fresh weight using the whole range of BCF’s (0.5-623 l/kg fresh weight, Table 3.2.34a&b). These Cd concentrations are below the PNECoral for birds or birds+mammals.  This assessment is made for freshwater systems and not for marine environments.  Nephrotoxic lesions ascribed to Cd have been found in sea birds from areas that are relatively uncontaminated and where natural Cd may be the source (Nicholson et al., 1983; IPCS, 1992b).  We propose that our assessment should not be used for the marine environment where the bioaccumulation of Cd differs from that in freshwater dominated systems.

The risk of secondary poisoning in the soil-worm-bird/mammal is predicted to be far more critical than the risk of soil Cd affecting plants, invertebrates or micro-organisms. This is readily demonstrated using the BAF’s of Cd in earthworms (Table 3.2.37). Cadmium concentrations in earthworms at the proposed PNECsoil = 2.3 mg Cd/kg (section 3.2.2.7) is predicted to range between 9.2 and 74 mg Cd/kg fresh weight using the whole range of BCF’s (4-32 kg/kg fresh weight, Table 3.2.37). All these concentrations are above the PNECoral of birds, mammals or birds+mammals and even overlap the LOEC range of the feeding studies.

The model for secondary poisoning of mammals and birds in the soil-worm-birds/mammals may, however, be questioned in case of Cd: concentrations of Cd in earthworms sampled in uncontaminated areas typically range between 1-10 mg Cd/kg fresh weight (Table 3.2.38) and are generally higher than the PNECoral proposed here.  It is either possible that soil Cd at background is indeed at risk for carnivorous mammals and birds or it is possible that the model that compares earthworm Cd with dietary Cd in feeding studies is overprotective.  Beyer (2000) concluded on this approach that ‘assessors have been overly cautious in evaluating toxicity of Cd’. Spurgeon and Hopkin (1996) used this model for risk assessment of secondary poisoning by Cd in the vicinity of a smelter and concluded that ‘it is unlikely to describe risk to predators correctly’. Spurgeon and Hopkin (1996) have argued that the model is overly protective because of

- the problems of quantifying the BAF: a mean BAF would overestimate earthworm concentrations at more contaminated sites because the BAF decreases with soil Cd (see, for example, Figure 3.2.11).

- higher availability of Cd in metal salt spiked meals in the laboratory tests than Cd in worms

- use of unrepresentative species for the predators

Other authors suggest that the model is not sufficiently protective and that additional safety factors should be used to account for differences in metabolic rate between laboratory and field animals, differences in caloric content between the laboratory diets and field prey, differences in food assimilation efficiency, differences in bioavailability of the toxic compound etc. (see Smit et al., 2000 for references).

One of the key assumptions in the model is that equal food Cd concentration leads to equal effects in laboratory animals and field animals.  None of the laboratory tests reviewed here have fed earthworms to the animals as the principal source of Cd.  Earthworms from even uncontaminated areas have Cd concentrations close to effect concentrations in Cd salt spiked laboratory meals.  The assumption of equal effects at equal total Cd intake can be tested indirectly by comparing internal Cd dose (body burden) between laboratory and field animals at equal Cd intake.  This comparison will be made here.

Cadmium intake by wildlife is probably most documented in shrews (Sorex araneus) because this mammal usually has a high Cd body burden (Hunter et al., 1989). Shrews have a high dietary Cd intake rate and feed on invertebrates active at the ground surface supplemented with soil dwelling macrofauna (Hunter et al., 1987b).  Earthworms can be the major source of dietary Cd in shrews ( Ma et al., 1991).  Kidney Cd concentrations up to 550 mg kg-1 dry weight have been observed in shrew (Hunter et al., 1989), i.e. close to critical concentration (see next section).  Data on cadmium intake rates and body burden Cd have been compiled by Shore and Douben (1994) from 4 different studies.  Kidney Cd concentrations increase with increasing Cd intake rate. This increase is linear at low intake rate but levels off at higher intake. Shore and Douben (1994) combined the data from four different studies and found a significant linear relation between the logCd intake rate and the kidney Cd (Fig. 3.2.12, P<0.015).  A laboratory feeding trial has been performed with shrew fed a CdCl2 spiked diet (Dodds-Smith et al., 1992a&b).  The body burden Cd (kidney Cd) after only 11 weeks exposure at the high Cd diets is significantly above that predicted by the log-linear regression line on field animals (Fig. 3.2.12).  A drawback in this analysis is the extrapolation from the regression line since Cd intake rate in the laboratory trials is about fourfold higher than the highest Cd intake rate recorded in field shrew. Taken together, this analysis suggests that Cd is more available in laboratory spiked meals than in the diet of field animals.

A recent feeding study compared Cd availability to cattle from hay grown on a smelter affected substrate with hay spiked with Cd salts (spiking at corresponding concentrations).  The kidney Cd of cattle fed hay grown on the smelter affected substrate was 3-fold above that of control animals whereas it was increased 12 fold in the Cd spiked hay treatment (Stuzynski et al., 2000). Clearly, Cd availability is higher in Cd salt spiked meals than in dietary Cd.

These arguments suggest that risk of secondary poisoning by Cd may be overestimated when based on Cd salt feeding studies.  Therefore, an alternative approach will be used based on renal thresholds.  The TGD allows that field data are used in this type of risk assessment provided that interpretation is made with caution (TGD 1996, p. 346). This effects assessment will only be made for mammals for which dose-response curves can be established.  The assessment for terrestrial birds will be discussed in the risk characterisation because there no paired data of soil Cd /kidney Cd for birds were found.

Fig. 3.2.12: Cd intake and kidney Cd in free living common shrew (S. araneus) and in laboratory cultivated shrew (control and Cd salt spiked diet).  The log-linear regression and 95% prediction interval is made on field animal data (compilation of Shore and Douben, 1994).  Data of laboratory animals is derived from Dodds-Smith et al. (1992 a&b).

##### An alternative approach for wildlife in the terrestrial environment based on renal thresholds

The alternative strategy to estimate the risks of secondary poisoning by Cd using renal threshold was formulated by Spurgeon and Hopkin, 1996.  This strategy was not elaborated in that paper but this method was already adopted in pathway calculations of the US-EPA 503 sludge regulations (Chaney and Ryan, 1991).

The alternative method uses kidney Cd concentrations of wildlife as an indicator of Cd exposure and risk.  The kidney is regarded as the critical organ in chronic Cd toxicity.  With continued exposure, there is a continual increase in Cd concentration in the renal cortex  until a critical value is reached and histopathological changes and renal dysfunction is found (proximal tubular cell necrosis, proteinuria and glycosuria; Scheuhammer, 1987 and references therein).  This critical value should be regarded as a sublethal endpoint. The risk of secondary poisoning will be assessed by calculating the exposure at which this critical value is not exceeded for wildlife.

The proposed approach overcomes the uncertainties in the traditional approach which uses foodchain modelling (i.e. soil-worm-mammal modelling) because the proposed approach does not require assumptions about the diet (e.g. 100% earthworms) and about Cd bioavailability during transfer soil-food-wildlife (i.e. the BAF value and assumption of equal exposure at equal diet Cd between spiked meals and environmental Cd).

The ecological relevance of kidney damage as the critical endpoint in this assessment deviates from traditional endpoints such as growth or reproduction which have obvious ecological relevance. Indeed, the relationship between ecological fitness and kidney damage is unknown and which is the major difficulty in understanding effects of Cd in wildlife (Cooke and Johnson, 1996). The kidney has spare functional capacity and proteinuria or calciuria might be tolerated without progression to renal failure (Cooke and Johnson, 1996). Seabirds showing signs of nephrotoxicity were ‘outwardly healthy’ (Nicholson et al., 1983).  A beaver population from the Mulde (a tributary of the Elbe in Germany) had average kidney Cd concentrations of 467 (g/g dw (above the threshold proposed below).  The fertility of this population was higher than 3 other population that had lower kidney Cd concentrations (Nolet et al., 1994).  The authors conclude that the habitat quality seemed to determine the fertility and that Cd did not seem to interfere with fertility.  Kidney damage in shrews (S. araneus) caught in a polluted smelter site was identified by electron microscopy although urine analyses showed no evidence for clinical renal dysfunction and animals were ‘in good condition’ (data of Hunter, 1984, quoted in Cooke and Johnson, 1996).

Dietary deficiencies can exacerbate Cd toxicity and one example was found where effects in wildlife due to Cd was related to kidney damage (as judged from exceedance of critical kidney Cd concentrations) and which was related to Ca deficiency (see bottom of this section: field validation). Therefore, we propose to use renal dysfunction as an endpoint with ecological relevance, realising that this endpoint leads to a more conservative approach than traditional endpoints in most conditions.

Kidney Cd of wildlife such as shrews, moles and badgers is markedly increased at sites with elevated Cd (Ma,1987; Ma and Broekhuizen,1989; Ma et al.,1991; Hendriks et al.,1995).  Some of the wildlife field data do allow to estimate a dose (soil Cd) response (kidney Cd) slope.  The critical soil Cd that is needed to reach the critical kidney Cd can be calculated with this slope.  This critical soil Cd (Cdsoil,crit) could then be considered as an acceptable concentration in soil assessed for secondary poisoning.  This approach would only yield assessments based on animals for which kidney Cd data are available at different Cd exposure.  Alternatively, critical soil Cd concentrations could also be derived based on a proportional extrapolation from any paired set of soil/kidney Cd concentration data, allowing to include more species in the assessment.  Fig. 3.2.13 illustrates this approach.  The proportional extrapolation method contains a safety factor since kidney Cd only increases proportionally with the dose at low concentrations. The less than proportional increase of kidney Cd with soil Cd is observed in most studies and may be explained by e.g. avoidance or metal interactions for Cd absorption (most gradient studies are derived from sites with mixed metal pollution).

Kidney-Cd concentrations of wildlife are compiled in Table 3.2.44.  The data are mean or median Cd concentrations for 9 different mammal species (no data found for birds). Paired sets of soil Cd/kidney-Cd were found for 8 mammal species.  Most of these studies have measured Cd concentrations at 2 or more locations differing in metal exposure (smelters).

Fig. 3.2.13: Two methods to estimate the critical Cd in soil (arrows) that would lead to critical Cd concentrations in the kidney of mammals: proportional extrapolation based on one data point (here: at lowest soil Cd) or extrapolation from a regression line fitted to all data. Data from Cd in common shrew (S. araneus) in a transect study (Hunter et al., 1989).

Table 3.2.44:.Kidney Cd concentrations in mammals and predicted critical soil Cd concentrations at which renal threshold (K-Cd) may be exceeded. Predictions are based on proportional extrapolation (Fig. 3.2.13).  Bold and underlined data are used for risk assessment.

| species | site | soil pH | soil Cd µg/g | kidney Cd µg/g dw | predicted critical soil Cd (µg/g) | reference: | remark |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | critical K-Cd 200 µg/g dw | critical K-Cd 400 µg/g dw |  |  |
| badger | Meles meles | NL |  |  | 9-213 49-405 |  |  | Ma and Broekhuizen, 1989 | n=15; 4-5 y old animals, habitat not close to floodplains of Meuse n=9; 4-5 y old animals, habitat close to floodplains of Meuse |
| beaver | Castor fiber | NL DE DE DE DE |  | 24 - - - - | 55(113 in adults) 467 50 30 20 | 42.5 - - - - | 85 (adults based) - - - - | Nolet et al., 1994 | soil:0-5 cm; Biesbosch estuary; young animals-modelling predicts K-Cd = 113 mg/kg dw in adults Elbe region: Mulde (adults) Elbe region: Elbe (adults) Elbe region: Elbe (adults) Elbe region: Heide (adults) |
| common shrew | Sorex araneus | UK | 5.2 5.4 4.4 5.05 4.9 4.85 | 0.6 1 2 1.7 3.3 19.9 | 10.9 37 9.3 41.3 154 142 | 11.0 5.4 43.0 8.2 4.3 28 | 22.0 10.8 86.0 16.5 8.6 56.1 | Read and Martin, 1993 | soil: litter layer; K-Cd in mature animals |
| common shrew | Sorex araneus | UK |  | 0.8 6.9 15.4 | 20.5 156 253 | 7.8 8.8 12.2 | 15.6 17.7 24.3 | Hunter et al.1989 | soil: 0-5 cm |
| common shrew | Sorex araneus | UK |  | 0.75 3.1 8.5 | 25.7 139 193 | 5.8 4.5 8.8 | 11.7 8.9 17.6 | Hunter and Johnson, 1982 | soil: 0-5 cm |
| common shrew | S. araneus | NL | 6.1 3.5 | 2.9 0.3 | 126-200 14-51 | 2.9 1.2 | 5.8 2.4 | Ma et al., 1991 | soil: 0-10 cm, Ao horizon Cd is 5.5 µg/g; range of means in season soil: 0-10 cm, Ao horizon Cd is 1.2 µg/g; range of means in season |
| common shrew | Sorex araneus | NL |  | 1.8 6.4 | 11 21 | 32.7 61.0 | 65.5 121.9 | Hendriks et al., 1995 | soil:0-20 cm; Rhine floodplains |
| cottontail rabbit | Sylvilagus floridanus | U.S. |  | ~6 ~60 ~10 | 166 380 284 | 7.2 31.6 7.0 | 14.5 63.2 14.1 | Storm et al., 1994 | Palmerton site; soil: A1 horizon |
| cottontail rabbit | Sylvilagus floridanus | U.S. |  | 0.1 0.4 | 5.3 12.3 | 3.8 6.5 | 7.5 13.0 | Dressler et al., 1986 | soil: 0-15 cm soil: 0-15 cm; soil received sludge |
| field vole | Microtus agrestis | UK |  | 0.8 6.9 15.4 | 1.7 23.9 88.8 | 94.1 57.7 34.7 | 188.2 115.5 69.4 | Hunter et al.1989 | soil: 0-5 cm |
| field vole | Microtus agrestis | UK |  | 0.75 3.1 8.5 | 1.3 4.06 23.3 | 115.4 152.7 73.0 | 230.8 305.4 145.9 | Hunter and Johnson, 1982 | soil: 0-5 cm |
| field vole | Microtus agrestis | NL | 6.1 3.5 | 2.9 0.3 | 1-3 0.1-0.3 | 193.3 200.0 | 386.7 400.0 | Ma et al., 1991 | soil: 0-10 cm, Ao horizon Cd is 5.5 µg/g; range of means in season soil: 0-10 cm, Ao horizon Cd is 1.2 µg/g; range of means in season |
| mole | Talpa europea | NL | 5.2 6 6.5 4.1 4 | 1.7 6 9.2 0.3 0.1 | 112 224 221 186 59 | 3.0 5.4 8.3 0.3 0.3 | 6.1 10.7 16.7 0.6 0.7 | Ma, 1987 | soil: 0-10 cm; Budel pasture soil: 0-10 cm; Budel heath site soil: 0-10 cm; Arnhem pasture |
| mole | Talpa europea | FI |  |  | 186 82 |  |  | Pankakoski et al., 1993 | Helsinki metropolitan area, adult animals only rural area, adult animpproacy |
| pygmy shrew | Sorex minutus | UK | 5.2 5.4 4.4 5.05 4.9 4.85 | 0.6 1 2 1.7 3.3 19.9 | 7.9 5.9 7.9 12.1 18.7 49.9 | 15.2 33.9 50.6 28.1 35.3 79.8 | 30.4 67.8 101.3 56.2 70.6 159.5 | Read and Martin, 1993 | soil: litter layer; K-Cd in mature animals |
| white-tailed deer | Odocoileus virginianus | U.S. |  | 6-100 | 70 | 17.1 | 34.3 | Storm et al., 1994 | Palmerton site; soil A1 horizon |
| woud mouse | Apodemus sylvaticus | UK |  | 0.8 6.9 15.4 | 2 8.5 41.7 | 80.0 162.4 73.9 | 160.0 324.7 147.7 | Hunter et al.1989 | soil: 0-5 cm |
| woud mouse | Apodemus sylvaticus | UK |  | 0.75 3.1 8.5 | 1.46 5.5 7.4 | 102.7 112.7 229.7 | 205.5 225.5 459.5 | Hunter and Johnson, 1982 | soil: 0-5 cm |

###### Critical concentration of Cd in kidney

There are several reviews of the critical kidney Cd concentrations in laboratory animals (IPCS, 1992a), small mammals (Cooke and Johnson, 1996) and birds (Furness, 1996).  The individual studies will not be discussed here but attention will be given to the conflicting evidence that has suggested lower limits.

The WHO has reviewed several studies on test animals (mouse, rat, rabbit, pig, horse, monkey and bird; IPCS, 1992a).  Histological tubular lesions are usually observed at 200-300 µg Cd/g wet weight.  In some studies on rats, monkeys, horses and birds certain effects were seen at lower levels.  The WHO concludes that ‘if one wishes to establish a range of values for the critical concentration in individuals at which a small but significant part of the exposed population will show effects, animal studies indicate that a renal cortex level of about 100-200 µg/g wet weight is likely to coincide with such a range’ (IPCS, 1992a).  This range corresponds with whole kidney, dry weight based values of 400-800 µg/g dw (wet weight concentrations are about 0.2 time dry weight concentrations and whole kidney concentrations are about 0.8 times kidney cortex values).

There are reports of kidney damage in wildlife at concentrations below the range suggested by WHO.  Nicholson et al. (1983) identified nephrotoxicity in seabirds at whole kidney concentrations of 100-200 µg/g dw, about fourfold lower than the WHO criterion.  Kidney ’s, however, also contained Hg (5-15 µg/g dw).  Starlings were injected CdCl2 and showed similar kidney lesions compared to the seabirds at comparable tissue Cd concentrations.  However, the Cd dosed animals may not be representative for the seabirds because of the acute exposure of the test animals.  Chmielnicka et al. (1989) suggested that the WHO criterion should be revised after identifying nephrotoxicity in Cd dosed rats at kidney Cd concentrations of 30 (g/g wet weight (about 120 (g/g dw).  However, this study was also based on an acute dose (injections during 8 weeks and histopathological effects in the liver after only 2 weeks), suggesting that it may not be relevant for a realistic chronic exposure (Beyer, 2000).  Leffler and Nyholm (1996) reported nephrotoxicity in bank voles (Clethrionomous glareolus) collected close to the smelter in Rönnskärsverken (Sweden) and in a control site. The voles from the contaminated area had increased proteinuria and increased kidney Cd concentrations.  The proteinuria was identified at only 4 µg/g wet weight (whole kidney, about 20 µg/g dw).  A comment on that paper was written by Elinder (1997) about the very low value at which nephrotoxicity was found. Elinder concluded that this study was confounded, basically because the voles urinated more in the contaminated site.  The authors have responded to this comment that other factors (other metals, biotope characteristics) may also have been involved in the proteinuria (Nyholm and Leffler, 1997).

We propose to use the lower limit of the WHO suggested critical range of Cd concentration for our assessment, i.e. 100 (g Cd/g wet weight in the renal cortex or 400 (g Cd/g dw.  The WHO suggested range is based on the largest review of animal data and Cooke and Johnson (1996) similarly suggested  100 (g Cd/g wet weight as a critical concentration.  This RAR repeats the WHO conclusions that mean renal cortex Cd should reach 200 µg/g wet weight to observe tubular proteinuria (section 4.1.2.6.3: studies in animals). There is indeed conflicting evidence suggesting lower limits (Nicholson et al., 1983, Chmielnicka et al., 1989 and Leffler and Nyholm, 1996) but there are arguments that these studies may be less relevant for chronic exposure to Cd-only contamination in wildlife (see above).

###### Critical soil Cd concentrations for wildlife

The critical soil Cd concentration is defined as that concentration at which a critical kidney Cd concentration of 400 (g/g dw (whole kidney) is predicted using a proportional extrapolation from each paired soil/kidney Cd concentration set (Fig. 3.2.13).  The lowest critical soil Cd concentration was selected from each transect study or when only a range in soil or kidney Cd concentrations was available (Table 3.2.44).  Different values were derived from the studies of Ma because the soil properties were markedly different between sites, clearly leading to different Cd exposure (Table 3.2.44). Twenty (20) values of critical Cd concentrations were derived from 8 different mammal species.  The frequency distribution of the 20 values illustrates that moles and shrews typically have high kidney Cd concentrations which is related to the high Cd intake rate (Fig. 3.2.14).

This compilation of field data will be used to derive a critical soil Cd concentration for terrestrial mammals (Cdsoil, crit).  We propose to derive this value with statistical extrapolation. The distribution of values (Fig. 3.2.14) reflects site specific species sensitivity if it is assumed that there are no differences in renal threshold between species.  In this regard, this distribution is conceptually equal to a distribution of Cd thresholds from toxicity tests in soil.

Fig. 3.2.14 Cumulative frequency of the critical soil Cd concentration at which the critical kidney Cd concentration (400 µg/g dw) may be exceeded in the average population of different species.  The line is the log-logistic curve fitted on all individual data.

Table 3.2.45: prediction of critical soil Cd for terrestrial mammals based on values at which the critical kidney Cd concentration (400 µg/g dw) may be exceeded in the average population of different species.  The critical soil concentrations is either the lowest value in the database or the HC5 predicted by statistical extrapolation (Aldenberg and Slob, 1993)

|  | lowest value | Statistical extrapolation (log-logistic model) |
| --- | --- | --- |
|  |  | HC5 at 50% (and 95% confidence interval) | significance* |
|  | Critical soil Cd (µg/g) |  |
| all data selected in table 3.1.2.44 (n=20) | 0.6 | 0.9 (0.2-2.3) | *** |
| Excluding data from soils with pH < 4.2 (n=16) | 5.8 | 3.3 (1.0-7.1) | *** |
| Geometric means of species (n=8) | 1.4 | 1.5 (0.1-5.7) | *** |

*goodness of fit, *** is significant at 1% level of significance

The statistical extrapolation method (log-logistic distribution) predicts that the HC5 for protecting mammals is 0.9 (g/g.  The HC5 is higher when based on species mean values.  Averaging data is not defensible: the data of Ma, 1987 (moles) and Ma et al., 1991 (shrews) have shown that soil acidity leads to higher Cd concentration in the prey (earthworms) and higher body burden in the predator.  Averaging data leads to a loss of information and species may not be protected in these soils. If the data from soils with reported pH <4.2 are excluded (i.e.4 values excluded), the HC5 increases from 0.9 to 3.3 µg Cd/g. Ma and van der Voet (1993) successfully predicted the Cd exposure to shrew for different values of soil pH and % organic matter.  This model is useful to derive soil criteria that vary with soil properties.  The model has not been incorporated in our assessment because it was validated with only 1 predator species and because soil properties are unknown for most other data. However, this generic  HC5 overestimates the risk associated to wildlife in pH neutral soils as indicated by the monitoring data of moled from Ma, 1987: while kidney Cd is already at 200 µg/g dw in acid soils near soil background values (0.3 µg/g), these kidney Cd concentrations are only found in pH neutral soils at soil Cd concentrations >6 µg/g and which is well above the HC5 of 0.9 µg/g.

The HC5 for protecting mammals is about twofold below the PNECsoil derived for protecting plants, soil fauna and microflora.  Effectively this assessment suggests that biotransfer of Cd from soil to higher trophic levels is the most critical pathway for Cd.  This HC5 value is mainly driven by the data on moles by Ma (1987) and, to a lesser extent, by data on shrews (Ma et al., 1991) and are valid for acid soils (soil pH <4.1, Table 3.2.44).  These soils are relatively uncontaminated, i.e. the predicted critical soil Cd concentrations derived from these data contain a safety factor due to the proportional extrapolation.  No data were found on moles or shrews in soils that are acid and that contain high Cd concentrations.

Assessment of secondary poisoning is obviously very complex.  There is currently only few field evidence that attributes pathological injury to Cd (Beyer, 2000).  This assessment here reveals that Cd may have a potential risk to mammals at only moderate soil Cd concentrations. Before reaching conclusions, this assessment should be evaluated.  The assessment may underestimate risk for mammals because:

- the value of the renal threshold (400 (g/g dw) that may be too high according to some studies (see previous section for a discussion).

- the assumption that the renal threshold is the same for all species. There is, however, currently no evidence suggesting that this is the case (Beyer, 2000).

- average kidney Cd data of populations were used, and not upper percentiles. Effectively, the assessment would protect the average population of a species and not individuals.  Some source documents have reported individual data .  The number of individuals with kidney Cd concentrations above 400 (g/g dw is small and we have not found such values reported below the soil HC5= 0.9 (g/g (details not shown).

On the other hand, this assessment has used margins of safety because:

- critical soil Cd concentrations are predicted by the proportional extrapolation (Fig. 3.2.13) and the lowest value was chosen from each study. The critical kidney Cd is never reached at or beyond the predicted ‘critical soil Cd concentrations’ in each transect. As an example, the critical soil Cd for the common shrew predicted from the transect study of Hunter et al, 1989 is 15.6 µg Cd/g (Table 3.2.44). The observed kidney Cd at the largest soil Cd (15.4 µg Cd/g) is 253 µg/g, i.e. only 60% of the critical kidney Cd. A proportional extrapolation from the data at the highest Cd concentration predicts that soil Cd should reach 24.3 µg Cd/g before the critical kidney Cd is reached. This means that the most conservative critical soil Cd estimate (15.6 µg/g) has a margin of safety of 1.6 (=24.3/15.6) or higher (Fig. 3.2.13 suggests a factor of about 3). The HC5 is driven by data where the kidney Cd was still below the renal threshold.  In addition, there is only 1 documented population with a mean/median kidney Cd concentrations above the renal threshold (the beaver population in the contaminated Elbe region, no soil Cd concentration known).

- the renal dysfunction is a sublethal endpoint and field data suggest that its relationship with ecological fitness still has to be demonstrated (Cooke and Johnson, 1996). One study was found for birds where ecological effects can be related to renal dysfunction at kidney Cd concentrations above the proposed kidney threshold (see below: field validation).

- the HC5 is driven by indicator organisms that are, probably, more documented than non-indicator organisms.

- the HC5 is driven by the mole and shrew thresholds applicable to acid sandy soil (pH 4.2) and which represent a reasonable worst case scenario. The HC5 excluding these soils is >3 fold above the ‘generic’ HC5.

Field validation: cadmium toxicity (ecological effects) towards wildlife in the field was recently reported for the white-tailed ptarmigan Lagopus leucurus (bird) in a Cd contaminated area of the Colorado Rocky Mountains (Larison et al., 2000). Evidence for ecological effects related to Cd are: increased mortality in the contaminated area for the adult female birds compared to that in an uncontaminated area, higher mortality for metal-contaminated ptarmigans and a distinctly lower female:male ratio in the adult population in the contaminated area. Ptarmigans are herbivorous and commonly eat willow buds and recently grown shoots of willow, both food items that are elevated in Cd but low in calcium. The low calcium diet exacerbates Cd poisoning as shown for humans (Chapter 4). Elevated kidney Cd (>400 µg/g dw, i.e. above the threshold chosen here) was found in adult birds in the contaminated area and which was associated with 8-10% lower bone calcium (and more fragile bones) compared to values in individuals with kidney Cd <400 µg/g dw. The calcium metabolic disorders may be related to renal tubular damage The larger effects on adult females than on males is explained by the foraging habitat of females that dwell longer in the Cd contaminated area than males and by their larger calcium demand for egg-laying females. Soil Cd concentrations are not directly reported in that study. The area is known as the Colorado ore-belt and well over a thousand mines, mostly abandoned, are situated there. The rocks and mineralized materials in the mining area contain, on average, 75 µg Cd g-1dw. The concentrations of Cd encountered in the surface waters and sediments of that area are > 5 µg/L and 15.2 µg Cd g-1dw (Nash et al., 2001 and Church et al., 2000).  All these data show that environmental Cd concentrations are >7-fold above corresponding EU average (section 3.1.2.4.3) suggesting that also the soil Cd is >7 fold above EU average (i.e. soil Cd >2.1 µg Cd g-1dw).  That soil Cd value is above the generic HC5 of 0.9 µg Cd g-1dw.

# Conclusion

# We propose a critical soil Cd concentration to protect mammals from soil borne Cd as

# Cdsoil,crit = 0.9 (g Cd g-1dw

which is the HC5 of values at which the critical kidney Cd concentration (400 µg/g dw) may be exceeded in the average population of 8 different species. This value is driven by the mole and shrew thresholds derived from data valid for acid sandy soils (pH 4.2)   This value is below the PNECsoil for direct effects on higher plants, soil fauna or soil microbial processes.  The risk characterisation of Cd in soil should be based on protecting mammals.

## Risk characterisation

### Introduction

The risk characterisation is based on a comparison of the PEC with PNEC values. Table 3.3.1 summarises the PNEC values that were calculated in the effects assessment (section 3.2).

Table 3.3.1: the PNEC values derived in section 3.2.

|  | value | units | remark |
| --- | --- | --- | --- |
| PNECwater | 0.19 | (g Cd L-1 | dissolved fraction |
| PNECwater | 0.09 * (H/50)0.7409 | (g Cd L-1 | for refined risk characterisation if hardness is known (section 3.2.1.6.4); dissolved fraction; not to be used below H=40 |
| PNECsoil | 1.15-2.3 | mg Cd kg-1dw | based on ecotoxicity |
| PNECsoil | 0.9 (selected) | mg Cd kg-1dw | based on secondary poisoning to mammals (local and regional) |
| PNECsediment | 2.3 | mg kg-1dw | PNEC is not corrected for bioavailability AVS and oc based normalisation could be used for regional as well as site-specific risk characterisation |
| PNECmicro-organisms | 20 | (g Cd L-1 | dissolved fraction only |
| PNECoral | 0.16 | mg Cd kg-1diet fw | birds/mammals |

Different effects assessments have led to different PNECsoil values for local risk estimates. The lowest PNEC for soil is based on the assessment of secondary poisoning to mammals. The risk of secondary poisoning is conventionally assessed separately from the direct toxic effect because the predators do not sample 100% of their food in the local environment.  However, the PNECsoil for secondary poisoning is determined by effects on organisms with a reasonably small habitat (moles and shrews) and we propose that local soil Cd concentrations should not exceed this PNEC as well. Therefore the PNECsoil = 0.9 mg/kg is proposed for local risk assessment.

### Risk characterisation for production and use (excluding batteries)

#### The aquatic compartment (including sediment and STP)

The risk factors (PEC/PNEC ratio) for local water (dissolved fraction) and sediment concentrations are given in Table 3.3.2. The PNEC was not corrected for water hardness because of lack of site-specific water hardness information. No bioavailability corrections were made for Cd in sediment because of lack of useful site-specific information.

Table 3.3.2: local risk characterisation for water and sediment. The factor risk = PEC/PNEC. The PNECwater is 0.19 (g Cd L-1 and the PNECsediment is 2.3 mg Cd kg-1dw.(Table 3.3.1). The factor risk for sediments is calculated for the concentration of added Cd (Clocalsediment, Table 3.1.85) and for the added+regional Cd (total Cd, i.e. PEClocalsediment, Table 3.1.85) without correction for bioavailability.

|  | N° | PEClocalwater | factor risk water | factor risk sediment | year |
| --- | --- | --- | --- | --- | --- |
| category |  | µg L-1 |  | added | total |  |
| Cd-production | 1 | 1.37 | 7.2 | 71.2 | 72.3 | 1996 |
|  | 2 | 0.59 | 3.1 | 26.7 | 27.9 | 1996 |
|  | 3* | 0.15* | 0.8* | 1.9 | 3.1 | 1996 |
|  | 4* | 0.52* | 2.7* | 23 | 24.2 | 1996 |
|  | 5 | 5.5 | 29 | 307 | 307.7 | 1996 |
|  | 6 | 0.11 | 0.6 | 0.0 | 1.2 | 1996 |
|  | 7*£ | 0.32* | 1.7* | 11.5 | 12.7 | 1996 |
|  | 8 | 0.12 | 0.7 | 0.6 | 1.8 | 1996 |
|  | 9* | 0.13* | 0.7* | 0.8 | 2.0 | 1999 |
|  | 10 | 0.11 | 0.6 | 0.0 | 1.2 | 1996 |
|  | 11 | 0.11 | 0.6 | 0.0 | 1.2 | 1996 |
|  | 13* | 0.69* | 3.6* | 33 | 33.7 | 1996 |
| CdO-producers | 11 | 0.11 | 0.6 | 0.0 | 1.2 | 1996 |
|  | 12 | 0.11 | 0.6 | 0.0 | 1.2 | 1993 |
| Cd-stabilisers | F | 0.11 | 0.6 | 0.0 | 1.2 | 1996 |
|  | G | 0.29 | 1.5 | 10.0 | 11.1 | 1996 |
|  | H | 0.14 | 0.7 | 1.5 | 2.7 | 1996 |
|  | I | 0.13 | 0.7 | 0.7 | 1.9 | 1996 |
|  | J | 0.11 | 0.6 | 0.0 | 1.2 | 1996 |
|  | K | 0.69 | 3.6 | 32.7 | 33.9 | 1996 |
|  | L | 0.11 | 0.6 | 0.0 | 1.2 | 1996 |
|  | M | 0.11 | 0.6 | 0.0 | 1.2 | 1996 |
|  | windows manufacturer | 0.11 | 0.6 | 0.0 | 1.2 | 1996 |
| Cd-pigments | A | 0.26 | 1.4 | 8.2 | 9.3 | 1996 |
|  | B | 0.11 | 0.6 | 0.0 | 1.2 | 1996 |
|  | C | 0.15 | 0.8 | 2.3 | 3.4 | 1996 |
|  | D | 0.14 | 0.8 | 1.7 | 2.8 | 1996 |
|  | E | 0.11 | 0.6 | 0.0 | 1.2 | 1996 |
| Cd-plating | EU | 2.9 | 15 | 155.2 | 156.3 | 1996 |
| Cd-alloys | EU | 1.81 | 9.5 | 95.8 | 97 | 1996 |

*Emission to the sea; n.a.: not available; £: recently delivered data were not yet taken into account, this will be done during the development of the Risk Reduction Strategy.

The table predicts elevated risks for the aquatic ecosystem at 11 locations/scenarios and risk to benthic organisms at all sites/scenarios. The risk for the Cd alloy processing sites is based on a generic scenario (see 3.1.2.1.1).

High risks are estimated for the sediment on the basis of PEC and PNEC values without correction for bioavailability, irrespective of the use of added or total Cd concentrations (Clocalsediment or PEClocalsediment).  Moreover, several sites in the production and processing area have a risk for benthic organisms irrespective of the regional background (cfr local added Cd, Clocalsediment  > PNECsediments).

Emissions to freshwater.  There are 6 sites (covering 3 scenarios) and 2 further scenarios with risk factors above 1 based on calculated local concentrations. Measured Cd concentrations (Table 3.1.84) in the receiving water remove some concern for two of the three sites where data are available: risk factors reduce to 5.6 (site 1), and 0.5 (site 2). The latter value, although measured, is judged less reliable than the calculated because it relates to a previous year (<1996), is rather poorly documented and is therefore of questionable representativeness for the reference reporting year (1996). Risk at the Cd producing plant 5 is high (risk factor 29). This risk is substantiated by the measured Cd concentration (5 µg L-1) which corresponds very well with the calculated PEClocal (5.5 µg L-1). An unknown factor in the risk assessment is the sedimentation rate of Cd after the on-site STP. This factor is not included here and may be of importance for an improved risk characterisation. The variability of the PECregional (which is added to Clocal to estimate the PEClocal) can only add to the uncertainty of the risk for these sites where the added Cd (Clocal, Table 3.1.5) is below the PNEC, i.e. at 2 sites (site G and A). However, the difference between Clocal and the PNEC is <0.05 µg/L, which is a small value for a regional PEC. Therefore, the uncertainty about the PECregional is unlikely to be of importance for the risk characterisation at these sites.

Emissions to the sea: using the PNEC freshwater risk factors are above 1 at the Cd producing plants 4, 7 and 13 that emit effluents to the sea.  Measured Cd concentrations (Table 3.1.84) at site 7 reduce the risk factor to below 1 but increase concern at site 4 and 13 (risk factor up to 16).  However, this risk characterisation is only indicative as no PNEC was derived for marine species.

Based on PECs and PNEC without correction for bioavailability, the risks for benthic organisms are elevated at all sites. Risk is always predicted even if emissions are zero because the regional Cd concentration in sediment is above the PNECsediment (i.e. 2.3 mg/kgdw). The regional Cd concentration in sediment is the 90th percentile of measured data. At 15 producing and processing sites/areas there is a predicted risk irrespective of the regional background (cfr local added Cd, Clocalsediment  > PNECsediments). Measured local Cd concentrations (not available) could remove concern. Moreover, the risk characterisation could also be refined by including indicators of Cd bioavailability. This can be achieved by measuring the organic carbon normalised excess of SEM over AVS. This refinement should use a worst case approach to account for seasonal variation in AVS and it is suggested that the AVS approach should be further validated (section 3.2.3.3) (conclusion i)). Furthermore, an uncertainty analysis regards the impact of an EU-wide variability in PEC reg (as a default approach in the absence of site-specific data) on the risk characterisation at local level, is not yet included. Both aspects, bioavailability and variability impact, will be implemented in an update of the risk assessment report once the results of the concl 1) program are agreed at TC NES level (see separate document, ‘RAR Stage II’).

The risk for micro-organisms in sewage treatment plants is investigated for on-site as well as off-site sewage treatement plants (STP).

On-site waste water treatment plants:

Information from the specific production and processing sites indicates that methods to remove cadmium from discharge to water are generally in place. However, no detailed data are available. The ratio of the effluent Cd concentration (Table 3.1.1) to PNEC micro-organisms (Table 3.3.1) predicts risk to the on-site STP for a number of sites in the production area (Cd metal) and in the processing areas, pigments, plating and alloys. The risk ratio ranges from 0.02 to 22 and is higher than 1 at 14 locations. There is a possibility that risk is overpredicted. Several toxicity tests (including sludge respiration test) showed that Cd affects micro-organisms of an STP at only about 1 mg Cd L-1 in the dissolved fraction (section 3.2.5). The PNECSTP was calculated from the lowest NOEC using an assessment factor, yielding a PNECmicro-organisms that is about 50-fold below the lowest LOEC and where sludge respiration was less than 30% affected (section 3.2.5). There is only 1 site (site 2 of the Cd producers) where the lowest NOEC is exceeded. Measured data may remove the concern. Wastewater treatment at the plants in the Cd metal production area are based on physical-chemical principles only (see also IPPC report on the best available techniques in the non ferrous metals industries, May 2000). Therefore, it is proposed that the conclusions related to the risk for micro-organisms in the on-site wwtp (STP) are considered as indicative only and are not taken forward to the section 5 (general conclusions).

Off-site waste water treatment plants (municipal sewage treatment plants):

For producers of Cd metal and CdO, no discharge occurs to municipal sewage system, as these sites do emit to surface/sea water or do not emit at all to the aquatic compartment. Therefore, the risk assessment of Cd and CdO producers for off site STP is not relevant. Risk to off site STP is only relevant for the processors that potentially have emissions to sewer systems. Only three stabiliser production sites have not reported flows of receiving water (Table 3.1.3). The Cd concentration in the effluent of these sites is already lower than the  PNECmicro-organisms suggesting no risk. The Cd plating and alloy scenario can potentially emit to off site STP and the predicted Cd concentrations in the effluent is 0.081 and 0.05 mg Cd L-1 respectively Assuming no further dilution in the STP (i.e. default  effluent flow of 2000 m3 day-1 and default STP capacity of 2000 m3 day-1) and assuming 60% removal rate in STP, there remains still a risk (risk factor 1.6 and 1.0¶). Apart from requests via the Lead company, no attempt was made by the Rapporteur to actively retrieve detailed data directly from the concerned sector. The predicted Cd concentrations in the effluents of the Cd pigment scenario’s range from 0.002 to 0.08 mg Cd L-1. Assuming no further dilution in the STP (i.e. default  effluent flow of 2000 m3 day-1 and default STP capacity of 2000 m3 day-1) and assuming 60% removal rate in STP, there is a risk for the Cd pigment scenario with the highest Cd concentration in the effluent (risk factor 1.6: conclusion (iii)).

# Regional and continental Cd concentrations:

Calculated values: the predicted Cd concentrations in water have been calculated for a range in Kp values (Table 3.1.157). At the average Kp values, the PEC/PNEC ratio’s are are 0.6- (regional) and 0.3 (continental). The PEC’s are larger if the Kp is lower. At the lowest value of Kp (17 10³ L kg-1) PEC/PNEC ratio’s are 1.8 (regional) or 1.7 (continental). The predicted concentrations in sediment have also been calculated for a range in Kp values. At the average Kp values, the PEC/PNEC ratio’s are 4.4 (regional) and 1.4 (continental). The PEC’s are lower if the Kp is lower. At the lowest value of Kp (17 10³ L kg-1) PEC/PNEC ratio’s are 3 (regional) or 1.3 (continental). At the largest value of Kp (224 103 L kg-1) PEC/PNEC ratio’s are 4.5 (regional) and 1.4 (continental).

Measured values: it is proposed to refine the risk characterisation with measured data which may be more relevant given the uncertainties in emissions, their geographical distribution, the wide range in natural environments, contributions from historic pollution etc.

Water.  Two assessment methods and a sensitivity analysis are presented. First of all, data from an EU-wide survey have been assessed. The FOREGS Geochemical Baseline Program (FGBP)  study determined a mean Cd concentration in European surface waters of 0.01 µg L-1 and a 90th percentile of 0.1 µg L-1, leading to risk factors of 0.05 to 0.5.

Secondly, a compilation of recent (>1995) data sets of EU countries has been made and data are classified in a tiered approach depending on the available background information (Table 3.1.184 and 3.1.185). The lowest number refers with data with highest quality, the higher number refer to data with lower quality but including those of the lowest number (i.e. a cumulative number of data). The first tier is a risk characterisation with the set of data with reliability index (RI) 1 which allow a ‘bioavailability correction’, i.e. a correction of the PNEC based on water hardness. However, it was only possible to make such corrections for water hardness for the dataset of Sweden with RI 1 and restriced to the data with hardness > 10 mg CaCO3/L. . In that case, risk factors were calculated for each monitoring point as the ratio of PEC to the hardness corrected PNEC. The 90th percentile of these risk factors is below 1 and is represented in the Table 3.3.2bis. The tiers 2 & 3 are the risk characterisations on data which do not allow bioavailability correction but for which the detection limit of Cd is at least 2-fold below the PNECwater. The tier 2 used data for which fractionation (dissolved or not) was known, the tier 3 also included data where information on fractionation was unknown. In that latter case, data with unknown fractionation were assumed to be identical to dissolved concentrations which is considred a conservative approach. From the table it can be seen that risk factors are all below 1 in tier 2 unless no outlier exclusion is made in the UK database, in which case risk factor >1 due to 20 sampling sites (of the 728 sites) with large Cd that are excluded in the analysis as proposed by the rapporteur (thus excluding outliers). It is unknown what the source of Cd is in these sites. However risk factors >1 are also found in tier 3 and tier 4 (case-by-case analysis) for the U.K and the Walloon region.

Table 3.3.3: regional risk characterisation for water in datasets varying in data quality (RI*). The factor risk = PEC/PNEC. The PNECwater is 0.19 (g Cd L-1(Table 3.3.1). Risk characterisation of dataset with RI=1 included bioavailability corrections (hardness correction) and risk factor given  is 90th percentile of risk factors. Datasets with RI>1 include also data of classes with lower RI index (i.e. cumulative number of data). Data refer to period 1995-2002 and details about data treatment are given in Table 3.1.184.

|  |  |  |  |  | supporting information: inclusion of outliers |
| --- | --- | --- | --- | --- | --- |
| RI* | Country | n | 90th percentile [µg L-1] | Factor risk | 90th percentile [µg L-1] | Factor risk |
| 1 | Sweden | 5466 | 0.04$ | 0.54 | 0.04$ | 0.58 |
| 2 | Finland | 803 | 0.0575 | 0.30 | 0.0575 | 0.30 |
|  | Germany | 608 | 0.07 | 0.39 | 0.07 | 0.39 |
|  | Norway | 985 | 0.055 | 0.29 | 0.055 | 0.29 |
|  | Sweden*** | 8999 | 0.044 | 0.23 | 0.044 | 0.23 |
|  | The Netherlands | 1825 | 0.07 | 0.38 | 0.12 | 0.63 |
|  | Greece | 39 | 0.18 | 0.93 | 0.18 | 0.93 |
|  | UK (WIMS) | 6905 | 0.15 | 0.79 | 0.87 | 4.6 |
| 3 | Finland | 803 | 0.06 | 0.30 | 0.06 | 0.30 |
|  | Germany | 608 | 0.07 | 0.39 | 0.07 | 0.39 |
|  | Greece | 39 | 0.18 | 0.93 | 0.18 | 0.93 |
|  | The Netherlands | 1825 | 0.07 | 0.38$ | 0.12 | 0.63 |
|  | Norway | 985 | 0.06 | 0.29 | 0.06 | 0.29 |
|  | Sweden*** | 8999 | 0.04 | 0.23 | 0.04 | 0.23 |
|  | U.K. (ECN) | 10 | 0.31 | 1.6 | 0.31 | 1.6 |
|  | U.K. (WIMS) | 6905 | 0.15 | 0.79 | 0.87 | 4.6 |
| 4 | Belgium; France, Italy,; Germany (datasets for the Main and Weser from the LAWA database); Portugal; Spain and The UK (COMMPS) |  |  | case-by-case (see text) |  |  |

*RI 1: DL<0.1 µg/L, Cd fractionation: D or ED (D: dissolved Cd; ED: estimated dissolved Cd ) and water hardness known; RI 2: DL<0.1  µg/L, Cd fractionation: D or ED; RI 3: DL<0.1  µg/L, Cd fractionation: D, ED or U (Unknown=assumed dissolved); RI 4: all data.

n: number of values in the dataset.** including the dataset of Skjelkvale et al. (1999) ; no hardness data known for individual points in this  dataset.$The Dutch rapporteur expressed concern about the P90 values>PNEC at  the monitoring sites on the rivers Schelde and Maas located at the border with Belgium (risk factors 1.6 and 1.1 respectively) while the average P90 values of these rivers in The Netherlands both show risk factors <1.0 (details not shown). Preference was given by the MSR to calculate the P90 value of the entire river system rather than to a P90 value of one site on a river because the TGD states that ‘The mean of the 90th percentiles of  the individual sites within one region is recommended for regional PEC determination’.$The average of P90 values of different sampling sites for the RI=1 data. The factor risk is based on the 90th percentile of individual values as the hardness changes within the sampling sites.

The risk factor for the Swedish data with RI=1 is 0.54. This risk factor is obtained after correction for water hardness using the formula for water hardness correction as presented in section 3.2.1.6.4 and using the proposed PNECwater for soft waters (from 40 mg/L down to 10 mg/L CaCO3) of 0.08 µg Cd L-1 . Uncorrected, the risk factor would become 0.22. As the corrected risk factor is much higher than the uncorrected one, it is advisable to use values corrected for water hardness for soft waters, when available. There are no data of PNECwater for the very soft waters (H below about 10 mg CaCO3/L) and these areas may be unprotected by the proposed PNECwater for soft water (0.08 µg Cd L-1). Therefore, there is a need for testing the Cd toxicity in these very soft waters (conclusion i) is drawn).

The data of Sweden in RI 2 and 3 are not corrected for water hardness.

Outliers have been removed in the calculation of P90 values to exclude local point sources in the regional assessment. The effect of either including or excluding outliers only marginally affects the risk characterisation except in UK (WIMS database) where the 20 outliers (of 728 sites) have a large impact on the average P90 (note: risk factor is 0.25 for the median P90 of the entire database, including these outliers). In all data-sets, the number of outliers was always less than 10% of the entire database.It is unknown what the source of Cd is in these outliers..

Datasets assigned as RI4 are considered least reliable because, most importantly, the reporting limit is near or above the PNEC. These databases will be considered on a case-by-case basis below. In some cases (Belgium, UK and France) it is still possible to make a risk characterisation for (part) of the region:

- Belgium

The Flemish region: 94% of the data in the 2000-2002 dataset of the Flemish Environment Agency (VMM) are smaller than the DL. The dataset has reporting limits exceeding 0.1 µg L-1. The P90-value (0.17 µg/L) is within the reporting limits and is therefore considered unreliable. The Walloon region: the reporting limit exceeds the critcal value of 0.1 µg/L defined in this report and even exceeds the PNEC, therefore this database was not included in Table 3.3.2bis. However the P90-value exceeds the critical reporting limit and can be considered as a reliable value because the P90 value is calculated from the rank in the observed frequency distribution and not from the rank in a curve fitted to the frequency distribution. This means that the P90 is not affected by the exact values of data at lower percentiles. All values below the reporting limit have been set to half the reporting limit. The P90 value indicates a risk for the Walloon region (risk factor: 3.5).

- France

The datasets for France were designated RI 4 and not included in the risk characterization. The reporting limits are unknown or exceed 0.1 µg L-1 or the dataset is not considered representative for a region. A small dataset with reliable background information was available for the river Seine. That dataset was considered too small to represent the Franch rive dataset for the Seine has a P90 value of 0.06 and a corresponding risk factor of 0.32, i.e. no risk is predicted for the Seine river.

- Germany

The data for the Main and Weser contained sampling points for which the DL was higher or identical to 0.1 µg/L. However, the average P90 value for these rivers is 0.04 and 0.09 µg/L respectively, suggesting no risk.

- The U.K

The COMMPS dataset for the U.K(n=1244) was designated RI 4 as the reporting limits exceed 0.1 µg L -1.  It was, therefore, not included in the Table 3.3.3. The P90-value, however, exceeds the reporting limits and can be considered reliable for reasons discussed above. This P90 values indicates a risk for the U.K (risk factor: 2.26). The risk factor increases to 5.36 by including the outliers (1.5 % of the entire dataset).

- Italy

The Italian dataset was considered not to be representative for the Italian region. The few values largely exceed those encountered in literature and the reporting limits exceed 0.1 µg L-1. The dataset itself is highly questionable as it indicates a 10-fold decrease of the risk factor from the year 1995 to the year 1996 (the risk factor decreases from 60 to 9.2). The dataset was designated RI 4 and not included in the risk characterization.

- Portugal

The dataset for Portugal, although very extensive, was not included in the risk characterization as the reporting limits exceed 0.1 µg L-1. Moreover, 84 % of the data have values< DL. The P90-values of different rivers are generally situated within the reporting limits interval and are, therefore, considered unreliable.The P90 value of the River Oeste might still be useful: the P90 value is 0.02 µg/L but this value is below the DL (0.03 µg/l). Since the DL is far below the PNEC, this P90 vlaues suggests no risk in that river.

- Spain

The dataset for Andalusia was not included as it obtains high values because of a historical contamination of the Guadalquivir river. The results can, therefore, not be considered to represent ambient Cd concentrations of Spanish waters. The COMMPS dataset for Spain was not included as the reporting limit, as well all the values in the dataset, equal 0.1 µg L-1. The resulting risk factor of 0.53 (=0.1/0.19), however, indicates no risk but the risk coefficient is highly uncertain.

Uncertainty analysis: the frequency distribution of individual 90th percentiles  is plotted relative to the PNEC derived from the HC5 with an assessment factor (AF) 1 or 2. The 90th percentiles refer to data with RI3 with outliers excluded and the values are either 90th percentiles of individual sites (Sweden, Germany, The Netherlands,UK-WIMS database) or, when no such data are available, the 90th percentiles of a dataset in which each site was only reported once (Greece, UK-ECN database, Norway, Finland). The uncertainty surrounding the PNEC is related to several aspects: statistical aspects (confidence limits on the HC5 estimated from the SSD) and more general concerns such as species representativity, the inherent uncertainty about NOEC values compared to benchmark values, mixed pollution etc. (see section 3.2). These uncertainty factors have crystallised in the AF=2 which was agreed.. The majority of 90th percentiles is below the PNEC while the risk cannot be excluded for about 10% of the P90 values (note that P90 values from data with RI4 such as Walloon region are not included). The choice of the assessment factor AF (i.e. either 0.19 µg/L by including the AF=2 as proposed or 0.38 µg/L with AF=1) only affects the conclusion of risk for a relatively limited number of data that fall in the range 0.19 – 0.38 µg/L  (6% of the data used in Fig 3.3.1). In terms of regions at risk, it should be noted that the choice of the AF (1 or 2) does only affect the conclusion for the small ECN database of UK whereas for the remaining countries (including UK, using the larger WIMS database) the choice of the AF (1 or 2) does not affect the conclusion about risk, in contrast with the discussion about the exclusion of outliers. For datasets with lower reliability (RI4), the risk factor is > 1 for UK (COMMPS dataset) and the Walloon region, and, again, this conclusion remains irrespective of the value of the AF for the PNEC.

Fig. 3.3.1: cumulative frequency of P90 values of dissolved Cd concentrations in EU surface waters. relative to the PNEC derived from the HC5 with an assessment factor (AF) 1 or 2. The AF=2 is agreed to be used for the PNEC and reflects most of the uncertainties . The P90 values refer to data with RI3 and the values are either 90th percentiles of individual sites (Sweden, Germany, The Netherlands, UK-WIMS database) or, when no such data are available, the 90th percentiles of a dataset in which each site was only reported once (Greece, UK-ECN databse, Norway, Finland). n=1020 with 70% of data from UK and 25% of the data from The Netherlands.

To conclude: no regional risk is predicted based on the majority of 90th percentiles of dissolved Cd values in EU with reliability index 1 to 3 (i.e. acceptable detection limit). Regional risk for the aquatic ecosystem cannot be excluded in certain regions such as UK and the Walloon region of Belgium. For the UK, the conclusion on risk is largely based on 20 of the 728 sites where elevated Cd was found and these outliers (unknown source) drive the conclusion about risk for the UK.  This shows that the risk of Cd in freshwater is  borderline. A conclusion iii) is proposed.  The overall conclusion is based on datasets evaluation with and without exclusion of outliers. The methodology proposed by the rapporteur i.e. exclusion of outliers that are detected by a statistical approach only was not endorsed by MSs. It should be noted however, that although a large number of measured data is available, more information is needed for better characterising the risks to surface water in EU. In particular data from eastern and southern Europe are underrepresented in the entire dataset, detection limits are often too high and the fractionation is often not reported. Current actions (e.g. Water Framework Directive) are already taking such measures. Special attention should be paid to waters with low hardness (H below 10 mg CaCO3 L-1).

Table 3.3.4: regional risk characterisation for sediment. The factor risk = PEC/PNEC. The PNECsediment  is 2.3 mg Cd kg-1dw (Table 3.3.1). All values are without correction for bioavailability.

|  |  |  |  | supporting information: inclusion of outliers |
| --- | --- | --- | --- | --- |
|  | n | 90th percentile [mg Cd kg-1dw] | Factor risk | 90th percentile [mg Cd kg-1dw] | Factor risk |
| Belgium (VMM) | 512 | 1.59 | 0.69 | 1.75 | 0.76 |
| France | –315 | 2.86 | 1.24 | 3.86 | 1.68 |
| France - Artois-Picardië | 126 | 2.05 | 0.89 | 37 | 16.08 |
| France- Rhône-Méditerannée | 66 | 0.93 | 0.4 | 0.93 | 0.4 |
| Spain | 8 | 2.20 | 0.96 | 8.3 | 3.63 |
| Sweden | 297 | 2.97 | 1.29 | 2.97 | 1.29 |
| The Netherlands Supporting information: 90th percentile of Cd in suspended matter | 18 | 3.69 8.5 | 1.60 3.7 | 11.48 | 3.31 |

Sediment: analysis based on PEC and PNEC values without correction for bioavailability: the limited data presented in Table 3.3.3 show risk factors varying from 0.4 to 1.6. The P90 value of the concentration of Cd in suspended matter in The Netherlands exceeds that of the P90 value of sediments. This suggests that risk factors based on suspended matter, as a model for newly deposited sediments, are even larger than those for whole sediment samples. The exclusion of outliers (see 3.1.3.4.3) largely affects the magnitude of the risk factors. For Belgium the risk factor increases from 0.69 to 0.76 by taking into account the outliers of the VMM dataset. 6.5% of the values in the VMM dataset (including outliers) exceed the PNECsediment. Including the COMMPS dataset would render a risk factor of 3.57. For France, the risk factor for the Artois-Picardië region is 0.89 and would augment to 16.08 if the outliers were taken into account with 19.8% of the values in the dataset (including outliers) exceeding the PNECsediment. The uppermost outlier is the Deule with a risk factor of 156. The risk factor for the Rhône-Méditerannée region is 0.4 with 1.5% of the values in the dataset exceeding the PNECsed. If only the outliers of the COMMPS dataset were taken into account, the risk factor for France would augment from 1.24 to 1.68.  The limited dataset from RWS for The Netherlands counts 4 values (of the 12) exceeding the PNECsediment. When including the one outlier of the COMMPS dataset for The Netherlands, the risk factor for The Netherlands would augment from 1.6 to 3.31. When including the outlier of the COMMPS dataset for Spain, the risk factor for Spain augments from 0.96 to 3.63. The Swedish risk factor is 1.29 with 19.19% of the dataset exceeding the PNECsed.The total risk factor would augment from 1.16 to 2.03 by only taking into account the COMMPS values that were discerned as outliers in the limited datasets of The Netherlands and Spain.

A large uncertainty surrounds the PNECsediment (2.3 mg Cd kg-1dw) and, hence, the risk characterization. The PNEC was calculated from one single chronic toxicity test using an AF of 50. The AVS/SEM method might further specify the PNECsediment value but this is subject of the conclusion (i) program on sediments.

Uncertainties surrounding the effects of Cd in sediments are related to the speciation of Cd in the sediment, e.g. the fraction of Cd present as insoluble sulphides. More information about the relationship between Cd speciation and Cd toxicity is given in the RAR Stage II: conclusion i) bioavailability in sediment (see separate document).

#### The terrestrial compartment

The ratio PEC/PNEC for local soil risk assessment is given in Table 3.3.3. The selected PNECsoil value is 0.9 mg kg-1dw, which is the lowest PNECsoil value and which is based on secondary poisoning to mammals (Table 3.3.1).

Risk is predicted at one location (site 2 of the Cd producers), the risk factors range from 0.5-1.1. This conclusion should be treated with caution. The local soil concentrations are calculated after 10 years exposure. The residence time of Cd in soil exceeds 100 years and predicted Cd concentrations after 50 years with current emissions will result in risk factors that are above 1 at the Cd producing sites 2, 3 and 5. (conclusion iii). Due to the long residence time of Cd in soil and the persistent availability  (Smolders et al, 1999), such contamination should be avoided.  Soil Cd is predicted to increase by more than 60 % in 10 years at three sites (site 2, 3 and 5 of the Cd producers).  These three sites have high emissions (>800 kg Cd year-1) and the highest emission factors are well above those of the other producers (> 3 kg Cd ton-1, Table 3.1.2). It is recommended that emission reduction measures should be adopted to reach emission factors that are similar to these of the other producers.

Table 3.3.5: local risk characterisation for soil. The factor risk = PEC/PNEC. The PNEC value = 0.9 mg kg-1dw is equivalent to 0.79 mg kg-1ww (standard environmental characteristics, TGD) and is the lowest for local risk assessment based on toxicity mammals through secondary poisoning (Table 3.3.1).

| Use-category | Plant N° | PEClocal soil | factor risk soil | Year |
| --- | --- | --- | --- | --- |
|  |  | mg kgww-1 |  |  |
| Cd-production | 1 | 0.37 | 0.5 | 1996 |
|  | 2 | 0.85 | 1.1 | 1996 |
|  | 3 | 0.59 | 0.7 | 1996 |
|  | 4 | 0.36 | 0.5 | 1996 |
|  | 5 | 0.63 | 0.8 | 1996 |
|  | 6 | 0.36 | 0.5 | 1996 |
|  | 7 | 0.41 | 0.5 | 1996 |
|  | 8 | 0.36 | 0.5 | 1996 |
|  | 9 | 0.39 | 0.5 | 1996 |
|  | 10 | 0.36 | 0.5 | 1996 |
|  | 11 | 0.36 | 0.5 | 1996 |
|  | 13 | 0.36 | 0.5 | 1996 |
| CdO-producers | 11 | 0.36 | 0.5 | 1996 |
|  | 12 | 0.36 | 0.5 | 1993 |
| Cd-stabilisers | F | 0.36 | 0.5 | 1996 |
|  | G | 0.36 | 0.5 | 1996 |
|  | H | 0.36 | 0.5 | 1996 |
|  | I | 0.36 | 0.5 | 1996 |
|  | J | 0.36 | 0.5 | 1996 |
|  | K | 0.36 | 0.5 | 1996 |
|  | L | 0.36 | 0.5 | 1996 |
|  | M | 0.36 | 0.5 | 1996 |
|  | window manufacturer | 0.36 | 0.5 | 1996 |
| Cd-pigments | A | 0.36 | 0.5 | 1996 |
|  | B | 0.36 | 0.5 | 1996 |
|  | C | 0.36 | 0.5 | 1996 |
|  | D | 0.36 | 0.5 | 1996 |
|  | E | 0.36 | 0.5 | 1996 |
| Cd-plating | EU | 0.36 | 0.5 | 1996 |
| Cd-alloys | EU | 0.58 | 0.7 | 1996 |

The regional risk assessment of soils should be based on the measured soil Cd concentration (Table 3.1.190) or using the regional PECsoil that is calculated with the detailed model 2 (for agricultural soils) or with EUSES (= model 1) for natural & industrial soils (Table 3.3.6).

Model 2 was developed to assess the risks of Cd in agricultural soils. The predicted soil Cd concentrations after 60 years with current immissions range from 0.20 to 0.44 mg kg-1dw. These concentrations are lower than the lowest PNECsoil  for mammals (Table 3.3.6).

Table 3.3.6: regional risk characterisation for soil. The factor risk = PEC/PNEC. The PNEC value is based on secondary poisoning to mammals (Table 3.3.1). PEC values derived from 3.1.183.

| Scenario | PECsoil after 60 years [mg kg-1dw] | PNECsoil | factor risk soil |
| --- | --- | --- | --- |
| Agricultural soils |
| 1. low input-low output (pH 6.8) | 0.257 | 0.9 | 0.29 |
| 2. low input-high output (pH 5.8) | 0.203 | 0.9 | 0.23 |
| 3. average input-low output | 0.385 | 0.9 | 0.43 |
| 4. average input-high output | 0.310 | 0.9 | 0.34 |
| 5. high input-low output | 0.411 | 0.9 | 0.46 |
| 6. high input-high output | 0.339 | 0.9 | 0.38 |
| 7. high input-very low output (worst case Mediterranean) | 0.439 | 0.9 | 0.49 |
| 8. EU average | 0.318 | 0.9 | 0.35 |
| Natural & Indutrial soil (PECsoil= PECsoil at steady state) |
|  | 0.322 | 0.9 | 0.35 |

Measured values:  average soil Cd concentrations typically range between 0.1 and 1.6 mg kg-1dw. The average (or median) Cd concentrations in natural and agricultural soils have risk factors 0.1-1.0 (mean 0.4). Corresponding factors for the 90th percentiles are 0.4-1.6 (Table 3.3.7). Soil Cd concentrations are often affected by soil type (texture and %OM) because background Cd is related to these properties. As an example, the 90th percentiles of German sand, löss and clay soils have been averaged (see section 3.1.2.4.3 – terrestrial compartment). The data were selected and compiled from the data set “Hintergrundwerte für anorganische und organische Stoffe in Böden” (LABO, 1998). Risk factors are 0.62 for the sandy soils, 0.74 for the loamy (löss) soils and 0.98 for the clay soils. Reported 90th percentiles of soil Cd are often, but not always, classified per soil groups; The lack of a harmonized way of reporting 90th percentiles obscures the regional EU risk characterization.

Local concentrations are often higher than the PNECsoil values, either due to pollution or due to high background concentrations. High background concentrations (> 2 mg kg-1) in soil are often associated with low plant availability (e.g. Mench et al.1997). There is no information on Cd toxicity to the soil ecosystem or to mammals in such soils. Soils with historic Cd contamination (smelters) have Cd concentrations that are often several fold higher than the PNECsoil  for soil organisms or for mammals. The elevated Cd in smelter affected soils is generally associated with elevated Zn concentrations. The usual Zn/Cd ratio is about 100 in these soils. The PNECsoil of Zn, added above background, is only 27 mg kg-1dw (RAR Zn, 2004) whereas the PNECsoil of Cd is 0.9 mg kg-1dw. In a smelter affected soil containing 2.5 mg Cd kg-1 and 250 mg kg-1 Zn (background about 50 Zn kg-1) it is likely that Zn and not Cd will be toxic to soil organisms.

Uncertainty analysis: if 90th percentiles of soil Cd concentrations are used, risk cannot be excluded in one region (Table 3.3.7). Reported 90th percentiles are averaged per country as a surrogate for region. No attempt was made to discriminate soil classes. The risk is predicted for the UK when using the PNECsoil of 0.9 mg Cd kg-1 derived from the study of secondary poisoning. This PNECsoil has a large (statitistical) uncertainty and the limited data available suggest that risk for secondary poisoning is mainly pronounced in very acid soils because data from such soil types has triggered the PNEC value (section 3.2.6.4.2),. As an illustration, the PNECsoil increases from 0.9 mg Cd kg-1  to 3.3 mg Cd kg-1 if data on acid soils (pH <4.2) are excluded in the derivation of the PNEC (section 3.2.6.4.2). Practically this means that the risk in UK could be excluded if the P90 values do not refer to acid soils, which is unknown. This analysis is qualitative because there is no validated model to estimate risk to mammals taking soil pH into account (section 3.2.6.4.2). Moreover, even if risk to secondary poisoning can be excluded, risk to soil microbial process in UK soils cannot be excluded because it falls within the range of the proposed PNECsoil based on direct toxicity to soil microbial processes (see Table 3.3.1). Taken together, regional soil Cd concentrations predict risk in one EU country for which data are available, but the uncertainty surrounding the PNEC values for soil suggests that risk is borderline. A conservative conclusion iii) is proposed.

Table 3.3.7: regional risk characterisation for soil. The factor risk = PEC/PNEC. The PNECsoil  is 0.9 mg Cd kg-1dw (Table 3.3.1).

| Location | 90th percentile [µg kg-1] | Factor risk |
| --- | --- | --- |
| Belgium | 0.51 | 0.56 |
| France | 0.85 | 0.94 |
| Germany | 0.65 | 0.73 |
| Sweden | 0.39 | 0.43 |
| The Netherlands | 0.83 | 0.92 |
| The United Kingdom | 1.40 | 1.56 |

#### Secondary poisoning

Effects of soil-borne Cd on mammals has already been included in the previous section since this pathway is more critical than direct effects on higher plants, soil fauna or soil microbial processes.

The PECoral for birds is calculated as ranges with PECsoil and PECwater and with the range in BAF and BCF values derived from the compilations in section 3.2.6.

The PECoral of worms is 5.4-9.1 mg kg-1ww if based on a median BAF for worms and is 1.4-19 mg kg-1ww if based on the entire range of BAF’s for worms. The PNECoral for birds is 0.16 mg kg-1 diet, i.e. the PEC/PNEC ratio varies between 9 and 121, with most ratios consistently above 1.   This suggests that Cd concentration in the worms may be at risk for the birds, even at ambient soil Cd concentrations.

The PECoral of fish is  <0.1-3.6 mg kg-1ww if based on a median BCF for fish and is <0.01-148 mg kg-1ww if based on the entire range of BCF and BAF’s for fish. The PNECoral for birds is 0.16 mg kg-1 diet, i.e. the PEC/PNEC ratio varies between <0.1-930 with most ratio’s, however, consistently below 1. This suggests that Cd concentration in the fish may be at risk for the birds in some situations. The PECoral at ambient Cd concentration in water (<0.3 µg Cd L-1) is 0.004 mg Cd kg-1ww using the median BCF for fish and is 0.19 mg kg-1ww based on the highest BAF or BCF value for whole fish. The first value is well below the PNECoral for birds, the latter is 1.2 fold the PNECoral suggesting potential risk at ambient concentrations.  This conclusion should be put into perspective: BAF or BCF values of whole fish are typically about 100 L/kgww with few extremes above 500 L/kg ww and at which risk factors are above unity (3.2.34a&b).

For different reasons it is felt that even the large PEC/PNEC ratio in water (local) or soil (at local and ambient concentrations) for birds may not reflect a severe risk:

- Kidney or liver Cd concentrations in terrestrial birds are below concentrations that are assumed to be acceptable (Furness, 1996-see below for more details) despite that measured Cd concentrations in worms from uncontaminated areas often exceed the PNECoral;

- the PNECoral is based on Cd salt spiked meals thereby overestimating Cd availability to the test animals (section 3.2.6.4.2);

- birds may not sample 50 % of their food as worms in a contaminated area.

The risk of Cd to birds may be refined with field data and critical tissue concentrations. This assessment is yet not possible due to the lack of dose (soil/food Cd)-response (tissue concentration).  Tissue concentrations of Cd in birds have been reviewed by Furness (1996).  Kidney Cd concentrations in pelagic seabirds are several orders of magnitude higher than in terrestrial seabirds. We will not make any risk assessment here for marine birds as discussed in 3.2.6.4.1.  Furness (1996) suggests a critical Cd concentration of 100 µg/g ww (about 400 µg/g dw). This threshold is the same as suggested for mammals (section 3.2.6.4.2).  Mean kidney Cd concentration in the kidney of terrestrial birds is below 11 µg/g ww and individual highest concentrations (70µg/g ww) have been found in feral pigeons collected around Heathrow airport (presumably enriched with Cd from tire debris, Hutton and Goodman, 1980).  A recent survey in Italy reported low kidney Cd concentration (<8 µg/g dw, or <2 µg/g ww ) in top predators little owl and common buzzard (Battaglia et al., 2005). It has been surprisingly difficult to show elevated Cd in birds inhabiting environments supposedly polluted by Cd (Furness, 1996). Kidney Cd in top predators barn owl and kestrel from the metal polluted Kempen (NL) are 24±26 µg/g dw and 4.8 ±6 µg/g dw respectively (Gorree et al, 1995), i.e. well below the critical value. The only exception with clearly elevated Cd exposure in a contaminated area are the white tailed ptarmigan (Lagopetus leucurus) with kidney Cd concentrations up to about 200 µg/g ww (as observed in Colorado, U.S.A.) which is 2-fold above the toxic threshold (Larson et al., 2000). The large exposure is related to the diet (herbivorous with preference for willow) as discussed in 3.2.6.4.2. The corresponding concentrations in samples from a non-contaminated environment are maximally 40 µg/g ww , i.e. below the toxic threshold. The elevated Cd exposure for that species is found in an area where soil Cd is estimated to be at least 2 mg Cd/kg (see 3.2.6.4.2). As none of the regional or local soil Cd concentrations in this study are > 2 mg Cd/kg, we conclude that risk of Cd for this species (rare in Europe) is unlikely at the PECsoil considered.

Table 3.3.8: The predicted environmental concentrations in food (PECoral). The choice for the parameters and the risk for secondary poisoning is discussed in the text.

|  | PEClocal mg kg-1ww (or (g L-1) min-max | PECregional mg kg-1dw (or (g L-1) | BAF//BCF median and min-max kgdw (or L) kgww-1 | PECoral= (0.5PEClocal+0.5PECregional)*BC(A)F mg kg-1 ww |
| --- | --- | --- | --- | --- |
| soil-worm | 0.36-0.85 | 0.36 | 15 4-32 | 5.4-9.1 (median BAF) 1.4-19.4 (range of BAF |
| water-fish | 0.1-477 | 0.11 | 15 0.5-623 | 0.002-3.6 (median BCF) <0.001-148(range of BCF/BAF) |

#### The atmospheric compartment

A quantitative risk characterisation for exposure of organisms to airborne cadmium is not done because there are no useful data on the effects of airborn cadmium in environmental organisms and thus no PNEC air could be derived. The PECs in air are used for the risk assessment of man indirectly exposed via the environment (chapter 4). Inorganic cadmium air emissions are primarily associated with particulates in the air. Emission to air will settle out to soil. The impact of industrial air emissions at local scale is therefore included in the conclusions on the terrestrial compartment.

#### Conclusions

Environmental Cd concentrations that were either modelled (based on local emissions from Cd/CdO production or processing and on diffuse emissions) or measured were combined with the effects assessment that was largely based on dose (Cd2+ salts)-response (chronic toxicity) studies. The effects assessment was based on protecting mammals from soil borne Cd. The following is concluded:

- modelled freshwater dissolved Cd concentrations based on site-specific emission data (without water hardness corrections) exceed the freshwater PNECwater at 11 sites where Cd is produced or processed, 3 of which have emissions into the sea. The measured Cd concentrations usually reduce concern. For one site risk is predicted if based on modelled concentrations but not if based on measured concentrations. However, the measured concentration refers to two years before the reference year and will therefore not be preferred over the modelled concentration. Risk at Cd containing alloy production sites cannot be excluded. There is potential risk for on-site STP at a number of Cd producing and processing sites (pigments, plating and alloys). Measured site-specific (toxicity)  data may remove this concern

- there is potential Cd toxicity for off site STP due to emissions from Cd plating, pigment and alloy industry.

- Modelled sediment concentrations (without bioavailability correction) result in elevated risks for benthic organisms at all sites/scenarios. Risk is always predicted even if emissions are zero because the regional Cd concentration in sediment is above the PNECsediment. The regional Cd concentration in sediment is the 90th percentile of measured data. No risk is predicted using average or median sediment Cd concentration and if emissions are zero. On the other hand, at 15 producing and processing sites/areas i.e. 7 Cd-production sites and 8 Cd-processing sites (i.e. stabiliser production, pigment production and the generic scenarios ‘Cd plating’ and ‘Cd alloys’), there is predicted risk irrespective of the regional background (cfr local added Cd, Clocalsediment  > PNECsediments). Measured local Cd concentrations (not available) could remove concern. A refined risk characterisation could be performed at these sites using an AVS and oc based normalisation . To that latter perspective, a conclusion i) was decided.

- predicted regional and continental Cd concentrations in water are below the PNECwater at a mean Kp value while the risk factor is 1.7 using a Kp value that is distinctly smaller than average. No regional risk is predicted based on the majority of 90th percentiles of measured data from monitoring programmes with acceptable detection limit. Regional risk for the aquatic ecosystem cannot be excluded in certain regions such as UK and the Walloon region of Belgium.

- In general, the current local standards for emissions to water mentioned in permits (maximum Cd concentration in the effluent and the volume of discharged effluent) should be reconsidered in the light of the derived PNECwater in order to prevent risk to the aquatic compartment.

- Regional predicted concentrations in the sediment are typically larger than the PNEC but overestimate measured concentrations. Risks for the 90th percentiles of the various European countries ranges from 0.69 to 1.6 (datasets excluding outliers). AVS/SEM analysis could remove the concern. To the latter perspective, conclusion i) is decided.

- modelled local soil Cd concentrations indicate immediate risks for mammals at one Cd metal production site.  Long term predictions (>20 years) show that current atmospheric emissions from 3 Cd metal producing sites can increase risk at the local scale. The emission factors of these sites should be reduced to those of other Cd producing plants. Given the total lack of information related to site-specific air emission data for the Cd alloy and Cd plating industry, long term risk at the local terrestrial scale cannot be excluded for these industry areas.

- predicted regional soil Cd concentrations that include different agricultural scenario’s are below the PNECsoil. The average (or median) measured Cd concentrations in natural and agricultural soils have risk factors 0.1-1.0 (mean 0.4). Corresponding factors for the 90th percentiles are 0.4-1.6. Risk cannot be excluded in one region but depends on the magnitude of the assessment factor chosen in the derivation of the PNECsoil (either 1 or 2, see 3.2.2.7). Averaging of all 90th percentiles within a region is clearly affected by the dominant soil types in each region because soil Cd concentration are affected by properties such as % clay and % organic matter.

- potential risk of Cd to terrestrial birds is predicted using soil-worm-bird or water-fish-bird modelling.  Field data (body burden: kidney and liver Cd data) of terrestrial birds do not indicate Cd poisoning, even in contaminated areas and in top predators.  Pelagic birds have reported kidney Cd concentrations above acceptable values but no risk characterisation of marine environments was made here.

### Risk characterisation for battery related life cycle steps

#### Overview assumptions and built-in conservatism

Within the approach used in this report to estimate the cadmium emissions associated with  waste management strategies such as landfilling and incinerations different assumptions have been made that lack validation due to the limited availability of data on this subject. As a general premise realistic worst case conditions were taken as input values to perform the calculations but in other cases average values were used instead of worst case estimated in order to conserve the environmental realisms of the estimates. Table 3.3.9 provides an overview of the assumptions and default values taken in this report and the associated level of conservatism introduced with them.

Table 3.3.9 : Overview of the input values used in the emission calculations of MSW landfills and MSW incinerators.

| Subject | Parameter | Value | Best case | Typical | Realistic worst case | Worst case | Description |
| --- | --- | --- | --- | --- | --- | --- | --- |
| General data |  |  |  |  |  |  |  |
| Information Ni-Cd batteries | Cd content portable Ni-Cd battery | 13.8 % |  |  |  |  | Average: referring to actual manufacturing and production data |
| Section 2.2.2.2 | Cd content industrial Ni-Cd battery | 8 % |  |  |  |  | Average: referring to actual manufacturing and production data |
| Section 2.2.2.4.2.2. | Weight portable Ni-Cd battery | 38 g |  |  |  |  | Average: referring to actual manufacturing and production data |
| Section 2.2.2.4.4.1 | Sales data portable Ni-Cd batteries | 14,000 tonnes |  |  |  |  | Upper limits used |
| Section 2.2.2.4.4.2 | Sales data industrial Ni-Cd batteries | 3,632 tonnes |  |  |  |  | Upper limits used |
| Section 2.2.2.4.4.3 | Future sales portable Ni-Cd batteries | 13,500 tonnes |  |  |  |  | Real consumption numbers show a decrease: 11,793 tonnes in 2000 -11,265 tonnes in 2001 |
| Section 2.2.2.5.1.1 | Recycling data portable Ni-Cd batteries | 1,446 tonnes |  |  |  |  | Lowest limits used |
| Section 2.2.2.5.1.2 | Recycling data industrial Ni-Cd batteries | 2,667 tonnes |  |  |  |  | Lowest limits used |
| Section 2.2.2.5.2 | Recycling % | 10 % |  |  |  |  |  |
|  | Recycling % | 75 % |  |  |  |  |  |
| Ni-Cd manufacturing:recycling sites | Cd concentration effluent |  |  |  |  |  | 90th percentile (in general: of the individual raw measurements) |
|  | Effluent flow |  |  |  |  |  | 90th percentile |
|  | Flow receiving water |  |  |  |  |  | Minimal flow rate or 1/3 average flow rate |
| Municipal Solid Waste (MSW) | Cd content | 10g/tonnes |  |  |  |  | 90th percentile |
| Section 3.1.2.2.5.2 | Moisture content | 30 % |  |  |  |  | Van der Poel (1999) and other references (see text) |
|  | Contribution Ni-Cd battery | 10 % |  |  |  |  | Typical percentages are between 10-20 % |
|  | Contribution Ni-Cd battery | 50 % |  |  |  |  | Maximum Ni-Cd battery contribution measured was 4.3g Cd/tonnes dry wt. MSW (Germany) used on the 90th percentile value of 10 g Cd /tonnes dry wt. |
| Section 3.1.2.2.5.4 | MSW incinerated/landfilled current situation |  |  |  |  |  | Average for EU. |
|  | MSW incinerated/landfilled 100 % incineration |  |  |  |  |  | Additional scenario added for the sensitivity analysis |
| MSW incineration | Volume fluegass | 5,500 Nm3/tonnes |  |  |  |  | Range reported in literature 5,000-6,000 |
| Section 3.1.2.2.5.5.1 | Cd concentration in flue gass |  |  |  |  |  | Most often average values were used, In some cases concentrations were P90 values |
| Above Table 3.1.27 | Waste water generated | 2,5 m3/tonnes |  |  |  |  | Range reported in literature 0.5-2.5 m3. For the regional PEC calculations this maximum value have been used. For the local calculations both min and max have been used. |
| Table 3.1.27 | Cd concentration in waste water before treatment | 0.3 mg/L |  |  |  |  | Average of measured data used for regional calculations |
|  | Cd concentration in waste water before treatment | 0.42 mg/L |  |  |  |  | 90th percentile of measured data used for local calculations |
|  | Cd concentration in waste water before treatment | 0.76 mg/L |  |  |  |  | Max value used for sensitivity analysis |
|  | Removal efficiency Cd | 98.8 % |  |  |  |  | Based on 104 measurements and the comparison of both average evalues of influent/effluent as maximum values |
| Table 3.1.30 | Cd percentage in fly ash | 87 % |  |  |  |  | Average value based on different literature data |
|  | Cd percentage in bottom ash | 13 % |  |  |  |  | Average value based on different literature data |
| MSW landfill Section 3.1.2.2.5.6 Table 3.1. | Cd concentration in leachate | 5 µg/L |  |  |  |  | Eggenberger and Waber (2000), Flyhammar, 1995, EREF, 1999. 90th percentile Germany < 5, 80th percentile Switserland < 3, 50th percentile Sweden = 5 and < 5, 50th percentile USA/France: 2,5-7 landfills (Germany) (Krümpelbeck, 1999, average concentrations): 1.5 years: 11µg/L 21-30 years: 2.8 µg/L landfills (Sweden) (Flyhammar et al, 1998): 1-2 years: 40 µg/L 20-22 years: 6 µg/L |
|  | Leachate volume | 2,500 m3/ha |  |  |  |  | Maximum value based on average to reasonable worst case precipitation of 800 mm/y |
| Table 3.1.44 | Rainfall | 800 mm/y |  |  |  |  | Rainfall representative for Mid Europe and the Scandinavian countries, reasonable worst case for South Europe |
| Table 3.1.51 | Surface landfill | 14,7 ha |  |  |  |  | Average value of reported landfill surface areas |
| Sewage Treatment plant | Removal efficiency Cd | 60 % |  |  |  |  | Average value (CBS, 2002) |
| Regional calculations |  |  |  |  |  |  |  |
| Ni-Cd manufacturing:recycling sites | Allocation to region |  |  |  |  |  | Highest emittor chosen |
| Incineration MSW | Regional air emissions |  |  |  |  |  | Average or 90P values have been used. |
|  | Regional water emissions |  |  |  |  |  | Maximum amount of water generated, average influent concentration and typical removal percentage used for calculations |
| Landfilling MSW | Regional water emissions |  |  |  |  |  | Maximum leachate volume (2,500 m3/ha,y) used in combination with average Cd concentration (5 µg/L) and average landfill surface (14,7 ha) |
| Local calculations |  |  |  |  |  |  |  |
| Incineration MSW | Aquatic compartment |  |  |  |  |  | P90 value of measured influent concentrations |
| Section 3.1.3.2.1 Figure 3.1.11 (below Table 3.1.93) | Dilution factor | 100 |  |  |  |  | Based on the 10th percentile of calculated DF with the maximum value of waste water generated (2.5 m3/tonne) |
|  | Dilution factor | 1,000 |  |  |  |  | Based on the 50th percentile of measured data and the maximum volume of waste water generated (2.5 m3/tonne). Could in fact also be considered as a realistic worst case since 75 % of the incinerators have a DF > 1,000 |
|  | Size plant | 112 ktonnes |  |  |  |  | Large plant |
|  | Terrestrial and atmospheric compartment |  |  |  |  |  | Country specific air emissions have been used. Sometimes based on P90 values measured data, sometimes highest emission factor and sometimes measured data represented average conditions. |
| Landfilling MSW | Surface landfill | 20 ha |  |  |  |  | Future landfills are expected to be large (at least 20ha), High surface equals high volume of leachate generated with average Cd leachate concentration (5µg/L). |
| Below Table 3.1.49 | Leachate volume | 100 m3/d |  |  |  |  | Based on large landfill surface area and high leachate volume (2,024 m3/ha/y) during operational phase |
|  | Dilution factor | 180 |  |  |  |  | Based on the release of the leachate in a river with TGD standard flow rate of 18,000 m3/d |
|  | Local water emission |  |  |  |  |  | Based on large landfill surface area, high leachate volume (2,024 m3/ha/y) during operational phase, average Cd leachate concentration (5 µg/L) |
| Future emissions | Landfill leachate concentration | 50 µg/L |  |  |  |  | According to the performed geochemical modelling on mature waste, carbonate precipitation is likely to prevent cadmium concentrations rising above 60 to 90 µg/l. The laboratory results indicated, however, that for the aerobic columns, cadmium concentrations generally remained below 10 µg/L suggesting that the retention mechanism is probably not precipitation alone. The leachate concentration of 50 µg/L can be considered as a conservative/realistic worst case leachate concentration because in this case we are assuming that aerobic precipitation is the only metal retention mechanisms |
| Section 3.1.2.2.5.3 | Future Cd content | 13.2 g/tonne |  |  |  |  | Based on 75 % collection but already 9 g/tonne Cd due to other sources. Also future sales figures (13,500 tonnes) kept constant while evidence of decreasing trend) The same trend is supposed in ‘consumption’ figures |
|  |  | 24 g/tonne |  |  |  |  | Based on 10 % collection but already 9 g/tonne Cd due to other sources, Also future sales figures (13,500 tonnes) kept constant while evidence of decreasing trend) The same trend is supposed in ‘consumption’ figures |

#### The aquatic compartment (including sediment and STP)

The risk factors (PEC/PNEC ratio) for local water and sediment concentrations are given in Table 3.3.10 for the Ni-Cd producers and recyclers and in Tables 3.3.11, 3.3.12, 3.3.13,  3.3.14, 3.3.15 and 3.3.16 for incinerators and landfills. By lack of relevant data, corrections for water hardness could not be done for the risk characterisation.

Risk characterisation Ni-Cd producing/recycling plants

Table 3.3.10: Local risk characterisation Ni-Cd producing/recycling plants for water, sediment and STP. The factor risk = PEC/PNEC. The PNECwater is 0.19 (g Cd/L. The PNECsediment is 2.3 mg/kg dry wt. The factor risk is calculated for the concentration of added Cd (Clocalsediment) and for the added+regional Cd (total Cd, i.e. PECsediment) without correction for bioavailability.The PNEC for micro-organisms is 20 µg/L (Table 3.3.1)

| use- | N° | PEClocal water site specific | factor risk water site specific | PEClocal water DF=1,000 | factor risk water DF=1,000 | PEClocalsediment DF=1,000 or site specific | factor risk sediment DF=1,000 or site specific Total | factor risk sediment DF=1,000 or site specific Added | Ceffluent | Factor risk STP | year |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| category |  | µg/L |  | µg/L |  | mg/kg dry wt. |  |  | (mg/L) |  |  |
| NiCd-batteries | 1 | 0.12 | 0.63 | N/A | N/A | 3.2 | 1.4 | 0.2 | 0.019a | 0.95 | 1999 |
|  | 2* | 0.15 | 0.79 | 0.15 | 0.79 | 8.0 | 3.5 | 2.3 | 0.12 | n.r | 2000 |
|  | 3 | 0.12 | 0.63 | 0.15 | 0.79 | 8.0 | 3.5 | 2.3 | 0.12 | n.r. | 2000 |
|  | 4 | 0.18 | 0.94 | N/A | N/A | 10.5 | 4.6 | 3.4 | 0.13 | n.r. | 2000 |
|  | 5 | 0.11 | 0.58 | 0.114 | 0.58 | 2.7 | 1.2 | 0 | 0.00007a | 0.005 | 2000 |
|  | 6 | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A | n.r. | 1999 |
|  | 7 | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A | n.r. | 1999 |
| Cdrecyclers | 1b | 0.19 | 1.0 | 0.27 | 1.4 | 22.6 | 9.8 | 8.6 | 0.45 | n.r. | 2000 |
|  | 1c | 0.13 | 0.68 | 0.17 | 0.89 | 19.8 | 8.6 | 7.5 | 0.17 | n.r. | 2000 |
|  | 2 | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A | 1999 |

N/A: not applicable, a influent concentration STP = effluent concentration plant*DF STP)

b based on P90 of daily measurements, c based on average effluent concentration and average effluent flow raten.r.:  not relevant.

* emission to the sea

Aquatic compartment

Freshwater and marine

For the Ni-Cd batteries producing plants emitting in fresh water ecosystems there are no sites with a risk factor larger than one. Plant 4 has a risk factor of 0.94. Although the P90 of concentrations in the effluent is calculated on monthly average values (and not on daily measurements) the risk factor of 0.94, calculated on the basis of several 'parameter' worst case assumptions, is judged as being 'without concern' for aquatic organisms. For the Ni-Cd recycling sites there is one site with an elevated risk, plant 1. If the risk characterisation is performed with the average flow rate and average cadmium concentration a risk factor of 0.89 is obtained (scenario 1b). This indicates that at plant 1, although operating fully in line with the current legislation and local permit, risk to aquatic organisms can potentially  occur at specific spatial-temporal conditions.

Ni-Cd producing plant 2 emits effluents to the marine environment.  The risk factor is below 1 at that site (based on the PNEC freshwater). However, the risk characterisation is indicative only, as no PNEC was derived for marine species.

Uncertainty analysis:

It should be noted that an assessment factor of 2 has been included in the PNEC water derivation due to remaining uncertainty.

The uncertainty surrounding the PNEC is related to several aspects:

- Statistical aspects:  for cadmium an effect database of 168 reliable tests on single species is available which contains 3 reliable LOEC’s below the derived HC5 (0.38 µg/L) whereas the 9 multi species studies identified 1 LOEC below this hardness corrected HC5. This suggests that NOEC and LOEC distributions overlap in the lower concentration range and that an additional assessment factor may be necessary.

- The inherent uncertainty about NOEC values compared to the benchmark values

- Species representativity

- Mixed pollution (etc. see section 3.2)

These factors have crystallised in the AF=2 which was agreed.

The uncertainty around the PNEC water influences the risk conclusion for the Ni-Cd recycling plant. If no assessment factor is applied the site would not have a local risk anymore  (RCR = 0.5-0.7) for the water compartment.

Using measured regional values:

Aforementioned exposure estimations and risk assessment are based on calculated PEC reg (i.e. 0.11 µg/L). Preference should, however, be given to measured values when available. However in the absence of reliable and representative regional measured data in the vicinity of the individual sites the RCR values have also been calculated (results not shown)  using the average of the measured P90 values for different countries (i.e. 0.12 µg/L) and also using the median of the measured P90 values (i.e. 0.07 µg/L),

The use of the average measured regional PEC concentration (0.12 µg/L) does not change the risk conclusions for the Ni-Cd producing sites. Only in the case of recycler 1 the observed risk ratio of 1 for a site specific dilution changes into a no risk scenario (RCR = 0.79) when the median measured regional concentration is used as regional background.

Sediments (assessment without bioavailability correction)

Based on PECs and PNEC not corrected for bioavailability, the risks for benthic organisms are elevated at sites 1 to 5 for the Ni-Cd producing plants and recycler 1. Risk factors based on ‘total’ (i.e. locally added and regional background contribution)  vary between 1.2 and 9.8.

It should be noted that a risk is always predicted even if emissions are zero because the regional Cd concentration in sediment is above the PNECsediment. The regional Cd concentration in sediment is the 90th percentile of measured data. (2.66 mg/kg dry wt.) No risk is predicted when the EU average or median sediment Cd concentration is used as regional Cd concentration. Based only on local emissions (i.e. without the background contribution), no risk is predicted at some sites if local background is low as suggested by risk factors based on locally added Cd only (e.g. plant 1). At several producing and processing sites (plant 2, 3 and 4), however, there is predicted risk irrespective of the regional background (cfr local added Cd, Clocalsediment  > PNECsediments). Measured local Cd concentrations (not available) could remove the concern.

Moreover, the risk characterisation could also be refined by including indicators of Cd bioavailability. This can be achieved by measuring the organic carbon normalised excess SEMCd over AVS. This refinement should use a worst case approach to account for seasonal variation in AVS and it is suggested that the AVS approach should be further validated (section 3.2.3.3). To that end a conclusion i) was decided by the Technical Meeting. Furthermore, an uncertainty analysis regards the impact of an EU-wide variability in PEC reg (as a default approach in the absence of site-specific data) on the risk characterisation at local level, is not yet included. Both aspects, bioavailability and variability impact, will be implemented in an update of the risk assessment report once the results of the concl 1) program are agreed at TC NES level (see separate document, ‘RAR Stage II’).

STP (off-site)

In this study, the risk for micro-organisms in sewage treatment plants is investigated for off-site sewage treatement plants (STP) only.

Only two plants discharge in a STP system. The ratio of effluent concentration to the PNEC micro-organisms (20 µg/L.) is suggested as the indicator of risk for a STP (TGD, 1996). This ratio is lower than 1 for both plants. However, for the reference year 1999, the risk factor calculated for Ni-Cd producing plant 1 is close to 1 (0.95). There is a possibility that the risk is overpredicted. Several toxicity tests (including sludge respiration test) showed that Cd affects micro-organisms of an STP at only about 1 mg Cd/L in the dissolved fraction. The PNECSTP was calculated from the lowest NOEC using an assessment factor, yielding a PNECmicro-organisms that is about 50-fold below the lowest LOEC and where sludge respiration was less than 30% affected (section 3.2.5). There is no site where effluent concentrations exceed about 1 mg Cd/L or  the lowest NOEC (200 µg/L).

For the other sites the STP risk factor is irrelevant because for these sites the industrial effluents are rejected to surface water after physico-chemical treatment on site.

Risk characterisation MSW incinerators

Since cadmium emissions from incinerators reflect always all cadmium sources a comparative risk assessment has been made. First the risk associated with the total cadmium emissions are given. This analysis is followed by the calculation of the risks associated with the total cadmium without Ni-Cd batteries.

Freshwater

Table 3.3.11: Local risk characterisation incinerators for water and STP (at dilution factor 100 and 1,000). The factor risk = PEC/PNEC. The PNECwater is 0.19 (g Cd/L . The PNECsediment is 2.3 mg/kg dry wt. The PNEC for micro-organisms is 20 µg/L (Table 3.3.1). Total cadmium.

|  | PEC local water DF = 100 | Factor risk water DF = 100 | PEC local water DF = 1,000 | Factor risk water DF = 1,000 | Ceffluent | Factor risk STP |
| --- | --- | --- | --- | --- | --- | --- |
|  | µg/L | - | mg/L | - | mg/L |  |
| Scenario 1/2 | 0.13 | 0.68 | 0.12 | 0.63 | 0.005 | 0.25 |

No risks are expected for aquatic organisms when the current estimated emission from a hypothetical local incineration plant is considered (for both dilution factor 100 and 1,000). If the effluent of a incinerator plant is released after a on site WWTP with high Cd removal efficiency (98.8%) in a STP no toxicity to the off-site STP micro-organisms is predicted Removing all Ni-Cd batteries from the MSW stream has a neglible influence on the obtained risk ratios (Table 3.3.12).

Table 3.3.12: Local risk characterisation incinerators for water (at dilution factor 100 and 1,000). The factor risk = PEC/PNEC. The PNECwater is 0.19 (g Cd/L . The PNECsediment is 2.3 mg/kg dry wt. The PNEC for micro-organisms is 20 µg/L (Table 3.3.1). Total cadmium without Ni-Cd contribution.

|  | PEC local water DF = 100 | Factor risk water DF = 100 | PEC local water DF = 1,000 | Factor risk water DF = 1,000 |
| --- | --- | --- | --- | --- |
|  | µg/L | - | µg/L | - |
|  | Assumption Ni-Cd batteries contributed 10 % to the overall Cd load |
| Scenario 1/2 | 0.13 | 0.68 | 0.11 | 0.58 |
|  | Assumption Ni-Cd batteries contributed 50 % to the overall Cd load |
| Scenario 1/2 | 0.12 | 0.63 | 0.11 | 0.58 |

Uncertainty analysis:

PNEC

It should be noted that an assessment factor of 2 has been included in the PNEC derivation due to remaining uncertainty.  The inclusion or exclusion of this assessment factor does not influence the risk conclusions for the MSW incinerator scenarios.

Using measured regional values:

Aforementioned exposure estimations and risk assessment are based on calculated PEC reg (i.e. 0.11 µg/L). Preference should, however, be given to measured values when available. However in the absence of reliable and representative regional measured data in the vicinity of the individual sites the RCR values have also been calculated (results not shown)  using the average of the measured P90 values for different countries (i.e. 0.12 µg/L) and also using the median of the measured P90 values (i.e. 0.07 µg/L). The use of the average measured regional PEC concentration (0.12 µg/L) or the median regional PEC concentration (0.07 µg/L) does not change the risk conclusions.

Dilution factors

The risk conclusions are based on a realistic worst case dilution factor of 100 and a typical value of 1,000. In case the dilution factor would be below 25 at an effluent concentration of 0.0056 mg/L or more, a risk would be predicted .

Cadmium removal efficiencies:

The risk conclusions are based on the use of an on-site WWTP with a removal efficiency of 98.8 % and an influent concentration of 0.47 mg/L. In case the removal efficiency is lower than 95.1 % while the influent concentration is 0.47 mg/L or more, a risk would be predicted.

Sediments (assessment without bioavailability correction)

Table 3.3.13: Local risk characterisation incinerators for sediments (at dilution factor 100 and 1,000). The factor risk = PEC/PNEC. The PNECsediment is 2.3 mg/kg dry wt. The factor risk is calculated for the concentration of added Cd (Clocalsediment) and for the added+regional Cd (total Cd, i.e. PECsediment) without correction for bioavailability.  Total cadmium.

|  | PEC local sediment DF = 100 | Factor risk sediment DF = 100 Total | Factor risk sediment DF = 100 Added | PEC local sediment DF = 1,000 | Factor risk sediment DF = 1,000 Total | Factor risk sediment DF = 1,000 Added |
| --- | --- | --- | --- | --- | --- | --- |
|  | mg/kg dry wt. | - | - | mg/kg dry wt. | - |  |
| Scenario 1/2 | 5.19 | 2.3 | 1.1 | 2.91 | 1.3 | 0.09 |

For all hypothetical local incineration scenarios a risk for sediment organisms is predicted. It should be noted that risk is always predicted even if local emissions are zero because the regional Cd concentration (90th percentile of measured data i.e. 2.66 mg/kg. dry wt. is already above the PNEC sediment. The risk factor based on total vary is 2.1 for the realistic worst case situation when a DF of 100 can be applied; and is 1.1 for a DF of 1,000. Based only on local emissions (i.e. without the background contribution), no risk is predicted for the scenario with the dlution factor of 1,000.

Table 3.3.14: Local risk characterisation incinerators for sediments (at dilution factor 100 and 1,000). The factor risk = PEC/PNEC. The PNECsediment is 2.3 mg/kg dry wt. The factor risk is calculated for the concentration of added Cd (Clocalsediment) and for the added+regional Cd (total Cd, i.e. PECsediment) without correction for bioavailability. Total cadmium without Ni-Cd contribution

|  | PEC local sediment DF = 100 | Factor risk sediment DF = 100 Total | Factor risk sediment DF = 100 Added | PEC local sediment DF = 1,000 | Factor risk sediment DF = 1,000 Total | Factor risk sediment DF = 1,000 Added |
| --- | --- | --- | --- | --- | --- | --- |
|  | mg/kg dry wt. | - | - | mg/kg dry wt. | - |  |
|  | Assumption Ni-Cd batteries contributed 10 % to the overall Cd load |
| Scenario 1/2 | 4.87 | 2.1 | 0.96 | 2.69 | 1.2 | 0.01 |
|  | Assumption Ni-Cd batteries contributed 50 % to the overall Cd load |
| Scenario 1/2 | 3.93 | 1.7 | 0.48 | 2.79 | 1.2 | 0,01 |

Removing all Ni-Cd batteries from the MSW stream has only a minor impact on the risk conclusions.

These results are based, however, on no correction for the bioavailability of cadmium in sediments (SEM/AVS method). A conclusion i) program is ongoing. Furthermore, an uncertainty analysis regards the impact of an EU-wide variability in PEC reg (as a default approach in the absence of site-specific data) on the risk characterisation at local level, is not yet included. Both aspects, bioavailability and variability impact, will be implemented in an update of the risk assessment report once the results of the concl 1) program are agreed at TC NES level (see separate document).

Future scenarios and sensitivity analysis MSW incinerators

Future scenario

Table 3.3.15: Local risk characterisation incinerator for water and STP (at dilution factor 100 and 1,000). Future scenarios: collection rate: 10 and 75%. The factor risk = PEC/PNEC. The PNECwater is 0.19 (g Cd/L. The PNEC for micro-organisms is 20 µg/L (Table 3.3.1). Total cadmium.

| Scenario | PEC local water DF = 100 | Factor risk water DF = 100 | PEC local water DF = 1,000 | Factor risk water DF = 1,000 | Ceffluent | Factor risk STP |
| --- | --- | --- | --- | --- | --- | --- |
|  | µg/L | - | µg/L | - | mg/L |  |
| MSW Incineration plant (10%; total cadmium) | 0.16 | 0.84 | 0.12 | 0.63 | 0.0135 | 0.68 |
| MSW Incineration plant (75%; total cadmium) | 0.14 | 0.74 | 0.12 | 0.63 | 0.007 | 0.35 |

Table 3.3.15 indicates no risks for the future hypothetical incineration plant (both scenarios) for aquatic organisms if a dilution factor of 1,000 is applicable. Performing the exercise for the different collection scenarios (10 and 75%) with a dilution factor of only 100 indicates also no risk for the aquatic compartment for both the 10 % and 75 % recycling scenario. No toxicity to off-site STP micro-organisms from the MSW local incineration plant is predicted for the future scenarios.

Removing all Ni-Cd batteries resembles the current scenario as presented in Table 3.3.12 (i.e.  assumption  at start that 10 % of the Cd load is due to Ni-Cd batteries).

Uncertainty analysis:

PNEC

It should be noted that an assessment factor of 2 has been included in the PNEC derivation due to remaining uncertainty.

The inclusion or exclusion of the assessment factor of 2 does not influence the conclusions.

Using measured regional values:

Aforementioned exposure estimations and risk assessment are based on calculated PEC reg (i.e. 0.11 µg/L). Preference should, however, be given to measured values when available. However in the absence of reliable and representative regional measured data in the vicinity of the individual sites the RCR values have also been calculated (results not shown)  using the average of the measured P90 values for different countries (i.e. 0.12 µg/L) and also using the median of the measured P90 values (i.e. 0.07 µg/L).The use of the measured regional PEC does not influence the conclusion of the risk characterisation.

Sediment (assessment without bioavailability correction)

For all future scenarios a risk is predicted for sediment organisms. Based only on local emissions (i.e. without the regional background contribution), no risk is predicted for the scenario with 10-75 % collection when a DF of 1,000 is applicable. A potential risk is still apparent for the 10-75 % collection when a DF of 100 is applied.

Table 3.3.16: Local risk characterisation incinerators for sediments for a generic MSW incineration plant in the EU. Future scenarios: collection rate: 10 and 75% (at dilution factor 100 and 1,000). The factor risk = PEC/PNEC. The PNECsediment is 2.3 mg/kg dry wt. The factor risk is calculated for the concentration of added Cd (Clocalsediment) and for the added+regional Cd (total Cd, i.e. PECsediment) without correction for bioavailability.  Total cadmium.

| Scenario | PEC local sediment DF = 100 | Factor risk sediment DF = 100 Total | Factor risk sediment DF = 100 Added | PEC local sediment DF = 1,000 | Factor risk sediment DF = 1,000 Total | Factor risk sediment DF = 1,000 Added |
| --- | --- | --- | --- | --- | --- | --- |
|  | mg/kg dry wt. | - | - | mg/kg dry wt. | - |  |
| MSW Incineration plant (10% collection; total cadmium) | 8.6 | 3.7 | 2.3 | 3.3 | 1.4 | 0.26 |
| MSW Incineration plant (75% collection; total cadmium) | 6.8 | 2.95 | 1.8 | 3.0 | 1.3 | 0.13 |

These results are based, however, on no correction for the bioavailability of cadmium in sediments (SEM/AVS method). A conclusion i) program is ongoing (see separate document).

Removing all Ni-Cd batteries resembles the current scenario as presented in Table 3.3.14 (i.e.  assumption  at start that 10 % of the Cd load is due to Ni-Cd batteries).

Sensitivity analysis

Table 3.3.17: Local risk characterisation incinerator for water and STP (at dilution factor 100 and 1,000). Sensitivity analysis: effluent = 0.009 mg/L. The factor risk = PEC/PNEC. The PNECwater is 0.19 (g Cd/L. The PNEC for micro-organisms is 20 µg/L (Table 3.3.1). Total cadmium.

| Scenario | PEC local water DF = 100 | Factor risk water DF = 100 | PEC local water DF = 1,000 | Factor risk water DF = 1,000 | Ceffluent | Factor risk STP |
| --- | --- | --- | --- | --- | --- | --- |
|  | µg/L | - | µg/L | - | mg/L |  |
| MSW Incineration plant (10%; total cadmium) | 0.14 | 0.68 | 0.13 | 0.68 | 0.009 | 0.45 |

Table 3.3.17 indicates no risks (both scenarios) for the aquatic compartment for a maximal measured effluent concentration of 0.009 mg/L

Table 3.3.18: Local risk characterisation incinerators for sediments for a generic MSW incineration plant in the EU. Sensitivity analysis: effluent = 0.009 mg/L (at dilution factor 100 and 1,000). The factor risk = PEC/PNEC. The PNECsediment is 2.3 mg/kg dry wt. The factor risk is calculated for the concentration of added Cd (Clocalsediment) and for the added+regional Cd (total Cd, i.e. PECsediment) without correction for bioavailability.  Total cadmium.

| Scenario | PEC local sediment DF = 100 | Factor risk sediment DF = 100 Total | Factor risk sediment DF = 100 Added | PEC local sediment DF = 1,000 | Factor risk sediment DF = 1,000 Total | Factor risk sediment DF = 1,000 Added |
| --- | --- | --- | --- | --- | --- | --- |
|  | mg/kg dry wt. | - | - | mg/kg dry wt. | - |  |
| MSW Incineration plant (10%; total cadmium) | 6.6 | 2.86 | 1.71 | 3.05 | 1.7 | 0.56 |

For all scenarios a risk is predicted for sediment organisms.. Based only on local emissions (i.e. without the regional background contribution), no risk is predicted when a dilution factor of 1,000 is applicable. These results are based, however, on no correction for the bioavailability of cadmium in sediments (SEM/AVS method). A conclusion i) program is ongoing (see separate document).

Risk characterisation for MSW landfills

Since cadmium emissions from landfills reflect always all cadmium sources a comparative risk assessment has been made. First the risk associated with the total cadmium emissions are given. This analysis is followed by the calculation of the risks associated with the total cadmium without Ni-Cd batteries.

Table 3.3.19: Local risk characterisation landfills (leachate concentration 5 µg/L) for water, sediment and STP. Scenario 1 = direct discharge to surface water. Scenario 2 = indirect discharge to surface water (STP). The factor risk = PEC/PNEC. The PNECwater is 0.19 (g Cd/L. The PNECsediment is 2.3 mg/kg dry wt.. The factor risk is calculated for the concentration of added Cd (Clocalsediment) and for the added+regional Cd (total Cd, i.e. PECsediment) without correction for bioavailability.The PNEC for micro-organisms is 20 µg/L (Table 3.3.1). Total cadmium

| use- category | N° | PEClocal water | factor risk water | PEClocal sediment | factor risk sediment Total | factor risk sediment Added | Ceffluent | Factor risk STP |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | µg /L |  | mg/kg dry wt. |  |  | mg/L |  |
| MSW landfill (total cadmium) | 1 | 0.12 | 0.63 | 3.8 | 1.6 | 0.5 | 0.005 | n.r. |
| MSW landfill (total cadmium) | 2 | 0.12 | 0.63 | 3.1 | 1.3 | 0.2 | 0.00024a | 0.012 |

n.r. = not relevant

a = 5 µg/L / 21  (21being the dilution factor in STP cfr Table 3.1.95)

No risks to the aquatic environment are observed for landfills emitting a leachate with total cadmium content of 5 µg/L.

A risk is observed for all scenarios for the sediment compartment. However, based only on local emissions (i.e. without the background contribution) no risk is predicted at landfills with a leachate concentration of 5 µg/L.

In Table 3.3.20 the RCR values for the scenario where all Ni-Cd batteries would be removed from the MSW stream is given.  The influence on the RCR values is negligible.

Table 3.3.20: Local risk characterisation landfills (leachate concentration 5 µg/L) for water, sediment and STP. Scenario 1 = direct discharge to surface water. Scenario 2 = indirect discharge to surface water (STP). The factor risk = PEC/PNEC. The PNECwater is 0.19 (g Cd/L. The PNECsediment is 2.3 mg/kg dry wt.. The factor risk is calculated for the concentration of added Cd (Clocalsediment) and for the added+regional Cd (total Cd, i.e. PECsediment) without correction for bioavailability.The PNEC for micro-organisms is 20 µg/L (Table 3.3.1). All cadmium without Ni-Cd batteries

| use- category | N° | PEClocal water | factor risk water | PEClocal sediment | factor risk sediment Total | factor risk sediment Added |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | µg /L |  | mg/kg dry wt. |  |  |
| MSW Landfill (Ni-Cd batteries contributed for 10 %) | 1 | 0.12 | 0.63 | 3.7 | 1.6 | 0.4 |
| MSW Landfill (Ni-Cd batteries contributed for 50 %) |  | 0.12 | 0.63 | 3.3 | 1.4 | 0.6 |
| MSW Landfill (Ni-Cd batteries contributed for 10 %) | 2 | 0.12 | 0.63 | 3.1 | 1.3 | 0.3 |
| MSW Landfill (Ni-Cd batteries contributed for 50 %) |  | 0.12 | 0.63 | 2.9 | 1.3 | 0.3 |

n.r. = not relevant

a = 5 µg/L / 21  (21being the dilution factor in STP cfr Table 3.1.95)

Sensitivity analysis

Table 3.3.21: Local risk characterisation landfills (leachate concentration 50 µg/L) for water, sediment and STP. Scenario 1 = direct discharge to surface water. Scenario 2 = indirect discharge to surface water (STP). The factor risk = PEC/PNEC. The PNECwater is 0.19 (g Cd/L. The PNECsediment is 2.3 mg/kg dry wt. The factor risk is calculated for the concentration of added Cd (Clocalsediment) and for the added+regional Cd (total Cd, i.e. PECsediment) without correction for bioavailability.The PNEC for micro-organisms is 20 µg/L (Table 3.3.1). Total cadmium.

| use- category | N° | PEClocal water | factor risk water | PEClocal sediment | factor risk sediment Total | factor risk sediment Added | Ceffluent | Factor risk STP |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | µg/L |  | mg/kg dry wt |  |  | mg/L |  |
| MSW landfill (total cadmium) | 1 | 0.21 | 1.1 | 14.9 | 6.5 | 5.3 | 0.050 | n.r. |
| MSW landfill (total cadmium) | 2 | 0.15 | 0.79 | 6.8 | 3 | 1.8 | 0.0024a | 0.12 |

n.r. = not relevant

a = 50 µg/L / 21  (21 being  the dilution factor in STP cfr Table 3.1.95)

No risks to the aquatic environment is observed for landfills emitting a leachate with a total cadmium content of 50 µg/L to a STP.  If this leachate concentration is discharged immediately to the surface water a risk is predicted for the scenario ‘all cadmium in MSW’. Based on PEC and PNEC values not corrected for bioavailability, a risk is observed for all scenarios for the sediment compartment. These results are based, however, on no correction for the bioavailability of cadmium in sediments (SEM/AVS method). A conclusion i) program is ongoing. Furthermore, an uncertainty analysis regards the impact of an EU-wide variability in PEC reg (as a default approach in the absence of site-specific data) on the risk characterisation at local level, is not yet included. Both aspects, bioavailability and variability impact, will be implemented in an update of the risk assessment report once the results of the concl 1) program are agreed at TC NES level (see separate document).

No risks are expected for the off-site STP.

Uncertainty analysis:

It should be noted that an assessment factor of 2 has been included in the PNEC derivation due to remaining uncertainty.

The uncertainty surrounding the PNEC water influences the risk conclusion for the landfill discharging a landfill leachate with a cadmium concentration of 50 µg/L directly in a river. If no assessment factor is applied this scenario would not have a local risk anymore  (RCR = 0.55) for the water compartment.

Using measured regional values

Aforementioned exposure estimations and risk assessment are based on calculated PEC reg (i.e. 0.11 µg/L). Preference should, however, be given to measured values when available. However in the absence of reliable and representative regional measured data in the vicinity of the individual sites the RCR values have also been calculated (results not shown)  using the average of the measured P90 values for different countries (i.e. 0.12 µg/L) and also using the median of the measured P90 values (i.e. 0.07 µg/L),

The use of the average measured regional PEC concentration (0.12 µg/L) or the median regional PEC concentration (0.07 µg/L) does not change the risk conclusions.

In Table 3.3.22 the RCR values for the scenario where all Ni-Cd batteries would be removed from the MSW stream is given.  The influence on the RCR values is negligible at the exception of the case where Ni-Cd batteries for their Cd content contribute to 50% of the MSW and the landfill leachate is directly discharged to surface water. In the latter case, a reduction of the factor risk water of 23.6% is obtained, resulting in a ‘no risk’ situation.

Table 3.3.22: Local risk characterisation landfills (leachate concentration 50 µg/L) for water and  sediment. Scenario 1 = direct discharge to surface water. Scenario 2 = indirect discharge to surface water (STP). The factor risk = PEC/PNEC. The PNECwater is 0.19 (g Cd/L. The PNECsediment is 2.3 mg/kg dry wt.. The factor risk is calculated for the concentration of added Cd (Clocalsediment) and for the added+regional Cd (total Cd, i.e. PECsediment) without correction for bioavailability.The PNEC for micro-organisms is 20 µg/L (Table 3.3.1). Total cadmium without Ni-Cd batteries

| use- category | N° | PEClocal water | factor risk water | PEClocal sediment | factor risk sediment Total | factor risk sediment Added |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | µg /L |  | mg/kg dry wt. |  |  |
| MSW Landfill (Ni-Cd batteries contributed for 10 %) | 1 | 0.20 | 1.1 | 13.7 | 6.0 | 4.8 |
| MSW Landfill (Ni-Cd batteries contributed for 50 %) |  | 0.16 | 0.84 | 8.8 | 3.8 | 2.7 |
| MSW Landfill (Ni-Cd batteries contributed for 10 %) | 2 | 0.14 | 0.7 | 6.3 | 2.7 | 1.6 |
| MSW Landfill (Ni-Cd batteries contributed for 50 %) |  | 0.13 | 0.68 | 4.7 | 2.0 | 0.9 |

n.r. = not relevant

a = 50 µg/L / 21  (21being the dilution factor in STP cfr Table 3.1.95)

#### The atmospheric compartment

No risk characterisation can be made since no data were found on Cd toxicity for organisms in the atmospheric compartment.

Calculated local PEC values range from 0.561 to 22.6 ng/m3 for Ni-Cd batteries producers and from 0.561 to 1.91 ng/m3 for Cd recycling plants.

The PEClocal in air at a distance of 100 m from a generic MSW incineration plant is 7.5 ng/m3 (average EU situation). Taking into account the contribution from batteries to the MSW (10%-50%), PEC local in air varies between 1.3 and 4.1 ng/m3.

In the worst case situation (France) a PEClocal in air of 28.5 ng/m3 can be calculated (all MSW). Taking into account the contribution from batteries to the MSW (10%-50 %), PEC local in air varies between 3.4 and 14.5 ng/m3.

#### The terrestrial compartment

Ni-Cd producing/recycling plants

The ratio PEC/PNEC for local soil risk assessment is given in Table 3.3.23. The PNECsoil value is 0.9 mg/kg dry wt and is the lowest for local risk assessment

No risk is predicted at all sites. The risk factors for soil are 0.5. This conclusion should be treated with caution. The local soil concentrations are calculated after 10 years exposure. In the section 3.1.3.1.3 it is mentioned that for Cd producing sites having high emissions to air (> 800 kg Cd/y) risk factors are above 1 when Cd concentrations are predicted in soil after 50 years aerial deposition. Since neither NiCd batteries producers nor Cd recyclers emit these high Cd quantities to air, the 50 years exposure calculation does not seem relevant in the context of this report.

MSW incinerators

No risk to soil organisms (nor higher food chain via secondary poisoning) is predicted at the hypothetical EU incineration plants.

Table 3.3.23: local risk characterisation for soil. The factor risk = PEC/PNEC. The PNEC value = 0.9 mg kg-dry wt. is equivalent to 0.79 mg kg wet wt. (standard environmental characteristics, TGD) and is the lowest for local risk assessment based on toxicity mammals through secondary poisoning (Table 3.3.1).

| Use-category | Plant N° | PEClocal soil | factor risk soil | Year |
| --- | --- | --- | --- | --- |
|  |  | mg kg wet wt. |  |  |
| Ni-Cd-batteries | 1 | 0.36 | 0.5 | 1999 |
|  | 2 | 0.36 | 0.5 | 1999 |
|  | 3 | 0.36 | 0.5 | 2000 |
|  | 4 | 0.37 | 0.5 | 2000 |
|  | 5 | 0.37 | 0.5 | 2000 |
|  | 6 | 0.36 | 0.5 | 1999 |
|  | 7 | 0.37 | 0.5 | 1999 |
| Cd recyclers | 1 | 0.36 | 0.5 | 2000 |
|  | 2 | 0.36 | 0.5 | 1999 |
| MSW incineration (all scenarios and total cadmium) |  | 0.36-0.3737 | 0.5 |  |

No future scenarios were developed for this compartment.

### Risk characterisation for all scenarios: update data (year 2002)

In the following subsections risk characterization is performed for those companies/sectors that submitted new exposure data (reference year 2002). This means that the current update assessment overwrites the RCR values and conclusions derived for corresponding companies/sectors reported in the previous stand-alone documents (global RAR, TRAR).

For the use scenarios ‘alloys’ and ‘plating’ no update exposure data were provided. Therefore the values and conclusions as previously reported remain valid.

#### The aquatic compartment (including sediment)

The risk factors (PEC/PNEC ratio) for WWTP/STP, local water (dissolved fraction) and sediment concentrations for the freshwater environment are given in Table 3.3.24. The PNEC was not corrected for water hardness because of lack of site-specific water hardness information.

Table 3.3.24: Local risk characterisation of Cd/CdO production/processing sites for WWTP/STP, water and sediment (modelled data). The factor risk = PEC/PNEC. The PNECmicro-organisms is 20 µg/l, The PNECwater is 0.19 (g Cd L-1 and the PNECsediment is 2.3 mg Cd kg-1dw.(Table 3.3.1). The factor risk for sediments is calculated for the concentration of added Cd (Clocalsediment, Table 3.1.137) and for the added+regional Cd (total Cd, i.e. PEClocalsediment, Table 3.1.137). The results for the sediment compartment are based on no correction for the bioavailability of cadmium in sediments (SEM/AVS method). A conclusion i) program is ongoing.

| plant N° | PECwwtp/stp (dissolved fraction) | factor risk wwtp/stp | PEClocalwater (dissolved Cd) | factor risk water | PEClocalsediment | factor risk sediment (added) | factor risk sediment (total) | year |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | µg L-1 |  | µg L-1 |  | mg kg-1dw |  |  |  |
| Cd metal production |  |  |  |  |  |  |  |  |
| 1 | 3.6(d) | n.r. | 0.64 | 3.36 | 71.5 | 29.9 | 31.1 | 2002 |
| 6 | 0.7 | n.r. | 0.11 | 0.58 | 2.7 | 0.01 | 1.2 | 2002 |
| 7* | 50* | n.r.* | 0.28* | 1.46 [1.25]* | 24.5* | 9.5* | 10.7* | 2002 |
| 7* | 30* | n.r. | 0.21* | 1.13 [0.92]* | 16.2* | 5.9* | 7.1* | 2004 |
| Cd oxide production |  |  |  |  |  |  |  |  |
| 12(a) | n.a. | n.a. | 0.11 | 0.58 | 2.7 | 0 | 1.2 | 2002 |
| Ni-Cd battery production |  |  |  |  |  |  |  |  |
| 2* | 107 | n.r. | 0.15 | 0.77 | 7.4 | 2.0 | 3.2 | 2002 |
| 3 | 63 | n.r. | 0.13 | 0.69 | 5.5 | 1.2 | 2.4 | 2002 |
| 4 | 103 | n.r. | 0.14 | 0.76 | 7.2 | 2.0 | 3.1 | 2002 |
| 6 | No update data |  |  |  |  |  |  |  |
| 7 | No update data |  |  |  |  |  |  |  |
| Ni-Cd battery recyling |  |  |  |  |  |  |  |  |
| 1 | 370 | n.r. | 0.24 | 1.24 | 19.0 | 7.1 | 8.2 | 2002 |
| 1(e) | 240 | n.r. | 0.19 | 1.01 | 13.2 | 4.6 | 5.8 | 2004 |
| 2(b) | n.a. | n.a. | n.a. | n.a. | n.a. | n.a. | n.a. | 2002 |
| Cd pigments production |  |  |  |  |  |  |  |  |
| A | 19 | n.r. | 0.38 | 1.98 | 37.4 | 15.1 | 16.2 | 2003 |
| B | 19 | n.r. | 0.12 | 0.61 | 3.5 | 0.4 | 1.5 | 2003 |
| C | 121 | n.r. | 0.25 | 1.32 | 21.0 | 8.0 | 9.1 | 2003 |
| C(90P) | 80 | n.r. | 0.25 | 1.34 | 21.3 | 8.1 | 9.3 | 2004 |
| Cd stabiliser producton |  |  |  |  |  |  |  |  |
| X WWTP | 5 | 0.25 |  |  |  |  |  |  |
| X STP© | 0.4 | 0.02 | 0.11 | 0.58 | 2.7 | 0.02 | 1.2 | 2002 |
| Y | <5(f) | n.r. | 0.12 | 0.62 | 3.6 | 0.4 | 1.5 | 2002 |
| Y | <1(g) | n.r. | 0.11 | 0.59 | 2.8 | 0.1 | 1.2 | 2002 |

*Emission to the sea: risk characterisation is only indicative and based on PNEC freshwater and PECreg water for freshwater. For water, Industry (Cd metal producer site 7) proposes to use 0.07 µg/l as local (regional?) background concentration as done by NIVA (NIVA report 4606-2002) resulting in a lower RCR value of 1.25 (2002) and 0.92 (2004) respectively. However, MSR could not validate this latter value. No formal conclusions are drawn for sites emitting to the marine environment; n.a.: not applicable; n.r.: not relevant for the on-site wwtp (only physc-chem based) (a) No emission to water; thermal/dry process; (b) No site emission to water. Cleaning water as well as processing water are collected internal (about 100 m3/year) and send to an external waste water treatment plant. c) Cd concentration in effluent from municipal STP; calculated from Cd concentration in effluent from on site WWTP; taking into account removal at STP: 60%; extra dilution: 2000 m3/d/370 m3/d = 5.4. (d) the biological based wastewater purification system contains fully adapted, specialised and dedicated micro-organisms. These bacteria are not at all representative for ‘standard’ micro-organisms communities used in municipal STPs. (e) Emissions from the site are further reduced in 2003/2004 due to efforts to conform to ISO 14000, for which the site has been certified in February 2005; (f) effluent analysis performed by internal laboratory (two times a month) method MIP-P-PRO-101 rev 2 year 2003; (g) effluent analysis performed by accreditated external laboratory (two times a year), method EPA 200.8 (1994).

From Table 3.3.24 it can be concluded that risks for freshwater aquatic organisms occur at 1 Cd metal production sites (site 1), 1 Ni-Cd battery recycling site (site 1) and 2 Cd-pigments producing sites (site A, C). It is to be noted that Cd metal producing plant 7 and NiCd production site 2 emit effluents to the marine environment. No risk assessment to the marine environment is done in this report. No formal conclusions are drawn for thess sites. The PECs presented in Table 3.3.24 are ‘calculated’ local concentrations.

Measured Cd concentrations in surface water –presented in Table 3.1.138 - are available for Cd metal production site 1 and 7 and Ni-Cd battery recycling site 1 and Cd stabiliser site Y.

In conclusion:

- Locally measured data near the Cd producer site 1 (i.e. 1 µg dissolved Cd/l; downstream from the site; including background and possible other sources) point there is predicted risk (risk factor: 5.3).

- For recycling site 1, risk is predicted as well by the locally measured data (i.e. 19.8 µg dissolved Cd/l, downstream from the discharge point; risk factor: 104) that however include the background and possibly other sources (historical contamination due to infiltration and run-off from old metallurgical slag heaps).

- Measurements at Cd stabiliser site Y are based on not sufficiently sensitive analytical method (detection limit too high) to make a judgment about the background and added concentrations in the receiving river.

Monitoring data are not available for any CdO producing or Cd metal/CdO processing company.

Marine environment:

- The risk characterisation for the marine environment (Cd metal producer site 7 and NiCd battery producer site 2) is based on PNECfreshwater and PECreg water for freshwater. Therefore the risk characterisation for this site is only indicative. No risk assessment to the marine environment is done in this report. Industry’s representative for the Cd metal producer site 7 proposes to use 0.07 µg/l as local (regional?) background concentration as done by NIVA (NIVA report 4606-2002) resulting in a lower RCR value of 1.25 (2002) and 0.92 (2004) respectively. However, MSR could not validate this latter value.

Uncertainty analysis:

The uncertainty surrounding the PNEC water is related to several aspects: statistical aspects (confidence limits on the HC5 estimated from the SSD) and more general concerns such as species representativity, the inherent uncertainty about NOEC values compared to the benchmark values, mixed pollution,… These factors have crystallised in the AF=2 which was agreed . The uncertainty around the PNEC water influences the risk conclusion for Cd recycling plant 1 and Cd pigment plants A and C. If no assessment factor is applied the sites would not have a local risk anymore (RCR = 0.6-0.99) for the water compartment.

Using measured regional values:

Aforementioned exposure estimations and risk assessment are based on calculated PEC reg (i.e. 0.11 µg/L). Preference should, however, be given to measured values when available. However in the absence of reliable and representative regional measured data in the vicinity of the individual sites the RCR values have also been calculated (results not shown) using the average of the measured P90 values for different countries (i.e. 0.12 µg/L) and also using the median of the measured P90 values (i.e. 0.07 µg/L).

The use of the average measured regional concentration (0.12 µg/L) or the median of the measured P90 values (0.07 µg/L) does not change the risk conclusions (based on 2002 exposure data) for the Cd metal/CdO producing or processing sites.

On the basis of PEC and PNEC values not corrected for bioavailability, risk for benthic organisms is predicted at all sites (PEClocal sediment). Most sites involved in Cd production and processing have a risk for benthic organisms irrespective of the regional background (Clocalsediment > PNECsediment) (Cd metal production site 1 (risk factor: 29.9); Ni-Cd battery production site 2, 3, 4 (risk factor: 1.2-2.0); Ni-Cd battery recycling site 1 (risk factor: 4.6-7.1) and Cd pigments production site A, C (risk factor: 8.0-15.1)

Measured Cd concentrations in sediments (without correction for bioavailability) –presented in Table 3.1.139- are available for all Cd metal producing sites, Ni-Cd battery manufacturing site 4 and Cd recycling site 1.

- For Cd metal production site 1, the measured Cd concentration in sediment sampled upstream and downstream near the discharge point is 5 mg/kg dw and 1.6 mg/kg dw respectively. Although still resulting in a risk factor above 1 (for the upstream Cd concentration i.e. 2.2) it is obvious that measured Cd concentrations are situated a factor 14-45 below the predicted concentrations; hence the risk is reduced. This site also submitted information on AVS and organic carbon content of the sediments. Using these data, the risk characterisation could further be refined (cfr outcome of concl. i) program, see separate document).

- Cadmium metal production site 6 provides recent upstream and downstream measurements in sediments of 0.64 mg Cd/kg dw and 1.14 mg Cd/kg dw respectively (year 2002). As for site 1, the measured Cd concentrations are below the calculated PECsediment (2.4-4.2 times lower). Risk factors on the basis of measured data are 0.27-0.50 respectively, hence the risk is removed.

- Ni-Cd battery manufacturing site 4 provides recent upstream and downstream measurements in sediments of 3.3 mg Cd/kg dw (100 m upstream) and 4.6 mg Cd/kg dw (3 km downstream) respectively (year 2001). Measured Cd concentrations are situated 1.6-2.2 times below the modelled sediment concentrations. On the basis of these data, the risk is reduced; risk factors varying between 1.4 and 2 are calculated. Please note that the sampling downstream is performed at a location 3 km downstream of the plant; hence influence from other sources is likely.

- Cd recycling site 1 provides recent upstream and downstream measurements in sediments of 55 mg/kg dw and 133 mg/kg dw respectively (year 2002). The measured Cd concentrations are 3-7 fold the calculated PEClocal sediment of 19.0 mg/kg dw. On the basis of these data, risk is confirmed; risk factors are 24-58. Please note that the measured data are influenced by historical contamination (infiltration and run-off waters from old metallurgical slag heaps), hence data should be treated with caution.

For all these scenarios and sites, risk is also predicted based on the measured data that include background and possible other sources.

Monitoring data are not available for any CdO producing or other Cd metal/CdO processing company/sector.

These results are based, however, on no correction for the bioavailability of cadmium in sediments (SEM/AVS method). A conclusion i) program is ongoing (see separate document: ‘RAR Stage II’).

Marine environment:

- For Cd metal production site 7, discharging in a marine environment, Cd concentrations in sediment are reported near the discharge point for the sampling year 1996: 1.1 mg/kg dw and in the open sea: 2.1-3.2 mg/kg dw. The same observation is made as for the other Cd metal producing plants. Measured Cd concentrations, representative for the year 1996, are situated 7.7-22.3 times below the modelled sediment concentrations. On the basis of these ‘old’ data; a risk factor ‘near the discharge point’ of 0.48 would be calculated.

The risk characterisation for the marine environment is only indicative as no PNEC was derived for marine species and the PEC regional is calculated for freshwater. No conclusions are drawn on the sites emitting to the sea.

The risk for micro-organisms in sewage treatment plants is investigated for on-site waste water treatment plants (WWTP) as well as off-site sewage treatement plants (STP).

On-site waste water treatment plants:

Information from the specific production and processing sites indicates that methods to remove cadmium from discharge to water are generally in place. However, in general no detailed and/or measured data are available.

Most wastewater treatment at the plants in the Cd production area is based on physical-chemical principles only (see also IPPC report on the best available techniques in the non ferrous metals industries, May 2000). Similar information was confirmed for NiCd battery producers and recyclers (cfr TRAR/batteries’ related sections, Industry Questionnaire 2002/2003) and Cd containing pigments producers (pers. com., 2005). One Cd metal production plant reports the use of a biological based wastewater purification system that contains fully adapted, specialised and dedicated micro-organisms. It is clear that this type of industrial on-site waste water treatment plant cannot be compared with municipal STPs based on ‘standard’ micro-organism communities. Therefore, it is decided that for the aforementioned sectors, the derivation of the risk factor for the wwtp is not relevant (n.r.) (Table 3.3.24).

Off-site waste water treatment plants (municipal sewage treatment plants):

For producers of Cd metal and CdO, no discharge occurs to municipal sewage systems, as these sites do emit to surface/sea water or do not emit at all to the aquatic compartment. Therefore, the risk assessment of Cd and CdO producers for off site STP is not relevant.

Risk to off site STP is only relevant for the processors that have actual emissions to sewer systems. One stabiliser production site (site X) reported to discharge its waste water to a municipal STP. Taking into account Cd removal and extra dilution of the WWTP effluent at the municipal STP (discharge rate STP/discharge rate WWTP=5.4) results in an STP effluent concentration of 0.4 µg/l. Consequently a risk factor of 0.02 is calculated, resulting in a no risk situation for this site.

NiCd battery recycling site 2 reports that waste waters are collected and treated off-site in an external waste water treatment plant (year 2002 data: total volume of waste water: 100 m3/year; no further data are available) (year 1996 data: 35 tonnes fluid waste per year; Cd content: 20 ppm (total Cd); effluent concentration of off-site STP: 0.2 mg/l). Although the site does not directly discharge any waste water to the receiving environment, the effluent concentration of the off-site STP is taken forward in the risk characterisation. Since the PECSTP of 200 µg Cd/l exceeds the PNECmicro-organims of 20 µg/l, a risk occurs at the off-site sewage treatment plant (risk factor = 10).

Conclusions to the risk assessment for the aquatic compartment:

(i)	There is a need for further information and/or testing.

This conclusion applies to the………………………………………….

- For the aquatic compartment, there is a need for better information regarding the toxic effects of cadmium to aquatic organisms under low water hardness conditions

In particular, information is required on:

Cd toxicity testing in very soft waters (H below about 10mg CaCO3/L). There are no data for the very soft waters and these areas may be unprotected by the proposed PNECwater for soft water (0.08 µg Cd/L)

- For sediment, there is a need for further information regarding the bioavailability of cadmium in order to possibly refine the assessment at regional and local level.

In particular:

the AVS and oc normalisation should be further validated (cfr outcome of concl i) study program, see separate document, ‘RAR Stage II’)

(ii)	There is at present no need for further information and/or testing and no need for risk reduction measures beyond those, which are being applied already.

This conclusion applies to the ……………………………………………………….

-	the local surface water compartment for the CdO production site and Cd recycling plant 2 because there are no emissions to water at these sites.

-	the local surface water compartment for Cd metal production site 6, the Ni-Cd battery producing plants (2, 3, 4), Cd pigments producing site B and all Cd stabilizer production sites (X, Y) emitting to the aquatic compartment.

-	no risk is predicted for the local sediment compartment for the CdO production site and NiCd recycling plant 2 because there are no emissions to water and no additional risk arises from their operations.

-	no risk is predicted for the micro-organisms of the STP for Cd stabilizer production site X discharging its effluent to a municipal STP

(iii)	 There is a need for limiting the risks; risk reduction measures which are already being applied shall be taken into account

This conclusion applies to the assessment of:

-	the local surface water (freshwater) at 1 Cd metal production sites (1) 1 Ni-Cd battery recycling site (1) and two Cd pigments producing sites (A, C). Local concentrations are based on modeling. Monitoring data are available for the Cd metal production site 1and the NiCd recycling site 1: these data indicate risk at background level but do not allow a judgment regards potential additional risk caused by the site’s operations.

-	a risk is predicted for the micro-organisms of the STP for NiCd battery recycling plant 2 discharging its effluent to an off-site STP.

#### The terrestrial compartment

The ratio PEC/PNEC for local soil risk assessment is given in Table 3.3.25. The selected PNECsoil value is 0.9 mg kg-1dw, which is the lowest PNECsoil value and which is based on secondary poisoning to mammals (Table 3.3.1).

Table 3.3.25: Local risk characterisation for soil (modelled data). The factor risk = PEC/PNEC. The PNEC value = 0.9 mg kg-1dw is equivalent to 0.79 mg kg-1ww (standard environmental characteristics, TGD) and is the lowest for local risk assessment based on toxicity mammals through secondary poisoning (Table 3.3.1).

| Plant N° | PEClocal soil | factor risk soil | Year |
| --- | --- | --- | --- |
|  | mg kgww-1 |  |  |
| Cd metal production |  |  |  |
| 1 | 0.37 | 0.47 | 2002 |
| 6 | 0.36 | 0.46 | 2002 |
| 7 | 0.38 – 0.45(d) | 0.48 – 0.57 | 2002 |
| Cd oxide production |  |  |  |
| 12 | 0.36 | 0.46 | 2005 |
| 12 | 0.36 | 0.46 | 2004 |
| Ni-Cd battery production |  |  |  |
| 2(a) | 0.36 | 0.46 | 2002 |
| 3(b) | n.d. | n.d. | n.d. |
| 4 | 0.36 | 0.46 | 2002 |
| 6 | No update data |  |  |
| 7 | No update data |  |  |
| Ni-Cd battery recyling |  |  |  |
| 1 | 0.36 | 0.46 | 2002 |
| 1 | 0.36 | 0.46 | 2004 |
| 2 | 0.36 | 0.46 | 2002 |
| 2bis(c) | 0.36 | 0.46 | 2002 |
| Cd pigments production |  |  |  |
| A | 0.36 | 0.46 | 2003 |
| B | 0.36 | 0.46 | 2003 |
| C | 0.36 | 0.46 | 2003 |
| Cd stabiliser producton |  |  |  |
| X | 0 | 0.46 | 2002 |
| Y | 0.36 | 0.46 | 2002 |

(a) Emission from battery manufacturing only; air emissions are broken down between two plants; battery manufacturing and Cd recycling; (b) Air emissons are not monitored. No requirement in the permit since the plant runs a wet process, therefore most emissions are releases in the water. (c) Emissions from Cd recycling unit on the site of battery manufacturing plant 4. (d) PEClocal soil derived on the basis of measured aerial deposition rates; n.d.: no data available.

Calculated PEClocalsoil values for all Cd/CdO production and processing sites are situated between 0.36 mg/kg ww and 0.45 mg/kg ww. Since the modelled PECsoil are situated below the PNECsoil -based on toxicity for mammals through secondary poisoining-, none of the sites are predicted to be at risk (risk ratio: 0.6).

Comparing the modelled PECsoil for the local sites with the PNECsoil of 1.15-2.3 mg/kg dw -based on ecotoxicity for soil organisms- results in the same conclusions i.e. no local risks are predicted (risk ratio: 0.2-0.4).

(ii)	There is at present no need for further information and/or testing and for risk reduction measures beyond those which are being applied already

This conclusion applies to the assessment of:

-	modelled local soil Cd concentrations for Cd metal/CdO production and processing plants  (10 years aerial deposition) indicate no risks neither for the terrestrial eco-system nor for mammals via secondary poisoning.

#### The atmospheric compartment

No risk characterisation can be made since no data were found on Cd toxicity in the atmospheric compartment.

For Cd metal producers, calculated local PEC values range from 8.2 to 41.8 ng/m3.

For the CdO production plant the local PEC value is varying from 5.6 ng/m3 (year 2005) to 9.4 ng/m3.

At the Cd/CdO processing plants the PEClocal in air (at a distance of 100 m) are in the following range:

Production of Ni-Cd batteries: 3.2 ng/m3 and 4.4 ng/m3

Recycling of Ni-Cd batteries: 0.6 ng/m3 and 3.6 ng/m3

Production of Cd containing pigments: 2.5 and 4.8 ng/m3

Production of Cd containing stabilisers: 0.6 and 1.0 ng/m3

Measurements for the Cd metal producers indicate that annual average Cd concentration– in air at a distance of  300 m - 450 m from the site vary between 1.8 and 8.5 ng/m3.

For Ni-Cd battery production site 4 an annual average Cd concentration of 0.3 ng/m3 (50 m from the site) is reported.

For NiCd recycling site 1, the measured data lay in the range of 37 to 126 ng/m3 (year 2002) and from 15 to 21 ng/m3 (year 2004), a factor 20 to 35 higher than the calculated values.

However, it should be born in mind that measured data have been reported to be influenced also or very probably by other (industrial) sources. In all cases except one i.e. Cd metal production site 7, the contribution of specific sources has not (yet) been investigated (semi)quantitatively.

#### Non compartment specific effects relevant for the food chain (Secondary poisoning)

Effects of soil-borne Cd on mammals has already been included in the previous section since this pathway is more critical than direct effects on higher plants, soil fauna or soil microbial processes.

No further changes are made to this section.

# HUMAN HEALTH

See separate document.

# CONCLUSIONS/RESULTS

## introduction

Remarks on the scope, the approach and the limitations of the study are given in section 0.1.

An overview of the batteries’ disposal scenarios is depicted in Figure 5.1.

Temporary note: conclusions are updated with exposure data for the reference year 2002.

|  | Regional scenarios |  |
| --- | --- | --- |
|  | 100 % incineration |  | 24.4 % incineration-75.6 % landfill |  | 100 % landfill |
|  | Current | Future |  | Current |  | Current |
|  | Total Cd content 10 g/tonne dry wt. Cd contribution from Ni-Cd batteries: 10-50 % | 10 % collection, total Cd content: 24 g/tonne dry wt. Cd contribution from Ni-Cd batteries: 63 % 75 % collection, total Cd content: 13.2 g/tonne dry wt. Cd contribution from Ni-Cd batteries: 32 % |  | Total Cd content 10 g/tonne dry wt. Cd contribution from Ni-Cd bat.: 10-50 % Total Cd concentration in leachate concentration : 5 µg/L |  | Total Cd concentration in leachate concentration : 5 µg/L Cd contribution from Ni-Cd bat.: 10-50 % |
|  |  |  | Local scenarios |  |  |
|  | Local scenarios future emissions incinerators (equipped with an on-site WWTP) |  | Local scenarios current emissions incinerators (equipped with an on-site WWTP) |  | Local scenarios emissions landfills |
|  | 75 % | 75 % | 10 % | 10 % |  | 90th P effluent concentration: 0.005 mg/L |  | 5 µg/L | 5 µg/L | 50 µg/L | 50 µg/L |
| Dilution factor | 100 | 1,000 | 100 | 1,000 | Dilution factor | 100 | 1,000 | 100 | 1,000 | Treatm. | STP | No STP | STP | No STP |

Figure 5.1: Overview of the different regional and local scenarios for the disposal phase taken forward in this report (batteries’ related sections)

## local level: current situation (=updated with 2002 data and assessment)

### Conclusions on cadmium metal

ENVIRONMENT: AQUATIC ECO-SYSTEM

(X)	i)	There is a need for further information and/or testing

(X)	ii)	There is at present no need for further information and/or testing or for			risk reduction measures beyond those which are being applied

(X)	iii) 	There is a need for limiting the risks: risk reduction measures which are already being applied shall be taken into account

Conclusion [i] is reached because:

- the AVS and OC based normalisation should be further validated to refine the risk characterisation to benthic organisms (on local as well as on regional level).

- there is a need for testing the Cd toxicity in very soft waters (H below about 10 mg CaCO3/L). There are no data for the very soft waters and these areas may be unprotected by the proposed PNECwater for  soft water (0.08 µg Cd L-1)

Conclusion [ii] is reached because:

- no risk is predicted for the aquatic ecosystem at the NiCd recycling site 2 because there are no emissions to water at this site

- no risk is predicted for the aquatic ecosystem at Cd metal production site 6, NiCd battery procuding sites (2, 3, 4), Cd pigments producing site B and all (two) Cd stabiliser production sites (X, Y) emitting to the aquatic compartment

- No risk is anticipated for aquatic organisms at 2 of the 5 Ni-Cd producing plants because they are not emitting to the aquatic compartment

- No risk is anticipated for aquatic organisms at a hypothetical landfill currently releasing a leachate with 5 µg/L of cadmium directly or indirectly in the aquatic environment

- No risks to aquatic organisms are anticipated for current hypothetical incinerator (equipped with an on-site WWTP) total Cd emissions discharging in a river with a dilution factor of 100  to 1,000. Removal of Ni-Cd batteries in the MSW has a negligible influence on the calculated risk ratios

- There is no risk for micro-organisms if the hypothetical landfill site is discharging a leachate with a cadmium concentration of 5µg/L to a STP.

- There is no risk for micro-organisms if the hypothetical incinerator plant (equipped with an on-site WWTP) is discharging to a STP.

Conclusion [iii] is reached because:

- there is a predicted local risk for the freshwater aquatic ecosystem at 5 Cd production (cadmium metal: 1 site) or Cd processing (pigments producing sites (A,C), plating and alloy) sites/scenarios. Both latter two are generic scenarios (‘Cd plating’ and ‘Cd alloys’). Local concentrations are based on modelling using site-specific and/or standard default values and could possibly have been refined if substantial monitoring data would have been provided. Monitoring data are available for the Cd metal production site 1: these data indicate risk at background level but do not allow a judgment regards potential additional risk caused by the site’s operations.

- There is anticipated local risk at 1 recycling site where modelled freshwater Cd concentrations exceed the PNECwater. This risk would be removed if no assessment factor (i.e. 2 and reflecting the uncertainty) is applied in deriving the PNEC. Monitoring data are available for this site: these data indicate risk at background level but do not allow a judgment regards potential additional risk caused by the site’s operations.

ENVIRONMENT: TERRESTRIAL ECO-SYSTEM

( )	i)	There is a need for further information and/or testing

(X)	ii)	There is at present no need for further information and/or testing or for			risk reduction measures beyond those which are being applied

(X)	iii)	There is a need for limiting the risks: risk reduction measures which			are already being applied shall be taken into account

Conclusion [ii] is reached because:

- modelled local soil Cd concentrations for Cd metal production and processing plants (10 years aerial deposition) indicate no risk.

- modelled local soil Cd concentrations for NiCd batteries producing and Cd recycling plants (10 years aerial deposition) indicate no risks neither for the terrestrial eco-system nor for mammals via secondary poisoning.

- modelled local soil Cd concentrations for the hypothetical MSW incineration plant (equipped with an on-site WWTP) indicate no risks neither for the terrestrial eco-system nor for mammals via secondary poisoning.

Conclusion [iii] is reached because:

(	there is a need for limiting the potential risks of cadmium plating and alloy production sites.

ENVIRONMENT: ASSESSMENT OF SECONDARY POISONING

( )	i)	There is a need for further information and/or testing

(X)	ii)	There is at present no need for further information and/or testing or for			risk reduction measures beyond those which are being applied

( )	iii)	There is a need for limiting the risks: risk reduction measures which		are already being applied shall be taken into account

Conclusion [ii] is reached because

- modelled local soil Cd concentrations for Cd metal production and processing plants (10 years aerial deposition) indicate no risk.

- modelled local soil Cd concentrations for NiCd batteries producing and Cd recycling plants (10 years aerial deposition) indicate no risks neither for the terrestrial eco-system nor for mammals via secondary poisoning.

- modelled local soil Cd concentrations for the hypothetical MSW incineration plant (equipped with an on-site WWTP) indicate no risks neither for the terrestrial eco-system nor for mammals via secondary poisoning.

ENVIRONMENT: ATMOSPHERE

(  )	i)	There is a need for further information and/or testing

(  )	ii)	There is at present no need for further information and/or testing or for			risk reduction measures beyond those which are being applied

(  )	iii)	There is a need for limiting the risks: risk reduction measures which		are already being applied shall be taken into account

Conclusion (   ) is reached because:

No risk characterisation was done for the atmosphere.

SEWAGE TREATMENT PLANT

(  )	i)	There is a need for further information and/or testing

(  )	ii)	There is at present no need for further information and/or testing or for			risk reduction measures beyond those which are being applied

(X )	iii)	There is a need for limiting the risks: risk reduction measures which		are already being applied shall be taken into account

Conclusion [iii] is reached because:

- risk to on-site and off-site STP cannot be excluded for plating and alloy industry.

- risk is predicted for the micro-organisms of the STP for the NiCd battery recycling plant (site 2) discharging its effluent to an off-site STP

### Conclusions on cadmium oxide

ENVIRONMENT: AQUATIC ECO-SYSTEM

(X)	i)	There is a need for further information and/or testing

(X)	ii)	There is at present no need for further information and/or testing or for			risk reduction measures beyond those which are being applied

(X)	iii) 	There is a need for limiting the risks: risk reduction measures which are already being applied shall be taken into account

Conclusion [i] is reached because:

- the AVS and OC based normalisation should be further validated to refine the risk characterisation to benthic organisms (on local as well as on regional level).

- there is a need for testing the Cd toxicity in very soft waters (H below about 10 mg CaCO3/L). There are no data for the very soft waters and these areas may be unprotected by the proposed PNECwater for  soft water (0.08 µg Cd L-1)

Conclusion [ii] is reached because:

- no risk is predicted for the aquatic ecosystem at the NiCd recycling site 2 because there are no emissions to water at this site

- no risk is predicted for the aquatic ecosystem at Cd metal production site 6, NiCd battery procuding sites (2, 3, 4), Cd pigments producing site B and all (two) Cd stabiliser production sites (X, Y) emitting to the aquatic compartment

- No risk is anticipated for aquatic organisms at 2 of the 5 Ni-Cd producing plants because they are not emitting to the aquatic compartment

- No risk is anticipated for aquatic organisms at a hypothetical landfill currently releasing a leachate with 5 µg/L of cadmium directly or indirectly in the aquatic environment

- No risks to aquatic organisms are anticipated for current hypothetical incinerator (equipped with an on-site WWTP) total Cd emissions discharging in a river with a dilution factor of 100  to 1,000. Removal of Ni-Cd batteries in the MSW has a negligible influence on the calculated risk ratios

- There is no risk for micro-organisms if the hypothetical landfill site is discharging a leachate with a cadmium concentration of 5µg/L to a STP.

- There is no risk for micro-organisms if the hypothetical incinerator plant (equipped with an on-site WWTP) is discharging to a STP.

Conclusion [iii] is reached because:

- there is a predicted local risk for the freshwater aquatic ecosystem at 5 Cd production (cadmium metal: 1 site) or Cd processing (pigments producing sites (A,C), plating and alloy) sites/scenarios. Both latter two are generic scenarios (‘Cd plating’ and ‘Cd alloys’). Local concentrations are based on modelling using site-specific and/or standard default values and could possibly have been refined if substantial monitoring data would have been provided. Monitoring data are available for the Cd metal production site 1: these data indicate risk at background level but do not allow a judgment regards potential additional risk caused by the site’s operations.

- There is anticipated local risk at 1 recycling site where modelled freshwater Cd concentrations exceed the PNECwater. This risk would be removed if no assessment factor (i.e. 2 and reflecting most of the uncertainty) is applied in deriving the PNEC. Monitoring data are available for this site: these data indicate risk at background level but do not allow a judgment regards potential additional risk caused by the site’s operations.

ENVIRONMENT: TERRESTRIAL ECO-SYSTEM

( )	i)	There is a need for further information and/or testing

(X)	ii)	There is at present no need for further information and/or testing or for			risk reduction measures beyond those which are being applied

(X)	iii)	There is a need for limiting the risks: risk reduction measures which		are already being applied shall be taken into account

Conclusion [ii] is reached because:

- modelled local soil Cd concentrations for Cd metal production and processing plants (10 years aerial deposition) indicate no risk.

- modelled local soil Cd concentrations for NiCd batteries producing and Cd recycling plants (10 years aerial deposition) indicate no risks neither for the terrestrial eco-system nor for mammals via secondary poisoning.

- modelled local soil Cd concentrations for the hypothetical MSW incineration plant (equipped with an on-site WWTP) indicate no risks neither for the terrestrial eco-system nor for mammals via secondary poisoning.

Conclusion [iii] is reached because:

(	there is a need for limiting the potential risks of cadmium plating and alloy production sites.

ENVIRONMENT: ASSESSMENT OF SECONDARY POISONING

( )	i)	There is a need for further information and/or testing

(X)	ii)	There is at present no need for further information and/or testing or for			risk reduction measures beyond those which are being applied

( )	iii)	There is a need for limiting the risks: risk reduction measures which		are already being applied shall be taken into account

Conclusion [ii] is reached because

- modelled local soil Cd concentrations for Cd metal production and processing plants (10 years aerial deposition) indicate no risk.

- modelled local soil Cd concentrations for NiCd batteries producing and Cd recycling plants (10 years aerial deposition) indicate no risks neither for the terrestrial eco-system nor for mammals via secondary poisoning.

- modelled local soil Cd concentrations for the hypothetical MSW incineration plant (equipped with an on-site WWTP) indicate no risks neither for the terrestrial eco-system nor for mammals via secondary poisoning.

ENVIRONMENT: ATMOSPHERE

(  )	i)	There is a need for further information and/or testing

(  )	ii)	There is at present no need for further information and/or testing or for			risk reduction measures beyond those which are being applied

(  )	iii)	There is a need for limiting the risks: risk reduction measures which		are already being applied shall be taken into account

Conclusion (   ) is reached because:

No risk characterisation was done for the atmosphere.

SEWAGE TREATMENT PLANT

(  )	i)	There is a need for further information and/or testing

(  )	ii)	There is at present no need for further information and/or testing or for			risk reduction measures beyond those which are being applied

(X )	iii)	There is a need for limiting the risks: risk reduction measures which		are already being applied shall be taken into account

Conclusion [iii] is reached because:

- risk to on-site and off-site STP cannot be excluded for plating and alloy industry.

- risk is predicted for the micro-organisms of the STP for the NiCd battery recycling plant (site 2) discharging its effluent to an off-site STP

## local level: disposal step: future situation and/or and sensitivity analysis

### Conclusions on cadmium metal and cadmium oxide

ENVIRONMENT: AQUATIC ECO-SYSTEM

(X)	i)	There is need for further information and/or testing

(X)	ii)	There is at present no need for further information and/or testing or for		 	risk reduction measures beyond those which are being applied

(X)	iii) and iii)*	There is a potential need for limiting the risks

Conclusion [i] is reached because:

- the AVS and oc based normalisation should be further validated to refine the risk characterisation to benthic organisms1 (on local as well as on regional level).

Conclusion [ii] is reached because:

- If a hypothetical landfill site discharge a leachate  with a cadmium concentration of 50 µg/L indirectly to surface water (i.e. via STP) no risk to aquatic organisms is expected

- If only the Ni-Cd contribution is taken into account there is also no risk to aquatic organisms predicted for landfills emitting directly to the surface water.

- No risk is anticipated to the micro-organisms in case a hypothetical incinerator, equipped with an on-site WWTP, discharges to a STP under the 75 % or 10 % collection scenario and landfill emitting a leachate at 50 µg Cd/L to an STP.

- No risks to aquatic organisms are anticipated for the future hypothetical incinerator, equipped with an on-site WWTP, (both scenario's: 10-75 % collection)  discharging in a river with a dilution factor of 100  to 1,000.

- No risks to aquatic organisms are anticipated for a hypothetical incinerator, equipped with an on-site WWTP, discharging a maximum effluent concentration of 0.007-0.0135 mg/L in a river with a dilution factor of 100  to 1,000.

Conclusion [iii] is reached because

- There is a potential risk if a hypothetical landfill site discharge a leachate  with a cadmium concentration of 50 µg/L directly to surface water. Removal of Ni-Cd batteries (if contributing to 50% of the Cd content in MSW) will remove the risk.

ENVIRONMENT: TERRESTRIAL ECO-SYSTEM/ SECONDARY POISONING

( )	i)	There is need for further information and/or testing

( )	ii)	There is at present no need for further information and/or testing or for		 	risk reduction measures beyond those which are being applied

( )	iii)	There is a need for limiting the risks: risk reduction measures which are  			already being applied shall be taken into account

Conclusion [] is reached :

No assessment was done neither for the terrestrial compartment nor for secondary poisoning.

ENVIRONMENT: ATMOSPHERE

( )	i)	There is need for further information and/or testing

()	ii)	There is at present no need for further information and/or testing or for		 risk reduction measures beyond those which are being applied

( )	iii)	There is a need for limiting the risks: risk reduction measures which are 	already being applied shall be taken into account

No environment risk characterization was done for the atmosphere.

## REGIONAL LEVEL

### Conclusions on cadmium metal and cadmium oxide

ENVIRONMENT: AQUATIC ECO-SYSTEM

(..)	i)	There is a need for further information and/or testing

(..)	ii)	There is at present no need for further information and/or testing or for			risk reduction measures beyond those which are being applied

(X)	iii) 	There is a need for limiting the risks: risk reduction measures which are 			already being applied shall be taken into account

Conclusion [iii] is reached because:

- the modelled regional PEC of surface water has a risk factor of 0.6 using a mean Kp value for EU while the risk factor is 1.7 using a Kp value that is distinctly smaller than average. This suggests potential regional risk. However, it is proposed to use measured values for the risk characterization because of the uncertainties in the choice of the natural background (which is combined with the added concentration to derive the regional PEC) and in the coverage of the surface water with small Kp values. Monitoring data were collected for 13 EU countries (of the EU-16 surveyed) but limitation in data quality (detection limit, geographical coverage etc.) reduced this information to 8 countries (as proxy for regions) for which conclusions can be derived. The regional averages of the 90th percentiles of measured Cd concentrations of European rivers and lakes in these regions range from 0.2 to 3. 5. The majority of regional averaged 90th percentiles have a risk factor < 1 whereas these values are >1 in the UK (based on a limited dataset of 1996) and the Walloon region of Belgium. Outliers have a large impact on the risk factors as, for example, 20 sites of the 728 investigated in the largest database of UK (data of 2003) determine risk in UK. The PNEC for water was derived with an assessment factor of 2 reflecting most of the uncertainties in the effects assessment. The conclusions about risk in the 2 regions mentioned are not affected by either in- or excluding this assessment factor. During the development of the RRS, decision about (possible) reduction measures has to take into account the information on potential cadmium emission sources in these regions. In order to better characterise the regional risks to surface water in part of the EU which have not been covered in this assessment (i.e. eastern and southern Europe are underrepresented in the entire dataset, because detection limits are often too high and because fractionation is often not reported) it might be useful to obtain more information for these regions. It may be that the foreseen monitoring actions under for example the Water Framework Directive will provide this information in the future.

ENVIRONMENT: TERRESTRIAL ECO-SYSTEM

( )	i)	There is a need for further information and/or testing

(X)	ii)	There is at present no need for further information and/or testing or for			risk reduction measures beyond those which are being applied

(X)	iii)	There is a need for limiting the risks: risk reduction measures which			are already being applied shall be taken into account

Conclusion [ii] is reached because:

- modelled regional soil Cd concentrations that include natural soil, industrial soil and 8 different agricultural scenario’s are all below the PNECsoil. All these modelled values are total concentrations that are expected after 60 years (agricultural soils) or far beyond that (natural and industrial soils) with current regional emissions to soil. The starting concentrations are EU average values for the ambient concentrations. If 90th percentiles of measured concentrations would have been used in such calculations , then risk cannot be excluded.

Conclusion [iii] is reached because:

- the 90th percentiles of measured Cd concentrations of European soils have risk factors 0.4-1.6 (mean: 0.86; data from 6 EU countries). Regional risk for the terrestrial ecosystem cannot be excluded in one region (UK). However, it should be noted that the 90th percentile for the UK falls within the range of the proposed PNECsoil values based on direct toxicity to soil microbial processes (see Table 3.3.1). Hence, risk cannot be excluded but will depend on the magnitude of the assessment factor chosen (either 1 or 2, see 3.2.2.7) in the derivation of the PNECsoil.

ENVIRONMENT: ASSESSMENT OF SECONDARY POISONING

( )	i)	There is a need for further information and/or testing

(X)	ii)	There is at present no need for further information and/or testing or for			risk reduction measures beyond those which are being applied

(X)	iii)	There is a need for limiting the risks: risk reduction measures which			are already being applied shall be taken into account

Conclusion [ii] is reached because

- field data (body burden: kidney and liver Cd data) of birds (excluding pelagic birds)  do not indicate Cd poisoning, even in top predators. No risk to mammals is predicted from modelled regional soil Cd concentrations.

Conclusion [iii] is reached because:

- measured soil Cd concentrations of European soils have risk factors 0.4-1.6 for poisoning to mammals (mean: 0.86; data from 6 EU countries). Regional risk for the terrestrial ecosystem cannot be excluded in one region (UK). The uncertainty surrounding the effects assessment, however; suggests that this is a borderline situation: the available information shows that literature data on Cd uptake in mammals dwelling in acid soils sensitively influences the effects assessment. If data on acid soils (pH <4.2) are excluded from the effects assessment, a larger PNEC is obtained and risk in the UK would be excluded. That conclusion would only remove concern provided that the P90 value in UK does not refer to acid soils, which is unknown. This analysis is, moreover, qualitative because there is no validated model to estimate risk to mammals along the entire range of soil pH.

| Table 5.2 Overview of conclusions: Regional level: Current situation: Cadmium contribution from batteries: All scenarios: 10% and 50% of the total cadmium content in MSW (resp. 1 g and 5 g Cd/tonne MSW (dry wt. basis) |
| --- |
| Compartment | Release Source | Subscenarios | Conclusions | Remarks |
| Surface water | MSW - incinerators (equipped with an on-site WWTP) | The emissions by incinerators to the aquatic compartment do not contribute significantly to the regional PEC value |
|  | MSW-landfills (leachate: 5µg/L) | The emissions by landfills to the aquatic compartment do not contribute significantly to the regional PEC value |
| Sediment | All sources | All scenarios | Concl i) |  |
|  | MSW - incinerators (equipped with an on-site WWTP) | The emissions by incinerators to the sediment compartment do not contribute significantly to the regional PEC value |
|  | MSW-landfills (leachate: 5µg/L) | The emissions by landfills to the sediment compartment do not contribute significantly to the regional PEC value |
| Soil | All sources | All scenarios | Concl ii) and iii) |  |
| Atmosphere | All sources | All scenarios | No conclusion drawn for env | Conclusion for hh cfr section 4.1.3.3 |
| Secondary poisoning |  |  | Concl ii) |  |

| Table 5.3 Overview of conclusions: Regional level: Future situation: Cadmium contribution from batteries: All scenarios: 10% and 75 % collection scenario. Resp. 4.2 g and 15 g Cd/tonne MSW (dry wt. basis) Ni-Cd contribution |
| --- |
| Compartment | Release Source | Subscenarios | Conclusions | Remarks |
| Surface water | MSW - incinerators (equipped with an on-site WWTP) | The emissions by incinerators to the aquatic compartment do not contribute significantly to the regional PEC value |
| Sediment | MSW - incinerators (equipped with an on-site WWTP) | The emissions by incinerators to the sediment compartment do not contribute significantly to the regional PEC value |

# references (HH still included; env still to complete/check references from revisions after SCTEE opinion)

Aalbers Th. G., De wilde P., Rood G., Vermij P., Saft R., Van De Beek A, Broekman H., Masereeuw M., Kamphuis C., Dekker P. and Valentijn E. (1996). Environmental quality of primary and secoondary construction materials in relation to re-use and protection of soil and surface water. RIVM report 771402007, 1996.

Abadin HG, Hibbs BF, and Pohl HR.(1997). Breast-feeding exposure of infants to cadmium, lead and mercury: a public health viewpoint. Toxicol.Ind.Health, 13, 495-517.

Abd Elghany N, Schumacher MC, Slattery ML, West DW, and Lee JS.(1990). Occupation, Cadmium Exposure, and Prostate Cancer. Epidemiology, 1, 107-115.

ACGIH (American Conference of Governmental Industrial Hygienists).(2001). Threshold Limit Values for Chemical Substances and Physical Agents & Biological Exposure Indices.

Adams RG and Crabtree N.(1961). Anosmia in alkaline battery workers. Br J Ind Med, 18, 216-221.

Adams RG, Harrison JF, and Scott P.(1969). The development of cadmium-induced proteinuria,impaired renal function, and osteomalacia in alkaline battery workers. Q.J.Med., 38, 425-443.

Adams RG.(1980).Osteopathy associated with tubular nephropathy in employees in an alkaline battery factory. In:Cadmium-induced Ostepathy. Edited by I Shigematsu and K Nomiyama. Japanese Public Health Association. Tokyo, 66-73.

Adamsson E, Piscator M, and Nogawa K.(1979). Pulmonary and gastrointestinal exposure to cadmium oxide dust in a battery factory. Environ Health Perspect, 28, 219-222.

Adamsson E.(1979). Calculation of Total Respiratory Doses for Workers Exposed to Cadmium in Air. Arh.Hig.rada.Toksikol., 30, S 1047-S 1050.

Adema DMM and Henzen L (1989). A comparison of plant toxicities of some industrial-chemicals in soil culture and soilless culture. Ecotoxicology and Environmental Safety, 18, 219-229.

ADEME (1999). http://www.environnement.gouv.fr dossiers dechets. Résultat des mesures demétaux à l'émission des usines d'incinération d'ordures ménagères.

Ades AE and Kazantzis G.(1988). Lung cancer in a non-ferrous smelter: the role of cadmium. Br J Ind Med, 45, 435-442.

Akahori F, Masaoka T, and Arai S.(1994). A nine-year chronic toxicity study of cadmium in monkeys II.Effects of dietary cadmium on circulatory function plasma cholesterol and triglyceride. Vet Hum Toxicol, 36, 290-294.

Ảkesson A (2000). Cadmium exposure and iron status. PhD thesis, Carolinska Institute, Stockholm, Sweden.

Akesson A, Berglund M, Schütz A, Bjellerup P, Bremme K, and Vahter M.(2002). Cadmium exposure in pregnancy and lactation in relation with iron status. Am J Public Health, 92, 284-287.

Aldenberg T and Slob W (1993). Confidence limits for hazardous concentrations based on logistically distributed NOEC toxicity data. Ecotoxicology and Environmental Safety, 25, 48-63.

Aldenberg T. and Slob W.(1993). Confidence limits for hazardous concentrations based on logistically distributed NOEC toxicity data. Ecotox. Environ. Safety, 25:48-63.

Alessio L, Apostoli P, Duca PG, and Braga M.(1992).Definition of reference values for Cd-B and Cd-U: methodological aspects and preliminary results. In:Cadmium in the Human Environment: Toxicity and Carcinogenicity. Edited by GF Nordberg, RFM Herber, and L Alessio. IARC, International Agency for Reasearch on Cancer. Lyon, 93-99.

Alessio L, Dell'Orto A, Calzaferri G, Buscaglia M, Motta G, and Rizzo M.(1984). Cadmium Concentrations in Blood and Urine of Pregnant Women at Delivery and their Offspring. Sci Total Environ, 34, 261-266.

Alfven T, Elinder CG, Carlsson MD, Grubb A, Hellström L, Persson B, Pettersson C, Spang G, Schütz A, and Järup L.(2000). Low-level cadmium exposure and osteoporosis. J Bone Mineral Res, 15, 1579-1586.

Ali MM, Murthy RC, and Chandra SV.(1986). Developmental and longterm neurobehavioral toxicity of low level in- utero cadmium exposure in rats. Neurobehav.Toxicol Teratol, 8, 463-468.

Allen HE, Hall RH and Brisbin TD (1980). Metal speciation. Effects on aquatic toxicity. Environmental Science & Technology, 14, 441-443.

Allen HE, van Beelen P and Struijs J (1993). Acid volatile sulphide. Science of the Total Environment Suppl l, 1789-1791.

Allison JD, Brown, DS and Novo-Gradac KJ (1991). MINTEQA2/PRODEFA2. A geochemical assessment model for environmental systems: Version 3.0. Report N° EPA/600/3-91/021.

Amdur ML and Caputi RA.(1953). Ind.Med.Surg., 22, 561-561.

Andersen C (1979). Cadmium, lead and calcium content, number and biomass, in earthworms (Lumbricidae) from sewage sludge treated soil. Pedobiologia, 19, 309-319.

Andersen O, Nielsen JB, and Nordberg GF.(1992).Factors affecting the intestinal uptake of cadmium from the diet. In:Cadmium in the Human Environment: Toxicity and Carcinogenicity. Edited by GF Nordberg, RFM Herber, and L Alessio. IARC. Lyon, 173-185.

Andersen O, Nielsen JB, and Svendsen P.(1988). Effects of dithiocarbamates on intestinal absorption and organ distribution of cadmium chloride in mice. Toxicology, 48, 225-236.

Andersen O, Nielsen JB, and Svendsen P.(1988). Oral cadmium chloride intoxication in mice: effects of dose on tissue damage, intestinal absorption and relative organ distribution. Toxicology, 48, 225-236.

Andersen O.(1989). Oral cadmium exposure in mice: Toxicokinetics and efficiency of chelating agents. Crit Rev Toxicol, 20, 83-112.

Andersson A and Bingefors S (1985). Trends and annual variations in Cd concentrations in grain of winter wheat. Acta Agriculturae Scandinavica, 35, 339-344.

Andersson H, Petersson-Grawé K, Lindqvist E, Luthman J, Oskarsson A, and Olson L.(1997). Low-level cadmium exposure of lactating rats causes alterations in brain serotonin levels in the offspring. Neurotoxicology and Teratology, 19, 105-115.

Andersson K, Elinder CG, Hogstedt C, Kjellström T, and Spang G.(1983). Mortality among cadmium workers in a Swedish battery factory. 152-154.

Ando Y, Shibata E, Sakai S, and Tsuchiyama F.(1995). Elevated urinary cadmium concentrations in a patient with acute cadmium pneumonitis. Scand J Work Environ Health, 22, 150-153.

Ankley GT (1996). Evaluation of metal/acid-volatile sulfide relationships in the prediction of metal bioaccumulation by benthic macroinvertebrates. Environmental Toxicology and Chemistry, 15, 2138-2146.

Ankley GT, Leonard EN and Mattson VR (1994). Prediction of bioaccumulation of metals from contaminated sediments by the oligochaete, Lumbricus variegatus. Water Research, 28, 1071-1076.

Ankley GT, Schubauer-Berigan MK and Dierkes JR (1996). Application of toxicity identification evaluation techniques to pore water from Buffalo River Sediments. Journal of Great Lakes Research, 22, 534-544.

Annex VIIA (1997). Existing Substances Data submission for cadmium metal and cadmium oxide. Compiled by Industry (UM/IZA-Europe) and in preparation to the risk assessment.

Anthonissen I.H. and Meijer P.J. (1993) Informatiedocument AVI reststoffen, RIVM report N° 738902025, 33 p.

Antila E, Mussalo Rauhamaa H, Kantola M, Atroshi F, and Westermarck T.(1996). Association of cadmium with human breast cancer. Sci Total Environ, 186, 251-256.

Antonio MT, Benito MJ, Leret ML, and Corpas I.(1998). Gestational administration of cadmium alters the neurotransmitter levels in newborn rat brains. J.Appl.Toxicol., 18, 83-88.

Argus (2000). The behaviour of PVC in landfill. Study for the European Commission DGXI.E3 by Argus in association with Prof. Spillmann, carl Bro (University Rostock) and Sigma Plan S.A., 82 p. + Annex.

Arillo A, Calamari D, Margiocco C, Melodia F and Mensi P (1984). Biochemical effects of long term exposure to Cd and Cu on rainbow trout (Salmo gairdneri Rich.): validation of water quality criteria. Ecotoxicology and Environmental Safety, 8, 106-117.

Arito H, Sudo A, and Suzuki Y.(1981). Aggressive behavior of the rat induced by repeated administration of cadmium. Toxicology Letters, 7, 457-461.

Armstrong BG and Kazantzis G.(1983). The mortality of cadmium workers. Lancet, 1, 1425-1427.

Arvidson B.(1986). Autoradiographic localization of cadmium in the rat brain. Neurotoxicology, 7, 89-96.

Assmuth T. (1992). Distribution and attenuation of hazardous substances in uncontrolled solid waste landfills. Waste Management and Research, 10, 235-255.

ATSDR (Agency for Toxic Substances and Disease Registry).(1998). Toxicological Profile for Cadmium.

ATSDR (Agency for Toxic Substances and Disease Registry).(1999). Toxicological Profile for Cadmium (Update).

Attar EN and Maly EJ (1982). Acute toxicity of Cd, Zn and Cd-Zn mixtures to Daphnia magna. Archives of Environmental Contamination and Toxicology, 11, 291-296.

Aufderheide M, Thiedemann KU, Riebe M, and Kohler M.(1989). Quantification of proliferative lesions in hamster lungs after chronic exposure to cadmium aerosols. Exp.Pathol., 37, 259-263.

Axelson O.(1978). Aspects on confounding in occupational health epidemiology. Scand J Work Environ Health, 4, 85-89.

Baader EW.(1951). Chronic cadmium poisoning. Dtsch Med Wochenschr, 76, 484-487.

Baader EW.(1952). Chronic cadmium poisoning. Ind Med Surg, 21, 427-430.

Baccini P., Henseler G., Figi, R. and Belevi H. (1987). Water and element balances of municipal solid waste landfills.Waste Management & Research, 5, 483-499.

Bachmann G, Bannick C, Giese G, Glante F, Kiene A, Konietzka A, Rück F, Schmidt S, Terytze K and Von Borries D (1998). Fachliche Aspekte zur Ableitung von Bodenwerten im Rahmen des Bodenschutzgesetzes. In: Rosenkranz et al. (eds) Bodenschutz. Ergänzbares Handbuch der Massnahmen und Empfehlungen für Schutz, Pflege und Sanierung van Böden, Landschaft und Grundwasser (Loseblattausgabe, begründet 1988). Erich Schmidt Verlag, Berlin.

Baecklund M, Pedersen NL, Björkman L, and Vahter M.(1999). Variation in blood concentrations of cadmium and lead in the elderly. Environmental Research Section A, 80, 222-230.

Baer KN and Benson WH.(1987). Influence of chemical and environmental stressors on acute cadmium toxicity. J Toxicol Environ Health, 22, 35-44.

Baeyens J. (2003). Pers. com., fax 29.01.03 and e-mail 30.01.03.

Baize D (1999). http://www.inra.fr/Internet/Produits/dpenv/baizec39.htm#ann1

Baker TD and Hafner WG.(1961). Cadmium poisoning from a refrigator shelf used as an improvised barbecue grill. Public Health Reports, 76, 543-544.

Bako G, Smith ESO, Hanson J, and Dewar R.(1982). The geographical distribution of high cadmium concentrations in the environment and prostate cancer in Alberta. Can.J.Publ.Health, 73, 92-94.

Baldi M., Bertanza G., Collivignarelli C. and Conti F. (1993). Mathemetical modelling of leachate quantity and quality for an industrial sludge landfill. Proceedings of the Fourth International landfill symposium, Sardinia, Iataly, October, 1993, 839-848.

BAM (Bundesanstalt für Materialforschung und –prüfung). (2002). Final GLP Report on testing the products ‘Cadmium metal powder’ and ‘Cadmium fine billes’ according to the EC-methods A.10, A.12 and A.13 to assess the flammability and pyrophoric properties. Nr. : II.2-886/02 (English translation of the German final report of 14 October 2002).

Baranski B and Sitarek K.(1987). Effect of oral and inhalation exposure to cadmium on the oestrous cycle in rats. Toxicology Letters, 36, 267-273.

Baranski B, Opacka J, Wronska Nofer T, Trzcinka Ochocka M, Sitarek K, and Matczak W.(1983). Effect of inhalation exposure to cadmium oxide on arterial blood pressure, lipid metabolism and tissue cadmium concentration in rats. Med Pr., 34, 11-19.

Baranski B, Stetkiewicz I, Sitarek K, and Szymczak W.(1983). Effects of Oral, Subchronic Cadmium Administration on Fertility, Prenatal and Postnatal Progeny Development in Rats. Arch.Toxicol., 54, 297-302.

Baranski B.(1983). Effect of prenatal exposure to cadmium on avoidance acquisition in rats. Med Pr., 34, 381-383.

Baranski B.(1984). Behavioral Alterations in Offspring of Female Rats Repeatedly Exposed to Cadmium Oxide by Inhalation. Toxicology Letters, 22, 53-61.

Baranski B.(1985). Effect of exposure of pregnant rats to cadmium on prenatal and postnatal development of the young. J Hyg.Epidemiol.Microbiol.Immunol., 29, 253-262.

Baranski B.(1986). Effect of maternal cadmium exposure on postnatal development and tissue cadmium, copper and zinc concentrations in rats. Arch.Toxicol., 58, 255-260.

Barbier (1996). Reference currently missing.

Barlas NA (1999). A pilot study of heavy metal concentration in various environments and fishes in the upper Sakarya river basin, Turkey. Environmental Toxicology, 14, 367-373.

Barlow SM and Sullivan FM.(1982).8. Cadmium and its compounds. In:Reproductive hazards of industrial chemicals. Edited byAcademic Press inc. London New York, 136-177.

Barltrop D and Strehlow CD.(18-12-1982). Cadmium and health in Shipham. Lancet, 2, 1394-1395.

Barnhart S and Rosenstock L.(1984). Cadmium chemical pneumonitis. Chest., 86, 789-791.

Barregard L, Svalander C, Schütz A, Westberg G, Sällsten G, Blohmé I, Mölne J, Attman PO, and Haglind P.(1999). Cadmium, mercury and lead in kidney cortex of the general Swedish population: a study of biopsies from living kidney donors. Environ Health Perspect, 107, 867-871.

Barrett HM and Card BY.(1947). Studies on the toxicity of inhaled cadmium II.The acute lethal dose of cadmium oxide for man. Journal of Industrial Hygiene and Toxicology, 29, 286-293.

Bar-Sela S, Levy M, Westin JB, Laster R, and Richter ED.(1992). Medical findings in nickel-cadmium battery workers. Israel J Med Sci, 8-9, 578-583.

Bartlett L, Rabe FW and Funk WH (1974). Effects of copper, zinc and cadmium on Selenastrum capricornutum. Water Research, 8, 179-186.

Basinger MA, Jones MM, Holscher MA, and et al.(1988). Antagonists for acute oral cadmium chloride intoxication. J Toxicol Environ Health, 231, 77-89.

Battaglia A, Ghidini S, Campanini G and Spaggiari R (2005). Heavy metal contamination in little owl (Athene noctua) and common buzzard (Buteo buteo) from northern Italy. Ecotoxicology and Environmental Safety, 60, 61–66.

Batteries’ Questionnaire (2000): was designed by the rapporteur to obtain information related to the amounts of batteries (i.e. Ni-Cds) put on the market, collection, recycling etc on a country basis. Three subtypes were made depending on the responder: a) Member state; b) Collection organisation (per country) and c) EPBA. This questionnaire was sent out in 2000. Replies in general were received in 2000.

Bauchinger M, Schmid E, Einbrodt HJ, and Dresp J.(1976). Chromosome Aberrations in Lymphocytes after Occupational Exposure to Lead and Cadmium. Mutat.Res., 40, 57-62.

Baudouin MF and Scoppa P (1974). Acute toxicity of various metals to freshwater zooplankton. Bulletin of Environmental Contamination and Toxicology, 12,745-751.

Bauer and LeScao.(1956). Arch.Mal.Profess., 17, 93-93.

Beck T (1981). Untersuchungen über die toxische wirkung der in Siedlungsabfällen häufigen Schwermetalle auf die Bodenmikroflora. Zeitschrift fur Pflanzenernährung und Bodenkunde, 144, 613-627.

Becker W and Kumpulainen J (1991). Contents of essential and toxic mineral elements in Swedish market-basket diets in 1987. British Journal of Nutrition, 66, 151-160.

Beevers D, Cruickshank J, Yeoman W, Carter G, Goldberg A, and Moore M.(1980). Blood lead and cadmium in human hypertension. J Environ Pathol Toxicol, 4, 251-260.

Beevers DG, Cruickshank JK, Yeoman WB, and et al.(1980). Blood-lead and cadmium in human hypertension. J Environ Pathol Toxicol, 4, 251-260.

Belevi and Baccine (1989a). Long-term behavior of municipal solidwaste landfills.Waste Management and Research, 7, 43-56.

Belevi and Baccine (1989b). Water and element fluxes from sanitary landfills, p. 391-397. In Christensen et al (ed). Sanitary landfilling : Process, technology and environmental impact. Academic Press, London.

Bengtsson G, Gunnarsson T and Rundgren S (1986). Effects of metal pollution on the earthworm Dendrobaena rubida (Sav.) in acidified soils. Water, Air, and Soil Pollution, 28, 361-383.

Benoit DA, Leonard EN, Christensen GM and Fiandt JT (1976). Toxic effects of Cd on three generations of brook trout. Transactions of the American Fisheries Society, 7, 550-560.

Bensryd I, Rylander L, Högstedt B, Aprea P, Bratt I, Fåhraéus C, Hólmen A, Karlosson A, Nilsson A, Svensson BL, Schütz A, Thomassen Y and Skerfving S (1994). Effect of acid precipitation on retention and excretion of elements in man. Science of the Total Environment, 145, 81-102.

Berdowski JJM, Pulles MPJ and Visschedijk AJH (1998). Incremental cost and remaining emission in 2010 of Heavy Metals (HM) resulting from the implementation of the draft HM Protocol under the UN/ECE Convention on Long Range Transboundary Air Pollution. TNO-report, TNO-MEP – R 98/020, Apeldoorn, The Netherlands.

Berglind R (1985). The effects of cadmium on ALA-D activity, growth and haemoglobin content in the water flea, Daphnia magna. Comparative Biochemistry and Physiology C-Toxicology & Pharmacology, 80, 407-410.

Berglund M, Åkesson A, Nermell B and Vahter M (1994). Intestinal absorption of dietary cadmium in women depends on body iron stores and fiber intake. Environmental Health Perspectives, 102, 1058-1066.

Berglund M, Akessson A, Bjellerup P, and Vahter M.(2000). Metal-bone interactions. Toxicol Lett, 112-113, 219-225.

Berglund M, Akessson A, Nermell B, and Vahter M.(1994). Intestinal Absorption of Dietary Cadmium in Women depends on Body Iron Stores and Fiber Intake. Environ Health Perspect, 102, 1058-1066.

Bergomi M, Borella P, and Fantuzzi G.(1989). Blood, teeth and hair: 3 different materials used to evaluate exposure to lead and cadmium in children living in an industrial zone. Ann.Ig., 1, 1185-1196.

Berk SG, Gunderson JH and Derk LA (1985). Effects of Cd and Cu on chemotaxis of marine and freshwater ciliates. Bulletin of Environmental Contamination and Toxicology, 34, 897-903.

Berlin A, Blanks RG, Catton M, Kazantzis G, Mottet NK, and Samiullah Y.(1992).Birth weight of children and cadmium accumulation in placentas of female nickel-cadmium (long-life) battery workers. In:Cadmium in the human environment: toxicity and carcinogenicity. Edited by GF Nordberg, RFM Herber, and L Alessio. IARC. Lyon, 257-262.

Bernard A and Hermans C.(1997). Biomonitoring of early effects on the kidney or the lung. Sci Total Environ, 199, 205-211.

Bernard A and Lauwerys R.(1986).Chapter 5 : Effects of Cadmium Exposure in Humans. In:Handbook of Experimental Pharmacology, vol.80. Edited by EC Foulkes. Springer-Verlag. Berlin Heidelberg

Bernard A and Lauwerys R.(1989). Epidemiological application of early markers of nephrotoxicity. Toxicology Letters, 46, 293-306.

Bernard A and Lauwerys R.(1991). Experimental evidence that the L-aspartate microproteinuria actually results from a tubular 'washout'. Nephron, 59, 345-346.

Bernard A, Goret A, Buchet J-P, and et al.(1980). Significance of cadmium levels in blood and urine during long- term exposure of rats to cadmium. J Toxicol Environ Health, 6, 175-184.

Bernard A, Lauwerys R, and Ouled-Amor A.(1992). Loss of glomerular polyanion correlated with albuminuria in experimental cadmium nephropathy. Arch.Toxicol., 66, 272-278.

Bernard A, Schadeck C, Cardenas A, Buchet JP, and Lauwerys R.(1991). Potentiation of diabetic glomerulopathy in uninephrectomized rats subchronically exposed to cadmium. Toxicol Lett., 58, 51-57.

Bernard A, Thielemans N, Roels H, and Lauwerys R.(1995). Association between NAG-B and cadmium in urine with no evidence of a threshold. Occup Env Med, 52, 177-180.

Bernard AM, Amor AO, and Lauwerys RR.(1988). Decrease of erythrocyte and glomerular membrane negative charges in chronic cadmium poisoning. Br J Ind Med, 45, 112-115.

Bernard AM, Buchet J-P, Roels H, Masson P, and Lauwerys R.(1979). Renal excretion of proteins and enzymes in workers exposed to cadmium. Eur J Clin Invest, 9, 11-22.

Bernard AM, de Russis R, Ouled-Amor A, and Lauwerys RR.(1988). Potentiation of cadmium nephrotoxicity by acetaminophen. Arch.Toxicol., 62, 291-294.

Bernard AM, de Russis R, Ouled-Amor A, and Lauwerys RR.(1988). Potentiation of cadmium nephrotoxicity by acetaminophen. Arch.Toxicol., 62, 291-294.

Bernard AM, Roels H, Cardenas A, and Lauwerys R.(1990). Assessment of urinary protein 1 and transferrin as early markers of cadmium nephrotoxicity. Br J Ind Med, 47, 559-565.

Bernard J., H. Ole & V. Jürgen (2000). The influence of PVC on the quantity and hazardnousness of flue gas residues from incineration. Finol report.Bertin Technologies.

Bertram PE and Hart BA (1979). Longevity and reproduction of Daphnia pulex (de Geer) exposed to cadmium-contaminated food or water. Environmental Pollution, 19, 295-305.

Beton DC, Andrews GS, Davies HJ, Howells L, and Smith GF.(1966). Acute Cadmium Fume Poisoning. Five Cases with one Death from Renal Necrosis. Br J Ind Med, 23, 292-301.

Bewley RJF and Stotzky G (1983). Effects of cadmium and simulated acid rain on ammonification and nitrification in soil. Archives of Environmental Contamination and Toxicology, 12, 285-291.

Beyer WN (2000). Hazards to wildlife from soil-borne cadmium reconsidered. Journal of Environmental Quality, 29, 1380-1384.

Beyer WN, Chaney RL and Mulhern BM (1982). Heavy metal concentrations in earthworms from soil amended with sewage sludge. Journal of Environmental Quality, 11, 381-386.

BFL (1997). Information about cadmium in Austria. Bundesamt und Forschunchszentrum für Landwirtschaft, Austria.

BGAA (Berufsgenossenschaftlicher Arbeitskreis Alstoffe Bundesrepublik Deutschland).(1998). Cadmium Occupational exposure. Exposure description no.37, 1-9.

Bhattacharyya MH, Whelton BD, and Peterson DP.(1981). Gastrointestinal Absorption of Cadmium in Mice during Gestation and Lactation I.Short-Term Exposure Studies. Toxicology and Applied Pharmacology, 61, 335-342.

Bhattacharyya MH, Whelton BD, and Peterson DP.(1982). Gastrointestinal Absorption of Cadmium in Mice during Gestation and Lactation II. Continuous Exposure Studies. Toxicology and Applied Pharmacology, 66 , 368-375.

Bhattacharyya MH.(1983). Bioavailability of orally administered cadmium and lead to the mother, fetus, and neonate during pregnancy and lactation: an overview. Sci Total Environ, 28, 327-342.

Bieber E (1995). Cadmium-Ausenluftkonzentrationen. UBA (Pilotstation FFM) Internal paper, 2 pp.

Biesinger KE and Christensen GM (1972). Effects of various metals on survival, growth, reproduction and metabolism of Daphnia magna. Journal of the Fisheries Research Board of Canada, 29, 1691-1700.

Bingham FT, Page AL, Mahler RJ and Ganje TJ (1975). Growth and cadmium accumulation of plants grown on a soil treated with a cadmium-enriched sewage sludge. Journal of Environmental Quality, 4, 207-211.

Bingham FT, Sposito G and Strong JE (1986). The effect of sulphate on the availability of cadmium. Soil Science, 141, 172-177.

Bishop WE and McIntosh AW (1981). Acute lethality and effects of sublethal Cd exposure on ventilation frequency and cough rate of bluegill (Lepomis macrochirus). Archives of Environmental Contamination and Toxicology, 10, 519-530.

Björkman L, Vahter M, and Pedersen NL.(2000). Both the Environment and Genes Are Important for Concentrations of Cadmium and Lead in Blood. Environ Health Perspect, 108, 719-722.

Black, HIJ, Garnett JS, Ainsworth G, Coward PA, Creamer R, Ellwood S, Horne J, Hornung M, Kennedy VH, Monson F, Raine L, Osborn D, Parekh NR, Parrington J, Poskitt JM, Potter E, Reeves N, Rowland AP, Self P, Turner S, Watkins J, Woods C, and Wright J (2002). MASQ: Monitoring And Assessing Soil Quality in Great Britain. Countryside Survey Module 6: Soils and Pollution R&D Technical Report P5-053/01/TR. Bristol: Environment Agency, 200pp.

Blainey JD, Adams RG, Brewer DB, and Harvey TC.(1980). Cadmium-induced osteomalacia. Br J Ind Med, 37, 278-284.

Blair A and Fraumeni JF.(1978). Geographic patterns of prostate cancer in the United States. J Natl Cancer Inst, 61, 1379-1384.

Blakley BR.(1986). The effect of cadmium on chemical- and viral-induced tumor production in mice. J Appl Toxicol, 6, 425-429.

Blejer HP, Caplan PE, and Alcocer AE.(1966). Acute Cadmium Fume Poisoning in Welders- A Fatal and a Nonfatal Case in California. California Medicine, 105, 290-295.

BMM (1997). Reference currently missing

BMM (2001). Réactualisation des dossiers relatifs a l'émission de substances prioritaires en Belgique. Cadmium Rapport Provisoire. Prion, C. and Vanderborght, J.-P. Université Libre de Bruxelles. Service Traitement des Eaux et Pollution, Bruxelles.

Bodar CWM, van der Sluis I and Voogt PA (1988b). Effects of cadmium on consumption, assimilation and biochemical parameters of Daphnia magna: possible implications for reproduction. Comparative Biochemistry and Physiology C-Toxicology & Pharmacology, 90, 341-346.

Bodar CWM, van der Sluis I, van Montfort JCP, Voogt PA and Zandee DI (1990). Cadmium Resistance in Daphnia magna. Aquatic Toxicology, 16, 33-40.

Bodar CWM, van der Zee A, Voogt PA, Wynne H and Zandee DI (1989). Toxicity of heavy metals to early life stages of Daphnia magna. Ecotoxicology and Environmental Safety, 17, 333-338.

Bodar CWM, Van Leeuwen CJ, Voogt PA and Zandee DI (1988a). Effect of cadmium on the reproduction strategy of Daphnia magna. Aquatic Toxicology, 12, 301-310.

Boffetta P.(1992).Methodological aspects of the epidemiological association between cadmium and cancer in humans. In:Cadmium in the Human Environment: Toxicity and Carcinogenicity. Edited by GF Nordberg, RFM Herber, and L Alessio. IARC. Lyon, 425-434.

Boisset M and Boudene C.(1981). Effect of a Single exposure to Cadmium Oxide Fumes on Rat Lung microsomal Enzymes. Toxicology and Applied Pharmacology, 57, 335-345.

Boisset M and Narbonne JF (1995). Le cadmium dans l’alimentation. Editions du Conseil de l’Europe, Strasbourg, France.

Boisset M, Girard F, Godin J, and Boudene C.(1978). Cadmium Content of Lung, liver and Kidney in Rats Exposed to Cadmium Oxide Fumes. Int.Arch.Occup.Environ.Health, 41, 41-53.

Boisset M, Girard F, Godin J, and Boudene C.(1978). Cinétique de l'épuration pulmonaire du cadmium inhalé et de son accumulation dans le foie et les reins,chez le rat. C.R.Acad.Sc.Paris, 287, 61-64.

Bollag JM and Barabasz W (1979). Effect of heavy metals on the denitrification process in soil. Journal Environmental Quality, 8, 196-201.

Bomhard E, Maruhn D, Paar D, and et al.(1984). Urinary enzyme measurements as sensitive indicators of chronic cadmium nephrotoxicity. Contrib Nephrol, 42, 142-147.

Bomhard E, Vogel O, and Loser E.(1987). Chronic effects on single and multiple oral and subcutaneous cadmium administrations on the testes of Wistar rats. Cancer Lett., 36, 307-315.

Bonassi S, Hagmar L, Stromberg U, Montagud AH, Tinnerberg H, Forni A, Heikkila P, Wanders S, Wilhardt P, Hansteen IL, Knudsen LE, and Norppa H.(15-3-2000). Chromosomal aberrations in lymphocytes predict human cancer independently of exposure to carcinogens. European Study Group on Cytogenetic Biomarkers and Health. Cancer Res, 60, 1619-1625.

Bond H, Lighthart B, Shimabuku R and Russell L (1976). Some effects of cadmium on coniferous forest soil litter microcosms. Soil Science, 121, 278-287.

Bonithon-Kopp C, Huel G, Moreau T, and Wendling R.(1986). Prenatal exposure to lead and cadmium and psychomotor development of the child at 6 years. Neurobehavioural Toxicology and Teratology, 9, 307-310.

Bonnell JA, Kazantzis G, and King E.(1959). A follow-up study of en exposed to cadmium oxide fume. Br J Ind Med, 16, 135-145.

Bonnell JA.(1955). Emphysema and proteinuria in men casting copper-cadmium alloys. Br J Ind Med, 12, 181-197.

Borelli S.(1965).Neuere Berufsschäden durch Öle bis Ölbeimisschungen und andere Noxen in der Industrie. In:De Structura e Functione Stratorum Epidermidis s.d. Barrierrae. Edited by JE Purkiyne. Acta Facultatis Medicae Universitatis Brunensis. 581-592.

Borg H (1987). Trace metals and water chemistry of forest lakes in northern Sweden. Water Research, 21, 65-72.

Borg H, Andersson P and Johansson K (1989). Influence of acidification on metal fluxes in Swedish forest lakes. The science of the total environment, 87/88, 241-253.

Borgmann U, Millard ES and Charlton CC (1989). Effect of cadmium on a stable, large volume, laboratory ecosystem containing Daphnia and phytoplankton. Canadian Journal of Fisheries and Aquatic Sciences, 46, 399-405.

Borjesson J, Bellander T, Jarup L, Elinder CG, and Mattsson S.(1997). In vivo analysis of cadmium in battery workers versus measurements of blood, urine, and workplace air. Occupational and Environmental Medicine, 54, 424-431.

Borzelleca JF, Clarke EC, and Condcie LWj.(1989). Short-term toxicity (1 and 10 days) of cadmium chloride in male and female rats: Gavage and drinking water. J Am Coll Toxicol, 8, 377-404.

Boscolo P and Carmignani M.(1986). Mechanisms of cardiovascular regulation in male rabbits chronically exposed to cadmium. Br J Ind Med, 43, 605-610.

Bosland MC.(1994).Male reproductive system. In:Carcinogenesis. Edited by MP Waalkes and RJ Ward. Raven Press. New York, 339-402.

Bouley G, Dubreuil A, Despaux N, and Boudene C.(1977). Toxic effects of cadmium microparticles on the respiratory system. Scand J Work Environ Health, 3, 116-121.

Bozkurt S. , L. Moreno, I. Neretnieks (2000). Long-term processes in waste deposits. The science of the total environment, 250, 101-121.

Breder R (1988). Cadmium in European inland waters. Environmental Toxin Series, 2, 159-169.

BREF, 2005. Draft refernce document on the Best Available Techniques fro Waste Incineration, Final draft May 2005. European Comission, Joint Research Centre, Integrated Pollution Prevention and Control.

Bresch H (1982). Investigation of the long-term action of xenobiotics on fish with special regard to reproduction. Ecotoxicology and Environmental Safety, 6, 102-112.

Bringmann G and Kühn R (1980). Comparison of the toxicity thresholds of water pollutants to bacteria, algae and protozoa in the cell multiplication test. Water Research, 14, 231-241.

Bringmann G. and Kühn R. (1980). Comparison of the toxicity thresholds of water pollutants to bacteria, algae and protozoa in the cell multiplication test. Water Res., 14:231-241.

Brkovic-Popovic I and Popovic M (1977). Effects of heavy metals on survival and respiration rate of tubified worms: Part I- Effects on survival. Environmental Pollution, 13, 65-72.

Bro S, Sandström B and Heydorrn K (1990). Intake of essential and toxic trace elements in a random sample of Danish men as determined by the duplicate portion sampling technique. Journal of Trace Elements and Electrolytes in Health and Disease, 4,147-155.

Brockhaus A, Collet W, Dolgner R, Engelke R, Ewers U, Freier I, Jerman E, Krämer U, Manojlovic N, Turfeld M, and Winneke G.(1988). Exposure to lead and cadmium of children living in different areas of North-West Germany: results of biological monitoring studies 1982-1986. Int.Arch.Occup.Environ.Health, 60, 211-222.

Brockhaus A, Freier I, Ewers U, Jerman E, and Dolgner R.(1983). Levels of cadmium and lead in blood in relation to smoking, sex, occupation, and other factors in an adult population of the FRG. Int.Arch.Occup.Environ.Health, 52, 167-175.

Bromley, J.; Young, P. J.; Rushbrook, P.; Bentley, J. (1983). Environmental aspects of the release and fate of cadmium in municipal landfills, with reference to the use and disposal of nickel-cadmium batteries and pigmented plastics. Ed. Proc. - Int. Cadmium Conf., 4th (1983), 61-6. Editor(s): Wilson,David; Volpe, Rosalind A. Publisher: Cadmium Association, London, UK.

Brookes PC (1995). The use of microbial parameters in monitoring soil pollution by heavy metals. Biology and Fertility of Soils, 19, 269-279.

Brown SL, Chaney RL, Angle JS and Ryan JA (1998). The phytoavailability of cadmium to lettuce in long-term biosolids amended soils. Journal of Environmental Quality, 27, 1071-1078.

Brown SL, Chaney RL, Lloyd CA, Angle JSA and Ryan JA (1996). Relative uptake of cadmium by garden vegetables and fruits grown on long-term biosolid-amended soils. Environmental Science and Technology, 30, 3508-3511.

Brunner P.H. and W.R. Ernst (1986). Alternative methods for the analysis of Municipal solid waste. Waste Management and Research, 4, 147-160.

Brunner P.H. and H. Mönch (1986). The flux of metals through municipal solid waste incinerators. Waste Management and Research, 4, 105-119.

Buchet J-P, Lauwerys R, Roels H, Bernard A, Bruaux P, Claeys F, Ducoffre G, De Plaen P, Staessen J, Amery A, and et al.(1990). Renal effects of cadmium body burden of the general population (published erratum appears in Lancet 1991 Jun 22;337 (8756):1554). Lancet, 336, 699-702.

Buchet JP, Lauwerys R, Roels H, Bernard A, Bruaux P, Claeys F, Ducoffre G, De Plaen P, Staessen J, Amery A, and .(22-9-1990). Renal effects of cadmium body burden of the general population. Lancet, 336, 699-702.

Buchet JP, Lauwerys R, Vandevoorde A and Pycke JM (1983). Oral daily intake of cadmium, lead, manganese, copper, chromium, mercury, calcium, zinc and arsenic in Belgium: a duplicate meal study. Food and Chemical Toxicology, 21, 19-24.

Buchet JP, Roels H, Hubermont G, and Lauwerys R.(1978). Placental transfer of lead, mercury, cadmium, and carbon monoxide in women. II. influence of some epidemiological factors on the frequency distributions of the biological indices in maternal and umbilical cord blood. Environ Res, 15, 494-503.

Buchet J-P, Roels H, Lauwerys R, Bruaux P, Claeys-Thoreau F, Lafontaine A, and Verduyn G.(1980). Repeated surveillance of exposure to cadmium, manganese, and arsenic in school-age children living in rural, urban, and nonferrous smelter areas in Belgium. Environ Res, 22, 95-108.

Buckler HM, Smith WD, and Rees WD.(1986). Self poisoning with oral cadmium chloride. British Medical Journal, 292, 1559-1560.

Buckley BJ and Bassett DJP.(1987). Pulmonary Cadmium Oxide Toxicity in the Rat. J Toxicol Environ Health, 21, 233-250.

Bui TH, Lindsten J, and Nordberg GF.(1975). Chromosome analysis of Lymphocytes from Cadmium Workers and Itai- Itai Patients. Environ Res, 9, 187-195.

Bulmer FMR, Rothwell HE, and Frankish ER.(1938). Industrial cadmium poisoning. Can.Publ.Health J., 29, 19-26.

Burton KW, Morgan E and Roig A (1984). The influence of heavy metals upon the growth of sitka-spruce in South Wales forests. Plant and Soil, 78, 271-282.

Buxton RSJ.(1956). Respiratory functon in men casting cadmium alloys. II. The estimation of the total lung volume, its subdivisions and the mixing coefficient. Br J Ind Med, 13, 36-40.

C.J. Jones, P.J. McGugan and P.F. Lawrence (1977/78) An investigation of the degradation of some dry cell batteries under domestic waste landfill conditions. Journal of Hazardous Materials, 2, 259-289.

Cadmium Association.(1991). Cadmium production, properties and uses.

Cai S, Yue L, Jin T, and Nordberg G.(1998). Renal dysfunction from cadmium contamination of irrigation water: dose-response analysis in a Chinese population. Bull WHO, 76, 153-159.

Cain BW, Sileo L, Fransson JC and Moore J (1983). Effects of dietary cadmium on mallard ducklings. Environmental Research, 32, 286-297.

Camobreco V., Ham R., Barlaz M., Repa E., Felker M., Rousseau C. and Rathle J. (1999). Life-cucle inventory of a modern municipal solid waste landfill. Waste Management Research, 17, 394-408.

Campbell TC, Chen J, Liu C, Li J, and Parpia B.(1990). Nonassociation of aflatoxin with primary liver cancer in a cross- sectional ecologcal survey in the People's Republic of China. Cancer Res, 50, 6882-6893.

Canton JH and Slooff W (1982). Toxicity and accumulation studies of cadmium (Cd2+) with freshwater organisms of different trophic levels. Ecotoxicology Environmental Safety, 6, 113-128.

Canziani and Cossu (1989). Landfill hydrology and leachate production. In: Christensen, T.H., Cossu, R., Stegmann, R. (eds) , Sanitary landfilling: Process, Technology and Environmental Impact. Academic Press, London, 185-212.

Carcone (1998). Reference currently missing

Cardenas A, Remis I, Hotter G, and et al.(1992). Human and experimental studies on renal eicosanoid response to long term cadmium exposure. Toxicol Appl Pharmacol, 116, 155-160.

Carlson AR, Phipps GL, Mattson VR, Kosian PA and Cotter AM (1991). The role of AVS in determining Cd bioavailability and toxicity in freshwater sediments. Environmental Toxicology and Chemistry, 10, 1309-1319.

Carmignani M and Boscolo P.(1984). Cardiovascular responsiveness to physiological agonists of female rats made hypertensive by long-term exposure to cadmium. Sci Total Environ, 34, 19-33.

Carroll JJ, Ellis SJ and Oliver WS (1979). Influences of hardness constituents on the acute toxicity of cadmium to brook trout (Salvelinus fontinalis). Bulletin of Environmental Contamination and Toxicology, 22, 575-581.

Carroll RE.(1966). The relationship of cadmium in the air to cardiovascular disease death rates. J Am Med Assoc, 198, 267-269.

Carvalho FM, Silvany Neto AM, Melo AM, Chaves ME, Brandao AM, and Tavares TM.(1989). Cadmium in hair of children living near a lead smelter in Brazil. Sci Total Environ, 84, 119-128.

Casali TA, Gomez RS, Moraes-Santos T, and Gomez MV.(1995). Differential effects of calcium channel antagonists on tityustoxin and ouabain-induced release of [3H]acetylcholine from brain cortical slices. Neuropharmacology, 34, 599-603.

CBS (2002). Statline. Zuivering van Afvalwater. CBS Voorburg/Heerlen.

CCRX (1985), Coördinatie-Commissie voor de metingen van Radioactiviteit en Xenobiotische stoffen Metingen van Radioactiviteit en Xenobiotische stoffen in het biologisch milieu in Nederland 1990. Bilthoven, The Netherlands.

CCRX (1985). Coördinatie-Commissie voor de metingen van Radioactiviteit en Xenobiotische stoffen.Metingen van Radioactiviteit en Xenobiotische stoffen in het biologisch milieu in Nederland 1990. Bilthoven, The Netherlands

CCRX (1991). Coördinatie-Commissie voor de metingen van Radioactiviteit en Xenobiotische stoffen. Metingen van Radioactiviteit en Xenobiotische stoffen in het biologisch milieu in Nederland 1990. Bilthoven, The Netherlands.

CCRX (1994). Metingen in het milieu in Nederland 1992. Coördinatie-commissie voor metingen in het milieu. RIVM, Bilthoven, The Netherlands.

CEC.(1978).Criteria (Dose/Effect Relationships) for Cadmium. Edited by Pergamon Press. Oxford

CEN.(2000). Packaging-Requirements for measuring and verifying the four heavy metals and other dangerous substances present in packaging and their release into the environment-Part 1: Requirements for measuring and verifying the four heavy metals present in packaging. CR 13695-1,

Centers for Disease Control and Prevention.(2001). National Report on Human Exposure to Environmental Chemicals. 19-21.

CEPA (Canadian Environmental Protection Act).(1994). Cadmium and its compounds. En 40-215/40E,

Cerna M, Spevackova V, Cejchanova M, Benes B, Rossner P, Bavorova H, Ocadlikova D, Smid J, and Kubinova R.(1-10-1997). Population-based biomonitoring in the Czech Republic--the system and selected results. Sci.Total Environ, 204, 263-270.

Cha CW.(1987). A study on the effect of garlic to the heavy metal poisoning of rat. J Korean Med Sci, 2, 213-224.

Chalkley SR, Richmond J, and Barltrop D.(1998). Measurement of vitamin D3 metabolites in smelter workers exposed to lead and cadmium. Occupational and Environmental Medicine, 55, 446-452.

Chan HM and Cherian MG.(1993). Mobilization of hepatic cadmium in pregnant rats. Toxicol Appl Pharmacol, 120, 308-314.

Chan OY, Poh SC, Lee HS, and et al.(1988). Respiratory function in cadmium battery workers-a follow-up study. Ann.Acad.Med Singapore., 17, 283-287.

Chandler (1995).Characterizing cadmium in Municipal Solid waste In: Proceedings of the OECD workshop on the sources of cadmium in the environment, Saltsjöbaden, Sweden 16-20 October, 1995, p. 393-398.

Chandler AJ (1996). Characterizing cadmium in municipal solid waste. In: OECD proceedings of the cadmium workshop, session C: products containing cadmium. OECD, Paris, France, pp. 393-398.

Chaney RL and Ryan JA (1991). The future of residuals management after 1991. pp. 13D-1 to 13D-15. In: AWWA/WPCF Joint Residuals Management Conference (Research Triangle Park, NC. Aug. 11-14, 1991). Water Pollution Control Federation, Arlington, VA.

Chaney RL and Hornick SB (1978). Accumulation and effects of cadmium on crops. In: Proceedings of the first International Cadmium Conference, San Francisco. pp. 125-140. Metals Bulletin, Ltd., London.

Chaney RL, Ryan JA and Brown SL (1999b). Environmentally acceptable endpoints for soil metals. In: Environmental Availability of Chlorinated Organics, Explosives and Metals in Soils. Edited by WC Anderson, RC Loehr and D Reible Am. Acad. Environ. Eng., Annapolis, MD.

Chaney RL, Ryan JA, Li Y-M and Brown S (1999a). Soil cadmium as a threat to human health. In: Cadmium in Soils, Plants and the Food Chain Edited by MJ McLaughlin and SL Brown. Kluwer Academic Publishers, Dordrecht. In press.

Chaney RL, Ryan JA, Li Y-M, Welch RM, Reeves PG, Brown SL and Green CE (1996). Phyto-availability and Bio-availability in risk assessment for cadmium in agricultural environments. pp. 49-78. In: Proc. OECD Cadmium workshop on Sources of Cadmium in the environment 1995, Sweden.

Chaney WR, Kelly JM and Strickland RC (1978). Influence of cadmium and zinc on carbon dioxide evolution from litter and soil from a black oak forest. Journal of Environmental Quality, 7, 115-119.

Chang CC, Lauwerys R, Bernard A, Roels H, Buchet JP, and Garvey JS.(1980). Metallothionein in cadmium-exposed workers. Environ Res, 23, 422-428.

Chapman GA (1978). Toxicities of Cadmium, Copper and Zinc to four juvenile stages of chinook salmon and steelhead. Transactions of the American Fisheries Society, 107, 841-847.

Chaudri AM, McGrath SP and Giller KE (1992). Survival of the indigenous population of Rhizobium leguminosarum biovar Trifolii in soil spiked with Cd, Zn, Cu and Ni salts. Soil Biology and Biochemistry, 24, 625-632.

Chaudri AM, Zhao SP, McGrath SP and Crosland AR (1995). The cadmium content of British wheat grain. Journal of Environmental Quality, 24, 850-855.

Chaumard C, Quero A-M, Bouley G, Girard F, Boudene C, and German A.(1983). Influence of inhaled Cadmium Microparticles on Mouse Influenza Pneumonia. Environ Res, 31, 428-439.

Chen CY and Lin KC (1997). Optimisation and performance evaluation of the continuous algae toxicity test. Environmental Toxicology and Chemistry, 16,1337-1344.

Cherian MG, Goyer RA, and Delaquerriere-Richardson L.(1976). Cadmium-metallothionein-induced nephrotoxicity. Toxicology and Applied Pharmacology, 38, 399-408.

Cherian MG, Goyer RA, and Valberg LS.(1978). Gastrointestinal absorption and organ distribution of oral cadmium chloride and cadmium-metallothionein in mice. J Toxicol Environ Health, 4, 861-868.

Cherian MG.(1983). Absorption and tissue distribution of cadmium in mice after chronic feeding with cadmium chloride and cadmium-metallothionein. Bull Environ Contam Toxicol, 30, 33-36.

Chia KS, Ong CN, Ong HY, and Endo G.(1989). Renal tubular function of workers exposed to low levels of cadmium. Br.J.Ind.Med., 46, 165-170.

Chia SE, Xu B, Ong CN, Tsakok M, and Lee ST.(1994). Effect of Cadmium Cigarette Smoking on Human Semen Quality. Int J Fertil, 39, 292-298.

Chmielnicka J, Halatek T and Jedlinska U (1989). Correlation of cadmium-induced nephropathy and themetabolism of endogenous copper and zinc in rats. Ecotoxicology and Environmental Safety, 18, 268-276.

Christensen FC and Olson EC.(1957). Arch.Ind.Health, 16, 8-8.

Christensen T.H., Kjeldsen P., Albrechtsen H.J., Heron G., Nielsen P.H., Bjerg, P.L., Holm, P.E. (1994) Attenuation of landfill leachate pollutatnts in aquifers. Critical reviews in Environmental Science and Technology, 24 (2), 119-202.

Christensen TH (1989). Cadmium soil sorption at low concentrations: VIII. Correlation with soil properties. Water, Air and Soil Pollution, 44, 71-82.

Christley J and Webster WS.(1983). Cadmium uptake and distribution in mouse embryos following maternal exposure during the organogenic period: a scintillation and autoradiographic study. Teratology, 27, 305-312.

Christoffersson JO, Welinder H, Spang G, Mattsson S, and Skerfving S.(1987). Cadmium concentration in the kidney cortex of occupationally exposed workers measured in vivo using X-ray fluorescence analysis. Environ Res, 42, 489-499.

Chung J, Nartey NO, and Cherian MG.(1986). Metallothionein levels in liver and kidney of Canadians - a potential indicator of environmental exposure to cadmium. Arch Environ Health, 41, 319-323.

Church SE, Fey DL, Unruh DM, Vaughn RB and Taggart JE Jr. (2000). Geochemical and isotopic data from streambed sediment, Animas River watershed, Colorado, 1995-1999. U.S. Department of the Interior, U.S. Geological Survey, Open-File Report 00-244, 17p.

Chvapil M.(1973). New aspects in the biological role of zinc: A stabiliser of macromolecules and biological membranes. Life Sci., 13, 1041-1049.

Cikutovic MA, Fitzpatrick LC, Venables BJ and Goven AJ (1993). Sperm count in earthworms (Lumbricus terrestris) as a biomarker for environmental toxicology: effects of cadmium and chlordane. Environmental Pollution, 81, 123-125.

Clark DE, Nation JR, Bourgeois AJ, Hare MF, Baker DM, and Hinderberger EJ.(1985). The regional distribution of cadmium in the brains of orally exposed rats. Neurotoxicology, 6, 109-114.

Cloke R. (1999).The cell and battery collection project in the UK. In: Proceedings of the OECD workshop on the effective collection and recycling of Nickel-Cadmium batteries, Lyon,-France 23-25 september 1997, p. 89-92., Series on Risk Management N°8.

Clough SR, Welsh MJ, Payne AH, Brown CD, and Brabec MJ.(1990). Primary rat Sertoli and interstitial celss exhibit a different response to cadmium. Cell Biol Toxicol, 6, 63-79.

CollectNiCad (2000). JP Wiaux, pers. com., Sept. 2000.

CollectNiCad (2000a). The European Market for Portable and Industrial Ni-Cd batteries: a report on available data. Prepared for Atrium 2000 and the European Economical Interest Group.

CollectNicad (2000b). Reports data collected after consulting the various actors in the collection and recycling field at the European level. Unpublished report.

CollectNiCad (2000c). The European market of portable and industrial Ni-Cd batteries. Unpublished report.

CollectNiCad (2000d). Country by Country data. Unpublished report.

CollectNiCad (2000e). Market trends 1999. Unpublished report.

CollectNiCad (2000f). Recycling country by country data. Unpublished report.

CollectNiCad (2000g) Overview of Ni-Cd collection systems in various European countries. Unpublished report.

CollectNiCad (2001a) Recycling country by country data. Unpublished report.

CollectNiCad (2002). Industrial NiCd batteries: collection and recycling: update figures for 2000 and 2001. Unpublished report.

CollectNiCad (2002). JP Wiaux, pers. com., July 2002.

CollectNiCad (2002). JP Wiaux, pers. com., Oct. 2002.

CollectNiCad (2002). Personal communication by Mr. J.-P. Wiaux.

CollectNiCad (2002a). Flow sheet figure 2.4.4. Unpublished report.

CollectNiCad (2002b). Market trends 2000. Unpublished report.

CollectNiCad (2002c): Sorting of Nickel-Cadmium batteries from MSW streams. Mass flow of cadmium in MSW incinerators. Unpublished report (see also Annex II)

Collins JF, Brown JP, Painter PR, Jamall IS, Zeise LA, Alexeeff GV, Wade MJ, Siegel DM, and Wong JJ.(1992). On the carcinogenicity of cadmium by the oral route [see comments]. Regul.Toxicol.Pharmacol., 16 , 57-72.

Coni E, Baldini M, Stacchini P and Zanasi F (1992). Cadmium intake with diet in Italy: a pilot study. Journal of Trace Elements, Electrolytes and Health Diseases, 6, 175-181.

Conrad CC, Walter CA, Richardson A, Hanes MA, and Grabowski DT.(26-12-1997). Cadmium toxicity and distribution in metallothionein-I and -II deficient transgenic mice. J Toxicol.Environ Health, 52, 527-543.

Conway HL (1978). Sorption of arsenic and cadmium and their effects on growth, micronutrient utilization, and photosynthesis pigment composition of Asterionella formosa. Journal of the Fisheries Research Board of Canada, 35, 286-294.

Conway HL and Williams SC (1979). Sorption of Cd and its effect on growth and the utilization of inorganic carbon and phosphorus of two freshwater diatoms. Journal of the Fisheries Research Board of Canada, 36, 579-586.

Coogan TP, Bare RM, and Waalkes MP.(1992). Cadmium-induced DNA strand damage in cultured liver cells: reduction in cadmium genotoxicity following zinc pretreatment. Toxicol Appl.Pharmacol., 113, 227-233.

Cooke JA and Johnson MS (1996). Cadmium in small mammals. In: Environmental contaminants in wildlife: interpreting tissue concentrations. Edited by WN Beyer et al. Lewis Publishers, Boca Raton, Florida., 377-388.

Cooper DC and Morse JW (1998). Extractability of metal sulphide minerals in acidic solutions: application to environmental studies of trace metal contamination within anoxic sediments. Environmental Science and Technology, 32: 1076-1078.

Corden C, Floyd P, Brooke D, Crookes M, MacCrae S and Moore L (2001). The risks to health and environment by cadmium used as a colouring agent or a stabiliser in polymers and for metal plating. Risk & Policy Analysts Ltd, Northfolk, U.K. Project: J316/Cadmium.

Cornelis C, Geuzens P, Corthouts V and Van den Broek D (1993). Achtergrondsgehalten van een aantal anorganische en organische verontreinigingen in Vlaamse bodems. Deelrapport 3 MIE/DI/99327, VITI, Mol, Belgium. (in Dutch).

Cornfield AH (1977). Effects of addition of 12 metals on carbon dioxide release during incubation of an acid sandy soil. Geoderma, 19, 199-203.

Cornu (1995). The Ni-Cd battery : a must for the public transit. NiCad94, Report on Conference : Geneva, Switserland, International Cadmium Association, p.39-44.

Cortona G, Apostoli P, Toffoletto F, Baldasseroni A, Ghezzi I, Goggi E, Fornari S, and Alessio L.(1992).Occupational exposure to cadmium and lung function. In:Cadmium in the Human Environment: Toxicity and Carcinogencity. Edited by GF Nordberg, RFM Herber, and L Alessio. IARC. Lyon, 205-210.

Cousins RJ, Barber AK and Trout JR (1973). Cadmium toxicity in growing swine. Journal of Nutrition, 103, 964-972.

COWI (2000). Mass Flow Analysis of Cadmium. Report prepared by COWI Consulting Engineers and Planners for the Danish Environmental Protection Agency, the Chemical Office.

CPSC (Consumer Product Safety Commission).(1997). CPSC Staff Report on Lead and Cadmium in Children's Polyvinylchloride (PVC) Products.

CRC 1985.(1985). Cadmium and Health: a toxicological and epidemiological appraisal. Exposure, Dose and Metabolism. Edited by L Friberg, CG Elinder, T Kjellström, and GF Nordberg. CRC Press. Boca Raton, Florida,

CRC 1986.(1986). Cadmium and Health: A Toxicological and Epidemiological Appraisal.Effects and Response. Edited by L Friberg, CG Elinder, T Kjellström, and GF Nordberg. CRC Press. Boca Raton Florida,

Cresta L, Perdelli F, franco Y, Raffo E, Cristina ML, and Diani F.(1989). Possibili correlazioni tra cadmio urinario e ritardato accrescimento fetale in gestanti fumatrici. Minerva Ginecologica, 41, 85-88.

Crommentuijn T, Brils J and van Straalen NM (1993). Influence of cadmium on life-history characteristics of Folsomia candida (Willem) in an artificial soil substrate. Ecotoxicology and Environmental Safety, 26, 216-227.

Crommentuijn T, Doornekamp A and van Gestel CAM (1997b). Bioavailability and ecological effects of cadmium on Folsomia candida (Willem) in an artificial soil substrate as influenced by pH and organic matter. Applied Soil Ecology, 5, 261-271.

Crommentuijn T, Polder MD and van de Plassche EJ (1997a). Maximum Permissible Concentrations and Negligible Concentrations for metals, taking background concentrations into account. National Institute of Public Health and Environmental Protection, Bilthoven, The Netherlands. Report N° 601501 001.

Crommentuijn T, Stäb JA, Doornekamp A, Estoppey O and van Gestel CAM (1995). Comparative ecotoxicity of cadmium, chlorpyrifos and triphenyltin hydroxide for four clones of the parthenogenetic collembolan Folsomia candida in an artificial soil. Functional Ecology, 9, 734-742.

Crommentuijn T., Polder M.D. and van de Plassche E.J. (1997a). Maximum Permissible Concentrations and Negligible Concentrations for metals, taking background concentrations into account. National Institute of Public Health and Environmental Protection, Bilthoven, the Netherlands. Report N° 601501 001.

Crössman G and Wüstemann M (1992). Belastung in Haus und Kleingärten durch anorganische und organische Stoffe mit Schadstoffpotential. Sachstandsdocumentation. Landwirtschaftliche Untersuchung und Forschungsanstalt des Landwirtschaftskammer Westfalen-Lippe. Münster, 207pp.

Cuadrado C, Kumpulainen J and Moreiras O (1995). Contaminants and nutrients in total diets in Spain. European Journal of Clinical Nutrition, 49, 767-778.

Cummins PE, Dutton J, Evans CJ, and et al.(1980). An in vivo study of renal cadmium and hypertension. Eur J Clin Invest, 10, 459-461.

Dachler M and Kernmayer (1997). Düngemittelaufwand in Österreich. In Köchl, A.: Bodenschutz in Österreich. Bundesamt und Forschungszentrum für Landwirtschaft, Wien.

Dahm W., Kollbach St. and Gebel J. (1994). Sickerwasserreinigung: Stand der Technik 1993/1994; zukünftige entwicklungen, EnviroConsult GmbH, Neuruppin: EF-Verl. für Energie-und Umwelttechnic, 1994 ISBN 3-924511-79-9

Dalenberg JW and Vandriel W (1990). Contribution of atmospheric deposition to heavy-metal concentrations in field crops. Netherlands Journal of Agricultural Sciences, 38, 369-379.

Danish EPA (1994). Heavy Metals. State of the Art, Targets and Reduction Instruments. Nr. 3. 54pp.

Danish EPA (1997). Danish Product Register Data on 31 substances from the third Priority List (incl. cadmium(oxide)). Danish EPA, 1997.

Danish EPA (1998). Danish Product Register. Arbejdstilsynet. 1998.

Danish EPA (2000). Massestromsanalyse for cadmium. Rapport, udkast (draft). April 2000. English summary.

Danish EPA (2001). Waste statistics, 1999.Orientering fra Miljostyrelsen Nr 4. 2001.

Dave G, Andersson K, Berglind R and Hasselrot B (1981). Toxicity of eight solvent extraction chemicals and of cadmium to water fleas, Daphnia magna, rainbow trout, Salmo gairdneri, and zebrafish, Brachydanio rerio. Comparative Biochemistry and Physiology C-Toxicology & Pharmacology, 69, 83-98.

Davis SF, Wood KD, Huss MT, Hathway JE, and Roberts SL.(1995). Odor-mediated performances is affected by cadmium ingestion. Psychol Rec, 45, 389-403.

Davison AG, Newman Taylor AJ, Darbyshire J, Chettle DR, Gutherie CJG, and O'Malley D.(1988). Cadmium fume inhalation and emphysema. Lancet, 663-667.

De Broe ME and Elseviers MM.(1998). Analgesic nephropathy. N Engl J Med, 338, 446-452.

De Broe ME and Elseviers MM.(1998). Analgesic nephropathy. N Engl J Med, 338, 446-452.

De Kort WL, Verschoor MA, Wibowo AA, and et al.(1987). Occupational exposure to lead and blood pressure: A study in 105 workers. Am J Ind Med, 11, 145-156.

De SK, McMaster MT, and Andrews GK.(1990). Endotoxin induction of murine metallothionein gene expression. J Biol Chem, 265, 15267-15274.

De Temmerman L, Vanongeval L, Boon W, Hoenig M and Geypens M (2000). Gehalten aan spoorelementen in akkerbodems in Vlaanderen. Publicatie CODA-BDB, 2000/1,16 pp.

Deauville (1999) Reference currently missing

Decker LE, Byerrum RU, Decker CF, and et al.(1958). Chronic toxicity studies.I.Cadmium administered in drinking water to rats. Ama Arch Ind Health, 18, 228-231.

Deknudt G and Léonard A.(1975). Cytogenetic Investigations on Leucocytes of Workers from a Cadmium Plant. Environ Physiol Biochem, 5, 319-327.

Deknudt G, Léonard A, and Ivanov B.(1973). Chromosome aberrations observed in male workers occupationally exposed to lead. Environ Physiol Biochem, 3, 132-132.

dell'Omo M, Muzi G, Piccinini R, Gambelunghe A, Morucci P, Fiordi T, Ambrogi M, and Abbritti G.(1999). Blood cadmium concentrations in the general population of Umbria, Central Italy. Sci Total Environ, 226, 57-64.

DeNoyelles F Jr, Knoechel R, Reinke D, Treanor D and Altenhofen C (1980). Continuous culturing of natural phytoplankton communities in the experimental lakes area: Effects of enclosure, in situ incubation, light, phosphorus, and calcium. Canadian Journal of Fisheries and Aquatic Sciences, 37, 4-433.

Denzer S., M. Herrchen, P. Lepper, M. Müller, R. Sehrt, A. Storm and J. Volmer (1999). Revised proposal for a list of priority substances in the context of the Water Framework Directive (COMMPS procedure). Declaration ref.: 98/788/3040/DEB/E1. Fraunhofer-Institut, Umweltchemie und Ökotoxikologie, Germany. 80p.

Desi I, Nagymagtenyi L, and Schulz H.(1998). Behavioural and neurotoxicological changes caused by cadmium treatment of rats during development. J Appl Toxicol, 18, 63-70.

Desole MS, Miele M, Esposito G, Fresu L, Enrico P, De Natale G, Anania V, and Miele E.(31-5-1991). [Cadmium-induced changes in the activity of the dopaminergic and purinergic systems and in ascorbic acid catabolism in the rat striatum]. Clin.Ter., 137, 229-234.

Di Toro DM, Hansen DJ, McGrath JA and Berry WJ (2000). Predicting the toxicity of metals in sediments using organic carbon normalized SEM and AVS. Draft manuscript. HydroQual, Inc., Mahwah, New Jersey.

Di Toro DM, Mahony JD, Hansen DJ, Scott KJ, Carlson AR and Ankley GT (1992). AVS predicts the acute toxicity of Cd and Ni in sediments. Environmental Science & Technology, 26, 6-101.

Dill JA, Greenspan BJ, Mellinger KH, Roycroft JH, and Dunnick J.(1994). Disposition of inhaled cadmium oxide aerosol in the rat. Inhalation Toxicology, 3, 379-393.

Ding GY, Sun GF, Fen ZL, Li LX, and Li CY.(1987). Epidemiologic research of cancer in exposed cadmium,lead and arsenic workers. J Chin Med Univ, 16, 368-371.

Dixon RL, Lee IP, and Sherins RJ.(1976). Methods to assess reproductive effects of environmental chemicals: studies of cadmium and boron administered orally. Environ Health Perspect, 13, 59-67.

Dodds-Smith ME, Johnson MS and Thompson DJ (1992a). Trace metal accumulation by the shrew. Sorex araneus. Ecotoxicology and Environmental Safety, 24, 2-117.

Dodds-Smith ME, Johnson MS and Thompson DJ (1992b). Trace metal accumulation by the shrew. Sorex araneus .2. Tissue distribution in kidney and liver. Ecotoxicology and Environmental Safety, 24, 118-130.

Doedens H. and Theilen U. (1992). Effluent requirements and related leachate treatment processes. In landfilling of waste: leachate. P. 417-428. Edited by Christensen T.H., Cossu R. and Stegmann R.

Doelman P and Haanstra L (1984). Short-term and long-term effects of cadmium, chromium, copper, nickel, lead and zinc on soil microbial respiration in relation to abiotic soil factors. Plant and Soil, 79, 317-327.

Doelman P and Haanstra L (1986). Short- and long-term effects of heavy metals on urease activity in soils. Biology and Fertility of Soils, 2, 213-218.

Doelman P and Haanstra L (1989). Short- and long-term effects of heavy metals on phosphatase activity in soils: An ecological dose-response model aproach. Biology and Fertility of Soils, 8, 235-241.

Doll R.(1992). Is Cadmium a Human Carcinogen? AEP, 3, 335-337.

Doyle JJ, Pfander WH, Grebing SE and Pierce JO (1974). Effect of dietary cadmium on growth, cadmium absorption and cadmium tissue levels in growing lambs. Journal of Nutrition, 104, 160-166.

Drasch G, Kauert G, and von Meyer L.(1985). Cadmium body burden of an occupationally non burdened population in southern Bavaria (FRG). Int.Arch.Occup Environ Health, 55, 141-148.

Dressler RL, Storm GL, Tzilkowski WM and Sopper WE (1986). Heavy-metals in cottontail rabbits on mined lands treated with sewage-sludge. Journal of Environmental Quality, 15, 8-281.

DTU (2001). Waste related emission scenario’s for risk assessment of chemicals. A background document for revision of the EU Technical Guidance Document on risk assessment of new and existing substances.

Dubrow R and Wegman DH.(1984). Cancer and occupation in Massachusetts: a death certificate study. Am J Ind Med, 6, 207-230.

Ducoffre G, Claeys F, and Sartor F.(1992). Decrease in blood cadmium levels over time in Belgium. Arch Environ Health, 47, 354-356.

Duddridge JE and Wainwright M (1980). Heavy metal accumulation by aquatic fungi and reduction in viability of Gammarus pulex fed Cd2+ contaminated mycelium. Water Research, 14, 5-1611.

Düngemann H, Borelli S, and Wittmann J.(1972). Kupfer- und Kadmium-Kontaktekzeme bei Schweissern, Schleifern und ähnlichen Berufsgruppen. Arbeitsmedizin, Sozialmedizin, Arbeitshygiene, 7, 85-93.

Dušek L (1995). The effect of cadmium on the activity of nitrifying populations in two different grassland soils. Plant and Soil, 177, 3-53.

Dziekanowska D.(1981). Studies on mutagenic effect of environmental factors in heavy metal plants. Pat.Pol., 32, 263-268.

Eaton JG (1974). Chronic cadmium toxicity to the bluegill (Lepomis macrochirus Rafinesque). Transactions of the American Fisheries Society, 4, 729-735.

Eaton JG, McKim JM and Holcombe GW (1978). Metal toxicity to embryos and larvae of seven fresh water fish species - I Cadmium. Bulletin of Environmental Contamination and Toxicology, 19, 95-113.

EBRC.(2001). Occupational inhalation exposure in the zinc oxide producing industry. Data base revision. Final report.

EC (1994). Report. Management and Composition of Leachate from Landfills. Water Quality Institute and Carl Bro Environment a/s. Sept. 1994.

EC (1999). EC/31/1999 Council directive on the landfilling of waste.

EC (2000). Council directive 2000/76/EC on the incineration of waste

EC (2003). DG ENTERPRISE: Environmental aspects of enterprise policy, resource-based and specific industries. Textiles, leather, toys. Expert Group on Toy Safety. Guidance Document N° 3, 3/02/03.

EC, 2003. Technical guidance document on Risk Assessment in support of Commission Directive 93/67/EEC on Risk Assessment for new notified substances, Commission Regulation (EC) No 1488/94 on Risk Assessment for existing substances and Directive 98/8/EC of the European Parliament and of the Council concerning the placing of biocidal products on the market. Part II: Environment. Office for Official Publications of the European Communities, Luxembourg.

EC, 2004a. European Union System for the Evaluation of Substances 2.0 (EUSES 2.0). Prepared for the European Chemicals Bureau by the National Institute of Public Health and the Environment (RIVM), Bilthoven, the Netherlands. Available via the European Chemicals Bureau, http://ecb.jrc.it.

EC, 2004b. Official Journal of the European Union, L. 216 of 16 June 2004, p. 3. Corrigendum of Directive 2004/73/EC in O.J., L 152 of 30 April 2004.

ECB (European Chemicals Bureau) (2000). ECBI/82/00-Rev. 1 (final minutes of C&L WG on ENV).

ECB (European Chemicals Bureau) (2002). ECBI/37/02-Rev. 2 (final minutes of C&L WG on ENV).

ECB (European Chemicals Bureau) (2003). ECBI/03/03 (draft minutes of CMR WG).

Ecolas (1995). Reference currently missing

Edling C, Elinder CG, and Randma E.(1986). Lung function in workers using cadmium containing solders. Br J Ind Med, 43, 657-662.

EEA (2000). Dangerous substances in waste. European Environment Agency, Technical rport N° 38, 50 p.

EEC (1985). La classification, l'emballage et l'étiquetage des substances dangereuses dans l'Union européenne. Partie II- Méthodes d'essai. Bijlage V: Methoden voor de bepaling van de fysisch-chemische eigenschappen, van de toxiciteit en van de ecotoxiciteit. C 8: Toxiciteit voor regenwormen. 1997, Commision Européenne, XI/64/97-Partie II.

Eggenberger and Waber (2000).Cadmium in seepage waters of landfills: a statistical and geochemical evaluation.

Ehrig (1989). Water and element balances of landfills p 83-155. In P. Baccini The landfill: Reactor and final storage. Lecture notes in Earth sciences, Springer, Heidelberg, Germany.

Ehrig and Scheelhase (1993). Pollution potential and long term behaviour of sanitary landfills. In proceedings Sardinia 93, Fourth International Landfill Symposium, Cagliari, Italy, 11-15 october 1993.

Ehrig H.J. (1989).Water and element balances of landfills. In : Baccini, P. (ed) : The landfill, reactor and final storage. Lecture Notes in Earth Sciences, 20, 83-115, Springer Verlag.

Eisenmann CJ and Miller RK.(1994). The placental transfer and toxicity of selenite relative to cadmium in the human term perfused placenta. Placenta, 15, 883-895.

Eklund G and Oskarsson A (1999). Exposure of cadmium from infant formulas and weaning foods. Food Additives and Contaminants, 16, 509-519.

Eklund G, Grawé KP and Oskarsson A (2001). Inorganic compounds. Bioavailability of cadmium from infant diets in newborn rats. Archives of Toxicology, DOI 10.1007/s00204-001-0280-z.

Elgersma F, Anderberg BS and Stigliani WM (1992). Emission factors for aqueous industrial Cd emissions in the river Rhine basin. A historical reconstruction for the period 1970-1988. Edited Proceedings Seventh International Cd Conference - New Orleans, Cd Association, London, Cd Council, Reston VA, International Lead Zinc Research Organization, Research Triangle Park NC.

Elinder CG (1997). Suggested causal association between cadmium and nephrotoxicity in voles: possibly confounded. Ambio, 26, 251.

Elinder CG and Nordberg M.(1982). Critical concentration of cadmium estimated by studies on horse kidney metallothionein. Dev.Toxicol.Environ.Sci., 9, 37-46.

Elinder CG and Nordberg M.(1985).Metallothionein. In:Cadmium and Health: a Toxicological and Epidemiological Appraisal. Volume I: Exposure, Dose, and Metabolism. Edited by L Friberg, CG Elinder, T Kjellström, and GF Nordberg. Boca Raton. 65-80.

Elinder CG, Edling C, Lindberg E, Kagedal B, and Vesterberg O.(1985). beta 2-Microglobulinuria among workers previously exposed to cadmium: follow-up and dose-response analyses. Am J Ind Med, 8, 553-564.

Elinder CG, Edling C, Lindberg E, Kagedal B, and Vesterberg O.(1985). Assessment of renal function in workers previously exposed to cadmium. Br J Ind Med, 42, 754-760.

Elinder CG, Friberg L, Lind B, and Jawaid M.(1983). Lead and cadmium levels in blood samples from the general population of Sweden. Environ Res, 30, 233-253.

Elinder CG, Kjellström T, Friberg L, Lind B, and Linnman L.(1976). Cadmium in kidney cortex, liver and pancreas, from Swedish autopsies. Arch Environ Health, 31, 292-302.

Elinder CG, Kjellström T, Hogstedt C, Andersson K, and Spang G.(1985). Cancer mortality of cadmium Workers. Br J Ind Med, 42, 651-655.

Elinder CG, Kjellström T, Lind B, Linnman L, Piscator M, and Sundstedt K.(1983). Cadmium exposure from smoking cigarettes: variations with time and country where purchased. Environ Res, 32, 220-227.

Elinder CG, Kjellström T, Lind B, Molander M-L, and Silander T.(1978). Cadmium concentrations in human liver, blood, and bile: comparison with a metabolic model. Environ Res, 17, 236-241.

Elinder CG, Piscator M, and Linnman L.(1977). Cadmium and zinc relationships in kidney cortex, liver and pancreas. Environ Res, 13, 432-440.

Elinder CG.(1985).Normal values for cadmium in human tissues, blood and urine in different countries. In:Cadmium and Health: a Toxicological and Epidemiological Appraisal. Exposure, dose, and metabolism. Edited by L Friberg, CG Elinder, T Kjellström, and GF Nordberg. CRC Press, Inc. Boca Raton, 81-102.

Ellen G, Egmond E, Van Loon JW, Sahertian ET and Tolsma K. (1990). Dietary intakes of some essential and non-essential trace elements, nitrate and nitrite and N-nitrosamines, by Dutch adults: estimated via a 24-hour duplicate portion study. Food Additives and Contaminants, 7, 207-221.

Ellickson KM, Meeker RJ, Gallo MA, Buckley BT, and Lioy PJ.(2001). Oral bioavailability of lead and arsenic from a NIST Standard Reference Soil Material. Arch Environ Contam Toxicol, 40, 128-135.

Elliott P, Arnold R, Cockings S, Eaton N, Järup L, Jones J, Quinn M, Rosato M, Thornton I, Toledano M, Tristan E, and Wakefield J.(2000). Risk of mortality, cancer incidence and stroke in a population potentially exposed to cadmium. Occupational and Environmental Medicine, 57, 94-97.

Ellis KJ and Stanton HC.(1985). Cadmium Inhalation Exposure Estimates: Their Significance With Respect to Kidney and Liver Cadmium Burden. J Toxicol Environ Health, 15, 173-187.

Ellis KJ, Morgan WD, Zanzi I, Yasumura S, Vartsky DD, and Cohn SH.(1980). In vivo measurement of ciritical level of kidney cadmium: dose- effect studies in cadmium smelter workers. Am J Ind Med, 1, 339-348.

Ellis KJ, Morgan WD, Zanzi I, Yasumura S, Vartsky DD, and Cohn SH.(1981). Critical concentrations of cadmium in human renal cortex: dose- effect studies in cadmium smelter workers. J Toxicol Environ Health, 7, 691-703.

Ellis KJ, Vartsky DD, Zanzi I, Cohn SH, and Yasumura S.(1979). Cadmium: in vivo measurement in smokers and nonsmokers. Science, 205, 323-325.

Elnabarawy MT, Welter AN and Robideau RR (1986). Relative sensitivity of three Daphnid species to selected organic and inorganic chemicals. Environmental Toxicology and Chemistry, 5, 393-398.

Eloy (19 ??) Reference currently missing

EMEP (2004). EMEP measurement data online: http://www.emep.int/ see Measurements, Heavy metals, EMEP heavy metal data. Last updated Sept. 2005 (also via www.nilu.no/projects/ccc/emepdata;html).

Engström B and Nordberg GF.(1979). Dose dependence of gastrointestinal absorption and biological half-time of cadmium in mice. Toxicology, 13, 215-222.

Engström B.(1981). Influence of chelating agents on toxicity and distribution of cadmium among proteins of mouse liver and kidney following oral or subcutaneous exposure. Acta Pharmacol Toxicol, 48, 108-117.

Engvall J and Perk J.(1985). Prevalence of hypertension among cadmium-exposed workers. Arch Environ Health, 40, 185-190.

Enserink L, Luttmer W and Maas-Diepeveen H (1990). Reproductive strategy of Daphnia magna affects the sensitivity of its progeny in acute toxicity tests. Aquatic Toxicology, 17, 15-26.

Environment Agency (2001): Pollution inventory 2001 http:// www.environment-agency-gov/uk/business

Environment Agency (2002). Pers. com. to MSR (comments to Aug.’02 version of TRAR), e-mail 28.10.02.

Environment Agency (2002). Solid residues from municipal waste incinerators in England and Wales. Environment Agency, May 2002.

EPBA (1997) Reference currently missing

Epstein M.(1996). Aging and the kidney. J.Am.Soc.Nephrol., 7, 1106-1122.

EREF (1999). Life Cycle Inventory of a Modern Municipal Solid Waste Landfill. USA Washington Environmental Research and Education Foundation. 403 p.

Eriksson J, Öborn I, Jansson G and Andersson A (1996). Factors influencing Cd-content in crops. Result from Swedish field investigations. Swedish Journal of agricultural Research, 26, 125-133.

ERL (1990). Environmental Resources Limited Final Report of the study to evaluate the sources of human and environmental contamination by cadmium, ref. No B6614-566-88.

ERM (1997). Market, evolution of technological progress and environmental impact of batteries and accumulators. Environmetal Resources Management, Oxford UK. Final Report, commissioned by the European Commission DGXI, 46 p. + annex.

ERM (2000). Analysis of the environmental impact and financial costs of a possible new European directive on batteries.

ERM (2000). Pers. com., 2000.

ERM (Environmental Resources Management) (1999). Study Requirements and Programme for Data Production and Gathering to Support a Future Evaluation of the Risks to Health and the Environment From Cadmium in Fertilisers. For: European Commission DG III. Final Report. March 1999.

ERM (Environmental Resources Management) (2001). Analysis and Conclusions from Member States’ Assessment of the Risk to Health and the Environment from Cadmium in Fertilisers. For the European Commission – DG Enterprise. Contract No. ETD/00/503201. Final Report. June 2001.

ESPA (European Stabilisers Producers Association).(2000). Cadmium exposure data in the stabiliser industry.

Estrela T, Marcuello C, and Dimas M (2000). Las agues continentales en los países mediterráneos de la unión Europea. Centro de Estudios Hydrográficos del CEDEX, España, 283p.

ETWC (2002) Wastebase, European Topic Centre on Waste, http://wastebase.eionet.eu.int.

EUPHEMET Synopsis (2000). EC project ENV4. Data and trends in production, consumption, use and theoretical background for the future policies on Cadmium, Lead & Mercury. M. Scoullos, I. Thornton & G. Vonkeman. Athens, Greece.

EUR 17527 (1997). Dietary exposure to cadmium. European Commission, DG 3. Office for Official Publications of the European Communities, Luxembourg.

EURAS, 2003. Zinc concentrations and bioavailability abiotic factors in the surface water and sediment upstream and downstream near the effluent discharge point of Cd metal production site 1. Final report, January 2003.

EUREX Follow-up CD-ROM (1998): List of all companies that submitted HEDSETs. EC. DG-JRC. ECB.

European Commission, 1999. Study on the prioritization of substances dangerous to the aquatic environment. ISBN 92-828-7981-X.

European Lead Stabilisers Association, 1996 Paper on cadmium compounds as stabilisers for PVC for the OECD workshop, Stockholm, October 1995. OECD. In: OECD proceedings of the cadmium workshop, session C: products containing cadmium. OECD, Paris, France, pp. 276-280.

EUSES 1.0 User Manual (1997). TSA Group Delft bv, European Chemicals Bureau, Ispra, Italy, 82pp.

Evans DM.(1960). Br.Med.J., 1, 173-173.

Evans J and Hastings L.(1992). Accumulation of Cd(II) in the CNS depending on the route of administration: Intraperitoneal, intratracheal or intranasal. Fundam.and Applied Toxicol, 19, 275-278.

Evjen J. and Catotti A. (2002). Vented sintered-plate nickel-cadmium batteries. In Handbook of batteries (eds. Linden & Reddy), 27.1-27.30.

Ewers U, Brockhaus A, Dolgner R, and et al.(1985). Environmental exposure to cadmium and renal function of elderly women living in cadmium-polluted areas of the Federal Republic of Germany. Int.Arch.Occup.Environ.Health, 55, 217-239.

Ewers U, Kramer M, and Körting H.(1993).Diagnostik der inneren Exposition (Human-Biomonitoring). In:Handbuch Umweltmedizin. Edited by, 1-19.

Ewers U, Turfeld M, Freier I, and Brockhaus A.(1996). Blei- und Cadmiumbelastung: Zähne als Indikatoren de Blei-und Cadmiumbelastung des Menschen. Z.Umweltchem.Ökotox., 8, 312-316.

Ewers U, Turfeld M, Freier I, Ferger S and Brockhaus A. (1990). Blei- und Cadmiumgehalte in Milchschneidezähnen von Kindern aus Duisburg und Gummersbach – Entwicklungstrend 1976-1988. Zbl. Hyg., 189, 333-351.

Ewers U, Turfeld M, Freier I, Hofstetter I, Stemmann G and Brockhaus A (1996). Blei- und Cadmiumgehalte in Milchschneidezähnen von Kindern aus Stolberg und anderen Städten Nordrhein-Westfalens: Entwicklungstrend 1968-1993. Zbl. Hyg., 318-330.

Falck FYJ, Fine LJ, Smith RG, Garvey J, Schork A, England B, McClatchey KD, and Linton J.(1983). Metallothionein and occupational exposure to cadmium. Br J Ind Med, 40, 305-313.

Farnsworth, M. (1980) : Cadmium Chemicals. International Lead Zinc Research Organization, Inc., New Yrok, N.Y. 10017., pp. 1 – 24.

Favino A, Candura F, Chiappino G, and Cavalleri A.(1968). Study on the androgen function of men exposed to cadmium. Med Lavoro, 59, 105-110.

FEA (2001). Personal communication air emissions Flemish Environment Agency. Air emissions extracted from Jaarmilieuverslagen.

Fennikoh KB, Hirshfield HI and Kneip TJ (1978). Cadmium toxicity in planktonic organisms of a freshwater food web. Environmental Research 15, 357-367.

Fernandez MA, Sanz P, Palomar M, Serra J, and Gadea E.(1996). Fatal chemical pneumonitis due to cadmium fumes. Occup.Med.Oxf., 46, 372-374.

Feustel A and Wennrich R.(1984). Zinc and Cadmium in Cell fractions of Prostatic Cancer Tissues of Different Histological Grading in Comparsion to BPH and Normal Prostate. Urol Res, 12, 147-150.

Feustel A, Wennrich R, Steiniger D, and KlauB P.(1982). Zinc and cadmium concentration in prostatic carcinoma of different histological grading in comparison to normal prostate tissue and adenofibromyomatosis (BPH). Urol Res, 10, 301-301.

Final Draft RAR Cd/CdO (2003). Risk Assessment Report Cadmium/cadmiumoxide, Environment part, draft of May 2003, Belgium.

Fingerle H, Fischer G, and Classen HG.(1982). Failure to produce hypertension in rats by chronic exposure to cadmium. Food Chem Toxicol, 20, 301-306.

Finnish Environment Institute (1997). Cadmium in fertilizers: risk to human health and the environment. Study report of the Finnish Ministry of Agriculture and Forestry.

Finnveden G. (1996). Solid waste treatment within the framework of Life Cycle Assessment : metals in municipal solid waste landfills. int. J. LCA, 1 (2), 74-78.

Fiolet DCM, Ritsema R, and Cuijpers CEJ.(1999). Metaalniveau's in volwassenen in Nederland, 1997. 529102 011, 1-55.

Fitzpatrick LC, Muratti-Ortiz JF, Venables BJ and Goven AJ (1996). Comparative toxicity in earthworms Eisenia fetida and Lumbricus terrestris exposed to cadmium nitrate using artificial soil and filter paper protocols. Bulletin of Environmental Contamination and Toxicology, 57, 63-98.

Flanagan PR, McLellan JS, Haist J, Cherian G, Chamberlain MJ, and Valberg LS.(1978). Increased dietary cadmium absorption in mice and human subjects with iron deficiency. Gastroenterology, 74, 841-846.

Flanders WD.(1984). Review: prostate cancer epidemiology. Prostate, 5, 621-629.

Fleig I, Rieth H, Stocker WG, and Thiess AM.(1983). Chromosome investigations of workers exposed to cadmium in the manufacturing of cadmium stabilisers and pigments. Ecotoxicology and Environmental Safety, 7, 106-110.

Flick DF, Kraybill HF, and Dimitroff JM.(1971). Toxic effects of cadium: a review. Environ Res, 4, 71-85.

Flyhammar P. (1995). Analysis of the cadmium flux in Sweden with special emphasis on landfill leachate. J. Environ. Qual, 24, 612-621.

Flyhammer P. and K. Hakansson (1999). The release of heavy metals in stabilsed MSW by oxidation. The Science of the total environment. 243/244, 291-303.

Flyhammer P., F. Tamaddon and L. Bengtsson (1998). Heavy metals in a municipal solid waste deposition cell. Waste Management Research, 16 (5), 403-410.

Food and Drug Administration (FDA).(1977). Total Diet Studies. 7320.08. Compliance Program Evaluation.

Foote RH.(1999). Cadmium affects testes and semenof rabbits exposed before and after puberty. Reprod.Toxicol., 13, 269-277.

Forni A, Toffoletto F, Ortisi E, and Alessio L.(1990).Occupational exposure to cadmium. cytogenetic findings in relation to exposure levels. In:Environmental Hygiene II. Edited by NH Seemayer and W Hadnagy. Springer-Verlag. Berlin, Heidelberg, New York, 161-164.

Forni A.(1992).Chromosomal effects of cadmium exposure in humans. In:Cadmium in the Human Environment: Toxicity and Carcinogenicity. Edited by GF Nordberg, RFM Herber, and L Alessio. IARC. Lyon, 377-383.

Forni A.(1994). Comparison of chromosome aberrations and micronuclei in testing genotoxicity in humans. Toxicology Letters, 72, 185-190.

Förstner and Carstens (1988) Reference currently missing

Forum of the European Geological Surveys Directors (2004). FOREGS Geochemical Baseline Program. Available on http://www.eurogeosurveys.org/foregs/ [2004].

Fouassin A and Fondu M (1981). Evolutie van het gemiddelde lood- en cadmiumgehalte in de dagelijkse voeding in België. Belgisch Archief van Sociale Geneeskunde, Hygiëne, Arbeidsgeneeskunde en Gerechtelijke Geneeskunde, 39, 1-14.

Fowler BA, Jones HS, Brown HW, and Haseman JK.(1975). The morphological effects of chronic cadmium administration on the renal vasculature of rats given low and normal calcium diets. Toxicol Appl Pharmacol, 34, 233-252.

Francis PC, Birge WJ and Black JA (1984). Effects of cadmium-enriched sediment of fish and amphibian embryo-larval stages. Ecotoxicology and Environmental Safety, 8, 378-387.

Fregert S and Hjorth N.(1969). Personal communication.

Fréry N, Nessmann C, Girard F, Lafond J, Moreau T, Blot P, Lellouch J, and Huel G.(1993). Environmental exposure to cadmium and human birthweight. Toxicology, 79, 109-118.

Friberg L and Kjellström T.(1974).Cadmium in the Environment. Edited by L Friberg, M Piscator, GF Nordberg, and T Kjellström. CRC Press. Boca Raton,Fla., 100-100.

Friberg L and Nyström A.(1952). Aspects on the prognosis in chronic cadmium poisoning. Läkartidningen., 49, 2629-2639.

Friberg L and Vahter M.(1983). Assessment of exposure to lead and cadmium through biological monitoring: results of a UNEP/WHO global study. Environ Res, 30, 95-123.

Friberg L.(1948). Proteinuria and kidney injury among workmen exposed to cadmium and nickel dust. J Ind hyg Toxicol, 30, 32-36.

Friberg L.(1950). Health hazards in the manufacture of alkaline accumulators with special reference to chronic cadmium poisoning. Acta Med Scand, Suppl 240, 1-124.

Friberg LT.(1985). Yant memorial lecture. The rationale of biological monitoring of chemicals--with special reference to metals. Am Ind.Hyg.Assoc.J, 46, 633-642.

Friis L, Petersson L and Edling C (1998). Reduced cadmium levels in human kidney cortex in Sweden. Environmental Health Perspectives, 106, 5-178.

Friis L, Petersson L, and Edling C.(1998). Reduced cadmium levels in human kidney cortex in Sweden. Environ Health Perspect, 106, 175-178.

Frostegard A, Tunlid A and Baath E (1993). Phospholipid fatty-acid composition, biomass, and activity of microbial communities from 2 soil types experimentally exposed to different heavy-metals. Applied and Environmental Microbiology, 59, 3605-3617.

Fu JY, Huang XS, and Zhu XQ.(1999). Study on peripheral blood lymphocytes chromosome abnormality of people exposed to cadmium in environment. Biomed Environ Sciences, 12, 15-19.

Fujimoto K. (1999). Consumer survey on hoarded rate of appliances with rechargeable batteries. Battery Association of Japan.

Fukuhara M, Bouley G, Godin J, Girard F, Boisset M, and Boudene C.(1981). Effects of Short-Term Inhalation of Cadmium Oxide on Rabbit Pulmonary Microsomal Enzymes. Biochem.Pharmacol., 30, 715-720.

Furness RW (1996). Cadmium in birds. In: Environmental contaminants in wildlife: interpreting tissue concentrations. Edited by WN Beyer et al. Lewis Publishers, Boca Raton, Florida, 389-404.

Furst A, Cassetta DM, and Sasmore DP.(1973). Rapid induction of pleural mesotheliomas in the rat. Proc west Pharmacol Soc, 16, 150-153.

Gade B., A. Heindl and H. Westermann (1998). Long term behaviour of hazardous waste landfills: observed reactions and geochemical modelling. 2nd International BayForrest Conference on development and application of Waste Technology, Garching, July 1-3, 1998.

Gade B., A. Heindl, H. Westermann and H. Pöllman (2000). Secondary mineral inventory of hazardous waste landfills. Applied mineralogy, Rammimair et al (eds) Balkema, Rotterdam, ISBN 90 5809 163 5.

Gade B., H. Westermann, A. Heindl R. Hengstmann, H. Pöllman, J. Riedmiller and G. Wiedemann (1997). Geochemistry and equilibrium models in hazardous waste landfills. Proceeding Sardinia 1997. Sixth International landfill symposium.

Gade, B., J. Riedmiller, H. Westermann, A. Heindl and H. Pöllmann (1999). Mineralogical investigations and chemical equilibrium calculations on the hazardous waste landfill of Raindorf/Germany. E. Schweizebart’sche Verlagbuchhandlung, D-70176 Stuttgart, 0077-7757/99/0174-0249.

Galicia Garcia V, Rojas Lopez M, Rojas R, and Olaiz G.(1997). Cadmium levels in maternal cord and newborn blood in Mexico city. Toxicology Letters, 91, 57-61.

Ganong P.(1997).Section VIII. Formation and Excretion of Urine. Renal function & Micturition. In:Edited by, 653-660.

Gatta A, Bazzerla G, Amodio P, and et al.(1989). Detection of the early steps of cadmium nephropathy-comparison of light-and electron-microscopical patterns with the urinary enzymes excretion: An experimental study. Nephron, 51, 20-24.

Gavi F, Basta NT and Raun WR (1997). Wheat grain cadmium as affected by long-term fertilisation and soil acidity. Soil Science Society of America Journal, 26, 265-271.

Geiger H, Bahner U, Anderes S, and et al.(1989). cadmium and renal hypertension. Journal of Human Hypertension, 3, 231-227.

Gennart JP, Buchet JP, Roels H, Ghyselen P, Ceulemans E, and Lauwerys R.(1992). Fertility of male workers exposed to cadmium, lead, or manganese. Am J Epidemiol, 135, 1208-1219.

Gerritse RG and Van Driel W (1984). The relationship between adsorption of trace metals, organic matter and pH in temperate soils. Journal of Environmental Quality, 13, 197-204.

Gerritse, R.G. and Van Driel, W. (1984). The relationship between adsorption of trace metals, organic matter and pH in temperate soils. Journal of Environmental Quality, 13:197-204.

Gervais J and Delpech P.(1963). Cadmium intoxication. Arch.Mal.Prof.Med.Trav.Secur.Soc., 24, 803-816.

Ghezzi I, Toffoletto Fo, Sesana G, Fagioli MG, Micheli A, Di Silvestro P, Zocchetti C, and Alessio L.(1985). Behaviour of biological indicators of cadmium in relation to occupational exposure. Int.Arch.Occup.Environ.Health, 55, 133-140.

Giesy JP, Kania HJ, Bowling JW, Knight RL, Mashburn S and Clarkin S (1979). Fate and Biological Effects of Cadmium Introduced into Channel Microcosms. Environmental Research Laboratory, Office of Research and Development, U.S. Environmental Protection Agency, Athens, Georgia. EPA-600/3-79-039.

Giesy JP, Leversee GJ and Williams DR (1977). Effects of naturally occuring aquatic organic fractions on Cd toxicity to Simocephalus serrulatus (Daphnidae) and Gambusia affinis (Poeciliidae). Water Research, 11, 1013-1020.

Gill KD, Pal R, Sandhir R, and et al.(1989). Effect of chronic cadmium exposure on lipid composition and peroxidation in liver and kidneys in rats. Med Sci Res, 17, 921-924.

Gill PF.(1978). Respiratory function in a group of workers exposed to cadmium in Hobart. 207-210.

Gish CD and Christensen RE (1973). Cadmium, nickel, lead and zinc in earthworms from roadside soil. Environmental Science & Technology, 7, 1060-1062.

Glaser U, Hochrainer D, Otto FJ, and Oldiges H.(1990). Carcinogenicity and toxicity of Four Cadmium Compounds inhaled by Rats. Toxicological and Environmental Chemistry, 27, 153-162.

Glaser U, Klöppel H, and Hochrainer D.(1986). Bioavailability Indicators of Inhaled Cadmium Compounds. Ecotoxicology and Environmental Safety, 11, 261-271.

Gorree M, Tamis WLM, Traas TP and Elbers MA (1995). Biomag – a model for biomagnification in terrestrial food - chains - the Case of Cadmium in the kempen, The Netherlands. Science of the Total Environment, 168, 215-223.

Gottofrey J and Tjälve H.(1991). Axonal transport of cadmium in the olfactory nerve of the pike. Pharmacol Toxicol, 69, 242-252.

Goyer RA and Cherian MG.(1992).Role of metallothionein in human placenta and rats exposed to cadmium. In:Cadmium in the Human Environment: Toxicity and Carcinogenicity. Edited by GF Nordberg, RFM Herber, and L Alessio. IARC. Lyon, 239-247.

Goyer RA.(1991). Transplacental Transfer of Cadmium and Fetal Effects. Fundam.and Applied Toxicol, 16, 22-23.

Granerus G and Aurell M.(1981). Reference values for 51Cr-EDTA clearance as a measure of glomerular filtration rate. Scand.J.Clin.Lab.Invest., 41, 611-616.

Grant CA, Bailey LD, McLaughlin MJ and Singh BR (1999). Management techniques to reduce cadmium transfer from soils: a review. In: Cadmium in Soils, Plants and the Human Food Chain. Edited by McLaughlin et al. Kluwer Academic Publishers, Dordrecht, The Netherlands. In press.

Greenwald P.(1982). New directions in cancer control. Johns.Hopkins.Med J, 151, 209-213.

Grimm RHJ, Svendsen KH, Kasiske B, Keane WF, and Wahi MM.(1997). Proteinuria is a risk factor for mortality over 10 years of follow-up. MRFIT Research Group. Multiple Risk Factor Intervention Trial. Kidney Int Suppl, 63, S10-S14.

Grimm RHJ, Svendsen KH, Kasiske B, Keane WF, and Wahi MM.(1997). Proteinuria is a risk factor for mortality over 10 years of follow-up. MRFIT Research Group. Multiple Risk Factor Intervention Trial. Kidney Int Suppl, 63, S10-S14.

Grose EC, Richards JH, Jaskot RH, Ménache MG, Graham JA, and Dauterman WC.(1987). A comparative Study of the Effects of Inhaled Cadmium Chloride and Cadmium Oxide: Pulmonary Response. J Toxicol Environ Health, 21, 219-232.

Gross S.(1995). A review of the cadmium electrode. In proceedings NiCd94,Switserland, September 1994. Published by International Cadmium Association, London, p. 10-12.

Gross SB, Yeager DW, and Middendorf MS.(1976). Cadmium in liver,kidney, and hair of humans, fetal through old age. J Toxicol Environ Health, 2, 153-167.

Groten JP, Sinkeldam EJ, Luten JB, and et al.(1990). Comparison of the toxicity of inorganic and liver-incorporated cadmium: A '-week feeding study in rats. Food Chem Toxicol, 28, 435-441.

Groten JP, Sinkeldam EJ, Luten JB, and van Bladeren PJ.(1991). Cadmium accumulation and metallothionein concentrations after 4- week dietary exposure to cadmium chloride or cadmium- metallothionein in rats. Toxicol Appl Pharmacol, 111, 504-513.

Groten JP, Sinkeldam EJ, Muys T, Luten JB and Vanbladeren PJ (1991). Interaction of dietary Ca, P, Mg, Mn, Cu, Fe, Zn and Se with the accumulation and oral toxicity of cadmium in rats. Food and Chemical Toxicology, 29, 249-258.

GRS (2000) Campaign for the identification of spent batteries in Household Waste in Germany. Year 2000. Dr. J. Fricke.GRS. Heidenkampfsweg, 44 Hamburg. Germany. info@grs-batterien.de.

Gupta A, Murthy RC, and Chandra SV.(1993). Neurochemical changes in developing rat brain after pre- and postnatal cadmium exposure. Bull Environ Contam Toxicol, 51, 12-17.

Haanstra L and Doelman P (1984). Glutamic acid decomposition as a sensitive measure of heavy metal pollution in soil. Soil Biology and Biochemistry, 16, 595-600.

Haanstra L and Doelman P (1991). An ecological dose-response model approach to short- and long-term effects of heavy metals on arylsulphatase activity in soil. Biology and Fertility of Soils, 11, 18-23.

Habeebu SS, Liu J, Liu Y, and Klaassen CD.(2000). Metallothionein-null mice are more susceptible than wild-type mice to chronic CdCl(2)-induced bone injury. Toxicol Sci, 56, 211-219.

Habib FK, Odoma S, Busuttil A, and Chisholm GD.(15-6-1986). Androgen receptors in cancer of the prostate. Correlation with the stage and grade of the tumor. CANCER, 57, 2351-2356.

Hadley JG, Conklin AW, and Sanders CL.(1979). Systemic Toxicity of Inhaled Cadmium Oxide. Toxicology Letters, 107-111.

Hadley JG, Conklin AW, and Sanders CL.(1980). Rapid Solubilization and Translocation of 109CdO following Pulmonary Deposition. Toxicology and Applied Pharmacology, 54, 156-160.

Haghiri F (1973). Cadmium uptake by plants. Journal of Environmental Quality, 2, 93-96.

Hagmar L, Bonassi S, Stromberg U, Mikoczy Z, Lando C, Hansteen IL, Montagud AH, Knudsen L, Norppa H, Reuterwall C, Tinnerberg H, Brogger A, Forni A, Hogstedt B, Lambert B, Mitelman F, Nordenson I, Salomaa S, and Skerfving S.(1998). Cancer predictive value of cytogenetic markers used in occupational health surveillance programs. Recent Results Cancer Res, 154, 177-184.

Hahn R, Ewers U, Jermann E, Freier I, Brockhaus A, and Schlipkoter HW.(1987). Cadmium in kidney cortex of inhabitants of North-West Germany: its relationship to age, sex, smoking and environmental pollution by cadmium. Int.Arch.Occup Environ Health, 59, 165-176.

Hall WS, Paulson RL, Hall LWJr and Burton DT (1986). Acute Toxicity of Cadmium and Sodium Pentachlorophenate to Daphnids and Fish. Bulletin of Environmental Contamination and Toxicology, 37, 308-316.

Hallen IP, Jorhem L, Lagerkvist BJ, and Oskarsson A.(21-4-1995). Lead and cadmium levels in human milk and blood. Sci.Total Environ, 166, 149-155.

Hamilton-Koch W, Snyder RD, and Lavelle JM.(1986). Metal-induced DNA damage and repair in human diploid fibroblasts and Chinese hamster ovary cells. Chem Biol Interact., 59, 17-28.

Hammer DI, Calocci AV, Hasselblad V, Williams ME, and Pinkerson C.(1973). Cadmium and lead in autopsy tissues. J Occup Med, 15, 956-963.

Hamon RE, Wundke J, McLaughlin MJ and Naidu R (1997). Availability of zinc and cadmium to different plant species. Australian Journal of Soil Research, 35, 1-11.

Hamon RE, McLaughlin MJ, Naidu R and Correll R (1998). Long-term changes in cadmium bioavailability in soil. Environmental Science and Technology, 32, 3699-3703.

Han C, Wu G, Yin Y, and Shen M.(1992). Inhibition by germanium oxide of the mutagenicity of cadmium chloride in various genotoxicity assays. Food Chem Toxicol, 30, 521-524.

Hansen DJ, Berry WJ, Mahony JD, Boothman WS, Di Toro DM, Robson DL, Ankley, G.T., Ma, D., Yan, Q. and Pesch, C.E. (1996a). Predicting the toxicity of metal-contaminated field sediments using interstitial concentration of metals and Acid-Volatile Sulfide normalizations. Environmental Toxicology and Chemistry, 15, 2080-2094.

Hansen DJ, Mahony JD, Berry WJ, Benyi SJ, Pratt SD, Di Toro DM and Abel MB (1996b). Chronic effects of cadmium in sediments on colonization by benthic marine organisms: An evaluation of the role of interstitial cadmium and acid-volatile sulfide in biological availability. Environmental Toxicology and Chemistry, 15, 2126-2137.

Hansen JC, Wulf HC, Kromann N, and et al.(1985). Cadmium concentrations in blood samples from an East Greenlandic population. Dan.Med.Bull, 32, 277-279.

Hanstock, M. (1996): The recycling of non-ferrous metals. Cadmium, Lead and Mercury. ICME. Ottawa, Ontario. pp. 135 – 155.

Harada A.(1987). Results of fifteen years health examinations on cadmium workers in a cadmium pigment factory. 53, 219-233.

Hardell L, Moberg Wing A, Ljungberg BL, Dreifaldt AC, Degerman A, and Halmans G.(1994). Levels of cadmium, zinc and copper in renal cell carcinoma and normal kidney. Eur.J.Can.Prev., 3, 45-48.

Hardy HL and Skinner JB.(1947). The possibility of chronic cadmium poisoning. J Ind hyg Toxicol, 29, 321-324.

Hardy JT, Sullivan MF, Crecelius EA and Apts CW (1984). Transfer of cadmium in a phytoplankton-oyster-mouse food chain. Archives of Environmental Contamination and Toxicology, 13, 419-425.

Hare L and Tessier A (1996). Predicting animal concentrations in lakes. Nature, 380, 430-432.

Hare L, Carigna R and Huertadiaz MA (1994). A field study of metal toxicity and accumulation by benthic invertebrates-implication for the acid volatile sulfide (AVS) model. Limnology and Oceonography, 39, 1653-1668.

HARP-HAZ (2002). Reports on discharges, emissions and losses of hazardous substances to the 5th North Sea Conference in 2002. Quantative reporting (HARP-HAZ Prototype). Heavy metals.

Harris G (1998). An analysis of global fertiliser application rates for major crops. International Fertiliser Industry Association, Paris, France.

Harrison RM and Chirgawi MB (1989). The assessment of air and soil as contributors of some trace metals to vegetable plants. I. Use of a filtered air growth cabinet. The Science of the Total Environment, 83, 13-34.

Hart BA, Voss GW, and Willean CL.(1989). Pulmonary tolerance to cadmium following cadmium aerosol pretreatment. Toxicol Appl Pharmacol, 101, 447-460.

Hart BA.(1986). Cellular and Biochemical Response of the Rat Lung to Repeated inhalation of Cadmium. Toxicology and Applied Pharmacology, 82, 281-291.

Hartwig A and Beyersmann D.(1989). Comutagenicity and inhibition of DNA repair by metal ions in mammalian cells. Biol Trace Elem.Res., 21, 359-365.

Hartwig A.(1994). Role of DNA repair inhibition in lead- and cadmium-induced genotoxicity: a review. Environ Health Perspect, 102 Suppl 3, 45-50.

Harvey TC, Chettle DR, Fremlin JH, Al Haddad IK, and Downey SPMJ.(1979). Cadmium in Shipham. Lancet, 8115, 551-

Harvey TC, Thomas BJ, McLellan JS, and Fremlin JH.(1975). Measurement of liver cadmium concentrations in patients and industrial workers by neutron activation analysis. Lancet, 1, 1269-1272.

Hassler E, Lind B, and Piscator M.(1983). Cadmium in blood and urine related to present and past exposure. A study of workers in an alkaline battery factory. Br J Ind Med, 40, 420-425.

Hassler E.(1983). Exposure to cadmium and nickel in an alkaline battery factory as evaluated from measurements in air and biological material.

Hastings L and Evans JE.(1991). Olfractory primary neurons as a route of entry for toxic agents into the CNS. Neurotoxicology, 12, 707-714.

Hastings L, Choudhury H, Petering HG, and Cooper GP.(1978). Behavioral and biochemical effects of low-level prenatal cadmium exposure in rats. Bull.Environ.Contam Toxicol., 20, 96-101.

Hays ES and Margaretten N.(1985). Long-term oral cadmium produces bone marrow hypoplasia in mice. Exp Hematol, 13, 229-234.

Heath JC and Daniel MR.(1964). The production of malignant tumours by cadmium in the rat. Br J Cancer, 18, 124-129.

Heath JC, Daniel MR, Dingle JT, and Webb M.(1962). Nature, 193, 592-

HEDSET (1995): Database on cadmium(oxide), submitted by producing/importing companies liable to Regulation 793/93/EEC.

Hegyi E, Dolezalova E, Buthovâ D, and Husar I.(1974). On epidemiology of the contact eczema caused by nickel. Berufsdermatosen, 22, 193-201.

Heinrich U, Peters L, Ernst He, Rittinghausen S, Dasenbrock C, and König H.(1989). Investigation on the carcinogenic effects of various cadmium compounds after inhalation exposure in hamsters and mice. Exp.Pathol., 37, 253-258.

Heinrich U.(1992).Pulmonary carcinogenicity of cadmium by inhalation in animals. In:Cadmium in the Human Environment: toxicity and Carcinogenicity. Edited by GF Nordberg, RFM Herber, and L Alessio. IARC. Lyon, 405-413.

Hellstrand S and Landner L (1998). Cadmium in fertilisers, soil, crops and foods – the Swedish situtation. Swedish Environmental Research Group (MFG).

Hellstrom L, Elinder CG, Dahlberg B, Lundberg M, Jarup L, Persson B, and Axelson O.(2001). Cadmium exposure and end-stage renal disease. Am J Kidney Dis., 38, 1001-1008.

Hendrick DJ.(1996). Occupation and chronic obstructive pulmonary disease. Thorax, 51, 947-955.

Hendriks AJ, Ma W-C, Brouns JJ, Deruiterdijkman EM and Gast R (1995). Modeling and monitoring organochlorine and heavy-metal accumulation in soils, earthworms, and shrews in Rhine-Delta Floodplains. Archives of Environmental Contamination and Toxicology, 29, 115-127.

Henke G, Sachs HW, and Bohn G.(1970). Cadmium determination in the liver and kidneys of children and juveliles by means of neutron activation analysis. Arch.Toxikol., 26, 8-16.

Hickey RJ, Schoff EP, and Clelland RC.(1967). Relationship between air pollution and cettain chronic disease death rates. Arch Environ Health, 15, 728-738.

Higgins IT.(1975). Importance of epidemiological studies relating to hazards of food and environment. Br.Med Bull, 31, 230-235.

Hirano S, Tsukamoto N, and Suzuki KT.(1990). Biochemical changes in the rat lung and liver following intratracheal instillation of cadmium oxide. Toxicology Letters, 50, 97-105.

Hirst RN, Perry HM, Cruz MG, and Pierce JA.(1973). Elevated Cadmium Concentration in Emphysematous Lungs. Am Rev Resp Dis, 108, 30-39.

Hjelmar O., Hansen E. and Rokkjaer A. (1988). Groundwater contamination from an incinerator ash and household waste co-disposal site. Proceedings of UNESCO workshop on impact of waste disposal on groundwater and surface water, Copenhagen, Denmark, August 15-19, 1988.

Hjelmar O., (1989). Characterization of leachate from landfilled MSWI ash. International conference on municipal waste combustion, Hollywoof, Florida, USA, April, 11-14.

Hjelmar O., Mikkel Johanssen L., Knox K., Ehrig H.J., Flyvberg J., Winther P. and Christensen T.H.. (1994). Management and composition of leachate from landfills. Report for DGXI Waste 92, B4-3040/013665/92. Prepared by Water Quality Institute and Carl Bro Environment. Final report september 1994.

Hochi Y, Kido T, Nogawa K, Kido H, and Shaikh ZA.(1995). Dose-response relationship between total cadmium intake and prevalence of renal dysfunction using general linear models. J Appl Toxicol, 15, 109-116.

Hoffmann K, Becker K, Friedrich C, Helm D, Krause C, and Seifert B.(2000). The German Environmental Survey 1990/1992 (GerES II): cadmium in blood, urine and hair of adults and children. J Expo.Anal.Environ.Epidemiol., 10, 126-135.

Hofstetter I, Ewers U, Turfeld M, Freier I, Westerweller S, and Brockhaus A.(1990). Untersuchungen zur Blei- und Cadmiumbelastung von Kindern aus Stolberg. Öff.Gesundh.Wes., 52, 232-237.

Højmark Jensen J and Møller A (1990). National surveillance of food and contaminant intake : the Danish experience. (Reference currently missing)

Holcombe GW, Phipps GL and Marier JW (1984). Methods for conducting snail (Aplexa hypnorum) embryo through adult exposures: effects of Cd and reduced pH levels. Archives of Environmental Contamination and Toxicol., 13,627-634.

Holden H.(1969). Cadmium toxicology. Lancet, 2, 57-57.

Holden H.(1980). A mortality study of workers exposed to cadmium fumes. 211-215.

Holden H.(1980). Further mortality studies on workers exposed to cadmium fume in Occupational exposure to cadmium, Report on Seminar: London, 20 March 1980. 23-24.

Holland MK and White IG.(1980). Heavy metals and human spermatozoa.1. inhibition of the motility and metabolism of spermatozoa by metals related to copper. Fertility and Sterility, 34, 483-489.

Honda R, Tsuritani I, Ishizaki M, and Yamada Y.(1997). Zinc and copper levels in ribs of cadmium-exposed persons with special reference to osteomalacia. Environ Res, 75, 41-48.

Hopf G, Bocker R, Bischoff A, and et al.(1990). Investigation of the combined effects of ethanol and cadmium on rat liver and kidneys. Arch.Toxicol., 64, 470-473.

Horiguchi H, Sato M, Konno N, and Fukushima M.(1996). Long-term cadmium exposure induces anemia in rats through hypoinduction of erythropoietin in the kidneys. Arch.Toxicol., 71, 11-19.

Horiguchi H, Teranishi H, Niiya K, Aoshima K, Kato T, Sakuragawa N, and Kasuya M.(1994). Hypoproduction of erythropoietin contributes to anemia in chronic cadmium intoxication: clinical study on Itai-Itai disease in Japan. Arch.Toxicol., 68, 632-636.

Horn G. and Holt G. (1989).The recycling of nickel-cadmium batteries-experimental studies. Edited Proceedings Sixth International Cadmium Conference.

Horstowa H, Sikorski M, and Tyborski H.(1966). Chronic cadmium poisoning in the clinical and radiological picture. Med Pracy, 17, 13-15.

Hotz P, Buchet JP, Bernard A, Lison D, and Lauwerys R.(1999). Renal effects of low-level environmental cadmium exposure: 5- year follow-up of a subcohort from the Cadmibel study. Lancet, 354, 1508-1513.

Hovmand MF, Tjell JC and Mosbaek H (1983). Plant uptake of airborne cadmium. Environmental Pollution Series A, 30, 27-38.

Hubermont G, Buchet JP, Roels H, and Lauwerys R.(1978). Placental transfer of lead, mercury and cadmium in women living in a rural area. Importance of drinking water in lead exposure. Int.Arch.Occup.Environ.Health, 41, 117-124.

Huck FF.(1947). Cadmium poisoning by inhalation, report of a case. Occup.Med., 3, 411-414.

Huel G, Boudene C, and Ibrahim MA.(1981). Cadmium and Lead Content of Maternal and Newborn Hair : Relationship to Parity, Birth Weight, and Hypertension. Arch Environ Health, 36, 221-227.

Huel G, Everson RB, and Menger I.(1984). Increased Hair Cadmium in Newborns of Women Occupationally Exposed to Heavy Metals. Environ Res, 35, 115-121.

Hughson GW and Cherrie JW.(2001). Validation of the EASE model in relation to Dermal Zinc Exposures.

Hunter BA and Johnson MS (1982). Food-chain relationships of copper and cadmium in contaminated grassland ecosystems. Oikos, 38, 108-117.

Hunter BA, Johnson MS and Thompson DJ (1987a). Ecotoxicology of copper and cadmium in a contaminated grassland ecosystem .2. Invertebrates. Journal of Applied Ecology 24, 587-599.

Hunter BA, Johnson MS and Thompson DJ (1987b). Ecotoxicology of copper and cadmium in a contaminated grassland ecosystem .3. Small mammals. Journal of Applied Ecology, 24, 601-614.

Hunter BA, Johnson MS and Thompson DJ (1989). Ecotoxicology of copper and cadmium in a contaminated grassland ecosystem .4. Tissue distribution and age accumulation in small mammals. Journal of Applied Ecology, 26, 89-99.

Hutton M (1982). Cadmium in the European Community : a prospective assessment of sources, human exposure and environmental impact. The monitoring and Assessment research Centre, Chelsea College, University of London.

Hutton M and Goodman GT (1980). Metal contamination of feral pigeons columba-livia from the London area.1. Tissue accumulation of lead, cadmium and zinc. Environmental Pollution Series a-Ecological and Biological, 22, 207-217.

Hutton M, Eduljee G and de Meeûs C. (2001). Analysis and conclusions from Member States' assessment of the risk to health and the environment from cadmium in fertilisers. ERM Interim Report 7440.

IARC (International Agency for Research on Cancer).(1992). Cadmium in the Human Environment: Toxicity and Carcinogenicity.

IARC (International Agency for Research on Cancer).(1993).Cadmium and Cadmium Compounds. In:Volume 58: Beryllium, Cadmium, Mercury and Exposures in the Glass Manufacturing Industry. Edited by IARC LYON. IARC. United Kingdom, 119-237.

IAWG (1995). An International perspective on characterisation and management of residues from municipal solid waste incineration. Final document (Summary only).

IAWG (1997). Chandler, A.J., Eighmy, T.T., Hartlen, J., Hjelmar O., Kosson, D.S, Sawell S.E., Van Der Sloot, H.A. and Vehlow J.. Municipal solid waste incinerator residues. Studies in Environmental Science 67, Elsevier Science B.V. Amsterdam.

Ibekwe AM, Angle JS, Chaney RL and Berkum P. (1995). Sewage sludge and heavy metal effects on nodulation and nitrogen fixation of legumes. Journal of Environmental Quality, 24, 1199-1204.

IBGE (1998-1999). Guide pour l’établissement d’un bilan de production de déchets ménagers. Institut Bruxellois pour la gestion de l’Environnement. D/5762/1998/11. Gulledelle, 100 B-1200 Bruxelles. Contact. Madame C. Koczab.

ICdA (2000). Pers. com. M. Taylor

ICdA (International Cadmium Association).(1997). Existing Substances Regulation/ Data Submission for Cadmium/ Exposure Data Sheet for Cadmium Use(r)s (a compilation of data).

ICdA (International Cadmium Association).(2003). M. Taylor, personal communication, e-mail from La Floridienne, 2003.

ICdA (International Cadmium Association).(2003). M. Taylor, personal communication, written comments on the draft RAR Cd/CdO, May 2003.

Ide G (1988). Sanering van groentetuinen en van sterk verontreinigde terreinen. In Cadmium; Voorkomen, impakt en Sanering. Proceedings of a LISEC symposium in Genk, 23 maart 1988. LISEC, Publ. Genk, Belgium.

IFA (1998). Mineral Production and the Environment. Part 1. The Fertiliser Industry’s Manufacturing Process and Environmental Issues. International Fertiliser Industry Association, Paris, France.

Ikeda M, Watanabe T, Zhang ZW, Moon CS, and Shimbo S.(1997). The integrity of the liver among people environmentally exposed to cadmium at various levels. Int.Arch.Occup.Environ.Health, 69, 379-385.

Ikeda M, Zhang ZW, Moon CS, Shimbo S, Watanabe T, Nakatsuka H, Matsuda-Inoguchi N, and Higashikawa K.(2000). Possible effects of environmental cadmium exposure on kidney function in the Japanese general population. Int.Arch.Occup.Environ.Health, 73, 15-25.

Impact of lead acid batteries and cadmium stabilizers on incinerator emissions. In proceedings of the 1993 International Conference on Municipal Waste Combustion, Williamsburg.

Industry (Union Minière, Lead-company) (2002). Mr H. Waeterschoot, personal communication, June 2002.

Industry Questionnaire (1997). Questionnaire submitted to Cd/CdO producing industry. Federal Ministry of Public Health and Environment, Brussels, Belgium.

Industry questionnaire (1998; updates of 2000 and 2001): for the collection of site-specific exposure data of batteries’ producers and recyclers. The initial questionnaire was sent out by Industry in 1998, updates by the rapporteur in 2000 and 2001. Replies were obtained from 1998 till 2003.

Industry Questionnaire on battery production/ recyclers (1998). Questionnaire submitted to NiCd battery producing/recycling industry.

Industry questionnaires, 2004. Site-specific/compiled emission information for Cd metal/CdO production plants, Ni-Cd battery producing and recycling plants, Cd pigments producing plants and Cd stabiliser producing plants in the EU-16.

Ingersoll C and Kemle N (2000). Methods development for long-term sediment toxicity tests with the amphipod Hyalella azteca and the midge Chironomus tentans. Study conducted by U.S. Geological Survey Columbia Environmental Research Centre in Columbia Missouri for EPA.

Inoue S, Suzumura Y, and Takahashi K.(1994). A case of interstitial pneumonitis caused by inhalation of cadmium fumes. Nippon.Kyobu.Shikkan.Gakkai.Zasshi., 32, 861-866.

INRS (1987): Fiche toxicologique N° 60. Cadmium et composés. 4 p.

Inskip H, Beral V, and McDowall M.(1982). Mortality of Shipham Residents : 40-year follow-up. Lancet, 1, 896-899.

IOW (1997). European ecolabel batteries for consumer goods. Institut für ökologische Wirtschaftsforschung (Ecological Economics Researc Institute) Fourth Report and Background Information.

IPCS, International Programme on Chemical Safety (1992a). Cadmium. Environmental Health Criteria; 134. World Health Organization, Geneva.

IPCS, International Programme on Chemical Safety (1992b). Cadmium. Environmental Health Criteria; 135. World Health Organization, Geneva.

IPPC (2000). Reference Document on Best Available Techniques in the Non-Ferrous Metals Industries. EC DG JRC. Technologies for sustainable Development. European IPPC Bureau. May 2000. Seville.

IPPC, 2004. Reference Document on Best Available Techniques on Metal Treatment sector. EC DG JRC. Technologies for sustainable Development. European IPPC Bureau.

IRIS USEPA.(1996). Integrated Risk Information System.

ISO (1994). Draft Soil Quality-Effects of Soil Pollutants on Collembola (Folsomia candida): Method for the Determination of Effects on Reproduction. International Standardisation Organisation.

ISWA (2002). Energy from waste. State of the art report, statistics 4. Edition January 2002. Working group on Thermal treatment of Waste. Published by The International Solid Waste Association. 156 p.

Itokawa Y, Abe T, Tabei R, and et al.(1974). Renal and skeletal lesions in experimental cadmium poisoning. Arch Environ Health, 29, 149-154.

IUCLID (1997): Compiled database on cadmium(oxide) as submitted by producing/importing companies liable to Regulation 793/93/EEC (on diskette). EC. DG-JRC. ECB.

IUTA-Prüfbericht (2004). Unpublished document. M 040301.Über die verfahrenstechnischen Emissionsmessungen in Rheingas der Recycling Anlage vom 19.02 und 26.03.2004. Institut für Energie- und Umwelttechnik e.V.

Iwami K and Moriyama T. (1993). Comparative effect of cadmium on osteoblastic cells and osteoclastic cells. Arch.Toxicol., 67 , 352-357.

Iwata K, Saito H, Moriyama M, and Nakano A.(1991). Association between renal tubular dysfunction and mortality among residents in a cadmium-polluted area, Nagasaki, Japan. Tohoku.J Exp.Med, 164, 93-102.

Iwata K, Saito H, Moriyama M, and Nakano A.(1992). Follow up study of renal tubular dysfunction and mortality in residents of an area polluted with cadmium. Br J Ind.Med, 49, 736-737.

Iwata K, Saito H, Moriyama M, and Nakano A.(1992). Follow up study of renal tubular dysfunction and mortality in residents of an area polluted with cadmium. Br J Ind.Med, 49, 736-737.

IZA (International Zinc Association – Europe) (1998). Personal communication by F. Van Assche during clarification of so-called ‘Annex VIIA dossier’ (6/5/98).

IZA-Europe, ICdA, UM and CollectNiCad (2000 & 2001). Personal communication by F. Van Assche, M. Taylor, H. Waeterschoot and J.-P. Wiaux at TMIII’00 and later in 2000 as well as during the preparation of the revised TRAR on batteries in 2001.

ICdA (International Cadmium Association).(2005). Written comments on the final draft RAR Cd/CdO, version of July 2005 : Industry comments to Cd RAR env version of July 2005, 29 and 30/08/05.

Izuno T, Sugita M, Arita S, Otahara Y, Nasu I, Tsuchiya K, and Hayashi Y.(2000). Validity of Cadmium Concentration in Rice as the "Dose" of the Dose-Response Relationship between Cadmium Intake and Renal Dysfunction. Environ.Res.Section A, 84, 275-281.

Jacobs A, L. De Bock & R.. Dijkmans (2001). Best Beschikbare Technieken (BBT) voor asfaltcentrales, VITO.

Jak RG, Maas JL and Scholten MCTh (1996). Evaluation of laboratory derived toxic effect concentrations of a mixture of metals by testing fresh water plankton communities in enclosures. Water Research, 30:1215-1227.

Jakobsson Lagerkvist B, Söderberg HA, Nordberg GF, Ekesrydh S, and Englyst V.(1993). Biological monitoring of arsenic, lead and cadmium in occupationally and environmentally exposed pregnant women. Scand J Work Environ Health, 19, 50-53.

Jakubowski M, Razniewska G, Halatek T, and Trzcinka Ochocka M.(1992). Integrated index of occupational exposure to cadmium as a predictor of kidney dysfunction. IARC.Sci.Publ., 319-324.

Jakubowski M, Trojanowska B, Kowalska G, Gendek E, Starzynski Z, Krajewska B, and Jajte J.(1987). Occupational exposure to cadmium and kidney dysfunction. Int.Arch.Occup.Environ.Health, 59, 567-577.

Jamall IS, Naik M, Sprowls JJ, and et al.(1989). A comparison of the effects of dietary cadmium on heart and kidney oxidant enzymes: Evidence for the greater vulnerability of the heart to cadmium toxicity. J Appl Toxicol, 9, 339-345.

Janssen Pharmaceutica (1993a). The acute toxicity of cadmium in the zebra fish (Brachydanio rerio), Final environmental assessment report. Report N° AFBr/0019, 19pp.

Janssen Pharmaceutica (1993b). The acute toxicity of cadmiumoxide in the zebra fish (Brachydanio rerio), Final environmental assessment report. Report N° AFBr/0018, 19p.

Janssen Pharmaceutica (1993c). The acute toxicity of cadmium in the water-flea Daphnia magna, Final environmental assessment report. Report N° ADK6/0027, 20pp.

Janssen Pharmaceutica (1993d). The acute toxicity of cadmiumoxide in the water-flea Daphnia magna, Final environmental assessment report. Report N° ADK6/0025, 20pp.

Janssen Pharmaceutica (1993e). The acute toxicity of cadmium on the growth of the unicellular green alga Selenastrum capricornutum, Final environmental assessment report. Report N° AASc/0013, 23pp.

Janssen Pharmaceutica (1993f). The acute toxicity of cadmiumoxide on the growth of the unicellular green alga Selenastrum capricornutum, Final environmental assessment report. Report N° AASc/0012, 22pp.

Jansson G and Öborn I (1997). A field study on cadmium content in carrots and the influence of soil factors. In: Proceedings of the Fourth International Conference on the Biogeochemistry of trace elements. Edited by IK Iskander et al. US Army Cold Regions Research and Engineering Laboratory, Hanover, NH., 123-124.

Järup L and Elinder CG.(1993). Incidence of renal stones among cadmium exposed battery workers. Br J Ind Med, 50, 598-602.

Järup L and Elinder CG.(1994). Dose-response relations between urinary cadmium and tubular proteinuria in cadmium-exposed workers [see comments]. Am.J.Ind.Med., 26, 759-769.

Järup L, Alfven T, Persson B, Toss G, and Elinder CG.(1998). Cadmium may be a risk factor for osteoporosis. Occup.Environ.Med., 55, 435-439.

Järup L, Bellander T, Hogstedt C, and Spang G.(1998). Mortality and cancer incidence in Swedish battery workers exposed to cadmium and nickel. Occup.Environ.Med., 55, 755-759.

Järup L, Berglund M, Elinder CG, Nordberg G and Vahter M (1998). Health effects of cadmium exposure-a review of the literature and a risk estimate. Scandinavian Journal of Work Environment & Health, 24, 1-51.

Järup L, Berglund M, Elinder CG, Nordberg G, and Vahter M.(1998). Health effects of cadmium exposure- a review of the literature and a risk estimate. Scand J Work Environ Health, 24, 52 p.-

Jarup L, Carlsson MD, Elinder CG, Hellstrom L, Persson B, and Schutz A.(1995). Enzymuria in a population living near a cadmium battery plant. Occupational and Environmental Medicine, 52, 770-772.

Järup L, Elinder CG, and Spang G.(1988). Cumulative blood-cadmium and tubular proteinuria: a dose- response relationship. Int.Arch.Occup.Environ.Health, 60, 223-229.

Järup L, Hellström L, Alfven T, Carlsson MD, Grubb A, Persson B, Pettersson C, Spang G, Schütz A, and Elinder CG.(2000). Low level exposure to cadmium and early kidney damage: the OSCAR study. Occup Env Med, 57, 668-672.

Järup L, Persson B, and Elinder CG.(1995). Decreased glomerular filtration rate in cadmium exposed solderers. Occupational and Environmental Medicine, 52, 818-822.

Järup L, Persson B, and Elinder CG.(1997). Blood cadmium as an indicator of dose in a long-term follow-up of workers previously exposed to cadmium. Scand J Work Environ Health, 231, 31-36.

Järup L, Persson B, Edling C, and Elinder CG.(1993). Renal function impairment in workers previously exposed to cadmium. Nephron, 64, 75-81.

Järup L, Rogenfelt A, Elinder CG, Nogawa K, and Kjellström T.(1983). Biological half-time of cadmium in the blood of workers after cessation of exposure. Scand J Work Environ Health, 9, 327-331.

Jasiewicz C (1994). The influence of liming on phytotoxicity of cadmium. Polish Journal of Soil Science, 27, 69-77.

Jensen A and Bro-Rasmussen F (1992). Environmental cadmium in Europe. Reviews of Environmental Contamination and Toxicology 125, 101-181.

Jensen A. and Bro-Rasmussen F. (1992). Environmental cadmium in Europe. Reviews of Environmental Contamination and Toxicology, 125, 101-181.

Jensen H and Mosbaek H (1990). Relative availability of 200 years old cadmium from soil to lettuce. Chemosphere, 20, 693-702.

Jin T and Frankel BJ.(1996). Cadmium-metallothionein nephrotoxicity is increased in genetically diabetic as compared with normal Chinese hamsters. Pharmacol Toxicol, 79, 105-108.

Jin T, Nordberg G, Wu X, Ye T, Kong Q, Wang Z, Zhuang F, and Cai S.(1999). Urinary N-acetyl-beta-D-glucosaminidase isoenzymes as biomarker of renal dysfunction caused by cadmium in a general population. Environ Res., 81, 167-173.

Jin T, Nordberg GF, and Nordberg M.(1986). Uptake of cadmium in isolated kidney cells - influence of binding form and in vivo pretreatment. J.Appl.Toxicol., 6, 397-400.

Jin T, Nordberg GF, Sehlin J, Leffler P, and Wu J.(18-4-1994). The susceptibility of spontaneously diabetic mice to cadmium- metallothionein nephrotoxicity. Toxicology, 89, 81-90.

Jockel W. and Hartjes J. (1995). Die Entwicklung der Schwermetallemissionen in der Bundesrepublik. Deutschland von 1985 bis 1995.

Johansson G, Åkesson A, Berglund M, Nermell B and Vahter M (1998). Validation with biological markers for food intake of a dietary assessment method used by Swedish women with three different dietary preferences. Public Health Nutrition, 1, 199-206.

John J, Gjessing ET, Grande M, Salbu B (1987). Influence of aquatic humus and pH on the uptake and depuration of cadmium by the Atlantic salmon (Salmo-Salar L). Science of the Total Environment, 62, 253-265.

Johnson C.A., M. Kaeppeli, S. Brandenberger; A. Ulrich and W. Baumann (1999). Journal of contaminant hydrology 40, 239-259.

Jones KC and Johnston AE (1989). Cadmium in cereal grain and herbage from long-term experimental plots at Rothamsted, UK. Environmental Pollution, 57, 199-216.

Jones KC, Symon CJ and Johnston AE (1987). Retrospective analysis of an archived soil collection. II. Cadmium. The Science of the Total Environment, 67, 75-89.

Jones MM, Basinger MA, Topping RJ, Gale GR, Jones SG, and Holscher MA.(1988). Meso-2,3-dimercaptosuccinic acid and sodium N-benzyl-N- dithiocarboxy-D-glucamine as antagonists for cadmium intoxication. Arch.Toxicol., 62, 29-36.

Jonsson A, Eklund M and Håkansson K (1997) Heavy metals of the 20th century recorded in oak tree rings. Journal of Environmental Quality, 26, 1638-1643.

Jop KM, Askew A.M. and Foster, R.B. (1995). Development of a Water-Effect Ratio for Copper, Cadmium, and Lead for the Great Works River in Maine Using Ceriodaphnia dubia and Salvelinus fontinalis. Bulletin of Environmental Contamination and Toxicology, 54:29-35.

Jorhem L and Sundström B (1993). Levels of lead, cadmium, zinc, copper, nickel, chromium, manganese and cobalt in foods on the Swedish market 1983-1990. Journal of Food Composition and Analysis, 6, 223-241.

Jouany JM, Ferard JF, Vasseur P, Gea J, Truhaut R and Rast C (1983). Interst of dynamic tests in acute ecotoxicity assessment of algae. Ecotoxicology and Environmental Safety, 7, 216-228.

Juniper (1997). European Energy from Waste Coalition. Energy from waste plants: databook of European sites. Juniper Consultancy services, November 1997.

Juste C and Tauzin J (1986). Evolution du contenu en métaux lourds d’un sol de limon maintenu en jachère nue après 56 années d’application continu de divers d’engrais et amendements. Comptes Rendus de l'Académie d’ Agriculture Française, 72, 739-746.

Kaaber S, Cramers M, and Jepsen FL.(1982). The role of cadmium as a skin sensitizing agent in denture and non-denture wearers. Contact Dermatitis, 8, 308-313.

Kádár I (1995). Effect of heavy metal load on soil and crop. Acta Agronomica Hungarica, 43, 3-9.

Kádár I, Szabo L and Sarkadi J (1998). Contamination of food chains with heavy metals and harmfull elements (in Hungarian). pp 63.

Kagamimori S, Williams WR, and Watanabe M.(1986). cGMP levels in chronic cadmium disease and osteoarthritis. Br J Exp.Pathol., 67, 517-521.

Kagamimori S, Williams WR, and Watanabe M.(1986). cGMP levels in chronic cadmium disease and osteoarthritis. Br J Exp.Pathol., 67, 517-521.

Kammenga JE, Van Koert PHG, Riksen JAG, Korthals GW and Bakker J (1996). A toxicity test in artificial soil based on the life-history strategy of the nematode Plectus acuminatus. Environmental Toxicology and Chemistry, 15, 722-727.

Kanisawa M and Schroeder HA.(1969). Life term studies on the effects of trace elements on spontaneous tumors in mice and rats. Cancer Res, 29, 892-895.

Karlsson-Norrgren L, Runn P, Haux C and Förlin L (1985). Cadmium-induced changes in gill morphology of zebrafish, Brachydanio rerio (Hamilton-Buchanan), and rainbow trout, Salmo gairdneri Richardson. Journal of Fish Biology, 27:81-95.

Kasuya M, Teranishi H, Horiguchi H, Kato T, Aoshima K, Morikawa Y, Saijo M, and Kanai M.(1991). A fifteen-year study on renal dysfunction among people living in a cadmium-polluted area. Kankyo Hoken Rep, 58, 120-122.

Kasuya M.(1996). Clinical records of itai-itai disease patients. 6, 86-233.

Katsuta O, Hiratsuka H, Matsumoto J, Iwata H, Toyota N, Tsuchitani M, Umemura T, and Marumo F.(1994). Cadmium-induced osteomalacic and osteopetrotic lesions in ovariectomized rats. Toxicol Appl Pharmacol, 126, 58-68.

Kawada T, Koyama H, and Suzuki S.(1989). Cadmium, NAG activity, and beta 2-microglobulin in the urine of cadmium pigment workers [see comments]. Br.J.Ind.Med., 46, 52-55.

Kawamura J, Yoshida O, Nishino K, and et al.(1978). Disturbances in kidney functions and calcium and phosphate metabolism in cadmium-poisoned rats. Nephron, 20, 101-110.

Kawano S and et al.(1981). J.Kanazawa Med univ, 6, 51-59.

Kawano S, Nakagawa H, Okumura Y, and Tsujikawa K.(1986). A mortality study of patients with Itai-itai disease. Environ Res., 40, 98-102.

Kazantzis G and Blanks RG.(1989). A mortality study of cadmium exposed workers.

Kazantzis G and Blanks RG.(1992). A mortality study of cadmium exposed workers. 150-157.

Kazantzis G and Hanbury WJ.(1966). The induction of sarcoma in the rat by cadmium sulphide and by cadmium oxide. Br J Cancer, 20, 190-199.

Kazantzis G, Blanks RG, and Sullivan KR.(1992).Is cadmium a human carcinogen? In:Cadmium in the Human Environment: Toxicity and Carcinogenicity. Edited by GF Nordberg, RFM Herber, and L Alessio. IARC. Lyon, 435-446.

Kazantzis G, Flynn FV, Spowage JS, and Trott DG.(1963). Renal tubular malfunction and pulmonary emphysema in cadmium pigment workers. Q J Med, 32, 165-192.

Kazantzis G, Lam TH, and Sullivan KR.(1988). Mortality of cadmium-exposed workers: a five-year update. Scand J Work Environ Health, 14, 220-223.

Kazantzis G.(1956). Respiratory function in men casting cadmium alloys. I. Assessment of ventilatory function. Br J Ind Med, 13, 30-36.

Kazantzis G.(1978). Some long-term effects of cadmium on the human kidney in Cadmium 77, Proc.1st Int.Cadmium Conf.San Francisco 1977. 194-198.

Kazantzis G.(1979). Cadmium nephropathy. Contrib Nephrol, 16, 161-166.

Kazantzis G.(1979). Renal tubular dysfunction and abnormalities of calcium metabolism in cadmium workers. Environ Health Perspect, 28, 155-159.

Keck C, Bramkamp G, Behre HM, Müller C, Jockenhövel F, and Nieschlag E.(1995). Lack of correlation between cadmium in seminal plasma and fertility status of nonexposed individuals and two cadmium-exposd patients. Reprod.Toxicol., 9, 35-40.

Kello D and Kostial K.(1977). Influence of age on whole body retention and distribution of 115mCd in the rat. Environmental Research, 14, 92-92.

Kelly, J.M., Parker, G.R. and Mc Fee, W.W. (1979). Heavy metal accumulation and growth of seedlings of five forest species as influenced by soil cadmium level. Journal of Environmental Quality, 8, 361-364.

Kemi (1996). Cadmium in fertilizers-Consultants report prepared for the OECD Cadmium workshop, Sweden, 16-20 October 1995. Swedish National Chemicals Inspectorate, Solna, Sweden.

Kemi (1997). Product Register for the year 1996 (15.09.97). Swedish National Chemicals Inspectorate, Solna, Sweden.

Kemi (1998). Cadmium Exposure in the Swedish Environment. Swedish National Chemicals Inspectorate, Solna, Sweden.

Kemi (1998a). Product Register. Swedish National Chemicals Inspectorate, Solna, Sweden.

Kemi (2000). Personal communication by Mrs M. (…).Swedish National Chemicals Inspectorate, Solna, Sweden.

Kemi (2000). Personal communication, written comments on the draft RAR Cd/CdO. As derived from Drake and Hellstrand, 1998, The economics of the Swedish Policy to Reduce cadmium in Fertilisers, KemI PM 2/98.

Kemi report (1998). Cadmium exposure in the Swedish environment. Swedish National Chemicals Inspectorate. Kemi Report Series N° 1/98. 113 p.

Kenaga C, Cherian G, Cox C, and Oberdörster G.(1996). Metallothionein Induction and Pulmonary Responses to Inhaled Cadmium Chloride in Rats and Mice. Fundam.and Applied Toxicol, 30, 204-212.

Khalil MA, Abdel-Lateif HM, Bayoumi BM and van Straalen N (1996a). Analysis of separate and combined effects of heavy metals on the growth of Aporrectodea caliginosa (Oligochaeta; Annelida), using the toxic unit approach. Applied Soil Ecology, 4, 213-219.

Khalil MA, Abdel-Lateif HM, Bayoumi BM, van Straalen NM and van Gestel CAM, (1996b). Effects of metals and metal mixtures on survival and cocoon production of the earthworm Aporrectodea caliginosa. Pedobiologia, 40, 548-556.

Khan DH and Frankland B (1983). Effects of cadmium and lead on radish plants with particular reference to movement of metals through soil profile and plant. Plant and Soil, 70, 335-345.

Khan DH and Frankland B (1984). Cellulolytic activity and root biomass production in some metal-contaminated soils. Environmental Pollution (Series A), 33, 63-74.

Khangarot BS and Ray PK (1989). Investigation of correlation between physicochemical properties of metals and their toxicity to the water flea Daphnia magna Straus. Ecotoxicology and Environmental Safety, 18, 109-120.

Khummongkol D, Canterford GS and Fryer C (1982). Accumulation of heavy metals in unicellular algae. Biotechnology and Bioengineering, 24, 2643-2660.

Kido T and Nogawa K.(1993). Dose-response relationship between total cadmium intake and beta-2-microglobulinuria using logistic regression analysis. Toxicol Lett, 69, 113-120.

Kido T, Honda R, Tsuritani I, Yamaya H, Ishizaki M, Yamada Y, and Nogawa K.(1988). Progress of renal dysfunction in inhabitants environmentally exposed to cadmium. Arch.Environ Health, 43, 213-217.

Kido T, Nogawa K, Honda R, Tsuritani I, Ishizaki M, Yamada Y, and Nakagawa H.(1990). The association between renal dysfunction and osteopenia in environmental cadmium-exposed subjects. Environ Res., 51, 71-82.

Kido T, Nogawa K, Honda R, Tsuritani I, Ishizaki M, Yamada Y, and Nakagawa H.(1990). The association between renal dysfunction and osteopenia in environmental cadmium-exposed subjects. Environ Res., 51, 71-82.

Kido T, Shaikh ZA, Kito H, Honda R, and Nogawa K.(11-6-1993). Dose-response relationship between total cadmium intake and metallothioneinuria using logistic regression analysis. Toxicology, 80, 207-215.

Kiene A (1999). Methodische Fragen der Bilanzierung von Ein-und Austrägen in Böden am Beispiel Cadmium. In: Pflanzenbelastung auf Kontaminierten Standorten (Plant impact at contaminated sites). Edited by UBA. Berichte 1/99. Erich Schmidt Verlag.

Kilburn KH and McKinley KL.(1996). Persistent Neurotoxicity From a Battery Fire: Is Cadmium the Culprit? South.Med.J., 89, 693-698.

Kimura M and Otaki N.(1972). Percutaneous absorption of cadmium in rabbit and hairless mouse. Ind.Health, 10, 7-10.

King E.(1955). An environmental study of casting copper-cadmium alloys. Br J Ind Med, 12, 198-205.

Kipling MD and Waterhouse JAH.(1967). Cadmium and prostatic carcinoma (Letter to the Editor). Lancet, 730-731.

Kirsch-Volders M, Aardema M, and Elhajouji A.(2000). Concepts of threshold in mutagenesis and carcinogenesis. Mutat Res, 464 , 3-11.

Kjeldsen, P. & Christensen, T.H. (2001): A simple model for the distribution and fate of organic chemicals in a landfill: MOCLA. Waste Management & Research, 19 (3), 201-216.

Kjellström T and Nordberg GF.(1978). A kinetic model of cadmium metabolism in the human being. Environ Res, 16, 248-269.

Kjellström T and Nordberg GF.(1985).Kinetic model of cadmium metabolism. In:Cadmium and Health: A toxicological and epidemiological appraisal. Edited by L Friberg, CG Elinder, T Kjellström, and GF Nordberg. CRC Press. Boca Raton, FL

Kjellström T, Borg K, and Lind B.(1978). Cadmium in feces as an estimator of daily cadmium intake in Sweden. Environ Res, 15, 242-251.

Kjellström T, Elinder CG, and Friberg L.(1984). Conceptual problems in establishing the critical concentration of cadmium in human renal cortex. Environ Res, 33, 284-295.

Kjellström T, Friberg L, and Rahnster B.(1979). Mortality and Cancer Morbidity among Cadmium-Exposed Workers. Environ Health Perspect, 28, 199-204.

Kjellström T, Lind B, Linnman L and Elinder CG (1975). Variation in cadmium concentration in Swedish wheat and barley. An indicator of changes in daily cadmium intake during the 20th century Archives of Environmental Health, 30, 321-328.

Kjellström T, Shiroishi K, and Evrin PE.(1977). Urinary -2-microglobulin excretion among people exposed to cadmium in the general environment. An epidemiologic study in cooperation between Japan and Sweden. Environ Res, 13, 318-344.

Kjellström T.(1977). Accumulation and Renal Effects of Cadmium in Man. A Dose- Response Study, Doctoral thesis.

Kjellström T.(1979). Exposure and accumulation of cadmium in populations from Japan, the United States and Sweden. Environ Health Perspect, 28, 169-197.

Kjellström T.(1992).Mechanism and epidemiology of bone effects of cadmium. In:Cadmium in the human environment: toxicity and carcinogenicity. Edited by G Nordberg, RF Herber, and L Alessio. IARC, International Agency for Research on Cancer (WHO). Lyon, 301-310.

Klaassen CD and Liu J.(1998). Metallothionein transgenic and knock-out mouse models in the study of cadmium toxicity. J Toxicol.Sci., 23 Suppl 2, 97-102.

Klass E, Rowe DW and Massaro EJ (1974). The effect of Cd on population growth of the green alga Scenedesmus quadricauda. Bulletin of Environmental Contamination and Toxicology, 12, 442-445.

Kleinfeld M, Messite J, and Giel CP.(1958). Am.J.Med.Sci., 235, 660-660.

Kleinfeld M.(1965). Acute pulmonary edema of chemical origin. Arch Environ Health, 10, 942-946.

Knowles CO and McKee M.J (1987). Protein and nucleic acid content in Daphnia magna during chronic exposure to cadmium. Ecotoxicology and Environmental Safety, 13, 290-300.

Kolakowski J, Baranski B, and Opalska B.(1983). Effect of Long-term Inhalation Exposure to Cadmium Oxide Fumes on Cardiac Muscle Ultrastructure in Rats. Toxicology Letters, 19, 273-278.

Kolonel L and Winkelstein WJ.(1977). Cadmium and prostatic carcinoma (letter). Lancet, 2, 566-567.

Kolonel L.(1976). Association of cadmium with renal cancer. CANCER, 32, 1782-1787.

Koropatnick J and Cherian MG.(1988). Exposure to different forms of cadmium in mice: differences in metallothionein and alphafetoprotein mRNA induction in liver and kidney. J Biochem Toxicol, 3, 159-172.

Korpela H, Loueniva R, Yrjanheikki E, and Kauppila A.(1986). Lead and cadmium concentrations in maternal and umbilical cord blood, amniotic fluid, placenta, and amniotic membranes. Am J Obstet Gynecol, 155, 1086-1089.

Korthals GW, van de Ende A, van Megen H, Lexmond TH, Kammenga JE and Bongers T (1996). Short-term effects of cadmium, copper, nickel and zinc on soil nematodes from different feeding and life-history strategy groups. Applied Soil Ecology, 4, 107-117.

Kosakowska A, Falkowski L and Lewandowska J (1988). Effects of amino acids on the toxicity of heavy metals to phytoplankton. Bulletin of Environmental Contamination and Toxicology, 40, 532-538.

Kossman S, Pierzchala W, Rusiecki Z, Scieszka J, Andrzejewski J, and Tomaszczyk S.(1979). Estimation of ventilation efficiency of lungs in workers of cadmium division of non-ferrous foundry. Pneumonol.Pol., 9, 627-633.

Kostial K, Blanusa M, Schonwald N, and et al.(1993). Organ cadmium deposits in orally exposed female rats and their pups and the depleting efficiency of sodium N-4-methoxybenzyl-d- glucamine-N-carbodithioate monohydrate (MeOBDCG). Appl Toxicol, 13, 203-207.

Kotsonis FN and Klaassen CD.(1977). Comparison of methods for estimating hepatic metallothionein in rats. Toxicology and Applied Pharmacology, 42, 583-588.

Kotsonis FN and Klaassen CD.(1977). Toxicity and distribution of cadmium administered to rats at sublethal doses. Toxicology and Applied Pharmacology, 41, 667-680.

Kotsonis FN and Klaassen CD.(1978). The relationship of metallothionein to the toxicity of cadmium after prolonged administration to rats. Toxicol Appl Pharmacol, 46, 39-54.

Kouzeli-Katsiri, Christoulas D. and Bosdogianny A; (1993). Leachate degradation after recirculation. Proceedings of the fourth international landfill symposium, Sardinia, Italy, October 1993, 1007-1018.

Kowal NE, Johnson DE, Kraemer DF, and Pahren HR.(1979). Normal levels of cadmium in diet, urine, blood, and tissues of inhabitants of the United States. J Toxicol Environ Health, 5, 995-1014.

Krajenbrink G. and Eggels (1997). Componentenonderzoek AVI-input. Componenten in het Nederlands huishoudelijk afval en daarmee vergelijkbaar bedrijfsafval in AVI’s. Herkomst en bestemming. TNO.

Krajncin EI, van Gestel CAM, Mulder HCM, de Vrijer FI, Sinkeldam EJ, Vink GJ, Canton JH, van Apeldoorn ME, and Janis JA.(1987). Integrated criteria document cadmium effects. 758476004,

Krasovskii GN, Varshavskaya SP, and Borisov AI.(1976). Toxic and gonadotropic effects of cadmium and boron relative to standards for these substances in drinking water. Environ Health Perspect, 13, 69-75.

Kreis IA, de Does M, Hoekstra JA, de Lezenne Coulander C, Peters PW, and Wentink GH.(1993). Effects of cadmium on reproduction, an epizootologic study. Teratology, 48, 189-196.

Krümpelbeck I. (1999). Untersuchungen zum langfristigen verhalten von siedlungsabfalldeponien. Dissertation Bergische Universität, Wuppertal.

Krzystyniak K, Fournier M, Trottier B, and et al.(1987). Immunosuppression inmice after inhalation of cadmium aerosol. Toxicol Lett, 38, 1-12.

Kühn R and Pattard M (1990). Results of the harmful effects of water pollutants to green algae (Scenedesmus subspicatus) in the cell multiplication inhibition test. Water Research, 24, 31-38.

Kühn R, Pattard M, Pernak KD and Winter A (1989). Results of the harmful effects of water pollutants to Daphnia magna in the 21 day reproduction test. Water Research, 23, 501-510.

Kuhnert BR, Kuhnert PM, and Zarlingo J.(1988). Associations Between placental Cadmium and Zinc and Age and Parity in Pregnant Women Who smoke. Journal of the American College of Obstetricians and Gynecologists, 71, 67-70.

Kuhnert BR, Kuhnert PM, Debanne S, and Williams TG.(1987). The relationship between cadmium, zinc and birth weight in pregnant women who smoke. Am J Obstet Gynecol, 157, 1247-1251.

Kuhnert PM, Kuhnert BR, Erhard P, Brashear WT, Groh-Wargo SL, and Webster MS.(1987). The effect of smoking on placental and fetal zinc status. Am J Obstet Gynecol, 157, 1241-1246.

Kumpulainen J and Tahvonen R (1989). Report of the 1989 Consultation of the European Co-operative Research Network on Trace Elements, Lausanne, Switzerland. FAO, Rome, pp. VI:1.

Kutzman RS, Drew RT, Shiotsuka RN, and et al.(1986). Pulmonary changes resulting from subchronic exposure to cadmium chloride aerosol. J Toxicol Environ Health, 17, 175-189.

La Floridienne (1997): Background information to Annex VIIA document.

LABO (1994). Hintergrund- und Referenzwerte für Böden – Entwurf. Bund-Länder-Arbeitsgemeinschaft Bodenschutz, 146 pp.

LABO (1998). Hintergrundwerte für anorganische und organische Stoffe in Bödem. 2. überarbeitete und ergänzte Auflage. Bund-Länder-Arbeitgemeinschaft Bodenschutz, Berlin, Germany, 114 pp.

Lagerkvist BI, Nordberg GF, Söderberg HA, Ekesrydh S, Englyst V, Gustavsson M, Gustavsson NO, and Wiklund DE.(1992).Placental transfer of cadmium. In:Cadmium in the Human Environment: Toxicity and Carcinogenicity. Edited by GF Nordberg, RFM Herber, and L Alessio. IARC. Lyon, 287-291.

Lahtonen R.(1985). Zinc and cadmium concentrations in whole tissue and in separated epithelium and stroma from human benign prostatic hypertrophic glands. Prostate, 6, 177-183.

Lam PKS (1996). Interpopulation differences in acute response of Brotia Hainanensis (Gastropoda, Prosobranchia) to Cd: genetic or environmental variance? Environmental Pollution, 94, 1-7.

Lamm SH, Parkinson M, Anderson M, and Taylor W.(1992). Determinants of lung Cancer Risk Among Cadmium-Exposed Workers. Ann Epidemiol, 2, 195-211.

Lamm SH.(1986). Analysis of Mortality Studies of Globe, Colorado Cadmium Workers. 120-123.

Lamm SH.(1988). Analysis of mortality studies of Globe, Colorado cadmium workers. 120-123.

Lamy P, Heully F, Pernot C, Antoine D, Couillaut S, and Thomas G.(1963). Pneumopathy caused by cadmium fumes. J.Fr.Med.Chir.Thorac., 17, 275-283.

Landner L, Folke J, Öberg MO, Mikaelsson H and Aringberg-Laanatza M (1996). Cadmium in Fertilisers. Consultants report prepared for the OECD cadmium workshop, Sweden, 16-20 October 1995 by the European Environmental Research Group Inc. on commission by The National Chemicals Inspectorate, Sweden.

Lane R and Campbell ACP.(1954). Fatal emphysema in two men making a copper cadmium alloy. Br J Ind Med, 11, 118-122.

Lankey R. (1998). Material management and recycling for Nickel-Cadmium batteries. PhD thesis, Department of Civil and Environmental Engineering, Carnegie Mellon University, 212 p.

Lansdown AB and Sampson B.(1996). Dermal toxicity and percutaneous absorption of cadmium in rats and mice. Lab Anim Sci, 46, 549-554.

Larison JR, Likens GE, Fitzpatrick JW and Crock JG (2000). Cadmium toxicity among wildlife in the Colorado Rocky Mountains. Nature, 406, 181-183.

Laskey JW and Phelps PV.(1991). Effect of cadmium and other metal cations on in vitro Leydig cell testosterone production. Toxicol Appl Pharmacol, 108, 296-306.

Laskey JW, Rehnberg GL, Favor MJ, Cahill DF, and Pietrzak-Flis Z.(1980). Chronic ingestion of cadmium and/or tritium. II. Effects on growth, development, and reproductive function. Environmental Research, 22, 466-475.

Lau JC, Joseph MG, and Cherian MG.(1998). Role of placental metallothionein in maternal to fetal transfer of cadmium in genetically altered mice. Toxicology, 127, 167-178.

Laudanski T, Sipowicz M, Modzelewski P, Bolinski J, Szamatowicz J, Razniewska G, and Akerlund M.(1991). Influence of high lead and cadmium soil content on human reproductive outcome. Int J Gynecol Obstet, 36, 309-315.

Lauwerys R (1980). Cadmium exposure, metabolism and health effects. In: Proceedings Second International Cadmium Conference cannes 6-8 February 1979, Cadmium Association (eds), Pub. Metal Bulletin, UK, pp 21-25

Lauwerys R and De Wals P.(1981). Environmental pollution by cadmium and mortality from renal diseases. Lancet, 383-383.

Lauwerys R and Hoet P.(2001).Cadmium. In:Industrial chemical exposure Guidelines for Biological Monitoring. Edited byLewis Publishers. Boca Raton Florida, 54-69.

Lauwerys R, Amery A, Bernard A, Bruaux P, Buchet JP, Claeys F, De Plaen P, Ducoffre G, Fagard R, Lijnen P, Nick L, Roels H, Rondia D, Saint-Remy A, Sartor F and Staessen J (1990). Health effects of environmental exposure to cadmium. Objectives, design and organization of the Cadmibel study: a cross sectional morbidity study carried out in Belgium from 1985-1989. Environmental Health Perspectives, 87, 283-289.

Lauwerys R, Bernard A, Buchet J-P, Roels H, Bruaux P, Claeys F, Ducoffre G, De Plaen P, Staessen J, Amery A, and et al.(1991). Does environmental exposure to cadmium represent a health risk? Conclusions from the Cadmibel study. Acta Clin Belg., 46, 219-225.

Lauwerys R, Buchet JP, Roels H, and Bernard A.(1982). [Cadmium toxicity: summary of personal studies]. Toxicol.Eur.Res., 4, 7-17.

Lauwerys R, Buchet JP, Roels H, and Hubermont G.(1978). Placental transfer of lead, mercury, cadmium, and carbon monoxide in women. I. Comparison of the frequency distributions of the biological indices in maternal and umbilical cord blood. Environ Res, 15, 278-289.

Lauwerys R, Buchet JP, Roels H, Berlin A, and Smeets J.(1975). Intercomparison program of lead, mercury, and cadmium analysis in blood, urine, and aqueous solutions. Clin.Chem., 21, 551-557.

Lauwerys R, Hardy R, Job M, Buchet JP, Roels H, Bruaux P and Rondia D (1984) Environmental pollution by cadmium and cadmium body burden: an autopsy study. Toxicology Letters, 23, 287-289.

Lauwerys R, Hardy R, Job M, Buchet JP, Roels H, Bruaux P, and Rondia D.(1984). Environmental pollution by cadmium and cadmium body burden: an autopsy study. Toxicology Letters, 23, 287-289.

Lauwerys R, Roels H, Regniers M, Buchet JP, Bernard A, and Goret A.(1979). Significance of cadmium concentration in blood and in urine in workers exposed to cadmium. Environ Res, 20, 375-391.

Lauwerys RR, Buchet JP, Roels HA, Brouwers J, and Stanescu D.(1974). Epidemiological survey of workers exposed to cadmium. Arch.Environ Health, 28, 145-148.

Lauwerys RR, Roels HA, Buchet JP, Bernard A, and Stanescu D.(1979). Investigations on the lung and kidney function in workers exposed to cadmium. Environ Health Perspect, 28, 137-145.

LAWA database (1998). Joint Water Commission of the Federal Länder (LAWA), Federal Institute of Hydrology, Berlin.

Lawrence SG, Holoka MH and Hamilton RD (1989). Effects of cadmium on a microbial food chain, Chlamydomonas reinhardii and Tetrahymena vorax. Science of the Total Environment, 87/88, 381-395.

Lawrence, S.G. and Holoka, M.H. (1991). Response of crustacean zooplankton impounded in situ to cadmium at low environmental concentrations. Verh. Internat. Verein. Limmol., 24, 2254-2259.

Lazarus JM and Brenner BM.(1998).Chronic Renal Failure. In:Harrison's Principles of Internal Medicine. Edited by JD Wilson, E Braunwald, KJ Isselbacher, RG Petersdorf, JB Martin, AS Fauci, and RK Root. McGraw-Hill,Inc. 1513-1514.

Lazebnik N, Kuhnert BR, and Kihnert PM.(1989). Zinc, cadmium, and hypertension in parturient women. Am J Obstet Gynecol, 161 , 437-440.

Leach RM, Wang KWL and Baker DE (1978). Cadmium and the food chain: the effect of dietary cadmium on tissue composition in chicks and laying hens. Journal of Nutrition,109, 437-443.

Leber AP and Miya TS.(1976). A mechanism for cadmium and zinc-induced tolerance to cadmium toxicity: involvement of metallothionein. Toxicology and Applied Pharmacology, 37, 403-414.

Leduc D, de Francquen P, Jacobovitz D, Vandeweyer R, Lauwerys R, and De Vuyst P.(1993). Association of cadmium exposure with rapidly progressive emphysema in a smoker. Thorax, 48, 570-571.

Lee B-G, Griscom SB, Lee J-S, Choi HJ, Koh C-H, Luoma SN and Fisher NS (2000). Influences of dietary uptake and reactive sulfides on metal bioavailability from aquatic sediments. Science, 287, 282-284.

Lee SZ, Allen HE, Huang CP, Sparks DL, Sanders PF and Peijnenburg WJGM (1996). Predicting soil-water partition coefficients for cadmium. Environmental Science and Technology, 30, 3418-3424.

Lee, S.Z., Allen H.E., Huang, C.P., Sparks, D.L., Sanders, P.F. and Peijnenburg, W.J.G.M. (1996). Predicting soil-water partition coefficients for cadmium. Environmental Science and Technology, 30:3418-3424.

Leffler PE and Nyholm NE (1996). Nephrotoxic effects in free living bank voles in a heavy metal polluted environment. Ambio, 25,417-420.

Legge TM.(1924). Ann.Rept.Chief Inspect.Factories for 1923, 74-74.

Lehman LD and Klaassen CD.(1986). Dosage-dependent disposition of cadmium administered orally to rats. Toxicol Appl Pharmacol, 84, 159-167.

Lehman LD and Poisner AM.(1984). Induction of Metallothionein Synthesis in Cultured Human Trophoblasts by Cadmium and Zinc. J Toxicol Environ Health, 14, 419-432.

Leinweber P (1996). Schwermetallgehalte und Schwermetallbindungsvermögen der Böden im agrarischen Intensivgebiet Südoldenburg. ISPA – Vechta: Vechtaer Druckerei und Verlag, Vechta.

Lemann M., Walder R. and Schwyn A.(1995). Heavy metals in municipal solid waste residues. Journal of Power Sources 57, 55-59.

Lemen R, Lee JS, Wagoner JK, and Blejer HP.(1976). Cancer Mortality among Cadmium Production Workers. Ann.N.Y.Acad.Sci., 271 , 273-279.

L'Epée P, Lazarini H, Franchome J, N'Doky T, and Larrivet C.(1968). Contribution to the study on cadmium intoxication. Arch.Mal.Prof.Med.Trav.Secur.Soc., 28, 137-145.

Levine RJ, Symons MJ, Balogh SA, and et al.(1980). A method for monitoring fertility of workers. I. Method and pilot studies. J Occup Med, 22, 781-791-

Levis S and Altman R.(1998). Bone densitometry: clinical considerations. Arthritis Rheum, 41, 577-587.

Levy LS and Clack J.(1975). Further studies on the effect of cadmium on the prostate gland.I. Absence of prostatic changes in rats given oral cadmium sulfate for two years. Ann.Occup Hyg., 17, 205-211.

Levy LS, Clack J, and Roe FJ.(1975). Further studies on the effect of cadmium on the prostate gland. II. Absence of prostatic changes in mice given oral cadmium sulfate for eighteen months. Ann Occup Hyg, 17, 213-220.

Lewis GP, Coughlin LL, Jusko WJ, and Hartz S.(1972). Contribution of cigarette smoking to cadmium accumulation in man. Lancet, 1, 291-292.

Lewis GP, Jusko WJ, and Coughlin LL.(1972). Cadmium accumulation in man: influence of smoking, occupation, alcoholic habit and disease. J Chronic Dis, 25, 717-726.

Lewis PA and Horning II WB (1991). Differences in acute toxicity test results of three reference toxicants on Daphnia at two temperatures. Environmental Toxicology and Chemistry, 10, 1351-1357.

Lexicon der non-ferrrometalen (1997). Uitgegeven door de sector “non-ferrometalen” van de Société Générale de Belgique. Union Minière (SWB). Standaard Uitgeverij. Antwerpen, Utrecht, 223 p.

Lexmond TM, Edelman T and Van Driel W (1986). Voorlopige referentiewaarden en huidige achtergrondgehalten voor een aantal zware metalen en arseen in de bovengrond van natuurterreinen en landbouwgronden. In: Advies Bodemkwaliteit. VTCB A86/02, Ministerie van Volkshuisvesting, Ruimtelijke Ordening en Milieubeheer, Leidschendam.

Li JP, Akiba T, and Marumo F.(1997). Long-term, low-dose, cadmium-induced nephropathy with renal osteopathy in ovariectomized rats. J Toxicol Sci, 22, 185-198.

Liang CN and Tabatabai MA (1978). Effects of trace metals on nitrification in soils. Journal of Environmental Quality,7, 291-293.

Lin FJ, Fitzpatrick JW, Iannotti CA, Martin DS, Mariani BD, and Tuan RS.(1997). Effects of cadmium on trophoblast calcium transport. Placenta, 18, 341-356.

Lin K-C, Lin C-I and Chen, C-Y (1996). The effect of limiting nutrient on metal toxicity to Selenastrum capricornutum. Toxicological and Environmental. Chemistry, 56,47-61.

Lind Y, Wicklund-Glynn A, Engman J, and Jorhem L.(1995). Bioavailability of cadmium from crab hepatopancreas and mushroom in relation to inorganic cadmium: a 9-week feeding study in mice. Food Chem Toxicol, 33, 667-673.

Lipor II (2002) Internal report. Calheiros JM. and Almeida A., pers. com., 2002.

LISEC (1998a). Alga, growth inhibition test effect of cadmium on the growth of Selenastrum capricornutum. Draft report, 22pp.

LISEC (1998b). Alga, growth inhibition test effect of cadmium oxide on the growth of Selenastrum capricornutum. Draft report, 22pp.

LISEC (1998c). Activated sludge: respiration inhibition test. Effects of cadmium powder. Draft report, 25pp.

LISEC (1998d). Activated sludge: respiration inhibition test. Effects of cadmium oxide powder. Draft report, 25pp.

LISEC, (1998e). Transformation dissolution of metals and sparingly soluble metal compounds in aqueous media. “cadmium powder”. Draft report, LISEC n(WE-14-002.

LISEC, (1998f). Transformation dissolution of metals and sparingly soluble metal compounds in aqueous media “cadmium oxide powder”. Draft report, LISEC n(WE-14-003.

LISEC, (2001). Transformation dissolution of metals and sparingly soluble metal compounds in aqueous media. “massive cadmium”. Draft report, LISEC n(WE- - .

Litchfield TM, Ishikawa Y, Wu LNY, Wuthier RE, and Sauer GR.(1998). Effect of metal ions on calcifying growth plate cartilage chondrocytes. Calcif.Tissue Int, 62, 341-349.

Lithner G, Holm K and Borg H (1995). Bioconcentration factors for metals in humic acid waters at different pH in the Rönnskär area (N. Sweden). Water, Air and Soil Pollution, 85, 785-790.

Liu J and Klaassen CD.(1996). Absorption and distribution of cadmium in metallothionein-I transgenic mice. Fundam.and Applied Toxicol, 29, 294-300.

Liu J, Liu Y, Habeebu SS, and Klaassen CD.(1-9-1999). Metallothionein-null mice are highly susceptible to the hematotoxic and immunotoxic effects of chronic CdCl2 exposure. Toxicology and Applied Pharmacology, 159, 98-108.

Liu J, Liu Y, Habeebu SS, and Klaassen CD.(1998). Susceptibility of MT-null mice to chronic CdCl2-induced nephrotoxicity indicates that renal injury is not mediated by the CdMT complex. Toxicol Sci, 46, 197-203.

Liu J, Liu Y, Michalska AE, Choo KH, and Klaassen CD.(1996). Distribution and retention of cadmium in metallothionein I and II null mice. Toxicology and Applied Pharmacology, 136, 260-268.

Liu Y, Liu J, Habeebu SM, Waalkes MP, and Klaassen CD.(2000). Metallothionein-I/II Null Mice Are Sensitive to Chronic Oral Cadmium-Induced Nephrotoxicity. Toxicol Sci, 57, 167-176.

Liu Y, Liu J, Habeebu SS, and Klaassen CD.(1999). Metallothionein protects against the nephrotoxicity produced by chronic CdMT exposure. Toxicol.Sci., 50, 221-227.

Liu YZ, Huang JX, Luo CM, Xu BH, and Zhang CJ.(1985). Effects of cadmium on cadmium smelter workers. Scand J Work Environ Health, 11, 29-32.

Livingstone HD.(1972). Measurement and distribution of zinc, cadmium, and mercury in human kidney tissues. Clin.Chem., 18, 67-72.

Loeser E and Lorke D.(1977). Semichronic oral toxicity of cadmium.II.Studies on dogs. Toxicology, 7, 225-232.

Loeser E and Lorke D.(1977). Semichronic oral toxicity of cadmium. I.Studies on rats. Toxicology, 7, 215-224.

Loiacono NJ, Graziano JH, Kline JK, Popovac D, Ahmedi X, Gashi E, Mehmeti A, and Rajovic B.(1992). Placental Cadmium and Birthweight in Women Living Near a Lead Smelter. Arch Environ Health, 47, 250-255.

Long E, MacDonald D, Cubbage J and Ingersoll C (1998). Predicting the toxicity of sediment associated trace metals: acid-volatile sulfide concentrations and dry weight normalized concentrations of critical comparison. Environmental Toxicology and Chemistry, 17, 972-974.

Long GJ.(28-4-1997). Cadmium perturbs calcium homeostasis in rat osteosarcoma (ROS 17/2.8) cells; a possible role for protein kinase C. Toxicol Lett., 91, 91-97.

LÓPEZ ARIAS, M. & GRAU CORBÍ, J.M. (2004). Metales pesados, materia orgánica y otros parameters de la capa superficial de los suelos agrícolas y de pastos de la España Peninsular. (Heavy metals concentrations, organic matter contents and other parameters in agricultural and grassland Spanish soils). No further details.

Lorenz H, Ocker HD, Brüggemann J, Weigert P and Sonneborn M (1986). Cadmiumgehalte in Getreideproben der Vergangenheit-Vergleich zur Gegenwart. Zeitschrift für Lebensmitteluntersuchung und Forschung, 183, 402-405.

Löser E (1980). A 2 year oral carcinogenicity study with cadmium on rats. Cancer Letters, 9, 191-198.

Löser E.(1980). A 2 year oral carcinogenicity study with cadmium on rats. Cancer Lett., 9, 191-198.

Louekari K, Jolkkonen L and Varo P (1987). Exposure to cadmium from foods, estimated by analysis and calculation-comparison of the methods. Food additives and contaminants, 5, 111-117.

Louekari K, Uusitalo U and Pietinen P (1989). Variation and modifying factors of the exposure to lead and cadmium based on an epidemiological study. The Science of the Total Environment, 84, 1-12.

Louekari K, Valkonen S, Pousi S, and Virtanen L.(1991). Estimated dietary intake of lead and cadmium and their concentration in blood. Sci Total Environ, 105, 87-99.

Lowe-Jinde L and Niimi AJ (1984). Short-term and long-term effects of Cd on glycogen reserves and liver size in rainbow trout (Salmo gairdneri Richardson). Archives of Environmental Contamination and Toxicology, 13, 759-764.

Lucas PA, Jariwalla AG, Jones IH, Gough J, and Vale PT.(1980). Fatal Cadmium Fume Inhalation. Lancet, 2, 205-205.

Lucis OJ, Lucis R, and Shaikh ZA.(1972). Cadmium and Zinc in Pregnancy and Lactation. Arch Environ Health, 25, 14-22.

Lutz E, Lind B, Herin P, Krakau I, Bui T-H, and Vahter M.(1996). Concentrations of mercury, cadmium and lead in brain and kidney of second trimester fetuses and infants. J.Trace Elements Med.Biol., 10, 61-67.

Lux W, Hintze B and Piening H (1998). Heavy metals in the soils of Hamburg. In: Contaminated Soil Edited by K Wolf, WJ van den Brink, FJ Colon. Kluwer Academic Publishers, 88, 265-267.

Lyon TD, Aughey E, Scott R, and Fell GS.(1999). Cadmium concentrations in human kidney in the UK: 1978-1993. J Environ Monit., 1, 227-231.

Ma WC (1982). The influence of soil properties and worm-related factors on the concentration of heavy metals in earthworms. Pedobiologia, 24, 109-119.

Ma W-C (1987). Heavy-metal accumulation in the mole, Talpa-europea, and earthworms as an indicator of metal bioavailability in terrestrial environments. Bulletin of Environmental Contamination and Toxicology, 39, 933-938.

Ma W-C and Broekhuizen S (1989). Belasting van dassen, Meles meles met zware metalen: invloed van de verontreinigde uiterwaarden? Lutra, 32, 139-149.

Ma W-C and van der Voet H (1993). A risk-assessment model for toxic exposure of small mammalian carnivores to cadmium in contaminated natural environments. The Science of the Total Environment, Supplement 1993, 1701-1714.

Ma W-C, Denneman W and Faber J (1991). Hazardous exposure of ground-living small Mammals to cadmium and lead in contaminated terrestrial ecosystems. Archives of Environmental Contamination and Toxicology, 20, 266-270.

MacGregor JT, Wehr CM, Henika PR, and Shelby MD.(1990). The in vivo erythrocyte micronucleus tes: Mesaurement at steady state increases assay efficiency and permits integration with toxicity studies. Fundam.and Applied Toxicol, 14, 513-522.

MacGregor JT, Wehr CM, Henika PR, and Shelby MD.(1990). The in vivo erythrocyte micronucleus tes: Mesaurement at steady state increases assay efficiency and permits integration with toxicity studies. Fundam.and Applied Toxicol, 14, 513-522.

Machemer L and Lorke D.(1981). Embrytoxic effect of cadmium on rats upon oral administration. Toxicol Appl Pharmacol, 58, 438-443.

Madle S, von der Hude W, Broschinski L, and Janig G.(2000). Threshold effects in genetic toxicity: perspective of chemicals regulation in Germany. Mutat Res, 464, 117-121.

MAFF (1997). Food surveillance information sheet N°131. Ministry of Agriculture, Food and Fisheries, UK.

Mahler RJ, Bingham FT and Page AL (1978). Cadmium-enriched sewage sludge application to acid and calcereous soils: Effect on yield and cadmium uptake by Lettuce and Chard. Journal of Environmental Quality, 7, 274-281.

Mai S and Alsen-Hinrichs C.(1997). Wie sieht die derzeitige alters-und geschlechtabhängige Kadmiumanreicherung in der menschlichen Nierenrinde aus? Gesundheitswesen, 89, 332-337.

Maitani T, Waalkes MP, and Klaassen CD.(1984). Distribution of cadmium after oral administration of cadmium- thionein to mice. Toxicol Appl Pharmacol, 74, 237-243.

Malley DF and Chang PSS (1991). Early observations on the zooplankton community of a Precambrian Shield lake receiving experimental additions of cadmium. Verh. Internat. Verein. Limmol., 24, 2248-2253.

Malmrose LC, Gray SL, Pieper CF, Blazer DG, Rowe JW, Seeman TE, and Albert MS.(1993). Measured versus estimated creatinine clearance in a high- functioning elderly sample: MacArthur Foundation Study of Succesful Aging. J Am Geriatric Soc, 41, 715-721.

Mancioli G.(1940). Rass.Med.industr., 11, 632-632.

Mandel R and Ryser HJP.(1984). Mutagenicity of cadmium in salmonella typhimurium and its synergism with two nitrosamines. Mutat Res, 138, 9-16.

Manthey J, Stoeppler M, Morgenstern W, Nussel E, Opherk D, Weintraut A, Wesch H, and Kubler W.(1981). Magnesium and trace metals: risk factors for coronary heart disease. Circulation, 64, 722-729.

Marlowe M, Cossairt A, Moon C, Errera J, MacNeel A, Peak R, Ray J, and Schroeder C.(1985). Main and interaction effects of metallic toxins on classroom behavior. J.Abnorm.Child Psychol., 13, 185-198.

Marshall JS (1978). Population dynamics of Daphnia galeata mendotae as modified by chronic Cd stress. Journal of the Fisheries Research Board of Canada, 35: 461-469.

Marshall JS and Mellinger DL (1980). Dynamics of cadmium-stressed plankton communities. Canadian Journal of Fisheries and Aquatic Sciences, 37, 403-414.

Masaoka T, Akahori F, Arai S, and et al.(1994). A nine-year chronic toxicity study of cadmium ingestion in monkeys.I.Effects of dietary cadmium on the general health of monkeys. Vet Hum Toxicol, 36, 189-194.

Masaoka T, Akahori F, Arai S, Nomiyama K, Nomiyama H, Kobayashi K, Nomura Y and Suzuki T (1994). A 9-year chronic toxicity study of cadmium ingestion in monkeys.1. Effects of dietary-cadmium on the general health of monkeys. Veterinary and Human Toxicology, 36, 189-194.

Mason HJ, Davison AG, Wright AL, Guthrie CJ, Fayers PM, Venables KM, Smith NJ, Chettle DR, Franklin DM, and Scott MC.(1988). Relations between liver cadmium, cumulative exposure, and renal function in cadmium alloy workers. Br J Ind Med, 45, 793-802.

Mason HJ, Williams FM, Armitage S, Morgan M, Green S, Perrin B, and Morgan WD.(1999). Follow up of workers previously exposed to silver solder containing cadmium. Occup Env Med, 56, 553-558.

Mason HJ.(1990). Occupational cadmium exposure and testicular endocrine function. Hum Exp Toxicol, 9, 91-94.

Massey LK and Whiting SJ.(1996). Dietary salt, urinary calcium, and bone loss (see comments). J Bone Miner Res, 11, 731-736.

Materne D, Lauwerys R, Buchet J-P, Roels H, Brouwers J, and Stanescu D.(1975). Investigations sur les risques résultant de l'exposition au cadmium dans deux entreprises de production et d'utilisation du cadmium. Cah Med Trav, 12, 1-76.

Matsusaka N, Tanaka M, Nishimura Y, Yujama A, and Kobayashi H.(1972). Whole body retention and intestinal absorption of 115mCd in young and adult mice (in Japanese). Med Biol, 85, 275-279.

Mayer LM, Chen Z, Findlay RH, Fang J, Sampson S, Self RFL, Jumars PA, Quetel C and Donard OFX (1996). Bioavailability of sedimentary contaminants subject to deposit-feeder digestion. Environmental Science and Technology, 30, 2641-2645.

Maystre L.Y, Duflon V., Diserens T., Leroy D., Simos J. and Viret F.(1994). Déchets Urbains. Nature et caractérisation.Presses Polytechniques et Universitaires Romandes. CH-1015 Lausanne., p. 167-193, ISBN 2-88074-256-0

Mc Bride et al. (1997). Reference currently missing

Mc Mellin G. (2002) Personal communication 02-07-2002, Environment Agency.

McBridge M, Sauvé S and Hendershot W (1997). Solubility control of Cu, Zn, Cd and Pb in contaminated soils. European Journal of Soil Science, 48, 337-346

McCarty LS, Henry JAC and Houston AH (1978). Toxicity of Cd to goldfish, Carassius auratus, in hard and soft water. Journal of the Fisheries Research Board of Canada, 35, 35-42.

McFarland HN.(1979).Pulmonary effects of cadmium. In:Cadmium Toxicity. Edited by JC Mennear. Marcel Dekker Inc. New York Basel, 113-132.

McGrath SP and Loveland PJ (1992). The Soil Geochemical atlas of England and Wales. Blackie Academic and Professional. Glasgow, 101 pp.

McGrath SP, Chaudri AM and Giller KE (1995). Long-term effects of metals in sewage sludge on soils, microorganisms and plants. Journal of Industrial Microbiology, 14, 94-104.

McKenna IM and Chaney RL.(1995). Characterisation of a cadmium-zinc complex in lettuce leaves. Biol Trace Elem Res, 48, 13-29.

McKenna IM, Chaney RL, Tao SH, Leach RMJ, and Williams FM.(1992). Interactions of plant zinc and plant species on the bioavailablity of plant cadmium to Japanese quail fed lettuce and spinach. Environ Res, 57, 73-87.

McKenna IM, Waalkes MP, Chen LC, and Gordon T.(1997). Comparison of inflammatory lung responses in Wistar rats and C57 and DBA mice following acute exposure to cadmium oxide fumes. Toxicology and Applied Pharmacology, 146, 196-206.

McKenzie J, Kjellström T, and Sharma R.(1982). Cadmium intake, metabolism and effects in people with a high intake of oysters in New Zealand.

McKenzie-Parnell JM, Kjellstrom TE, Sharma RP and Robinson MF (1988). Unusually high intake and fecal output of cadmium, and fecal output of other trace elements in New Zealand adults consuming dredge oysters. Environmental Research, 46, 1-14.

McLaughlin MJ, Maier NA, Freeman K, Tiller KG, Williams CMJ and Smart MK (1995). Effect of potassic and phosphatic fertiliser Cd content and additions of zinc on cadmium uptake by commercial potato crops. Fertiliser Research, 40, 63-70.

McLaughlin MJ, Tiller KG, Naidu R and Stevens DP (1996). Review: the behaviour and environmental impact of contaminants in fertilisers. Australian Journal of Soil Research, 34, 1-54.

McLellan JS, Thomas BJ, Fremlin JH, and Harvey TC.(1975). Cadmium : its in vivo detection in man. Phys.Med.Biol., 20, 88-95.

Melchiorri C, Grella A, Bonacci S and Di Caro A (1989). Il cadmio nelle diete totali di tipiche collettivati Italiane. Annali di Igiene Medicina Preventiva e di Communità. I, 841-849.

Mench M, Baize D and Mocquot B (1997). Cadmium availability to wheat in five soil series from the Yonne district, Burgundy, France. Environmental Pollution, 95, 93-103.

Mench M, Tancogne J, Gomez A and Juste C (1989). Cadmium bioavailability to Nicotiana tabacum L., Nicotiana rustica L., and Zea mays L. grown in soil amended or not amended with cadmium nitrate. Biology and Fertility of Soils, 8, 48-53.

Mench MJ (1998). Cadmium availability to plants in relation to major long-term changes in agronomy systems. Agriculture, Ecosystems and Environment, 67, 175-187.

Meplan C, Mann K, and Hainaut P.(29-10-1999). Cadmium induces conformational modifications of wild-type p53 and suppresses p53 response to DNA damage in cultured cells. J Biol.Chem., 274, 31663-31670.

Merrington G, Miller D, McLaughlin MJ and Keller MA (2001). Trophic barriers to fertilizer Cd bioaccumulation through the food chain: a case study using a plant-insect predator pathway. Archives of Environmental Contamination and Toxicology. In press.

Mersiowsky I. (2001). Long-term behaviour of PVC products and their additives under landfill conditions. Report TUHH Technology GmbH.

Mersiowsky I., 2001. Contribution of post-consumer PVC products to lead inventory in landfilled waste. Substance Flow Analysis report commissioned by the European Council of Vinyl Manufacturers (ECVM) and the European Stabilisers Producers Association (ESPA). Report TUHH Technology GmbH.

Michalska AE and Choo KH.(1-9-1993). Targeting and germ-line transmission of a null mutation at the metallothionein I and II loci in mouse. Proc.Natl.Acad.Sci.U.S.A, 90, 8088-8092.

Miles LJ and Parker GR (1979). The effect of soil-added cadmium on several plant species. Journal of Environmental Quality, 8, 229-232.

Milieucompendium (2001). Het Milieu in cijfers. Klein, P., Lagas, P., Slokker, A.D., Wit, AkH (eds). Kluwer, The Netherlands.

Miljostyrelsen (2000). Massestromsanalyse for cadmium (by COWI), Miljoprojekt n° 557, Kobenhavn.

Miller GJ, Wyllie MJ, and McKeown D.(1976). Cadmium exposure and renal accumulation in an Australian urban population. Med.J.Austr., 1, 20-23.

Miller JE, Hassett JJ and Koeppe DE (1976). Uptake of cadmium as influenced by soil cation exchange capacity, pH and available phosphorus. Journal of Environmental Quality, 5, 157-160.

Miller JE, Hassett JJ and Koeppe DE (1977). Interactions of lead and cadmium on metal uptake and growth of corn plants. Journal of Environmental Quality, 6, 18-26.

Miller ML, Murthy L, and Sorenson JR.(1974). Fine structure of connective tissue after ingestion of cadmium: Observations on interstitium on male rat lung. Arch.Pathol., 98, 386-392.

Min KS, Nakatsubo T, Kawamura S, Fujita Y, Onosaka S, and Tanaka K.(1992). Effects of mucosal metallothionein in small intestine on tissue distribution of cadmium after oral administration of cadmium compounds. Toxicol Appl Pharmacol, 113, 306-310.

Ministerio de medio ambiente (2005). Monitoring data for surface water in Spain. Unpublished documents. Received 11.05.2005 via post mail (pers. com. Dr. A. Fresno).

Minoia C, Sabbioni E, Apostoli P, Pietra R, Pozzoli L, Gallorini M, Nicolaou G, Alessio L, and Capodaglio E.(1990). Trace element reference values in tissues from inhabitants of the European community.1.A study of 46 elements in urine, blood and serum of Italian subjects. Sci Total Environ, 95, 89-105.

Miyahara T, Takata M, Miyata M, Nagai M, Sugure A, Kozuka H, and Kuze S.(1991). Cadmium stimulates osteoclast-like multinucleated cell formation in mouse bone marrow cell cultures. Bull.Environ Contam Toxicol, 47, 283-287.

Miyahara T, Takata M, Mori-Uchi S, Miyata M, Nagai M, Sugure A, Matsusista M, Kozuka H, and Kuze S.(1992). Stimulative effects of cadmium on bone resorption in neonatal parietal bone resorption. Toxicology, 73, 93-99.

Miyahara T, Yamada H, Takeuchi M, Kozuka H, Kato T, and Sudo H.(1988). Inhibitory effects of cadmium on in vitro calcification of a clonal osteogenic cell, MC3T3-E1. Toxicol Appl Pharmacol, 96, 52-59.

MMA (2002). Inventario Nacional de Contaminantes Atmosféricos. Ministreio de Medio Ambiente.

Monzawa K, Kido T, Yamaya H, Kobayashi E, and Nogawa K.(1998). Urinary excretion levels of sodium and potassium in environmental cadmium-exposed subjects. Toxicology, 127, 187-193.

Moolenaar SW and Lexmond TM (1998). Heavy-metal balances of agro-ecosytems in The Netherlands. Netherlands Journal of Agricultural Science, 46, 171-192.

Moreau T, Lellouch J, Juguet B, Festy B, Orssaud G, and Claude JR.(1983). Blood cadmium levels in a general male population with special reference to smoking. Arch Environ Health, 38, 163-167.

Morf L.S., Brunner P.H. and Spaun S. (2000). Effect of operating conditions and input variations on the partioning of metals in a municipal solid waste incinerator. Waste Managemnt Research, 18, 4-15.

Morgan H and Simms DL.(15-8-1988). The Shipham report. An investigation into cadmium contamination and its implications for human health. Discussion and conclusions. Sci Total Environ, 75, 135-143.

Morgan JE and Morgan AJ (1988). Earthworms as biological monitors of Cd, Cu, Pb and Zn in metalliferous soils. Environmental Pollution, 54, 123-138.

Morgan JM, Burch HB, and Watkin JB.(1971). Tissue cadmium and zinc content in emphysema and bronchogenic carcinoma. J Chron Dis, 24, 107-110.

Morgan JM.(1969). Tissue cadmium concentrations in man. Arch Int Med, 123, 405-408.

Morgan JM.(1970). Cadmium and Zinc Abnormalities in Bronchogenic Carcinoma. CANCER, 25, 1394-1398.

Morrow H (1998). Cadmium. The issues and answers. Brussels, Great Falls: ICdA.

Morrow H. and Keating J. (1997) Overview paper on effective recycling of Ni-Cd batteries. In: Proceedings of the OECD workshop on the effective collection and recycling of Nickel-Cadmium batteries, Lyon,-France 23-25 september 1997, p. 23-34., Series on Risk Management N°8.

Morrow, H. (2001). Cadmium and Cadmium Alloys. In: Kirk-Othmer Encyclopedia of Chemical Technology. Online edition. Article Online posting Date: June 4, 2001). John Wiley & Sons, Inc. http://www.mrw.interscience.wiley.com

Morrow, H. Cadmium. The issues and answers.Anonymous Brussels,Great Falls:ICdA., 1998.

MSDS (1992). US Defense Logistics Agency. Occup. Health Services Inc.

MSDS (1995). Cadmium metal. PC Wiaux S.A. 5p.

Müller KW and Payer HD (1979). The influence of pH on the cadmium-repressed growth of the alga Coelastrum proboscideum. Physiologia Plantarum, 45, 415-418.

Müller M, Anke M, Thiel C and Hartmann E (1993). Zur Cadmiumaufnahme Erwachsener in den neuen Bundesländern. Ernährungs-Umschau, 40,240-243.

MUMM (2001): Reactualisation des dossiers relatifs a l'emission de substances prioritaires en Belgique. Cadmium. Rapport Final. Mai 2001.

Munger C and Hare L (1997). Relative importance of water and food as cadmium sources to an aquatic insect (Chaoborus punctipennis): implications for predicting Cd bioaccumulation in nature. Environmental Science and Technology, 31, 891-895.

Muramoto S (1981). Vertebral column damage and decrease of calcium concentration in fish exposed experimentally to cadmium. Environmental Pollution, 24, 125-133.

Muramoto S, Nishizaki H and Aoyama I (1991). The effect of several cadmium compounds in soil on the metal content of unpolished rice. Ber. Ohara Inst. landw. Biol., Okayama Univ., 20, 1-9.

Murphy BR, Atchison JG, McIntosh AW and Kolar DJ (1978). Cadmium and zinc content of fish from an industrially contaminated lake. Journal of Fish Biology, 13, 327-335.

Murthy RC, Migally N, Doye A, and Zambernard J.(1982). Ultrastructural Changes in Rat Alveolar Macrophages Exposed to Oxides of Copper and Cadmium. J.Submicrosc.Cytol., 14, 347-353.

Nagymagtenyi L, Schulz H, and Desi I.(1997). Behavioural and functional neurotoxicological changes caused by cadmium in a three-generational study in rats. Hum Exp Toxicol, 16, 691-699.

Nakagawa H, Nishijo M, Morikawa Y, Tabata M, Senma M, Kitagawa Y, Kawano S, Ishizaki M, Sugita N, Nishi M, Kido T, and Nogawa K.(1993). Urinary beta 2-Microglobulin Concentration and Mortality in a Cadmium-Polluted Area. Archives of Environmental Health, 48, 428-435.

Nakagawa H, Tabata M, Morikawa Y, Kitagawa Y, Senma M, Kanamori C, and Kawano S.(1990). [A study on the survival rates for patients and suspected patients with Itai-itai disease]. Nippon.Eiseigaku.Zasshi., 44, 1059-1064.

Nakhone LN and Young SD (1993). The significance of (radio-) labile cadmium pools in soil. Environmental Pollution, 82, 73-77.

Nasatir AV.(1941). Month.Pub.Div.Ind.Hyg., Natl.Inst.Health, 1, 7-7.

Nash JT , Day WC and Wilson AB (2001). Geochemical data for historic mining areas, central western slope, Colorado. U.S. Department of the Interior, U.S. Geological Survey, Open-File Report 01-003, 13p.

Nasu Y and Kugimoto M (1981). Lemna (Duckweed) as an indicator of water pollution. I. The sensitivity of Lemna paucicostata to heavy metals. Archives of Environmental Contamination and Toxicology, 10, 159-169.

National Toxicology Program.(2001). 9th Report on Carcinogens. U.S.Department of Health and Human ServicesPublic Health Service,

Nebeker AV, Cairns MA, Onjukka ST and Titus RH (1986a). Effect of age on sensitivity of Daphnia magna to cadmium, copper and cyanazine. Environmental Toxicology and Chemistry, 5, 527-530.

Nebeker AV, Onjukka ST, Cairns MA and Krawczyk DF (1986b). Survival of Daphnia magna and Hyalella azteca in Cd-spiked water and sediment. Environmental Toxicology and Chemistry, 5, 933-938.

Neuhauser EF, Loehr RC, Milligan DL and Malecki MR (1985). Toxicity of metals to the eartworm Eisenia fetida. Biology and Fertility of Soils, 1, 149-152.

Newton D, Johnson P, Lally AE, Pentreath RJ and Swift DJ (1984). The uptake by man of cadmium ingested in crab meat. Human Toxicology, 3, 23-28.

Newton D, Johnson P, Lally AE, Pentreath RJ, and Swift DJ.(1984). The uptake by man of cadmium ingested in crab meat. Hum.Toxicol., 3, 23-28.

Nicaud P, Lafitte A, and Gros A.(1942). Symptoms of chronic cadmium intoxication. Arch.Mal.Prof.Med.Trav.Secur.Soc., 4, 192-202.

Nicholson FA, Jones KC and Johnston AE (1994). Effect of phosphate fertilisers and atmospheric deposition on long-term changes in the cadmium content of soils and crops. Environmental Science and Technology, 28, 2170-2175.

Nicholson FA, Jones KC and Johnston AE (1996). Evidence for the leaching of surface deposited Cd in the agricultural soils. In: Fertilisers as a source of Cd, Organisation for Economic Cooperation and Development, Paris, France.

Nicholson JK, Kendall MD and Osborn D (1983). Cadmium and mercury nephrotoxicity. Nature, 304, 633-635.

Niederlehner BR, Pratt JR, Buikema AL and Cairns J (1985). Laboratory Tests Evaluating the Effects of Cadmium on Fresh- Water Protozoan Communities. Environmental Toxicology and Chemistry, 4, 155-165.

Nielsen P.H. and Hausschild M. (1998). Product specific emissions from Municipal Solid Waste Landfills. Part 1 : landfill model. int. J. LCA, 3 (3), 158-168.

Nielsen P.H., Exner S., Jorgensen, A.M and Hauschild M.(1998) Product specific emissions from Municipal Solid Waste Landfills. Part 2: Presentation and verification of the computer tool LCA-LAND. int. J. LCA, 3 (4), 225-236.

Nilsson (1993). Optimizing biogas by controlled deposition of solid waste. ISWA yearbook 1993/94 International directory of solid waste management.

Nilsson U, Schutz A, Bensryd I, Nilsson A, Skerfving S, and Mattsson S.(2000). Cadmium levels in kidney cortex in Swedish farmers. Environmental Research, 82, 53-59.

Nilsson U, Schütz A, Skerfving S, and Mattsson S.(1995). Cadmium in kidneys in Sweden measured in vivo using X-ray fluorescence analysis. Int.Arch.Occup.Environ.Health, 67, 405-411.

Nishijo M, Nakagawa H, and Tabata M.(1995). Environmental exposure level and blood and urinary cadmium concentrations. Environmental Sciences, 3, 125-135.

Nishijo M, Nakagawa H, and Tabata M.(1995). Environmental exposure level and blood and urinary cadmium concentrations. Environmental Sciences, 3, 125-135.

Nishijo M, Nakagawa H, Morikawa M, Tabata M, Miura T, Yoshita K, Higashiguchi K, Seto T, Kido T, Nogawa K, Mizukoshi K, and Nishi M.(5-9-1999). Relationship between urinary cadmium and mortality among inhabitants living in a cadmium polluted area in Japan. Toxicol Lett, 108, 321-327.

Nishijo M, Nakagawa H, Morikawa Y, Tabata M, Senma M, Kitagawa Y, Kawano S, Ishizaki M, Sugita N, Nishi M, Kido T, and Nogawa K.(1994). Prognostic Factors of Renal Dysfunction Induced by Environmental Cadmium Pollution. Environmental Research, 64, 112-121.

Nishijo M, Nakagawa H, Morikawa Y, Tabata M, Senma M, Miura K, Takahara H, Kawano S, Nishi M, Mizukoshi K, Kido T, and Nogawa K.(1995). Mortality of inhabitants in an area polluted by cadmium: 15 year follow up. Occupational and Environmental Medicine, 52, 181-184.

NIVA, 2002. Report n° 4606-2002. Time trend monitoring in Sorfjorden/Hardangerfjorden. Comparison of environmental data. Norwegian Institute for Water Research.

Noack Fuller G, De Beer C, and Seibert H.(1993). Cadmium, lead, selenium, and zinc in semen of occupationally unexposed men. Andrologia., 25, 7-12.

Nogawa K, Honda R, Kido T, Tsuritani I, Yamada Y, Ishizaki M, and Yamaya H.(1989). A dose-response analysis of cadmium in the general environment with special reference to total cadmium intake limit. Environ Res, 48, 7-16.

Nogawa K, Kobayashi E, Honda R, Ishizaki A, Kawano S, and Matsuda H.(1980). Renal dysfunctions of inhabitants in a cadmium-polluted area. Environ Res, 23, 13-23.

Nogawa K, Kobayashi E, Honda R, Ishizaki A, Kawano S, Ohmura T, Nakagawa H, Toga H, and Matsuda H.(1981). [Clinico-chemical studies on chronic cadmium poisoning. (Part 5) Renal functions (author's transl)]. Nippon Eiseigaku Zasshi, 36, 512-517.

Nogawa K.(1984). Biologic indicators of cadmium nephrotoxicity in persons with low-level cadmium exposure. Environ Health Perspect., 54, 163-169.

Nolet BA, Dijkstra VAA and Heidecke D (1994). Cadmium in beavers translocated from the elbe river to the Rhine Meuse estuary, and the possible effect on population- growth rate. Archives of Environmental Contamination and Toxicology, 27, 154-161.

Nomura Reference currently missing

Noonan CW, Sarasua SM, Campagna D, Kathman SJ, Lybarger JA, and Mueller PW.(2002). Effects of exposure to low levels of environmental cadmium on renal biomarkers. Environ Health Perspect, 110, 151-155.

Norberg AB and Molin N (1983). Toxicity of Cd, Co, U and Zn to Zoogloea ramigera. Water Research, 17, 1333-1336.

Nordberg G and Nordberg M.(1988).Biological Monitoring of Cadmium. In:Biological Monitoring of Toxic Metals. Edited by TW Clarkson, L Friberg, GF Nordberg, and PR Sager. Plenum Press. New York and London, 151-168.

Nordberg G, Kjellström T, and Nordberg M.(1985).Kinetics and Metabolism, cadmium and health: A toxicological and Epidemiological Appraisal. In:Vol.I: Exposure, Dose and Metabolism. Edited by L Friberg, CG Elinder, T Kjellström, and GF Nordberg. Boca Raton CRC Press. 103-178.

Nordberg G, Slorach S, and Stenstrom T.(1973). [Cadmium poisoning caused by a cooled-soft-drink machine]. Läkartidningen., 70, 601-604.

Nordberg GF, Jin T, and Nordberg M.(1994). Subcellular targets of cadmium nephrotoxicity: cadmium binding to renal membrane proteins in animals with or without protective metallothionein synthesis. Environ Health Perspect, 102, 191-194.

Nordberg GF, Jin T, Kong Q, Ye T, Cai S, Wang Z, Zhuang F, and Wu X.(20-6-1997). Biological monitoring of cadmium exposure and renal effects in a population group residing in a polluted area in China. Sci Total Environ, 199, 111-114.

Nordberg GF.(1992). Application of the 'critical effect' and 'critical concentration' concept to human risk assessment for cadmium. IARC.Sci.Publ., 3-14.

North Sea Conference (1995). Fourth International Conference on the Protection of the North Sea. Progress Report. Esbjerg - Denmark, 8-9 June 1995.

NTP (1995). NTP Technical Report on Toxicity Studies of Cadmium Oxide (CAS No.1306-19-0) Administered by Inhalation to F344/N Rats and B6C3F1 Mice. 39,

Nyholm E and Leffler P (1997). Response to the comment by C.G. Elinder, Ambio, 4, 1997, pp.251. Ambio, 26, 406-407.

Oberdörster G and Cox C.(1989).Kinetics of inhaled CdCl2, CdO, and CdS in rats and monkeys. In:Edited Proceedings of the Sixth International Cadmium Conference. Edited by S Hiscock and R Volpe. Cadmium Association/Cadmium Council. London/New York, 147-154.

Oberdörster G, Baumert HP, Hochrainer D, and Stoeber W.(1979). The clearance of cadmium aerosols after inhalation exposure. Am Ind Hyg Assoc J, 40, 443-450.

Oberdörster G, Oldiges H, and Zimmermann B.(1980). Lung deposition and clearance of cadmium in rats exposed by inhalation or by intratracheal instillation. Zbl.Bakteriol.Hyg.I.Abt.Orig., 170, 35-43.

Oberdörster G. (1992).Pulmonary deposition, clearance and effects of inhaled soluble and insoluble cadmium compounds. In:Cadmium in the Human Environment: Toxicity and Carcinogenicity. Edited by GF Nordberg, RFM Herber, and L Alessio. IARC. Lyon, 189-204.

Ochi T and Ohsawa M.(1983). Induction of 6-thioguanine-resistant mutants and single-strand scission of DNA by cadmium chloride in cultured Chinese hamster cells. Mutat Res, 111, 69-78.

Ochi T and Ohsawa M.(1985). Participation of active oxygen species in the induction of chromosomal aberrations by cadmium chloride in cultured Chinese hamster cells. Mutat.Res., 143, 137-142.

Ochi T, Mogi M, Watanabe M, and Ohsawa M.(1984). Induction of chromosomal aberrations in cultured Chinese hamster cells by short-term treatment with cadmium chloride. Mutat.Res., 137, 103-109.

Ochi T, Takahashi K, and Ohsawa M.(1987). Indirect evidence for the induction of a prooxidant state by cadmium chloride in cultured mammalian cells and a possible mechanism for the induction. Mutat.Res., 180, 257-266.

Oda S. (1993) In-ground burial test for Ni-Cd batteries.

OECD (1984). Guidelines for the testing of chemicals No. 207 Earthworm acute toxicity tests. OECD Adopted 4 April 1984.

OECD (1994). Risk reduction monograph no. 5: cadmium : Background and National Experience with Reducing Risk OECD Environment Monograph Series no. 104, Environment Directorate, Organisation for Economic Cooperation and Development, Paris, France.

OECD (1999). OECD Environmental Data Compendium 1999.Organisation for Economic Coöperation and Development, Paris, France. 328 p.

OECD (Organisation for Economic Co-operation and Development) (2001). OECD series on testing and assessment. Guidance document on transformation/dissolution of metals and metal compounds in aqueous media. Guideline 29. Paris, 19pp.

Ogunlewe JO and Osegbe DN.(1-4-1989). Zinc and cadmium concentrations in indigenous blacks with normal, hypertrophic, and malignant prostate. CANCER, 63, 1388-1392.

Oldereid NB, Thomassen Y, Attramadal A, Olaisen B, and Purvis K.(1993). Concentrations of lead, cadmium and zinc in the tissues of reproductive organs of men. J Reprod Fertil, 99, 421-425.

Oleru UG.(1975). Epidemiological implications of environmental cadmium. I. The probable utility of human hair for occupational trace metal (cadmium) screening. Am Ind Hyg Assoc J, 36, 229-233.

Olsson P-E and Haux C (1986). Increased hepatic metallothionein content correlates to cadmium accumulation in environmentally exposed perch (Perca fluviatilis). Aquatic Toxicology, 9, 231-242.

Oo YK, Kobayashi E, Nogawa K, Okubo Y, Suwazono Y, Kido T, and Nakagawa H.(2000). Renal effects of cadmium intake of a Japanese general population in two areas unpolluted by cadmium. Arch Environ Health, 55, 98-103.

Orlowski C, Piotrowski JK, Subdys JK, and Gross A.(1998). Urinary cadmium as indicator of renal cadmium in humans: an autopsy study. Hum.Exp.Toxicol., 17, 302-306.

Osawa T, Kobayashi E, Okubo Y, Suwazono Y, Kido T, and Nogawa K.(2001). A Retrospective Study on the Relation between Renal Dysfunction and Cadmium Concentration in Rice in Individual Hamlets in the Jinzu River Basin, Toyama Prefecture, Japan. Environ.Res.Section A, 86, 51-59.

Osman K, Akesson A, Berglund M, Bremme K, Schutz A, Ask K, and Vahter M.(2000). Toxic and essential elements in placentas of Swedish women. Clin Biochem, 33, 131-138.

Otte F.P. (1995). Analysis of metals and calorific value in components from household waste, 1988-1992 (including the results from 1986 and 1987. RIVM report 776201024

OVAM (2001). Inventarisatie van de afvalverbrandingssector in Vlaanderen. Achtergronddocument afvalstoffen, D/2001/5024/7, 103 p.

OVAM (2002). Peter Loncke, pers. com., 2002.

Pacyna JM, Münch J, Alcamo J and Anderberg S (1991). Emission trends for heavy metals in Europe. In: Farmer et al (eds) Proceedings of the 8th International Conference on Heavy metals in the Environment, Edinburgh.

Page KR, Abramovich DR, Aggett PJ, Bain M, Chipperfield AR, Durdy H, McLachlan J, and Smale A.(1992). Uptake of zinc by human placental microvillus border membranes and charaterisation of the effects of cadmium on this process. Placenta, 13, 151-161.

Panasonic (2002). Pers. com., letter of 30.09.02.

Pandya CB, Parikh DJ, Patel TS, Kulkarni PK, Sathawara NG, Shah GM, and Chatterjee BB.(1985). Accumulation and interrelationship of cadmium and zinc in human kidney cortex. Environ Res, 36, 81-88.

Pankakoski E, Hyvarinen H, Jalkanen M and Koivisto I. (1993). Accumulation of heavy-metals in the mole in Finland. Environmental Pollution, 80, 9-16.

Park CB.(1991). Cadmium intake and age in beta 2-microglobulinuria: categorical data analysis in epidemiology [letter]. Ind.Health, 29, 77-84.

Parkman H, Borg H, Iverfeldt A and Lithner G (1998). Cadmium in Sweden – environmental risks. KEMI, National Chemical Inspectorate, Solna, Sweden.

Parmelee RW, Phillips CT, Checkai RT and Bohlen PJ (1997). Determining the effects of pollutants on soil faunal communities and trophic strucure using a refined microcosm system. Environmental Toxicology and Chemistry, 16, 1212-1217.

Pascoe D and Mattey DL (1977). Studies of the toxicity of cadmium to the three-spined stickleback Gasterosteus aculatus L. Journal of Fish Biology, 11, 207-215.

Patwardhan JR and Finckh ES.(1976). Fatal cadmium-fume pneumonitis. Med.J.Austr., 1, 962-966.

PC Wiaux (1998): Presentation of General information on cadmium(oxide), Human heath and Environmental results by Mr. De Schepper and Mr. M. Paulus. Visit to the company.

Pearse J (1996). Cadmium: Some aspects of risk reduction. In: Publikatiereeks Stoffen, Veiligheid, Straling, Ministerie van Volkshuisvesting. Ruimtelijke Ordening en Milieubeheer, Bilthoven, The Netherlands.

Pearse, J. (1996). Cadmium: Some aspects of risk reduction. In: Publikatiereeks Stoffen, Veiligheid, Straling, Ministerie van Volkshuisvesting. Ruimtelijke Ordening en Milieubeheer, Bilthoven, The Netherlands.

Penttinen S, Kukkonen J and Oikari A (1995). The kinetics of cadmium in Daphnia magna as affected by humic substances and water hardness. Ecotoxicology and Environmental Safety, 30, 72-76.

Pesch CE, Hansen DJ, Boothman WS, Berry WJ and Mahony JD (1995). The role of AVS and interstitial water metal concentrations in determining bioavailability of Cd and Ni from contaminated sediments to the marine polychaete Neanthes arenaceodentata. Environmental Toxicology and Chemistry, 14, 129-141.

Petering HG, Choudhury H, and Stemmer KL.(1979). Some effects of Oral Ingestion of Cadmium on Zinc, Copper, and Iron Metabolism. Environ Health Perspect, 28, 97-106.

Peterson GS, Ankley GT and Leonard EN (1996). Effect of bioturbation on metal-sulfide oxidation in surficial freshwater sediments. Environmental Toxicology and Chemistry, 15, 2147-2155.

Petersson Grawé K, Thierfelder T, Jorhem L and Oskarsson A (1997). Cadmium levels in kidneys from Swedish pigs in relation to environmental factors - temporal and spatial trends. The Science of the Total Environment, 208, 111-122.

Pfannhauser W (1991). Die Schwermetall-Belastung der Österreichischen Nahrung im interantionalen Vergleich. Ernährungsforschung, 36, 13-17.

Phipps GL and Holcombe GW (1985). A method for aquatic multiple species toxicant testing: acute toxicity of 10 chemicals to 5 vertebrates and 2 invertebrates. Environmental Pollution (Series A), 38, 141-157.

Pickering QH and Gast MH (1972). Acute and chronic toxicity of Cd to the fathead minnow (Pimephales promelas). Journal of the Fisheries Research Board of Canada, 29, 1099-1106.

Pickering QH and Henderson C (1966). The acute toxicity of some heavy metals to different species of warmwater fishes. Air and Water Pollution International Journal, 10, 453-463.

Pietrzak-Flis Z, Rehnberg GL, Favor MJ, Cahill DF, and Laskey JW.(1978). Chronic ingestion of cadmium and/or tritium in rats. I.Accumulation and distribution of cadmium in two generations. Environ Res, 16 , 9-17.

Pinto SS, Enterline PE, Henderson V, and Varner MO.(1977). Mortality experience in relation to a mesaured arsenic trioxide exposure. Environ Health Perspect, 19, 127-130.

Piscator M and Lind B.(1972). Cadmium, zinc, copper, and lead in human renal cortex. Arch Environ Health, 24, 426-431.

Piscator M.(1984). Long-term observations in tubular and glomerular function in cadmium-exposed persons. Environ Health Perspect, 54, 175-179.

Plasman C and Verreet G (1992). Cadmium. Ministerie van Volksgezondheid en Leefmilieu. Beheerseenheid van het Mathematisch Model Noordzee, Belgium.

Pleasants EW, Sandow ME, DeCandido S, and et al.(1992). The effect of vitamin D3 and 1,25-dihydroxyvitamin D3 on the toxic symptoms of cadmium exposed rats. Nutrition Research, 12, 1393-1403.

Pleasants EW, Waslien C, Naughton BA, and et al.(1993). Dietary modulation of the symptoms of cadmium toxicity in rats: Effects of vitamins A,C,D,DD hormone and fluoride. Nutrition Research, 13, 839-850.

Pless-Mulloli T, Boettcher M, Steiner M, and Berger J.(1998). alpha-1-microglobulin: epidemiological indicator for tubular dysfunction induced by cadmium? Occup Env Med, 55, 440-445.

Poldoski JE (1979). Cadmium bioaccumulation assays. Their relationship to various ionic equilibria in Lake Superior water. Environmental Science and Technology, 13, 701-706.

Pond WG and Walker EF.(1975). Effect of dietary Ca and Cd level of pregnant rats on reproduction and on dam and progeny mineral concentrations. Proc Soc Exp Biol Med, 148, 665-668.

Popenoe EA and Schmaeler MA.(1979). Interaction of human DNA polymerase beta with ions of copper, lead, and cadmium. Arch.Biochem.Biophys, 196, 109-120.

Potts CL.(1965). Cadmium proteinuria-the health of battery workers exposed to cadmium oxide dust. Ann Occup Hyg, 8, 55-61.

Power EA and Chapman PM (1996). Assessing sediment quality. In: G.A. Burton Jr. (ed.), Sediment toxicity assessment. pp. 1-18, Lewis Publishers, Chelsea, Michigan.

Prigge E.(1978). Early Signs of Oral and Inhalative Cadmium Uptake in Rats. Arch.Toxicol., 40, 231-247.

Princi F and Geever EF.(1950). Prolonged inhalation of cadmium. Arch.Ind.Hyg.Occup.Med., 1, 651-661.

Princi F.(1947). A study of industrial exposure to cadmium. J Ind hyg Toxicol, 29, 315-320.

Prodan L.(1932). J.Ind.Hyg.Toxicol., 14, 174-174.

Qian X., Koerner R.M and D.H. Gray (2002). Geotechnical aspects of landfill design and construction. Prentice Hall. 710 p.

Quataert P and Claeys F.(1997). Epidemiological Surveillance of the General Population. Blood Lead and Cadmium Levels in Belgium 1996. Highlights of the Technical Report. RP96d1.doc, 1-25.

Quemerais and Lum (1997). Reference currently missing

Quemerais B and Lum KR (1997). Distribution and temporal variation of cadmium in the St. Lawrence River basin. Aquatic Sciences, 59, 243-259.

Questionnaire: cfr Industry questionnaire and cfr Questionnaire on Batteries or Batteries’ questionnaire

Rachootin P and Olsen J.(1983). The Risk of Infertility and Delayed Conception Associated With Exposures in the Danish Workplace. J Occup Med, 25, 394-402.

Radisch B, Luck W, and Nau H.(1987). Cadmium concentrations in milk and blood of smoking mothers. Toxicology Letters, 36, 147-152.

Ramel C and Magnusson J.(1979). Chemical induction of nondisjunction in drosophila. Environ Health Perspect, 31, 59-66.

RAR CdO (1999). Risk assessment cadmium oxide CAS-No.: 1306-19-0, draft text, submitted.

RDCHW (Research and Development Centre of Hazardous Waste) (2002). Behaviour of Nickel_Cadmium Batteries in Wastes and Landfills. Additional information. Dr. A. Heindl. Unpublished document. Sept., 2002.

Read HJ and Martin MH (1993). The effect of heavy-metals on populations of small mammals from woodlands in Avon (England), with particular emphasis on metal concentrations in Sorex araneus L and Sorex minutus L. Chemosphere, 27, 2197-2211.

Reber HH (1989). Treshold levels of cadmium for soil respiration and growth of spring wheat (Triticum aestivum L.), and difficulties with their determination. Biology and Fertility of Soils, 7, 152-157.

Reeves PG and Chaney RL.(2001). Mineral status of female rats affects the absorption and organ distribution of dietary cadmium derived from edible sunflower kernels (Helianthus annuus L.). Environ.Res.Section, 85, 215-225.

Reimann D.O (2002). Experiences with TMT 15 for mercury minimization in wastewater from waste incineration. Veranstaltungsort Hydroline Spa/Eigenmann & Veronelli Spa. Rho (Milano) 28 Februari 2002.

Reimann D.O. (1989). Heavy metals in domestic refuse and their distribution in incinerator reidues. Waste Management & Research, 7, 57-62.

Reinl W.(1953). Med.Klin., 19, 152-152.

Reinl W.(1961). On a mass-intoxication through cadmium oxide vapor. Arch.Toxikol., 19, 152-157.

Rème and Peres.(1959). A propos d'une intoxication collective par le cadmium. Arch.Mal.Prof.Med.Trav.Secur.Soc., 20, 783-785.

Rentz. O., Sasse H., Karl U., Schleef H. and Dorn R. (1997). Emission control at stationary sources in the Federal Republic of Germany. Voll II. Heavy Metal Emission Control. UBA TEXTE 67/97.

Report prepared for Federal Office of Environment, Forests and Landscape, Switeserland. In press.

Richardson ME, Spivey Fox MR and Fry BE (1974). Pathological-changes produced in japanese-quail by ingestion of cadmium. Journal of Nutrition, 104, 323-338.

Rigo H.G., Chandler A.J. and Sawell, S.E.(1993a).

Rigo H.G., Chandler A.J. and Sawell, S.E.(1993b). Debunking some myths about metals. In proceedings of the 1993 International Conference on Municipal Waste Combustion, Williamsburg.

Rijpkema L.P.M. (1993a). The impact of a change in EC legislation on the combustion of municipal solid waste. TNO-rapport for the EC, ref.93-312, 1993.

Rijpkema L.P.M. (1996). Specific processing costs of waste materials in a municipal solid waste facility. TNO report, Institute of Environmental sciences, energy research and process innovation, TNO-MEP-R93/248.

Rivedal E and Sanner T.(1981). Metal salts as promoters of in vitro morphological transformation of hamster embryo cells initiated by benzo(a)pyrene. Cancer Res, 41, 2950-2953.

RIVM (1997) Milieubalans 1997: Het Nederlandse milieu verklaard. Samson, Alphen aan den Rijn.

RIVM/LAE (1998). Monitoring prioritaire afvalstoffen, gegevens 1998.

Robinson H. (1995). A review of the composition of leachates from domestic wastes in landfill sites. Report prepared for the UK Department of the Environment.

Robison SH, Cantoni O, and Costa M.(1982). Strand breakage and decreased molecular weight of DNA induced by specific metal compounds. Carcinogenesis, 3, 657-662.

Roekaerts M. (2002). The Biogeographical Regions Map of Europe. Basic principles of its creation and overview of its development. European Topic Centre Nature Protection and Biodiversity, Paris Cedex, France, 17p

Roels H and Lauwerys R.(1984). Early detection of nephrotoxic effects of industrial chemicals. Umwelthygiene Supplement 1, 217-

Roels H, Bernard AM, Cardenas A, Buchet JP, Lauwerys RR, Hotter G, Ramis I, Mutti A, Francini I, Bundschuh I, and et al.(1993). Markers of early renal changes induced by industrial pollutants. III. Application to workers exposed to cadmium. Br J Ind Med, 50, 37-48.

Roels H, Buchet JP, Truc J, Croquet F, and Lauwerys R.(1982). The possible role of direct ingestion on the overall absorption of cadmium or arsenic in workers exposed to CdO or As2O3 dust. Am J Ind Med, 3 , 53-65.

Roels H, Hubermont G, Buchet JP, and Lauwerys R.(1978). Placental transfer of lead, mercury, cadmium, and carbon monoxide in women. III. Factors influencing the accumulation of heavy metals in the placenta and the relationship between metal concentration in the placenta and in maternal and cord blood. Environ Res, 16, 236-247.

Roels H, Lauwerys R, Buchet JP, Bernard A, Garvey JS, and Linton HJ.(1983). Significance of urinary metallothionein in workers exposed to cadmium. Int.Arch.Occup.Environ.Health, 52, 159-166.

Roels HA, Lauwerys RR, and Dardenne AN.(1983). The critical level of cadmium in human renal cortex: a reevaluation. Toxicology Letters, 15, 357-360.

Roels HA, Lauwerys RR, Bernard AM, Buchet JP, Vos A, and Oversteyns M.(1991). Assessment of the filtration reserve capacity of the kidney in workers exposed to cadmium. Br J Ind Med, 48, 365-374.

Roels HA, Lauwerys RR, Buchet JP, and Bernard A.(1981). Environmental exposure to cadmium and renal function of aged women in three areas of Belgium. Environ Res, 24, 117-130.

Roels HA, Lauwerys RR, Buchet JP, Bernard A, Chettle DR, Harvey TC, and Al Haddad IK.(1981). In vivo measurement of liver and kidney cadmium in workers exposed to this metal: its significance with respect to cadmium in blood and urine. Environ Res, 26, 217-240.

Roels HA, Lauwerys RR, Buchet JP, Bernard AM, Vos A, and Oversteyns M.(1989). Health significance of cadmium induced renal dysfunction: a five year follow up. Br J Ind Med, 46, 755-764.

Roels HA, Van Assche FJ, Oversteyns M, De Groof M, Lauwerys RR, and Lison D.(1997). Reversibility of Microproteinuria in Cadmium Workers With Incipient Tubular Dysfunction After Reduction of Exposure. Am J Ind Med, 31, 645-652.

Romare A and Lundholm CE.(1999). Arch Toxicol, 73, 223-228.

Römbke J (1989). Enchytraeus albidus (Enchytraeidae, Oligochaeta) as a test organism in terrestrial laboratory systems. Archives of Toxicology, Suppl., 13, 402-405.

Rombough PJ and Garside ET (1982). Cadmium toxicity and accumulation in eggs and alevins of atlantic salmon Salmo salar. Canadian Journal of Zoology, 60, 2006-2014.

Romijn CAFM, Luttik R and Canton JH (1994). Presentation of a general algorithm to include effect assessment on secondary poisoning in the derivation of environmental-quality criteria .2. Terrestrial food-chains. Ecotoxicology and Environmental Safety, 27, 107-127.

Römkens and Salomons W. (1998). Cd, Cu and Zn solubility in arable and forest soils : consequences of land use changes for metal mobility and risk assessment. Soil Science, 163 : 859-871.

Römkens PFAM and Salomons W (1998). Cd, Cu and Zn solubility in arable and forest soils: consequences of land use changes for metal mobility and risk assessment. Soil Science, 163, 859-871.

Ros JPM and Slooff W (1990). Basisdocument cadmium. Rapport no. 4 serie basisdocumenten publikatiereeks milieubeheer, Rijksinstituut voor volksgezondheid en milieuhygiëne, Bilthoven, Nederland.

Ros, J.P.M. en Slooff, W. (1990). Basisdocument cadmium. Rapport no. 4 serie basisdocumenten publikatiereeks milieubeheer, Rijksinstituut voor volksgezondheid en milieuhygiëne, Bilthoven, Nederland.

Rosko JJ and Rachlin JW (1977). The effect of Cd, Cu, Hg, Zn and Pb on cell division, growth and chlorophyll and content of the chlorophyte Chlorella vulgaris. Bulletin of the Torrey Botanical Club, 104, 226-233.

Rosmann TG, Roy NK, and Lin Wc.(1992).Genotoxicity of cadmium. In:Cadmium in the Human Environment: Toxicity and Carcinogenicity. Edited by G Nordberg, RF Herber, and L Alessio. IARC (International Agency for Research on Cancer). Lyon, 367-375.

Ross MR, Wood MD, Copplestone D, Warriner M and Crook P (The Environment Agency, Bristol, draft).

Ross P.(1944). Br.Med.J., 1, 252-252.

Ross, D; C. Harries, A. Revans, C. Cross and P. Nathanail (2000). Long term fate of metals in landfill a combined experimental and modelling study, R&D Technical Report P249, Environment Agency.

Rothbaum HP, Goguel RL, Johnston AE and Mattingly GEG (1986). Cadmium accumulation in soils from long-continued application of superphosphate. Journal of Soil Science, 37, 99-107.

RPA (2001). The risk to health and environment by cadmium used as a colouring agent or a stabiliser in polymers and for metal plating. Final report, december, 2001.

RPA Ltd (Risk & Policy Analysts Limited) (2001). The risks to health and environment by cadmium used as a colouring agent or a stabiliser in polymers and for metal plating. Final report. Prepared for the European Commission, DG Enterprise. J316/Cadmium.

Ruggenenti P, Perna A, Mosconi L, Pisoni R, and Remuzzi G.(1998). Urinary protein excretion rate is the best independent predictor of ESRF in non-diabetic proteinuric chronic nephropathies. "Gruppo Italiano di Studi Epidemiologici in Nefrologia" (GISEN). Kidney Int, 53, 1209-1216.

Rusch GM, O'Grodnick JS, and Rinehart WE.(1986). Acute Inhalation Study in the Rat of Comparative Uptake, Distribution and Excretion for Different Cadmium Containing Materials. Am Ind Hyg Assoc J, 47, 754-763.

Russel LR, DeHaven JI and Botts RP (1981). Toxic effects of cadmium on the garden snail (Helix aspersa). Bulletin of Environmental Contamination and Toxicology, 26, 634-640.

RVF (2002). Website Swedish Waste Management. http://www.rvf.se

Ryan JA, Pahren HR and Lucas JB (1982). Controlling cadmium in the human food chain: a review and a rationale based on health effects. Environmental Research, 28, 251-302.

Saaranen M, Kantloa S, Saarikoski S, and Vanha-Perttula T.(1989). Human Seminal Plasma Cadmium: Comparison with Fertility and Smoking Habits. Andrologia, 21, 140-145.

Sacco-Gibson N, Chaudhry S, Brock A, Sickles AB, Patel B, Hegstad R, Johnston S, Peterson D, and Bhattacharyya M.(1992). Cadmium effects on bone metabolism: accelerated resorption in ovariectomized, aged beagles. Toxicol Appl Pharmacol, 113, 274-283.

Sajwan KS, Ornes WH, Youngblood TV and Alva AK (1995). Uptake of soil applied cadmium, nickel and selenium by bush beans. Water, Air and Soil Pollution, 91, 209-217.

Sakurai H, Omae K, Toyama T, Higashi T, and Nakadate T.(1982). Cross-sectional study of pulmonary function in cadmium alloy workers. Scand J Work Environ Health, suppl.1, 122-130.

Salminen R, Chekushin V.,Tenhola, M., Bogatyrev, I., Glavatskikh, S. P., Gregorauskiene, V., Niskavaara, H., Polischuok, A., Selenok, L., and Tomilina, O. (2004). Geochemical Atlas of Eastern Barents Region. Journal of Geochemical Exploration, In Press

Saltzman RA, Miller RK, and di Sant'Agnese PA.(1989). Cadmium exposure on day 12 of gestation in the Wistar rat: distribution, utero-placental blood flow, and fetal viability. Teratology, 39, 19-30.

Sangster B, de Groot G, Loeber JG, Derks HJGM, Krajnc EI, and Savelkoul TJF.(1984). Urinary excretion ofcadmium, protein,beta-2-microglobulin and glucose in individuals living in a cadmium-polluted area. Hum.Toxicol., 3, 7-21.

Saplakoglu U and Iscan M.(30-1-1998). Sister chromatid exchanges in human lymphocytes treated in vitro with cadmium in G(o) and S phase of their cell cycles. Mutat Res, 412, 109-114.

Sartor F, Rondia D, Claeys F, Buchet JP, Ducoffre G, Lauwerys R, Staessen J, and Amery A.(1992).Factors influencing the cadmium body burden in a population study. In:Cadmium in the Human Environment: Toxicity and Carcinogenicity. Edited by GF Nordberg, RFM Herber, and L Alessio. IARC, International Agency for Research on Cancer. Lyon, 101-106.

Sartor FA, Rondia DJ, Claeys FD, Staessen JA, Lauwerys RR, Bernard AM, Buchet JP, Roels HA, Bruaux PJ, Ducoffre GM, and et al.(1992). Impact of environmental cadmium pollution on cadmium exposure and body burden. Arch Environ Health, 47, 347-353.

Sasser LB and Jarboe GE.(1977). Intestinal absorption and retention of cadmium in neonatal rat. Toxicol Appl Pharmacol, 14, 423-431.

Sauvé S, Dumestre A, McBride M and Hendershot W (1998). Derivation of soil quality criteria using predicted chemical speciation of Pb2+ and Cu2+. Environmental Toxicology and Chemistry, 17, 1481-1489.

Saviozzi A, Levi-Minzi R, Cardelli R and Riffaldi R (1997). The influence of heavy metals on carbon dioxide evolution from a typic Xerochrept soil. Water, Air and Soil Pollution, 93, 409-417.

Saxena DK, Murthy RC, and Chandra SV.(1986). Embryotoxic and teratogenic effects of interaction of cadmium and lindane in rats. Acta Pharmacol Toxicol, 59, 175-178.

Saygi S, Deniz G, Kutsal O, and Vural N.(1991). Chronic effects of cadmium on kidney, liver, testis, and fertility of male rats. Biol Trace Elem Res, 31, 209-214.

Sbrana I, Di Sibio A, Lomi A, and Scarcelli V.(1993). C-mitosis and numerical chromosome aberration analyses in human lymphocytes: 10 known or suspected spindle poisons. Mutat Res, 287, 57-70.

Scarpa C and Ferrea E.(1967). Ricerche allergologiche concernenti il cadmio, il berillio, l'arsenico e la diazodietilanilina. Minerva Dermatologica, 42, 126-129.

Schellmann B, Rohmer E, Schaller KH and Weltle D (1984). Cadmium- und Kupferkonzentrationen in Stuhl, Urin und Blut nach Aufnahme wildwachsender Champignons. Zeitschrift für Lebensmitteluntersuchung und–Forschung, 178, 445-449.

Scheuhammer AM (1987). The chronic toxicity of aluminum, cadmium, mercury, and lead in birds - a review. Environmental Pollution, 46, 263-295.

Schilderman PAEL, Moonen EJC, Kempkers P and Kleinjans JCS (1997). Bioavailability of soil-adsorbed cadmium in orally exposed male rats. Environmental Health Perspectives, 105, 234-238.

Schroeder HA and Balassa JJ.(1961). Abnormal trace metals in man: cadmium. J Chronic Dis, 14, 236-258.

Schroeder HA and Mitchener M.(1971). Toxic effects of trace elements on the reproduction of mice and rats. Arch Environ Health, 23, 102-106.

Schroeder, P.R., N.M. Aziz, C.M. Lloyd and P. Zappi, 1994a.The hydrologic evaluation of landfill performance (HELP model). User’s guide for version 3. EPA/600/R-94/168a, September 1994, U.S. Environmental Protection Agency Office of Research and Development, Washington, DC.

Schroeder, P.R., T.S. Dozier, P. Zappi, B.M McEnroe, J.W. Sjöstrom and R.L Peyton, 1994b.The hydrologic evaluation of landfill performance (HELP model). Engineering documentation for version 3. EPA/600/R-94/168b, September 1994, U.S. Environmental Protection Agency Office of Research and Development, Washington, DC.

Schuster (1999). Waste incineration plants in Austria. Greenpeace.

Schuytema GS, Nelson PO, Malueg KW, Nebeker AV, Krawczyk DF, Ratcliff AK and Gakstatter JH (1984). Toxicity of cadmium in water and sediment slurries to Daphnia magna. Environmental Toxicology and Chemistry, 3, 293-308.

Schweinsberg F, Baron P, Hahn W, Hermann U, and Tausch-Walz G.(1987). [Determination and assessment of the content of lead, cadmium and mercury in hair, nails and organs of persons in clean and polluted areas]. Schriftenr.Ver.Wasser Boden Lufthyg., 71, 91-100.

Scott R, Aughey E, Fell GS, and Quinn MJ.(1987). Cadmium concentrations in human kidneys from the UK. Hum.Toxicol., 6, 111-120.

Scott R, Patterson PJ, Burns R, Ottoway JM, Hussain FE, Fell GS, Dumbuya S, and Iqbal M.(1978). Hypercalciuria related to cadmium exposure. Urology, 11, 462-465.

SCRELEC & ADEME (1999) Sorting of batteries from M.S.W. of the Montmorency area.1999.Mrs. J.Michaux. SCRELEC. Rue Hamelin, 17. F-75116 Paris. France.

Seidal K, Jörgensen N, Elinder CG, Sjögren B, and Vahter M.(1993). Fatal cadmium-induced pneumonitis. Scand J Work Environ Health, 19, 429-431.

SEPA (1987). Cadmium in the environment – a classification system (Kadmium I miljön, bedömningsgrunder). Swedish EPA, report n° 3317, ISBN 91-620-3317-4, 76 pp. (in Swedish).

SFSP (1999). L'incinération des déchets et la santé publique: bilan des connaissances récents et évaluation du risque. Société Française de Santé Publique, ISBN 2-911489-07-1

SFT (2002). Website Norwegian Pollution Control Authority (SFT). http://www.sft.no/english/publications/air/TA1235.html

Shaham J, Meltzer A, Ashkenazi R, and Ribak J.(1996). Biological monitoring of exposure to cadmium, a human carcinogen, as a result of active and passive smoking. J Occup Environ Med, 38, 1220-1228.

Shaikh ZA, Ellis KJ, Subramanian KS, and Greenberg A.(1990). Biological monitoring for occupational cadmium exposure: the urinary metallothionein. Toxicology, 63, 53-62.

Shaikh ZA, Kido T, Kito H, Honda R, and Nogawa K.(1990). Prevalence of metallothioneinuria among the population living in the Kakehashi River basin in Japan--an epidemiological study. Toxicology, 64, 59-69.

Shaikh ZA, Tohyama C, and Nolan CV.(1987). Occupational exposure to cadmium: effect on metallothionein and other biological indices of exposure and renal function. Arch.Toxicol., 59, 360-364.

Sharma R, Kjellström T, and McKenzie J.(1983). Cadmium in blood and urine among smokers and non-smokers with high cadmium intake via food. Toxicology, 29, 163-171.

Sharma RP, Kjellström T and McKenzie JM (1983). Cadmium in blood and urine among smokers and non-smokers with high cadmium intake via food. Toxicology, 29, 163-171.

Shiels DO and Robertson I.(1946). Br J Ind Med, 3, 213-213.

Shigematsu I, Kitamura S, Takeuchi J, Minowa M, Nagai T, and Fukushima M.(1982).A retrospective mortality study on cadmium-exposed populations in Japan. In:Proceedings of the Third International Cadmium Conference, Miami. Edited by, 115-118.

Shigematsu I, Takeuchi J, Minowa M, Nagai M, Usui T, and Fukushima M.(1980). A retospective mortality study on cadmium-exposed pollution in Japan. Kankyo Hoken Rep, 46 part 2, 1-71.

Shiwen C, Lin Y, Zhineng H, and et al.(1990). Cadmium exposure and health effects among residents in an irrigation area with ore dressing wastewater. Sci Total Environ, 90, 67-73.

Shore RF and Douben PET (1994). The ecotoxicological significance of cadmium intake and residues in terrestrial small mammals. Ecotoxicology and Environmental Safety, 29, 101-112.

Shuman MS, Voors AW, and Gallagher PN.(1974). Contribution of cigarette smoking to cadmium accumulation in man. Bull Environ Contam Toxicol, 12, 570-576.

Sipowicz M, Kostrzewska A, Laudanski T, and Akerlund M.(1995). Effects of cadmium on myometrial activity of the nonpregnant human.Interactions with calcium and oxytocin. Acta Obstet Gynecol Scand, 74, 93-96.

Sjöbeck M-L, Haux C, Larsson A and Lithner G (1984). Biochemical and hematological studies on perch, Perca fluviatilis, from the cadmium-contaminated River Eman. Ecotoxicology and Environmental Safety, 8, 303-312.

Skjelkvåle BL, Andersen T, Fjeld E, Mannio J, Wilander A, Johansson K, Jensen JP, Moiseenko T (2001). Heavy metal surveys in Nordic lakes; concentrations, geographic patterns and relation to critical limits. Ambio, 30, 2-10.

Skjelkvåle BL, Mannio J, Wilander A, Johansson K, Jensen JP, Moiseenko T, Fjeld E, Andersen T, Vuorenmaa J and Røyseth O (1999). Heavy metal surveys in Nordic lakes; harmonised data for regional assessment of critical limits. NIVA report sn° 4039-99, ISBN 82-577-3641-4.

Smit CE, van Wezel AP, Jager T and Traas TP (2000). Secondary poisoning of cadmium, copper and mercury: implications for the maximum permissible concentrations and negligible concentrations in water and soil. RIVM report 601501 009. RIVM, Bilthoven, The Netherlands.

Smith JC, Kench JE, and Smith JP.(1957). Chemical and histological post-mortem studies on a workman exposed for many years to cadmium oxide fume. Br J Ind Med, 14, 246-249.

Smith JP, Smith JC, and McCall AJ.(1960). Chronic poisoning from cadmium fume. J Pathol Bacteriol, 80, 297-296.

Smith MJ, Pihl RO, and Garber B.(1982). Postnatal cadmium exposure and longterm behavioral changes in the rat. Neurobehav.Toxicol.Teratol., 4, 283-287.

Smith NJ, Topping MD, Stewart JD, and Fletcher JG.(1986). Occupational cadmium exposure in jig solderers. Br.J.Ind.Med., 43, 663-666.

Smith TJ, Anderson RJ, and Reading JC.(1980). Chronic cadmium exposures associated with kidney function effects. Am J Ind.Med, 1, 319-337.

Smith TJ, Ferrell WC, Varner MO, and Putnam RD.(1980). Inhalation exposure of cadmium workers: effects of respirator usage. Am Ind.Hyg.Assoc.J, 41, 624-629.

Smith TJ, Petty TL, Reading JC, and Lakshminarayan S.(1976). Pulmonary Effects of Chronic Exposure to Airborne Cadmium. Am Rev Resp Dis, 114, 161-169.

Smolders E, Brans K, Földi A and Merckx R (1999). Cadmium fixation in soils measured by isotopic dilution. Soil Science Society of America Journal, 63, 78-85.

Snyder RD, Davis GF, and Lachmann P.(1989). Inhibition by metals of X-ray and ultraviolet-induced DNA repair in human cells. Biol Trace Elem Res, 21, 389-398.

Snyder RD.(1988). Role of active oxygen species in metal-induced DNA strand breakage in human diploid fibroblasts. Mutat.Res., 193, 237-246.

Sokoll LJ, Russell RM, Sadowski JA, and Morrow FD.(1994). Establishment of creatinine clearance reference values for older women. Clin Chem, 40, 2276-2281.

Sorahan T and Lancashire R.(1997). Lung cancer mortality in a cohort of workers employed at a cadmium recovery plant in the United States: an analysis with detailed job histories. Occupational and Environmental Medicine, 54, 194-201.

Sorahan T, Lister A, Gilthorpe MS, and Harrington JM.(1995). Mortality of copper cadmium alloy workers with special reference to lung cancer and non-malignant diseases of the respiratory system, 1946-92. Occupational and Environmental Medicine, 52, 804-812.

Sorell TL and Graziano JH.(1990). Effect of Oral Cadmium Exposure during pregnancy on Maternal and Fetal Zinc Metabolism in the Rat. Toxicology and Applied Pharmacology, 102, 537-545.

Sörensen EMB (1991). Metal poisoning in fish. Environmental and Life Sciences Associates, pp. 175-234.

Sparrow LA, Salardini AA and Bishop AC (1993). Field studies of cadmium in potatoes (Solanum tuberosum L.). II. Response of cv. Russet Burbank and Kennebec to two double superphosphates of different cadmium concentrations. Australian Journal of Agricultural Research, 44, 855-861.

SPEED, 1993. Zware metalen. Rijkswaterstaat/RIZA, VROM/DGM, RIVM.

Spehar RL (1976). Cadmium and Zinc toxicity to flagfish, Jordanella floridae. Journal of the Fisheries Research Board of Canada, 33, 1939-1945.

Spehar RL and Carlson AR (1984). Derivation of site-specific water quality criteria for cadmium and the St. Louis river basin, Duluth, Minnesota. Environmental Toxicology Chemistry, 3, 651-665.

Spehar RL, Anderson RL and Fiandt JT (1978). Toxicity and bioaccumulation of Cd and Pb in aquatic invertebrates. Environmental Pollution, 15, 195-208.

Spolyar LW, Keppler JF, and Porter HG.(1944). J.Ind.Hyg., 26, 232-232.

Spurgeon DJ and Hopkin SP (1995). Extrapolation of the laboratory-based OECD earthworm toxicity test to metal-contaminated field sites. Ecotoxicology, 4, 190-205.

Spurgeon DJ and Hopkin SP (1996). Risk assessment of the threat of secondary poisoning by metals to predators of earthworms in the vincinity of a primary smelting works. Science of the Total Environment, 187,167-183.

Spurgeon DJ, Hopkin SP and Jones DT (1994). Effects of Cadmium, Copper, Lead and Zinc on growth, reproduction and survival of the eartworm Eisenia fetida (savigny): assessing the environmental impact of point-source metal contamination in terrrestrial ecosystems. Environmental Pollution, 84, 123-130.

Stackhouse RA and Benson WH (1989). Interaction of humic acids with selected trace elements: influence on bioaccumulation in daphnids. Environmnetal Toxicology and Chemistry, 8, 639-644.

Staessen J and Lauwerys R.(1993). Health effects of environmental exposure to cadmium in a population study. J Hum Hypertens, 7, 195-199.

Staessen J, Amery A, Bernard A, Bruaux P, Buchet J-P, Bulpitt C-J, Claeys F, De Plaen P, Ducoffre G, Fagard R, Lauwerys RR, Lijnen P, Nick L, Saint remy A, Roels H, Rondia D, Sartor F, and Thijs L.(1991). Blood pressure, the prevalence of cardiovascular diseases, and exposure to cadmium: a population study. Am.J.Epidemiol., 134, 257-267.

Staessen J, Amery A, Bernard A, Bruaux P, Buchet JP, Claeys F, De Plaen P, Ducoffre G, Fagard R, Lauwerys RR, and et al.(1991). Effects of exposure to cadmium on calcium metabolism: a population study. Br J Ind Med, 48, 710-714.

Staessen J, Kuznetsova T, Roels H, Emelianov D, and Fagard R.(2000). Exposure to cadmium and conventional and ambulatrory blood pressures in a prospective population study. Public Health and Environmental Exposure to Cadmium Study Group. Am J Hypertens, 13, 146-156.

Staessen J, Yeoman W, Fletcher AE, Markowe HLJ, Marmott MG, Rose G, Semmence A, Shipley MJ, and Bulpitt CJ.(1990). Blood cadmium in London civil servants. Int J Epidemiol, 19, 362-366.

Staessen JA, Kuznetsova T, Roels HA, Emelianov D, and Fagard R.(2000). Exposure to cadmium and conventional and ambulatory blood pressures in a prospective population study. Public Health and Environmental Exposure to Cadmium Study Group. Am J Hypertens, 13, 146-156.

Staessen JA, Lauwerys RR, Ide G, Roels HA, Vyncke G, and Amery A.(1994). Renal function and historical environmental cadmium pollution from zinc smelters. Lancet, 343, 1523-1527.

Staessen JA, Roels HA, Emelianov D, Kuznetsova T, Thijs L, Vangronsveld J, and Fagard R.(1999). Environmental exposure to cadmium, forearm bone density, and risk of fractures: prospective population study. Public Health and Environmental Exposure to Cadmium (Pheecad) Study Group. Lancet, 353, 1140-1144.

Staessen JA, Vyncke G, Lauwerys RR, Roels HA, Celis HG, Claeys F, Dondeyne F, Fagard R, Ide G, Lijnen PJ, Rondia D, Sartor F, Thijs L, and Amery A.(1992). Transfer of cadmium from a sandy acidic soil to man: a population study. Environ Res, 58, 25-34.

Stanescu D, Veriter C, Frans A, Goncette L, Roels H, Lauwerys R, and Brasseur L.(1977). Effects on lung of chronic occupational exposure to cadmium. Scand J Resp Dis, 58, 289-303.

Steinnes E, Hanssen JE, Rambaek JP and Vogt NB (1994). Atmospheric deposition of trace elements in Norway: temporal and spatial trends studied by moss analysis. Water, Air and Soil Pollution, 74, 121-140.

Stephens GA.(1920). J.Ind.Hyg., 2, 129-129.

Stephonson M and Turner MA (1993). A field study of cadmium dynamics in periphyton and in Hyalelle azteca (crustacea: amphipoda). Water, Air and Soil Pollution, 68, 341-361.

STIBAT (1998). Battery in M.S.W. : Composition and Characterisation. 1998.

STIBAT (2000). Battery in M.S.W. : Composition and Characterisation. 2000.

STIBAT ( ). Mr. J.Bartels. Director. STIBAT. Boerhaavelaan, 40.Postbus 190.2700 AD Zoetermeer.The Netherlands.

Storm GL, Fosmire GJ and Bellis ED (1994). Persistence of metals in soil and selected vertebrates in the vicinity of the palmerton zinc smelters. Journal of Environmental Quality, 23, 508-514.

Streck T and Richter J (1997). Heavy metal displacement in a sandy soil at the field scale: II. Modeling. Journal of Environmental Quality, 26, 56-62.

Strehlow CD and Barltrop D.(1988). Health Studies. Sci Total Environ, 75, 101-133.

Strickland RC, Chaney WR and Lamoreaux RJ (1979). Organic matter influences phytotoxicity of cadmium to soybeans. Plant Soil, 52, 393-402.

Stubenvoll J., S. Böhmer and I. Szednyj (2002). State of the art for waste incinerator plants. Federal ministry of agriculture and forestry, environment and water management, Austria.

Stuczynski TI, Pistelok F, Siebielec G, Kukla H, Daniels W, Chaney R, Pantuck K (2000). Biological aspects of metal waste reclamation with biosolids in Poland. on In Proc Symposium on Mining, Forest and Land Restoration: The Successful Use of Residuals/Biosolids/Organic Matter for Reclamation Activities (Denver, CO, July 17-20, 2000). Rocky Mountain Water Environment Association, Denver, CO.

Stumm W and Morgan JJ (1996). Aquatic Chemistry, chemical equilibria and rates in natural waters. 3rd ed., 1022 pp. Environmental Science and Technology. Wiley-Interscience, New-York.

Sumino K, Hayakawa K, Shibata T, and Kitamura S.(1975). Heavy metals in normal Japanese tissues. Amounts of 15 heavy metals in 30 subjects. Arch Environ Health, 30, 487-494.

Sunda WG, Engel DW and Thuotte RM (1978). Effect of chemical speciation on toxicity of cadmium to grass shrimp, Palaemonetes pugio: Importance of free cadmium ion. Environmental Science & Technology, 12, 409-413.

Sutou S, Yamamoto K, Sendota H, and Sugiyama M.(1980). Toxicity, Fertility, Teratogenicity, and Dominant Lethal Tests in Rats Administered Cadmium Subchronically. Ecotoxicology and Environmental Safety, 4 , 51-56.

Suzuki CA and Cherian MG.(1987). Renal toxicity of cadmium-metallothionein and enzymuria in rats. J.Pharmacol.Exp.Ther., 240 , 314-319.

Svartengren M, Elinder CG, Friberg L, and Lind B.(1986). Distribution and concentration of cadmium in human kidney. Environ Res, 39, 1-7.

Swedish Products Register on cadmium(oxide) (KEMI, 1997).

Swedish Products Register on cadmium(oxide) (KEMI, 1998).

Tabacova S and Balabaeva L.(1992). Environmental pollutants in relation to complication of pregnancy. Environ Health Perspect, 102, 29-33.

Tabacova S, Little RE, Balabaeva L, Pavlova S, and Petrov I.(1994). Complications of pregnancy in relation to maternal lipid peroxides, glutathione, and exposure to metals. Reprod.Toxicol., 8, 217-224.

Tahvonen R (1996). Contents of lead and cadmium in foods and diets. Food Reviews International, 12, 1-70.

Takahashi K, Imaeda T, and Kawazoe Y. (1988). Effect of metal ions on the adaptive response induced by N-methyl-N- nitrosourea in Escherichia coli. Biochem.Biophys Res Commun., 157, 1124-1130.

Takahashi K, Imaeda T, and Kawazoe Y.(1991). Inhibitory effect of cadmium and mercury ions on induction of the adaptive response in Escherichia coli.

Takenaka S, Glaser U, Oldiges H, and Mohr U.(1990). Morphological effects of CdO-aerosols on the rat lung. Toxicol Environ Chem, 27, 163-172.

Tang W, Sadovic S, and Shaikh ZA.(1998). Nephrotoxicity of cadmium-metallothionein: protection by zinc and role of glutathione. Toxicol Appl Pharmacol, 151, 276-282.

Task Group on Lung Dynamics.(1966). Deposition and retention models for internal dosmietry of the human respiratory tract. Health Phys, 12, 173-208.

Task Group on Metal Accumulation.(1973). Accumulation of toxic metals with special reference to their absorption, excretion and biological halftime. Environ Physiol Biochem, 3, 65-107.

Taylor D (1983). The significance of the accumulation of Cd by aquatic organisms. Ecotoxicology and Environmental Safety, 7, 33-42.

Taylor SA, Jackson MA, Patil D, Burston J, and Lee HA.(1984). Poisoning with cadmium fumes after smelting lead. British Medical Journal, 288, 1270-1271.

Technical notes on cadmium (1991). Cadmium production, properties and uses. Cadmium Association, London. Reedprint Ltd., Windsor, Berkshire, 8 p.

Teculescu DB and Stanescu D.(1970). Pulmonary Function in Workers with Chronic Exposure to Cadmium Oxide Fumes. Int.Arch.Arbeitsmed., 26, 335-345.

Telisman S, Jurasovic J, Pizent A, and Cvitkovic P.(1997). Cadmium in the blood and seminal fluid of nonoccupationally exposed adult male subjects with regard to smoking habits. Int.Arch.Occup.Environ.Health, 70, 243-248.

TGD (1996). Technical Guidance Document in support of Commission Directive 93/67/EEC on Risk Assessment for New Notified Substances and Commission Regulation (EC) N° 1488/94 on Risk Assessment for Existing Substances. ISBN 92-827-8012-0, Luxembourg.

Thiedemann KU, Lüthe N, Paulini I, Kreft A, Heinrich U, and Glaser U.(1989). Ultrastructural observations in hamster and rat lungs after chronic inhalation of cadmium compounds. Exp.Pathol., 37, 264-268.

Thiessen L and Lenelle Y (1990). Evaluation de la teneur en métaux lourds dans l’air en Belgique. Brussels: Institute of Hygiene and Epidemiology; 1985, p. 12 and 1990, p. 17.

Thomas BJ, Harvey TC, Chettle DR, McLellan JS, and Fremlin JH.(1979). A transportable system for the measurement of liver cadmium in vivo. Phys.Med.Biol., 24, 432-437.

Thun MJ, Osorio AM, Schober S, Hannon WH, Lewis B, and Halperin W.(1989). Nephropathy in cadmium workers: assessment of risk from airborne occupational exposure to cadmium. Br J Ind Med, 46, 689-697.

Thun MJ, Schnorr TM, Blair Smith A, Halperin W, and Lemen RA.(1985). Mortality Among a Cohort of U.S. Cadmium Production Workers- an Update. JNCI, 74, 325-333.

Thürauf J, Schaller KH, Valentin H, and Weltle D.(1981). Current cadmium load in the population. Comparison of cadmium concentrations in the kidney tissue of autopsies from 1969-1980. Fortschr Med, 99, 1312-1317.

Thürauf J, Schaller KH, Valentin H, Weltle D, Grote K, and Schellmann B.(1986). Cadmium concentrations in autopsy material from differently polluted areas of Wesr Germany (FRG). Zbl.Bakt.Hyg.B, 182, 337-347.

Tiller KG (1989). Heavy metals in soils and their environmental significance. Advances in Soil Science, 9, 113-142.

Tiller KG, Oliver DP, McLaughlin MJ, Merry RH and Naidu R (1994). Managing cadmium contamination of agricultural land. In: Advances in Environmental Sciences: ‘Biogeochemistry of Trace Metals, 2’. In press

Tiran B, Karpf E, and Tiran A.(1995). Age dependency of selenium and cadmium content in human liver, kidney, and thyroid. Arch Environ Health, 50, 242-246.

Tjell JC and Christensen TH (1985). Evidence of increasing cadmium contents of agricultural soils. In: Heavy Metals in the Environment, Volume 2 (T.D. Lekkas, ed.). CEP Consultants, Edinburgh, UK.

Tjell JC and Christensen TH (1992). Sustainable management of cadmium in Danish agriculture. In: Impact of Heavy Metals on the Environment (J.P. Vernet ed.). Elsevier, Amsterdam.

Tjell JC and Hovmand MF (1978). Metal concentrations in Danish arable soils. Acta Agriculturae Scandinavica, 28, 81-89.

TMO-CSA (2001). Quantitative hoarding study of electrical and electronic equipment and of portable rechargeable batteries in France. Summary draft, April 2001.

Toffoletto F, Apostoli P, Ghezzi I, Baj A, Cortona G, Rizzi L, and Alessio L.(1992).Ten-year follow-up of biological monitoring of cadmium-exposed workers. In:Cadmium in the human environment: Toxicity and Carcinogenicity. Edited by GF Nordberg, RFM Herber, and L Alessio. IARC, International Agency for Research on Cancer. Lyon

Tohyama C, Shaikh ZA, Nogawa K, Kobayashi E, and Honda R.(1981). Elevated urinary excretion of metallothionein due to environmental cadmium exposure. Toxicology, 20, 289-297.

Townshend RH.(1968). A case of acute cadmium pneumonitis : lung function tests during a four-year follow-up. Br J Ind Med, 25, 68-71.

Townshend RH.(1982). Acute cadmium pneumonitis : a 17-year follow-up. Br J Ind Med, 39, 411-412.

Toxicological Profile for Cadmium: Draft for Public Comment. Anonymous Agency for Toxic Substances and Disease Registry. Atlanta, Georgia 30333:U.S. Department of Health & Human Services, Public Health Service, 1998.

Trottier B, Athot J, Ricard AC, and Lafond J.(28-3-2002). Maternal--fetal distribution of cadmium in the guinea pig following a low dose inhalation exposure. Toxicol Lett, 129, 189-197.

Trzcinka-Ochocka M, Jakubowski M, Halatek T, and Razniewska G.(2001). Reversibility of microproteinuria in nickel-cadmium battery workers after removal from exposure. 54-

Tsoumbaris P and Tsoukali-Papadopoulou H (1994). Heavy metals in common foodstuff: daily intake. Bulletin of Environmental Contamination and Toxicology, 53, 67-70.

Tsuchiya K and Iwao S.(1978). Interrelationships among zinc, copper, lead, and cadmium in food, feces, and organs of humans. Environ Health Perspect, 25, 119-124.

Tsuchiya K.(1967). Proteinuria of workers exposed to cadmium fume. The relationship to concentration in the working environment. Arch Environ Health, 14, 875-880.

Tsuchiya K.(1976). Proteinuria of cadmium workers. J Occup Med, 18, 463-466.

Tsuchiya K.(1978). Cadmium Studies in Japan: A Review. Edited by K Tsuchiya, SK Sted, and CM Hamagami. Kodansha, Elsevier. Tokyo,

Tsuchiya K.(1992). Health effects of cadmium with special reference to studies in Japan. IARC.Sci.Publ., 35-49.

Tsuritani I, Honda R, Ishizaki M, Yamada Y, and Nishijo M.(1996). Ultrasonic assessment of calclaneus in inhabitants in a cadmium- polluted area. J Toxicol Environ Health, 48, 131-140.

Tsuritani I, Honda R, Ishizaki M, Yamada Y, Aoshima K, and Kasuya M.(1994). Serum bone-type alkaline phosphatase activity in women living in a cadmium-polluted area. Toxicology Letters, 71, 209-216.

Tsvetkova RP.(1970). Materials on the study of the influence of cadmium compounds on the generative function. Gig Tr Prof Zabol, 14, 31-33.

Turbak SC, Olson SB and Mcfeters GA (1986). Comparison of algae assay systems for detecting waterborne herbicides and metals. Water Research, 20, 91-96.

UBA (Umweltbundesamt) (2001). Daten zur Umwelt. Der Zustand der Umwelt in Deutschland 2000. Erich Schmidt Verlag, Berlin. ISBN 3-503-05974-1 (CD-ROM).

UBA (Umweltbundesamt) (2001). Grundsätze und Maßnahmen für eine vorsorgeorientierte Begrenzung von Schadstoffeinträgen in landbaulich genutzten Böden. UBA-Texte 59/01.

UBA (Umweltbundesamt) (2001). Pers. com. within comments to April (?) version of TRAR, 2001.

UBA (Umweltbundesamt) (2002). Comments to the ‘global’ RA on Cd/CdO, 21.05.02.

UBA (Umweltbundesamt) (1996). Eintrag von Blei, cadmium und quecksilber in die Umwelt. Umweltforschungsplan des Bundesministers für Umwelt, Naturschutz und Reaktorsicherheit. Forschungsbericht 106 01 047.

U.B.F. (Umwelt Batterien Forum) (2000). Sorting campaign of spent batteries in Municipal Solid Waste. Reported by Rumpold AG. Mr. F.Richter. Roseggergasse,4. A-8793 Trofaiach. franz.richter@rumpold.at

Ulander A and Axelson O.(1974). Measurement of blood-cadmium levels. Lancet, 682-683.

Umemura T.(2000). Experimental reproduction of itai-itai disease, a chronic cadmium poisoning of humans, in rats and monkeys. Jpn.J Vet.Res., 48, 15-28.

Union Minière (1998): Information given during the visit to the cadmium production plant in Balen (Belgium). A. Delen, J. Tegenbos, M. De Groof.

Uriu K, Morimoto I, Kai K, Okazaki Y, Okada Y, Qie YL, Okimoto N, Kaizu K, Nakamura T, and Eto S.(1-5-2000). Uncoupling between bone formation and resorption in ovariectomized rats with chronic cadmium exposure. Toxicol Appl Pharmacol, 164, 264-272.

US EPA (1985). Freshwater algae acute toxicity test . Fed. Register 50, 39, 323-339.

US EPA (1991). Methodology for assessing environmental releases of and exosure to municipal solid waste combustor residuals, US Environmental Protection Agency, Report EPA/600/8-91/031

US EPA (1993). Locating and estimating air emissions from sources of cadmium and cadmium compounds. US Environmental Protection Agency, Report EPA-454/R-93-040.

US-EPA (1989). Development of risk assessment methodology for land application and distribution of and marketing of municipal sludge. EPA/600/6-89/001.

US-EPA (1993). 40 CFR Part 257 et al. Standards for the use or disposal of sewage sludge; final rules. Fed. Reg. 58(32):9248-9415.

US-EPA (2000). Update of ambient water quality criteria for cadmium. Draft, EPA Contract No. 68-C-98-134, Work Assignment No. 1-11.

US-EPA (2001). Update of ambient water quality criteria for cadmium. EPA-822-R-01-001.

USGS (1998). Mineral Commodity Summaries 1998, US Geological Survey, January 1998.

Vahter M, Berglund M, Lind B, Jorhem L, Slorach S, and Friberg L.(1991). Personal monitoring of lead and cadmium exposure-a Swedish study with special reference to methodological aspects. Scand J Work Environ Health, 17, 65-74.

Vahter M, Berglund M, Nermell B and Åkesson A (1996). Bioavailability of cadmium from shellfish and mixed diet in women. Toxicology and applied pharmacology, 136, 332-341.

Vahter M, Berglund M, Slorach S, Friberg L, Saric M, Zheng XQ, and Fujita M.(1991). Methods for integrated exposure monitoring of lead and cadmium. Environ Res, 56, 78-89.

Vahter M, Berglund M, Slorach S, Jorhem L, and Lind B.(1992).Integrated personal monitoring of cadmium exposure in Sweden. In:Cadmium in the Human Environment: Toxicity and Carcinogenicity. Edited by GF Nordberg, RFM Herber, and L Alessio. IARC, International Agency for Research on Cancer. Lyon, 113-119.

Vahter M.(1982). Assessment of Human Exposure to Lead and Cadmium through Biological Monitoring.

Valetas P.(1946). Cadmiose or Cadmium Intoxication.

Van Assche F (1998). The relative contribution of different environemental sources to human cadmium exposure and the EU risk assessment. Paper presenten on the NiCd workshop, Prague, September 21-22.

Van Assche F and Ciarletta P (1993). Environmemental exposure to cadmium in Belgium: decreasing trends during the 1980s. In: Heavy Metals in the Environment, Proceedings of the 9th International Conference, Volume I (R.J., Allen and J.O., Nriagu, Eds.) 34-37.

Van de Wijdeven (1991). Beoordelingsstudie inertisatie van reststoffen van afvalverbrandingsinstallaties en van zuiveringsslibvebrandingsgas. Utrecht. The Netherlands. Novem report 90369.

van den Berg GA, Loch JPG, van der Heijdt LM and Zwolsman JJG (1998). Vertical distribution of AVS and simultaneously extracted metals in a recent sedimentation area of the river Meuse in the Netherlands. Environmental Toxicology and Chemistry, 17, 758-763.

van der Poel P. (1999). Supplement to the Uniform Sysyem for the Evaluation of Substances (USES). Emission scenarios for waste treatment (elaborated for biocides). RIVM report 601450 003.

van Dokkum W (1995). The intake of selected minerals and trace elements in European countries. Nutrition Research Reviews, 8, 271-302.

van Driel W and Smilde KW (1982). Heavy-metal contents of Dutch arable soils. Landwirtschaftlich Forsung Sonderheft, 38, 305-313.

van Gestel CAM and Hensbergen PJ (1997). Interaction of Cd and Zn toxicity for Folsomia candida Willem (Collembola : Isotomidae) in relation to bioavailability in soil. Environmental Toxicology and Chemistry, 16, 1177-1186.

van Gestel CAM and van Diepen MF (1997). The influence of soil moisture content on the bioavailability and toxicity of cadmium for Folsomia candida willem (Collembola: Isotomidae). Ecotoxicology and Environmental Safety, 36, 123-132.

van Gestel CAM and van Dis WA (1988). The influence of soil characteristics on the toxicity of four chemicals to the earthworm Eisenia fetida andrei (Oligochaeta). Biology and Fertility of Soils, 6, 262-265.

van Gestel CAM, Dirven-van Breemen EM and Baerselman R (1993). Accumulation and elimination of cadmium, chromium and zinc and effects on growth and reproduction in Eisenia andrei (Oligochaeta; Annelida), The Science of the Total Environment, Supplement, 585-597.

van Gestel CAM., van Dis WA, Dirven-van Breemen EM, Sparenburg PM and Baerselman R (1991). Influence of cadmium, copper, and pentachlorophenol on growth and sexual development of Eisenia fetida (Oligochaeta; Annelida). Biology and Fertility of Soils, 12, 117-121.

Van Hattum B, De Voogt P, and Copius Peereboom JW.(1981). An analytical procedure for the determination of cadmium in human placentae. Intern.J.Environ.Anal.Chem., 10, 121-133.

van Hattum B, de Voogt P, van den Bosch L, van Straalen NM and Joosse ENG (1989). Bioaccumulation of cadmium by freshwater isopod Asellus aquaticus (L.) from aqeous and dietary sources. Environmental Pollution, 62, 129-151.

van Hattum B, Korthals G, van Straalen NM, Govers HAJ and Joosse ENG (1993). Accumulation patterns of trace metals in freshwater isopods in sediment bioassays - Influence of substrate characteristics, temperature and pH. Water Research, 27, 669-684.

Van Hook RI (1974). Cadmium, lead and zinc distributions between earthworms and soils: potential for biological accumulation. Bulletin of Environmental Contamination and Toxicology, 12, 509-512.

Van Leeuwen CJ, Luttmer WJ and Griffioen PS (1985). The use of cohorts and populations in chronic toxicity studies with Daphnia magna: a cadmium example. Ecotoxicology and Environmental Safety, 9, 26-39.

van Sittert NJ.(1992). A 9 year follow-up renal function study of workers exposed to cadmium in a zinc ore refinery. HSE Reports 92.001.,

Venugopal NBRK, Ramesh TVDD, Reddy DS and Reddy SLN (1997). Effect of cadmium on antioxidant enzyme activities and lipid peroxidation in a freshwater field crab Barytelphusa guerini. Bulletin of Environmental Contamination and Toxicology, 59, 132-138.

Verhagen & Meijer (2000). Monitoring Prioritaire Afvalstoffen. Gegevens 1998.

Verschoor M, Herber RF, van Hemmen J, Wibowo A, and Zielhuis RL.(1987). Renal function of workers with low-level cadmium exposure. Scand J Work Environ Health, 13, 232-238.

Verstraete W. (2003). Pers. com., tel. 3.02.03.

VIBNA (1994). Evolutie van de kwaliteit van het scheldewater. Vereniging van de Industriële Bedrijven van Noord-Antwerpen, Antwerpen, Belgium.

Vinyl 2010 (2002). The Voluntary Commitment of the PVC Industry. Progress Report.

VLAREA (1998). Vlaams reglement inzake afvalvoorkoming en -beheer (VLAREA). OVAM, D/1998/5024/2

VLAREBO (1996). Vlaams reglement betreffende de bodemsanering. 63pp. In Dutch. Publication number D/1996/5024/5. Openbare Vlaamse Afvalstoffen Maatschappij, Mechelen, Belgium.

VMM (1997). Evaluatie van de gehalten zware metalen in zwevende stof in Vlaanderen. Vlaamse Milieumaatschappij, Belgium.

VMM (1999). Meetresultaten "Deposities Cd (1989-1997) te Knokke".

VMM (2004). Luchtkwaliteit in het Vlaams Gewest 2003. VMM, Erembodegem, 2004.

VROM (1997): Componentenonderzoek AVI input, Publicatiereeks Afvalstoffen nr, 1997/37; VROM. Information on 4 Incinerators in the Netherlands.

VROM/DGM/SVS (J. Pearse) (1996). Cadmium. Some aspects of risk reduction. Report nr. SVS 1996/32. Distributiecentrum VROM, Zoetermeer. 158 pp.

Vuori E, Huunan-Seppala A, Kiplio JO, and Salmela SS.(1979). Biologically active metals in human tissues. II The effects of age on the concentration of cadmium in aorta, heart, kidney, liver, lung, pancreas, and skeletal muscle. Scand J Work Environ Health, 5, 16-22.

VVAV (2000). Afvalverwerking in Nederland, gegevens 1999, rapportnummer VVAV00007IR.R

Waalkes MP and Goering PL.(1990). Metallothionein and other cadmium-binding proteins: recent developments. Chem.Res.Toxicol., 3, 281-288.

Waalkes MP and Oberdörster G.(1990).Cadmium Carcinogenesis. In:Biological Effects of Heavy Metals, Vol.II, Metal Carcinogenesis. Edited by EC Foulkes. CRC Press. Boca Raton, Florida, 129-158.

Waalkes MP, Anver MR, and Diwan BA.(29-10-1999). Chronic toxic and carcinogenic effects of oral cadmium in the Noble (NBL/Cr) rat: induction of neoplastic and proliferative lesions of the adrenal, kidney, prostate, and testes. J Toxicol Environ Health A, 58, 199-214.

Wahlberg JE and Boman A.(1979). Guinea pig maximisation method-cadmium chloride. Contact Dermatitis, 3, 293-296.

Wahlberg JE. (1965). Percutaneous toxicity of metal compounds. Arch.Environ Health, 11, 201-204.

Wahlberg JE. (1977). Routine patch testing with cadmium chloride. Contact Dermatitis, 3, 293-296.

Wahle (1932). Zbl.GewHyg., 19, 223-223.

Walker (1995). Estimation of cadmium discards in Municipal Solid Waste. In: Proceedings of the OECD workshop on Sources of Cadmium in The Environment, Saltsjöbaden, Sweden, 16-20 october 1995, p. 415-450.

Walter C and Stadelmann F (1979). Influence du zinc et du cadmium sur les microorganismes ainsi que sur quelques processus biochimiques du sol. Schweizerische Landwirtschaftliche Forschung, 18, 311-324.

Wang C and Bhattacharyya MH.(1993). Effect of cadmium on bone calcium and 45Ca in nonpregnant mice on a calcium-deficient diet: evidence of direct effect of cadmium on bone. Toxicol Appl Pharmacol, 120, 228-239.

Ward RJ, Fisher M, and Tellez-Yudilevich M.(1978). Significance of blood cadmium concentrations in patients with renal disorders or essential hypertension and the normal population. Ann Clin Biochem, 15, 197-200.

Warnick SL and Bell HL (1969). The acute toxicity of some heavy metals to different species of aquatic insects. Journal of Water Pollution Control Federal, 41, 280-284.

Watanabe T, Koizumi A, Fujita H, Kumai M, and Ikeda M.(1983). Cadmium levels in the blood of inhabitants in non-polluted areas in Japan with special references to aging and smoking. Environ Res, 31, 472-483.

Webb M and Samarawickrama GP.(1981). Placental transport and embryonic utilization of essential metabolites in the rat at the teratogenic dose of cadmium. J.Appl.Toxicol., 1, 270-277.

Webber J (1973). Uptake of cadmium by crops. Pp. 13-14. In: Cadmium in the environment: report of a seminar held at Alhambra House, Charing Cross Road, 15 March, 1973. London.

Webster WS.(1978). Cadmium-induced fetal growth retardation in the mouse. Arch.Environ Health, 33, 36-42.

Webster WS.(1979). Cadmium-induced fetal growth retardation in mice and the effects of dietary supplements of zinc, copper, iron and selenium. J.Nutr., 109, 1646-1651.

Weigel HJ, Jäger HJ, and Elmadfa I.(1984). Cadmium Accumulation in Rat Organs After Extended Oral Administration with Low Concentrations of Cadmium Oxide. Arch Environ Contam Toxicol, 13, 279-287.

Weigert P, Muller J, Klein H, Zufelde KP and Hillebrand J (1984). Arsen, Blei, Cadmium und Quecksilber in und auf Lebensmitteln. ZEBS Hefte 1. (Federal Republic of Germany).

Wesselink (1995). Relatie uitlooggedrag laboratorium-praktijk bij wegenbouwkundige projecten. Geo-chemische modellering uitlooggedrag vliegas Vondelingenweg en AVI-bodemas Coloradoweg, Rotterdam. RIVM report 771402016.

Wester RC, Maibach HI, Sedik L, Melendres J, DiZio S, and Wade M.(1992). In vitro percutaneous absorption of cadmium from water and soil into human skin. Fundam.Appl.Toxicol., 19, 1-5.

Whelton BD, Bhattacharyya MH, Carnes BA, Moretti ES, and Peterson DP.(1988). Female reproduction and pup survival and growth for mice fed a cadmium-containing purified diet through six consecutives rounds of gestation and lactation. J Toxicol Environ Health, 24, 321-343.

Whelton BD, Bhattacharyya MH, Peterson DP, Moretti ES, Toomey JM, and Williams LL.(1994). Skeletal changes in multiparous and nulliparous mice fed a nutrient-deficient diet containing cadmium. Toxicology, 91, 235-251.

Whelton BD, Peterson DP, Moretti ES, Mauser RW, and Bhattacharyya MH.(1997). Kidney changes in multiparous, nulliparous and ovariectomized mice fed either a nutrient-sufficient or -deficient diet containing cadmium. Toxicology, 119, 123-140.

Whelton BD, Toomey JM, and Bhattacharyya MH.(1993). Cadmium-109 Metabolism in Mice.IV.Diet versus Maternal Stores as a Source of Cadmium Transfer to Mouse Fetuses and Pups During Gestation and Lactation. J Toxicol Environ Health, 40, 531-546.

White DH, Finley MT and Ferrell JF (1978). Histopathologic effects of dietary cadmium on kidneys and testes of mallard ducks. Journal of Toxicology and Environmental Health, 4, 551-558.

White MA and Sabbioni E.(1998). Trace element reference values in tissues from inhabitants from the European union.X. A study of 13 elements in blood and urine of a United Kingdom population. Sci Total Environ, 216, 253-270.

WHO (World Health Organisation).(1992). Cadmium. Environmental Health Criteria 134. WHO, Geneva.

WHO (1996) Guidelines for drinking water quality. Volume 2 : health Criteria and other supporting information. World Health Organization, p.200.

WHO (1996). Biological Monitoring of Chemical Exposure in the Workplace. Guidelines Vol.1.

WHO (2000). World Health Organization. Air quality guidelines for Europe. WHO Regional Publ. European Series N° 91.

Wiaux J.P. (1997). La reduction des flux en metaux lourds contenus dans les ordures menageres par le tri selectif des piles usagees. 12p

Wibowo AA, Herber RF, van Deyck W, and Zielhuis RL.(1982). Biological assessment of exposure in factories with second degree usage of cadmium compounds. Int.Arch.Occup.Environ.Health, 49, 265-273.

Wiener JG and Giesy JP Jr. (1979). Concentrations of Cd, Cu, Mn, Pb, and Zn in fishes in a highly organic softwater pond. Journal of the Fisheries Research Board of Canada., 36, 270-279.

Wier CF and Walter WM (1976). Toxicity of cadmium in the freshwater snail, Physa gyrina Say. Journal of Environmental Quality, 5, 359-362.

Wier PJ, Miller RK, Maulik D, and di Sant'Agnese PA.(1990). Toxicity of cadmium in the perfused human placenta. Toxicol Appl Pharmacol, 105, 156-171.

Wiersma D, van Goor BJ and van der Veen NG (1986). Cadmium, lead, mercury and arsenic concentrations in crops and corresponding soils in The Netherlands. Journal of Agricultural Food Chemistry, 34, 1067-1074.

Wilhelm M, Hafner D, Lombeck I, and Ohnesorge FK.(1988). Variables influencing cadmium concentrations in hair of pre- school children living in different areas of the Federal Republic of Germany. Int.Arch.Occup.Environ.Health, 60, 43-50.

Wilhelm M, Lombeck I, Kouros B, Wuthe J and Ohnesorge F-K (1995). Duplikatstudie zur alimentären Aufnahme von einigen Metallen/Metalloiden bei Kindern in Deutschland. Teil II: Aluminium, Cadmium und Blei. Zbl. Hyg., 197, 357-369.

Willers S, Attewell R, Bensryd I, Schütz A, Skarping G, and Vahter M.(1992). Exposure to Environmental Tobacco Smoke in the Household and Urinary Cotinine Excretion, Heavy Metals Retention, and Lung Function. Arch Environ Health, 47, 357-363.

Willers S, Schütz A, Attewell R, and Skerfving S.(1988). Relation between lead and cadmium in blood and the involuntary smoking of children. Scand J Work Environ Health, 14, 385-389.

Williams KA, Green DWJ and Pascoe D (1985). Studies on the acute toxicity of pollutants to freshwater macroinvertebrates. I. Cadmium. Archives in Hydrobiology, 102, 461-471.

Williams P.T. (1998). Waste treatment and disposal. John Wiley and Sons. 407 p.

Wilson AK and Bhattacharyya MH.(1997). Effects of cadmium on bone: an in vivo model for the early response. Toxicol Appl Pharmacol, 145, 68-73.

Wilson AK, Cerny EA, Smith BD, Wagh A, and Bhattacharyya MH.(1996). Effects of cadmium on osteoclast formation and activity in vitro. Toxicol Appl Pharmacol, 140, 451-460.

Winner RW (1988). Evaluation of the relative sensitivities of 7-D Daphnia magna and Ceriodaphnia dubia toxicity tests for cadmium and sodium pentachlorophenate. Environmental Toxicology and Chemistry, 7, 153-159.

Winner RW and Gauss J (1986). Relationship between chronic toxicity and bioaccumulation of copper, cadmium and zinc as affected by water hardness and humic acid. Aquatic Toxicology, 8, 149-161.

Winston RM.(1971). Cadmium Fume Poisoning. British Medical Journal, 2, 401-401.

Wisniewska-Knypl JM, Jablonska J, and Myslak Z.(1971). Binding of cadmium on metallothionein in man: An analysis of a fatal poisoning by cadmium iodide. Arch Toxicol, 28, 46-55.

Witzenhausen Intstitut (2001). Batterien im Hausmull. Cited in Allgaier and Stegmann (2004), Untersuchungen zum batteriefluss in den restmüllbehandlungsverfahren MBA und MVA sowie der auswirkungen auf die verwertungsrelevanten metallschrottfraktionen.

Witzenhausen Institut (2004). Cost analysis for the monitoring of Nickel-Cadmium batteries in municipal solid waste. Analysis of the Argus study.

Wolfsperger M, Hauser G, Gossler W, and Schlagenhaufen C.(1994). Heavy metals in human hair samples from Austria and Italy: influence of sex and smoking habits. Sci Total Environ, 156, 235-242.

Wong PTS, Burnison G and Chau YK (1979). Cadmium toxicity to freshwater algae. Bulletin of Environmental Contamination and Toxicology, 23, 487-490.

World Bureau of Metal Statistics (2000). World metal statistics yearbook 2000. World Bureau of Metal Statistics, 73 p.

Wright MA and Stringer A (1980). Lead, zinc and cadmium content of earthworms from pasture in the vicinity of an industrial smelting complex. Environmental Pollution Series A, 23, 313-321.

WS Atkins International Ltd. (1998a). Assessment of the risks to health and to the environment of cadmium contained in certain products and of the effects of further restrictions on their marketing and use. Final Report for the European Commission, dated September 1998.

WS Atkins International Ltd. (1998b). Additional assessment of the risks to health and to the environment of cadmium contained in certain products and of the effects of further restrictions on their marketing and use. Final Report for the European Commission, dated September 1998.

Wulf HC, Kromann N, Kousgaard N, Hansen JC, Niebuhr E, and Alboge K.(1986). Sister chromatid exchange (SCE) in Greenlandic Eskimos. Dose-response relationship between SCE and seal diet, smoking, and blood cadmium and mercury concentrations. Sci.Total Environ, 48, 81-94.

Wulff M, Högberg U, and Sandström A.(1995). Perinatal outcome among the offspring of employees and people around a Swedish smelter. Scand J Work Environ Health, 21, 277-282.

Xu B, Chia SE, Tsakok M, and Ong CN.(1993). Trace Elements in Blood and Seminal Plasma and Their Relatopnship to Sperm Quality. Reprod.Toxicol., 7, 613-618.

Yamanaka O, Kobayashi E, Nogawa K, Suwazono Y, Sakurada I, and Kido T.(1998). Association between renal effects and cadmium exposure in cadmium-nonpolluted area in Japan. Environ Res., 77, 1-8.

Yoshikawa H and Homma K.(1974). Japan.J.Ind.Health, 16, 212-212.

Yoshikawa H, Kawai K, Suzuki Y, Nozaki K, and Ohsawa M.(1975). Studies on cadmium effects in living organisms: impairment due to inhalation.

Yoshikawa H.(1973). Preventive effects of pretreatment with cadmium on acute cadmium poisoning inrats. Ind.Health, 11, 113-119.

Zasukhina GD and Sinel'shchikova TA.(1976). [Mechanism of action of mutagens on human cell DNA]. Dokl.Akad.Nauk SSSR, 230, 719-721.

Zavon MR and Meadows CD.(1970). Vascular Sequelae to Cadmium Fume Exposure. Am Ind Hyg Assoc J, 31, 180-182.

Zeiger E, Anderson B, Haworth S, Lawlor T, and Mortelmans K.(1992). Salmonella mutagenicity tests: V. Results from the testing of 311 chemicals. Environ Mol Mutagen, 19, 2-141.

Zenick H, Hastings L, Goldsmith M, and Nieuwenhuis RJ.(1982). Chronic cadmium exposure: relation to male reproductive toxicity and subsequent fetal outcome. J Toxicol Environ Health, 9, 377-387.

Zhang ZW, Moon CS, Watanabe T, Shimbo S, and Ikeda M.(1997). Contents of pollutant and nutrient elements in rice and wheat grown on the neightboring fields. Biol Trace Elem Res, 57, 39-50.

Zhuang Y, Allen HA and Fu G (1994). Effect of aeration of sediment on Cd binding. Environmental Toxicology and Chemistry, 13, 717-724.

Zielhuis RL, del Castilho P, Herber RF, Wibowo AA, and Sallé HJ.(1979). Concentrations of Lead and Other Metals in Blood of Two and Three Year-Old Children Living Near a Secondary Smelter. Int.Arch.Occup.Environ.Health, 42, 231-239.

Zielhuis RL, Struik EJ, Herber RF, Sallé HJ, Verbeerk MM, Posma FD, and Hager JH.(1977). Smoking habits and levels of lead and cadmium in blood in urban women. Int.Arch.Occup.Environ.Health, 39, 53-58.

Zuurdeeg BW et al. (1992). Natuurlijke achtergrondgehalten van zware metalen en enkele andere spoorelementen in Nederlands oppervlaktewater. (in Dutch). Geochem-Research, Utrecht. Project Number VROM/DGM/AMS 361346.

Zwarun AA (1973). Tolerance of Escherichia coli to Cd. Journal of Environmental Quality, 2, 353-355.

# GLOSSARY

| Standard term / Abbreviation | Explanation/Remarks and Alternative Abbreviation(s) |
| --- | --- |
| , | Comma is used to indicate thousands |
| . | Point is used to indicate decimals |
| AC | Active Carbon |
| AF | assessment factor |
| Ann. | Annex |
| Ann. | annual |
| Avg. | average |
| AVS | Acid Volatile Sulphides |
| BCF | bioconcentration factor |
| BDS | Biological DeSulfurisation |
| BOD5 | Biological oxygen demand (to complete….) |
| bw | body weight / Bw, b.w. |
| °C | degrees Celsius (centigrade) |
| C50 | median immobilisation concentration or median inhibitory concentration 1 / explained by a footnote if necessary |
| CAS | Chemical Abstract System |
| Cd | Cadmium (metal) |
| CdO | cadmium oxide |
| CEC | Commission of the European Communities |
| CEN | European Committee for Normalisation |
| CEPE | European Council of the Paint, Printing Ink and Artists’ Colours Industry |
| COD | Chemical oxygen demand |
| CPT | Cordless power tools |
| d | day(s) |
| dl | Detection limit |
| DF | Dilution factor |
| DG | Directorate General |
| DRY | Dry flue air cleaning technique |
| DT50 | period required for 50 percent dissipation (define method of estimation) |
| DT50lab | period required for 50 percent dissipation under laboratory conditions (define method of estimation) |
| DT90 | period required for 90 percent dissipation (define method of estimation) |
| DT90field | period required for 90 percent dissipation under field conditions (define method of estimation) |
| Dry wt. | dry weight / dw / DW / d.wt |
| EC | European Communities |
| EC | European Commission |
| EC50 | median effective concentration |
| EEC | European Economic Community |
| EEE | Electrical and Electronic Equipment |
| EEIG | Abbreviation for former ‘Industry’s Interest Group’ working on Ni-Cd batteries |
| EINECS | European Inventory of Existing Commercial Chemical Substances |
| ELU | Emergency Lighting Units |
| EPA | Environmental Protection Agency |
| EU | European Union |
| EU-16 | Member states of the EU AND Norway |
| EUSES | European Union System for the Evaluation of Substances |
| ESP | Electrostatic precipitator (air cleaning technique) |
| FF | Fabric Filter (air cleainign technique) |
| FGCS | Flue Gas Cleaning System |
| Fww | Release factor to wastewater |
| foc | Fraction of organic carbon |
| g | gram(s) |
| Global RAR | EU RAR on cadmium metal and cadmium oxide / overall RAR on Cd/CdO |
| GLP | Good Laboratory Practice |
| h | hour(s) |
| ha | Hectares / h |
| HDPE |  |
| HELP | Hydrologic Evaluation of Landfill Production (US-EPA model see Schroeder) |
| HPLC | High Pressure Liquid Chromatography |
| IARC | International Agency for Research on Cancer |
| ICP | Inductively Coupled Plasma |
| IC50 | median immobilisation concentration or median inhibitory concentration 1 / explained by a footnote if necessary |
| ICdA | International Cadmium Association |
| IND | Industry |
| IPPC | Integrated Pollution Prevention and Control |
| ISO | International Standards Organisation |
| IUPAC | International Union for Pure Applied Chemistry |
| IUTA | Institut für Energie- und Umwelttechnik |
| IZA | International Zinc Association |
| J | Joule |
| kg | kilogram(s) |
| kPa | kilo Pascals |
| Koc | organic carbon adsorption coefficient |
| Kow | octanol-water partition coefficient |
| Kp | Solids water partition coefficient |
| kt | Kilotonnes / ktonnes |
| L | litre(s) / l |
| log | logarithm to the basis 10 |
| L(E)C50 | Lethal Concentration, Median |
| LEV | Local Exhaust Ventilation |
| m | Meter |
| µg | microgram(s) |
| mg | milligram(s) |
| MAC | Maximum Acceptable Concentration |
| Model I (soil) | Standard EUSES model calculation |
| Model II (soil) | The alternative model to calculate regional and continental concentrations in agricultural soil is based on the Cd mass balance in the plough layer (cfr section 3.1.2.4.2 of the ‘global’ RAR on Cd/CdO) |
| MOS | Margins of Safety |
| MS | Member states |
| MSR | Member state Rapporteur / RMS |
| MSW | Municipal Solid Waste |
| N/A | Not applicable / n.a. |
| n.d. | No data available |
| ng | Nanograms (to complete with conversion factor to grams) |
| Ni | Nickel |
| Ni-Cd | Nickel-cadmium batteries / NiCd |
| NIVA | Norwegian Institute for Water Research |
| NOAEL | No Observed Adverse Effect Level |
| NOEC | No Observed Effect Concentration |
| NOEL | No Observed Effect Level |
| oc | Organic carbon |
| OECD | Organisation for Economic Co-operation and Development |
| OEL | Occupational Exposure Limit |
| OEM | Original Equipment Manufacturer |
| OJ | Official Journal |
| OPS model | Operational Priority Substances model |
| Pa | Pascal unit(s) |
| P90 | 90-percentile of a dataset (result of statistical analysis: 90% of the values in the dataset are situated below the P90) |
| PBE | Plastic Bonded Electrode |
| PEC | Predicted Environmental Concentration |
| pH | potential hydrogen -logarithm (to the base 10) of the hydrogen ion concentration {H+} |
| pKa | -logarithm (to the base 10) of the acid dissociation constant |
| pKb | -logarithm (to the base 10) of the base dissociation constant |
| PM10 | Fine particulate matter (<10 µm) |
| PNEC(s) | Predicted No Effect Concentration(s) |
| PNECwater | Predicted No Effect Concentration in Water |
| (Q)SAR | Quantitative Structure Activity Relationship |
| Questionnaire | To collect the needed information different types of questionnaires were used dependent on the aim and the target group: Industry questionnaire: for the collection of site-specific exposure data of batteries’ producers and recyclers. The initial questionnaire was sent out by Industry in 1998, updates by the rapporteur in 2000 and 2001. The Questionnaire on Batteries : was designed by the rapporteur to obtain information related to the amounts of batteries (i.e. Ni-Cds) put on the market, collection, recycling etc on a country basis. Three subtypes were made depending on the responder: a) Member state (competent authority for the implementation of the Battery Directive); b) Collection organisation (per country) and c) EPBA. This questionnaire was sent out in 2000. |
| RAR | Risk assessment report |
| RCR | Risk Characterisation Ratio |
| SCTEE | Scientific Committe on Toxicity, Ecotoxicity and the Environment / CSTEE |
| SEM | Simultaneously extracted metal |
| SRB | Sulphate Reducing Bacteria |
| STP | Sewage Treatment Plant |
| St. dev. | Standard deviation |
| t | Metric tonnes / tonnes / T |
| TGD | Technical Guidance Document |
| Revised TGD | Technical Guidance Document |
| TMT | Trimercaptotriazine (flocculans used in wastewater purification) |
| TOC | Total organic carbon |
| TRAR | Targeted Risk Assessment Report (this report) |
| UASB | Upflow Anaerobic Sludge Blanket |
| UV | Ultraviolet Region of Spectrum |
| UVCB | Unknown or Variable composition, Complex reaction products or Biological material |
| v/v | volume per volume ratio |
| VDI | Verein Deutscher Ingenieure |
| w/w | weight per weight ratio |
| w | gram weight |
| WET | Wet scrubbing (air cleaning technique) |
| WWTP | Wastewater Treatment Plant |
| Wet wt. | Wet weight / WW / ww |
| y | Year |

# annexes

Annex 1.4.2.A: 	Dissolution/transformation test: cadmium metal powder: Summarised description of test parameters in LISEC tests with cadmium metal powder

Annex 1.4.2.B: 	Dissolution/transformation test: cadmium metal powder: Results of all LISEC tests (1-3) with cadmium metal powder

Annex 1.4.2.C: 	Dissolution/transformation test: massive cadmium metal: Summarised description of test parameters in LISEC tests with cadmium metal (massive form: shots)

Annex 1.4.2.D: 	Dissolution/transformation test: massive cadmium metal: Results of all LISEC tests (1-3) with massive cadmium metal (shots)

Annex 1.4.2.E: 	Dissolution/transformation test: cadmium oxide : Summarised description of test parameters in LISEC tests with cadmium oxide

Annex 2.1.3.1: 	The occurrence of cadmium (metal) in products according to the Swedish product register.

Annex 1.4.2.F: 	Dissolution/transformation test: cadmium oxide powder: Results of all LISEC tests (1-2) with cadmium oxide powder

Annex 2.1.3.2: 	The occurrence of cadmium oxide in products according to the Swedish product register.

Annex 3.1.1: 	EUSES outprints related to the calculations of regional and continental PECs

Annex 3.1.2A to D: 	Temporal trends in measured Cd concentrations in the environment

Annex I:	Information on EU batteries’ collection, schemes and programs (dd. Febr.’02)

Annex II:	Methodology of MSW sorting studies (as submitted by CollectNiCad, 2002)

Annex III: 	Models for predicting waste arisings due to (sealed) portable Ni-Cd batteries

Annex IV: 	Emission data from earlier years 1994-‘96

Annex V: 		EUSES outprints related to the calculations of regional and continental PECs

Annex VI:	Overview of Cd emissions to water, air and PECs water, sediment, air, soil for other non-ferrous metals producers (site-specific information submitted)

in separate document ‘R302+303_0512_env_annexes.pdf’

# Footnotes

O.J. No L 084, 05/04/199 p. 0001 - 0075

O.J. No. L 161, 29/06/1994 p. 0003 – 0011

3 Technical Guidance Document, Part I-V, ISBN 92-827-801[1234]

Although a quantitative risk characterisation for exposure of organisms to airborne cadmium has not been done due to lack of useful data on the effects of airborn cadmium in environmental organisms, the (calculated) cadmium air emissions and concentrations of MSW incinerators are used in the risk assessment of man indirectly exposed via the environment (cfr. Section 4.1.3.3 of the overall RAR).

After the TMIV’02 last visit discussion on cadmium in sediment a number of MSs (UK, F, DE) and Industry commented on the sediment assessment and the current conclusions drawn in line with the outcome of that last TM (for more details, see effects assessment and risk characterisation).

no risk characterisation of marine environments was made in this report

This conclusion iii) is based on exposure data of 1996 and in absence of more recent emission and/or reliable measured data. To date, (some of) the plants may have ceased activity or changed their production process.

no further details on testing conditions are available

given that the results of testing could be dependent on the physical properties of the test material (particle size, possible coating, etc), as it is with other metal/metal powders, the testing programme should contain specifications on this issue (cfr NL comments).

on the other hand, IND was asked to continue its efforts related to replying to the questions asked on the NTP mutagenicity testing for mechanistic reasons.

dipping and spraying are no longer used (ICdA, com., 2003)

mechanical coating has declined significantly (ICdA, com., 2003)

this use is not known by Industry (ICdA, pers. com., 2003)

Rechargeable batteries can be charged many times. After a certain amount of charge cycles they are no more rechargeable and must also be disposed of.

For information: the definition as set by the EC Battery Directive reads: Battery: any source of electrical energy generated by direct conversion of chemical energy and consisting of one or more primary battery cells (non rechargeable). Accumulator: any secondary battery cell or set of secondary battery cells (rechargeable).

Cadmium has been used in some primary batteries in the past. There is no current application of cadmium in primary batteries (ICdA, pers. comm., 2000)

definitions may differ within, between MSs, IND, OECD, etc; e.g. the weight limit by industry is/can be different from those applicable elsewhere e.g. by Member States

Since household applications represent to date less than 20 % of the market by weight (cfr section 2.2.6.3) it is deemed more appropriate to use the term portable batteries (instead of consumer batteries) in order to indicate that the figures presented in this TRAR may include professional applications next to household applications.

For information: the definition as set by the draft EC Battery Directive ‘industrial and automotive batteries and accumulators’: any battery or accumulator use for industrial purposes, for instance as standby or traction power, emergency lighting, or for automotive starting power for vehicles. Remark: definitions may differ within and between MSs, IND, OECD, etc

OEM= Original Equipment Manufacturer

Since household applications represent to date less than 20 % of the market by weight it is deemed more appropriate to use the term  portable batteries (instead of consumer batteries) in order to indicate that the figures presented in this TRAR may include professional applications next to  household applications.

Those MSs replied to the Questionnaire under the section ‘Consumer batteries’. Some MSs gave details related to the types and applications of batteries while others did not.

The reference year 1999 has been chosen because this was the most recent year for which cross validation of the data provided by industry with those provided by the Member States was possible.

With update for 2000 and 2001, via CollectNiCad, 2002.

Long life articles are defined in the revised TGD as articles having a service life longer than one year

Council Common Position (EC) No 62/98 adopted on 13 October 1998, O.J. of 14.12.98, C 388, p. 1 – 3.

The cadmium emissions during the production of battery raw materials have been covered by the section 3.1.2.1 issuing from the previously separate overall RAR on Cd/CdO () and are not repeated here.

Belgian manufacturer has stopped manufacturing cells and shifted to assembly (of non-EU manufactured cells into packs) only since June 2001, Panasonic (former Philips), letter 30.09.02.

more information on the applied methodology is given in Annex III (as submitted by CollectNiCad, 2002)

Industrial Ni-Cd batteries, representing 20 % of the cadmium used in Ni-Cd batteries, are recycled at a high rate. In 1999 2,677 tonnes of industrial Ni-Cd batteries were recycled (Cfr. 2.2.2.5.1.2). This represents 72 % of the total sales for the same year (Cfr 2.5.4.2). If it is assumed that there is no time delay between the sales and the occurrence in the waste stream, 82 tonnes ((3,700 – 2,677) X 0.08) of cadmium is disposed in industrial landfills each year. The emissions of industrial landfills are not addressed here.

The current overall cadmium content of MSW is estimated to be 10 g/tonne dry wt. If it is assumed that at present only 10 % of this content can be allocated to the presence of Ni-Cd batteries – resulting in a worst case assumption for the future Cd content in MSW (cfr Table 3.1.20) - a current contribution of all other cadmium sources  of  9 g/tonnes dry wt. can be calculated.

However, it is clear that even when the production of Ni-Cd batteries has ceased the non-refined cadmium cements obtained as a by-product of zinc refining will obviously still have to be landfilled. This TRAR will not address this issue as it is out of the scope of the study. Moreover, it is obvious that after the year 2040, Cd from other sources will still be present (if no legislative action is taken to prevent these).

Only incineration and landfill practices are being considered in this TRAR. Other treatment methods as composting and recycling of MSW are either not applicable for Ni-Cd batteries (presorting) or irrelevant in view of the quantities.

For the calculation the detection limit value was divided by two

This value is also  well below the emission limit of 0.05 mg/L. (EC, 2000)

obtained via the modelling of future Ni-Cd waste arisings (section 3.1.2.2.5.3). Remark: note that the total amount of the MSW will probably also further increase (EEA, 2000) but this has not been taken into account.

These values are below the current EC limit of 0.05 mg/L (EC, 2000).

up to 500 year and under the assumption that the leachate concentration keeps constant during this time frame

this value is much smaller than the calculated amount of MSW landfille each year for the local generic landfill scenario, i.e. 80-160 ktonne wet wt. MSW/year). However, the driving parameter is the surface area. For the generic local landfill a surface area of 20 ha has been assumed which is in within the same order of magnitude as  the average landfill surface area of 14.7 hectare based on reported values.

Although it could be questioned that the removal rate of 60 % is also applicable to effluents with low cadmium concentrations (µg/L range) the removal percentage of 60 % is deemed appropriate since the landfill leachate is not the only cadmium source in the STP resulting in overall higher cadmium concentrations in the final STP influent. At local scale, the landfill on-site STP needs in general further tertiary ‘polishing’ water treatment techniques to reduce cadmium concentrations below 5 µg/L (cfr Baeyens, pers. com., 2003; Verstraete, pers. com., 2003) and this does not seem (yet) a standard practice in landfill management to date (EC Report, 1994; UK, com. 2002; RDCHW, 2002).

Via laboratory experiments and modelling techniques it was concluded that levels close to 5 µg/L and an order of magnitude higher could be expected from moderately mature and mature wastes, respectively.

obtained via the modelling of future Ni-Cd waste arisings (section 3.1.2.2.5.3). Remark: note that the total amount of the MSW will probably also further increase (EEA, 2000) but this has not been taken into account in this TRAR.

median of averages, median or geometric means (of min-max) of all European surveys listed in Tables 3.1.184 and 3.1.187. Observations near point sources and industrial activities are excluded and only the most recent data are included when data were reported for various periods. Concentrations in water refer to the dissolved fraction (see Table 3.1.184) but also include the data with ‘unknown fractionation’ (i.e. dissolved or not; this means that the median Cd water concentration can somewhat be overestimated).

In line with national and EU legislation sludges from on-site wwtp of Cd processors are likely to be classified as hazardous (e.g. see for the sector of metal treatment in IPPC, 2004; EC legislation in: EC, 1991 and EC, 2000)

the effect of an increase in MSW cadmium content up to 24 mg/kg dry wt. (‘future’ scenarios) will have only a minor influence on the currently derived PECs regional for air, water and soil (cfr EUSES outprints in Annex V).  Therefore there is no need to revise the current PEC reg, water and the PEC reg, air in order to derive the PEC values for the future situation

28 PEC reg, water, future = PEC reg, water, current. Indeed, the effect of an increase in MSW cadmium content up to 24 mg/kg dry wt. (‘future’ scenarios) will have only a minor influence on the currently derived PECs regional for air, water and soil (cfr EUSES outprints in Annex V).  Therefore there is no need to revise the current PEC reg, water and the PEC reg, air in order to derive the PEC values for the future situation

PEC reg, air, future = PEC reg, air, current. Indeed, the effect of an increase in MSW cadmium content up to 24 mg/kg dry wt. (‘future’ scenarios) will have only a minor influence on the currently derived PECs regional for air, water and soil (cfr EUSES outprints in Annex V).  Therefore there is no need to revise the current PEC reg, water and the PEC reg, air in order to derive the PEC values for the future situation.

In line with national and EU legislation sludges from on-site wwtp of Cd processors are likely to be classified as hazardous (e.g. see for the sector of metal treatment in IPPC, 2004; EC legislation in: EC, 1991 and EC, 2000)

¶ The current average Cd content in P fertilisers might also be 35 mg Cd/kg P2O5 or 79 mg Cd/kg P (personal communication). At an application rate of 407000 ton P fertiliser per year, this makes a Cd input of 32 ton Cd/y.

¶ The current average Cd content in P fertilisers might also be 35 mg Cd/kg P2O5 or 79 mg Cd/kg P (personal communication). At an application rate of 407000 ton P fertiliser per year, this makes a Cd input of 32 ton Cd/y.

¶ In Germany, the total production of municipal STP sludge is at the moment approximately 3 million tons per year (in dry weight). The following table indicates the fate of the sludge (rates are from year 1996). The source for the data is Umweltbundesamt (2001).

| Use in agriculture Use for landscaping Composting Incineration Deposition into landfills Other | 44,1 % 11,8 % 10 % 19,5 % 11,4 % 3,2 % |
| --- | --- |

MS have also made predictions for fertiliser Cd concentrations that are larger than currently applied values to evaluate the effect of new regulations on future trends in soil Cd. For example, Denmark predicted that future soil Cd may increase by 53%-74% in 100 years if fertiliser Cd contains 140 mg Cd/kg P (60 mg Cd/kg P205) and which is fourfold above the current concentrations in Denmark.

However, the methodology proposed by the rapporteur i.e. exclusion of outliers that are detected by statistical approach only was not endorsed by MSs (cfr ECB document ‘mi_302+303_tc0404_env’).

¶ The reporting limit (RL) is the lowest reported Cd concentration if no detection limit is indicated.

data were submitted in August 2005 and thus well beyond the agreed deadline for new data submission to be incorporated within the RAR following the CSTEE opinion

data were submitted in May 2005 and thus well beyond the agreed deadline for new data submission to be incorporated within the RAR following the CSTEE opinion

For Spain measured data (LÓPEZ ARIAS, M. & GRAU CORBÍ, J.M., 2004) were submitted in May 2005 and thus well beyond the agreed deadline for new data submission to be incorporated within the RAR following the CSTEE opinion

¶ Test media are considered to be similar if the difference in pH is 5% or less, if the difference in water hardness is 15% or less and if the difference in dissolved oxygen concentration, aluminium concentration, and temperature is 10% or less. Biomass and total weight of young per female are considered to be the same endpoint. Pond fish and laboratory fry (P. promelas) are considered to be the same species.

¶ Soils are considered similar if their pH differs by maximum 0.2 units, and if the %OC and %clay difference is less than or equal to 1 and 8% respectively.

For Cd metal producers: Industry statements, Zinc RAR; for CdO producers: no release of water effluent

¶ There is no dilution of the plating effluent in the water treatment plant in this scenario. As a dilution of 2 would remove the risk, UK suggested that it would be worth trying to obtain information on possible water volumes from that use (UK EA comments, Jan. 2003).

Industry analysed the data of 2000 showing that the P90 is largely affected by sites with historical pollution; the more recent databases revealed no risk, however this was not verified by MRS.

The type of the wwtp at the plants in the production area (Cd metal) being based on physical-chemical principles only, it is proposed that the conclusions related to the risk for micro-organisms in the on-site wwtp are considered as indicative only and are not taken forward to the section 5 (general conclusions).

After the TMIV’02 last visit discussion on cadmium in sediment a number of MSs (UK, F, DE) and Industry commented on the sediment assessment and the current conclusions drawn in line with the outcome of that last TM (for more details, see effects assessment and risk characterisation).

Remark: the type of the on-site STP (WWTP) at the battery production sites is essentially based on physical-chemical principles only (cfr information in Table 3.1.7).

For the year 2000, due to the implementation of a new wastewater treatment plant and the changing in the production process and cleaning method, a significant reduction in total emission towards the municipal STP is reported (cfr section 3.1.2.2.1) and based on measured data (concentration of Cd in effluent and the effluent flow) a lower PEC local and risk factor can be calculated.

For health risk evaluation reference is made to the ‘global’ RAR on Cd/CdO (Human Health cfr section 4.1.1.3 and 4.1.3.3 in separate document as well as to section 2.3 (legislative) control measures).

for Cd metal producers: Industry statements, Zinc RAR; for CdO producers: no release of water effluent

After the TMIV’02 last visit discussion on cadmium in sediment a number of MSs (UK, F, DE) and Industry commented on the sediment assessment and the current conclusions drawn in line with the outcome of that last TM (for more details, see effects assessment and risk characterisation).

Not all production sites submitted update exposure information. No data were provided by sites 6 and 7. Previous estimates remain valid.

After the TMIV’02 last visit discussion on cadmium in sediment a number of MSs (UK, F, DE) and Industry commented on the sediment assessment and the current conclusions drawn in line with the outcome of that last TM (for more details, see effects assessment and risk characterisation in the overall RAR on Cd/CdO).

After the TMIV’02 last visit discussion on cadmium in sediment a number of MSs (UK, F, DE) and Industry commented on the sediment assessment and the current conclusions drawn in line with the outcome of that last TM (for more details, see effects assessment and risk characterisation in the overall RAR on Cd/CdO).

1 After the TMIV’02 last visit discussion on cadmium in sediment a number of MSs (UK, F, DE) and Industry commented on the sediment assessment and the current conclusions drawn in line with the outcome of that last TM (for more details, see effects assessment and risk characterisation in the overall RAR Cd/CdO).

Commission of the European Communities, 1996. Technical Guidance Documents in Support of the  Commission Directive 93/67/EEC on risk assessment for new substances and the Commission Regulation (EC) No 1488/94 on risk assessment for existing substances. Commission of the European Communities, Brussels, Belgium.

ISBN 92-827-801[1234]

Commission of the European Communities, 2003. Technical Guidance Document on risk assessment in Support of the  Commission Directive 93/67/EEC on risk assessment for new notified substances, Commission Regulation (EC) No 1488/94 on risk assessment for existing substances and Directive 98/8/EC of the European Parliament and the Council concerning the placing of biocidal products on the market. Office for Official Publications of the European Communities, Luxembourg.

# Text boxes

NiCd

1983

26

Cd metal

2200

NiCd batteries

2733

(portable and industrial)

Alloy

26

106

plating

106

CdO

2536

Cd metal

5808

Cd metal

(1920)

(including NiCd batteries 653)

Pigments

830

NiCd

750

Stock

> 100

Stabilisers

297

Pigments

392

Stabilisers

131

Pigments 438

Stabilisers

166

CdO

1416

Recycling

337

IMPORT

INTO THE EU

PRODUCTION IN THE EU

CONSUMPTION IN THE EU

EXPORT

Cd(OH)2

Recycling of scrap:

400

Stock

Approx.

500

sludge

water

WWTP

Waste

water

Nickel strip

Steel strip perforation

Steel strips

Figure 2.2.7: Cadmium mass balance flow in the EU for the reference year 2000-2002 (mass balance drawn up by ICdA, IZA-Europe and Recharge)

*Data refers to 1996.  No update in figures was received

** Due to the Vinyl 2010 Commitment

***Not included is cadmium contained in imported raw materials (zinc, copper and lead ores). For zinc ores the estimated amount of cadmium in the EU-16 is 5000 t per year. Most of this cadmium is stated to be separated in the production processes, stabilized and disposed of in authorized hazardous waste disposal sites.

Estimated amount is 5000 T for EU zinc industry.

Air emission

Air emission

Waste

water

Powder filter collectors

Electrolyte addition

Cell Finishing

Electrical/Electrochemical Tests

Formation Process

Assembling Process

Manufacturing of pocket plates

Manufacture of active materials

(positive (Ni) and negative (Cd))

sludge

water

Discharge

Charge

Battery Assembling

solid

waste

WWTP

Waste

water

Air emission

Figure 2.2.1: Flowsheet manufacturing process pocket plate Ni-Cd batteries

Figure2.2.2: Flowsheet production process Nickel fiber plate Ni-Cd batteries

Manufacture of Nickel fiber plates

Electroless and Galvanic

Metallization Process

Tab/Plate Welding Process

Positive Electrode Impregnation with Nickel hydroxide

Negative Electrode Impregnation with Cadmium oxide

Separation Process

Stack Assembling Process

Formation Process

Cell Assembling Process

Cell Finishing

Electrical/Electrochemical Tests

Battery Assembling

CdO

Waste air

Filter cake from formation process

Air emission

Production

waste

Figure 2.2.3: Flowsheet of major operations in sintered plate Ni-Cd batteries manufacture

Nickel-plated steel

Nickel powder

Sintered

strip formed

Impregnating

Impregnating

Nickel nitrate

Concentrated solution

drying

immersion

washing

assembly

Electrolyte addition

Test and pack

Neutralisation

To surface water

sludge (dry)

Cd(OH)2

Ni(OH)2

Rejected cells

NaOH 20%solution

felted nylon

cellullose separator

nickel-plated

steel case

KOH,NaOH

Cadmium nitrate

solution

Water effluent

Ni(OH)2

Cd(OH)2

Figure 2.2.4: Ni-Cd Battery Recycling (CollectNiCad, 2000b adapted)

Industrial

Portable

Sorting         *

Single Cells/Packs

Dismantling

Electrode Separation

Dismantling:         *

External Case Separation

Pyrolysis

Distillation

Plastic

Nickel

Fe – Ni

smelting

Cadmium

refining

Ni-Cd Batteries Recycling Scheme

Steel production

cadmium

(batteries, etc)

* facultative step(s)

Water treatment and plastics recovery

Air filtration

Water treatment and Electrolyte Re-use

Production Ni-Cd batteries

Production

Waste

End of

life

Selective

Collection

Incineration

Landfill

Collected waste

Accumulated

stocks

product

recycling

Re-use of incineration residues

Soil (0.3 m)

Soil  (1.5 m)

Clay (1m)

Clay (1m)

HDPE

Sand  (0.5m)

Sand  (0.5m)

Soil

(1.5 m)

Soil

(1.5 m)

Clay (1m)

HDPE

Sand  (0.5m)

Clay (1m)

Sand  (0.5m)

Clay (1m)

HDPE

Sand  (0.5m)

Clay (1m)

Sand  (0.5m)

Clay (1m)

HDPE

Sand  (0.5m)

Clay (1m)

Sand  (0.5m)

Clay (1m)

HDPE

Sand  (0.5m)

Clay (1m)

Sand  (0.5m)

Waste (20 m)

Waste (20 m)

Waste (20 m)

Waste (20 m)

Predicted waste arisings (tonnes/year)

Collection

(section 2.2.2.5.2)

Used Ni-Cd batteries becoming available for collection (tonnes/year)

Clearance rate (%/year)

(section 3.1.2.2.5.3)

Historical market data (tonnes/year)

(section 2.2.2.4.2 and 2.2.2.4.3)